## Slide 1: Tools for Evaluating Memory and Memory-Centric Computing DRAM, Storage, Virtual Memory
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
27 June 2026
2nd Ramulator & DRAM Bender Tutorial @ ISCA 2026

## Slide 2: Tutorial on DRAM Bender & Ramulator
https://events.safari.ethz.ch/asplos26-ramulator-drambender/

## Slide 3: ISCA 2026: DRAM Bender & Ramulator
https://events.safari.ethz.ch/isca26-ramulator-drambender/

## Slide 4: ICS 2026: DRAM Bender & Ramulator
https://events.safari.ethz.ch/ics26-ramulator-drambender/

## Slide 5: Virtuoso Tutorial & Workshop
https://cmu-safari.github.io/Virtuoso/workshop/asplos2026.html

## Slide 6: Evaluating New Ideas for New (Memory) Architectures

## Slide 7: Potential Evaluation Methods
How do we assess how an idea will affect a target metric X?
A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling/estimation
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 8: An Example Testing Platform

## Slide 9: Infrastructures to Understand Memory Issues
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), temperature (±0.5°C ),
and voltage (±1mV)
*Olgun et al., “DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips,” in TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
*
Notes: To build a better understanding of read disturbance, we develop and use an FPGA-based experimental setup programmed with DRAM Bender, which is our own design and open-sourced on github [CLICK]
We plug in a DRAM module to test on the FPGA board [CLICK]
The board communicates with the host machine to run the test routines and collect experimental data[CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We also have an external power supply that we use to sweep voltage on certain power rails [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and voltage [CLICK]
=======

## Slide 10: HBM2 DRAM Testing Infrastructure
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-Based Infrastructure to Easily Test State-of-the-Art DRAM Chips,” TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
Fine-grained control over DRAM commands,
timing parameters (±1.67ns), and temperature (±0.5°C )
  DRAM Bender on a Bittware XUPVVH
Notes: This is another version of the same infrastructure we use to test HBM2 DRAM chips.

## Slide 11: Laboratory for Understanding Memory

## Slide 12: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 13: Laboratory for Understanding Memory
https://arxiv.org/pdf/2606.13725

## Slide 14: DRAM Testing Infrastructures (I)
DDR4 DRAM R/UDIMMs
Xilinx Alveo U200
DDR4 DRAM (SODIMM)
Bittware XUSP3S
HBM2 DRAM Chips
Xilinx Alveo U50
DDR3 DRAM SODIMMs Xilinx ML605
Notes: Over time we built several versions of this infrastructure to support various memory standards, including DDR3 SODIMMs [CLICK]
DDR4 RDIMMS, UDIMMS [CLICK]
And SODIMMs [CLICK]
And HBM2 DRAM Chips [CLICK]

## Slide 15: DRAM Testing Infrastructures (II)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 16: DRAM Testing Infrastructures (III)
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 17: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 18: SoftMC: Open Source DRAM Infrastructure
https://github.com/CMU-SAFARI/SoftMC
Hasan Hassan, Nandita Vijaykumar, Samira Khan, Saugata Ghose, Kevin Chang, Gennady Pekhimenko, Donghyuk Lee, Oguz Ergin, and Onur Mutlu, "SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA), Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture (39 minutes)] [Source Code]

## Slide 19: DRAM Bender
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 20
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 21: Modern DRAM is Prone to Disturbance Errors
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly reading a row enough times (before memory gets refreshed) induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 22: Read Disturbance Worsens with Scaling
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Technology Scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2

## Slide 23: RowHammer [ISCA 2014]
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue). Winner of the 2024 IFIP Jean-Claude Laprie Award in dependable computing (link).

## Slide 24: Many RowHammer Security Exploits
One can exploit RowHammer to
Take over a system
Read data they do not have access to
Break out of virtual machine sandboxes
Corrupt important data  render ML inference useless
Steal secret data (e.g., crypto keys & ML model parameters)

## Slide 25: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. IEEE Micro Top Pick in 2024.

## Slide 26: RowPress vs. RowHammer
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
RowPress reduces the number of activations
to induce a bitflip by 1-2 orders of magnitude
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 27: RowPress
Amplifies Read Disturbance in DRAM
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
Notes: RowPress amplifies read disturbance because
First, it reduces the minimum number of row activations needed to induce a bitflip by 1-2 orders of magnitude
Second, in extreme cases, activating a row only once induces bitflips

## Slide 28: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 29: An “Early” Position Paper [IMW 2013]
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 30: Updated Paper 12 Years Later [IMW 2025]
Onur Mutlu, Ataberk Olgun, and İsmail Emir Yüksel, "Memory-Centric Computing: Solving Computing's Memory Problem" Invited Paper in Proceedings of the 17th IEEE International Memory Workshop (IMW), Monterey, CA, USA, May 2025. [Slides (pptx) (pdf)]
https://www.arxiv.org/pdf/2505.00458

## Slide 31: Industry’s Intelligent DRAM Controllers (I)

## Slide 32: Industry’s Intelligent DRAM Controllers (II)

## Slide 33: Industry’s Intelligent DRAM Controllers (III)

## Slide 34: Finally: Serious Changes in Standards (2024)

## Slide 35: Are Solutions Good?
https://www.reddit.com/r/CrappyDesign/comments/arw0q8/now_this_this_is_poor_fencing/

## Slide 36: Simulating New Ideas: Ramulator
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 37: Ramulator 2.0: A Much Better Ramulator
Haocong Luo, Yahya Can Tugrul, F. Nisa Bostanci, Ataberk Olgun, A. Giray Yaglikci, and Onur Mutlu, "Ramulator 2.0: A Modern, Modular, and Extensible DRAM Simulator" Preprint on arxiv, August 2023. [arXiv version] [Ramulator 2.0 Source Code]
https://arxiv.org/pdf/2308.11030.pdf
https://github.com/CMU-SAFARI/ramulator2

## Slide 38: Ramulator 2.1: A Recent Update
Appears at ICS 2026 Workshops Proceedings
https://arxiv.org/pdf/2606.13844
https://github.com/CMU-SAFARI/ramulator2

## Slide 39: Evaluation of Industry’s Recent Solutions
Appears at DRAMSec 2024
https://arxiv.org/pdf/2406.19094
https://github.com/CMU-SAFARI/ramulator2

## Slide 40: Evaluation of Industry’s Recent Solutions
Oguzhan Canpolat, Abdullah Giray Yaglikci, Geraldo Francisco de Oliveira, Ataberk Olgun, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Oguz Ergin, and Onur Mutlu, "Chronus: Understanding and Securing the Cutting-Edge Industry Solutions to DRAM Read Disturbance" Proceedings of the 31st International Symposium on High-Performance Computer Architecture (HPCA), Las Vegas, NV, USA, March 2025. [Chronus Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, functional, and reproduced.
https://arxiv.org/pdf/2502.12650
https://github.com/CMU-SAFARI/Chronus

## Slide 41: Asking the Right Question
Can We Do Better?

## Slide 42: Better Partitioning of DRAM & Controller
Hasan Hassan, Ataberk Olgun, A. Giray Yaglikci, Haocong Luo, and Onur Mutlu, "Self-Managing DRAM: A Low-Cost Framework for Enabling Autonomous and Efficient DRAM Maintenance Operations" Proceedings of the 57th International Symposium on Microarchitecture (MICRO), Austin, TX, USA, November 2024. [Slides (pptx) (pdf)] [SelfManagingDRAM Source Code]
https://arxiv.org/pdf/2207.13358.pdf

## Slide 43: SMD Key Idea: Autonomous Maintenance
Memory Controller (MC)
DRAM Chip
DRAM command
data
do maintenance
DRAM chip controls in-DRAM maintenance operations
Enable implementing new maintenance mechanisms without modifying the standard and exposing DRAM-internal proprietary information
Notes: In our work, we introduce autonomous in-DRAM maintenance operations
[CLICK] in which the DRAM chip has full control over in-DRAM maintenance operations
[CLICK] This allows us to add new maintenance mechanisms inside a DRAM chip without modifying the standard and without
Exposing DRAM-internal proprietary informatino

## Slide 44: SMD Key Contribution
orchestrates all access operations
performs its own maintenance autonomously
Memory Controller (MC)
DRAM Chip
DRAM command
data
negative acknowledgment (nack)
Partition the work nicely between the memory controller and the DRAM chip
DRAM chip controls in-DRAM maintenance operations
with a single, simple interface change
Notes: In summary, SMD enables [CLICK] autonomous in-DRAM maintenance operations with [CLICK] a simple change in the interface.
[CLICK] SMD divides the work nicely between the memory controller and the DRAM chip such that new maintenance mechanisms can be implemented without modifying the DRAM standard

## Slide 45: SMD-Based Maintenance Mechanisms
DRAM
Refresh
RowHammer Protection
Memory Scrubbing
Fixed Rate (SMD-FR)
Variable Rate (SMD-VR)
uniformly refreshes all DRAM rows with a fixed refresh period
skips refreshing rows that can retain their data for longer than the default refresh period
Probabilistic (SMD-PRP)
Deterministic (SMD-DRP)
keeps track of most frequently activated rows and performs neighbor row refresh when activation count threshold is exceeded
Periodic Scrubbing (SMD-MS)
periodically scans the entire DRAM for errors and corrects them
Performs neighbor row refresh with a small probability on every row activation
Notes: Using the Self-Managing DRAM architecture, we develop various maintenance mechanisms.
[CLICK] For DRAM refresh, [CLICK] we develop Fixed-Rate Refresh (SMD-FR), which uniformly refreshes all DRAM rows with a fixed refresh period.
[CLICK] Also, we develop Variable Rate Refresh (SMD-VR), which uses retention profiling information to skip refreshing rows that can retain their data correctly for extended periods.
[CLICK] For RowHammer Protection, [CLICK] we develop Probabilistic RowHammer Protection (SMD-PRP), which performs neighbor row refresh with a small probability on every row activation.
[CLICK] Second, we develop Deterministic RowHammer Protection (SMD-DRP), which identifies frequently activated rows and refreshes only their neighbor rows when needed.
[CLICK] Last, we develop a mechanism for memory scrubbing. [CLICK] SMD-MS periodically scans the entire DRAM for errors and corrects them.
Thanks to SMD, we all these mechanisms can be implemented completely within DRAM and they can operate together.

## Slide 46: Talk on Self-Managing DRAM
https://www.youtube.com/watch?v=mGa6-vpExbE

## Slide 47: Self-Managing DRAM
Hasan Hassan, Ataberk Olgun, A. Giray Yaglikci, Haocong Luo, and Onur Mutlu, "Self-Managing DRAM: A Low-Cost Framework for Enabling Autonomous and Efficient DRAM Maintenance Operations" Proceedings of the 57th International Symposium on Microarchitecture (MICRO), Austin, TX, USA, November 2024. [Slides (pptx) (pdf)] [SelfManagingDRAM Source Code]
https://arxiv.org/pdf/2207.13358

## Slide 48: More in My MICRO 2025 Keynote Talk
https://www.youtube.com/watch?v=Mk6j9zP3s9E

## Slide 49: More to Come…

## Slide 50: Can We Do Better?
There Is Still
a Whole Lot
We Do Not Know
About DRAM

## Slide 51: RowHammer Becomes Worse with Aging
Preliminary data on aging via 68-day of continuous hammering
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)
Aging can lead to read disturbance bitflips at smaller hammer counts
Minimum hammer count to induce the first bitflip HCfirst (before aging)
Minimum hammer count to induce the first bitflip HCfirst (after aging)

## Slide 52: RowHammer (Spatial Variation) Analysis (2024)
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18652

## Slide 53: Variable Read Disturbance (2025)
The Read Disturbance Threshold (RDT) of a row changes randomly and unpredictably over time
Accurately identifying RDT is challenging
Key Takeaway
https://arxiv.org/pdf/2406.13080v2
Notes: … starting with this takeaway message.
We find that the read disturbance threshold of a row changes randomly and unpredictably over time.
This makes accurately identifying RDT very challenging.

## Slide 54: Variable Read Disturbance (2025)
Appears at HPCA 2025
https://arxiv.org/pdf/2502.13075
Read disturbance threshold varies unpredictably over time

## Slide 55: ColumnDisturb (2025)
Appears at MICRO 2025
https://arxiv.org/pdf/2510.14750
A single row activation flips bits across three DRAM subarrays (up to 3072 DRAM rows)

## Slide 56: PuDHammer (2025)
Appears at ISCA 2025
https://arxiv.org/pdf/2506.12947
Read disturbance becomes much worse with processing using DRAM

## Slide 57: PuDGhost (2026)
Appears at ISCA 2026
https://arxiv.org/pdf/2606.19119
Data in non-activated rows affect PuD computation results

## Slide 58: DejaVu (2026)
Appears at ISCA 2026
https://arxiv.org/pdf/2606.22297
Data previously written to a row
affects the row’s read disturbance vulnerability

## Slide 59: Emerging Memories Also Need Intelligent Controllers
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf) One of the 13 computer architecture papers of 2009 selected as Top Picks by IEEE Micro. Selected as a CACM Research Highlight. 2022 Persistent Impact Prize.

## Slide 60: Laboratory for Understanding Memory

## Slide 61: Laboratory for Understanding Memory
https://arxiv.org/pdf/2606.13725

## Slide 62: A Very Recent PhD Thesis
A. Giray Yaglikci, "Enabling Efficient and Scalable DRAM Read Disturbance Mitigation via New Experimental Insights into Modern DRAM Chips," PhD Thesis, ETH Zürich, 2024. [Slides (pdf) (pptx)] [Thesis arXiv (abs) (pdf)] [SAFARI News]
https://arxiv.org/pdf/2408.15044.pdf
SIGMICRO & DSN Carter Dissertation Awards & SIGARCH/TCCA Honorable Mention

## Slide 63: Capabilities of Off-The-Shelf Memory
Existing DRAM Chips
Are Already Quite Capable

## Slide 64: The Capability of COTS DRAM Chips
64
We demonstrate that COTS DRAM chips:
Can copy one row into up to 31 other rows
with >99.98% success rate
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 65: Functionally-Complete DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024. [Slides (pptx) (pdf)] [arXiv version] [FCDRAM Source Code]
https://arxiv.org/pdf/2402.18736

## Slide 66: Simultaneous Row Activation & Multi-Row Copy
Ismail Emir Yuksel, Yahya Can Tugrul, F. Nisa Bostanci, Geraldo F. Oliveira, A. Giray Yaglikci, Ataberk Olgun, Melina Soysal, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 54th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Brisbane, Australia, June 2024. [Slides (pptx) (pdf)] [arXiv version] [SiMRA-DRAM Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as both code and dataset available, reviewed and reproducible.
https://arxiv.org/pdf/2405.06081

## Slide 67: In-DRAM Multiple Row Copy (Multi-RowCopy)
d
s
t
r
c
s
Simultaneously activate many rows to copy one row’s content to multiple destination rows
d
s
t
s
r
c
RowClone
s
r
c
r
c
s
s
r
c
d
s
t
d
s
t
d
s
t
Multi-RowCopy
s
r
c
s
r
c
s
r
c
Notes: [CLICK] Our key idea is since we can activate many rows simultaneously, we can copy one row’s content to other simultaneously activated rows
[CLICK] Let’s recall the RowClone example where we copy source to destination
[CLICK] In RowClone, we first activate the source row which will copy its content to sense amplifiers
[CLICK] And then, we activate destination row to drive the sense amplifier’s content to destination row
[CLICK] In our mechanism, which we call Multi-RowCopy, we have several destination rows
[CLICK] Here we activate many destination rows simultaneously
[CLICK] and thus sense amplifier drives its content to these destination rows.

## Slide 68: Key Idea: NOT Operation
68
Connect rows in neighboring subarrays
through a NOT gate by consecutively activating rows
SA
A
src
dst
ACT src
ACT dst
SA
A
src
dst
SA
A
src
dst
~A
NOT gate
Notes: Our key idea is to leverage the connection between neighboring subarrays,
[CLICK] the NOT gate in the sense amplifier.
[CLICK] By simultaneously activating rows in neighboring subarrays, we can connect these rows through a NOT gate
[CLICK] As an example, source and destination in neighboring subarrays and if we first activate src
[CLICK] and then activate destination, this result in sense amplifier to drive the negated src value to the dst

## Slide 69: Key Idea: NAND, NOR, AND, OR
69
Manipulate the bitline voltage to express
a wide variety of functions using
simultaneous multi-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amplifier
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in X and Y and the bitline at the top subarray becomes the function of voltages in A and B
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 70: Two-Input AND and NAND Operations
VDD=1 & GND = 0
70
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1

## Slide 71: Many-Input AND, NAND, OR, and NOR Operations
VDD=1 & GND = 0
X
Y
AND
0
0
0
0
1
0
1
0
0
1
1
1
NAND
1
1
1
0
71
Reference Subarray (REF)
Compute Subarray (COM)
VDD/2
VDD
X
Y
ACT REF
PRE
ACT COM
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
We can express AND, NAND, OR, and NOR operations
by carefully manipulating the reference voltage
(More details in the paper)
https://arxiv.org/pdf/2402.18736.pdf
Notes: By carefully choosing the voltage levels of the cells in the reference subarray, we can express many-input AND, NAND, OR, and NOR operations
[CLICK] As our time is limited, please check our paper for more details.

## Slide 72: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
72
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 73: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
73
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 74: Robustness of Multi-RowCopy
COTS DRAM chips can copy one row’s content to up to 31 rows with a very high success rate
Average: >99.98%
Notes: Now let me show you the first result
[CLICK] In this plot, y-axis shows the success rate
[CLICK] x-axis shows the number of destination rows from 1 to 31
[CLICK] And we plot the success rate distribution as a box-and-whiskers plot
[CLICK] We observe that the average success rate is higher than 99.98% across all tested number of destination rows
[CLICK] Hence, we conclude that off-the-shelf DRAM chips can copy one row’s content to up to 31 rows with a very high success rate

## Slide 75: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
75
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 76: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
16-input AND, NAND, OR, and NOR operations
with very high success rate (>94%)
76
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 77: More on Multi-Row Copy
Ismail Emir Yuksel, Yahya Can Tugrul, F. Nisa Bostanci, Geraldo F. Oliveira, A. Giray Yaglikci, Ataberk Olgun, Melina Soysal, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 54th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Brisbane, Australia, June 2024. [Slides (pptx) (pdf)] [arXiv version] [SiMRA-DRAM Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as both code and dataset available, reviewed and reproducible.
https://arxiv.org/pdf/2405.06081

## Slide 78: More on Functionally-Complete DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024. [Slides (pptx) (pdf)] [arXiv version] [FCDRAM Source Code]
https://arxiv.org/pdf/2402.18736

## Slide 79: An Example Prototyping Platform

## Slide 80: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 81: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 82: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 83: Microbenchmark Copy/Initialization Throughput
In-DRAM Copy and Initialization improve throughput by 119x and 89x
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 84: More on PiDRAM
Ataberk Olgun, Juan Gomez Luna, Konstantinos Kanellopoulos, Behzad Salami, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "PiDRAM: A Holistic End-to-end FPGA-based Framework for Processing-in-DRAM" ACM Transactions on Architecture and Code Optimization (TACO), March 2023. [arXiv version] Presented at the 18th HiPEAC Conference, Toulouse, France, January 2023. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (40 minutes)] [PiDRAM Source Code]

## Slide 85: Simulation: The Field of Dreams

## Slide 86: Dreaming and Reality
An architect is in part a dreamer, a creator
Simulation is a key tool of the architect
  Allows the evaluation & understanding of non-existent systems
Simulation enables
  The exploration of many dreams
  A reality check of the dreams
  Deciding which dream is better
Simulation also enables
  The ability to fool yourself with false dreams

## Slide 87: Tradeoffs in Simulation
Three metrics to evaluate a simulator
  Speed
  Flexibility
  Accuracy
Speed: How fast the simulator runs (xIPS, xCPS, slowdown)
Flexibility: How quickly one can modify the simulator to evaluate different algorithms and design choices?
Accuracy: How accurate the performance (energy) numbers the simulator generates are vs. a real design (Simulation error)
The relative importance of these metrics varies depending on where you are in the design process (what your goal is)

## Slide 88: Trading Off Speed, Flexibility, Accuracy
Speed & flexibility affect:
  How quickly you can make design tradeoffs/decisions
Accuracy affects:
  How good your design tradeoffs/decisions might end up being
  How fast you can build your simulator (simulator design time)
Flexibility also affects:
  How much human effort you need to spend modifying the simulator
You can trade off between the three to achieve design exploration and decision goals

## Slide 89: Making The Best of Architecture
A good architect is comfortable at all levels of refinement
  Including the extremes
A good architect knows when to use what type of simulation
  And, more generally, what type of evaluation method
Recall: A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 90: More on Simulation: A Lecture
https://www.youtube.com/watch?v=lJ5UpGvdm4Y

## Slide 91: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 92: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 93: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 94: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 95: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 96: Ramulator: Free & Open Source
https://github.com/CMU-SAFARI/ramulator

## Slide 97: Ramulator: Integration with Other Simulators
https://github.com/CMU-SAFARI/ramulator

## Slide 98: Ramulator: Reproducibility
https://github.com/CMU-SAFARI/ramulator

## Slide 99: An Example Study using Ramulator (I)
Saugata Ghose, Tianshi Li, Nastaran Hajinazar, Damla Senol Cali, and Onur Mutlu, "Demystifying Workload–DRAM Interactions: An Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Phoenix, AZ, USA, June 2019. [Preliminary arXiv Version] [Abstract] [Slides (pptx) (pdf)] [MemBen Benchmark Suite] [Source Code for GPGPUSim-Ramulator]

## Slide 100: Key Takeaways
DRAM latency remains a critical bottleneck for many applications
Bank parallelism is not fully utilized by a wide variety of our applications
Spatial locality continues to provide significant performance benefits if it is exploited by the memory subsystem
For some classes of applications, low-power memory can provide energy savings without sacrificing significant performance

## Slide 101: BlockHammer Study in 2021
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)

## Slide 102: BlockHammer: Free & Open Source
https://github.com/CMU-SAFARI/BlockHammer

## Slide 103: Many Other Ideas Evaluated w/ Ramulator
https://www.youtube.com/watch?v=pJ3mdIvMOY4&list=PL5Q2soXY2Zi-cAls3cyauNzM7-74Eq31O&index=9

## Slide 104: Ramulator Project Course Exploration of Emerging Memory Systems (Spring/Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 105: Ramulator 2.0: A Much Better Ramulator
Haocong Luo, Yahya Can Tugrul, F. Nisa Bostanci, Ataberk Olgun, A. Giray Yaglikci, and Onur Mutlu, "Ramulator 2.0: A Modern, Modular, and Extensible DRAM Simulator" Preprint on arxiv, August 2023. [arXiv version] [Ramulator 2.0 Source Code]
https://arxiv.org/pdf/2308.11030.pdf
https://github.com/CMU-SAFARI/ramulator2

## Slide 106: Ramulator 2.0 Design and Features (I)
Hierarchical state-machine based modeling of DRAM
Level: “Channel”
Id: 0
State: …
Level: “Rank”
Id: 1
State: …
Parent
Level: “Rank”
Id: 0
State: …
Sibling
Level: “BankGroup”
Id: 0
State: …
Children
Level: “BankGroup”
Id: 1
State: …
State of a DRAM node:
Current state: open, close, activating, etc.
Timing constraints: Earliest time in the future that each DRAM command is allowed to be issued
Energy & power: Time spent in each state and the number of DRAM commands served (DRAMPower model)
Can be extended to include more

## Slide 107: Ramulator 2.0 Design and Features (III)
Modular and extensible software architecture
  All components in the memory system modeled with the same interface and different implementations
  Example: The memory controller include:
    Address Mapper, Request Scheduler, Refresh Controller, Row Policy, ...
    Each can be flexibly changed without hardcoding other parts

## Slide 108: Ramulator 2.0 Design and Features (IV)
In the paper
  More detailed explanation of modeling methodology
  Authoring of DRAM specifications (organization, timings, etc.)
  Memory controller plugin & RowHammer mitigations
  Performance comparison with other DRAM simulators
  …
IEEE CAL Paper
Open-source version Github repo: CMU-SAFARI/ramulator2

## Slide 109: Ramulator 2.0 Case Studies (I)
Cross-section performance overhead evaluation of different RowHammer mitigation techniques [Luo+, IEEE CAL]
  Six different RowHammer mitigation techniques all implemented as plugins to the same memory controller implementation

## Slide 110: Ramulator 2.0 Case Studies (II)
Performance evaluation of DDR5 Per Row Activation Counting (PRAC) [Canpolat+, DRAMsec’24]
  Memory controller implementation extended with support for per-row activation count tracking and back-off signal

## Slide 111: Evaluation of Industry’s Recent Solutions
Oguzhan Canpolat, Abdullah Giray Yaglikci, Geraldo Francisco de Oliveira, Ataberk Olgun, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Oguz Ergin, and Onur Mutlu, "Chronus: Understanding and Securing the Cutting-Edge Industry Solutions to DRAM Read Disturbance" Proceedings of the 31st International Symposium on High-Performance Computer Architecture (HPCA), Las Vegas, NV, USA, March 2025. [Chronus Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, functional, and reproduced.
https://arxiv.org/pdf/2502.12650
https://github.com/CMU-SAFARI/Chronus

## Slide 112: Ramulator 2.1: A Recent Update
Appears at ICS 2026 Workshops Proceedings
https://arxiv.org/pdf/2606.13844
https://github.com/CMU-SAFARI/ramulator2

## Slide 113: More to Come…

## Slide 114: Read Disturbance Sessions @ HPCA 2025
Tuesday, March 4th, 11am and 2pm

## Slide 115: Read Disturbance Papers @ ASPLOS 2025

## Slide 116: Read Disturbance Session @ ISCA 2025

## Slide 117: Read Disturbance Papers @ DRAMSec 2025
https://www.youtube.com/watch?v=5KmKxFjPopM
https://dramsec.ethz.ch/

## Slide 118: RowHammer @ USENIX Security 2025

## Slide 119: Read Disturbance Papers @ MICRO 2025

## Slide 120: Read Disturbance Papers @ HPCA 2026

## Slide 121: Read Disturbance Papers @ ASPLOS 2026

## Slide 122: Read Disturbance Papers @ S&P 2026

## Slide 123: RowHammer on GPUs
https://gddr.fail/
https://gpubreach.ca/
https://www.gpuhammer.com/

## Slide 124: Read Disturbance Papers @ DRAMSec 2026
https://dramsec.ethz.ch/

## Slide 125: Read Disturbance Papers @ ISCA 2026

## Slide 126: Tutorial on DRAM Bender & Ramulator
https://events.safari.ethz.ch/asplos26-ramulator-drambender/

## Slide 127: ISCA 2026: DRAM Bender & Ramulator
https://events.safari.ethz.ch/isca26-ramulator-drambender/

## Slide 128: ICS 2026: DRAM Bender & Ramulator
https://events.safari.ethz.ch/ics26-ramulator-drambender/

## Slide 129: Goal: Processing Inside Memory/Storage
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory/Storage
Database
Graphs
Media
ML Model
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 130: Ramulator for Processing in Memory

## Slide 131: Simulation Infrastructure for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator-pim
  https://github.com/CMU-SAFARI/ramulator
  [Source Code for Ramulator-PIM]

## Slide 132: Ramulator for PIM
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira, Stefano Corda, Sander Stujik, Onur Mutlu, and Henk Corporaal, "NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning" Proceedings of the 56th Design Automation Conference (DAC), Las Vegas, NV, USA, June 2019. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code for Ramulator-PIM]

## Slide 133: Ramulator Project Course Exploration of Emerging Memory Systems (Spring/Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 134: Memory-Centric Computing Systems Workshop
https://events.safari.ethz.ch/asplos26-MCCSys/

## Slide 135
6th Workshop on Memory-Centric Computing Systems
A full-day workshop @ ISCA 2026
28th June 2026 (Sunday)
Organizers: Ismail Emir Yuksel, F. Nisa Bostanci, Ataberk Olgun, Prof. Onur Mutlu
Overview of PIM & PIM Taxonomy
PIM in Memory & Storage
Infrastructures for PIM Research
Real-World PnM Systems
PuM for Bulk Bitwise Operations
Programming Techniques & Tools
Research Challenges & Opportunities
MCCSys
https://events.safari.ethz.ch/isca26-mccsys/
More information &
call for papers:

## Slide 136
7th Workshop on Memory-Centric Computing Systems
A full-day workshop @ ICS 2026
6th July 2026 (Monday)
Organizers: Ismail Emir Yuksel, F. Nisa Bostanci, Ataberk Olgun, Prof. Onur Mutlu
Overview of PIM & PIM Taxonomy
PIM in Memory & Storage
Infrastructures for PIM Research
Real-World PnM Systems
PuM for Bulk Bitwise Operations
Programming Techniques & Tools
Research Challenges & Opportunities
MCCSys
https://events.safari.ethz.ch/ics26-mccsys/
More information &
call for papers:

## Slide 137: Some Other Useful Simulators

## Slide 138: Virtuoso Tutorial & Workshop
https://cmu-safari.github.io/Virtuoso/workshop/asplos2026.html

## Slide 139: Many Simulators for Many Purposes
Ramulator 2.0 for memory simulation
gem5 full system multi-core simulation
MQSim for SSD simulation
DiskSim for Hard Disk simulation
DAMOV-Sim for Processing-near-Memory simulation
Virtuoso for Virtual Memory (HW/SW codesign) simulation
Sniper for fast Processor Simulation
Scarab for detailed Microarchitectural Simulation
Simics, Bochs, QEMU for full-system functional simulation
…
Or, develop your own simulator for your purpose…

## Slide 140: DAMOV Simulator, Methods & Benchmarks
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 141: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 142: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 143: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 144: PIM Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 145: MQSim for Modern SSD Simulation
Arash Tavakkol, Juan Gomez-Luna, Mohammad Sadrosadati, Saugata Ghose, and Onur Mutlu, "MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices" Proceedings of the 16th USENIX Conference on File and Storage Technologies (FAST), Oakland, CA, USA, February 2018. [Slides (pptx) (pdf)] [Source Code]

## Slide 146: Solid-State Drives Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=modern_ssds
Youtube Livestream:
  https://www.youtube.com/watch?v=_q4rm71DsY4&list=PL5Q2soXY2Zi8vabcse1kL22DEcgMl2RAq
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 147: Many More Simulators …
https://github.com/CMU-SAFARI/

## Slide 148: Virtuoso
Konstantinos Kanellopoulos, Konstantinos Sgouras, Nisa Bostanci, Andreas Kosmas Kakolyris, Berkin Kerim Konar, Rahul Bera, Rakesh Kumar, Mohammad Sadrosadati, Nandita Vijaykumar, and Onur Mutlu, "Virtuoso: Enabling Fast and Accurate Virtual Memory Research via an Imitation-based Operating System Simulation Methodology," Proceedings of the 30th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Rotterdam, Netherlands, April 2025. [Slides (pptx) (pdf)] [Virtuoso Source Code]
https://arxiv.org/pdf/2403.04635
https://github.com/CMU-SAFARI/Virtuoso

## Slide 149: Virtuoso Tutorial & Workshop
https://cmu-safari.github.io/Virtuoso/workshop/asplos2026.html

## Slide 150: Virtuoso
Konstantinos Kanellopoulos Konstantinos Sgouras F. Nisa Bostanci
Andreas Kosmas Kakolyris Berkin Kerim Konar Rahul Bera
Mohammad Sadrosadati Rakesh Kumar Nandita Vijaykumar Onur Mutlu
Enabling Fast and Accurate Virtual Memory Research with an Imitation-based Operating System Simulation Methodology
https://github.com/CMU-SAFARI/Virtuoso

## Slide 151: Existing Architectural Simulators
Emulation-based
Simulation Speed
Accuracy in Estimating VM overheads
Our goal
Full-System

## Slide 152: Enabling Fast and Accurate VM Research
New simulation framework that enables
fast and accurate prototyping and evaluation of
the software and hardware components of VM
Virtuoso

## Slide 153: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based address mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing the HW/SW components
of multiple state-of-the-art VM techniques
Speculative Translation
TLB Prefetching

## Slide 154
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
ChampSim
MQSim
Focus on
storage devices
[Tavakkol+ FAST 2018]
https://github.com/CMU-SAFARI/MQSim

## Slide 155: More Details in the Virtuoso Paper
- Detailed description of communication primitives
- Detailed description of MimicOS modules
- Integration methodology with different simulators
- Evaluation of intermediate address space schemes
- Evaluation of swapping activity and translation latency in hash-based address mapping schemes
- Evaluation of two additional hash-based page tables
https://arxiv.org/pdf/2403.04635

## Slide 156: Tools for Evaluating Memory and Memory-Centric Computing DRAM, Storage, Virtual Memory
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
22 March 2026
1st Ramulator & DRAM Bender Tutorial @ ASPLOS 2026

## Slide 157: Virtuoso
Konstantinos Kanellopoulos Konstantinos Sgouras F. Nisa Bostanci
Andreas Kosmas Kakolyris Berkin Kerim Konar Rahul Bera
Mohammad Sadrosadati Rakesh Kumar Nandita Vijaykumar Onur Mutlu
Enabling Fast and Accurate Virtual Memory Research with an Imitation-based Operating System Simulation Methodology
https://github.com/CMU-SAFARI/Virtuoso

## Slide 158
Co-design the hardware and the OS
to reduce VM overheads
Leverage VA-to-PA Contiguity
Software-managed TLB Subsystem
Accelerate Memory Allocation
Alternative Address Mappings
Rethinking the Page Table Design
Employing multiple page sizes
Wide range of hardware-OS co-design
techniques that aim to improve virtual memory

## Slide 159
Effectively evaluating VM techniques is crucial for progress in the domain

## Slide 160: Challenges in Evaluation
Interplay between system components
Hardware MMU
Software-level Memory Management
System Components

## Slide 161: Example: TLB and Memory Allocator
TLB
Memory Allocator
TLB performance heavily depends on the memory allocator (e.g., # of 2MB pages)

## Slide 162: Challenges in Evaluation
Hardware MMU
Software-level Memory Management
System Components
Evaluating the interplay between components is critical when assessing current and new VM techniques

## Slide 163: Existing Architectural Simulators
Emulation-based
Full-system
1
2
Two main classes of simulators

## Slide 164: Emulation-based Simulators
Ramulator
Sniper
ChampSim
Limited support for OS primitives
ZSim
Analytically estimate
VM Overheads
High simulation speed with a focus on modeling microarchitectural features

## Slide 165: Full-System Simulators
gem5-FS
QFlex
PTLsim
Enable the execution of a full-blown OS
on top of a hardware simulator
Low simulation speed
Hard to develop

## Slide 166: Existing Architectural Simulators
Emulation-based
Simulation Speed
Accuracy in Estimating VM overheads
Our goal
Full-System

## Slide 167: Enabling Fast and Accurate VM Research
New simulation framework that enables
fast and accurate prototyping and evaluation of
the software and hardware components of VM
Virtuoso

## Slide 168: Imitation-based Simulation Methodology
Lightweight Userspace Kernel
written in a high-level programming language
Choose OS modules only related
to the desired research
“I will try to imitate
the full-blown OS”

## Slide 169: Imitation-based Simulation Methodology
Full-blown Kernel
Thread Scheduler
Data Sharing Support
Managing NUMA
Virtual Memory Area Handling
Block device driver
Protection
Transparent Huge Pages
hugetlbfs
Cgroups
SLAB Allocator
Swapping
Interrupts
Monitoring
Boot process

## Slide 170: Imitation-based Simulation Methodology
Rapid development and prototyping
High simulation speed by executing
only the desired OS kernel functionality
Accurate evaluation by integrating
Virtuoso with an architectural simulator
1
2
3

## Slide 171: Imitation-based Simulation Methodology
add R1, R1 ,R2
load R1, [0xA]
Lightweight Userspace Kernel
Desired Memory Management modules written in a high-level language
Simulator
Binary Instrumentation
Core Model
Userspace Kernel Instruction Stream
+ Imitates the OS-level
Overhead

## Slide 172: Imitation-based Simulation Methodology
add R1, R1 ,R2
load R1, [0xA]
Lightweight Userspace Kernel
Desired Memory Management modules written in a high-level language
Simulator
Binary Instrumentation
Core Model
Userspace Kernel Instruction Stream
Functional Outcome
+ Enables emulation of kernel modules

## Slide 173: MimicOS: Imitating the Linux Kernel
MimicOS modules written in C++
Transparent Huge Pages
Buddy Allocator
Radix-based page table
hugetlbfs
Swap Space
Page Cache
More details in the paper
https://arxiv.org/pdf/2403.04635

## Slide 174: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based address mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing the HW/SW components
of multiple state-of-the-art VM techniques
Speculative Translation
TLB Prefetching

## Slide 175: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing multiple state-of-the-art VM techniques
Enables researchers to evaluate
and prototype current and
brand new VM techniques

## Slide 176: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing multiple state-of-the-art VM techniques
Virtuoso is a highly versatile
simulation framework

## Slide 177
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
System-call emulation
mode of gem5
http://gem5.org/
[Lowe-Power+ arXiv 2020]
[Binkert+ SIGARCH News 2011]

## Slide 178
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Focus on main memory subsystem
https://github.com/CMU-SAFARI/ramulator2
[Luo+ CAL 2023]

## Slide 179
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
Focus on
multicore systems
[Carlson+ TACO 2012]
https://github.com/snipersim/snipersim

## Slide 180
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
ChampSim
Focus on
microarchitecture
https://github.com/ChampSim/ChampSim
[Gober+ arXiv 2022]

## Slide 181
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
ChampSim
MQSim
Focus on
storage devices
[Tavakkol+ FAST 2018]
https://github.com/CMU-SAFARI/MQSim

## Slide 182: Virtuoso’s Versatility
We showcase Virtuoso’s
versatility by evaluating multiple
different use cases
5 use cases in the paper
https://arxiv.org/pdf/2403.04635
Demonstrate new insights on
state-of-the-art VM techniques

## Slide 183: Virtuoso Example Use Cases
Evaluating Different
Page Table Designs
Evaluating Physical Memory
Allocation Policies

## Slide 184: Evaluation Methodology
Buddy: Baseline allocator with the buddy system
Utopia:1 Part of memory is organized using a hash-based mapping
Workloads: Short-input Short-output LLM inference
[1] Kanellopoulos et al. “Utopia: Fast and Efficient Address Translation via Hybrid Restrictive & Flexible Virtual-to-Physical Address Mappings” MICRO 2023
Mistral-7B
Llama-2-7B
Bagel-2.8B

## Slide 185: Accelerating Memory Allocation
Chart: Physical Memory Allocation Speedup
| Llama-2-7B | Mistral-7B | Bagel-2.8B
Utopia - 32MB Hash-based Segment | 2.0419 | 2.179 | 2.1783
Restricting the virtual-to-physical mapping speeds up memory allocation by up to 2.17x

## Slide 186: More Details in the Paper
- Detailed description of communication primitives
- Detailed description of MimicOS modules
- Integration methodology with different simulators
- Integration with heterogeneous system simulation
- Evaluation of intermediate address space schemes
- Evaluation of swapping activity and translation latency in hash-based address mapping schemes
- Evaluation of two additional hash-based page tables
and more to come …

## Slide 187: More Details in the Paper
- Detailed description of communication primitives
- Detailed description of MimicOS modules
- Integration methodology with different simulators
- Evaluation of intermediate address space schemes
- Evaluation of swapping activity and translation latency in hash-based address mapping schemes
- Evaluation of two additional hash-based page tables
https://arxiv.org/pdf/2403.04635

## Slide 188: Virtuoso is Open-Source
https://github.com/CMU-SAFARI/Virtuoso

## Slide 189: Virtuoso Website – Getting Started
https://github.com/CMU-SAFARI/Virtuoso/website

## Slide 190: Virtuoso Website - Documentation
https://safari.ethz.ch/virtuoso

## Slide 191: Backup Slides

## Slide 192: Tradeoffs in Simulation
Three metrics to evaluate a simulator
  Speed
  Flexibility
  Accuracy
Speed: How fast the simulator runs (xIPS, xCPS, slowdown)
Flexibility: How quickly one can modify the simulator to evaluate different algorithms and design choices?
Accuracy: How accurate the performance (energy) numbers the simulator generates are vs. a real design (Simulation error)
The relative importance of these metrics varies depending on where you are in the design process (what your goal is)

## Slide 193: Trading Off Speed, Flexibility, Accuracy
Speed & flexibility affect:
  How quickly you can make design tradeoffs/decisions
Accuracy affects:
  How good your design tradeoffs/decisions might end up being
  How fast you can build your simulator (simulator design time)
Flexibility also affects:
  How much human effort you need to spend modifying the simulator
You can trade off between the three to achieve design exploration and decision goals

## Slide 194: Making The Best of Architecture
A good architect is comfortable at all levels of refinement
  Including the extremes
A good architect knows when to use what type of simulation
  And, more generally, what type of evaluation method
Recall: A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 195: An Example Study using Ramulator (I)
Saugata Ghose, Tianshi Li, Nastaran Hajinazar, Damla Senol Cali, and Onur Mutlu, "Demystifying Workload–DRAM Interactions: An Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Phoenix, AZ, USA, June 2019. [Preliminary arXiv Version] [Abstract] [Slides (pptx) (pdf)] [MemBen Benchmark Suite] [Source Code for GPGPUSim-Ramulator]

## Slide 196: Why Study Workload–DRAM Interactions?
Manufacturers are developing many new types of DRAM
  DRAM limits performance, energy improvements: new types may overcome some limitations
  Memory systems now serve a very diverse set of applications: can no longer take a one-size-fits-all approach
So which DRAM type works best with which application?
  Difficult to understand intuitively due to the complexity of the interaction
  Can’t be tested methodically on real systems: new type needs a new CPU
We perform a wide-ranging experimental study to uncover the combined behavior of workloads and DRAM types
  115 prevalent/emerging applications and multiprogrammed workloads
  9 modern DRAM types: DDR3, DDR4, GDDR5, HBM, HMC, LPDDR3, LPDDR4, Wide I/O, Wide I/O 2

## Slide 197: Modern DRAM Types: Comparison to DDR3
Bank groups
3D-stacked DRAM
DRAM Type | Banks per Rank | Bank Groups | 3D-Stacked | Low-Power
DDR3 | 8 |  |  | 
DDR4 | 16 |  |  | 
GDDR5 | 16 |  |  | 
HBM High-Bandwidth Memory | 16 |  |  | 
HMC Hybrid Memory Cube | 256 |  |  | 
Wide I/O | 4 |  |  | 
Wide I/O 2 | 8 |  |  | 
LPDDR3 | 8 |  |  | 
LPDDR4 | 16 |  |  | 
Memory Layers
high bandwidth with
Through-Silicon Vias (TSVs)
dedicated Logic Layer
DRAM Type | Banks per Rank | Bank Groups | 3D-Stacked | Low-Power
DDR3 | 8 |  |  | 
DDR4 | 16 |  |  | 
GDDR5 | 16 |  |  | 
HBM High-Bandwidth Memory | 16 |  |  | 
HMC Hybrid Memory Cube | 256 |  |  | 
Wide I/O | 4 |  |  | 
Wide I/O 2 | 8 |  |  | 
LPDDR3 | 8 |  |  | 
LPDDR4 | 16 |  |  | 
Bank Group
Bank Group
Bank
Bank
Bank
Bank
memory channel
increased latency
increased area/power
narrower rows, higher latency

## Slide 198: 4. Need for Lower Access Latency: Performance
New DRAM types often increase access latency in order to provide more banks, higher throughput
Many applications can’t make up for the increased latency
  Especially true of common OS routines (e.g., file I/O, process forking)
  A variety of desktop/scientific, server/cloud, GPGPU applications
Chart: Speedup
| shell (0.2) | bootup (1.1) | forkbench (49.5) | UDP_RR (0.1) | TCP_RR (0.1) | UDP_STREAM (0.1) | TCP_STREAM (0.1) | Test 4 (3.4) | Test 11 (4.5) | Test 10 (4.7) | Test 9 (4.7) | Test 8 (4.7) | Test 5 (10.1) | Test 3 (13.3) | Test 1 (13.6) | Test 7 (13.7) | Test 12 (15.4) | Test 2 (15.6) | Test 0 (15.7) | Test 6 (16.5)
DDR4 | 1.0002 | 0.999 | 0.9975 | 1 | 1 | 1 | 1 | 0.9952 | 0.9937 | 0.9935 | 0.9934 | 0.9932 | 1.0017 | 1.0083 | 1.008 | 1.0074 | 0.9938 | 0.999 | 0.994 | 0.9955
GDDR5 | 1.0033 | 1.0125 | 1.1306 | 1.0011 | 1.0012 | 1.0011 | 1.0011 | 1.0266 | 1.0329 | 1.0356 | 1.0347 | 1.0344 | 1.0577 | 1.0519 | 1.0523 | 1.0514 | 1.1046 | 1.103 | 1.1077 | 1.1242
HBM | 0.9958 | 1.0008 | 1.0849 | 0.9994 | 0.9993 | 0.999 | 0.9992 | 1.0135 | 1.0163 | 1.0206 | 1.0177 | 1.0179 | 0.9907 | 0.9679 | 0.9648 | 0.9657 | 1.1135 | 1.066 | 1.1202 | 1.1205
HMC | 0.989 | 0.9641 | 0.9721 | 0.9974 | 0.9975 | 0.9967 | 0.9966 | 1.0191 | 1.0233 | 1.03 | 1.0261 | 1.0255 | 0.8719 | 0.8633 | 0.8548 | 0.8607 | 0.981 | 0.941 | 0.9867 | 0.9811
Several applications don’t benefit from more parallelism

## Slide 199: Key Takeaways
DRAM latency remains a critical bottleneck for many applications
Bank parallelism is not fully utilized by a wide variety of our applications
Spatial locality continues to provide significant performance benefits if it is exploited by the memory subsystem
For some classes of applications, low-power memory can provide energy savings without sacrificing significant performance

## Slide 200: Conclusion
Manufacturers are developing many new types of DRAM
  DRAM limits performance, energy improvements: new types may overcome some limitations
  Memory systems now serve a very diverse set of applications: can no longer take a one-size-fits-all approach
  Difficult to intuitively determine which DRAM–workload pair works best
We perform a wide-ranging experimental study to uncover the combined behavior of workloads, DRAM types
  115 prevalent/emerging applications and multiprogrammed workloads
  9 modern DRAM types
12 key observations on DRAM–workload behavior
Open-source tools: https://github.com/CMU-SAFARI/ramulator
Full paper: https://arxiv.org/pdf/1902.07609

## Slide 201: For More Information…
Saugata Ghose, Tianshi Li, Nastaran Hajinazar, Damla Senol Cali, and Onur Mutlu, "Demystifying Workload–DRAM Interactions: An Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Phoenix, AZ, USA, June 2019. [Preliminary arXiv Version] [Abstract] [Slides (pptx) (pdf)] [MemBen Benchmark Suite] [Source Code for GPGPUSim-Ramulator]

## Slide 202: BlockHammer Study in 2021
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)

## Slide 203: Summary: BlockHammer
BlockHammer is the first work to practically enable throttling-based RowHammer mitigation
BlockHammer is implemented in the memory controller (no proprietary information of / no modifications to DRAM chips)
BlockHammer is both scalable with worsening RowHammer and compatible with commodity DRAM chips
BlockHammer is open-source along with six state-of-the-art mechanisms: https://github.com/CMU-SAFARI/BlockHammer
Source
Notes: In summary, BlockHammer is the first work to practically enable throttling-based RowHammer mitigation and [CLICK]
it is implemented solely in the memory controller without requiring proprietary information of or modifications to DRAM chips [CLICK]
It overcomes both scalability and compatibility challenges [CLICK]
To further aid future research and development, we make BlockHammer’s source code freely and openly available

## Slide 204: BlockHammer: Free & Open Source
https://github.com/CMU-SAFARI/BlockHammer

## Slide 205: Many Other Ideas Evaluated w/ Ramulator
https://www.youtube.com/watch?v=pJ3mdIvMOY4&list=PL5Q2soXY2Zi-cAls3cyauNzM7-74Eq31O&index=9

## Slide 206: Ramulator for Processing in Memory

## Slide 207: Simulation Infrastructure for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator-pim
  https://github.com/CMU-SAFARI/ramulator
  [Source Code for Ramulator-PIM]

## Slide 208: Ramulator for PIM
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira, Stefano Corda, Sander Stujik, Onur Mutlu, and Henk Corporaal, "NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning" Proceedings of the 56th Design Automation Conference (DAC), Las Vegas, NV, USA, June 2019. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code for Ramulator-PIM]

## Slide 209: Ramulator Project Course Exploration of Emerging Memory Systems (Spring/Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 210: What We Discussed Is Applicable to Simulation in Other Domains

## Slide 211: Agent-Based Simulation

## Slide 212: Introduction to Agent-Based Modeling: Modeling a Flock of Birds
Agent is a bird with the following attributes:
  position
  velocity
And three behaviors:
Ref: Craig Reynolds, 1987, https://doi.org/10.1145/37401.37406, Simulator: Thierry Escande https://github.com/tescande/boids.git
Separation
Alignment
Cohesion
Notes: To explain what ABM is, I want to start with an example that models swarm behavior as can be seen in this video.
In this example, the agent is a bird which has two attributes: a position and a velocity.
**CLICK** In the simplified 2D model on the right, birds are represented as a dot and are initially randomly distributed.
**CLICK** By default, these birds move straight ahead.
Craig Reynolds, in his 1987 article, distilled three bird behaviors.
Let's activate them one after the other and see what happens in the simulation.
**CLICK** First, the agents are avoiding collisions with nearby flock mates.
**CLICK** Second, birds align to the velocity vector of their neighbors
**CLICK** And third, birds try to stay close to each other.
We can observe that these three simple rules give rise to the natural swarm dynamics although we did not program them directly.
This phenomenon is called emergent behavior and describes that in ABM the whole is greater than the sum of its parts.
The other AB characteristic is local interaction, as we can see from the three behaviors.
Agents only interact with their immediate surrounding.

## Slide 213: Agent-Based Simulation is Versatile
Ref: Icons from Flaticon.com
Finance
Marketing
and more …
Ecology
Transport
Social Sciences
Medicine
Epidemiology
Biology
Notes: ABM is a very versatile approach and is used in many different domains as shown on this slide.
Modelers first define what an agent represents
This can be very different entities: birds, cells, persons, cars, traders.
And the behaviors which define their interactions
…

## Slide 214: Cell Sorting in BioDynaMo
Agent
  Spherical cell with type attribute (red and blue)
Behaviors
Substance secretion
Chemotaxis
Mechanical forces
Notes: Let's dive deeper by investigating a biological model to sort cells.
We start with a random distribution of two types of cells and want to obtain clusters of the same cell type at the end.
CLICK In this model, the agent represents a spherical cell.
CLICK Cells release a substance
CLICK move in the direction of high substance concentration,
CLICK and exert forces on each other when they collide

## Slide 215: BioDynamo Modeling Infrastructure
Lukas Breitwieser, Ahmad Hesam, Fons Rademakers, Juan Gómez Luna, and Onur Mutlu, "High-Performance and Scalable Agent-Based Simulation with BioDynaMo" Proceedings of the 28th ACM SIGPLAN Annual Symposium on Principles and Practice of Parallel Programming (PPoPP), Montreal, QC, Canada, February 2023. [arXiv version] [Slides (pdf) (web)] [BioDynamo Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at PPoPP 2023.
https://arxiv.org/pdf/2301.06984

## Slide 216: BioDynamo Modeling Infrastructure
Lukas Breitwieser, Ahmad Hesam, Jean de Montigny, Vasileios Vavourakis, Alexandros Iosif, Jack Jennings, Marcus Kaiser, Marco Manca, Alberto Di Meglio, Zaid Al-Ars, Fons Rademakers, Onur Mutlu, and Roman Bauer, "BioDynaMo: A General Platform for Scalable Agent-based Simulation" Bioinformatics, 16 September 2021. [Online link at Bioinformatics Journal] [Preprint in arXiv and bioRxiv, 5 February 2021] [bioRxiv preprint] [arXiv preprint] [BioDynaMo Source Code and Data]
https://people.inf.ethz.ch/omutlu/pub/biodynamo_scalable-agent-based-simulation_biorxiv21

## Slide 217: Case Study: COVID-19 Spread Modeling and Prediction

## Slide 218
https://arxiv.org/pdf/2102.03667.pdf

## Slide 219: COVID-19 Measures: Evaluation Methods
How do we assess how an idea will affect a target metric X?
A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling/estimation
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 220: Simulating & Predicting COVID-19 Spread
An architect is in part a dreamer, a creator
Simulation is a key tool of the architect
  Allows the evaluation & understanding of non-existent systems
Simulation enables
  The exploration of many dreams
  A reality check of the dreams
  Deciding which dream is better
Simulation also enables
  The ability to fool yourself with false dreams

## Slide 221: Simulating & Predicting COVID-19 Spread
https://arxiv.org/pdf/2102.03667.pdf

## Slide 222: Simulating & Predicting COVID-19 Spread
https://arxiv.org/pdf/2102.03667.pdf

## Slide 223: Predicting Effectiveness of Measures
Prediction
Real Outcome
https://mealser.github.io/COVIDHunter/index.html