## Slide 1: MASK: Redesigning the GPU Memory Hierarchy to Support Multi-Application Concurrency
Rachata Ausavarungnirun
Vance Miller Joshua Landgraf Saugata Ghose
Jayneel Gandhi Adwait Jog Christopher J. Rossbach Onur Mutlu

## Slide 2: Executive Summary
Problem: Address translation overheads limit the latency hiding capability of a GPU
Key Idea
Prioritize address translation requests over data requests
MASK: a GPU memory hierarchy that
  Reduces shared TLB contention
  Improves L2 cache utilization
  Reduces page walk latency
MASK improves system throughput by 57.8% on average
over state-of-the-art address translation mechanisms
Large performance loss vs. no translation
High contention at the shared TLB
Low L2 cache utilization
Notes: Add the intro to running multiple application before jumping right in.
Too micro level animation

## Slide 3: Outline
Executive Summary
Background, Key Challenges and Our Goal
MASK: A Translation-aware Memory Hierarchy
Evaluation
Conclusion
Notes: Add some spacing

## Slide 4: Why Share Discrete GPUs?
Enables multiple GPGPU applications to run concurrently
Better resource utilization
  An application often cannot utilize an entire GPU
  Different compute and bandwidth demands
Enables GPU sharing in the cloud
  Multiple users spatially share each GPU
Key requirement: fine-grained memory protection
Notes: GPU can benefit from sharing. For example, a cloud provider can increase GPU utilization by allowing multiple users to share the GPU. Applications with heterogeneous resource demand can be co-schedule and executed concurrently to maximize all the available GPU resources. For example, application that demands high compute units can concurrently share GPU resource with applications that demand high memory bandwidth.
However, to safely share GPU across multiple applications, the GPU needs to be able to provide memory protection, which can be enabled to virtual address translation.

## Slide 5: State-of-the-art Address Translation in GPUs
GPU Core
Private TLB
GPU Core
GPU Core
GPU Core
Shared TLB
Private TLB
Page Table Walkers
Page Table
(in main memory)
Private TLB
Private TLB
Private
Shared
App 1
App 2
Notes: In this example, the GPU contains four cores and is shared among two applications, app 1 and app 2. In this scenario, when the GPU want to load or store data, it first needs to translate the virtual address into the physical address. To do this, the page table walk walk the page table using the virtual address. This process incur multiple reads to the main memory, and is a high latency operation. To alleviate this performance penalty, modern processor, including the state-of-the-art GPU design employs a private translation lookaside buffer to reduce the latency of address translation. This TLB can include the private per-core TLB, as shown in this example, and a second level shared TLB. With these structures, the page table walker only need to translate addresses that miss in both private and the shared TLB. However, we found that as the GPU is shared across multiple applications, each application generates contention at the shared TLB, decreasing the effectiveness of these components.

## Slide 6: A TLB Miss Stalls Multiple Warps
GPU Core
Private TLB
GPU Core
GPU Core
GPU Core
Shared TLB
Private TLB
Page Table Walkers
Page Table
(in main memory)
Private TLB
Private TLB
Private
Shared
App 1
App 2
Stalled
Stalled
Data in a page is shared by many threads
All threads
access the same page
Notes: Make the warp lines bigger

## Slide 7: Multiple Page Walks Happen Together
GPU Core
Private TLB
GPU Core
GPU Core
GPU Core
Shared TLB
Private TLB
Page Table Walkers
Page Table
(in main memory)
Private TLB
Private TLB
Private
Shared
App 1
App 2
GPU’s parallelism creates parallel page walks
Stalled
Stalled
Stalled
Stalled
Data in a page is shared by many threads
All threads
access the same page
Notes: High number of concurrent walks
Get rid of the warp thingy
Stalled have different color

## Slide 8: Effect of Translation on Performance
Chart: 
| Average
PWCache | 0.544
SharedTLB | 0.62644
Ideal | 1
Normalized Performance
Notes: As a result, we found that the long latency page walk and the contention at the shared TLB leads to two phenomenon. First, because GPU execute instructions in a lockstep, each TLB miss stalls multiple warps, leading to significantly lower throughput. Furthermore, the high amount of parallelism generate high number of concurrent page walks. Both of these limits the latency hiding capability of the GPUs, leading to lower performance.
In our evaluation, we found that address translation leads to 45.6% performance degradation even with the state-of-the-art GPU MMU design. So, we would like to identify any inefficiency in order to reduce the overhead of address translation.

## Slide 9: Effect of Translation on Performance
Chart: 
| Average
PWCache | 0.544
SharedTLB | 0.62644
Ideal | 1
Normalized Performance
Notes: As a result, we found that the long latency page walk and the contention at the shared TLB leads to two phenomenon. First, because GPU execute instructions in a lockstep, each TLB miss stalls multiple warps, leading to significantly lower throughput. Furthermore, the high amount of parallelism generate high number of concurrent page walks. Both of these limits the latency hiding capability of the GPUs, leading to lower performance.
In our evaluation, we found that address translation leads to 45.6% performance degradation even with the state-of-the-art GPU MMU design. So, we would like to identify any inefficiency in order to reduce the overhead of address translation.

## Slide 10: Effect of Translation on Performance
What causes the large performance loss?
Chart: 
| Average
PWCache | 0.544
SharedTLB | 0.62644
Ideal | 1
37.4%
Normalized Performance
Notes: As a result, we found that the long latency page walk and the contention at the shared TLB leads to two phenomenon. First, because GPU execute instructions in a lockstep, each TLB miss stalls multiple warps, leading to significantly lower throughput. Furthermore, the high amount of parallelism generate high number of concurrent page walks. Both of these limits the latency hiding capability of the GPUs, leading to lower performance.
In our evaluation, we found that address translation leads to 45.6% performance degradation even with the state-of-the-art GPU MMU design. So, we would like to identify any inefficiency in order to reduce the overhead of address translation.

## Slide 11: Problem 1: Contention at the Shared TLB
Multiple GPU applications contend for the TLB
Chart: L2 TLB Miss Rate (Lower is Better)
| App 1 | App 2 | App 1 | App 2 | App 1 | App 2 | App 1 | App 2
Alone | 0.49324 | 0.39922 | 0.2974 | 0.034602 | 0.91176 | 0.39922 | 0.11742 | 0.64129
Shared | 0.6707 | 0.82203 | 0.42424 | 0.47649 | 0.9443 | 0.78015 | 0.41567 | 0.7585
3DS_HISTO
CONS_LPS
MUM_HISTO
RED_RAY
Notes: To further understand the performance overhead in more detail, we provide three key observations. First, we found that there is a significant amount of thrashing at the shared TLB when GPU is being shared across multiple applications. In this example, on the y-axis we show the TLB miss rate of each application pair assuming that it is running along on the GPU.

## Slide 12: Problem 1: Contention at the Shared TLB
Multiple GPU applications contend for the TLB
Chart: L2 TLB Miss Rate (Lower is Better)
| App 1 | App 2 | App 1 | App 2 | App 1 | App 2 | App 1 | App 2
Alone | 0.49324 | 0.39922 | 0.2974 | 0.034602 | 0.91176 | 0.39922 | 0.11742 | 0.64129
Shared | 0.6707 | 0.82203 | 0.42424 | 0.47649 | 0.9443 | 0.78015 | 0.41567 | 0.7585
3DS_HISTO
CONS_LPS
MUM_HISTO
RED_RAY
Contention at the shared TLB leads to lower performance
Notes: And this red bar shows the TLB miss rate of the application pair when the two applications are running together. As shown here, when multiple applications are sharing the shared L2 TLB, the TLB miss rate significantly increases, and each individual applications on all four pairs observe higher than 40% shared TLB miss rate. As you can see here, we found this shared TLB contention leads to significant trashing and causing unnecessary high number of page table walks.

## Slide 13: Problem 2: Thrashing at the L2 Cache
L2 cache can be used to reduce page walk latency
   Partial translation data can be cached
Thrashing Source 1: Parallel page walks
   Different address translation data evicts each other
Thrashing Source 2: GPU memory intensity
   Demand-fetched data evicts address translation data
L2 cache is ineffective at reducing page walk latency
Notes: If we have the data use the data, if not say thrashing from multiple page walk requests + normal data requests

## Slide 14: Observation: Address Translation Is Latency Sensitive
Multiple warps share data from a single page
Chart: Warps Stalled Per One TLB Miss
| 3DS | BFS2 | BLK | BP | CFD | CONS | FFT | FWT | GUPS | HISTO | HS | JPEG | LIB | LPS | LUD | LUH | MM | MUM | NN | NW | QTC | RAY | RED | SAD | SC | SCAN | SCP | SPMV | SRAD | TRD | Average
Warps Stalled Per TLB Entry | 4.9823 | 22.6714 | 2.0987 | 18.5 | 11.2548 | 8.4803 | 2.1604 | 20.1782 | 4.6016 | 2.7453 | 6.3464 | 2.918 | 2.2253 | 5.4585 | 4.4688 | 4.8093 | 8.7018 | 2.1074 | 5.426 | 1.3605 | 4.1473 | 3.6941 | 6.3519 | 1.2702 | 10.1084 | 17 | 4 | 2.184 | 33.2563 | 22.0693 | 8.1859
A single TLB miss causes 8 warps to stall on average
Notes: Say the average PER CORE

## Slide 15: Observation: Address Translation Is Latency Sensitive
Multiple warps share data from a single page
GPU’s parallelism causes multiple concurrent page walks
Chart: Concurrent Page Walks
| 3DS | BFS2 | BLK | BP | CFD | CONS | FFT | FWT | GUPS | HISTO | HS | JPEG | LIB | LPS | LUD | LUH | MM | MUM | NN | NW | QTC | RAY | RED | SAD | SC | SCAN | SCP | SPMV | SRAD | TRD | Average
Concurrent Page Walks | 4.127 | 26.153 | 1.7475 | 19.2579 | 17.6029 | 8.4803 | 2.9958 | 14.3853 | 4.1575 | 2.6093 | 6.2982 | 3.6873 | 1.798 | 4.8382 | 4.0156 | 6.605 | 10.3298 | 1.7541 | 5.3537 | 1.1946 | 6.4307 | 3.6941 | 6.6449 | 1.2017 | 11.2975 | 2 | 2 | 2.1134 | 22.1317 | 17.2586 | 7.4055
High address translation latency  More stalled warps
Notes: Say the average

## Slide 16: Our Goals
Reduce shared TLB contention
Improve L2 cache utilization
Lower page walk latency
Notes: To this end, our design goal are the following: we would like to be able to achieve high TLB reach with low demand paging latency. In addition, we want our design our mechanism to be application-transparent such that programmers do not need to modify GPGPU applications to take advantage of our design.

## Slide 17: Outline
Executive Summary
Background, Key Challenges and Our Goal
MASK: A Translation-aware Memory Hierarchy
Evaluation
Conclusion
Notes: But in order to achieve the best of both large and small pages, we first present key challenges and our design goal

## Slide 18: MASK: A Translation-aware Memory Hierarchy
Reduce shared TLB contention
  A. TLB-fill Tokens
Improve L2 cache utilization
  B. Translation-aware L2 Bypass
Lower page walk latency
  C. Address-space-aware Memory Scheduler
Notes: To this end, our design goal are the following: we would like to be able to achieve high TLB reach with low demand paging latency. In addition, we want our design our mechanism to be application-transparent such that programmers do not need to modify GPGPU applications to take advantage of our design.

## Slide 19: A: TLB-fill Tokens
Goal: Limit the number of warps that can fill the TLB
   A warp with a token fills the shared TLB
   A warp with no token fills a very small bypass cache
Number of tokens changes based on TLB miss rate
   Updated every epoch
Tokens are assigned based on warp ID
Benefit: Limits contention at the shared TLB
Notes: We limit the Prioritizing warps with a token

## Slide 20: MASK: A Translation-aware Memory Hierarchy
Reduce shared TLB contention
  A. TLB-fill Tokens
Improve L2 cache utilization
  B. Translation-aware L2 Bypass
Lower page walk latency
  C. Address-space-aware Memory Scheduler
Notes: To this end, our design goal are the following: we would like to be able to achieve high TLB reach with low demand paging latency. In addition, we want our design our mechanism to be application-transparent such that programmers do not need to modify GPGPU applications to take advantage of our design.

## Slide 21: B: Translation-aware L2 Bypass
L2 hit rate decreases for deep page walk levels
Chart: 
| Average
Page Table Level 4 | 0.010457
Page Table Level 3 | 0.68671
Page Table Level 2 | 0.98876
Page Table Level 1 | 0.99842
L2 Cache Hit Rate
Page Table Level 1
Notes: Put in the radix tree
Make it horizontal. Use it for the graph of the next slide, show what is cached and what is bypassed
Move the title down to the first bullet and keep the title

## Slide 22: B: Translation-aware L2 Bypass
L2 hit rate decreases for deep page walk levels
Chart: 
| Average
Page Table Level 4 | 0.010457
Page Table Level 3 | 0.68671
Page Table Level 2 | 0.98876
Page Table Level 1 | 0.99842
L2 Cache Hit Rate
Page Table Level 1
Page Table Level 2
Notes: Put in the radix tree
Make it horizontal. Use it for the graph of the next slide, show what is cached and what is bypassed
Move the title down to the first bullet and keep the title

## Slide 23: B: Translation-aware L2 Bypass
L2 hit rate decreases for deep page walk levels
Chart: 
| Average
Page Table Level 4 | 0.010457
Page Table Level 3 | 0.68671
Page Table Level 2 | 0.98876
Page Table Level 1 | 0.99842
L2 Cache Hit Rate
Page Table Level 1
Page Table Level 2
Page Table Level 3
Notes: Put in the radix tree
Make it horizontal. Use it for the graph of the next slide, show what is cached and what is bypassed
Move the title down to the first bullet and keep the title

## Slide 24: B: Translation-aware L2 Bypass
L2 hit rate decreases for deep page walk levels
Some address translation data does not benefit from caching
Only cache address translation data with high hit rate
Chart: 
| Average
Page Table Level 4 | 0.010457
Page Table Level 3 | 0.68671
Page Table Level 2 | 0.98876
Page Table Level 1 | 0.99842
L2 Cache Hit Rate
Page Table Level 1
Page Table Level 2
Page Table Level 3
Page Table Level 4
Notes: Put in the radix tree
Make it horizontal. Use it for the graph of the next slide, show what is cached and what is bypassed
Move the title down to the first bullet and keep the title

## Slide 25: B: Translation-aware L2 Bypass
Cache
Chart: 
| Average
Page Table Level 4 | 0.010457
Page Table Level 3 | 0.68671
Page Table Level 2 | 0.98876
Page Table Level 1 | 0.99842
Goal: Cache address translation data with high hit rate
L2 Cache Hit Rate
Page Table Level 1
Page Table Level 2
Page Table Level 3
Page Table Level 4
Bypass
Benefit 1: Better L2 cache utilization for translation data
Benefit 2: Bypassed requests  No L2 queuing delay
Average L2 Cache Hit Rate
Notes: Make it horizontal. Use it for the graph of the next slide, show what is cached and what is bypassed
Banner: Same width

## Slide 26: MASK: A Translation-aware Memory Hierarchy
Reduce shared TLB contention
  A. TLB-fill Tokens
Improve L2 cache utilization
  B. Translation-aware L2 Bypass
Lower page walk latency
  C. Address-space-aware Memory Scheduler
Notes: To this end, our design goal are the following: we would like to be able to achieve high TLB reach with low demand paging latency. In addition, we want our design our mechanism to be application-transparent such that programmers do not need to modify GPGPU applications to take advantage of our design.

## Slide 27: C: Address-space-aware Memory Scheduler
Cause: Address translation requests are treated similarly to data demand requests
Idea: Lower address translation request latency
Chart: DRAM Latency
| Average
Address Translation Requests | 297.9283
Data Demand Requests | 268.3416
Chart: DRAM Bandwidth
| Average
Address Translation Requests | 0.040258
Data Demand Requests | 0.23168
Address Translation Requests
Data Demand Requests

## Slide 28: C: Address-space-aware Memory Scheduler
Idea 1: Prioritize address translation requests over data demand requests
To
DRAM
Memory Scheduler
Golden Queue
Address Translation Request
Normal Queue
Data Demand Request
High Priority
Low Priority
Notes: This one should not have the silver queue
Double check the term

## Slide 29: C: Address-space-aware Memory Scheduler
Idea 1: Prioritize address translation requests over data demand requests
Idea 2: Improve quality-of-service using the Silver Queue
To
DRAM
Memory Scheduler
Golden Queue
Address Translation Request
Silver Queue
Data Demand Request
(Applications take turns)
Normal Queue
Data Demand Request
High Priority
Low Priority
Each application takes turn injecting into the Silver Queue
Notes: Motion path for blue (if have time)

## Slide 30: Outline
Executive summary
Background, Key Challenges and Our Goal
MASK: A Translation-aware Memory Hierarchy
Evaluation
Conclusion
Notes: But in order to achieve the best of both large and small pages, we first present key challenges and our design goal

## Slide 31: Methodology
Mosaic simulation platform [MICRO ’17]
  - Based on GPGPU-Sim and MAFIA [Jog et al., MEMSYS ’15]
  - Models page walks and virtual-to-physical mapping
  - Available at https://github.com/CMU-SAFARI/Mosaic
NVIDIA GTX750 Ti
Two GPGPU applications execute concurrently
CUDA-SDK, Rodinia, Parboil, LULESH, SHOC suites
  - 3 workload categories based on TLB miss rate
Notes: We uses a modified version GPGPU-sim, which models a 30-core GTX750 Ti. We allows multiple GPGPU applications to be executed concurrently. Our infrastructure models the page table walk, page table as well as the virtual to physical mapping. We evaluate our framework using various benchmark suite and in total we run 235 workloads. Our framework is publicly available on Github.

## Slide 32: Comparison Points
State-of-the-art CPU–GPU memory management [Power et al., HPCA ’14]
   PWCache: Page Walk Cache GPU MMU design
   SharedTLB: Shared TLB GPU MMU design
Ideal: Every TLB access is an L1 TLB hit
Notes: We compare Mosaic to two designs. The first baseline is the state-of-the-art CPU-GPU memory management proposed by Power et al in HPCA 2014. We call this baseline GPU-MMU. We also compare our mechanism against the Ideal TLB baseline with every single TLB access is a TLB hit.

## Slide 33: Performance
Chart: Normalized Performance
| 0-HMR | 1-HMR | 2-HMR | Average
PWCache | 0.9133 | 0.83403 | 0.8746 | 0.86255
SharedTLB | 1 | 1 | 1 | 1
MASK | 1.5875 | 1.6168 | 1.5196 | 1.5784
Ideal | 2.2592 | 2.1024 | 1.8765 | 2.0534
57.8%
52.0%
61.2%
58.7%
MASK outperforms state-of-the-art design for every workload
Notes: We compare Mosaic to two baselines. The first baseline is the state-of-the-art CPU-GPU memory management proposed by Power et al in HPCA 2014. We call this baseline GPU-MMU. We also compare our mechanism against the Ideal TLB baseline with every single TLB access is a TLB hit.

## Slide 34: Other Results in the Paper
MASK reduces unfairness
Effectiveness of each individual component
  All three MASK components are effective
Sensitivity analysis over multiple GPU architectures
  MASK improves performance on all evaluated architectures, including CPU–GPU heterogeneous systems
Sensitivity analysis to different TLB sizes
  MASK improves performance on all evaluated sizes
Performance improvement over different memory scheduling policies
  MASK improves performance over other state-of-the-art memory schedulers

## Slide 35: Conclusion
Problem: Address translation overheads limit the latency hiding capability of a GPU
Key Idea
Prioritize address translation requests over data requests
MASK: a translation-aware GPU memory hierarchy
  TLB-fill Tokens reduces shared TLB contention
  Translation-aware L2 Bypass improves L2 cache utilization
  Address-space-aware Memory Scheduler reduces page walk latency
MASK improves system throughput by 57.8% on average
over state-of-the-art address translation mechanisms
Large performance loss vs. no translation
High contention at the shared TLB
Low L2 cache utilization
Notes: Add the intro to running multiple application before jumping right in.
Too micro level animation

## Slide 36: MASK: Redesigning the GPU Memory Hierarchy to Support Multi-Application Concurrency
Rachata Ausavarungnirun
Vance Miller Joshua Landgraf Saugata Ghose
Jayneel Gandhi Adwait Jog Christopher J. Rossbach Onur Mutlu
Notes: At the end: Thank you. I am happy to take any questions.