## Slide 1: Reducing Solid-State Drive Read Latency by Optimizing Read-Retry
Jisung Park1, Myungsuk Kim2, Myoungjun Chun2, Lois Orosa1, Jihong Kim2, and Onur Mutlu1
ASPLOS 2021 (Session 17: Solid State Drives)
1
2

## Slide 2: Executive Summary
Problem: Long read latency in modern SSDs due to read-retry
  Frequently requires multiple retry steps to read an erroneous page
Goal: Reduce the latency of each read-retry operation
Key Ideas:
  Pipelined Read-Retry (PR2): Concurrently perform consecutive retry steps using the CACHE READ command
  Adaptive Read-Retry (AR2): Reduce read-timing parameters for every retry step by exploiting the reliability margin provided by strong ECC
  Small implementation overhead and no changes to NAND flash chips
Evaluation Results: Our proposal improves SSD response time by
  Up to 51% (35% on average) compared to a high-end SSD
  Up to 32% (17% on average) compared to a state-of-the-art baseline

## Slide 3: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 4: NAND Flash Basics
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
Read-Reference Voltage
NAND flash memory stores data by using cells’ VTH values

## Slide 5: NAND Flash Basics
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
NAND flash memory stores data by using cells’ VTH values
VTH < VREF
VTH > VREF
V
REFx

## Slide 6: NAND Flash Basics
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
NAND flash memory stores data by using cells’ VTH values
V
REFx

## Slide 7: NAND Flash Basics
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-2)
V
REF(x+1)
NAND flash memory stores data by using cells’ VTH values
V
REF(x-1)
V
REFx
VTH < VREF
VTH > VREF
Cell’s Threshold Voltage ( )
V
TH

## Slide 8: Errors in NAND Flash Memory
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
Various sources shift and widen programmed VTH states
  Retention loss, program interference, read disturbance, etc.
Retention loss
Interference/disturbance
Modern NAND flash memory is highly error-prone due to narrow VTH margins
Erroneous cells

## Slide 9: Error-Correcting Codes (ECC)
Store redundant information (ECC parity) for error correction
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Read Page 0

## Slide 10: Error-Correcting Codes (ECC)
Store redundant information (ECC parity) for error correction
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Corrected data
# of raw bit errors > ECC correction capability  Uncorrectable errors in stored data

## Slide 11: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
Erroneous cells

## Slide 12: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
V’
REF(x-2)
V’
REF(x-1)
V’
REFx
V’
REF(x+1)
Erroneous cells
Read using properly-adjusted VREF values
 Decreases # of raw bit errors
Read-retry: Adjusting VREF values

## Slide 13: Read-Retry: Performance Overhead
NERR = 32
< ECC capability CECC = 72
READ A
tREAD
tR: Page sensing
tDMA: Data transfer
tECC: ECC decoding

## Slide 14: Read-Retry: Performance Overhead
tR
tDMA
tECC
ECC Capability CECC= 72
Read-retry increases the read latency
almost linearly with the number of retry steps
READ A
NERR= 232
tREAD
RR1
NERR= 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2

## Slide 15: Read-Retry in Modern SSDs: Experimental Data
Characterization of 160 real 3D TLC NAND flash chips
  ECC correction capability: 72 bits per 1-KiB data
 | 0 P/E cycles |  |  |  |  | 1K P/E cycles |  |  |  |  | 2K P/E cycles |  |  |  | 
 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12
5
10
15
20
25
Retention age [months]
0
# of retry steps
Probability
0
1
0.2
0.4
0.6
0.8
max.
avg.
min.
Elapsed time since the page was programmed
~40%

## Slide 16: Read-Retry in Modern SSDs: Experimental Data
Characterization of 160 real 3D TLC NAND flash chips
  ECC correction capability: 72 bits per 1-KiB data
 | 0 P/E cycles |  |  |  |  | 1K P/E cycles |  |  |  |  | 2K P/E cycles |  |  |  | 
 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12
5
10
15
20
25
Retention age [months]
0
# of retry steps
Probability
0
1
0.2
0.4
0.6
0.8
max.
avg.
min.
Up to 25
High P/E cycles and long retention age  More retry steps per read

## Slide 17: Read-Retry in Modern SSDs: Experimental Data
Characterization of 160 real 3D TLC NAND flash chips
  ECC correction capability: 72 bits per 1-KiB data
 | 0 P/E cycles |  |  |  |  | 1K P/E cycles |  |  |  |  | 2K P/E cycles |  |  |  | 
 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12 | 0 | 3 | 6 | 9 | 12
5
10
15
20
25
Retention age [months]
0
# of retry steps
Probability
0
1
0.2
0.4
0.6
0.8
max.
avg.
min.
Many reads require multiple retry steps even under modest operating conditions
100%
3

## Slide 18: Existing Read-Retry Mitigation Schemes
Px state
P(x+1) state
V
OPT
V
REFx
Read retry: Adjusting VREF
…
Probability
density
Px state
P(x-1) state
After retention loss
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Right after programming
Try to reduce NRR by predicting near-optimal VREF values
V
RRN
V
RR1
…
V
RR(N-1)
…
Gradually adjusting

## Slide 19: Existing Read-Retry Mitigation Schemes
Px state
P(x+1) state
V
OPT
V
REFx
Read retry: Adjusting VREF
…
Probability
density
Px state
P(x-1) state
After retention loss
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Right after programming
Try to reduce NRR by predicting near-optimal VREF values
V
RRN
Prediction using error models
Skip unnecessary
retry steps
VTH changes are fast and large in modern SSDs  Hard to eliminate read-retry
V
RR1
…
V
RR(N-1)
…

## Slide 20: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 21: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
tRETRY
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps

## Slide 22: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
tRETRY
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
CACHE READ

## Slide 23: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
CACHE READ
tRETRY’
= N×tR+tDMA+tECC
Latency reduction
PR2: Removes tDMA & tECC (~30% of each retry step) from the critical path

## Slide 24: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
tRETRY’
= N×tR+tDMA+tECC
Latency reduction

## Slide 25: PR2: Pipelined Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
⋯
⋯
READ A
NERR= 232
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
RRN
tREAD
NERR= 23
tRETRY’
= N×tR+tDMA+tECC
Latency reduction
RR(N+1)
Unnecessarily started
ECC Capability CECC= 72

## Slide 26: PR2: Pipelined Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
tRETRY’
= N×tR+tDMA+tECC
Latency reduction
RR(N+1)
RESET
ECC Capability CECC= 72
NERR= 23
Unnecessarily started

## Slide 27: PR2: Pipelined Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
tRETRY’
= N×tR+tDMA+tECC
Latency reduction
RR(N+1)
RESET
ECC Capability CECC= 72
NERR= 23
Unnecessarily started
PR2: Large latency reduction (~30%) w/ negligible performance penalty

## Slide 28: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 29: AR2: Adaptive Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
tRETRY’
= N×tR+tDMA+tECC
NERR= 23

## Slide 30: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
tRETRY’
= N×tR+tDMA+tECC
NERR= 23
ECC Capability CECC= 72
Observation: A positive ECC margin in the final retry step when read-retry succeeds

## Slide 31: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
tRETRY’
= N×tR+tDMA+tECC
NERR= 23
ECC Capability CECC= 72
Shorter tR

## Slide 32: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
NERR= 23
ECC Capability CECC= 72
tRETRY’
= N×ρ×tR+tDMA+tECC
Latency reduction
Shorter tR

## Slide 33: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
NERR= 23
ECC Capability CECC= 72
tRETRY’
= N×ρ×tR+tDMA+tECC
+α
+α
+α
+α
+α
(additional errors)
Latency reduction
Needs to ensure that # of additional errors < ECC margin
Shorter tR

## Slide 34: AR2: Necessary Conditions
Condition 1: Large ECC margin in the final retry step
  Strong ECC: 72 bits correctable per 1-KiB data
  Use of near-optimal VREF in the final retry step
    # of raw bit errors drastically increases if VREF >> VOPT
    ∴ In the final retry step, VRRN ~ VOPT
Condition 2: Sufficient reliability margin in read-timing parameters
  Manufacturers pessimistically set read-timing parameters
  To cover for worst-case process variation and operating conditions
We experimentally analyze if these conditions hold

## Slide 35: AR2: Real-Device Characterization
Goals: Rigorously characterize
  The ECC margin in the final retry step
  Reliability impact of reducing read-timing parameters
  Under different operating conditions
Methodology
  160 real chips (48WL-layer 3D TLC NAND memory)
  Randomly selected 11,059,200 pages
  FPGA-based custom flash controller
    Basic commands + test-mode commands (e.g., changing VREF values and read-timing parameters)

## Slide 36: AR2: ECC Margin in the Final Retry Step
0
1K
2K
P/E cycles:
Chart: 
| 0 | 3 | 6 | 9 | 12
0K | 7 | 15 | 20 | 23 | 26
1K | 10 | 19 | 26 | 28 | 30
2K | 15 | 25 | 31 | 33 | 35
ECC capability = 72 bits per 1 KiB
Retention age [months]
Max. # of errors per 1-KiB data
ECC margin
Large ECC margin in the final retry step
even under worst-case operating conditions
Smaller ECC margin at higher P/E cycles and longer retention age

## Slide 37: AR2: Effect of Reducing Timing Parameters
Chart: 
| 1 | 0.9 | 0.85 | 0.8 | 0.7 | 0.65 | 0.6 | 0.5 | 0.45 | 0.4
(0, 6) | 0 | 0 | 0 | 1 | 3 | 6 | 10 | 19 | 30 | 51
(0, 12) | 0 | 0 | 1 | 2 | 4 | 7 | 13 | 22 | 35 | 56
(2, 0) | 0 | 0 | 1 | 3 | 5 | 11 | 17 | 24 | 37 | 59
(2, 12) | 0 | 0 | 2 | 5 | 9 | 15 | 23 | 35 | 51 | 77
Reduction in page-sensing latency (ΔtR)
P/E Cycles:
0
2K
[months]:
0
12
t
RET
0%
Safe reduction point @ PEC=2K, tRET =12
Safe reduction point @ PEC=0K, tRET =0
60% increase
Max. increase in errors per 1-KiB data @ 85°C
Considerable variation depending on operating conditions
12.5%
25%
37.5%
Large reliability margin in read-timing parameters
 25% tR reduction under worst-case conditions

## Slide 38: AR2: Effect of Reducing Timing Parameters
Chart: 
| 1 | 0.9 | 0.85 | 0.8 | 0.7 | 0.65 | 0.6 | 0.5 | 0.45 | 0.4
(0, 6) | 0 | 0 | 0 | 1 | 3 | 6 | 10 | 19 | 30 | 51
(0, 12) | 0 | 0 | 1 | 2 | 4 | 7 | 13 | 22 | 35 | 56
(2, 0) | 0 | 0 | 1 | 3 | 5 | 11 | 17 | 24 | 37 | 59
(2, 12) | 0 | 0 | 2 | 5 | 9 | 15 | 23 | 35 | 51 | 77
Reduction in page-sensing latency (ΔtR)
P/E Cycles:
0
2K
[months]:
0
12
t
RET
0%
Safe reduction point @ PEC=2K, tRET =12
Safe reduction point @ PEC=0K, tRET =0
60% increase
Max. increase in errors per 1-KiB data @ 85°C
Considerable variation depending on operating conditions
12.5%
25%
37.5%
Large reliability margin in read-timing parameters
 25% tR reduction even under worst cases
AR2 Device-Characterization Takeaways
AR2 can easily work in state-of-the-art NAND flash chips
Must properly reduce tR depending on the current operating conditions

## Slide 39: Pipelined & Adaptive Read-Retry
PEC | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
⋯
⋯
Read–timing Parameter Table
⋯
⋯
⋯
⋯
⋯
❺ SET FEATURE
tRETRY
ECC success
❹ RESET
tRST
Best tR
PAGE READ(A)
Best tR
❶
tDMA
tECC
tR
ECC fail
❷ SET FEATURE
⋯
CACHE READ(A)
❸
No change to chips and no impact on VTH states
 Easy to combine with other techniques
Current conditions

## Slide 40: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 41: Evaluation Methodology
Simulator: MQSim [Tavakkol, FAST18]
  Extend NAND flash models w/ real-device characterization results
Workload: 12 real-world I/O workloads
  6 from Microsoft Research Cambridge (MSRC) traces
    2 write-dominant: stg-0, hm-0
    4 read-dominant: prn-1, proj-1, mds-1, usr-1
  6 from Yahoo! Cloud Service Benchmark (YCSB)
Baselines
  IDEAL: An ideal SSD where no read-retry occurs
  BASE: A high-end SSD w/o read-retry mitigation
  SOTA: A state-of-the-art read-retry mitigation scheme [Shim, MICRO19]
    Reduces the average number of retry steps by 70%
    By predicting VREF values close to the optimal values

## Slide 42: Results: PR2+AR2 Performance
Chart: 
| MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB
PnAR2 | 0.90486 | 0.72048 | 0.91362 | 0.82275 | 0.63462 | 0.73785 | 0.70165 | 0.5786 | 0.68143
STOA | 0.9053 | 0.53765 | 0.72299 | 0.77523 | 0.41031 | 0.57549 | 0.53199 | 0.34396 | 0.48271
STOA+PnAR2 | 0.89456 | 0.46064 | 0.68344 | 0.75447 | 0.31073 | 0.50284 | 0.48636 | 0.24541 | 0.40128
IDEAL | 0.86896 | 0.29821 | 0.58691 | 0.71841 | 0.14856 | 0.37684 | 0.40862 | 0.0951 | 0.26904
SSD response time
(Normalized to BASE)
3-month retention @ 0 P/E cycles
3-month retention @ 1K P/E cycles
6-month retention @ 2K P/E cycles
PnAR2
-9.5%
-28%
-8.6%
-17.7%
-36.5%
-26.2%
-29.8%
-42.1%
-31.9%
Large response time improvement:
Up to 42% (26% on average)
Considerable improvement in write-dominant workloads due to garbage-collection reads

## Slide 43: Results: SOTA & Optimal Performance
Chart: 
| MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB
PnAR2 | 0.90486 | 0.72048 | 0.91362 | 0.82275 | 0.63462 | 0.73785 | 0.70165 | 0.5786 | 0.68143
STOA | 0.9053 | 0.53765 | 0.72299 | 0.77523 | 0.41031 | 0.57549 | 0.53199 | 0.34396 | 0.48271
STOA+PnAR2 | 0.89456 | 0.46064 | 0.68344 | 0.75447 | 0.31073 | 0.50284 | 0.48636 | 0.24541 | 0.40128
IDEAL | 0.86896 | 0.29821 | 0.58691 | 0.71841 | 0.14856 | 0.37684 | 0.40862 | 0.0951 | 0.26904
SSD response time
(Normalized to BASE)
3-month retention @ 0 P/E cycles
3-month retention @ 1K P/E cycles
6-month retention @ 2K P/E cycles
PnAR2
SOTA

## Slide 44: Results: SOTA & Optimal Performance
Chart: 
| MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB
PnAR2 | 0.90486 | 0.72048 | 0.91362 | 0.82275 | 0.63462 | 0.73785 | 0.70165 | 0.5786 | 0.68143
STOA | 0.9053 | 0.53765 | 0.72299 | 0.77523 | 0.41031 | 0.57549 | 0.53199 | 0.34396 | 0.48271
STOA+PnAR2 | 0.89456 | 0.46064 | 0.68344 | 0.75447 | 0.31073 | 0.50284 | 0.48636 | 0.24541 | 0.40128
IDEAL | 0.86896 | 0.29821 | 0.58691 | 0.71841 | 0.14856 | 0.37684 | 0.40862 | 0.0951 | 0.26904
SSD response time
(Normalized to BASE)
3-month retention @ 0 P/E cycles
3-month retention @ 1K P/E cycles
6-month retention @ 2K P/E cycles
PnAR2
SOTA
IDEAL
+4%
+80%
+23%
+8%
+176%
+53%
+30%
+262%
+79%
SOTA has large gap from ideal SSD

## Slide 45: Evaluation Results: SSD Response Time
Chart: 
| MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB | MSR-W | MSR-R | YCSB
PnAR2 | 0.90486 | 0.72048 | 0.91362 | 0.82275 | 0.63462 | 0.73785 | 0.70165 | 0.5786 | 0.68143
STOA | 0.9053 | 0.53765 | 0.72299 | 0.77523 | 0.41031 | 0.57549 | 0.53199 | 0.34396 | 0.48271
STOA+PnAR2 | 0.89456 | 0.46064 | 0.68344 | 0.75447 | 0.31073 | 0.50284 | 0.48636 | 0.24541 | 0.40128
IDEAL | 0.86896 | 0.29821 | 0.58691 | 0.71841 | 0.14856 | 0.37684 | 0.40862 | 0.0951 | 0.26904
SSD response time
(Normalized to BASE)
3-month retention @ 0 P/E cycles
3-month retention @ 1K P/E cycles
6-month retention @ 2K P/E cycles
PnAR2
SOTA
IDEAL
SOTA+PnAR2
-1%
-14%
-5%
-3%
-24%
-13%
-9%
-29%
-17%
Up to 29% performance improvement
when combined with SOTA

## Slide 46: Other Analyses in the Paper
Thorough analysis of read mechanism in modern SSDs
More detailed results from real-device characterization
  Effect of reducing individual read-timing parameters
  Effect of reducing multiple read-timing parameters
  Effect of operating temperature
  How to choose the best read-timing paratmers
Detailed evaluation of PR2 and AR2 when applied individually
Discussion of future directions to reduce SSD read latency

## Slide 47: Executive Summary
Problem: Long read latency in modern SSDs due to read-retry
  Frequently requires multiple retry steps to read an erroneous page
Key Ideas:
  Pipelined Read-Retry (PR2): Concurrently perform consecutive retry steps using the CACHE READ command
  Adaptive Read-Retry (AR2): Reduce read-timing parameters for every retry step by exploiting the reliability margin provided by strong ECC
Evaluation Results: Our proposal improves SSD response time by
  Up to 51% (35% on average) compared to a high-end SSD
  Up to 32% (17% on average) compared to a state-of-the-art baseline
We hope that our key idea and characterization results inspire many valuable studies going forward

## Slide 48: Reducing Solid-State Drive Read Latency by Optimizing Read-Retry
Jisung Park1, Myungsuk Kim2, Myoungjun Chun2, Lois Orosa1, Jihong Kim2, and Onur Mutlu1
ASPLOS 2021 (Session 17: Solid State Drives)
1
2