## Slide 1: Evaluating Homomorphic Operations on a Real-World Processing-In-Memory System
Harshita Gupta* Mayank Kabra*
Juan Gómez-Luna Konstantinos Kanellopoulos
Onur Mutlu

## Slide 2: Homomorphic Encryption
2

## Slide 3: Homomorphic Encryption
User
Data
Host System
Encrypted data
Encrypts data
3

## Slide 4: Homomorphic Encryption
User
Data
Host System
Encrypted data
Central/Cloud Server
Performs operations on the encrypted data without decrypting it
Encrypted data
Encrypts data
4

## Slide 5: Homomorphic Encryption
Central/Cloud Server
Performs operations on the encrypted data without decrypting it.
Encrypted data
Encrypted result
Decrypts result
Result
5
User
Data
Host System
Encrypted data
Encrypts data

## Slide 6: Motivation
Homomorphic operations suffer from
large memory capacity and data movement bottlenecks
Acceleration Techniques

## Slide 7: Motivation
Acceleration Techniques
These approaches face challenges in resource limitations, data movement, and practical implementation

## Slide 8: Our Goal
Evaluate the suitability of real-world general-purpose processing-in-memory (PIM) architectures to perform homomorphic operations.

## Slide 9: Our Goal
Evaluate the suitability of real-world general-purpose processing-in-memory (PIM) architectures to perform homomorphic operations.
UPMEM: First Real World PIM Architecture

## Slide 10: Our Goal
Evaluate the suitability of real-world general-purpose processing-in-memory (PIM) architectures to perform homomorphic operations.
UPMEM: First Real World PIM Architecture

## Slide 11
Evaluation of homomorphic addition and multiplication on UPMEM PIM system
1
Evaluation Methodology​
11

## Slide 12
Evaluation of homomorphic addition and multiplication on UPMEM PIM system
1
Evaluation with statistical workloads
(mean, variance, linear regression)
2
Evaluation Methodology​

## Slide 13
Evaluation of homomorphic addition and multiplication on UPMEM PIM system
1
Comparison with custom CPU and GPU libraries
and an optimized CPU library (SEAL)
3
Evaluation with statistical workloads
(mean, variance, linear regression)
2
Evaluation Methodology​

## Slide 14
Evaluation: Homomorphic Addition
Chart: Number of Ciphertexts
| 20480 | 40960 | 81920 | 163840 | 327680
CPU | 807.636 | 1627.494 | 3287.24 | 6505.403 | 12986.554
PIM | 37.71 | 58.86 | 123.84 | 258.79 | 536.33
CPU-SEAL | 565.438 | 1268.146 | 2156.795 | 5359.329 | 8609.573
GPU | 82.685 | 165.508 | 331.025 | 660.508 | 1309.579

## Slide 15
Evaluation: Homomorphic Addition
50 − 100× speedup provided by PIM over CPU
2 − 15× speedup over GPU
Chart: Number of Ciphertexts
| 20480 | 40960 | 81920 | 163840 | 327680
CPU | 807.636 | 1627.494 | 3287.24 | 6505.403 | 12986.554
PIM | 37.71 | 58.86 | 123.84 | 258.79 | 536.33
CPU-SEAL | 565.438 | 1268.146 | 2156.795 | 5359.329 | 8609.573
GPU | 82.685 | 165.508 | 331.025 | 660.508 | 1309.579

## Slide 16
Evaluation: Homomorphic Multiplication
Chart: Number of Ciphertexts
| 5120 | 10240 | 20480 | 40960 | 81920
CPU | 5473882.197 | 11005033.76 | 21970278.49 | 35266399.32 | 45957681.94
PIM | 131645.135 | 263991.946 | 527854.011 | 1055931.786 | 2137988.562
CPU-SEAL | 27889.706 | 55691.293 | 111695.209 | 224452.435 | 449237.07
GPU | 3462.7346 | 6530.458 | 13369.3576 | 27439.2448 | 55109.8277

## Slide 17
Evaluation: Homomorphic Multiplication
PIM lags 10 − 15× behind the GPU
due to the lack of native multiplication support
Chart: Number of Ciphertexts
| 5120 | 10240 | 20480 | 40960 | 81920
CPU | 5473882.197 | 11005033.76 | 21970278.49 | 35266399.32 | 45957681.94
PIM | 131645.135 | 263991.946 | 527854.011 | 1055931.786 | 2137988.562
CPU-SEAL | 27889.706 | 55691.293 | 111695.209 | 224452.435 | 449237.07
GPU | 3462.7346 | 6530.458 | 13369.3576 | 27439.2448 | 55109.8277

## Slide 18
Evaluation: Linear Regression
Chart: Execution time (ms)
| 32 Ciphertexts | 64 Ciphertexts
CPU | 9243236.848 | 16116650.33
PIM | 1238286.259 | 2476532.17
CPU-SEAL | 110852.6704 | 216799.532
GPU | 22426.9344 | 45094.9064

## Slide 19
Evaluation: Linear Regression
CPU-SEAL and GPU are faster than PIM
Chart: Execution time (ms)
| 32 Ciphertexts | 64 Ciphertexts
CPU | 9243236.848 | 16116650.33
PIM | 1238286.259 | 2476532.17
CPU-SEAL | 110852.6704 | 216799.532
GPU | 22426.9344 | 45094.9064
PIM is 6.4-7.5x faster than the
custom CPU implementation

## Slide 20: Key Takeaways
1
UPMEM PIM system natively supports
32-bit integer addition and outperforms
CPU and GPU for homomorphic addition

## Slide 21: Key Takeaways
The lack of native support for 32-bit integer multiplication hampers the performance of PIM for homomorphic multiplication.
2
1
UPMEM PIM system natively supports
32-bit integer addition and outperforms
CPU and GPU for homomorphic addition

## Slide 22: Key Takeaways
The lack of native support for 32-bit integer multiplication hampers the performance of PIM for homomorphic multiplication.
2
1
UPMEM PIM system natively supports
32-bit integer addition and outperforms
CPU and GPU for homomorphic addition
The computational power of PIM scales with memory capacity via the addition of more memory banks and PIM cores
3

## Slide 23: Executive Summary
Homomorphic encryption (HE) enables computation on encrypted data, however it suffers from memory usage and data movement bottlenecks.
PROBLEM

## Slide 24: Executive Summary
Our goal is to extensively evaluate homomorphic operations on real-world general-purpose processing-in-memory architectures.
GOAL
Homomorphic encryption (HE) enables computation on encrypted data, however it suffers from memory usage and data movement bottlenecks.
PROBLEM

## Slide 25: Executive Summary
Our goal is to extensively evaluate homomorphic operations on real-world general-purpose processing-in-memory architectures.
GOAL
Homomorphic encryption (HE) enables computation on encrypted data, however it suffers from memory usage and data movement bottlenecks.
PROBLEM
Novel Implementation: First to implement homomorphic addition and multiplication on a real PIM system.
Performance Evaluation: Evaluated the performance of PIM across different HE security levels with real-world workloads: (i) mean, (ii) variance, (iii) linear regression.
Key Insights: Revealed PIM system capabilities and trade-offs for cryptography.
CONTRIBUTIONS

## Slide 26: Executive Summary
Our goal is to extensively evaluate homomorphic operations on real-world general-purpose processing-in-memory architectures.
GOAL
PIM is 50-100× faster than CPU and 2-15× faster than GPU in vector addition.
PIM outperforms CPU by 40-50× in vector multiplication but lags 10-15× behind GPU.
For statistical operations, PIM achieves 30× to 300× improvement over CPU and 10× to 30× over GPU.
EVALUATIONS
Homomorphic encryption (HE) enables computation on encrypted data, however it suffers from memory usage and data movement bottlenecks.
PROBLEM
Novel Implementation: First to implement homomorphic addition and multiplication on a real PIM system.
Performance Evaluation: Evaluated the performance of PIM across different HE security levels with real-world workloads: (i) mean, (ii) variance, (iii) linear regression.
Key Insights: Revealed PIM system capabilities and trade-offs for cryptography.
CONTRIBUTIONS