## Slide 1: A Case for Core-Assisted Bottleneck Acceleration in GPUs Enabling Flexible Data Compression with Assist Warps
Nandita Vijaykumar
Gennady Pekhimenko, Adwait Jog, Abhishek Bhowmick, Rachata Ausavarangnirun, Chita Das, Mahmut Kandemir, Todd C. Mowry, Onur Mutlu
Session 2A: Today, 10:20 AM
Notes: In this work we observe that different bottlenecks and imbalances in execution leave different GPU resources idle
Our goal in this work is employ these idle resources to accelerate different bottlenecks in execution
In order to do this we propose to employ light-weight helper threads
However, there are some key challenges that need to be addressed to enable helper threading in GPUs
We propose a new framework CABA that effectively addresses these challenges
The framework is flexible enough to be applied to a wide range of use case
In this work, the apply the framework to enable flexible data compression
We find that CABA shows that improves the performance of a wide range of GPGPU applications evaluated

## Slide 2
Our Goal: Employ idle resources to do something useful: accelerate the bottleneck − using helper threads
Observation: Imbalances in execution leave GPU resources underutilized
Memory
Hierarchy
Register File
Cores
GPU Threads
Idle!
Idle!
Saturated!
Memory
Hierarchy
Register File
Cores
GPU Threads
Running!
Helper Threads
Challenge: How do you manage and use helper threads in a throughput-oriented architecture?

## Slide 3: Our Solution: CABA
A new framework to enable helper threading in GPUs
  CABA (Core-Assisted Bottleneck Acceleration)
Wide set of use cases
  Compression, prefetching, memoization, …
  Flexible data compression using CABA alleviates the memory bandwidth bottleneck
  41.7% performance improvement