## Slide 1: Improving DRAM Performance by Parallelizing Refreshes with Accesses
Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, Onur Mutlu
Kevin Chang

## Slide 2: Executive Summary
DRAM refresh interferes with memory accesses
  Degrades system performance and energy efficiency
  Becomes exacerbated as DRAM density increases
Goal: Serve memory accesses in parallel with refreshes to reduce refresh interference on demand requests
Our mechanisms:
  1. Enable more parallelization between refreshes and accesses across different banks with new per-bank refresh scheduling algorithms
  2. Enable serving accesses concurrently with refreshes in the same bank by exploiting DRAM subarrays
Improve system performance and energy efficiency for a wide variety of different workloads and DRAM densities
  20.2% and 9.0% for 8-core systems using 32Gb DRAM
  Very close to the ideal scheme without refreshes

## Slide 3: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
Results

## Slide 4: Refresh Penalty
Processor
Memory Controller
DRAM
Refresh
Read
Data
Capacitor
Access transistor
Refresh delays requests by 100s of ns
Refresh interferes with memory accesses

## Slide 5: Existing Refresh Modes
Time
Per-bank refresh in mobile DRAM (LPDDRx)
Time
All-bank refresh in commodity DRAM (DDRx)
Bank 7
Bank 1
Bank 0
…
Bank 7
Bank 1
Bank 0
…
Refresh
Round-robin order
…
Per-bank refresh allows accesses to other banks while a bank is refreshing

## Slide 6: Shortcomings of Per-Bank Refresh
Problem 1: Refreshes to different banks are scheduled in a strict round-robin order
  The static ordering is hardwired into DRAM chips
  Refreshes busy banks with many queued requests when other banks are idle
Key idea: Schedule per-bank refreshes to idle banks opportunistically in a dynamic order

## Slide 7: Shortcomings of Per-Bank Refresh
Problem 2: Banks that are being refreshed cannot concurrently serve memory requests
Time
Bank 0
RD
Delayed by refresh
Per-Bank Refresh

## Slide 8: Shortcomings of Per-Bank Refresh
Problem 2: Refreshing banks cannot concurrently serve memory requests
Key idea: Exploit subarrays within a bank to parallelize refreshes and accesses across subarrays
Time
Bank 0
Subarray 1
Subarray 0
RD
Subarray Refresh
Time
Parallelize

## Slide 9: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
Results

## Slide 10: DRAM System Organization
Rank 1
Bank 7
Bank 1
Bank 0
…
Rank 0
Rank 1
DRAM
Banks can serve multiple requests in parallel

## Slide 11: DRAM Refresh Frequency
DRAM standard requires memory controllers to send periodic refreshes to DRAM
tRefPeriod (tREFI): Remains constant
tRefLatency (tRFC): Varies based on DRAM chip density (e.g., 350ns)
Timeline
Read/Write: roughly 50ns

## Slide 12: Increasing Performance Impact
DRAM is unavailable to serve requests for of time
6.7% for today’s 4Gb DRAM
Unavailability increases with higher density due to higher tRefLatency
  23% / 41% for future 32Gb / 64Gb DRAM
tRefLatency
tRefPeriod

## Slide 13: All-Bank vs. Per-Bank Refresh
Shorter tRefLatency than that of all-bank refresh
More frequent refreshes (shorter tRefPeriod)
Timeline
Bank 0
Bank 1
Refresh
Per-Bank Refresh: In mobile DRAM (LPDDRx)
Refresh
Timeline
Bank 0
Bank 1
All-Bank Refresh: Employed in commodity DRAM (DDRx, LPDDRx)
Refresh
Refresh
Refresh
Staggered across banks to limit power
Read
Read
Read
Read
Can serve memory accesses in parallel with refreshes across banks

## Slide 14: Shortcomings of Per-Bank Refresh
1) Per-bank refreshes are strictly scheduled in round-robin order (as fixed by DRAM’s internal logic)
2) A refreshing bank cannot serve memory accesses
Goal: Enable more parallelization between refreshes and accesses using practical mechanisms

## Slide 15: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
  1. Dynamic Access-Refresh Parallelization (DARP)
  2. Subarray Access-Refresh Parallelization (SARP)
Results

## Slide 16: Our First Approach: DARP
Dynamic Access-Refresh Parallelization (DARP)
  An improved scheduling policy for per-bank refreshes
  Exploits refresh scheduling flexibility in DDR DRAM
Component 1: Out-of-order per-bank refresh
  Avoids poor static scheduling decisions
  Dynamically issues per-bank refreshes to idle banks
Component 2: Write-Refresh Parallelization
  Avoids refresh interference on latency-critical reads
  Parallelizes refreshes with a batch of writes

## Slide 17: 1) Out-of-Order Per-Bank Refresh
Dynamic scheduling policy that prioritizes refreshes to idle banks
Memory controllers decide which bank to refresh

## Slide 18: 1) Out-of-Order Per-Bank Refresh
Bank 1
Bank 0
Our mechanism: DARP
Refresh
Read
Timeline
Bank 1
Bank 0
Refresh
Read
Refresh
Read
Baseline: Round robin
Refresh
Read
Saved cycles
Delayed by refresh
Saved cycles
Read
Request queue (Bank 0)
Request queue (Bank 1)
Read
Reduces refresh penalty on demand requests by refreshing idle banks first in a flexible order

## Slide 19: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
  1. Dynamic Access-Refresh Parallelization (DARP)
    1) Out-of-Order Per-Bank Refresh
    2) Write-Refresh Parallelization
  2. Subarray Access-Refresh Parallelization (SARP)
Results

## Slide 20: Refresh Interference on Upcoming Requests
Problem: A refresh may collide with an upcoming request in the near future
Bank 1
Bank 0
Refresh
Read
Read
Delayed by refresh
Time

## Slide 21: DRAM Write Draining
Observations:
1) Bus-turnaround latency when transitioning from writes to reads or vice versa
  To mitigate bus-turnaround latency, writes are typically drained to DRAM in a batch during a period of time
2) Writes are not latency-critical
Timeline
Bank 1
Bank 0
Write
Read
Write
Turnaround
Write

## Slide 22: 2) Write-Refresh Parallelization
Proactively schedules refreshes when banks are serving write batches
Timeline
Bank 1
Bank 0
Turnaround
Refresh
Read
Read
Baseline
Delayed by refresh
Write
Write
Write
Write-refresh parallelization
Timeline
Bank 1
Bank 0
Read
Turnaround
Read
Write
Write
Write
Refresh
1. Postpone refresh
Refresh
2. Refresh during writes
Saved cycles
Avoids stalling latency-critical read requests by refreshing with non-latency-critical writes

## Slide 23: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
  1. Dynamic Access-Refresh Parallelization (DARP)
  2. Subarray Access-Refresh Parallelization (SARP)
Results

## Slide 24: Our Second Approach: SARP
Observations:
1. A bank is further divided into subarrays
  Each has its own row buffer to perform refresh operations
2. Some subarrays and bank I/O remain completely idle during refresh
Bank 7
Bank 1
Bank 0
…
Subarray
Bank I/O
Row Buffer
Idle

## Slide 25: Our Second Approach: SARP
Subarray Access-Refresh Parallelization (SARP):
  Parallelizes refreshes and accesses within a bank

## Slide 26: Our Second Approach: SARP
Subarray Access-Refresh Parallelization (SARP):
  Parallelizes refreshes and accesses within a bank
Very modest DRAM modifications: 0.71% die area overhead
Bank 7
Bank 1
Bank 0
…
Subarray
Bank I/O
Timeline
Subarray 1
Subarray 0
Bank 1
Data
Refresh
Refresh
Read
Read

## Slide 27: Outline
Motivation and Key Ideas
DRAM and Refresh Background
Our Mechanisms
Results

## Slide 28: Methodology
100 workloads: SPEC CPU2006, STREAM, TPC-C/H, random access
System performance metric: Weighted speedup
DDR3 Rank
Simulator configurations
Memory Controller
8-core processor
Memory Controller
Bank 7
Bank 1
Bank 0
…
L1 $: 32KB
L2 $: 512KB/core

## Slide 29: Comparison Points
All-bank refresh [DDR3, LPDDR3, …]
Per-bank refresh [LPDDR3]
Elastic refresh [Stuecheli et al., MICRO ‘10]:
  Postpones refreshes by a time delay based on the predicted rank idle time to avoid interference on memory requests
  Proposed to schedule all-bank refreshes without exploiting per-bank refreshes
  Cannot parallelize refreshes and accesses within a rank
Ideal (no refresh)

## Slide 30: System Performance
Chart: DRAM Chip Density
All-Bank | 5.5359 | 5.3024 | 4.8311
Per-Bank | 5.7551 | 5.5256 | 5.0271
Elastic | 5.6343 | 5.3803 | 4.8911
DARP | 5.9537 | 5.8162 | 5.2317
SARP | 5.9777 | 5.9152 | 5.7295
DSARP | 5.9723 | 5.9543 | 5.8059
Ideal | 6.0252 | 6.0252 | 6.0252
7.9%
12.3%
20.2%
1. Both DARP & SARP provide performance gains and combining them (DSARP) improves even more
2. Consistent system performance improvement across DRAM densities (within 0.9%, 1.2%, and 3.8% of ideal)

## Slide 31: Energy Efficiency
3.0%
5.2%
9.0%
Consistent reduction on energy consumption
Chart: DRAM Chip Density
All-Bank | 38.2974 | 40.28 | 44.8967
Per-Bank | 38.0134 | 39.9893 | 44.5521
Elastic | 37.5049 | 39.3169 | 44.1509
DARP | 37.191 | 38.5881 | 43.25
SARP | 37.1096 | 38.322 | 41.0809
DSARP | 37.137 | 38.197 | 40.8495
Ideal | 36.6284 | 36.6284 | 36.6284

## Slide 32: Other Results and Discussion in the Paper
Detailed multi-core results and analysis
Result breakdown based on memory intensity
Sensitivity results on number of cores, subarray counts, refresh interval length, and DRAM parameters
Comparisons to DDR4 fine granularity refresh

## Slide 33: Executive Summary
DRAM refresh interferes with memory accesses
  Degrades system performance and energy efficiency
  Becomes exacerbated as DRAM density increases
Goal: Serve memory accesses in parallel with refreshes to reduce refresh interference on demand requests
Our mechanisms:
  1. Enable more parallelization between refreshes and accesses across different banks with new per-bank refresh scheduling algorithms
  2. Enable serving accesses concurrently with refreshes in the same bank by exploiting DRAM subarrays
Improve system performance and energy efficiency for a wide variety of different workloads and DRAM densities
  20.2% and 9.0% for 8-core systems using 32Gb DRAM
  Very close to the ideal scheme without refreshes

## Slide 34: Improving DRAM Performance by Parallelizing Refreshes with Accesses
Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, Onur Mutlu
Kevin Chang