## Slide 1
Heterogeneous Architectures
Effects of Application Interference
Scheme
Summary
Performance Benefits
Onur Kayıran1 Nachiappan CN1 Adwait Jog1 Rachata Ausavarungnirun2
Mahmut T. Kandemir1 Gabriel H. Loh3 Onur Mutlu2 Chita R. Das1
1The Pennsylvania State University 2Carnegie Mellon University 3AMD Research
Managing GPU Concurrency in Heterogeneous Architectures
SIMT Cores
Warp Scheduler
ALUs
L1 Caches
Interconnect
DRAM
LLC cache
CTA Scheduler
ALUs
L1 Caches
L2 Caches
ROB
CPU Cores
Latency optimized cores and throughput optimized cores share the memory hierarchy
Chart: Normalized GPU IPC
| KM | MM | PVR
noCPU | 1 | 1 | 1
mcf | 0.92533 | 0.99517 | 0.80508
omnetpp | 0.942 | 1.0001 | 0.90604
perlbench | 0.99858 | 0.99923 | 0.9913
GPU applications are affected moderately due to CPU interference
Up to 20%
Chart: Normalized CPU IPC
| mcf | omnetpp | perlbench
noGPU | 1 | 1 | 1
KM | 0.37024 | 0.57433 | 0.96902
MM | 0.91235 | 0.99603 | 0.9995
PVR | 0.13576 | 0.25954 | 0.85019
CPU applications are affected significantly due to GPU interference
Up to 85%
Latency Tolerance of CPUs vs. GPUs
Chart: Normalized IPC
| 1 warp | 4 warps | 6 warps | 8 warps | 16 warps | 48 warps
GPU IPC | 0.34647 | 0.97949 | 1.0303 | 1.0031 | 0.94474 | 0.95299
CPU IPC | 1.4292 | 1.2264 | 1.1557 | 1.0358 | 0.97965 | 0.97983
High GPU TLP causes memory and network congestion
High memory congestion degrades CPU performance
GPU cores can tolerate memory congestion due to multi-threading
The optimal TLP for CPUs and GPUs might be different due to the disparity between latency tolerance of CPUs and GPUs
Achieved by an existing GPU-based technique
Effective for GPU performance
23% potential CPU improvements w/o significant performance loss for the GPU
Problem:
Existing GPU-based TLP management techniques for GPUs might not be effective in heterogeneous systems
Existing Works
CPU-based Scheme
CPU-GPU Balanced Scheme
Improved GPU performance
Improved CPU performance

×
×



+ control the trade-off
Increase # of warps
Decrease # of warps
No change in # of warps
Memory congestion
Network congestion
L
M
H
L
M
H
CPU-based Scheme: CM-CPU
GPU TLP is reduced if memory or network congestion is high.
Improves CPU performance.
Might cause low latency tolerance for GPU cores.
GPU scheduler stalls
can be high due to:
High memory congestion
Low latency tolerance due to low TLP
CPU-GPU Balanced Scheme: CM-BAL
GPU TLP is increased if GPU cores suffer from low latency tolerance.
Provides balanced improvements.
The CPU-GPU benefits trade-off can be controlled.
CM-BAL1:
Balanced improvements for both CPUs and GPUs
CM-BAL4:
Tuned to favor CPU applications
Chart: Normalized GPU IPC
| DYNCTA | CM-CPU | CM-BAL1 | CM-BAL2 | CM-BAL3 | CM-BAL4
 | 1.0193 | 0.89197 | 1.0677 | 1.0452 | 0.98948 | 0.89476
7%
-11%
2%
-11%
Chart: Normalized CPU WS
| DYNCTA | CM-CPU | CM-BAL1 | CM-BAL2 | CM-BAL3 | CM-BAL4
 | 1.0155 | 1.2391 | 1.0737 | 1.1053 | 1.1736 | 1.1918
19%
7%
24%
2%
Warp Scheduler
Controls GPU Thread-Level Parallelism