## Slide 1: Managing GPU Concurrency in Heterogeneous Architectures
Onur Kayıran, Nachiappan CN, Adwait Jog, Rachata Ausavarungnirun, Mahmut T. Kandemir, Gabriel H. Loh, Onur Mutlu, Chita R. Das

## Slide 2: Era of Heterogeneous Architectures
Intel Haswell
AMD Fusion
NVIDIA Echelon
NVIDIA Denver

## Slide 3: Executive Summary
When sharing the memory hierarchy, CPU and GPU applications interfere with each other
  GPU applications significantly affect CPU applications due to multi-threading
Existing GPU Thread-level Parallelism (TLP) management techniques (MICRO12, PACT13)
  Unaware of CPUs
  Not effective in heterogeneous systems
Our Proposal:
Warp scheduling strategies to
Adjust GPU TLP to improve CPU and/or GPU performance

## Slide 4: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance

## Slide 5: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance
IF Memory Congestion
GPU TLP

## Slide 6: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance
IF Memory Congestion
GPU TLP
Results Summary:
+24% CPU & -11% GPU

## Slide 7: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance
IF Memory Congestion
GPU TLP
Results Summary:
+24% CPU & -11% GPU
CPU-GPU Balanced Strategy
GPU TLP
GPU Latency Tolerance

## Slide 8: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance
IF Memory Congestion
GPU TLP
Results Summary:
+24% CPU & -11% GPU
CPU-GPU Balanced Strategy
GPU TLP
GPU Latency Tolerance
IF Latency Tolerance
GPU TLP

## Slide 9: Executive Summary
CPU-centric Strategy
Memory Congestion
CPU Performance
IF Memory Congestion
GPU TLP
Results Summary:
+24% CPU & -11% GPU
CPU-GPU Balanced Strategy
GPU TLP
GPU Latency Tolerance
IF Latency Tolerance
GPU TLP
Results Summary:
+7% both CPU & GPU

## Slide 10: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 11: Many-core Architecture
SIMT Cores
Warp Scheduler
ALUs
L1 Caches
Interconnect
DRAM
LLC cache
CTA Scheduler
ALUs
L1 Caches
L2 Caches
ROB
CPU Cores
Latency optimized cores
Throughput optimized cores

## Slide 12: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 13: Application Interference
Chart: Normalized GPU IPC
| KM | MM | PVR
noCPU | 1 | 1 | 1
mcf | 0.92533 | 0.99517 | 0.80508
omnetpp | 0.942 | 1.0001 | 0.90604
perlbench | 0.99858 | 0.99923 | 0.9913
Chart: Normalized CPU IPC
| mcf | omnetpp | perlbench
noGPU | 1 | 1 | 1
KM | 0.37024 | 0.57433 | 0.96902
MM | 0.91235 | 0.99603 | 0.9995
PVR | 0.13576 | 0.25954 | 0.85019
GPU applications are affected moderately due to CPU interference
CPU applications are affected significantly due to GPU interference
Up to 20%
Up to 85%

## Slide 14: Latency Tolerance in CPUs vs. GPUs
High GPU TLP -> memory system congestion
High GPU TLP -> low CPU performance
GPU cores can tolerate latencies due to multi-threading
Chart: Normalized IPC
| 1 warp | 4 warps | 6 warps | 8 warps | 16 warps | 48 warps
GPU IPC | 0.34647 | 0.97949 | 1.0303 | 1.0031 | 0.94474 | 0.95299
CPU IPC | 1.4292 | 1.2264 | 1.1557 | 1.0358 | 0.97965 | 0.97983
DYNCTA (PACT 2013)
Higher performance potential at low TLP
Problem:
TLP management strategies for GPUs are not aware of the latency tolerance disparity between CPU and GPU applications

## Slide 15: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 16: Effect of GPU Concurrency on GPU Performance
Reduction in GPU TLP
GPU performance

## Slide 17: Effect of GPU Concurrency on CPU Performance
Reduction in GPU TLP
CPU performance

## Slide 18: Effect of GPU Concurrency on CPU Performance
?
Change in CPU performance
2 metrics:
Memory congestion
Network congestion
congestion
:
CPU performance

## Slide 19: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 20: Our Approach
Existing works
CPU-centric Strategy
CPU-GPU Balanced Strategy
Improved GPU performance
Improved CPU performance

×
×



+ control the trade-off

## Slide 21: CM-CPU: CPU-centric Strategy
Categorize congestion: low, medium, or high
Increase # of warps
Decrease # of warps
No change in # of warps
memory
network
L
M
H
L
M
H
GPU-unaware TLP management:
Insufficient GPU latency tolerance

## Slide 22: CM-BAL: CPU-GPU Balanced Strategy
GPU TLP
stallGPU
Latency tolerance of GPU cores:
  stallGPU: scheduler stalls @ GPU cores
High memory congestion
Low latency tolerance
same strategy as CM-CPU
×
Overrides CM-CPU
can only increase TLP

## Slide 23: CM-BAL: CPU-GPU Balanced Strategy
GPU TLP
stallGPU
Latency tolerance of GPU cores:
  stallGPU: scheduler stalls @ GPU cores
High memory congestion
Low latency tolerance
same strategy as CM-CPU
×
Overrides CM-CPU
can only increase TLP

## Slide 24: CM-BAL: CPU-GPU Balanced Strategy
GPU TLP
stallGPU
Latency tolerance of GPU cores:
  stallGPU: scheduler stalls @ GPU cores
High memory congestion
Low latency tolerance
same strategy as CM-CPU

Overrides CM-CPU
can only increase TLP

## Slide 25: CM-BAL: CPU-GPU Balanced Strategy
GPU TLP
stallGPU
Latency tolerance of GPU cores:
  stallGPU: scheduler stalls @ GPU cores
High memory congestion
Low latency tolerance
same strategy as CM-CPU
Overrides CM-CPU
can only increase TLP
Control the triggering of the condition
=
Control the trade-off between CPU or GPU benefits

## Slide 26: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 27: Evaluated Architecture
LLC/
MC
LLC/
MC
LLC/
MC
LLC/
MC
LLC/
MC
LLC/
MC
LLC/
MC
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
LLC/
MC
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
Tile-based design

## Slide 28: Evaluation Methodology
Evaluated on an integrated platform with an in-house x86 CPU simulator and GPGPU-Sim
Baseline Architecture
  28 GPU cores, 14 CPU cores, 8 memory controllers, 2D mesh
  GPU: 1400MHz, SIMT Width = 16*2, Max. 1536 threads/core, GTO Sch.
  CPU: 2000 MHz, OoO, 128-entry instr. win., max. 3 inst./cycle
  8MB, 128B Line, 16-way, 700MHz
  GDDR5 800MHz
Workloads:
  13 GPU applications
  34 CPU applications, 6 CPU application mixes
  36 diverse workloads
    1 GPU application + 1 CPU mix

## Slide 29: GPU Performance Results
Chart: Normalized GPU IPC
| DYNCTA | CM-CPU | sch8_0 | sch8_512 | CM-BAL1 | CM-BAL2 | CM-BAL3 | CM-BAL4
 | 1.0193 | 0.89197 | 1.0348 | 1.0615 | 1.0677 | 1.0452 | 0.98948 | 0.89476
7%
-11%
2%
-11%
All 36 workloads

## Slide 30: CPU Performance Results
Chart: Normalized CPU WS
 | 1.0155 | 1.2391 | 1.0737 | 1.1053 | 1.1736 | 1.1918
24%
7%
2%
19%
All 36 workloads

## Slide 31: System Performance
OSS = (1 − α) × WSCPU + α × SUGPU (ISCA 2012)
α is between 0 and 1
Higher α -> higher GPU importance
Chart: alpha (0 - 1)
CM-CPU
CM-BAL

## Slide 32: More in the Paper
Motivation
  Analysis of the metrics used by our algorithm
Scheme
  Detailed hardware walkthrough of our scheme
Results
  Analysis over time
  Change in GPU TLP
  Change in the metrics used by our algorithm
  Comparison against static approaches
  Lower number of LLC accesses

## Slide 33: Outline
Summary
Background
Motivation
Analysis of TLP
Our Proposal
Evaluation
Conclusions

## Slide 34: Conclusions
Sharing the memory hierarchy leads to CPU and GPU applications to interfere with each other
Existing GPU TLP management techniques are not well-suited for heterogeneous architectures
We propose two GPU TLP management techniques for heterogeneous architectures
  CM-CPU reduces GPU TLP to improve CPU performance
  CM-BAL is similar to CM-CPU, but increases GPU TLP when it detects low latency tolerance in GPU cores
  TLP can be tuned based on user’s preference for higher CPU or GPU performance

## Slide 35: Thanks!

## Slide 36: Managing GPU Concurrency in Heterogeneous Architectures
Onur Kayıran, Nachiappan CN, Adwait Jog, Rachata Ausavarungnirun, Mahmut T. Kandemir, Gabriel H. Loh, Onur Mutlu, Chita R. Das

## Slide 37: BACKUP

## Slide 38: Application Interference
Chart: Normalized GPU IPC
| KM | MM | PVR
noCPU | 1 | 1 | 1
mcf | 0.92533 | 0.99517 | 0.80508
omnetpp | 0.942 | 1.0001 | 0.90604
perlbench | 0.99858 | 0.99923 | 0.9913
Chart: Normalized CPU IPC
| mcf | omnetpp | perlbench
noGPU | 1 | 1 | 1
KM | 0.37024 | 0.57433 | 0.96902
MM | 0.91235 | 0.99603 | 0.9995
PVR | 0.13576 | 0.25954 | 0.85019
GPU applications are affected moderately due to CPU interference
Memory intensive GPU applications are affected more than compute intensive GPU applications
Memory intensive CPU applications affect GPU performance more than compute intensive CPU applications
CPU applications are affected significantly due to GPU interference
Memory intensive CPU applications are affected more than compute intensive CPU applications
Memory intensive GPU applications affect CPU performance more than compute intensive GPU applications

## Slide 39: Network Partitioning
Chart: Normalized CPU IPC
| KM | IIX | MST
1G3C | 0.90374 | 0.87322 | 1.08
2G2C | 1.0557 | 1.0279 | 1.1847
3G1C | 1.1267 | 1.097 | 1.1513
Chart: Normalized GPU IPC
| KM | IIX | MST
1G3C | 0.048611 | 0.12926 | 0.28094
2G2C | 0.14561 | 0.3813 | 0.48592
3G1C | 0.34272 | 0.91144 | 0.85041

## Slide 40: Memory Controller Partitioning
Chart: Normalized CPU IPC
| KM | IIX | MST
1G7C | 0.78626 | 0.76581 | 1.2522
2G6C | 0.94803 | 0.97613 | 1.3663
4G4C | 1.1716 | 1.1553 | 1.7565
6G2C | 0.93621 | 0.83986 | 1.3972
7G1C | 0.24411 | 0.25632 | 0.73654
Chart: Normalized GPU IPC
| KM | IIX | MST
1G7C | 0.15958 | 0.17551 | 0.47824
2G6C | 0.28636 | 0.31993 | 0.60956
4G4C | 0.54375 | 0.56465 | 0.71576
6G2C | 0.77531 | 0.81317 | 0.91266
7G1C | 0.94949 | 0.96986 | 0.99348

## Slide 41: Network + MC partitioning
Chart: Normalized CPU IPC
| KM | IIX | MST
3G1C-7G1C | 0.15533 | 0.15421 | 0.41235
3G1C-4G4C | 0.55115 | 0.54717 | 1.459
Chart: Normalized GPU IPC
| KM | IIX | MST
3G1C-7G1C | 0.76259 | 0.79015 | 0.98392
3G1C-4G4C | 0.46162 | 0.49063 | 0.70652

## Slide 42: Effect of GPU TLP on GPU performance
Chart: Normalized GPU IPC
| MUM | BP | MM | PVR | MST | SSSP | HMEAN
4 warps | 1.1573 | 0.53686 | 0.62841 | 0.92857 | 0.991 | 1.0592 | 0.81653
6 warps | 1.1338 | 0.7164 | 0.85704 | 0.99103 | 0.99893 | 1.1042 | 0.94333
8 warps | 1.0857 | 0.8246 | 0.97363 | 1.0125 | 1.0075 | 1.0834 | 0.98943
16 warps | 1 | 0.99265 | 1 | 1.0173 | 0.99723 | 1.0031 | 1.0016
24 warps | 1 | 1 | 1 | 1 | 1 | 1 | 1
48 warps | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 43: Congestion Metrics
Chart: stallMC
| MUM | BP | MM | PVR | MST | SSSP
4 warps | 1.8989 | 0.23608 | 0.014095 | 3.7493 | 4.9957 | 0.79902
6 warps | 2.1827 | 0.32166 | 0.011492 | 5.0074 | 4.9321 | 1.1599
8 warps | 2.2199 | 0.39889 | 0.010547 | 5.2308 | 4.9237 | 1.7373
16 warps | 2.2884 | 0.5726 | 0.010431 | 5.2781 | 4.5414 | 1.9227
24 warps | 2.2884 | 0.63417 | 0.010431 | 5.3099 | 4.5768 | 1.9771
48 warps | 2.2884 | 0.63417 | 0.010431 | 5.3099 | 4.5768 | 1.9771
Chart: stallnet
| MUM | BP | MM | PVR | MST | SSSP
4 warps | 0.39321 | 0.0018908 | 0.072186 | 0.0019989 | 0.011759 | 1.3976
6 warps | 0.41611 | 0.0026466 | 0.041871 | 0.0017679 | 0.027296 | 4.8198
8 warps | 0.38245 | 0.0022877 | 0.04303 | 0.0016152 | 0.069425 | 6.9541
16 warps | 0.36973 | 0.0037681 | 0.051072 | 0.0014691 | 0.1532 | 7.231
24 warps | 0.36973 | 0.002439 | 0.051072 | 0.0014123 | 0.1517 | 7.2949
48 warps | 0.36973 | 0.002439 | 0.051072 | 0.0014123 | 0.1517 | 7.2949

## Slide 44: Effect of GPU TLP on CPU - omnetpp
Chart: Normalized CPU IPC
| MUM | BP | MM | PVR | MST | SSSP
4 warps | 1.1354 | 1.3513 | 0.99907 | 1.5489 | 1.1458 | 1.221
6 warps | 1.1012 | 1.0245 | 0.99955 | 1.2325 | 0.99073 | 1.0921
8 warps | 1.0664 | 1.0034 | 1.0001 | 1.0288 | 0.99447 | 1.0428
16 warps | 1 | 1.0018 | 1 | 1.0074 | 0.99783 | 0.99753
24 warps | 1 | 1 | 1 | 1 | 1 | 1
48 warps | 1 | 1 | 1 | 1 | 1 | 1

## Slide 45: Effect of GPU TLP on CPU - perlbench
Chart: Normalized CPU IPC
| MUM | BP | MM | PVR | MST | SSSP
4 warps | 1.0019 | 1.0022 | 1.0001 | 1.0938 | 0.98892 | 1.0021
6 warps | 1.0037 | 1.0016 | 1.0002 | 1.0469 | 1.0023 | 1.0135
8 warps | 0.99872 | 1.0016 | 1.0001 | 1.0165 | 0.99988 | 0.99743
16 warps | 1 | 1.0004 | 1 | 0.99709 | 1.0056 | 1.0065
24 warps | 1 | 1 | 1 | 1 | 1 | 1
48 warps | 1 | 1 | 1 | 1 | 1 | 1

## Slide 46: Hardware Organization
CM-CPU
logic
GTO priority logic
Ready warps [1:N]
Prioritized warps
[1:N]
Warp-limiting scheduler (SWL)
Warps to be scheduled
[1:warp_limit]
N==0
Pipeline register full
Fetch/Decode
I-Buffer/Scoreboard
Warp Issue Arbiter
Registers/Execute
Memory Unit
Fetch/Decode
I-Buffer/Scoreboard
Warp Issue Arbiter
Registers/Execute
Memory Unit
Fetch/Decode
I-Buffer/Scoreboard
Warp Issue Arbiter
Registers/Execute
Memory Unit
GPU cores
Interconnect
CTA
scheduler
congestionMC
MC
congestionnet
CPU cores
current
warp_limit
stallGPU table
1 warp - stallGPU
2 warps - stallGPU
48 warps - stallGPU
…
From CM-CPU logic
CM-BAL logic
LLC
LLC
LLC
MC
MC
congestionMC
congestionMC
congestionnet
congestionnet
stallMC
stallnet
k
10
11
1
2
3
4
5
6
7
8
9
13
12
True
Warp Issue Arbiter

## Slide 47: GPU latency tolerance
Part 1 of CM-BAL
Part 2 of CM-BAL
GPU TLP
stallGPU
Lowest TLP that provides enough latency tolerance
CM-CPU
CM-BAL
R1
R2
CM-CPU’s working domain
1
2

## Slide 48: GPU Performance
Chart: Normalızed GPU IPC
| DYNCTA | CM-CPU | CM-BAL1 | CM-BAL2 | CM-BAL3 | CM-BAL4
Type-H / L-MPKI | 0.98868 | 0.916 | 0.9998 | 0.99965 | 0.98533 | 0.95203
Type-H / M-MPKI | 0.99186 | 0.82513 | 0.99367 | 0.98819 | 0.97497 | 0.89174
Type-H / H-MPKI | 0.99796 | 0.78261 | 0.99352 | 0.96836 | 0.97289 | 0.82278
Type-M / L-MPKI | 0.99625 | 0.73106 | 0.99563 | 0.96112 | 0.8787 | 0.77164
Type-M / M-MPKI | 0.99937 | 0.76371 | 0.99786 | 0.98344 | 0.89033 | 0.83215
Type-M / H-MPKI | 1.0125 | 0.8519 | 1.0106 | 0.99411 | 0.88897 | 0.88436
Type-L / L-MPKI | 1.0857 | 1.3894 | 1.4679 | 1.4521 | 1.4028 | 1.008
Type-L / M-MPKI | 1.0431 | 0.99487 | 1.0758 | 1.0401 | 0.99408 | 0.9951
Type-L / H-MPKI | 1.0681 | 1.0723 | 1.2349 | 1.1725 | 1.0842 | 0.95598

## Slide 49: CPU Performance
Chart: Normalızed CPU WS
| DYNCTA | CM-CPU | CM-BAL1 | CM-BAL2 | CM-BAL3 | CM-BAL4
Type-H / L-MPKI | 1.0006 | 1.0249 | 1.0021 | 1.0004 | 1.0129 | 1.0275
Type-H / M-MPKI | 0.98905 | 1.2069 | 1.0205 | 1.0355 | 1.0798 | 1.1358
Type-H / H-MPKI | 0.99832 | 1.138 | 1.0138 | 1.0332 | 1.0495 | 1.0984
Type-M / L-MPKI | 1.0662 | 1.4777 | 1.1061 | 1.1921 | 1.3714 | 1.4534
Type-M / M-MPKI | 0.99989 | 1.404 | 1.063 | 1.1134 | 1.3028 | 1.3842
Type-M / H-MPKI | 1.0141 | 1.2172 | 1.0954 | 1.1008 | 1.1683 | 1.1809
Type-L / L-MPKI | 1.0086 | 1.1009 | 1.0624 | 1.0683 | 1.093 | 1.0537
Type-L / M-MPKI | 1.0243 | 1.3935 | 1.1846 | 1.2311 | 1.2887 | 1.2835
Type-L / H-MPKI | 1.0434 | 1.344 | 1.1434 | 1.2261 | 1.3175 | 1.2473

## Slide 50: Static Warp Limits
Chart: Normalized GPU IPC
| 1 warp | 4 warps | 6 warps | 8 warps | 16 warps | 48 warps | DYNCTA | CM-CPU | CM-BAL1
Type-H | 0.19103 | 0.63455 | 0.83285 | 0.91958 | 0.99803 | 1 | 0.99282 | 0.83766 | 0.99565
Type-M | 0.53565 | 0.97572 | 0.99883 | 1.0067 | 0.99942 | 1 | 1.0027 | 0.779 | 1.0013
Type-L | 0.70358 | 1.097 | 1.0664 | 1.0436 | 0.99862 | 1 | 1.0654 | 1.1289 | 1.2394
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Normalized CPU IPC
| 1 warp | 4 warps | 6 warps | 8 warps | 16 warps | 48 warps | DYNCTA | CM-CPU | CM-BAL1
L-MPKI | 1.203 | 1.064 | 1.0335 | 1.0163 | 0.99986 | 1 | 1.0243 | 1.1715 | 1.0551
M-MPKI | 1.5518 | 1.1572 | 1.0896 | 1.0369 | 1.0011 | 1 | 1.0042 | 1.3283 | 1.085
H-MPKI | 1.4807 | 1.1531 | 1.0767 | 1.035 | 1.0043 | 1 | 1.0183 | 1.2273 | 1.0815
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 51: Average number of active warps
Chart: Average # of active warps
| Type-H / L-MPKI | Type-H / M-MPKI | Type-H / H-MPKI | Type-M / L-MPKI | Type-M / M-MPKI | Type-M / H-MPKI | Type-L / L-MPKI | Type-L / M-MPKI | Type-L / H-MPKI
CM-CPU | 31.8244 | 19.0359 | 16.9354 | 2.102 | 2.3771 | 2.7305 | 2.9737 | 2.928 | 2.846
CM-BAL1 | 40.4605 | 33.6695 | 31.4955 | 6.2866 | 6.6597 | 5.9747 | 4.1193 | 4.9747 | 5.1958

## Slide 52: Auxiliary Metrics
Chart: Normalized stallMC/cycle
| H-L | H-M | H-H | M-L | M-M | M-H | L-L | L-M | L-H
CM-CPU | 0.86613 | 0.72621 | 0.67862 | 0.27242 | 0.48557 | 0.4884 | 0.22921 | 0.48234 | 0.30693
CM-BAL1 | 1.0011 | 0.99108 | 1.0138 | 0.8751 | 0.86875 | 0.77607 | 0.5604 | 0.7634 | 0.70336
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Normalized stallGPU/inst.
| H-L | H-M | H-H | M-L | M-M | M-H | L-L | L-M | L-H
CM-CPU | 1.0417 | 1.0581 | 1.0615 | 1.2697 | 1.1705 | 1.1006 | 0.73641 | 1.0071 | 0.96133
CM-BAL1 | 1.0003 | 1.0016 | 1.0011 | 0.9988 | 0.99356 | 0.97982 | 0.68861 | 0.9259 | 0.83605
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1