## Slide 1: Computer Architecture: Emerging Memory Technologies (Part II)
Prof. Onur Mutlu
Carnegie Mellon University

## Slide 2: Emerging Memory Technologies Lectures
These slides are from the Scalable Memory Systems course taught at ACACES 2013 (July 15-19, 2013)
Course Website:
    http://users.ece.cmu.edu/~omutlu/acaces2013-memory.html
This is the second lecture on this topic:
  Lecture 4a (July 18, 2013): Emerging Memory Technologies and Hybrid Memories: Hybrid Memory Design and Management (pptx) (pdf)

## Slide 3: Scalable Many-Core Memory Systems Lecture 4, Topic 2: Emerging Technologies and Hybrid Memories
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 18, 2013

## Slide 4: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 5: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 6: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two idea directions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 7: DRAM as a Cache for PCM
Goal: Achieve the best of both DRAM and PCM/NVM
  Minimize amount of DRAM w/o sacrificing performance, endurance
  DRAM as cache to tolerate PCM latency and write bandwidth
  PCM as main memory to provide large capacity at good cost and power
DATA
PCM Main Memory
DATA
T
DRAM Buffer
PCM Write Queue
T=Tag-Store
Processor
Flash
Or
HDD
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 8: Write Filtering Techniques
Lazy Write: Pages from disk installed only in DRAM, not PCM
Partial Writes: Only dirty lines from DRAM page written back
Page Bypass: Discard pages with poor reuse on DRAM eviction
Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Processor
DATA
PCM Main Memory
DATA
T
DRAM Buffer
Flash
Or
HDD

## Slide 9: Results: DRAM as PCM Cache (I)
Simulation of 16-core system, 8GB DRAM main-memory at 320 cycles, HDD (2 ms) with Flash (32 us) with Flash hit-rate of 99%
Assumption: PCM 4x denser, 4x slower than DRAM
DRAM block size = PCM page size (4kB)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Notes: Workloads:
Database workloads & Data parallel kernels
1. Database workloads: db1 and db2
2. Unix utilities: qsort and binary search
3. Data Mining : K-means and Gauss Seidal
4. Streaming: DAXPY and Vector Dot Product

## Slide 10: Results: DRAM as PCM Cache (II)
PCM-DRAM Hybrid performs similarly to similar-size DRAM
Significant power and energy savings with PCM-DRAM Hybrid
Average lifetime: 9.7 years (no guarantees)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 11: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
    Row-Locality Aware Data Placement
    Efficient DRAM (or Technology X) Caches
Conclusions
Discussion

## Slide 12: Row Buffer Locality Aware Caching Policies for Hybrid Memories
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD),
Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 13: Hybrid Memory
Key question: How to place data between the heterogeneous memory devices?
DRAM
PCM
CPU
MC
MC
Notes: One key question in the design of a hybrid memory system is: How to place data between the heterogeneous memory devices?
Our goal in this work is to answer this question.

## Slide 14: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Here’s the outline for the talk.
I’ve talked about some background in hybrid memory systems.
Next I will talk about row buffers and their implications on data placement.

## Slide 15: Hybrid Memory: A Closer Look
MC
MC
DRAM
(small capacity cache)
PCM (large capacity store)
CPU
Memory channel
Bank
Bank
Bank
Bank
Row buffer
Notes: Here’s a closer look at a hybrid memory system employing both DRAM and PCM.
Typically, the DRAM is used as a small capacity cache, and the PCM is used as a large capacity store.
When the processor needs data, it will first look to see if the data is in DRAM. If the data is indeed in DRAM, the processor will retrieve the data from there. If the data is not in DRAM, the processor will retrieve the data from PCM.
Both DRAM and PCM are organized into banks that are capable of operating independently. Also, in each bank, there are peripheral circuitries known as the row buffers.

## Slide 16: Row Buffers and Latency
Row (buffer) hit: Access data from row buffer  fast
Row (buffer) miss: Access data from cell array  slow
LOAD X
LOAD X+1
LOAD X+1
LOAD X
ROW ADDRESS
ROW DATA
Row buffer miss!
Row buffer hit!
Bank
Row buffer
CELL ARRAY
Notes: Row buffers affect memory latency is a profound way.
Row buffers effectively store the most recently accessed row in memory.
They are typically 2 to 8KB in length, for a single rank.
When data is requested in memory, it is first checked to see if the data is in the row buffer. If the data is not in the row buffer, this is called a row buffer miss. In this case, we need to read a row full of data from the memory cell array into the row buffer, and the memory request is served. In a subsequent memory request, if the requested data is already latched in the row buffer, this is called a row buffer hit, and the data can be retrieved without having to access the memory cell array, which in the case of PCM, is a high latency operation.
In summary, on a row hit, data is accessed from the row buffer, which is fast. On a row miss, data is accessed from the cell array, which is slow.

## Slide 17: Key Observation
Row buffers exist in both DRAM and PCM
  Row hit latency similar in DRAM & PCM [Lee+ ISCA’09]
  Row miss latency small in DRAM, large in PCM
Place data in DRAM which
  is likely to miss in the row buffer (low row buffer locality) miss penalty is smaller in DRAM
  AND
  is reused many times  cache only the data worth the movement cost and DRAM space
Notes: Our key observation is that row buffers exist in both DRAM and PCM.
Row hit latency, which does not access the memory cell array, is similar in DRAM and PCM.
It is for a row miss that the memory access latency is small in DRAM and large in PCM.
Therefore we would like to place data in DRAM which:
Is likely to miss in the row buffer, which we call as having low row buffer locality, since the row buffer miss penalty is small in DRAM than it is in PCM.
And we would like to place data in DRAM which is reused many times, so that we cache only the data that is worth the movement cost.

## Slide 18: RBL-Awareness: An Example
Let’s say a processor accesses four rows
Row A
Row B
Row C
Row D
Notes: Let’s look at an example how row buffer locality affects hybrid memory performance.
Let’s say a processor accesses four rows…

## Slide 19: RBL-Awareness: An Example
Let’s say a processor accesses four rows with different row buffer localities (RBL)
Row A
Row B
Row C
Row D
Low RBL
(Frequently miss
in row buffer)
High RBL
(Frequently hit
in row buffer)
Case 1: RBL-Unaware Policy (state-of-the-art)
Case 2: RBL-Aware Policy (RBLA)
Notes: With different row buffer localities.
Rows A and B have low row buffer locality, which means that they frequently miss in the row buffer, and rows C and D have high row buffer locality, which means that they frequently hit in the row buffer.
We will look at two types of caching policies: Case 1 will be row buffer locality unaware, and case 2 will be row buffer locality aware.

## Slide 20: Case 1: RBL-Unaware Policy
A row buffer locality-unaware policy could
place these rows in the following manner
DRAM (High RBL)
PCM (Low RBL)
Row C
Row D
Row A
Row B
Notes: Here’s Case 1: The row buffer locality unaware policy.
A row buffer locality unaware policy could place rows A, B, C, and D in the following manner, where rows with high row buffer locality are placed in DRAM, and rows with low row buffer locality are placed in PCM.

## Slide 21: Case 1: RBL-Unaware Policy
RBL-Unaware: Stall time is 6 PCM device accesses
DRAM (High RBL)
PCM (Low RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Access pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
time
Notes: For such a policy, this diagram shows the amount of time it takes to serve a stream of memory requests.
This is the access pattern to memory.
Clearly, the high row buffer miss latency of PCM acts as a bottleneck to serving all of the memory requests, and this happens because the rows with low row buffer locality is placed in PCM.

## Slide 22: Case 2: RBL-Aware Policy (RBLA)
A row buffer locality-aware policy would place these rows in the opposite manner
DRAM (Low RBL)
PCM (High RBL)
 Access data at lower row buffer miss latency of DRAM
 Access data at low row buffer hit latency of PCM
Row A
Row B
Row C
Row D
Notes: Here’s Case 2: The row buffer locality aware policy, or RBLA.
A row buffer locality aware policy would place these rows in the following manner, where the rows with low row buffer locality are placed in DRAM, since the data can be accessed at the lower row buffer miss latency of DRAM.
Rows with high row buffer locality will be placed in PCM, since data can be frequently accessed at the low row buffer hit latency of PCM.

## Slide 23: Case 2: RBL-Aware Policy (RBLA)
Saved cycles
DRAM (High RBL)
PCM (Low RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Access pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
DRAM (Low RBL)
PCM (High RBL)
time
A
B
C
D
C
C
D
D
A
B
A
B
RBL-Unaware: Stall time is 6 PCM device accesses
RBL-Aware: Stall time is 6 DRAM device accesses
Notes: Now we compare the two policies in terms of the time it takes to serve the same stream of memory requests.
Remember, this was the timeline shown before for the row buffer locality-unaware policy.
For case 2, the row buffer locality aware policy, although the PCM row buffer miss latency is high, many of the accesses to PCM are row buffer hit accesses that can be served quickly.
And overall, it takes less time to serve all of the memory requests in the row buffer locality aware policy.
The row buffer locality aware policy gains because it places rows with low row buffer locality in DRAM.
This is the goal of our mechanism: To place rows with low row buffer locality in DRAM.

## Slide 24: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Now I will talk about how we do that.

## Slide 25: Our Mechanism: RBLA
For recently used rows in PCM:
  Count row buffer misses as indicator of row buffer locality (RBL)
Cache to DRAM rows with misses  threshold
  Row buffer miss counts are periodically reset (only cache rows with high reuse)
Notes: Our Mechanism is called RBLA, which stands for row buffer locality aware.
For recently used rows in PCM, our mechanism counts row buffer misses as indicator of row buffer locality of each row.
I will talk more about how this is physically achieved.
Then, we cache to DRAM rows with row buffer miss counts that exceed a certain threshold.
And row buffer miss counts are periodically reset, so that we only cache rows with high reuse.
That is our base mechanism, RBLA.

## Slide 26: Our Mechanism: RBLA-Dyn
For recently used rows in PCM:
  Count row buffer misses as indicator of row buffer locality (RBL)
Cache to DRAM rows with misses  threshold
  Row buffer miss counts are periodically reset (only cache rows with high reuse)
Dynamically adjust threshold to adapt to workload/system characteristics
  Interval-based cost-benefit analysis
Notes: We also extend RBLA to RBLA-Dyn, which performs an extra step.
RBLA-Dyn dynamically adjusts the threshold value to adapt to different workload and system characteristics.
This is based on an interval-based cost-benefit analysis, for which the details can be found in the paper.
I would encourage you to read the paper, and I’d be happy to answer any questions.

## Slide 27: Implementation: “Statistics Store”
Goal: To keep count of row buffer misses to recently used rows in PCM
Hardware structure in memory controller
  Operation is similar to a cache
    Input: row address
    Output: row buffer miss count
  128-set 16-way statistics store (9.25KB) achieves system performance within 0.3% of an unlimited-sized statistics store
Notes: The implementation of our mechanism requires a statistics store, or what we simply call a stats store.
The goal of the stats store is to keep count of the row buffer misses to recently used rows in PCM.
The stats store is a hardware structure in the memory controller, and its operation is similar to a cache.
It is organized into sets and ways, and is indexed using the row address of the row we wish to find the row buffer miss count for.
If the queried row is currently in the stats store, then its row buffer miss count will be output.
We find that a 128-set 16-way stats store, 9.25KB in size, achieves system performance within 0.3% of an unlimited-sized stats store.

## Slide 28: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Now let’s take a look at our results.

## Slide 29: Evaluation Methodology
Cycle-level x86 CPU-memory simulator
  CPU: 16 out-of-order cores, 32KB private L1 per core, 512KB shared L2 per core
  Memory: 1GB DRAM (8 banks), 16GB PCM (8 banks), 4KB migration granularity
36 multi-programmed server, cloud workloads
  Server: TPC-C (OLTP), TPC-H (Decision Support)
  Cloud: Apache (Webserv.), H.264 (Video), TPC-C/H
Metrics: Weighted speedup (perf.), perf./Watt (energy eff.), Maximum slowdown (fairness)
Notes: Here’s our evaluation methodology.
We use a cycle-level x86 simulator to test our hybrid memory caching policies.
We simulate a 16-core system with 1GB of DRAM and 16GB of PCM.
We use 36 multi-programmed server and cloud workloads to test our caching policies.
For server workloads, we use TPC-C, which is an online transaction processing benchmark, and TPC-H, which is a decision support benchmark.
For cloud workloads, we use Apache, which is a webserver application, and H.264, a video processing application, as well as TPC-C and H.
We report multi-core performance in terms of weighted speedup, multi-core fairness in terms of maximum slowdown, and energy efficiency in terms of performance per Watt.

## Slide 30: Comparison Points
Conventional LRU Caching
FREQ: Access-frequency-based caching
  Places “hot data” in cache [Jiang+ HPCA’10]
  Cache to DRAM rows with accesses  threshold
  Row buffer locality-unaware
FREQ-Dyn: Adaptive Freq.-based caching
  FREQ + our dynamic threshold adjustment
  Row buffer locality-unaware
RBLA: Row buffer locality-aware caching
RBLA-Dyn: Adaptive RBL-aware caching
Notes: And here are our comparison points.
The standard conventional LRU caching caches any row from PCM to DRAM when the data is touched. We find this scheme to generate too much data movement between DRAM and PCM and consequently to not perform well. So we’re not going to use it as a comparison point in this talk.
Frek is access frequency based caching. It is inspired by prior work that selectively caches hot data.
The downsides of frek is that it is row buffer locality aware. Hence, it would place a row with high row buffer locality in DRAM, although that row may be accessed as efficiently in PCM.
Frek-Dyn augments frek with the adaptive threshold adjustment technique.
It has the same drawback as frek, in that it is row buffer locality unaware.
Our mechanisms, RBLA and RBLA-Dyn, are specifically designed to be aware of row buffer locality and to exploit it.

## Slide 31: System Performance
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
17%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 3: Balanced memory request load between DRAM and PCM
Notes: Here are the system performance results of the different hybrid memory caching policies.
RBLA-Dyn achieves 17% performance improvement over frek in server workloads, 10% in cloud, and 14% overall.
This is due to a number of reasons.
The first is that RBLA-Dyn increases row buffer locality in PCM by moving low row buffer locality data to DRAM.
The second is that RBLA-Dyn reduces memory bandwidth consumption due its stricter caching criteria.
And RBLA-Dyn also has the effect of balancing the memory request load between DRAM and PCM by letting rows with high row buffer locality remain in PCM, instead of fetching all accessed data to DRAM.

## Slide 32: Average Memory Latency
Chart: Workload
| Server | Cloud | Avg
FREQ | 1.1028 | 0.9068 | 1
FREQ-Dyn | 1.0156 | 0.85733 | 0.9331
RBLA | 1.0006 | 0.8704 | 0.93324
RBLA-Dyn | 0.94644 | 0.82222 | 0.88214
14%
9%
12%
Notes: These benefits are also reflected in the average memory latency, which RBLA-Dyn reduces by 14% over frek in server workloads, by 9% in cloud, and by 12% overall.

## Slide 33: Memory Energy Efficiency
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.99688 | 1.0031 | 1
FREQ-Dyn | 1.0786 | 1.0475 | 1.0629
RBLA | 1.0901 | 1.0386 | 1.064
RBLA-Dyn | 1.1281 | 1.0731 | 1.1002
Increased performance & reduced data movement between DRAM and PCM
7%
10%
13%
Notes: RBLA-Dyn improves memory system energy efficiency by 13% in server workloads, 7% in cloud, and 10% overall.
This is partly due to the increased system performance, and partly due to the reduced data movement between DRAM and PCM because of RBLA-Dyn’s stricter caching criteria.

## Slide 34: Compared to All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
Our mechanism achieves 31% better performance than all PCM, within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 35: Summary
Different memory technologies have different strengths
A hybrid memory system (DRAM-PCM) aims for best of both
Problem: How to place data between these heterogeneous memory devices?
Observation: PCM array access latency is higher than DRAM’s – But peripheral circuit (row buffer) access latencies are similar
Key Idea: Use row buffer locality (RBL) as a key criterion for data placement
Solution: Cache to DRAM rows with low RBL and high reuse
Improves both performance and energy efficiency over state-of-the-art caching policies
Notes: Here’s a one-slide summary of what I’ll describe.
Different memory technologies have different strengths and weaknesses.
A hybrid memory system, for example, one that combines DRAM and Phase Change Memory, aims for the best of both memory technologies.
The Problem is how to place data between these heterogeneous devices in a way that exploits each memory technology’s strengths while minimizing its weaknesses.
Our key observation is that PCM array access latency is higher than DRAM’s, but peripheral circuit access latencies, or what is called row buffer access latencies, are similar.
Our key idea is to use row buffer locality as a key criterion for data placement in a hybrid memory system.
Our solution is to cache to DRAM rows with low row buffer locality and high reuse because these are the rows that would benefit most from DRAM.
This improves both performance and energy efficiency over state-of-the-art caching policies for hybrid memories.

## Slide 36: Row Buffer Locality Aware Caching Policies for Hybrid Memories
HanBin Yoon
Justin Meza
Rachata Ausavarungnirun Rachael Harding
Onur Mutlu

## Slide 37: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
    Row-Locality Aware Data Placement
    Efficient DRAM (or Technology X) Caches
Conclusions
Discussion

## Slide 38: The Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 39: Idea 1: Tags in Memory
Store tags in the same row as data in DRAM
  Store metadata in same row as their data
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 40: Idea 2: Cache Tags in SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 41: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
  Group main memory into sets of rows
  Some row sets follow a fixed caching granularity
  The rest of main memory follows the best granularity
    Cost–benefit analysis: access latency versus number of cachings
    Performed every quantum

## Slide 42: TIMBER Tag Management
A Tag-In-Memory BuffER (TIMBER)
  Stores recently-used tags in a small amount of SRAM
Benefits: If tag is cached:
  no need to access DRAM twice
  cache hit determined quickly
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Row Tag
LOAD X
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 43: TIMBER Tag Management Example (I)
Case 1: TIMBER hit
Bank
Bank
Bank
Bank
CPU
Mem Ctlr
Mem Ctlr
LOAD X
TIMBER: X  DRAM
X
Access X
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Our proposal

## Slide 44: TIMBER Tag Management Example (II)
Case 2: TIMBER miss
CPU
Mem Ctlr
Mem Ctlr
LOAD Y
Y  DRAM
Bank
Bank
Bank
Bank
Access Metadata(Y)
Y
1. Access M(Y)
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Miss
M(Y)
2. Cache M(Y)
Row143
3. Access Y (row hit)

## Slide 45: Methodology
System: 8 out-of-order cores at 4 GHz
Memory: 512 MB direct-mapped DRAM, 8 GB PCM
  128B caching granularity
  DRAM row hit (miss): 200 cycles (400 cycles)
  PCM row hit (clean / dirty miss): 200 cycles (640 / 1840 cycles)
Evaluated metadata storage techniques
  All SRAM system (8MB of SRAM)
  Region metadata storage
  TIM metadata storage (same row as data)
  TIMBER, 64-entry direct-mapped (8KB of SRAM)

## Slide 46
Metadata Storage Performance
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
(Ideal)

## Slide 47
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
-48%
Performance degrades due to increased metadata lookup access latency
(Ideal)

## Slide 48
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
36%
Increased row locality reduces average memory access latency
(Ideal)

## Slide 49
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
23%
Data with locality can access metadata at SRAM latencies
(Ideal)

## Slide 50
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
Dynamic Granularity Performance
10%
Reduced channel contention and improved spatial locality

## Slide 51
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Reduced channel contention and improved spatial locality
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 52
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
Fewer migrations reduce transmitted data and channel contention
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 53: More on Large DRAM Cache Design
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.
Fundamental Latency Trade-offs in Architecting DRAM Caches (pdf, slides) Moinuddin K. Qureshi and Gabriel Loh Appears in the International Symposium on Microarchitecture (MICRO) 2012

## Slide 54: Enabling and Exploiting NVM: Issues
Many issues and ideas from technology layer to algorithms layer
Enabling NVM and hybrid memory
  How to tolerate errors?
  How to enable secure operation?
  How to tolerate performance and power shortcomings?
  How to minimize cost?
Exploiting emerging technologies
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 55: Security Challenges of Emerging Technologies
1. Limited endurance  Wearout attacks
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
3. Multiple bits per cell  Information leakage (via side channel)

## Slide 56: Securing Emerging Memory Technologies
1. Limited endurance  Wearout attacks
Better architecting of memory chips to absorb writes
Hybrid memory system management
Online wearout attack detection
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
Efficient encryption/decryption of whole main memory
Hybrid memory system management
3. Multiple bits per cell  Information leakage (via side channel)
System design to hide side channel information

## Slide 57: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 58: Summary: Memory Scaling (with NVM)
Main memory scaling problems are a critical bottleneck for system performance, efficiency, and usability
Solution 1: Tolerate DRAM
Solution 2: Enable emerging memory technologies
  Replace DRAM with NVM by architecting NVM chips well
  Hybrid memory systems with automatic data management
An exciting topic with many other solution directions & ideas
  Hardware/software/device cooperation essential
  Memory, storage, controller, software/app co-design needed
  Coordinated management of persistent memory and storage
  Application and hardware cooperative management of NVM

## Slide 59: Further: Overview Papers on Two Topics
Merging of Memory and Storage
  Justin Meza, Yixin Luo, Samira Khan, Jishen Zhao, Yuan Xie, and Onur Mutlu, "A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory" Proceedings of the 5th Workshop on Energy-Efficient Design (WEED), Tel-Aviv, Israel, June 2013. Slides (pptx) Slides (pdf)
Flash Memory Scaling
  Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.

## Slide 60: Scalable Many-Core Memory Systems Lecture 4, Topic 2: Emerging Technologies and Hybrid Memories
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 18, 2013

## Slide 61: Computer Architecture: Emerging Memory Technologies (Part II)
Prof. Onur Mutlu
Carnegie Mellon University

## Slide 62: Additional Material

## Slide 63: Overview Papers on Two Topics
Merging of Memory and Storage
  Justin Meza, Yixin Luo, Samira Khan, Jishen Zhao, Yuan Xie, and Onur Mutlu, "A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory" Proceedings of the 5th Workshop on Energy-Efficient Design (WEED), Tel-Aviv, Israel, June 2013. Slides (pptx) Slides (pdf)
Flash Memory Scaling
  Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.

## Slide 64: Merging of Memory and Storage: Persistent Memory Managers

## Slide 65: A Case for Efficient Hardware/Software Cooperative Management of Storage and Memory
Justin Meza*, Yixin Luo*, Samira Khan*†, Jishen Zhao§,
Yuan Xie§‡, and Onur Mutlu*
*Carnegie Mellon University
§Pennsylvania State University
†Intel Labs ‡AMD Research

## Slide 66: Overview
Traditional systems have a two-level storage model
  Access volatile data in memory with a load/store interface
  Access persistent data in storage with a file system interface
  Problem: Operating system (OS) and file system (FS) code and buffering for storage lead to energy and performance inefficiencies
Opportunity: New non-volatile memory (NVM) technologies can help provide fast (similar to DRAM), persistent storage (similar to Flash)
  Unfortunately, OS and FS code can easily become energy efficiency and performance bottlenecks if we keep the traditional storage model
This work: makes a case for hardware/software cooperative management of storage and memory within a single-level
  We describe the idea of a Persistent Memory Manager (PMM) for efficiently coordinating storage and memory, and quantify its benefit
  And, examine questions and challenges to address to realize PMM

## Slide 67: Talk Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 68: A Tale of Two Storage Levels
Traditional systems use a two-level storage model
  Volatile data is stored in DRAM
  Persistent data is stored in HDD and Flash
Accessed through two vastly different interfaces
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …

## Slide 69: A Tale of Two Storage Levels
Two-level storage arose in systems due to the widely different access latencies and methods of the commodity storage devices
  Fast, low capacity, volatile DRAM  working storage
  Slow, high capacity, non-volatile hard disk drives  persistent storage
Data from slow storage media is buffered in fast DRAM
  After that it can be manipulated by programs  programs cannot directly access persistent storage
  It is the programmer’s job to translate this data between the two formats of the two-level storage (files and data structures)
Locating, transferring, and translating data and formats between the two levels of storage can waste significant energy and performance

## Slide 70: Opportunity: New Non-Volatile Memories
Emerging memory technologies provide the potential for unifying storage and memory (e.g., Phase-Change, STT-RAM, RRAM)
  Byte-addressable (can be accessed like DRAM)
  Low latency (comparable to DRAM)
  Low power (idle power better than DRAM)
  High capacity (closer to Flash)
  Non-volatile (can enable persistent storage)
  May have limited endurance (but, better than Flash)
Can provide fast access to both volatile data and persistent storage
Question: if such devices are used, is it efficient to keep a two-level storage model?

## Slide 71: Eliminating Traditional Storage Bottlenecks
Today (DRAM + HDD) and two-level storage model
Replace HDD with NVM (PCM-like), keep two-level storage model
Replace HDD and DRAM with NVM (PCM-like), eliminate all OS+FS overhead
Results for PostMark
Notes: On the x axis are three system designs that we will look at throughout this talk.
The system on the left is a traditional HDD Baseline system that uses DRAM for volatile memory and an HDD for storage and all of the levels of operating system and file system code and buffering required to access persistent data.
The system in the middle is an NVM Baseline system that simply replaces the HDD for NVM – and doesn’t change anything else.
The system on the right is equipped with a Persistent Memory composed entirely of NVM. It manages the placement and location of data using hardware and software and does not execute any OS or FS code to access persistent data.
On the y axis is the fraction of total energy consumed by these systems normalized to the HDD baseline and averaged across the workloads we will later evaluate. As we can see, simply switching the HDD for NVM can greatly reduce total system energy consumption, as is expected from future systems employing such technology. But what is less obvious is how much energy can be reduced by switching from the traditional two-level storage model of the NVM Baseline to the single-level storage model of the Persistent Memory. As we can see, the energy savings can be quite drastic: reducing energy by around 80% on average.
Let’s take a look at where these energy savings come from.

## Slide 72: Eliminating Traditional Storage Bottlenecks
Results for PostMark

## Slide 73: Where is Energy Spent in Each Model?
HDD access
wastes energy
FS/OS overhead becomes important
Additional DRAM energy due to buffering overhead of two-level model
No FS/OS overhead
No additional buffering overhead in DRAM
Results for PostMark
Notes: This figure shows the same systems as before, but breaks down how the they consume energy among several different categories:
User CPU – on the bottom – is the amount of energy consumed by the process executing code on the CPU.
Syscall CPU is the amount of energy consumed to execute the operating system and file system on the program’s behalf on the CPU. Notice that the Persistent Memory system does not consume energy in this category because it does away with OS and FS code for persistent data.
DRAM, NVM, and HDD are the amounts of energy consumed to access and operate each of those devices.
What we can see from this graph is that while the energy spent handling persistent data in the traditional HDD Baseline system is dwarfed by the energy of accessing its devices, in the NVM Baseline system – by just switching the HDD with NVM – the energy consumed to manage persistent data in the traditional way begins to emerge as a significant bottleneck. By eliminating this source of inefficiency in the Persistent Memory system, however, we can improve energy (and as we will later see, performance as well).

## Slide 74: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 75: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well

## Slide 76: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well
Before: Traditional Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …

## Slide 77: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well
After: Coordinated HW/SW Management
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback

## Slide 78: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 79: The Persistent Memory Manager
Persistent Memory Manager
  Exposes a load/store interface to access persistent data
  Manages data placement, location, persistence, security
  Manages metadata storage and retrieval
  Exposes hooks and interfaces for system software
Example program manipulating a persistent object:
Create persistent object and its handle
Allocate a persistent array and assign
Load/store interface
Notes: Here is an example of what a program might look like if written for a system equipped with a persistent memory.
The main function creates a new persistent object called “myData” with the handle “file.dat”. You can see that we use a similar notation to C’s FILE structure. The contents of myData is then set to a newly-allocated *persistent* array of 64 integers.
Later (perhaps after reboots of the machine), the data for the handle “file.dat” is retrieved and the contents of myData is modified and will remain persistent.

## Slide 80: Putting Everything Together
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 81: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 82: Opportunities and Benefits
We’ve identified at least five opportunities and benefits of a unified storage/memory system that gets rid of the two-level model:
  Eliminating system calls for file operations
  Eliminating file system operations
  Efficient data mapping/location among heterogeneous devices
  Providing security and reliability in persistent memories
  Hardware/software cooperative data management

## Slide 83: Eliminating System Calls for File Operations
A persistent memory can expose a large, linear, persistent address space
  Persistent storage objects can be directly manipulated with load/store operations
This eliminates the need for layers of operating system code
  Typically used for calls like open, read, and write
Also eliminates OS file metadata
  File descriptors, file buffers, and so on

## Slide 84: Eliminating File System Operations
Locating files is traditionally done using a file system
  Runs code and traverses structures in software to locate files
Existing hardware structures for locating data in virtual memory can be extended and adapted to meet the needs of persistent memories
  Memory Management Units (MMUs), which map virtual addresses to physical addresses
  Translation Lookaside Buffers (TLBs), which cache mappings of virtual-to-physical address translations
Potential to eliminate file system code
At the cost of additional hardware overhead to handle persistent data storage

## Slide 85: Efficient Data Mapping among Heterogeneous Devices
A persistent memory exposes a large, persistent address space
  But it may use many different devices to satisfy this goal
  From fast, low-capacity volatile DRAM to slow, high-capacity non-volatile HDD or Flash
  And other NVM devices in between
Performance and energy can benefit from good placement of data among these devices
  Utilizing the strengths of each device and avoiding their weaknesses, if possible
  For example, consider two important application characteristics: locality and persistence

## Slide 86: Efficient Data Mapping among Heterogeneous Devices
Notes: Here, we’ve plotted these two important characteristics as axes on a graph. On the bottom is persistence, from temporary – the data does not need to be saved across program executions – on the left to persistent – the data must remain across executions for correct operation – on the right. From bottom to top we have data that has more locality – and is accessed very frequently in a short amount of time or space – to data that has less locality – which may predominantly be accessed in a random manner.
Let’s take a look at two examples of data and how they map onto this space.

## Slide 87: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
Notes: First we have some data that requires high persistence but has little locality. Such data might be the columns in a column store that are only scanned through infrequently. While it is essential that this data remain persistent across runs of the program, it may not be accessed that frequently, and therefore may be more beneficial to place on slightly slower, persistent memory devices, such as Flash.

## Slide 88: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
X
Frequently-updated index for a Content Delivery Network (CDN)  place in DRAM
Applications or system software can provide hints for data placement
Notes: On the other end of the perspective is data that has high locality but is only ephemeral and not needed between executions. Data in a Content Delivery Network that is cached as it is accessed and is constantly being updated and replaced, is a great candidate for placing in DRAM on such systems.

## Slide 89: Providing Security and Reliability
A persistent memory deals with data at the granularity of bytes and not necessarily files
  Provides the opportunity for much finer-grained security and protection than traditional two-level storage models provide/afford
  Need efficient techniques to avoid large metadata overheads
A persistent memory can improve application reliability by ensuring updates to persistent data are less vulnerable to failures
  Need to ensure that changes to copies of persistent data placed in volatile memories become persistent

## Slide 90: HW/SW Cooperative Data Management
Persistent memories can expose hooks and interfaces to applications, the OS, and runtimes
  Have the potential to provide improved system robustness and efficiency than by managing persistent data with either software or hardware alone
Can enable fast checkpointing and reboots, improve application reliability by ensuring persistence of data
  How to redesign availability mechanisms to take advantage of these?
Persistent locks and other persistent synchronization constructs can enable more robust programs and systems

## Slide 91: Quantifying Persistent Memory Benefits
We have identified several opportunities and benefits of using persistent memories without the traditional two-level store model
We will next quantify:
  How do persistent memories affect system performance?
  How much energy reduction is possible?
  Can persistent memories achieve these benefits despite additional access latencies to the persistent memory manager?

## Slide 92: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 93: Evaluation Methodology
Hybrid real system / simulation-based approach
  System calls are executed on host machine (functional correctness) and timed to accurately model their latency in the simulator
  Rest of execution is simulated in Multi2Sim (enables hardware-level exploration)
Power evaluated using McPAT and memory power models
16 cores, 4-wide issue, 128-entry instruction window, 1.6 GHz
Volatile memory: 4GB DRAM, 4KB page size, 100-cycle latency
Persistent memory
  HDD (measured): 4ms seek latency, 6Gbps bus rate
  NVM: (modeled after PCM) 4KB page size, 160-/480-cycle (read/write) latency

## Slide 94: Evaluated Systems
HDD Baseline (HB)
  Traditional system with volatile DRAM memory and persistent HDD storage
  Overheads of operating system and file system code and buffering
HDD without OS/FS (HW)
  Same as HDD Baseline, but with the ideal elimination of all OS/FS overheads
  System calls take 0 cycles (but HDD access takes normal latency)
NVM Baseline (NB)
  Same as HDD Baseline, but HDD is replaced with NVM
  Still has OS/FS overheads of the two-level storage model
Persistent Memory (PM)
  Uses only NVM (no DRAM) to ensure full-system persistence
  All data accessed using loads and stores
  Does not waste energy on system calls
  Data is manipulated directly on the NVM device

## Slide 95: Evaluated Workloads
Unix utilities that manipulate files
  cp: copy a large file from one location to another
  cp –r: copy files in a directory tree from one location to another
  grep: search for a string in a large file
  grep –r: search for a string recursively in a directory tree
PostMark: an I/O-intensive benchmark from NetApp
  Emulates typical access patterns for email, news, web commerce
MySQL Server: a popular database management system
  OLTP-style queries generated by Sysbench
  MySQL (simple): single, random read to an entry
  MySQL (complex): reads/writes 1 to 100 entries per transaction

## Slide 96: Performance Results

## Slide 97: Performance Results: HDD w/o OS/FS
For HDD-based systems, eliminating OS/FS overheads typically leads to small performance improvements  execution time dominated by HDD access latency

## Slide 98: Performance Results: HDD w/o OS/FS
Though, for more complex file system operations like directory traversal (seen with cp -r and grep -r), eliminating the OS/FS overhead improves performance

## Slide 99: Performance Results: HDD to NVM
Switching from an HDD to NVM greatly reduces execution time due to NVM’s much faster access latencies, especially for I/O-intensive workloads (cp, PostMark, MySQL)

## Slide 100: Performance Results: NVM to PMM
For most workloads, eliminating OS/FS code and buffering improves performance greatly on top of the NVM Baseline system
(even when DRAM is eliminated from the system)
Notes: grep and grep -r are CPU-intensive, so the change is not as large

## Slide 101: Performance Results
The workloads that see the greatest improvement from using a Persistent Memory are those that spend a large portion of their time executing system call code due to the two-level storage model

## Slide 102: Energy Results

## Slide 103: Energy Results: HDD to NVM
Between HDD-based and NVM-based systems, lower NVM energy leads to greatly reduced energy consumption

## Slide 104: Energy Results: NVM to PMM
Between systems with and without OS/FS code, energy improvements come from:
1. reduced code footprint, 2. reduced data movement
Large energy reductions with a PMM over the NVM based system
Notes: Reduced code footprint lowers *both* static and dynamic energy consumption by reducing number of instructions required to perform the same amount of work
Reduced data movement lowers static energy consumption

## Slide 105: Scalability Analysis: Effect of PMM Latency
Even if each PMM access takes a non-overlapped 50 cycles (conservative),
PMM still provides an overall improvement compared to the NVM baseline
Future research should target keeping PMM latencies in check
Notes: Up until this point, we have assumed that the PMM requires no additional overhead in order to explore the potential of systems with persistent memory. This figure shows how execution time varies as the latency *per memory access* to the PMM is varied from 1 to 100 cycles. Note that this estimate is conservative in the sense that it does not consider the potential for overlapping multiple access latencies in the PMM.
For each benchmark, the categories are normalized to the performance of the NVM Baseline system, shown on the left.

## Slide 106: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 107: Related Work
We provide a comprehensive overview of past work related to single-level stores and persistent memory techniques
  Integrating file systems with persistent memory
    Need optimized hardware to fully take advantage of new technologies
  Programming language support for persistent objects
    Incurs the added latency of indirect data access through software
  Load/store interfaces to persistent storage
    Lack efficient and fast hardware support for address translation, efficient file indexing, fast reliability and protection guarantees
  Analysis of OS overheads with Flash devices
    Our study corroborates findings in this area and shows even larger consequences for systems with emerging NVM devices
The goal of our work is to provide cheap and fast hardware support for memories to enable high energy efficiency and performance

## Slide 108: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 109: New Questions and Challenges
We identify and discuss several open research questions
Q1. How to tailor applications for systems with persistent memory?
Q2. How can hardware and software cooperate to support a scalable, persistent single-level address space?
Q3. How to provide efficient backward compatibility (for two-level stores) on persistent memory systems?
Q4. How to mitigate potential hardware performance and energy overheads?
Notes: (Say *in words* some of the talking points from the paper):
Q1. How should data be intelligently partitioned among devices?
How can data be efficiently transmitted between devices?
How can software be designed for improved fault tolerance?
How does persistent memory change models for availability?
Q2. What is the right interface between persistent memory and software?
What types of hooks and access data should be exposed to the software?
How can software signal to hardware that applications have particular access patterns?
How can software help provide consistency, reliability, and protection among heterogeneous devices?
Q3. How to efficiently support legacy system functionality (e.g., run HDD Baseline code on Persistent Memory and have it run nearly as fast as code designed for the Persistent Memory system)
How can devices in a persistent memory efficiently manage legacy interface (e.g., filesystem, page table) metadata?
Q4. A key challenge will be to keep accesses to a persistent memory fast, how this can be done efficiently (e.g., in between 10 to 50 cycles per access) is an important open area for future research.

## Slide 110: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 111: Summary and Conclusions
Traditional two-level storage model is inefficient in terms of performance and energy
  Due to OS/FS code and buffering needed to manage two models
  Especially so in future devices with NVM technologies, as we show
New non-volatile memory based persistent memory designs that use a single-level storage model to unify memory and storage can alleviate this problem
We quantified the performance and energy benefits of such a single-level persistent memory/storage design
  Showed significant benefits from reduced code footprint, data movement, and system software overhead on a variety of workloads
Such a design requires more research to answer the questions we have posed and enable efficient persistent memory managers
   can lead to a fundamentally more efficient storage system

## Slide 112: A Case for Efficient Hardware/Software Cooperative Management of Storage and Memory
Justin Meza*, Yixin Luo*, Samira Khan*†, Jishen Zhao§,
Yuan Xie§‡, and Onur Mutlu*
*Carnegie Mellon University
§Pennsylvania State University
†Intel Labs ‡AMD Research

## Slide 113: Flash Memory Scaling

## Slide 114: Readings in Flash Memory
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (ppt) (pdf)
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 115: Evolution of NAND Flash Memory
Flash memory widening its range of applications
  Portable consumer devices, laptop PCs and enterprise servers
Seaung Suk Lee, “Emerging Challenges in NAND Flash Technology”, Flash Summit 2011 (Hynix)
CMOS scaling
More bits per Cell

## Slide 116: Decreasing Endurance with Flash Scaling
UBER: Uncorrectable bit error rate. Fraction of erroneous bits after error correction.
Endurance of flash memory decreasing with scaling and multi-level cells
Error correction capability required to guarantee storage-class reliability (UBER < 10-15) is increasing exponentially to reach less endurance
Ariel Maislos, “A New Era in Embedded Flash Memory”, Flash Summit 2011 (Anobit)
Chart: P/E Cycle Endurance
| SLC | 5x-nm MLC | 3x-nm MLC | 2x-nm MLC | 3-bit-MLC
 | 100000 | 10000 | 5000 | 3000 | 1000
100k
10k
5k
3k
1k
4-bit ECC
8-bit ECC
15-bit ECC
24-bit ECC
Error Correction Capability
(per 1 kB of data)

## Slide 117: Future NAND Flash Storage Architecture
Memory
Signal
Processing
Error
Correction
Raw Bit
Error Rate
Hamming codes
BCH codes
Reed-Solomon codes
LDPC codes
Other Flash friendly codes
BER < 10-15
Need to understand NAND flash error patterns
Read voltage adjusting
Data scrambler
Data recovery
Soft-information estimation
Noisy

## Slide 118: Test System Infrastructure
Host USB PHY
USB Driver
Software Platform
USB
PHYChip
Control
Firmware
FPGA
USB controller
NAND
Controller
Signal Processing
Wear Leveling
Address Mapping
Garbage Collection
Algorithms
ECC
(BCH, RS, LDPC)
Flash
Memories
Host Computer
USB Daughter Board
Mother Board
Flash Board
Reset
Erase block
Program page
Read page

## Slide 119: NAND Flash Testing Platform
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash

## Slide 120: NAND Flash Usage and Error Model
…
(Page0 - Page128)
Program
Page
Erase
Block
Retention1
(t1 days)
Read
Page
Retention j
(tj days)
Read
Page
P/E cycle 0
P/E cycle i
Start
…
P/E cycle n
…
End of life
Erase Errors
Program Errors
Retention Errors
Read Errors
Read Errors
Retention Errors
Notes: 13
lots of diagrams of boxes and text, need to find a way to differentiate them

## Slide 121: Error Types and Testing Methodology
Erase errors
  Count the number of cells that fail to be erased to “11” state
Program interference errors
  Compare the data immediately after page programming and the data after the whole block being programmed
Read errors
  Continuously read a given block and compare the data between consecutive read sequences
Retention errors
  Compare the data read after an amount of time to data written
    Characterize short term retention errors under room temperature
    Characterize long term retention errors by baking in the oven under 125℃

## Slide 122: Observations: Flash Error Analysis
retention errors
Raw bit error rate increases exponentially with P/E cycles
Retention errors are dominant (>99% for 1-year ret. time)
Retention errors increase with retention time requirement
P/E Cycles
Raw Bit Error Rate

## Slide 123: Retention Error Mechanism
LSB/MSB
Electron loss from the floating gate causes retention errors
  Cells with more programmed electrons suffer more from retention errors
  Threshold voltage is more likely to shift by one window than by multiple
11
10
01
00
Vth
REF1
REF2
REF3
Erased
Fully programmed
Stress Induced Leakage Current (SILC)
Floating
Gate
Notes: 16
explain what the diagram is showing
animate in distribution spread

## Slide 124: Retention Error Value Dependency
00 01
01 10
Cells with more programmed electrons tend to suffer more from retention noise (i.e. 00 and 01)

## Slide 125: More Details on Flash Error Analysis
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 126: Threshold Voltage Distribution Shifts
As P/E cycles increase ...
Distribution shifts to the right
Distribution becomes wider
Notes: This plot shows the probability density function of the cell threshold voltage as the number of program/erase cycles increases.
As the wear on the cells increase, we can see the distributions broadening and shifting to the right (higher voltages).
As around 30k cycles, the distributions in adjacent states begin to overlap, meaning that a read error is possible.
However, we note that the manufacturer cell lifetime is typically only around 5k cycles, so errors due to wear would not be evident at those wear levels.

## Slide 127: More Detail
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)

## Slide 128: Flash Correct-and-Refresh Retention-Aware Error Management for Increased Flash Memory Lifetime
Yu Cai1 Gulay Yalcin2 Onur Mutlu1 Erich F. Haratsch3
Adrian Cristal2 Osman S. Unsal2 Ken Mai1
1 Carnegie Mellon University
2 Barcelona Supercomputing Center
3 LSI Corporation

## Slide 129: Executive Summary
NAND flash memory has low endurance: a flash cell dies after 3k P/E cycles vs. 50k desired  Major scaling challenge for flash memory
Flash error rate increases exponentially over flash lifetime
Problem: Stronger error correction codes (ECC) are ineffective and undesirable for improving flash lifetime due to
  diminishing returns on lifetime with increased correction strength
  prohibitively high power, area, latency overheads
Our Goal: Develop techniques to tolerate high error rates w/o strong ECC
Observation: Retention errors are the dominant errors in MLC NAND flash
  flash cell loses charge over time; retention errors increase as cell gets worn out
Solution: Flash Correct-and-Refresh (FCR)
  Periodically read, correct, and reprogram (in place) or remap each flash page before it accumulates more errors than can be corrected by simple ECC
  Adapt “refresh” rate to the severity of retention errors (i.e., # of P/E cycles)
Results: FCR improves flash memory lifetime by 46X with no hardware changes and low energy overhead; outperforms strong ECCs

## Slide 130: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
Evaluation
Conclusions

## Slide 131: Problem: Limited Endurance of Flash Memory
NAND flash has limited endurance
  A cell can tolerate a small number of Program/Erase (P/E) cycles
  3x-nm flash with 2 bits/cell  3K P/E cycles
Enterprise data storage requirements demand very high endurance
  >50K P/E cycles (10 full disk writes per day for 3-5 years)
Continued process scaling and more bits per cell will reduce flash endurance
One potential solution: stronger error correction codes (ECC)
  Stronger ECC not effective enough and inefficient

## Slide 132: Decreasing Endurance with Flash Scaling
UBER: Uncorrectable bit error rate. Fraction of erroneous bits after error correction.
Endurance of flash memory decreasing with scaling and multi-level cells
Error correction capability required to guarantee storage-class reliability (UBER < 10-15) is increasing exponentially to reach less endurance
Ariel Maislos, “A New Era in Embedded Flash Memory”, Flash Summit 2011 (Anobit)
Chart: P/E Cycle Endurance
| SLC | 5x-nm MLC | 3x-nm MLC | 2x-nm MLC | 3-bit-MLC
 | 100000 | 10000 | 5000 | 3000 | 1000
100k
10k
5k
3k
1k
4-bit ECC
8-bit ECC
15-bit ECC
24-bit ECC
Error Correction Capability
(per 1 kB of data)

## Slide 133: The Problem with Stronger Error Correction
Stronger ECC detects and corrects more raw bit errors  increases P/E cycles endured
Two shortcomings of stronger ECC:
  1. High implementation complexity
   Power and area overheads increase super-linearly, but correction capability increases sub-linearly with ECC strength
  2. Diminishing returns on flash lifetime improvement
   Raw bit error rate increases exponentially with P/E cycles, but correction capability increases sub-linearly with ECC strength

## Slide 134: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
Evaluation
Conclusions

## Slide 135: Methodology: Error and ECC Analysis
Characterized errors and error rates of 3x-nm MLC NAND flash using an experimental FPGA-based flash platform
  Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Quantified Raw Bit Error Rate (RBER) at a given P/E cycle
  Raw Bit Error Rate: Fraction of erroneous bits without any correction
Quantified error correction capability (and area and power consumption) of various BCH-code implementations
  Identified how much RBER each code can tolerate
   how many P/E cycles (flash lifetime) each code can sustain

## Slide 136: NAND Flash Error Types
Four types of errors [Cai+, DATE 2012]
Caused by common flash operations
  Read errors
  Erase errors
  Program (interference) errors
Caused by flash cell losing charge over time
  Retention errors
    Whether an error happens depends on required retention time
    Especially problematic in MLC flash because voltage threshold window to determine stored value is smaller

## Slide 137: Observations: Flash Error Analysis
retention errors
Raw bit error rate increases exponentially with P/E cycles
Retention errors are dominant (>99% for 1-year ret. time)
Retention errors increase with retention time requirement
P/E Cycles
Raw Bit Error Rate

## Slide 138: Methodology: Error and ECC Analysis
Characterized errors and error rates of 3x-nm MLC NAND flash using an experimental FPGA-based flash platform
  Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Quantified Raw Bit Error Rate (RBER) at a given P/E cycle
  Raw Bit Error Rate: Fraction of erroneous bits without any correction
Quantified error correction capability (and area and power consumption) of various BCH-code implementations
  Identified how much RBER each code can tolerate
   how many P/E cycles (flash lifetime) each code can sustain

## Slide 139: ECC Strength Analysis
Examined characteristics of various-strength BCH codes with the following criteria
  Storage efficiency: >89% coding rate (user data/total storage)
  Reliability: <10-15 uncorrectable bit error rate
  Code length: segment of one flash page (e.g., 4kB)
Error correction capability increases sub-linearly
Power and area overheads increase super-linearly

## Slide 140: Resulting Flash Lifetime with Strong ECC
Lifetime improvement comparison of various BCH codes
Chart: P/E Cycle Endurance
| 512b-BCH | 1k-BCH | 2k-BCH | 4k-BCH | 8k-BCH | 32k-BCH
Lifetime | 3000 | 7000 | 10000 | 10500 | 11200 | 12000
4X Lifetime
Improvement
71X Power Consumption
85X Area Consumption
Strong ECC is very inefficient at improving lifetime

## Slide 141: Our Goal
Develop new techniques
to improve flash lifetime
without relying on stronger ECC

## Slide 142: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
Evaluation
Conclusions

## Slide 143: Flash Correct-and-Refresh (FCR)
Key Observations:
  Retention errors are the dominant source of errors in flash memory [Cai+ DATE 2012][Tanakamaru+ ISSCC 2011]
   limit flash lifetime as they increase over time
  Retention errors can be corrected by “refreshing” each flash page periodically
Key Idea:
  Periodically read each flash page,
  Correct its errors using “weak” ECC, and
  Either remap it to a new physical page or reprogram it in-place,
  Before the page accumulates more errors than ECC-correctable
  Optimization: Adapt refresh rate to endured P/E cycles

## Slide 144: FCR Intuition
Errors with
No refresh
ProgramPage
×
After time T
×
×
×
After time 2T
×
×
×
×
×
After time 3T
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
×
Errors with
Periodic refresh
×
×
Retention Error
×
Program Error

## Slide 145: FCR: Two Key Questions
How to refresh?
  Remap a page to another one
  Reprogram a page (in-place)
  Hybrid of remap and reprogram
When to refresh?
  Fixed period
  Adapt the period to retention error severity

## Slide 146: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
  1. Remapping based FCR
  2. Hybrid Reprogramming and Remapping based FCR
  3. Adaptive-Rate FCR
Evaluation
Conclusions

## Slide 147: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
  1. Remapping based FCR
  2. Hybrid Reprogramming and Remapping based FCR
  3. Adaptive-Rate FCR
Evaluation
Conclusions

## Slide 148: Remapping Based FCR
Idea: Periodically remap each page to a different physical page (after correcting errors)
  Also [Pan et al., HPCA 2012]
  FTL already has support for
  changing logical  physical
  flash block/page mappings
  Deallocated block is
  erased by garbage collector
Problem: Causes additional erase operations  more wearout
  Bad for read-intensive workloads (few erases really needed)
  Lifetime degrades for such workloads (see paper)

## Slide 149: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
  1. Remapping based FCR
  2. Hybrid Reprogramming and Remapping based FCR
  3. Adaptive-Rate FCR
Evaluation
Conclusions

## Slide 150: In-Place Reprogramming Based FCR
Idea: Periodically reprogram (in-place) each physical page (after correcting errors)
  Flash programming techniques
  (ISPP) can correct retention
  errors in-place by recharging
  flash cells
Problem: Program errors accumulate on the same page  may not be correctable by ECC after some time
Reprogram corrected data
Notes: Observations:
  Retention errors occur due to loss of charge
  Simply recharging the cells can correct the retention errors
  Flash programming mechanisms can accomplish this recharging
ISPP (Incremental Step Pulse Programming)
  Iterative programming mechanism that increases the voltage level of a flash cell step by step
  After each step, voltage level compared to desired voltage threshold
  Can inject more electrons but cannot remove electrons

## Slide 151: In-Place Reprogramming of Flash Cells
Pro: No remapping needed  no additional erase operations
Con: Increases the occurrence of program errors
Retention errors are caused by cell voltage shifting to the left
ISPP moves cell voltage to the right; fixes retention errors
Floating Gate
Voltage Distribution
for each Stored Value
Floating Gate

## Slide 152: Program Errors in Flash Memory
When a cell is being programmed, voltage level of a neighboring cell changes (unintentionally) due to parasitic capacitance coupling
 can change the data value stored
Also called program interference error
Program interference causes neighboring cell voltage to shift to the right

## Slide 153: Problem with In-Place Reprogramming
11
10
01
00
VT
REF1
REF2
REF3
Floating
Gate
Additional
Electrons Injected
…
…
11
01
00
10
11
00
00
Original data
to be programmed
…
…
10
01
00
10
11
00
00
Program errors after
initial programming
…
…
Retention errors
after some time
10
10
00
11
11
01
01
…
…
Errors after in-place
reprogramming
10
01
00
10
10
00
00
1. Read data
2. Correct errors
3. Reprogram back
Problem: Program errors can accumulate over time
Floating Gate
Voltage Distribution

## Slide 154: Hybrid Reprogramming/Remapping Based FCR
Idea:
  Monitor the count of right-shift errors (after error correction)
  If count < threshold, in-place reprogram the page
  Else, remap the page to a new page
Observation:
  Program errors much less frequent than retention errors  Remapping happens only infrequently
Benefit:
  Hybrid FCR greatly reduces erase operations due to remapping

## Slide 155: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
  1. Remapping based FCR
  2. Hybrid Reprogramming and Remapping based FCR
  3. Adaptive-Rate FCR
Evaluation
Conclusions

## Slide 156: Adaptive-Rate FCR
Observation:
  Retention error rate strongly depends on the P/E cycles a flash page endured so far
  No need to refresh frequently (at all) early in flash lifetime
Idea:
  Adapt the refresh rate to the P/E cycles endured by each page
  Increase refresh rate gradually with increasing P/E cycles
Benefits:
  Reduces overhead of refresh operations
  Can use existing FTL mechanisms that keep track of P/E cycles

## Slide 157: Adaptive-Rate FCR (Example)
Acceptable raw BER for 512b-BCH
3-year
FCR
3-month
FCR
3-week
FCR
3-day
FCR
P/E Cycles
Raw Bit Error Rate
Select refresh frequency such that error rate is below acceptable rate

## Slide 158: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
  1. Remapping based FCR
  2. Hybrid Reprogramming and Remapping based FCR
  3. Adaptive-Rate FCR
Evaluation
Conclusions

## Slide 159: FCR: Other Considerations
Implementation cost
  No hardware changes
  FTL software/firmware needs modification
Response time impact
  FCR not as frequent as DRAM refresh; low impact
Adaptation to variations in retention error rate
  Adapt refresh rate based on, e.g., temperature [Liu+ ISCA 2012]
FCR requires power
  Enterprise storage systems typically powered on

## Slide 160: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
Evaluation
Conclusions

## Slide 161: Evaluation Methodology
Experimental flash platform to obtain error rates at different P/E cycles [Cai+ DATE 2012]
Simulation framework to obtain P/E cycles of real workloads: DiskSim with SSD extensions
Simulated system: 256GB flash, 4 channels, 8 chips/channel, 8K blocks/chip, 128 pages/block, 8KB pages
Workloads
  File system applications, databases, web search
  Categories: Write-heavy, read-heavy, balanced
Evaluation metrics
  Lifetime (extrapolated)
  Energy overhead, P/E cycle overhead

## Slide 162: Extrapolated Lifetime
Maximum full disk P/E Cycles for a Technique
Total full disk P/E Cycles for a Workload
×
# of Days of Given Application
Obtained from Experimental Platform Data
Obtained from Workload Simulation
Real length (in time) of
each workload trace

## Slide 163: Normalized Flash Memory Lifetime
Chart: Normalized Lifetime
| 512b-BCH | 1k-BCH | 2k-BCH | 4k-BCH | 8k-BCH | 32k-BCH
Base (No-Refresh) | 1 | 2.3 | 3.4 | 3.6 | 3.7 | 4
Remapping-Based FCR | 9.6244 | 21.329 | 26.7111 | 31.2028 | 34.4125 | 42.8304
Hybrid FCR | 31.3981 | 68.2528 | 85.4755 | 99.8488 | 110.1199 | 137.0573
Adaptive FCR | 46.5972 | 102.3792 | 128.2132 | 149.7732 | 165.1799 | 197.8765
46x
Adaptive-rate FCR provides the highest lifetime
Lifetime of FCR much higher than lifetime of stronger ECC
4x

## Slide 164: Lifetime Evaluation Takeaways
Significant average lifetime improvement over no refresh
  Adaptive-rate FCR: 46X
  Hybrid reprogramming/remapping based FCR: 31X
  Remapping based FCR: 9X
FCR lifetime improvement larger than that of stronger ECC
  46X vs. 4X with 32-kbit ECC (over 512-bit ECC)
  FCR is less complex and less costly than stronger ECC
Lifetime on all workloads improves with Hybrid FCR
  Remapping based FCR can degrade lifetime on read-heavy WL
  Lifetime improvement highest in write-heavy workloads

## Slide 165: Energy Overhead
Adaptive-rate refresh: <1.8% energy increase until daily refresh is triggered
Chart: Energy Overhead
| 1 Year | 3 Months | 3 Weeks | 3 Days | 1 Day
Remapping-based Refresh | 0.0002 | 0.0009 | 0.0037 | 0.026 | 0.078
Hybrid Refresh | 0.0002 | 0.0005 | 0.0026 | 0.0183 | 0.055
7.8%
5.5%
2.6%
1.8%
0.4%
0.3%
Refresh Interval

## Slide 166: Overhead of Additional Erases
Additional erases happen due to remapping of pages
Low (2%-20%) for write intensive workloads
High (up to 10X) for read-intensive workloads
Improved P/E cycle lifetime of all workloads largely outweighs the additional P/E cycles due to remapping

## Slide 167: More Results in the Paper
Detailed workload analysis
Effect of refresh rate

## Slide 168: Outline
Executive Summary
The Problem: Limited Flash Memory Endurance/Lifetime
Error and ECC Analysis for Flash Memory
Flash Correct and Refresh Techniques (FCR)
Evaluation
Conclusions

## Slide 169: Conclusion
NAND flash memory lifetime is limited due to uncorrectable errors, which increase over lifetime (P/E cycles)
Observation: Dominant source of errors in flash memory is retention errors  retention error rate limits lifetime
Flash Correct-and-Refresh (FCR) techniques reduce retention error rate to improve flash lifetime
  Periodically read, correct, and remap or reprogram each page before it accumulates more errors than can be corrected
  Adapt refresh period to the severity of errors
FCR improves flash lifetime by 46X at no hardware cost
  More effective and efficient than stronger ECC
  Can enable better flash memory scaling

## Slide 170: Flash Correct-and-Refresh Retention-Aware Error Management for Increased Flash Memory Lifetime
Yu Cai1 Gulay Yalcin2 Onur Mutlu1 Erich F. Haratsch3
Adrian Cristal2 Osman S. Unsal2 Ken Mai1
1 Carnegie Mellon University
2 Barcelona Supercomputing Center
3 LSI Corporation