## Slide 1: Scalable Many-Core Memory Systems Topic 3: Memory Interference and QoS-Aware Memory Systems
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013

## Slide 2: Parallelism-Aware Batch Scheduling
Onur Mutlu and Thomas Moscibroda, "Parallelism-Aware Batch Scheduling: Enhancing both
Performance and Fairness of Shared DRAM Systems” 35th International Symposium on Computer Architecture (ISCA),
pages 63-74, Beijing, China, June 2008. Slides (ppt)
PAR-BS ISCA 2008 Talk

## Slide 3: Another Problem due to Memory Interference
Processors try to tolerate the latency of DRAM requests by generating multiple outstanding requests
  Memory-Level Parallelism (MLP)
  Out-of-order execution, non-blocking caches, runahead execution
Effective only if the DRAM controller actually services the multiple requests in parallel in DRAM banks
Multiple threads share the DRAM controller
DRAM controllers are not aware of a thread’s MLP
  Can service each thread’s outstanding requests serially, not in parallel
Notes: Modern processors try to amortize the latency of DRAM requests by generating multiple outstanding requests
This concept is called memory-level parallelism.
Many techniques, such as OOO, non-blocking caches and runahead execution, are designed or used to tolerate long memory latencies by exploiting memory-level parallelism
These latency tolerance techniques are effective only if the DRAM controller actually services the multiple requests of a thread in parallel in DRAM banks
This is true in a single-threaded system since only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads share the DRAM controller.
Unfortunately, existing DRAM controllers are not aware of each thread’s memory level parallelism
As a result they can service each thread’s outstanding requests serially, not in parallel
Let’s take a look at why this happens.
-----------------------------------------
Assuming requests are to different banks
In a single core system this is fine because only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads shared the DRAM controller.
Unfortunately, DRAM controllers are unaware of a thread’s MLP. As a result, because threads can interfere with each other in the DRAM system, they can service each thread’s requests serially instead of in parallel.
Let’s take a look at why this happens.

## Slide 4: Bank Parallelism of a Thread
Thread A: Bank 0, Row 1
Thread A: Bank 1, Row 1
Bank access latencies of the two requests overlapped
Thread stalls for ~ONE bank access latency
Thread A :
Bank 0
Bank 1
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
Single Thread:
Notes: I will demonstrate this pictorially with an example.
Let’s say a thread A executes until it encounters 2 DRAM requests caused by two of its load instructions. These requests are sent to the DRAM controller. And, the controller services them by first scheduling the request to Bank 0 and then scheduling the request to Bank 1. While the requests are being serviced in parallel in the banks, the thread stalls (waiting for the data). Once the servicing of the requests completes, the thread can continue execution.
Since the requests were serviced in parallel in the two banks, bank access latencies of the two requests are overlapped. As a result, the thread stalls for approximately one bank access latency, instead of two bank access latencies.

## Slide 5: Bank Parallelism Interference in DRAM
Compute
Compute
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
Compute
2 DRAM Requests
Bank 0
Stall
Bank 1
Baseline Scheduler:
B:
Compute
Bank 0
Stall
Bank 1
Stall
Stall
Bank access latencies of each thread serialized
Each thread stalls for ~TWO bank access latencies
Notes: What happens when we run two of these threads together in a dual-core system? Again, both threads execute until each encounters 2 DRAM requests. These requests are sent to the DRAM controller. Assume they arrive in the order shown. And the controller services them in the order they arrive.
The controller first takes Thread A’s request to Bank 0 and schedules it. It then schedules Thread B’s request to Bank 1. While these two requests are serviced in parallel, both threads stall.
Once the first request to Bank 0 is done, the controller takes Thread B’s request to bank 0 and schedules it. And it takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel, both threads stall.
Once the requests are complete, the threads continue computation.
In this case, because the threads’ requests interfered with each other in the DRAM system, the bank access latencies of each thread were serialized because the requests were serialized. As a result both threads stall for two bank access latencies instead of 1, which is what each thread experienced when running alone.
This is because the DRAM controller did not try to preserve the bank parallelism of each thread.

## Slide 6: Parallelism-Aware Scheduler
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
2 DRAM Requests
Parallelism-aware Scheduler:
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
2 DRAM Requests
A :
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
Stall
Baseline Scheduler:
Compute
Bank 0
Stall
Compute
Bank 1
Saved Cycles
Average stall-time: ~1.5 bank access latencies
Notes: Can we do better than this? Let me describe what a parallelism aware scheduler would do.
This is the same example. The two threads compute until they each generate 2 DRAM requests, which arrive at the controller in the same order as before. The controller first takes Thread A’s request to Bank 0 and schedules it. But then, instead of servicing the requests in their arrival order, it realizes there is another request from Thread A to Bank 1 and if it schedules that one back to back with Thread A’s previous request, thread A’s request latencies would be overlapped.
Therefore, the controller takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel in the banks, both threads stall.
Once the request to Bank 0 is complete, the controller takes Thread B’s request to Bank 0 and schedules it. Later, it schedules Thread B’s request to Bank 1. While these two requests are being serviced, Thread B stalls (because it does not have the data it needs), but thread A can do useful computation! This is because its requests were serviced in parallel in the banks, instead of serially, and the thread has all the data it needs to do useful computation. As a result, the execution time of Thread A reduces compared to the baseline scheduler that was not aware of the threads’ bank parallelism.
Overall system throughput also improves because the average stall-time of the threads is 1.5 bank access latencies instead of 2. Instead of stalling, cores can make progress executing their instruction streams.

## Slide 7: Parallelism-Aware Batch Scheduling (PAR-BS)
Principle 1: Parallelism-awareness
  Schedule requests from a thread (to different banks) back to back
  Preserves each thread’s bank parallelism
  But, this can cause starvation…
Principle 2: Request Batching
  Group a fixed number of oldest requests from each thread into a “batch”
  Service the batch before all other requests
  Form a new batch when the current one is done
  Eliminates starvation, provides fairness
  Allows parallelism-awareness within a batch
Bank 0
Bank 1
T1
T1
T0
T0
T2
T2
T3
T3
T2
T2
T2
Batch
T0
T1
T1
  Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008.
Notes: Parallelism aware batch scheduling uses two key principles. The first principle is parallelism awareness. As I showed you before, a thread’s bank parallelism is improved by scheduling requests from a thread to different banks back to back. Unfortunately, doing this greedily can cause starvation because a thread whose requests are continuously scheduled back to back can keep on generating more requests and therefore deny service to other threads that are waiting to access the same bank.
  To avoid this, we use a second principle, called request batching. With this, the controller groups a fixed number of oldest requests from each thread into a “batch”. And, it services the batch before all other requests. It forms a new batch when the current one is done.
  Batching eliminates starvation of requests and threads, and provides fairness. It also allows parallelism of each thread to be optimized for within a batch.
  Let’s take a look at how this works pictorially.
  Multiple threads send requests to the DRAM controller. The controller groups these requests into a batch. Once a batch is formed any newly arriving requests are not included in the batch. Within the batch, the controller schedules each thread’s requests in parallel. It first takes TX’s requests and schedules them in parallel. Then it takes TY’s requests and schedules them in parallel. Note that incoming requests from T3 that are outside the batch are not serviced. Once all requests in the batch are serviced in a parallelism-aware manner, the controller forms a new batch with the requests in the memory request buffer.

## Slide 8: PAR-BS Components
Request batching
Within-batch scheduling
  Parallelism aware
Notes: PAR-BS has two components, which I will describe in more detail. The first is request batching. Aside from guaranteeing starvation freedom and providing fairness, a batch provides a flexible substrate that enables aggressive scheduling optimizations (within the batch).
The second component is the within-batch scheduling component. Within a batch, any DRAM scheduling policy can be employed. And, this policy can be very aggressive and possibly unfair in the global sense. Because the overlying batching scheme ensures forward progress in each thread. In fact, we use a globally unfair shortest job first scheduling policy within a batch, to optimize each thread’s bank parallelism.

## Slide 9: Request Batching
Each memory request has a bit (marked) associated with it
Batch formation:
  Mark up to Marking-Cap oldest requests per bank for each thread
  Marked requests constitute the batch
  Form a new batch when no marked requests are left
Marked requests are prioritized over unmarked ones
  No reordering of requests across batches: no starvation, high fairness
How to prioritize requests within a batch?
Notes: To implement batching, Each memory request has a bit (called the marked bit) associated with it
When a batch is formed, the controller marks up to a Marking-Cap pending requests per bank for each thread. Marked requests constitute the batch. A new batch is formed when no marked requests are left.
  The key idea is that marked requests are always prioritized over unmarked ones. Hence, there is no reordering of requests across batches: As a result, there is no starvation, and a high degree of fairness.
  But how does the controller prioritize requests within a batch?

## Slide 10: Within-Batch Scheduling
Can use any existing DRAM scheduling policy
  FR-FCFS (row-hit first, then oldest-first) exploits row-buffer locality
But, we also want to preserve intra-thread bank parallelism
  Service each thread’s requests back to back
Scheduler computes a ranking of threads when the batch is formed
  Higher-ranked threads are prioritized over lower-ranked ones
  Improves the likelihood that requests from a thread are serviced in parallel by different banks
    Different threads prioritized in the same order across ALL banks
HOW?
Notes: Within a batch, the controller can use any existing DRAM scheduling policy. For example, the baseline FR-FCFS policy is very good at exploiting row buffer locality.
However, in addition to exploiting row-buffer locality, we also want to preserve intra-thread bank parallelism. As I showed you before, this can be accomplished by servicing each thread’s requests back to back
To do so, the DRAM scheduler computes a ranking of threads when the batch is formed
And it prioritizes requests that belong to higher-ranked threads over those that belong to lower ranked ones
  This Improves the likelihood that requests from a thread are serviced in parallel by different banks
  Because Different threads prioritized in the same order (the RANK ORDER) across ALL banks
But how does the scheduler compute this ranking?

## Slide 11: Thread Ranking
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread A
thread B
thread execution timeline
WAIT
WAIT
thread B
thread A
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread execution timeline
WAIT
WAIT
rank
thread B
thread A
thread A
thread B
SAVED CYCLES
Key Idea:
Notes: A memory scheduler can actively exploit bank-level parallelism to reduce the effective memory access latency. Here’s how.
Let us assume a case where two threads send two memory requests to two different banks.
A naïve memory scheduler that doesn’t exploit bank-level parallelism would schedule the requests in the order they arrived.
As shown in their thread execution timeline, both threads must wait for two bank latencies before all their requests are serviced.
In contrast, a memory scheduler that is aware of bank-level parallelism was proposed by Mutlu and Moscibroda.
Their key idea was to rank the threads so that thread’s memory requests are prioritized in the same order across all the banks.
In this case, let us assume that the blue thread’s request are the most prioritized.
The scheduler would then reorder the requests at bank 1’s request buffer…
so that the blue requests are serviced concurrently, after which the red requests can be serviced concurrently.
The memory service timeline shows how the access latencies for requests from the same thread are overlapped.
And, as a result, thread A has to wait less for its requests to be serviced.

## Slide 12: How to Rank Threads within a Batch
Ranking scheme affects system throughput and fairness
Maximize system throughput
  Minimize average stall-time of threads within the batch
Minimize unfairness (Equalize the slowdown of threads)
  Service threads with inherently low stall-time early in the batch
  Insight: delaying memory non-intensive threads results in high slowdown
Shortest stall-time first (shortest job first) ranking
  Provides optimal system throughput [Smith, 1956]*
  Controller estimates each thread’s stall-time within the batch
  Ranks threads with shorter stall-time higher
* W.E. Smith, “Various optimizers for single stage production,” Naval Research Logistics Quarterly, 1956.
Notes: The thread ranking scheme affects system throughput and fairness
A good ranking scheme should achieve two objectives.
First, it should maximize system throughput
Second, it should minimize unfairness; in other words it should balance the slowdown of the threads compared to when each is run alone.
These two objectives call for the same ranking scheme, as I will show soon.
Maximizing system throughput is achieved by minimizing the average stall-time of the threads within the batch (as I showed in the earlier example). By minimizing the average stall time, we maximize the amount of time the system spends on computation rather than waiting for DRAM accesses.
Minimizing unfairness is achieved by servicing threads with inherently low stall-time early in the batch, The insight is that if a thread has low stall time to begin with (if it is not intensive) delaying that thread would result in very high slowdown compared to delaying a memory-intensive thread.
To achieve both objectives, we use the “shortest job first” principle. Shortest job first scheduling has been proven to provide the optimal throughput in generalized machine scheduling theory. The controller estimates each thread’s stall-time within the batch (assuming the thread is run alone). And, it ranks a thread higher if the thread has a short stall time.

## Slide 13: Shortest Stall-Time First Ranking
Maximum number of marked requests to any bank (max-bank-load)
  Rank thread with lower max-bank-load higher (~ low stall-time)
Total number of marked requests (total-load)
  Breaks ties: rank thread with lower total-load higher
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
 | max-bank-load | total-load
T0 | 1 | 3
T1 | 2 | 4
T2 | 2 | 6
T3 | 5 | 9
Ranking:
T0 > T1 > T2 > T3
Notes:     How is this exactly done? The controller keeps track of two values for each thread. First, the maximum number of marked requests from the thread to any bank. This is called max-bank-load. A lower value of this correlates with low stall time (and less memory intensiveness). As a result the scheduler ranks a thread with lower max-bank-load higher than a thread with higher max-bank load.
    If the max-bank-load of the two threads are equal, the scheduler uses another value it keeps track of to break the ties. It keeps the total number of requests in the batch from each thread. This is called total-load. If a thread has lower total-load it is less intensive, therefore it is ranked higher.
    Let’s take a look at these concepts with an example. Assume these are the requests within the batch.
    T0 has at most 1 request to any bank, so its max-bank-load is 1. Its total-load is 3 since it has total 3 marked requests.
    T1 has at most 2 requests to any bank so its max-bank-load is 2. Its total load is 6.
    T2 similarly has a max-bank-load of 2, but its total load is higher.
    Finally, T3 has a maximum of 5 requests to Bank 3. Therefore, its max-bank load is 5.
    Because T1 has the smallest max-bank-load, it is ranked highest. The scheduler ranks T1 higher than T2 because T1 has fewer total requests. The most memory intensive thread, T2 is ranked the lowest.
    ----------------------------
    Insight: Memory-intensive threads can be delayed more within a batch since their baseline stall-time is high
    How do you break the ties? A thread with lower total-load is ranked higher
    Goal: Finish non-intensive threads first and fill in the gaps in parallelism as much as possible
    Shortest job first within a batch might seem unfair, but remember the batch boundaries. Less intensive threads will be penalized across batches because if their requests are not marked, they cannot be serviced. Shortest job first balances this delay caused to the less intensive threads
Thread 0 has at most one request to any bank
Thread 1 has at most 2: it has two requests to Bank 0.
Thread 2 has at most 2 as well.
Thread 3 has max number of requests to Bank 3 (5 reqs)

## Slide 14: Example Within-Batch Scheduling Order
7
5
3
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
Baseline Scheduling
Order (Arrival order)
PAR-BS Scheduling
Order
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
T0 | T1 | T2 | T3
4 | 4 | 5 | 7
AVG: 5 bank access latencies
AVG: 3.5 bank access latencies
Stall times
T0 | T1 | T2 | T3
1 | 2 | 4 | 7
Stall times
Time
1
2
4
6
Ranking: T0 > T1 > T2 > T3
1
2
3
4
5
6
7
Time
Notes: How does this ranking affect the scheduling order? Let’s take a look at this pictorially.
First, let’s look at the baseline scheduler. I will show the time at which the requests are serviced, where time is expressed abstractly in terms of bank access latency. In the baseline scheduler, the batched requests are serviced in their arrival order. As a result, the last request of T0 is serviced after 4 bank access latencies, the last request of T1 is also serviced after 4 bank access latencies. Consequently, the average stall time of the threads is approximately 5 bank access latencies within this batch of requests.
If we use PAR-BS to rank the threads, the scheduler will prioritize requests based on their thread-rank order, which I showed before. It prioritizes T0’s requests first (as shown in the ranking order). As a result, T0’s requests complete after 1 bank access latency. T1’s requests are serviced after 2 bank access latencies. T2’s requests are serviced after 4 bank access latencies.
Note that the bank parallelism of each thread is preserved as much as possible. Because of this, the average stall time reduces by 30%. Thus, system throughput improves.
Also note that, to keep this example simple, I assumed there are no row-buffer hits. A more complicated example with row-buffer hits is provided in the paper, and I encourage you to look at it.
--------------------------------------
Time is in bank access latencies (note that this is an approximation to demonstrate the idea… real DRAM system is much more complex than this…)
Last request from a thread is scheduled at TIME

## Slide 15: Putting It Together: PAR-BS Scheduling Policy
PAR-BS Scheduling Policy
  (1) Marked requests first
  (2) Row-hit requests first
  (3) Higher-rank thread first (shortest stall-time first)
  (4) Oldest first
Three properties:
  Exploits row-buffer locality and intra-thread bank parallelism
  Work-conserving
    Services unmarked requests to banks without marked requests
  Marking-Cap is important
    Too small cap: destroys row-buffer locality
    Too large cap: penalizes memory non-intensive threads
Many more trade-offs analyzed in the paper
Batching
Parallelism-aware
within-batch
scheduling
Notes: The resulting scheduling policy of our mechanism is based on four simple prioritization rules.
Marked requests are prioritized over others. This is the batching component.
Within a batch, row-hit requests are prioritized over others to exploit row-buffer locality (as in FR-FCFS). Then, higher-ranked threads’ requests are prioritized over lower ranked threads’ requests (to preserve each thread’s bank parallelism). Finally all else being equal, older requests are prioritized over others.
This scheduling policy has three properties.
First, it exploits both row-buffer locality and intra-thread bank parallelism. I assumed no row buffer hits in the previous example, to keep it simple, but this is taken into account in our scheduling algorithm. There is a balance between exploiting row buffer locality and bank parallelism, and our scheduling algorithm tries to achieve this balance. An example with row hits is provided in the paper.
Second, it is work conserving. It services unmarked requests in banks without marked requests.
Third, and I will not go into much detail on this, Marking-Cap is the most important parameter. Remember that the Marking-Cap determines how many requests from each thread to each bank can be admitted into a batch. If the cap is too small, too few requests from each thread are admitted into the batch. As a result, a thread’s row buffer locality cannot be exploited. If the cap is too large too many requests from intensive threads enter the batch, which slows down non-intensive threads.
Many other similar trade-offs are analyzed in the paper and I encourage you to read it.

## Slide 16: Hardware Cost
<1.5KB storage cost for
  8-core system with 128-entry memory request buffer
No complex operations (e.g., divisions)
Not on the critical path
  Scheduler makes a decision only every DRAM cycle
Notes: The implementation of PAR-BS is relatively simple. It requires three pieces of logic. Marking logic and thread ranking logic are utilized only when a new batch is formed. Extensions to request prioritization logic are needed to take into account the marked status and the thread-rank of each request.
There are no complex operations and the logic is not on the critical path of execution.
Our implementation requires less than 1.5KB storage cost within a reasonably large system with 8 cores.
More details are provided in the paper.

## Slide 17: Unfairness on 4-, 8-, 16-core Systems
Unfairness = MAX Memory Slowdown / MIN Memory Slowdown [MICRO 2007]
1.11X
1.08X
1.11X
Notes: This graph compares the five schedulers in terms of unfairness averaged over all workloads run on the 4, 8, and 16 core systems. Unfairness is computed as the max memory slowdown in the system divided by the minimum memory slowdown in the system. PAR-BS reduces unfairness significantly compared to the best previous scheduler, STFM, on all systems.
We conclude that the combination of batching and shortest stall-time first within batch scheduling provides good fairness without the need to explicitly estimate each thread’s slowdown and adjust scheduling policy based on that.

## Slide 18: System Performance (Hmean-speedup)
8.3%
6.1%
5.1%
Notes: This graph compares the system performance provided by the five schedulers. Performance is normalized to that of the baseline FR-FCFS scheduler. PAR-BS also improves system performance compared to the best previous scheduler, STFM, on all systems. In the 4-core system, PAR-BS provides an 8.3% performance improvement. The main reason is that PAR-BS improves each thread’s bank level parallelism: as a result, it reduces the average stall time per each request by 7.1% in the four core system (from 301 cycles to 281 cycles)

## Slide 19: PAR-BS Pros and Cons
Upsides:
  Identifies the problem of bank parallelism destruction across multiple threads
  Simple mechanism
Downsides:
  Does not always prioritize the latency-sensitive applications  lower overall throughput
  Implementation in multiple controllers needs coordination for best performance  too frequent coordination since batching is done frequently

## Slide 20: ATLAS Memory Scheduler
Yoongu Kim, Dongsu Han, Onur Mutlu, and Mor Harchol-Balter, "ATLAS: A Scalable and High-Performance
Scheduling Algorithm for Multiple Memory Controllers" 16th International Symposium on High-Performance Computer Architecture (HPCA),
Bangalore, India, January 2010. Slides (pptx)
ATLAS HPCA 2010 Talk

## Slide 21: ATLAS: Summary
Goal: To maximize system performance
Main idea: Prioritize the thread that has attained the least service from the memory controllers (Adaptive per-Thread Least Attained Service Scheduling)
  Rank threads based on attained service in the past time interval(s)
  Enforce thread ranking in the memory scheduler during the current interval
Why it works: Prioritizes “light” (memory non-intensive) threads that are more likely to keep their cores busy

## Slide 22: System Throughput: 24-Core System
Chart: System throughput
| 1 | 2 | 4 | 8 | 16 | Memory controllers
FCFS | 4.4802 | 7.1516 | 9.4221 | 11.9271 | 14.3903
FR_FCFS | 4.5363 | 7.4098 | 9.452 | 11.9951 | 14.4325
STFM | 5.6079 | 7.2459 | 9.2466 | 11.8455 | 14.376
PAR-BS | 5.3181 | 7.9826 | 9.8744 | 12.148 | 14.4958
ATLAS | 6.2242 | 8.7648 | 10.6995 | 12.8597 | 15.0021
System throughput = ∑ Speedup
ATLAS consistently provides higher system throughput than all previous scheduling algorithms
17.0%
9.8%
8.4%
5.9%
3.5%
System throughput
# of memory controllers

## Slide 23: System Throughput: 4-MC System
Chart: System throughput
| 4 | 8 | 16 | 24 | 32 | Cores
PAR-BS | 3.2707 | 4.8105 | 7.5074 | 9.8744 | 11.6321
ATLAS | 3.307 | 4.9796 | 7.8079 | 10.6995 | 12.8871
# of cores increases  ATLAS performance benefit increases
1.1%
3.5%
4.0%
8.4%
10.8%
System throughput
# of cores

## Slide 24: ATLAS Pros and Cons
Upsides:
  Good at improving overall throughput (compute-intensive threads are prioritized)
  Low complexity
  Coordination among controllers happens infrequently
Downsides:
  Lowest/medium ranked threads get delayed significantly  high unfairness

## Slide 25: TCM: Thread Cluster Memory Scheduling
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling:
Exploiting Differences in Memory Access Behavior" 43rd International Symposium on Microarchitecture (MICRO),
pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)
TCM Micro 2010 Talk

## Slide 26: Previous Scheduling Algorithms are Biased
No previous memory scheduling algorithm provides both the best fairness and system throughput
Chart: Weighted Speedup
| 7.21 | 8.166 | 8.26 | 8.527000000000001 | 8.778
FCFS | 8.513
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput bias
Fairness bias
Ideal
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
Notes: The problem is that previously proposed scheduling algorithms are biased.
Shown here is a plot, where the x-axis is weighted speedup, a metric of system throughput and system throughput increases as you move towards the right on the x-axis.
The y-axis is maximum slowdown, which is the slowdown of the most unfairly treated thread within a workload. Correspondingly, fairness increases as you move downwards on the y-axis.
Ideally, a memory scheduling algorithm would be situated towards the lower right part of the graph where fairness and system throughput are both high.
However, some previous algorithms are biased towards system throughput, whereas some are biased towards fairness, while others are optimized for neither.
The takeaway is that no previous memory scheduling algorithm provides both the best fairness and system throughput.

## Slide 27: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient
Notes: So why do previous algorithms fail?
On the one hand there is the throughput biased approach that prioritizes less memory-intensive threads.
Servicing memory requests from such threads allow them to make progress in the processor, increasing throughput.
However, the most memory-intensive thread, thread C, remains persistently deprioritized and and becomes prone to starvation causing large slowdowns and, ultimately, unfairness.
On the other hand there is the fairness biased approach where threads take turns accessing the memory.
In this case, the most memory-intensive thread does not starve.
However, the least memory-intensive thread, thread A, is not prioritized, leading to reduced throughput.
As you can see, a single policy applied to all threads is insufficient since different threads have different memory access needs.

## Slide 28: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread
Notes: So how do we achieve the best of both worlds? Our algorithm is based on the following insights:
First, we would like to prioritize the memory-non-intensive threads to increase system throughput.
Doing so does not degrade unfairness, since memory-non-intensive threads are inherently “light” and rarely cause interference for the memory-intensive threads.
For fairness, we discovered that unfairness is usually caused when one memory-intensive thread is prioritized over another.
As we’ve seen, the most deprioritized thread can starve.
To address this problem, we would like to shuffle their priority so that no single thread is persistently prioritized over another thread.
However, memory-intensive threads are not created equal.
They have different vulnerability to memory interference.
To address their differences, shuffling should be performed in an asymmetric manner.

## Slide 29: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Notes: Our algorithm, Thread Cluster Memory Scheduling, first groups threads into two clusters.
Among the threads executing in the system, some are memory-non-intensive whereas some are memory-intensive.
We isolate the memory-non-intensive threads into the non-intensive cluster and the memory-intensive threads into the intensive cluster.
This is so that we can apply different policies for different threads.
Subsequently, we prioritize the non-intensive cluster over the intensive cluster since the non-intensive threads have greater potential for making progress IN THEIR CORES [ONUR].
Finally, we apply different policies within each cluster, one optimized for throughput and the other for fairness.

## Slide 30: TCM Outline
1. Clustering
Notes: First, I will talk about how threads are grouped into two clusters.

## Slide 31: Clustering Threads
Step1 Sort threads by MPKI (misses per kiloinstruction)
thread
thread
thread
thread
thread
thread
higher
MPKI
T
α < 10% ClusterThreshold
Intensive
cluster
αT
Non-intensive
cluster
T = Total memory bandwidth usage
Step2 Memory bandwidth usage αT divides clusters
Notes: To group threads into two clusters, we first sort threads according to their MPKI, which stands for last-level cache-misses per kiloinstruction and is a metric of memory intensity.
After sorting, the leftmost thread is the thread with the lowest MPKI.
We then define a quantity called T, which is the total memory bandwidth usage across all threads.
Second, we form the non-intensive cluster by including threads whose bandwidth usage sums up to a certain fraction of the memory bandwidth usage.
That fraction is defined by a parameter called the ClusterThreshold. I will show later in the presentation how adjusting this parameter we can trade off between throughput and fairness.
Lastly, the remaining threads become the intensive cluster.

## Slide 32: TCM Outline
1. Clustering
2. Between
Clusters
Notes: Now I will talk about the scheduling policy between the two clusters.

## Slide 33: Prioritization Between Clusters
  Prioritize non-intensive cluster
Increases system throughput
  Non-intensive threads have greater potential for making progress
Does not degrade fairness
  Non-intensive threads are “light”
  Rarely interfere with intensive threads
>
priority
Notes: Between the two clusters, we statically prioritize the non-intensive cluster [ONUR: fixed plural  singular] so that non-intensive threads’ [ONUR: fixed wording] memory requests are serviced first.
This increases system throughput because non-intensive threads have greater potential for making progress BY QUICKLY RETURNING TO COMPUTE PERIODS IN THEIR CORES [ONUR].
Doing so does not degrade fairness, since non-intensive threads are “light” and consequently rarely interfere with intensive threads. [ONUR: removed “by design”… can be confusing if the listener is not in the right mindset]

## Slide 34: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
Throughput
Notes: Now I’ll discuss the scheduling policies applied within each cluster, starting first with the non-intensive cluster.

## Slide 35: Non-Intensive Cluster
Prioritize threads according to MPKI
Increases system throughput
  Least intensive thread has the greatest potential for making progress in the processor
thread
thread
thread
thread
higher
priority
lowest MPKI
highest MPKI
Notes: Within the memory non-intensive cluster, threads are prioritized according to their memory intensity where the least intensive thread receives the highest priority. [ONUR: replaced latency-sensitive]
This is, again, to increase system throughput. The least intensive thread has the greatest potential for making progress.

## Slide 36: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Throughput
Fairness
Notes: Now I’ll talk about the scheduling policy applied within the intensive cluster.

## Slide 37: Intensive Cluster
Periodically shuffle the priority of threads
Is treating all threads equally good enough?
BUT: Equal turns ≠ Same slowdown
thread
thread
thread
  Increases fairness
  Most prioritized
higher
priority
thread
thread
thread
Notes: Within the intensive cluster, we periodically shuffle the priority of threads.
By shuffling, we can increase fairness, since every thread is given a fair chance of being the most prioritized.
Treating all threads in an such an equal manner may be good enough in some cases.
But we noticed that in other cases, giving each thread equal turns does not necessarily lead to equal slowdowns.
Specifically, threads are not created equal and some threads are more easily slowed down than others.

## Slide 38: Case Study: A Tale of Two Threads
Chart: Slowdown
| random-access | streaming
Series 1 | 11 | 1
Case Study: Two intensive threads contending
  random-access
  streaming
Prioritize random-access
Prioritize streaming
random-access thread is more easily slowed down
Chart: Slowdown
| random-access | streaming
Series 1 | 1 | 7
7x
prioritized
1x
11x
prioritized
1x
Which is slowed down more easily?
Notes: We illustrate how some threads are more easily slowed down than others using a case study, where two memory-intensive threads are contending for memory: a random-access thread and a streaming thread.
Which of these two threads is slowed down more easily?
In the first case, we prioritize the random-access thread and see that the streaming thread is slowed down by a factor of 7.
In the second case, we prioritize the streaming thread and see that the random-access thread is slowed down by a factor of 11.
Clearly, comparing the two cases, we see that the random-access threads is more easily slowed down.

## Slide 39: Why are Threads Different?
random-access
streaming
req
req
req
req
Bank 1
Bank 2
Bank 3
Bank 4
Memory
rows
All requests parallel
High bank-level parallelism
All requests  Same row
High row-buffer locality
req
req
req
req
activated row
req
req
req
req
req
req
req
req
stuck
Vulnerable to interference
Notes: ONUR: Again, if you prefer, you can use “vulnerable” instead of “susceptible.”
So why are these two threads different?
To explain their difference, we must examine their memory access behavior.
First, the memory comprises multiple memory banks which can be accessed in parallel. [ONUR: removed structurally]
Additionally, each bank is basically a two-dimensional bit-array and comprises multiple rows.
The random access thread distributes its memory requests, to different banks.
Across the banks, the requests are serviced concurrently and their individual latencies are overlapped.
Therefore, the random-access thread has high bank-level parallelism.
On the other hand, the streaming thread sends its memory requests to the same bank.
There it is serviced at the same row over and over again.
When consecutive requests are serviced at the same row, it is called a row-buffer hit and has a lower latency.
Therefore, the streaming thread has higher row-buffer locality.
What would happen if we put those threads together?
For the purpose of illustration, we will assume that the streaming thread is prioritized.
You can see that the random-access thread’s request becomes stuck behind those of the streaming thread at Bank 3.
This breaks the bank-level parallelism of the random-access thread and serializes its latency, leading to reduced performance.
This is why, the random-access thread is more susceptible to interference.
If the two threads were prioritized the other way around, the streaming thread would not be interfered with as much, since the random-access thread has only a single request to Bank 3.

## Slide 40: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Fairness
Throughput

## Slide 41: Niceness
How to quantify difference between threads?
  Vulnerability to interference
Bank-level parallelism
  Causes interference
Row-buffer locality
+
Niceness
-
Niceness
High
Low

## Slide 42: TCM: Quantum-Based Operation
Time
Previous quantum (~1M cycles)
During quantum:
Monitor thread behavior
Memory intensity
Bank-level parallelism
Row-buffer locality
Beginning of quantum:
Perform clustering
Compute niceness of intensive threads
Current quantum
(~1M cycles)
Shuffle interval
(~1K cycles)
Notes: Clustering is performed at regular time intervals called quanta.
THIS IS DONE [ONUR] to account for phase changes in threads’ memory access behavior.
During A [ONUR] quantum, TCM monitors each thread’s memory access behavior:
memory intensity, bank-level parallelism, and row-buffer locality.
At the beginning of the next quantum, TCM is invoked to perform clustering and calculate niceness for the intensive threads.
Throughout the quantum, shuffling of the intensive threads is performed periodically.

## Slide 43: TCM: Scheduling Algorithm
Highest-rank: Requests from higher ranked threads prioritized
    Non-Intensive cluster > Intensive cluster
    Non-Intensive cluster: lower intensity  higher rank
    Intensive cluster: rank shuffling
Row-hit: Row-buffer hit requests are prioritized
Oldest: Older requests are prioritized
Notes: To bring it all together, TCM comprises three simple request prioritization rules.
The first is the highest-rank rule, where requests from higher ranked threads are prioritized.
The intensive cluster is prioritized over the non-intensive cluster TO IMPROVE SYSTEM [ONUR] throughput.
Within the intensive cluster, threads are assigned higher rank in the order of decreasing intensity. This, again, is to increase SYSTEM [ONUR] throughput.
Within the non-intensive cluster, the rank of threads are periodically shuffled and does not stay constant, TO ACHIEVE FAIRNESS [ONUR].
As a tie-breaker, the second rule is row-hit where row-buffer hitting requests are prioritized.
Lastly, all else being the same, we prioritize the oldest request.

## Slide 44: TCM: Implementation Cost
Required storage at memory controller (24 cores)
No computation is on the critical path
Thread memory behavior | Storage
MPKI | ~0.2kb
Bank-level parallelism | ~0.6kb
Row-buffer locality | ~2.9kb
Total | < 4kbits
Notes: ONUR: Have a separate bullet saying “No computation is on the processor critical path; Can be approximated.”
Basically, DRAM latency is very long so we can afford to do this computation especially since we are doing it over intervals.
You can have 4 cores in the first bullet and remove the subbullet.

## Slide 45: Previous Work
FRFCFS [Rixner et al., ISCA00]: Prioritizes row-buffer hits
  Thread-oblivious  Low throughput & Low fairness
STFM [Mutlu et al., MICRO07]: Equalizes thread slowdowns
  Non-intensive threads not prioritized  Low throughput
PAR-BS [Mutlu et al., ISCA08]: Prioritizes oldest batch of requests while preserving bank-level parallelism
  Non-intensive threads not always prioritized  Low throughput
ATLAS [Kim et al., HPCA10]: Prioritizes threads with less memory service
  Most intensive thread starves  Low fairness

## Slide 46: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.778 | 9.179
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput
Notes: This figure shows the performance of the four previous scheduling algorithms in addition to TCM, averaged over 96 workloads.
FRFCFS has low system throughput and fairness.
STFM and PAR-BS is biased towards fairness, while ATLAS is biased towards system throughput.
TCM lies towards the lower right part of the figure and provides the best fairness and system throughput.
Compared to ATLAS, TCM provides approx 5% better throughput and 39% better fairness.
Compared to PAR-BS, TCM provides approx 5% better fairness and 8% better throughput.

## Slide 47: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13.0 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 48: Operating System Support
ClusterThreshold is a tunable knob
  OS can trade off between fairness and throughput
Enforcing thread weights
  OS assigns weights to threads
  TCM enforces thread weights within each cluster

## Slide 49: Conclusion
No previous memory scheduling algorithm provides both high system throughput and fairness
  Problem: They use a single policy for all threads
TCM groups threads into two clusters
  Prioritize non-intensive cluster  throughput
  Shuffle priorities in intensive cluster  fairness
  Shuffling should favor nice threads  fairness
TCM provides the best system throughput and fairness

## Slide 50: TCM Pros and Cons
Upsides:
  Provides both high fairness and high performance
Downsides:
  Scalability to large buffer sizes?
  Effectiveness in a heterogeneous system?

## Slide 51: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 52: SMS: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 53: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 54: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 55: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 56: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 57: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 58: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 59: Strong Memory Service Guarantees
Goal: Satisfy performance bounds/requirements in the presence of shared main memory, prefetchers, heterogeneous agents, and hybrid memory
Approach:
  Develop techniques/models to accurately estimate the performance of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance

## Slide 60: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu
Notes: Hello everyone. My name is Lavanya Subramanian.
Today, I will present “MISE: Providing perfomance …”.
This is work done in collaboration with my co-authors Vivek ….

## Slide 61: Unpredictable Application Slowdowns
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
An application’s performance depends on
which application it is running with
Notes: This graph shows two applications from the SPEC CPU 2006 suite, leslie3d and gcc. These applications are run on either core of a two core system and share main memory. The y-axis shows each application’s slowdown as compared to when the application is run standalone on the same system.
Now, let’s look at leslie3d. It slows down by 2x when run with gcc.
Let’s look at another case when leslie3d is run with another application, mcf. Leslie now slows down by 5.5x, while it slowed down by 2x when run with gcc. Leslie experiences different slowdowns when run with different applications.
More generally, an application’s performance depends on which applications it is running with. Such performance unpredictability is undesirable….

## Slide 62: Need for Predictable Performance
There is a need for predictable performance
  When multiple applications share resources
  Especially if some applications require performance guarantees
Example 1: In mobile systems
  Interactive applications run with non-interactive applications
  Need to guarantee performance for interactive applications
Example 2: In server systems
  Different users’ jobs consolidated onto the same server
  Need to provide bounded slowdowns to critical jobs
Our Goal: Predictable performance
in the presence of memory interference
Notes: …because there is a need for predictable performance
When multiple applications share resources and
Especially when some applications require guarantees on performance.
For example, in mobile systems, interactive applications are run with non-interactive ones.
And there is a need to provide guarantees on performance to the interactive applications.
In server systems, different users’ jobs are heavily consolidated onto the same server.
In such a scenario, there is a need to achieve bounded slowdowns for critical jobs of users.
These are a couple of examples of systems that need predictable performance.
There are many other systems (such as …) in which performance predictability is necessary.
Therefore, our goal in this work is to provide predictable performance in the presence of memory interference.

## Slide 63: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
Notes: Towards this goal, we propose to first estimate application slowdowns due to main memory interference.
And once we have accurate slowdown estimates, we propose to leverage them to control application slowdowns.

## Slide 64: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: First, let me describe the key observations that enable us to estimate application slowdowns.

## Slide 65: Slowdown: Definition
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 66: Key Observation 1
For a memory bound application,
Performance  Memory request service rate
Chart: Normalized Request Service Rate
| 0.358607859 | 0.408507739 | 0.532531575 | 0.580993121999996 | 0.632877307000005 | 0.690879954000007 | 0.726945501000005 | 0.796354682 | 0.837558983 | 0.938360254 | 0.948305607000005 | 1.0
omnetpp | 0.34972 | 0.39891 | 0.5217 | 0.56944 | 0.61954 | 0.67835 | 0.71425 | 0.78346 | 0.8265 | 0.928 | 0.94883 | 1
mcf | 0.34876 | 0.39942 | 0.4869 | 0.53653 | 0.54337 | 0.55102 | 0.58278 | 0.61457 | 0.65149 | 0.74316 | 0.84741 | 0.93386 | 0.9689 | 1
astar | 0.41586 | 0.48052 | 0.66786 | 0.72536 | 0.77686 | 0.79876 | 0.84877 | 0.88035 | 0.92559 | 0.95012 | 0.98596 | 1
Easy
Harder
Intel Core i7, 4 cores
Mem. Bandwidth: 8.5 GB/s
Notes: We observe that for a memory bound application, its performance is roughly proportional to the rate at which its memory requests are serviced.
This plot shows the results of our experiment on an Intel, 4-core system. We run omnetpp, a SPEC CPU 2006 benchmark along with another memory hog, whose memory intensity can be varied. This, in turn, lets us vary the rate at which the memory requests of omnetpp are serviced.
The x-axis shows the normalized request service rate of omnetpp, normalized to when it is run alone.
The y-axis shows the performance of omnetpp, normalized to when it is run alone.
As can be seen, there is a very strong, y=x like correlation between request service rate and performance.
We observe the same trend for various memory bound applications. Here are a couple of more examples.
Therefore, memory request service rate can be used as a proxy for performance.
Now, going back to the slowdown equation. We can replace performance by request service rate, based on our first observation, enabling us to express slowdown as the ratio of alone to shared request service rates.
Shared request service rate can be measured in a relatively straightforward manner when an application is run along with other applications.
Measuring alone request service rate, without actually running an application alone is harder. This is where our second observation comes into play.

## Slide 67: Key Observation 2
Request Service Rate Alone (RSRAlone) of an application can be estimated by giving the application highest priority in accessing memory
Highest priority  Little interference
(almost as if the application were run alone)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 68: Key Observation 2
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 69
Memory Interference-induced Slowdown Estimation (MISE) model for memory bound applications
Notes: Based on these two observations, our memory interference induced slowdown estimation (MISE) model for memory bound applications is as follows. Now, let’s analyze why this request service rate ratio based model holds for memory bound applications

## Slide 70: Key Observation 3
Memory-bound application
No interference
Compute Phase
Memory Phase
With interference
Memory phase slowdown dominates overall slowdown
time
time
Req
Req
Req
Req
Req
Req
Notes: A memory-bound application spends significant fraction of its execution time waiting for memory.
Let’s first look at the case when a memory-bound application is not receiving any interference.
The application does a small amount of compute at the core and then sends out a bunch of memory requests. The application cannot do any more compute until these requests are serviced.
Now, when this application experiences interference, the length of its compute phase does not change. However, the time taken to service the memory requests increases. In essence, since the application spends most of its time in the memory phase, the memory induced slowdown of the application dominates the overall slowdown of the application.

## Slide 71: Key Observation 3
Non-memory-bound application
time
time
No interference
Compute Phase
Memory Phase
With interference
Only memory fraction ( ) slows down with interference
Memory Interference-induced Slowdown Estimation (MISE) model for non-memory bound applications
Notes: However, this is not the case for a non-memory-bound application.
A non-memory-bound application spends a sizeable fraction of its time doing compute at the core and a smaller fraction of time waiting for memory. When the application experiences interference, the length of the compute phase does not change, whereas the memory phase slows down with interference.
Specifically, if alpha is the fraction of time the application spends in the memory phase, then 1 – alpha is the fraction of time it spends in the compute phase. The 1 – alpha fraction does not change with memory interference, however the alpha fraction slows down as the ratio of request service rate alone to request service rate shared.
We augment the MISE model to take this into account. Slowdown for non-memory-bound applications can be expressed as the sum of two quantities - 1 – alpha, the compute fraction that does not change with interference and the memory induced slowdown.

## Slide 72: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having discussed the key observations behind our MISE model, let me describe its implementation.

## Slide 73: Interval Based Operation
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
This repeats during every interval.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 74: Measuring RSRShared and α
Request Service Rate Shared (RSRShared)
  Per-core counter to track number of requests serviced
  At the end of each interval, measure
Memory Phase Fraction ( )
  Count number of stall cycles at the core
  Compute fraction of cycles stalled for memory
Notes: Shared request service rate can be measured using per-core counters to track the number of requests serviced during each interval.
At the end of the interval, SRSR can be computed as the number of requests serviced divided by the length of the interval.
Memory phase fraction of each application can be computed by counting the number of cycles the core stalls waiting for memory and then computing what fraction are these cycles of the interval length.
Measuring SRSR and alpha is the straightforward part. Now, for the more interesting part, estimating alone request service rate.

## Slide 75: Estimating Request Service Rate Alone (RSRAlone)
Divide each interval into shorter epochs
At the beginning of each epoch
  Memory controller randomly picks an application as the highest priority application
At the end of an interval, for each application, estimate
Goal: Estimate RSRAlone
How: Periodically give each application highest priority in accessing memory
Notes: Our goal is to estimate alone request service rate. To do this, we periodically give each application the highest priority in accessing memory, based on observation 2.
How exactly do we do this. First, each interval is divided into shorter epochs. At the beginning of each epoch, the memory controller picks one application at random and designates it the highest priority application. This way each application is given highest priority at different epochs during the interval.
At the end of the interval, ARSR is estimated for each application as the ratio of the number of requests of the application serviced during the high priority epochs to the number of cycles the application was given highest priority.
Now, is this an accurate way of estimating ARSR. It turns out not. We have been ignoring an inaccuracy all along.

## Slide 76: Inaccuracy in Estimating RSRAlone
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
When an application has highest priority
  Still experiences some interference
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
Time units
Service order
Main Memory
1
2
3
Interference Cycles
High Priority
Main Memory
Time units
Service order
Main Memory
1
2
3
Request Buffer
State
Notes: That is, even when an application has highest priority, it still experiences some interference from other applications.
Here is an example showing why.
The red application has highest priority and is run along with another application, the blue application. First, there is just one request in the request buffer and it is from the red application. Since this is the only request, it is scheduled by the memory controller and completes in one time unit.
While this request is being serviced, there comes another request from the blue application. Our memory controller is work conserving and schedules another application’s request, if there is no request from the red application. So, it schedules the blue application’s request next.
However, just as the blue application’s request is being scheduled comes another request from the red application. Ideally, we would like to pre-empt the blue application’s request. However, because of the way DRAM operates, preempting the blue application’s request incurs overhead. Therefore, the red application’s request would have to wait until the blue application’s request completes and only then is it serviced. These extra cycles that the red application spent waiting for the blue application’s request to complete are interference cycles that it would not have experienced had it been running alone.

## Slide 77: Accounting for Interference in RSRAlone Estimation
Solution: Determine and remove interference cycles from RSRAlone calculation
A cycle is an interference cycle if
  a request from the highest priority application is waiting in the request buffer and
  another application’s request was issued previously
Notes: The solution to account for this interference is to determine and remove such interference cycles from the ARSR computation.
How we do this is to subtract these cycles from the number of high priority epoch cycles.
Now, the question is how do we determine which cycles are interference cycles.
We deem a cycle an interference cycle if …. (read from slide)

## Slide 78: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having described the key observations behind our model and its implementation, we will put it all together

## Slide 79: MISE Model: Putting it All Together
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 80: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Now, having described the model and its implementation, let me present an evaluation of the model.

## Slide 81: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu+, MICRO ‘07]
  FST (Fairness via Source Throttling) [Ebrahimi+, ASPLOS ‘10]
  Per-thread Cycle Accounting [Du Bois+, HiPEAC ‘13]
Basic Idea:
Hard
Easy
Count number of cycles application receives interference
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 82: Two Major Advantages of MISE Over STFM
Advantage 1:
  STFM estimates alone performance while an application is receiving interference  Hard
  MISE estimates alone performance while giving an application the highest priority  Easier
Advantage 2:
  STFM does not take into account compute phase for non-memory-bound applications
  MISE accounts for compute phase  Better accuracy
Notes: Let me now present the two major advantages of MISE over STFM, qualitatively.
First, STFM estimates alone performance of an application while it is receiving interference. This is hard because of BLP effects.
MISE addresses this difficulty by giving an application highest priority and then estimating its alone performance.
Second, STFM does not take into account compute phase for non-mem-bound applications. MISE accounts for compute phase and hence achieves better accuracy.

## Slide 83: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1066 DRAM
  512 KB private cache/core
Workloads
  SPEC CPU2006
  300 multi programmed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 84: Quantitative Comparison
Chart: Million Cycles
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 2.7467 | 2.8146 | 2.981 | 2.6916 | 3.5156 | 2.4446 | 3.3601 | 3.2667 | 2.8783 | 2.9401 | 2.7229 | 2.9719 | 2.71 | 2.1736 | 2.0285 | 2.4098 | 2.0056 | 2.2585 | 2.1279 | 2.4625
STFM | 1.8517 | 1.9219 | 1.8786 | 1.8294 | 1.9487 | 1.8759 | 1.7936 | 1.7677 | 1.83 | 1.817 | 1.7232 | 1.7709 | 1.704 | 1.6746 | 1.6715 | 1.7352 | 1.6427 | 1.7084 | 1.6918 | 1.7477
MISE | 2.6655 | 2.8713 | 2.8244 | 2.6053 | 3.1741 | 2.6867 | 3.5471 | 3.4317 | 3.3 | 2.6747 | 2.8604 | 3.0821 | 2.8909 | 2.235 | 2.1161 | 2.3639 | 1.999 | 2.0667 | 2.1632 | 2.3161
SPEC CPU 2006 application
leslie3d
Notes: This graph shows the actual slowdown of leslie3d, a memory-bound application, with time (in million cycles).
Here are slowdown estimates from STFM and here are slowdown estimates from MISE. As can be seen, MISE’s slowdown estimates are much closer to the actual slowdowns. This is because MISE estimates leslie’s alone performance while giving it highest priority, whereas STFM tries to estimate it while leslie receives interference from other applications.

## Slide 85: Comparison to STFM
cactusADM
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.495 | 1.5295 | 1.6709 | 1.5475 | 1.6605 | 1.5731 | 1.9783 | 1.7095 | 1.5337 | 1.5256 | 1.4754 | 1.5235 | 1.5214 | 1.7913 | 1.6855 | 1.6301 | 1.5933 | 1.6732 | 1.5495 | 1.6973
STFM | 1.25 | 1.3555 | 1.3435 | 1.3721 | 1.3293 | 1.3149 | 1.2341 | 1.3128 | 1.3228 | 1.3579 | 1.3509 | 1.344 | 1.4008 | 1.3967 | 1.5397 | 1.5867 | 1.5517 | 1.5683 | 1.5638 | 1.3614
MISE | 1.5723 | 1.5685 | 1.6897 | 1.5829 | 1.73 | 1.6866 | 2.1706 | 1.8114 | 1.5947 | 1.5898 | 1.5347 | 1.5537 | 1.6001 | 1.8673 | 1.7348 | 1.6758 | 1.6313 | 1.7322 | 1.6362 | 1.7298
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.7536 | 1.697 | 1.8734 | 1.7248 | 1.9225 | 1.6413 | 1.9296 | 2.1339 | 2.0504 | 1.9754 | 1.8732 | 2.1705 | 2.0085 | 2.239 | 2.2425 | 2.2469 | 1.9042 | 2.3715 | 2.0927 | 2.5902
STFM | 1.3661 | 1.3843 | 1.3635 | 1.3908 | 1.3589 | 1.35 | 1.3746 | 1.5894 | 1.5811 | 1.5995 | 1.5987 | 1.5832 | 1.5771 | 2.0246 | 1.9878 | 1.9883 | 1.9797 | 1.9406 | 1.9709 | 1.9629
MISE | 1.8607 | 1.9645 | 1.9765 | 1.8835 | 2.5202 | 1.8326 | 2.2231 | 2.3347 | 2.178 | 2.097 | 2.1736 | 2.1054 | 2.0591 | 2.3181 | 2.2502 | 2.3946 | 2.1703 | 2.5387 | 2.2735 | 2.6647
GemsFDTD
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.9414 | 2.1412 | 2.406 | 2.0632 | 2.7223 | 2.6572 | 3.1068 | 3.1879 | 2.6035 | 2.4937 | 2.4704 | 2.8774 | 2.6478 | 2.6947 | 2.7804 | 2.9653 | 2.8228 | 2.5796 | 2.6027 | 2.7846
STFM | 1.5023 | 1.4705 | 1.8931 | 1.4971 | 1.6676 | 1.6306 | 1.8055 | 1.7004 | 1.5827 | 1.7021 | 1.7571 | 1.8054 | 1.974 | 2.2827 | 2.3098 | 2.107 | 1.6316 | 2.0168 | 2.0447 | 2.0375
MISE | 1.916 | 2.3469 | 2.5021 | 2.481 | 2.7434 | 2.413 | 3.2611 | 3.5557 | 2.6948 | 2.6542 | 3.0171 | 2.4489 | 2.5681 | 2.7574 | 3.1405 | 3.0343 | 2.527 | 2.8438 | 3.1033 | 3.2769
soplex
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0179 | 1.0228 | 1.5311 | 1.2016 | 1.0185 | 1.0121 | 1.0059 | 1.0071 | 1.1261 | 1.5714 | 1.0808 | 1.0167 | 1.0097 | 1.2303 | 1.0956 | 1.0308 | 1.0187 | 1.3242 | 1.3257 | 1.0134
STFM | 2.6564 | 2.8136 | 2.323 | 1.9913 | 2.1243 | 2.8472 | 2.9844 | 2.4594 | 2.5397 | 2.2388 | 3.0174 | 2.8437 | 3.3951 | 3.9402 | 2.5308 | 2.8686 | 3.3191 | 2.5052 | 2.3033 | 2.0445
MISE | 1.0005 | 1.0032 | 1.7563 | 1.0691 | 0.99707 | 1.0011 | 1.0016 | 0.99869 | 1.0593 | 1.3748 | 1.0555 | 1.0003 | 1.0006 | 1.0639 | 1.0105 | 0.98886 | 1.0009 | 0.9221 | 1.0907 | 1.0039
wrf
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0394 | 1.0432 | 1.0258 | 1.0358 | 1.031 | 1.0316 | 1.0304 | 1.0232 | 1.0226 | 1.0158 | 1.0543 | 1.0328 | 1.0751 | 1.0632 | 1.0517 | 1.053 | 1.029 | 1.0322 | 1.031 | 1.0246
STFM | 2.1276 | 2.0414 | 1.9127 | 1.8201 | 2.3708 | 1.9609 | 1.9559 | 2.062 | 2.2477 | 2.173 | 3.9673 | 2.3084 | 2.4138 | 2.5477 | 2.8093 | 2.6087 | 2.1795 | 1.9627 | 1.8871 | 2.0011
MISE | 1.0191 | 1.0068 | 1.0168 | 0.98223 | 1.031 | 0.96844 | 1.0017 | 1.0177 | 0.99417 | 1.0091 | 1.0383 | 1.0293 | 1.0276 | 1.0128 | 1.0242 | 1.0231 | 0.99687 | 1.0223 | 0.89507 | 1.0191
calculix
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0008 | 1.0011 | 1.0029 | 1.0014 | 1.0016 | 1.0015 | 1.0038 | 1.0016 | 1.0011 | 1.0034 | 1.0391 | 1.1297 | 1.0014 | 1.0018 | 1.0019 | 1.002 | 1.0012 | 1.0008 | 1.0011 | 1.0012
STFM | 2.5587 | 2.6401 | 2.5897 | 1.8924 | 2.9635 | 3.1523 | 2.659 | 2.2124 | 3.2205 | 2.9929 | 3.5898 | 2.7107 | 2.1336 | 3.0915 | 3.0289 | 3.0638 | 3.0873 | 2.3554 | 2.7464 | 2.2834
MISE | 1.0002 | 1.0002 | 1.0015 | 1.0003 | 1.0007 | 0.99984 | 1.0012 | 0.99949 | 0.99671 | 1.0015 | 0.99044 | 0.86466 | 1.0003 | 1.0004 | 1.0006 | 0.99474 | 0.99903 | 0.99882 | 1.0001 | 1.0004
povray
Average error of MISE: 8.2%
Average error of STFM: 29.4%
(across 300 workloads)
Notes: Several more applications. For most applications, MISE’s slowdown estimates are more accurate.
On average, MISE’s error is 8.2%, while STFM’s error is 29.4%, across our 300 workloads.

## Slide 86: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: I have described our MISE model to estimate application slowdowns. Now, once we have slowdown estimates from our model, we can leverage them to control slowdowns. Let me present our first mechanism to control slowdowns – providing soft slowdown guarantees.

## Slide 87: Providing “Soft” Slowdown Guarantees
Goal
  1. Ensure QoS-critical applications meet a prescribed slowdown bound
  2. Maximize system performance for other applications
Basic Idea
  Allocate just enough bandwidth to QoS-critical application
  Assign remaining bandwidth to other applications
Notes: The goal of this mechanism is to .. <read off slide>.
The basic idea is to allocate just enough bandwidth the QoS-critical application, while assigning the remaining bandwidth among the other applications.

## Slide 88: MISE-QoS: Mechanism to Provide Soft QoS
Assign an initial bandwidth allocation to QoS-critical application
Estimate slowdown of QoS-critical application using the MISE model
After every N intervals
  If slowdown > bound B +/- ε, increase bandwidth allocation
  If slowdown < bound B +/- ε, decrease bandwidth allocation
When slowdown bound not met for N intervals
  Notify the OS so it can migrate/de-schedule jobs
Notes: SLIDE NEEDS WORK

## Slide 89: Methodology
Each application (25 applications in total) considered the QoS-critical application
Run with 12 sets of co-runners of different memory intensities
Total of 300 multiprogrammed workloads
Each workload run with 10 slowdown bound values
Baseline memory scheduling mechanism
  Always prioritize QoS-critical application
  [Iyer+, SIGMETRICS 2007]
  Other applications’ requests scheduled in FRFCFS order
  [Zuravleff +, US Patent 1997, Rixner+, ISCA 2000]
Notes: Read off slide

## Slide 90: A Look at One Workload
Chart: Slowdown
| leslie3d | hmmer | lbm | omnetpp
AlwaysPrioritize | 1.9301 | 2.511 | 2.8159 | 2.7346
MISE-QoS-10/1 | 2.8374 | 2.2769 | 2.0523 | 2.0142
MISE-QoS-10/3 | 2.6976 | 2.3196 | 2.1221 | 2.084
MISE-QoS-10/5 | 2.0128 | 2.5056 | 2.6593 | 2.5534
MISE-QoS-10/7 | 1.9063 | 2.508 | 2.8014 | 2.6609
MISE-QoS-10/9 | 1.9063 | 2.508 | 2.8014 | 2.6609
QoS-critical
non-QoS-critical
MISE is effective in
meeting the slowdown bound for the QoS-critical application
improving performance of non-QoS-critical applications
Slowdown Bound = 10
Slowdown Bound = 3.33
Slowdown Bound = 2

## Slide 91: Effectiveness of MISE in Enforcing QoS
 | Predicted Met | Predicted Not Met
QoS Bound Met | 78.8% | 2.1%
QoS Bound Not Met | 2.2% | 16.9%
Across 3000 data points
MISE-QoS meets the bound for 80.9% of workloads
AlwaysPrioritize meets the bound for 83% of workloads
MISE-QoS correctly predicts whether or not the bound is met for 95.7% of workloads

## Slide 92: Performance of Non-QoS-Critical Applications
Chart: Number of Memory Intensive Applications
| 0 | 1 | 2 | 3 | Avg
AlwaysPrioritize | 1.2932 | 0.92684 | 0.63783 | 0.47247 | 0.83259
MISE-QoS-10/1 | 1.3105 | 1.0515 | 0.75708 | 0.556 | 0.91875
MISE-QoS-10/3 | 1.3105 | 1.0471 | 0.75276 | 0.54982 | 0.91504
MISE-QoS-10/5 | 1.3104 | 1.0268 | 0.71476 | 0.51722 | 0.89229
MISE-QoS-10/7 | 1.3101 | 0.96233 | 0.65406 | 0.47556 | 0.85051
MISE-QoS-10/9 | 1.2966 | 0.92898 | 0.64287 | 0.47149 | 0.83499
Higher performance when bound is loose
When slowdown bound is 10/3
MISE-QoS improves system performance by 10%

## Slide 93: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown

## Slide 94: Other Results in the Paper
Sensitivity to model parameters
  Robust across different values of model parameters
Comparison of STFM and MISE models in enforcing soft slowdown guarantees
  MISE significantly more effective in enforcing guarantees
Minimizing maximum slowdown
  MISE improves fairness across several system configurations

## Slide 95: Summary
Uncontrolled memory interference slows down applications unpredictably
Goal: Estimate and control slowdowns
Key contribution
  MISE: An accurate slowdown estimation model
  Average error of MISE: 8.2%
Key Idea
  Request Service Rate is a proxy for performance
  Request Service Rate Alone estimated by giving an application highest priority in accessing memory
Leverage slowdown estimates to control slowdowns
  Providing soft slowdown guarantees
  Minimizing maximum slowdown

## Slide 96: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu

## Slide 97: Memory Scheduling for Parallel Applications
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin,
Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 98: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread that is falling behind the most in a parallel for loop
PAMS Micro 2011 Talk

## Slide 99: QoS-Aware Memory Systems: The Dumb Resources Approach

## Slide 100: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 101: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 102: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
102

## Slide 103: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 104: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 105: Fairness via Source Throttling (FST) [ASPLOS’10]
105
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 106: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 107: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control

## Slide 108: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 109: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 110: Another Way to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 111: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 112: 1. Profile Applications
Hardware counters collect application memory access characteristics
Memory access characteristics
  Memory intensity:
  Last level cache Misses Per Kilo Instruction (MPKI)
  Row-buffer locality:
  Row-buffer Hit Rate (RBH) - percentage of accesses that hit in the row buffer

## Slide 113: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 114: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications

## Slide 115: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit

## Slide 116: Comparison to Previous Scheduling Policies
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Significant performance improvement over baseline FRFCFS
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 117: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 118: Application-to-Core Mapping to Reduce Interference
Reetuparna Das, Rachata Ausavarungnirun, Onur Mutlu, Akhilesh Kumar, and Mani Azimi, "Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)
Key ideas:
  Cluster threads to memory controllers (to reduce across chip interference)
  Isolate interference-sensitive (low-intensity) applications in a separate cluster (to reduce interference from high-intensity applications)
  Place applications that benefit from memory bandwidth closer to the controller

## Slide 119: Application-to-Core Mapping
Balancing
Isolation
Radial Mapping
Clustering
Improve Locality
Reduce Interference
Improve Bandwidth
Utilization
Reduce Interference
Improve Bandwidth
Utilization
Notes: We take four steps to a2c
First we adopt clustering for improving locality and reducing interference
Then we balance the load across the clusters
Next we ensure to isolate sensitive applications such they suffer minimal interference
Finally we schedule critical application close to shared memory system resources

## Slide 120: System Performance
Chart: Normalized Weighted Speedup
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 1.0372 | 1.1184 | 1.1114 | 1.1307 | 1.0935
A2C | 1.0655 | 1.2016 | 1.2154 | 1.2299 | 1.1672
System performance improves by 17%
Notes: Radial mapping was consistently beneficial for all workloads

## Slide 121: Network Power
Chart: Normalized NoC Power
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 0.71297 | 0.70762 | 0.68333 | 0.68711 | 0.6911
A2C | 0.39619 | 0.50039 | 0.49336 | 0.49562 | 0.47611
Average network power consumption reduces by 52%

## Slide 122: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 123: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request/thread scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 124: Summary: Memory Interference and QoS
QoS-unaware memory 
uncontrollable and unpredictable system
Providing QoS awareness improves performance, predictability, fairness, and utilization of the memory system
Discussed many new techniques to:
  Minimize memory interference
  Provide predictable performance
Many new research ideas needed for integrated techniques and closing the interaction with software

## Slide 125: Course Agenda
Scalable Many-Core Memory Systems
  July 15-19, 2013
Topic 1: Main memory basics, DRAM scaling
Topic 2: Emerging memory technologies and hybrid memories
Topic 3: Main memory interference and QoS
Topic 4 (unlikely): Cache management
Topic 5 (unlikely): Interconnects
Major Overview Reading:
  Mutlu, “Memory Scaling: A Systems Architecture Perspective,” IMW 2013.

## Slide 126: Readings for Topic 3 (Memory QoS)
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Mutlu and Moscibroda, “Stall-Time Fair Memory Access Scheduling,” MICRO 2007.
Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008, IEEE Micro 2009.
Kim et al., “ATLAS: A Scalable and High-Performance Scheduling Algorithm for Multiple Memory Controllers,” HPCA 2010.
Kim et al., “Thread Cluster Memory Scheduling,” MICRO 2010, IEEE Micro 2011.
Muralidhara et al., “Memory Channel Partitioning,” MICRO 2011.
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Das et al., “Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems,” HPCA 2013.

## Slide 127: Readings for Topic 3 (Memory QoS)
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS 2010, ACM TOCS 2012.
Lee et al., “Prefetch-Aware DRAM Controllers,” MICRO 2008, IEEE TC 2011.
Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.
Ebrahimi et al., “Prefetch-Aware Shared Resource Management for Multi-Core Systems,” ISCA 2011.

## Slide 128: Course Materials and Beyond
Website for Course Slides and Papers
  http://users.ece.cmu.edu/~omutlu/acaces2013-memory.html
  http://users.ece.cmu.edu/~omutlu
  Lecture notes and readings (for all 5 topics)

## Slide 129: You Can Contact Me Any Time
My Contact Information
  Onur Mutlu
  onur@cmu.edu
  http://users.ece.cmu.edu/~omutlu
  +1-512-658-0891 (my cell phone)
  You can contact me any time.

## Slide 130: Thank You!

## Slide 131: Scalable Many-Core Memory Systems Topic 3: Memory Interference and QoS-Aware Memory Systems
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013

## Slide 132: Additional Material

## Slide 133: Two Works
Reetuparna Das, Rachata Ausavarungnirun, Onur Mutlu, Akhilesh Kumar, and Mani Azimi, "Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 134: Application-to-Core Mapping Policies to Reduce Memory System Interference
Reetuparna Das* Rachata Ausavarungnirun$ Onur Mutlu$ Akhilesh Kumar§ Mani Azimi§
*University of Michigan $Carnegie Mellon University §Intel
Notes: Hi I am Reetuparna Das and I will present our work on Application-to-Core Mapping policies to reduce memory system interference
I did this work with my collaborators at Carnegie Mellon Onur and Rachata and my colleagues at Intel Mani and Akhilesh

## Slide 135: Multi-Core to Many-Core
Multi-Core
Many-Core
Notes: Processor industry has adopted multi-cores a power-efficient way for throughput scaling
Today as processors move from few cores to few hundred cores we face several new challenges

## Slide 136: Many-Core On-Chip Communication
Memory
Controller
Shared
Cache Bank
$
$
Light
Heavy
Applications
Notes: In a many-core processor with several hundred cores communication plays a key role in system design
I show an example of on-chip communication
An application generates requests to memory sub-system which can be either satisfied by caches or have to go all the way to main memory via memory controllers
Some applications may generate few requests and are light and some may generate lots of requests and thus heavy

## Slide 137: Task Scheduling
Traditional
  When to schedule a task? – Temporal
Many-Core
  When to schedule a task? – Temporal
  + Where to schedule a task? – Spatial
Spatial scheduling impacts performance of memory hierarchy
  Latency and interference in interconnect, memory, caches
Notes: Typically task scheduling determines when to schedule a job
As we move from few cores to few hundred cores the scheduler also needs to determine where to schedule a task – hence there is a spatial aspect
Spatial scheduling impacts performance of memory hierarchy because latency for memory requests generated from different cores could be very different

## Slide 138: Problem: Spatial Task Scheduling
Applications
Cores
How to map applications to cores?
Notes: In this paper we try to solve the problem of spatial task scheduling
For spatial scheduling there will be lots of applications with diverse characteristics and there will be lots of cores
The key question is how to map these applications to cores to maximize performance fairness and energy efficiency

## Slide 139: Challenges in Spatial Task Scheduling
Applications
Cores
How to reduce destructive interference between applications?
How to reduce communication distance?
How to prioritize applications to improve throughput?
Notes: When doing the application to core mapping we need to answer several questions –
The first obvious question is how do we reduce the distance that your requests travel
Then how do you ensure that requests generated by two different applications donot destructively interfere with each other and degrade the overall performance
Finally if we have applications which are very sensitive to memory system performance how do you prioritize them and still ensure good fairness and load balance

## Slide 140: Application-to-Core Mapping
Balancing
Isolation
Radial Mapping
Clustering
Improve Locality
Reduce Interference
Improve Bandwidth
Utilization
Reduce Interference
Improve Bandwidth
Utilization
Notes: We take four steps to a2c
First we adopt clustering for improving locality and reducing interference
Then we balance the load across the clusters
Next we ensure to isolate sensitive applications such they suffer minimal interference
Finally we schedule critical application close to shared memory system resources

## Slide 141: Step 1 — Clustering
Inefficient data mapping to memory and caches
Memory
Controller
Notes: In a naive scheduler the requests generated by your application could go to all corners of a chip
How do you clustering the data so that requests generated by an application are satisfied by the resources within a cluster

## Slide 142: Step 1 — Clustering
Improved Locality
Reduced Interference
Cluster 0
Cluster 2
Cluster 1
Cluster 3
Notes: If you could somehow make sure to map the data to the resources within a cluster then there are two benefirs first you can improve communication locality second you can also reduce the interference between requests generated by different applications
Say first divide the chip into clusters

## Slide 143: Step 1 — Clustering
Clustering memory accesses
  Locality aware page replacement policy (cluster-CLOCK)
    When allocating free page, give preference to pages belonging to the cluster’s memory controllers (MCs)
    Look ahead “N” pages beyond the default replacement candidate to find page belonging to cluster’s MC
Clustering cache accesses
  Private caches automatically enforce clustering
  Shared caches can use Dynamic Spill Receive* mechanism
*Qureshi et al, HPCA 2009
Notes: For achieving clustering we use two techniques
We adapted to commonly used clock page replacement policy for clustering
First to cluster memory accesses we make simple modifications to commonly used CLOCK page replacement policy Our cluster-CLOCK looks “N” pages beyond the default replacement candidate in the hope of finding a page which belongs to the cluster where the application is mapped
Second we cluster cache accesses for private caches the accesses are trivially clustered
For shared caches we use a technique called Adaptive Spill Receive proposed by Qureshi et al in 2009 An application’s data is mapped to cache bank closest to it—in case it needs more cache space then its data is spilled to the next closest cache bank and so on

## Slide 144: Step 2 — Balancing
Heavy
Light
Applications
Cores
Too much load in clusters with heavy applications
Notes: After clustering we look at how to map applications to different clusters
If the conventional schedulers does not attempt to load balance you can come up with a “pathological” case shown in this slide
Where the clusters with heavy applications are heavily oversubscribed
Remind heavy and light

## Slide 145: Step 2 — Balancing
Is this the best we can do? Let’s take a look at application characteristics
Heavy
Light
Applications
Cores
Better bandwidth utilization
Notes: Obviously we shouldn’t be doing it and we employ a simple scheme to ensure that the aggregate bandwidth demand of applications in each clusters is approximately same
Two steps we discussed are fairly intuitive heuristics that has been explored in other contexts In this work identify a new opportunity for optimizing our spatial scheduler

## Slide 146: Application Types
（c） PHD Comics
Notes: Let me try to explain the application characteristics by drawing an analogy to the typical characters in a thesis committee
Applications are like the characters in your thesis committee and you are like the spatial scheduler who is trying to cater to these different characters
Thesis committee an impossibly difficult group of people to get together in a room

## Slide 147: Application Types
Identify and isolate sensitive applications while ensuring load balance
Medium
Med Miss Rate
High MLP
Guru
There for cookies
Heavy
High Miss Rate
High MLP
Adversary
Bitter rival
Light
Low Miss Rate
Nice Guy
No opinions
Asst.
Professor
Sensitive
High Miss Rate
Low MLP
Advisor
Sensitive
Thesis Committee
Applications
（c） PHD Comics
Notes: Don’t say bad guys and fillers say who still doesn’t believe that just yesterday they were on the other side
Sensitive: these applications are sensitive to latency of memory subsystem. They have high miss rates such that memory system performance matters But at the same time they have low MLP. with MLP cores issue several memory requests in parallel in the hope of overlapping future load misses with current load misses. Because of low MLP they requests are serialized and each one of them is critical Thus they would benefit from prioritization techniques which can reduce network and memory latency These applications are like your advisor who are sensitive and you can’t ignore any of their requests 
Heavy: These applications have high miss rate and high MLP. Thus they can issue lot of memory requests, how ever since they have high MLP they can hide the latency of memory requests. These applications are the ones which eat way all resources, flood the network and memory controllers and can potentially deny service to other applications. So these applications are like the : your professors bitter rival will argue the exact opposite view and ask a lot of questions
Medium: have medium miss rates and high MLP. They are less adversarial than Heavy, if you give them just enough resources they are happy They are like the Guru who is there for only cookies – just need to feed them cookies
Light: these applications have low miss rates, thus they do not effect other applications. These can be considered as fillers if you have enough slots The Strawman/woman : nice guy no opinions The Asst Prof: still doesn’t believe few months ago they were on the other side just like you--pretending to be adults

## Slide 148: Step 3 — Isolation
Heavy
Light
Applications
Cores
Sensitive
Medium
Isolate sensitive applications to a cluster
Balance load for remaining applications across clusters

## Slide 149: Step 3 — Isolation
How to estimate sensitivity?
  High Miss— high misses per kilo instruction (MPKI)
  Low MLP— high relative stall cycles per miss (STPM)
  Sensitive if MPKI > Threshold and relative STPM is high
Whether to or not to allocate cluster to sensitive applications?
How to map sensitive applications to their own cluster?
  Knap-sack algorithm
Notes: To estimate sensitive we rely on 2 performance counter values one that gives us the miss rate and the other which tells us the average number of cycles a miss spends at the head of the re-order buffer If I have high stall cycles and high enough miss rate I will classify the application as sensitive
Next we need to determine how many clusters to allocate to sensitive applications

## Slide 150: Step 4 — Radial Mapping
Heavy
Light
Applications
Cores
Sensitive
Medium
Map applications that benefit most from
being close to memory controllers close to these resources

## Slide 151: Step 4 — Radial Mapping
What applications benefit most from being close to the memory controller?
  High memory bandwidth demand
  Also affected by network performance
  Metric => Stall time per thousand instructions

## Slide 152: Putting It All Together
Balancing
Radial Mapping
Isolation
Clustering
Inter-Cluster
Mapping
Intra-Cluster
Mapping
Improve Locality
Reduce Interference
Improve Shared Resource Utilization

## Slide 153: Evaluation Methodology
60-core system
  x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  32KB private L1 and 256KB per core private L2 caches
  4GB DRAM, 160 cycle access latency, 4 on-chip DRAM controllers
  CLOCK page replacement algorithm
Detailed Network-on-Chip model
  2-stage routers (with speculation and look ahead routing)
  Wormhole switching (4 flit data packets)
  Virtual channel flow control (4 VCs, 4 flit buffer depth)
  8x8 Mesh (128 bit bi-directional channels)

## Slide 154: Configurations
Evaluated configurations
  BASE—Random core mapping
  BASE+CLS—Baseline with clustering
  A2C
Benchmarks
  Scientific, server, desktop benchmarks (35 applications)
  128 multi-programmed workloads
  4 categories based on aggregate workload MPKI
    MPKI500, MPKI1000, MPKI1500, MPKI2000
Notes: Say outermost private cache miss
Dont enumerate all steps

## Slide 155: System Performance
Chart: Normalized Weighted Speedup
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 1.0372 | 1.1184 | 1.1114 | 1.1307 | 1.0935
A2C | 1.0655 | 1.2016 | 1.2154 | 1.2299 | 1.1672
System performance improves by 17%
Notes: Radial mapping was consistently beneficial for all workloads

## Slide 156: Network Power
Chart: Normalized NoC Power
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 0.71297 | 0.70762 | 0.68333 | 0.68711 | 0.6911
A2C | 0.39619 | 0.50039 | 0.49336 | 0.49562 | 0.47611
Average network power consumption reduces by 52%

## Slide 157: Summary of Other Results
A2C can reduce page fault rate
Chart: memory footprint of workload (GB)
Chart: memory footprint of workload (GB)
Notes: We find that A2C can also help reduce interference for main memory space. Each controller manages a separate DRAM. By biasing replacement decisions to be made within each memory controller as much as possible, applications mapped to different controllers interfere less with each other in the physical memory space. As a result, applications with lower page locality disturb applications with higher page locality less, improving page fault rate. Note that our execution time results do not include this effect of reduced page faults.

## Slide 158: Summary of Other Results
A2C can reduce page faults
Dynamic A2C also improves system performance
  Continuous “Profiling” + “Enforcement” intervals
  Retains clustering benefits
  Migration overheads are minimal
A2C complements application-aware packet prioritization* in NoCs
A2C is effective for a variety of system parameters
  Number of and placement of memory controllers
  Size and organization of last level cache
*Das et al, MICRO 2009
Notes: 8086

## Slide 159: Conclusion
Problem: Spatial scheduling for Many-Core processors
  Develop fundamental insights for core mapping policies
Solution: Application-to-Core (A2C) mapping policies
A2C improves system performance, system fairness and network power significantly
Clustering
Balancing
Radial
Isolation

## Slide 160: Application-to-Core Mapping Policies to Reduce Memory System Interference
Reetuparna Das* Rachata Ausavarungnirun$ Onur Mutlu$ Akhilesh Kumar§ Mani Azimi§
*University of Michigan $Carnegie Mellon University §Intel
Notes: Hi I am Reetuparna Das and I will present our work on Application-to-Core Mapping policies to reduce memory system interference
I did this work with my collaborators at Carnegie Mellon Onur and Rachata and my colleagues at Intel Mani and Akhilesh

## Slide 161: Parallel Application Memory Scheduling
Eiman Ebrahimi*
Rustam Miftakhutdinov*, Chris Fallin‡ Chang Joo Lee*+, Jose Joao* Onur Mutlu‡, Yale N. Patt*
* HPS Research Group The University of Texas at Austin
‡ Computer Architecture Laboratory
Carnegie Mellon University
+ Intel Corporation
Austin

## Slide 162: Background
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM
Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
162

## Slide 163: Background
Memory requests from different cores interfere in shared memory resources
Multi-programmed workloads
  System Performance and Fairness
A single multi-threaded application?
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
...
DRAM
Bank K
...
Shared Memory
Resources
Chip Boundary
163
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2

## Slide 164: Memory System Interference in A Single Multi-Threaded Application
Inter-dependent threads from the same application slow each other down
Most importantly the critical path of execution can be significantly slowed down
Problem and goal are very different from interference between independent applications
  Interdependence between threads
  Goal: Reduce execution time of a single application
  No notion of fairness among the threads of the same application
164

## Slide 165: Potential in A Single Multi-Threaded Application
Chart: Normalized Execution Time
| hist | mg | cg | is | bt | ft | gmean
Series 1 | 0.7 | 0.595 | 0.345 | 0.566 | 0.861 | 0.408 | 0.552
If all main-memory related interference is ideally eliminated, execution time is reduced by 45% on average
165
Normalized to system
using FR-FCFS memory
scheduling

## Slide 166: Outline
Problem Statement
Parallel Application Memory Scheduling
Evaluation
Conclusion

## Slide 167: Outline
Problem Statement
Parallel Application Memory Scheduling
Evaluation
Conclusion

## Slide 168: Parallel Application Memory Scheduler
Identify the set of threads likely to be on the critical path as limiter threads
  Prioritize requests from limiter threads
Among limiter threads:
  Prioritize requests from latency-sensitive threads (those with lower MPKI)
Among non-limiter threads:
  Shuffle priorities of non-limiter threads to reduce inter-thread memory interference
  Prioritize requests from threads falling behind others in a parallel for-loop
168

## Slide 169: Parallel Application Memory Scheduler
Identify the set of threads likely to be on the critical path as limiter threads
  Prioritize requests from limiter threads
Among limiter threads:
  Prioritize requests from latency-sensitive threads (those with lower MPKI)
Among non-limiter threads:
  Shuffle priorities of non-limiter threads to reduce inter-thread memory interference
  Prioritize requests from threads falling behind others in a parallel for-loop
169

## Slide 170: Runtime System Limiter Identification
Contended critical sections are often on the critical path of execution
Extend runtime system to identify thread executing the most contended critical section as the limiter thread
  Track total amount of time all threads wait on each lock in a given interval
  Identify the lock with largest waiting time as the most contended
  Thread holding the most contended lock is a limiter and this information is exposed to the memory controller
170

## Slide 171: Prioritizing Requests from Limiter Threads
171
Critical Section 1
Barrier
Non-Critical Section
Waiting for Sync or Lock
Thread D
Thread C
Thread B
Thread A
Time
Barrier
Time
Barrier
Thread D
Thread C
Thread B
Thread A
Critical Section 2
Critical Path
Saved Cycles
Limiter Thread:
D
B
C
A
Most Contended Critical Section:
1
Limiter Thread Identification

## Slide 172: Parallel Application Memory Scheduler
Identify the set of threads likely to be on the critical path as limiter threads
  Prioritize requests from limiter threads
Among limiter threads:
  Prioritize requests from latency-sensitive threads (those with lower MPKI)
Among non-limiter threads:
  Shuffle priorities of non-limiter threads to reduce inter-thread memory interference
  Prioritize requests from threads falling behind others in a parallel for-loop
172

## Slide 173: Time-based classification of threads as latency- vs. BW-sensitive
Critical Section
Barrier
Non-Critical Section
Waiting for Sync
Thread D
Thread C
Thread B
Thread A
Time
Barrier
Time
Interval 1
Time
Interval 2
Thread Cluster Memory Scheduling (TCM) [Kim et. al., MICRO’10]

## Slide 174: Terminology
A code-segment is defined as:
  A program region between two consecutive synchronization operations
  Identified with a 2-tuple: <beginning IP, lock address>
Important for classifying threads as latency- vs. bandwidth-sensitive
  Time-based vs. code-segment based classification

## Slide 175: Code-segment based classification of threads as latency- vs. BW-sensitive
Thread D
Thread C
Thread B
Thread D
Thread C
Thread B
Thread A
Time
Code-Segment Changes
Barrier
Thread A
Time
Barrier
Time
Interval 1
Time
Interval 2
Code
Segment 1
Code
Segment 2
Critical Section
Barrier
Non-Critical Section
Waiting for Sync

## Slide 176: Parallel Application Memory Scheduler
Identify the set of threads likely to be on the critical path as limiter threads
  Prioritize requests from limiter threads
Among limiter threads:
  Prioritize requests from latency-sensitive threads (those with lower MPKI)
Among non-limiter threads:
  Shuffle priorities of non-limiter threads to reduce inter-thread memory interference
  Prioritize requests from threads falling behind others in a parallel for-loop
176

## Slide 177: Shuffling Priorities of Non-Limiter Threads
Goal:
  Reduce inter-thread interference among a set of threads with the same importance in terms of our estimation of the critical path
  Prevent any of these threads from becoming new bottlenecks
Basic Idea:
  Give each thread a chance to be high priority in the memory system and exploit intra-thread bank parallelism and row-buffer locality
  Every interval assign a set of random priorities to the threads and shuffle priorities at the end of the interval
177

## Slide 178: Shuffling Priorities of Non-Limiter Threads
Barrier
Thread A
Thread B
Thread C
Thread D
Barrier
Time
Thread A
Thread B
Thread C
Thread D
Time
Thread A
Thread B
Thread C
Thread D
Time
Thread A
Thread B
Thread C
Thread D
Barrier
Barrier
Time
Thread A
Thread B
Thread C
Thread D
Time
Thread A
Thread B
Thread C
Thread D
Time
4
3
2
1
3
2
1
2
1
1
Saved Cycles
Saved Cycles
Saved
Lost Cycles
178
Baseline (No shuffling)
Policy 1
Threads with similar memory behavior
Policy 2
Shuffling
Shuffling
4
2
3
1
1
2
3
2
1
1
Cycles
Active
Waiting
Legend
Threads with different memory behavior
PAMS dynamically monitors memory intensities and chooses appropriate shuffling policy for non-limiter threads at runtime

## Slide 179: Outline
Problem Statement
Parallel Application Memory Scheduling
Evaluation
Conclusion

## Slide 180: Evaluation Methodology
x86 cycle accurate simulator
Baseline processor configuration
  Per-core
    4-wide issue, out-of-order, 64 entry ROB
  Shared (16-core system)
    128 MSHRs
    4MB, 16-way L2 cache
  Main Memory
    DDR3 1333 MHz
    Latency of 15ns per command (tRP, tRCD, CL)
    8B wide core to memory bus

## Slide 181: PAMS Evaluation
Chart: Normalized Execution Time (normalized to FR-FCFS)
| hist | mg | cg | is | bt | ft | gmean
Thread cluster memory scheduler [Kim+, MICRO'10] | 0.96 | 1 | 0.95 | 0.97 | 1 | 0.85 | 0.95
Thread criticality prediction (TCP)-based memory scheduler | 0.88 | 1.12 | 1.03 | 0.72 | 1 | 0.68 | 0.895
Parallel application memory scheduler | 0.8 | 0.95 | 0.93 | 0.7 | 1 | 0.66 | 0.83
13%
181
7%
Thread criticality predictors (TCP) [Bhattacherjee+, ISCA’09]

## Slide 182: Sensitivity to system parameters
-10.5%
-15.9%
-16.7%
L2 Cache Size
4 MB
8 MB
16 MB
Δ FR-FCFS
Δ FR-FCFS
Δ FR-FCFS
-10.4%
-11.6%
-16.7%
Number of Memory Channels
1 Channel
2 Channels
4 Channels
Δ FR-FCFS
Δ FR-FCFS
Δ FR-FCFS

## Slide 183: Conclusion
Inter-thread main memory interference within a multi-threaded application increases execution time
Parallel Application Memory Scheduling (PAMS) improves a single multi-threaded application’s performance by
  Identifying a set of threads likely to be on the critical path and prioritizing requests from them
  Periodically shuffling priorities of non-likely critical threads to reduce inter-thread interference among them
PAMS significantly outperforms
  Best previous memory scheduler designed for multi-programmed workloads
  A memory scheduler that uses a state-of-the-art thread criticality predictor (TCP)

## Slide 184: Parallel Application Memory Scheduling
Eiman Ebrahimi*
Rustam Miftakhutdinov*, Chris Fallin‡ Chang Joo Lee*+, Jose Joao* Onur Mutlu‡, Yale N. Patt*
* HPS Research Group The University of Texas at Austin
‡ Computer Architecture Laboratory
Carnegie Mellon University
+ Intel Corporation
Austin

## Slide 185: Related Works

## Slide 186: Some Related Past Work
That I could not cover…
How to handle prefetch requests in a QoS-aware multi-core memory system?
  Prefetch-aware shared resource management, ISCA’11.
  Prefetch-aware memory controllers, MICRO’08, IEEE-TC’11.
  Coordinated control of multiple prefetchers, MICRO’09.
How to design QoS mechanisms in the interconnect?
  Topology-aware, scalable QoS, ISCA’11, IEEE Micro’12.
  Slack-based packet scheduling, ISCA’10, IEEE Micro’11.
  Efficient bandwidth guarantees, MICRO’09.
  Application-aware request prioritization, MICRO’09.
ISCA 2011 Talk
Micro 2009 Talk
Micro 2008 Talk

## Slide 187: Some Issues in Cache Design

## Slide 188: DRAM-Aware LLC Writeback
Problem 1: Writebacks to DRAM interfere with reads and cause additional performance penalty
  Write-to-read turnaround time in DRAM bus
  Write-recovery latency in DRAM bank
  Change of row buffer  reduced row-buffer locality for read requests
Problem 2: Writebacks that occur once in a while have low row buffer locality
Idea: When evicting a dirty cache block to a row, proactively search the cache for other dirty blocks to the same row  evict them  write to DRAM in a batch
  Improves row buffer locality
  Reduces write-to-read switching penalties on DRAM bus
  Improves performance on both single-core and multi-core systems

## Slide 189: More Information
  Chang Joo Lee, Veynu Narasiman, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems" HPS Technical Report, TR-HPS-2010-002, April 2010.

## Slide 190: DRAM-Aware Cache Design: An Example of Resource Coordination

## Slide 191: DRAM-Aware Cache Design
Coordination of cache policies with memory controllers
Chang Joo Lee, Veynu Narasiman, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems" HPS Technical Report, TR-HPS-2010-002, April 2010.
Chang Joo Lee, Eiman Ebrahimi, Veynu Narasiman, Onur Mutlu, and Yale N. Patt, "DRAM-Aware Last-Level Cache Replacement" HPS Technical Report, TR-HPS-2010-007, December 2010.

## Slide 192: Write-Caused Interference: Read-Write Switching
Read-write switching penalty for requests to any bank
Data bus:
Idle (~10 processor cycles)
Data A
Idle (~85 processor cycles)
Data C
Frequent read-write switching incurs many idle cycles
Data B
Command:
Read A
Write C
Read B
Data bus:
Data A
Data B
Command:
Read A
Read B
Row-hit read-to-read (write-to-write) to any bank: back-to-back data transfer
Notes: Two row-hit reads that are scheduled to DRAM can transfer data back-to-back as shown in the figure. It is also the case for two row-hit writes.
However (CLICK)) let’s say we have a write scheduled between the two reads (CLICK). As shown in the red box, Data C for the write cannot be written for some time after the data transfer for Read A.(CLICK) Also the data for Read B cannot be read a longer time (CLICK) after Data C is written. The data bus must be idle for these cycles regardless of which bank these reads and the write belong to.
Therefore, (CLICK) frequent read-write switching incurs many idle cycles.
6+11: 17 DRAM cycles = 85 processor cycles (4GHz, DDR-1600)

## Slide 193: Write-Caused Interference: Write-to-Row-Conflict
No precharge (~60 processor cycles)
Row-conflict after read (in the same bank)
Row-conflict after a write causes more idle cycles
Command:
Read A
Precharge
Data bus:
Data A
Idle (~120 processor cycles)
Data B
Activate B
Read or write B
Command:
Write A
Precharge
Data bus:
Data A
Data B
Activate B
Read or write B
Row-conflict after write (in the same bank)
Idle (~225 processor cycles)
Row-conflict
Row-conflict
Notes: I’ve already discussed that when a row conflict occurs, three commands need to be sent to perform the access, which are precharge, activate, and read or write. However, the effect of a conflict after a write is very different from the effect after a read. (CLICK) When a row-conflict happens after a read. It causes idle cycles as shown in red box if no request is present in other banks.
(CLICK) When it happens after a write, (CLICK) No precharge is allowed many cycles after the write burst. Therefore the row-conflict take more time to be serviced. This leads to many more idle bus cycles (CLICK) if there is no requests in other banks. (CLICK) Therefore row-conflict after write may cause many idle cycles.
Row conflict after read (2 + 11 + 11 =24): 120 idle cycles
Write-to-precharge (12): 60 idle cycles
Row conflict after write (12+ 11 + 11 + 11): 225 idle cycles

## Slide 194: Write-Caused Interference
Read-Write Switching
  Frequent read-write switching incurs many idle cycles
Write-to-Row-Conflict
  A row-conflict after a write causes more idle cycles
Generating many row-hit writes rather than row-conflict writes is preferred
Notes: To avoid frequent read--write switching and row-conflict after write penalties, (CLICK) generating many row-hit writes rather than row-conflict writes from the last-level cache is desirable.

## Slide 195: LRU vs. Interference-Aware Replacement
Read A
Write B
Row B
Row Buffer in Bank 0
DRAM
All requests are to the same cache set
DRAM Controller
Read buffer
Write buffer
Dirty C
Set X
Conventional LRU:
Reading A
Row-conflict after write penalty
Writing B
Writing C
Servicing
Write B (row-hit), Write C (row-conflict)
Clean
Clean A
Clean
Dirty B
Write C
Last-level cache
Less recently used
Notes: Let’s look at how the write-caused interference-aware replacement policy would work compared to the conventional LRU replacement policy. The figure shows DRAM and the last level cache states. Currently Read A is being serviced and a write to Row B is about to be scheduled. The cache contains two dirty lines, which are Dirty line B and Dirty line C which are mapped to Row B and Row C respectively. Dirty C is in the LRU position and Dirty B is in the second LRU position. Let’s look at the LRU policy first.
(CLICK) (CLICK) After Read A is serviced, it is inserted to the cache set. (CLICK) Since Dirty C is the LRU, LRU replacement evicts Dirty C. And (CLICK) A is inserted. (CLICK) As you see, Write B is a row-hit, however Write C from dirty C is a row-conflict. (CLICK) This results in row-conflict after write penalty.

## Slide 196: LRU vs. Interference-Aware Replacement
Read A
Write B
Row B
Row Buffer for writes
DRAM
All requests are to the same cache set
DRAM Controller
Read buffer
Write buffer
Dirty C
Last-level cache
Set X
Conventional LRU:
Less recently used
Interference-aware:
Reading A
Row-conflict after write penalty
Writing B
Writing C
Writing B
Reading A
Writing B
Reduced idle cycles
Servicing
Write B (row-hit), Write C (row-conflict)
Clean
Clean A
Clean
Dirty B
Write B
Write B (row-hit), Write B (row-hit)
A simple policy can reduce write service time
Notes: On the other hand. (CLICK) (CLICK) When A is inserted, (CLICK)A interference-aware policy would evict Dirty B because it is mapped to the same row as Write B in the write buffer. Because two writes are row-hit, (CLICK) they can be scheduled back-to-back. (CLICK) This reduces many idle cycles. (CLICK) This example shows a simple interference-aware policy can reduce write service time.

## Slide 197: Performance of DRAM-Aware Replacement
12.3%
4-core
1-core
11.4%
Notes: This slide shows the performance of the DRAM-aware replacement including both Latency-and-parallelism-aware and write-caused interference-aware components. The middle bar in each graph is the memory-level-parallelism-aware replacement policy proposed by Qureshi et al in ISCA 2006. This mechanism is not aware of DRAM characteristics. Our DRAM-aware replacement (CLICK) outperforms both the baseline and MLP-aware replacement on the single-core and 4 CMP systems by reducing cost of misses and dirty line evictions.

## Slide 198
Outline
Problem
Solutions
  Prefetch-Aware DRAM Controller
  BLP-Aware Request Issue Policies
  DRAM-Aware Cache Replacement
  DRAM-Aware Writeback
Combination of Solutions
Related Work
Conclusion
Notes: Now, I will talk about the last mechanism, DRAM-aware writeback.

## Slide 199: DRAM-Aware Writeback
Write-caused interference-aware replacement is not enough
  Row-hit writebacks are sent only when a replacement occurs
    Lose opportunities to service more writes quickly
To minimize write-caused interference, proactively clean row-hit dirty lines → Reads are serviced without write-caused interference for a longer period
Notes: Our write-cause interference-aware replacement is not enough to reduce write-caused interference. This is because it sends out row-hit writebacks only when a replacement occurs. There may be more row-hit dirty lines in the last-level cache which can be written back fast. We can think about an aggressive mechanism to further reduce write-cause interference. (CLICK) Our DRAM-aware writeback does this. It aims to minimize write-caused interference by proactively cleaning row-hit dirty lines even before replaced. Since more writebacks can be serviced quickly, reads can be serviced without interference for a longer period.

## Slide 200: DRAM-Aware Writeback
1. When a dirty line is evicted for the last-level cache, store its address
2. Using the stored address, search all possible sets for row-hit dirty lines and clean them whenever the cache bank is idle
Many row-hit writes (up to the row size) are m serviced quickly
  Reads can be serviced for a longer time without being interfered with by writes
Notes: When a dirty line is evicted from the last-level cache, the DRAM-aware writeback stores its address. And then using the stored address, it searches all possible sets for row-hit dirty lines and send writebacks of them. This is done whenever the cache is idle. Once it finishes search for all possible sets, it waits for a dirty line eviction by the underlying replacement policy. (CLICK) This can send writebacks up to the DRAM row size divided by cache line size. Therefore, once this write burst is done, reads can be serviced for a long time without interference from writes.

## Slide 201: Performance of DRAM-Aware Writeback
12.8%
4-core
1-core
7.1%
Notes: This slide shows the performance of the baseline, eager writeback, and the DRAM-aware writeback mechanisms. Eager writeback was proposed by Lee et al in MICRO 2000 to avoid write-caused interference in Rambus DRAM systems. However, it is not still DRAM characteristic-aware. Therefore, as shown, Eager writeback does not improve performance compared to the baseline. In contrast, (CLICK) the DRAM-aware writeback significantly improves performance both on single-core and 4-core systems.

## Slide 202: Readings and Videos

## Slide 203: Memory Lecture Videos
Memory Hierarchy (and Introduction to Caches)
  http://www.youtube.com/watch?v=JBdfZ5i21cs&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=22
Main Memory
  http://www.youtube.com/watch?v=ZLCy3pG7Rc0&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=25
Memory Controllers, Memory Scheduling, Memory QoS
  http://www.youtube.com/watch?v=ZSotvL3WXmA&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=26
  http://www.youtube.com/watch?v=1xe2w3_NzmI&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=27
Emerging Memory Technologies
  http://www.youtube.com/watch?v=LzfOghMKyA0&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=35
Multiprocessor Correctness and Cache Coherence
  http://www.youtube.com/watch?v=U-VZKMgItDM&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=32

## Slide 204: Readings for Topic 1 (DRAM Scaling)
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim et al., “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Liu et al., “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” CMU CS Tech Report 2013.
David et al., “Memory Power Management via Dynamic Voltage/Frequency Scaling,” ICAC 2011.
Ipek et al., “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.

## Slide 205: Readings for Topic 2 (Emerging Technologies)
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009, CACM 2010, Top Picks 2010.
Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Meza et al., “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
Meza et al., “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 206: Readings for Topic 3 (Memory QoS)
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Mutlu and Moscibroda, “Stall-Time Fair Memory Access Scheduling,” MICRO 2007.
Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008, IEEE Micro 2009.
Kim et al., “ATLAS: A Scalable and High-Performance Scheduling Algorithm for Multiple Memory Controllers,” HPCA 2010.
Kim et al., “Thread Cluster Memory Scheduling,” MICRO 2010, IEEE Micro 2011.
Muralidhara et al., “Memory Channel Partitioning,” MICRO 2011.
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Das et al., “Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems,” HPCA 2013.

## Slide 207: Readings for Topic 3 (Memory QoS)
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS 2010, ACM TOCS 2012.
Lee et al., “Prefetch-Aware DRAM Controllers,” MICRO 2008, IEEE TC 2011.
Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.
Ebrahimi et al., “Prefetch-Aware Shared Resource Management for Multi-Core Systems,” ISCA 2011.

## Slide 208: Readings in Flash Memory
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (ppt) (pdf)
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 209: Online Lectures and More Information
Online Computer Architecture Lectures
  http://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Online Computer Architecture Courses
  Intro: http://www.ece.cmu.edu/~ece447/s13/doku.php
  Advanced: http://www.ece.cmu.edu/~ece740/f11/doku.php
  Advanced: http://www.ece.cmu.edu/~ece742/doku.php
Recent Research Papers
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en

## Slide 210: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
ATLAS memory scheduler [Kim+ HPCA’10]

## Slide 211: Within-Thread Bank Parallelism
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread A
thread B
thread execution timeline
WAIT
WAIT
thread B
thread A
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread execution timeline
WAIT
WAIT
rank
thread B
thread A
thread A
thread B
SAVED CYCLES
Key Idea:
Notes: A memory scheduler can actively exploit bank-level parallelism to reduce the effective memory access latency. Here’s how.
Let us assume a case where two threads send two memory requests to two different banks.
A naïve memory scheduler that doesn’t exploit bank-level parallelism would schedule the requests in the order they arrived.
As shown in their thread execution timeline, both threads must wait for two bank latencies before all their requests are serviced.
In contrast, a memory scheduler that is aware of bank-level parallelism was proposed by Mutlu and Moscibroda.
Their key idea was to rank the threads so that thread’s memory requests are prioritized in the same order across all the banks.
In this case, let us assume that the blue thread’s request are the most prioritized.
The scheduler would then reorder the requests at bank 1’s request buffer…
so that the blue requests are serviced concurrently, after which the red requests can be serviced concurrently.
The memory service timeline shows how the access latencies for requests from the same thread are overlapped.
And, as a result, thread A has to wait less for its requests to be serviced.

## Slide 212: Parallelism-Aware Batch Scheduling [ISCA’08]
Principle 1: Schedule requests from a thread back to back
  Preserves each thread’s bank parallelism
  But, this can cause starvation…
Principle 2: Group a fixed number of oldest requests from each thread into a “batch”
  Service the batch before all other requests
  Form a new batch when the current batch is done
  Eliminates starvation, provides fairness
Bank 0
Bank 1
T0
T0
T1
T1
T3
T3
T2
T2
T3
T3
T3
Batch
T1
T0
T0
Notes: Threads are ordered such that 1) system throughput is maximized and 2) stall-time fairness is maintained
(An ordering/ranking is formed among threads)
The key idea of this ordering is to maximize system throughput

## Slide 213: ATLAS Memory Scheduler
Yoongu Kim, Dongsu Han, Onur Mutlu, and Mor Harchol-Balter, "ATLAS: A Scalable and High-Performance
Scheduling Algorithm for Multiple Memory Controllers" 16th International Symposium on High-Performance Computer Architecture (HPCA),
Bangalore, India, January 2010. Slides (pptx)
ATLAS HPCA 2010 Talk

## Slide 214: Rethinking Memory Scheduling
A thread alternates between two states (episodes)
  Compute episode: Zero outstanding memory requests  High IPC
  Memory episode: Non-zero outstanding memory requests  Low IPC
Goal: Minimize time spent in memory episodes
Outstanding memory requests
Time
Memory episode
Compute episode

## Slide 215: How to Minimize Memory Episode Time
Minimizes time spent in memory episodes across all threads
Supported by queueing theory:
  Shortest-Remaining-Processing-Time scheduling is optimal in single-server queue
Remaining length of a memory episode?
Prioritize thread whose memory episode will end the soonest
Time
Outstanding
memory requests
How much longer?

## Slide 216: Predicting Memory Episode Lengths
Large attained service  Large expected remaining service
Q: Why?
A: Memory episode lengths are Pareto distributed…
We discovered: past is excellent predictor for future
Time
Outstanding
memory requests
Remaining service
FUTURE
Attained service
PAST

## Slide 217: Pareto Distribution of Memory Episode Lengths
401.bzip2
Favoring least-attained-service memory episode
= Favoring memory episode which will end the soonest
Pr{Mem. episode > x}
x (cycles)
Memory episode lengths of
SPEC benchmarks
Pareto distribution
Attained service correlates with remaining service
The longer an episode has lasted  The longer it will last further

## Slide 218: Least Attained Service (LAS) Memory Scheduling
Prioritize the job with
shortest-remaining-processing-time
Provably optimal
Remaining service: Correlates with attained service
Attained service: Tracked by per-thread counter
Prioritize the memory episode with least-remaining-service
Our Approach
Queueing Theory
Least-attained-service (LAS) scheduling: Minimize memory episode time
However, LAS does not consider
long-term thread behavior
Prioritize the memory episode with least-attained-service

## Slide 219: Long-Term Thread Behavior
Mem. episode
Thread 1
Thread 2
Short-term thread behavior
Mem. episode
Long-term thread behavior
Compute
episode
Compute episode
>
priority
<
priority
Prioritizing Thread 2 is more beneficial:
results in very long stretches of compute episodes
Short memory episode
Long memory episode

## Slide 220: Quantum-Based Attained Service of a Thread
Time
Outstanding memory requests
Attained service
Short-term thread behavior
We divide time into large, fixed-length intervals:
quanta (millions of cycles)
Attained service
Long-term thread behavior
Outstanding memory requests
Time
…
Quantum (millions of cycles)

## Slide 221: LAS Thread Ranking
Each thread’s attained service (AS) is tracked by MCs
ASi = A thread’s AS during only the i-th quantum
Each thread’s TotalAS computed as:
TotalASi = α · TotalASi-1 + (1- α) · ASi
High α  More bias towards history
Threads are ranked, favoring threads with lower TotalAS
Threads are serviced according to their ranking
During a quantum
End of a quantum
Next quantum

## Slide 222: ATLAS Scheduling Algorithm
ATLAS
Adaptive per-Thread Least Attained Service
Request prioritization order
1. Prevent starvation: Over threshold request
2. Maximize performance: Higher LAS rank
3. Exploit locality: Row-hit request
4. Tie-breaker: Oldest request
How to coordinate MCs to agree upon a consistent ranking?

## Slide 223: System Throughput: 24-Core System
Chart: System throughput
| 1 | 2 | 4 | 8 | 16 | Memory controllers
FCFS | 4.4802 | 7.1516 | 9.4221 | 11.9271 | 14.3903
FR_FCFS | 4.5363 | 7.4098 | 9.452 | 11.9951 | 14.4325
STFM | 5.6079 | 7.2459 | 9.2466 | 11.8455 | 14.376
PAR-BS | 5.3181 | 7.9826 | 9.8744 | 12.148 | 14.4958
ATLAS | 6.2242 | 8.7648 | 10.6995 | 12.8597 | 15.0021
System throughput = ∑ Speedup
ATLAS consistently provides higher system throughput than all previous scheduling algorithms
17.0%
9.8%
8.4%
5.9%
3.5%
System throughput
# of memory controllers

## Slide 224: System Throughput: 4-MC System
Chart: System throughput
| 4 | 8 | 16 | 24 | 32 | Cores
PAR-BS | 3.2707 | 4.8105 | 7.5074 | 9.8744 | 11.6321
ATLAS | 3.307 | 4.9796 | 7.8079 | 10.6995 | 12.8871
# of cores increases  ATLAS performance benefit increases
1.1%
3.5%
4.0%
8.4%
10.8%
System throughput
# of cores

## Slide 225: Properties of ATLAS
LAS-ranking
Bank-level parallelism
Row-buffer locality
Very infrequent coordination
Scale attained service with thread weight (in paper)
Low complexity: Attained service requires a single counter per thread in each MC
Maximize system performance
Scalable to large number of controllers
Configurable by system software
Goals
Properties of ATLAS

## Slide 226: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
 What can go wrong?
A
B
C
D
D
A
B
C
D

## Slide 227: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
 What can go wrong?
A
B
C
D
D
A
B
C
D
A
B
D
C
B
C
A
D
C
D
B
A
D
A
C
B
BAD: Nice threads receive lots of interference
GOOD: Each thread prioritized once

## Slide 228: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
A
B
C
D
D
C
B
A
D

## Slide 229: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
A
B
C
D
D
C
B
A
D
D
A
C
B
B
A
C
D
A
D
B
C
D
A
C
B
GOOD: Each thread prioritized once
GOOD: Least nice thread stays
mostly deprioritized

## Slide 230: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Fairness
Throughput

## Slide 231: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 232: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 233: Outline
Background
Motivation
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: <continue from previous slide>
Let me first go over some background on memory scheduling
<click>

## Slide 234: Main Memory is a Bottleneck
All cores contend for limited off-chip bandwidth
  Inter-application interference degrades system performance
  The memory scheduler can help mitigate the problem
How does the memory scheduler deliver good performance and fairness?
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
Memory Request Buffer
Req
Req
Req
Req
Req
Req
Req
Data
Data
Req
Req
Notes: Main memory is a major bottleneck in current multi-core systems
<click three times>,
Because memory requests from different core contend for a limited off-chip bandwidth
<click>
This inter-application interference degrades system performance. And designing a good memory scheduler can mitigate the problem…
<click>
But how does memory scheduler deliver good performance and fairness.
<click to the next slide>

## Slide 235: Three Principles of Memory Scheduling
Currently open row
B
Prioritize row-buffer-hit requests [Rixner+, ISCA’00]
  To maximize memory bandwidth
Prioritize latency-sensitive applications [Kim+, HPCA’10]
  To maximize system throughput
Ensure that no application is starved [Mutlu and Moscibroda, MICRO’07]
  To minimize unfairness
Req 1 | Row A
Req 2 | Row B
Req 3 | Row C
Req 4 | Row A
Req 5 | Row B
Application | Memory Intensity (MPKI)
1 | 5
2 | 1
3 | 2
4 | 10
Older
Newer
Notes: State-of-the-art memory schedulers can deliver good performance and fairness generally based on three principles.
<click>
The first principle is to prioritize row-buffer-hit requests over other requests. The reason is because DRAM can service row-buffer-hit requests faster than requests that miss in the row buffer. This principle will maximize memory bandwidth
<click>
For example, suppose that there are five requests sorted by age as shown, and the current open row is row B. Even though request 1 is older than request 2, in this case, servicing a row hitting requests 2 first is faster than servicing requests that go to other rows. As a result, request 2 is prioritized over other requests.
<click>
The second principle is the scheduler should prioritize latency sensitive applications. Previous works have shown that latency sensitive applications can make faster forward progress when their memory requests are serviced quickly. In order to identify a latency sensitive application, memory intensity is generally used as a metric because application with lower memory intensity can make faster progress when a memory request is serviced.
<click>
For example, suppose that there are four applications in the system, and the memory intensity is defined by misses per thousand instructions. In this case, application number two will have more priority than other applications because it has the lowest memory intensity.
<click>
The third principle is the scheduler needs to make sure that the system is fair by ensuring that every application are making progress and none of the applications are starved.
<transition>
So far I have talked about memory scheduling in CPU-only systems. Now I will talk about the CPU-GPU heterogeneous system because current and future systems integrate a GPU along with multiple cores.

## Slide 236: Outline
Background
Motivation: CPU-GPU Systems
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: So far I have talked about memory scheduling in CPU-only systems. Now I will talk about the CPU-GPU heterogeneous system because current and future systems integrate a GPU along with multiple cores.

## Slide 237: Memory Scheduling for CPU-GPU Systems
Current and future systems integrate a GPU along with multiple cores
GPU shares the main memory with the CPU cores
GPU is much more (4x-20x) memory-intensive than CPU
How should memory scheduling be done when GPU is integrated on-chip?
Notes: So far I have talked about memory scheduling in CPU-only systems. Now I will talk about the CPU-GPU heterogeneous system because current and future systems integrate a GPU along with multiple cores.
This integrated GPU shares the main memory with the CPU cores; however, the GPU is four to twenty times more memory-intensive compared to CPU. So, how should the memory scheduling be done when GPU is integrated on-chip?
Let’s see how does the memory scheduling problem change when we add a GPU into the system
[picture of the current APU/Sandy Bridge]

## Slide 238: Introducing the GPU into the System
GPU occupies a significant portion of the request buffers
  Limits the MC’s visibility of the CPU applications’ differing memory behavior  can lead to a poor scheduling decision
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
Req
Req
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Notes: When GPU is introduced into the system <click>, because the GPU is memory-intensive, requests from cores contend heavily with request from the GPU, as you can see from this example
<click>
The memory-intensive GPU application will send a lot of request to the memory request buffer
<click>
As a result, some of the requests are unable to be inject into the request buffer, as illustrated by this blue request from core 2.
<click>
When only some of the memory requests can inject into the request buffer, memory scheduler cannot observe full applications behavior. This can lead to a poor scheduling decision
<click… transition>
A naïve solution to this problem is to increase the size of the monolithic request buffer…

## Slide 239: Naïve Solution: Large Monolithic Buffer
Memory Scheduler
To DRAM
Core 1
Core 2
Core 3
Core 4
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
GPU
Notes: The naïve solution is to increase the size of the batch scheduler
<click> transition: however …

## Slide 240: Problems with Large Monolithic Buffer
A large buffer requires more complicated logic to:
  Analyze memory requests (e.g., determine row buffer hits)
  Analyze application characteristics
  Assign and enforce priorities
This leads to high complexity, high power, large die area
Memory Scheduler
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
More Complex Memory Scheduler
Notes: <However (continue from the previous slide) a large buffer requires more complicated logic to analyze memory requests (for example, to determine if each request is a row hit), analyze application characteristics, assign and enforce priorities.
<click>
This leads to high complexity, high power, and large die area
<click, the big Mem sched. Appears>
<click, transition>
Our goal in this project is…

## Slide 241: Our Goal
Design a new memory scheduler that is:
  Scalable to accommodate a large number of requests
  Easy to implement
  Application-aware
  Able to provide high performance and fairness, especially in heterogeneous CPU-GPU systems
Notes: Our goal in this project is to design a new memory scheduler that is <click> scalable to accommodate a large number of requests, <click> easy-to-implement, <click> application-aware and <click> able to provide high performance and fairness especially in heterogeneous CPU-GPU systems.
<transition … >
To this end, we have made several observations that lead to our new memory scheduler design

## Slide 242: Outline
Background
Motivation: CPU-GPU Systems
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: <continue from previous slide>
To this end, we have made several observations that lead to our new memory scheduler design
<click>

## Slide 243: Key Functions of a Memory Controller
Memory controller must consider three different things concurrently when choosing the next request:
1) Maximize row buffer hits
  Maximize memory bandwidth
2) Manage contention between applications
  Maximize system throughput and fairness
3) Satisfy DRAM timing constraints
Current systems use a centralized memory controller design to accomplish these functions
  Complex, especially with large request buffers
Notes: … we observe that there are three key functions that an application aware memory scheduler need to provide concurrently when choosing the next request
<click>
First, a memory scheduler should maximize row buffer hits because this increases the bandwidth utlization
<click>
Second, a memory scheduler should be able to manage contention between different applications. This will increase system throughput and fairness
<click>
Third, a memory scheduler need to satisfy DRAM timing constraints
<click>
Current systems use a centralized memory controller design to accomplish these functions, which is complex when the request buffer is large
<click … transition>
So, our key idea is to …

## Slide 244: Key Idea: Decouple Tasks into Stages
Idea: Decouple the functional tasks of the memory controller
  Partition tasks across several simpler HW structures (stages)
1) Maximize row buffer hits
  Stage 1: Batch formation
  Within each application, groups requests to the same row into batches
2) Manage contention between applications
  Stage 2: Batch scheduler
  Schedules batches from different applications
3) Satisfy DRAM timing constraints
  Stage 3: DRAM command scheduler
  Issues requests from the already-scheduled order to each bank
Notes: Our key idea is to decouple these functional tasks <click> into different stages.
<click>
We partition these three <click> tasks across several simpler hardware structures, which we call stages.
<click>
Stage 1 is the batch formation. This stage maximizes row buffer hits by grouping requests that access the same row within each application into batches
<click>
Stage 2 is the batch scheduler. This stage manages contention by scheduling batches from different applications
<click>
And stage 3 is the DRAM command scheduler. This stage issues requests from an already scheduled order and make sure that it satisfy DRAM timing constraints
<click … transition>
With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through …

## Slide 245: Outline
Background
Motivation: CPU-GPU Systems
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: <transition>
With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through …

## Slide 246: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 247: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 248: Stage 1: Batch Formation
Goal: Maximize row buffer hits
At each core, we want to batch requests that access the same row within a limited time window
A batch is ready to be scheduled under two conditions
  1) When the next request accesses a different row
  2) When the time window for batch formation expires
Keep this stage simple by using per-core FIFOs
Notes: The goal in the batch formation stage is to maximize row buffer hits.
<click>
At each core, we want to batch request that access the same row within a limited time window
<click>
And a batch is ready to be scheduled by the batch scheduler under to conditions. The first condition is when the next request accesses a different row. The second condition is when the time window for batch formation expires to ensure forward progress
<click>
We keep this stage simple by using per-core FIFO queues
<click … transition>
And now I will show an example of how batch formation works.

## Slide 249: Stage 1: Batch Formation Example
Core 1
Core 2
Core 3
Core 4
Row A
Row B
Row B
Row C
Row D
Row D
Row E
Row F
Row E
Batch Boundary
To Stage 2 (Batch Scheduling)
Row A
Time window expires
Next request goes to a different row
Stage 1
Batch Formation
Notes: I will show an example of how the batch formation work
<click>
When there is an incoming requests that access the same row as an earlier requests. (This yellow request that accesses row B), they will be batched. And a batch will become ready to be scheduled under two conditions. First, it will become ready when a subsequent request wants to access a different row, in this case row C. The earlier request to row B will become ready to be scheduled.
A batch can become ready to be scheduled under another condition, which is when the time window for the batch formation expires, which is shown in this example in core 1. this batch formation will happen across all the cores including the GPU.

## Slide 250: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: <transition>
Now, let me tell you how Stage 2 works: the batch scheduler.

## Slide 251: Stage 2: Batch Scheduler
Goal: Minimize interference between applications
Stage 1 forms batches within each application
Stage 2 schedules batches from different applications
  Schedules the oldest batch from each application
Question: Which application’s batch should be scheduled next?
Goal: Maximize system performance and fairness
  To achieve this goal, the batch scheduler chooses between two different policies
Notes: The goal for the batch scheduler is to minimize interference between applications.
Because the batch formation forms batches within each application
<click>
The batch scheduler only need schedule batches among different applications
<click>
And because batches in stage 1 is sorted in a FIFO order, the batch scheduler only needs to consider the oldest batch from each application
<click>
The question is how can the scheduler pick the next batch?
<click>
The goal is to maximize system performance and fairness. And in order to achieve this goal, we employ two batch scheduling algorithms.
<click … transition>

## Slide 252: Stage 2: Two Batch Scheduling Algorithms
Shortest Job First (SJF)
  Prioritize the applications with the fewest outstanding memory requests because they make fast forward progress
  Pro: Good system performance and fairness
  Con: GPU and memory-intensive applications get deprioritized
Round-Robin (RR)
  Prioritize the applications in a round-robin manner to ensure that memory-intensive applications can make progress
  Pro: GPU and memory-intensive applications are treated fairly
  Con: GPU and memory-intensive applications significantly slow down others
Notes: The first algorithm we employ is the Shortest Job First policy, which
  Prioritizes the applications with the fewest outstanding memory requests because they make fast forward progress
    The benefit is shortest job first policy is it provides good system performance and fairness
    However, the GPU and memory-intensive applications get deprioritized
In order to mitigate this problem, the batch scheduler can use Round-Robin policy, which
  Prioritizes the applications in a round-robin manner to ensure that memory-intensive applications can make progress
    The benefit of using a round-robin policy is it provides high GPU performance (because it is memory-intensive)
    However, the GPU and memory-intensive applications significantly slow down others

## Slide 253: Stage 2: Batch Scheduling Policy
The importance of the GPU varies between systems and over time  Scheduling policy needs to adapt to this
Solution: Hybrid Policy
At every cycle:
  With probability p : Shortest Job First  Benefits the CPU
  With probability 1-p : Round-Robin  Benefits the GPU
System software can configure p based on the importance/weight of the GPU
  Higher GPU importance  Lower p value
Notes: The importance of the GPU varies between systems and also over time. The batch scheduling policy needs to adapt to this change.<click>
In order to adapt to this change, we propose a hybrid policy, where at every cycle:
<click> at every cycle <click>
With a probability of p, the scheduler will use SJF policy. <click>
With a probability of 1-p, the scheduler will use RR policy.<click>
And the system software can configure p based on the importance of the GPU. The more important the GPU, the low p value
<transition>
And with these two stages, batch formation and batch scheduler, both inter-application and intra-application ordering are handled. Now, I will explain the last stage of our design: the DRAM command scheduler.

## Slide 254: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: And with these two stages, batch formation and batch scheduler, both inter-application and intra-application ordering are handled. Now, I will explain the last stage of our design, which is the DRAM command scheduler.

## Slide 255: Stage 3: DRAM Command Scheduler
High level policy decisions have already been made by:
  Stage 1: Maintains row buffer locality
  Stage 2: Minimizes inter-application interference
Stage 3: No need for further scheduling
Only goal: service requests while satisfying DRAM timing constraints
Implemented as simple per-bank FIFO queues
Notes: Because high level policy decisions have already been made by stages 1 and 2, where stage 1 maintains row buffer locality and stage 2 minimizes inter-application interference. There is no need for this stage to optimize for row buffer locality, performance or fairness.
<click>
As a result, the goal of this stage is to service requests while satisfying DRAM timing constraints
<click>
And this can be implemented as simpler per-bank FIFO queues
<transition>
Now, we will show an example of how the three stages work with each other.

## Slide 256: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 257: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 258: Outline
Background
Motivation: CPU-GPU Systems
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: <continue from previous slide>
And I will go over the results
<click>

## Slide 259: Methodology
Simulation parameters
  16 OoO CPU cores, 1 GPU modeling AMD Radeon™ 5870
  DDR3-1600 DRAM 4 channels, 1 rank/channel, 8 banks/channel
Workloads
  CPU: SPEC CPU 2006
  GPU: Recent games and GPU benchmarks
  7 workload categories based on the memory-intensity of CPU applications
     Low memory-intensity (L)
     Medium memory-intensity (M)
     High memory-intensity (H)
Notes: We use an in-house cycle level simulator that models 16 OoO CPU cores and 1 GPU modeling AMD Radeon 5870. We model the main memory using DDR3 DRAM with 4 channels, 1 rank and 8 banks.
<click>
We use SPEC 2006 for the CPU applications and recent games and GPU Benchmarks for the GPU. We divide the workload into 7 workload categories based on the memory intensity of the CPU and this varies from low, medium and high memory-intensity applications measured based on LLC MPKI
<click, transition>

## Slide 260: Comparison to Previous Scheduling Algorithms
FR-FCFS [Rixner+, ISCA’00]
  Prioritizes row buffer hits
  Maximizes DRAM throughput
  Low multi-core performance  Application unaware
ATLAS [Kim+, HPCA’10]
  Prioritizes latency-sensitive applications
  Good multi-core performance
  Low fairness  Deprioritizes memory-intensive applications
TCM [Kim+, MICRO’10]
  Clusters low and high-intensity applications and treats each separately
  Good multi-core performance and fairness
  Not robust  Misclassifies latency-sensitive applications
Notes:     We compare our proposed mechanism with three previous state-of-the-art memory scheduling algorithms.
    <click>
    The first algorithm we compare to is a row-hit first algorithm that prioritize row buffer hitting requests first. And this will maximizes DRAM throughput. However, as previous work have shown, FR-FCFS has low multi-core performance because it is application unaware
    <click>
    The second algorithm we compare to is adaptive per thread least attained service memory scheduling algorithm, which prioritizes latency sensitive applications. This algorithm gives good multi-core performance. However, previous work has shown that this algorithm is unfair because memory-intensive applications are deprioritized
    <click>
    The last algorithm we compare to is thread cluster memory scheduling algorithm, which cluster low and high memory intensity applications into two different clusters, and treats each cluster differently to improve both performance and fairness. However, we observe that TCM is not robust enough in the context of CPU-GPU heterogeneous system. Because TCM misclassify latency sensitive applications and put these applications in a wrong cluster, and it uses a wrong scheduling policy on these miss-classified applications.
    <click … transition>

## Slide 261: Evaluation Metrics
CPU performance metric: Weighted speedup
GPU performance metric: Frame rate speedup
CPU-GPU system performance: CPU-GPU weighted speedup
Notes: We evaluated CPU performance using weighted speedup which is defined by the sum of IPC of the CPU when it is running with other applications compared to when it is running alone
<click>
We evaluated GPU performance using GPU speedup which is defined by the frame rate speedup of the GPU when it is running with other applications compared to when it is running alone
<click>
In terms of the system performance, we use CPU-GPU weighted speedup, which is the sum of CPU weighted speedup and the GPU speedup. However, we multiply the GPU speedup with the GPU weight <click> which can be changed based on the important of the GPU.
<click … transition>

## Slide 262: Evaluated System Scenarios
CPU-focused system
GPU-focused system
Notes: We will evaluate SMS using two different scenarios
<click> The first scenario is the CPU-focus system <click> and the second scenario is the GPU-focused system.
We will now talk about the CPU-focused system

## Slide 263: Evaluated System Scenario: CPU Focused
GPU has low weight (weight = 1)
Configure SMS such that p, SJF probability, is set to 0.9
  Mostly uses SJF batch scheduling  prioritizes latency-sensitive applications (mainly CPU)
1
Notes: On a CPU-focused system <click> The GPU has low weight of 1, and in this case, SMS is configured such that P, the probablity of using the shortest job first batch scheduling policy, is set to 0.9. This will mostly use shortest job first batch scheduling, which prioritize latency sensitive applications.
<click>

## Slide 264: Performance: CPU-Focused System
SJF batch scheduling policy allows latency-sensitive applications to get serviced as fast as possible
Chart: CGWS
| L | ML | M | HL | HML | HM | H | Avg
FR-FCFS | 7.066 | 5.678 | 3.023 | 4.0314 | 3.6181 | 2.2517 | 1.5751 | 3.8919
ATLAS | 7.8662 | 6.6578 | 4.0265 | 5.4299 | 5.0318 | 3.0926 | 1.9522 | 4.8653
TCM | 7.6659 | 6.388 | 3.5808 | 5.0101 | 4.5112 | 2.744 | 1.8778 | 4.5397
SMS_0.9 | 11.0198 | 8.6314 | 4.5778 | 5.801 | 5.2337 | 3.0224 | 1.6682 | 5.7077
+17.2% over ATLAS
SMS is much less complex than previous schedulers
p=0.9
Workload Categories
Notes: This plot shows the performance of SMS on a CPU focused system. The y-axis represents the system performance measured by the CPU-GPU weighted speedup with the GPU weight of 1, and the X-axis is the performance on each workload categories sorted from low intensity to high intensity.
<click>
When the CPU performance is important, setting the probability of using the shortest job first batch scheduling policy to a high value, allows the latency-sensitive applications to get serviced as fast as possible. <click> This improve system performance by 17.2% on average compared to the previous best scheduling mechanism.
<click>
In addition to the performance gain, the design of SMS is much simpler compared to previous designs.

## Slide 265: Evaluated System Scenario: GPU Focused
GPU has high weight (weight = 1000)
Configure SMS such that p, SJF probability, is set to 0
  Always uses round-robin batch scheduling  prioritizes memory-intensive applications (GPU)
1000
Notes: On a GPU-focused system <click> The GPU has high weight of 1000, and in this case, SMS is configured such that P, the probability of using the shortest job first batch scheduling policy, is set to 0. This will use round-robin batch scheduling policy all the time, which gives priority to the GPU.
<click>

## Slide 266: Performance: GPU-Focused System
Round-robin batch scheduling policy schedules GPU requests more frequently
Chart: CGWS
| L | ML | M | HL | HML | HM | H | Avg
FR-FCFS | 980.2029 | 951.8914 | 939.388 | 783.8121 | 862.3228 | 800.7138 | 779.8686 | 871.1714
ATLAS | 950.0175 | 865.8395 | 746.4181 | 537.4795 | 577.1246 | 525.2205 | 467.7448 | 667.1207
TCM | 967.3195 | 914.1203 | 869.5664 | 649.7908 | 726.5373 | 632.6294 | 562.7337 | 760.3854
SMS_0 | 927.6489 | 910.4414 | 908.4153 | 847.6915 | 891.603 | 870.5232 | 839.1282 | 885.0645
+1.6% over FR-FCFS
SMS is much less complex than previous schedulers
p=0
Workload Categories
Notes: This plot shows the performance of SMS on a GPU focused system. The y-axis represents the system performance measured by the CPU-GPU weighted speedup with the GPU weight of 1000, and the X-axis is the performance on each workload categories sorted from low intensity to high intensity.
<click>
When the GPU performance is important, always using the round-robin policy will schedule GPU requests more frequently.
<click> This improve system performance by 1.6% on average compared to the previous best scheduling mechanism, which is FR-FCFS.
<click>
In addition to the performance gain, the design of SMS is much simpler compared to previous designs.

## Slide 267: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 268: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 269: Additional Results in the Paper
Fairness evaluation
  47.6% improvement over the best previous algorithms
Individual CPU and GPU performance breakdowns
CPU-only scenarios
  Competitive performance with previous algorithms
Scalability results
  SMS’ performance and fairness scales better than previous algorithms as the number of cores and memory channels increases
Analysis of SMS design parameters
Notes: In addition to the previous results, we also provide other key results in the paper. We have shown that SMS provides significant fairness improvement over previous algorithms. We also provided individual CPU and GPU performance breakdowns. SMS performs competitively in CPU-only scenarios. We have shown that SMS scales better with the increasing number of cores and memory channels, and we also provide an analysis of different design parameters in the paper.

## Slide 270: Outline
Background
Motivation: CPU-GPU Systems
Our Goal
Observations
Staged Memory Scheduling
  1) Batch Formation
  2) Batch Scheduler
  3) DRAM Command Scheduler
Results
Conclusion
Notes: Now I will conclude

## Slide 271: Conclusion
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer size
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution is to decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 272: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores

## Slide 273: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 274: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
274

## Slide 275: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 276: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 277
A4
B1
A1
A2
A3
Oldest
⎧
⎪
⎪
⎩
Shared Memory
Resources
A:
Compute
Stall on A1
Stall on A2
Stall on A3
Stall on A4
Compute
Stall waiting for shared resources
Stall on B1
B:
Request Generation Order:
A1, A2, A3, A4, B1
Unmanaged Interference
Core A’s stall time
Core B’s stall time
A4
B1
A1
A2
A3
⎧
⎪
⎪
⎩
Shared Memory
Resources
A:
Compute
Stall on A1
Stall on A2
Compute
Stall wait.
Stall on B1
B:
Dynamically detect application A’s interference for application B and throttle down application A
Core A’s stall time
Core B’s stall time
Fair Source Throttling
Stall wait.
Request Generation Order
A1,
A2, A3, A4,
B1
B1,
A2, A3, A4
queue of requests to
shared resources
queue of requests to
shared resources
Saved Cycles Core B
Oldest
Intensive application A generates many requests and causes long stall times for less intensive application B
Throttled
Requests
Stall on A4
Stall on A3
Extra Cycles
Core A
Notes: Lets look at an example of how this approach can intuitively work
Lets assume two concurrently executing applications A, and B,
and we compare two scenarios, one where interference is left unmanaged, and in the second we show how fair source throttling can improve unfairness and performance.
Here we see the queue of requests to shared resources which will be filled with entries from both applications.
Now each of the applications does compute for some time, during which each of them generates some memory requests. Lets say application A is very memory intensive and generates many more memory requests than application B.
This results in the requests being generated in the order shown on the slide. Lets assume that these requests all interfere with one another. First four requests are generated from application A and then one request from application B.
These requests fill in the queue of requests to shared resources. Lets say requests are issued to the shared memory resources from this queue based on a first come first served policy. As a result,
Application A’s requests get serviced by the shared resources first, and
result in the shown memory related stall time for application A
During this time application B stalls waiting for application A’s requests to get serviced,
and only then gets its request serviced. This results in the shown memory related stall time for application B.
In summary the intensive application A generates many requests which cause long stall times for the less intensive application B.
Now our approach with fair source throttling was to pose the question: what if at runtime we could dynamically detect that application A was interfering significantly with application B, and upon detecting this situation we could throttle application A back such that
some of its requests would be generated after the request from application B
the queue of requests to the shared resources
would now be filled in as shown in the slide. As a result,
The first access to be serviced by the shared resources is A1.
and As A1 is being serviced, application B stalls waiting for the shared resources.
Then request B1 gets serviced by the shared resources
which results in a much smaller stall time for application B than in the first scenario.
After this, the throttled requests from application A get serviced, and
This results in the shown stall time for application A which is slightly longer than the first scenario. However we managed to
reduce application B’s memory related stall time a lot. Overall, this can improve fairness as application A is a memory intensive application that has large stall times even when running in isolation, so increasing application A’s stall time a little bit only slightly increases its slowdown compared to the first scenario. But the large reduction in the stall time of application B significantly reduces its associated slowdown. This can also improve system throughput as the less memory intensive application B can now go back to its compute phase faster and stall less.
so we want to be able to dynamically detect application A’s interference for application B, and throttle the cores appropriately to improve fairness and performance.
-----

## Slide 278: Fairness via Source Throttling (FST)
Two components (interval-based)
Run-time unfairness evaluation (in hardware)
  Dynamically estimates the unfairness in the memory system
  Estimates which application is slowing down which other
Dynamic request throttling (hardware or software)
  Adjusts how aggressively each core makes requests to the shared resources
  Throttles down request rates of cores causing unfairness
    Limit miss buffers, limit injection rate

## Slide 279: Fairness via Source Throttling (FST)
279
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 280: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
280

## Slide 281: Estimating System Unfairness
Unfairness =
Slowdown of application i =
How can be estimated in shared mode?
is the number of extra cycles it takes application i to execute due to interference
Max{Slowdown i} over all applications i
Min{Slowdown i} over all applications i
Shared
Ti
Ti
Alone
Ti
Alone
Ti
Excess
Ti
Shared
=
Ti
Alone
-
Ti
Excess

## Slide 282: Tracking Inter-Core Interference
0
0
0
0
Interference per core
bit vector
Core #
0
1
2
3
Core 0
Core 1
Core 2
Core 3
Bank 0
Bank 1
Bank 2
Bank 7
...
Memory Controller
Shared Cache
Three interference sources:
1. Shared Cache
2. DRAM bus and bank
3. DRAM row-buffers
FST hardware
Bank 2
Row

## Slide 283: Tracking DRAM Row-Buffer Interference
Row A
Core 0
Core 1
Bank 0
Bank 1
Bank 2
Bank 7
…
Shadow Row Address Register
(SRAR) Core 1:
Shadow Row Address Register
(SRAR) Core 0:
Queue of requests to bank 2
0
0
Row B
Row A
Row A
Row B
Row B
Interference
per core bit vector
Row Conflict
Row Hit
Interference
induced row conflict
1
Row A

## Slide 284: Tracking Inter-Core Interference
0
0
0
0
Interference per core
bit vector
Core #
0
1
2
3
0
0
0
0
Excess Cycles
Counters per core
1
T
Cycle Count
T+1
1
T+2
2
FST hardware
1
T+3
3
1
Core 0
Core 1
Core 2
Core 3
Bank 0
Bank 1
Bank 2
Bank 7
...
Memory Controller
Shared Cache
Ti
Excess
⎪
⎪
Ti
Shared
=
Ti
Alone
-
Ti
Excess

## Slide 285: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
285
Notes: The runtime unfairness evaluation component should also determine which application causes most interference for Appslowest, this application is called app-interfering

## Slide 286: Tracking Inter-Core Interference
To identify App-interfering, for each core i
  FST separately tracks interference caused by each core j ( j ≠ i )
Cnt 3
Cnt 2
Cnt 1
Cnt 0
0
0
0
0
-
Interference per core
bit vector
Core #
0
1
2
3
-
Cnt 1,0
Cnt 2,0
Cnt 3,0
Excess Cycles
Counters per core
0
0
-
0
0
-
0
0
-
0
0
0
⎪
⎨
⎪
⎧
⎩
⎪
⎨
⎪
⎧
⎩
Interfered with core
Interfering
core
Cnt 0,1
-
Cnt 2,1
Cnt 3,1
Cnt 0,2
Cnt 1,2
-
Cnt 3,2
Cnt 0,3
Cnt 1,3
Cnt 2,3
-
1
core 2
interfered
with
core 1
Cnt 2,1+
0
1
2
3
Row with largest count
determines App-interfering
App-slowest = 2
Pairwise interference
bit matrix
Pairwise excess cycles
matrix

## Slide 287: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering

## Slide 288: Dynamic Request Throttling
Goal: Adjust how aggressively each core makes requests to the shared memory system
Mechanisms:
  Miss Status Holding Register (MSHR) quota
    Controls the number of concurrent requests accessing shared resources from each application
  Request injection frequency
    Controls how often memory requests are issued to the last level cache from the MSHRs

## Slide 289: Dynamic Request Throttling
Throttling level assigned to each core determines both MSHR quota and request injection rate
Throttling level | MSHR quota | Request Injection Rate
100% | 128 | Every cycle
50% | 64 | Every other cycle
25% | 32 | Once every 4 cycles
10% | 12 | Once every 10 cycles
5% | 6 | Once every 20 cycles
4% | 5 | Once every 25 cycles
3% | 3 | Once every 30 cycles
2% | 2 | Once every 50 cycles
Total # of
MSHRs: 128

## Slide 290: FST at Work
Time
Interval i
Interval i+1
Interval i+2
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
FST
Unfairness Estimate
App-slowest
App-interfering
Throttling Levels
Core 0
Core 1
Core 3
50%
100%
10%
100%
25%
100%
25%
100%
25%
50%
50%
100%
Interval i
Interval i + 1
Interval i + 2
3
Core 2
Core 0
Core 0
Core 2
Throttle down
Throttle up
2.5
Core 2
Core 1
Throttle down
Throttle up
System software fairness goal: 1.4
Slowdown
Estimation
⎪
⎨
⎪
⎧
⎩
Slowdown
Estimation
⎪
⎨
⎪
⎧
⎩

## Slide 291: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 292: FST Hardware Cost
Total storage cost required for 4 cores is ~12KB
FST does not require any structures or logic that are on the processor’s critical path

## Slide 293: FST Evaluation Methodology
x86 cycle accurate simulator
Baseline processor configuration
  Per-core
    4-wide issue, out-of-order, 256 entry ROB
  Shared (4-core system)
    128 MSHRs
    2 MB, 16-way L2 cache
  Main Memory
    DDR3 1333 MHz
    Latency of 15ns per command (tRP, tRCD, CL)
    8B wide core to memory bus

## Slide 294: FST: System Unfairness Results
grom+art+astar+h264
lbm+omnet+apsi+vortex
art+leslie+games+grom
art+astar+leslie+crafty
lbm+Gems+astar+mesa
gcc06+xalanc+lbm+cactus
gmean
44.4%
36%
art+games+Gems+h264
art+milc+vortex+calculix
lucas+ammp+xalanc+grom
mgrid+parser+soplex+perlb

## Slide 295: FST: System Performance Results
295
gmean
25.6%
14%
grom+art+astar+h264
art+games+Gems+h264
lbm+omnet+apsi+vortex
art+leslie+games+grom
art+astar+leslie+crafty
art+milc+vortex+calculix
lucas+ammp+xalanc+grom
lbm+Gems+astar+mesa
mgrid+parser+soplex+perlb
gcc06+xalanc+lbm+cactus
295

## Slide 296: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control
FST ASPLOS 2010 Talk

## Slide 297: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores

## Slide 298: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 299: Outline
Goal:
Mitigate
Inter-Application Interference
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling

## Slide 300: Previous Approach
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Previous Approach:
Application-Aware Memory Request Scheduling
Goal:
Mitigate
Inter-Application Interference

## Slide 301: Application-Aware Memory Request Scheduling
Monitor application memory access characteristics
Rank applications based on memory access characteristics
Prioritize requests at the memory controller, based on ranking

## Slide 302: An Example: Thread Cluster Memory Scheduling
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Figure: Kim et al., MICRO 2010

## Slide 303: Application-Aware Memory Request Scheduling
Advantages
Reduces interference between applications by
request reordering
Improves system performance
Disadvantages
Requires modifications to memory scheduling logic for
  Ranking
  Prioritization
Cannot completely eliminate interference by request reordering

## Slide 304: Our Approach
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Goal:
Mitigate
Inter-Application Interference

## Slide 305: Observation: Modern Systems Have Multiple Channels
A new degree of freedom
Mapping data across multiple channels
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory

## Slide 306: Data Mapping in Current Systems
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Causes interference between applications’ requests
Page

## Slide 307: Partitioning Channels Between Applications
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Page
Eliminates interference between applications’ requests

## Slide 308: Overview: Memory Channel Partitioning (MCP)
Goal
  Eliminate harmful interference between applications
Basic Idea
  Map the data of badly-interfering applications to different channels
Key Principles
  Separate low and high memory-intensity applications
  Separate low and high row-buffer locality applications

## Slide 309: Key Insight 1: Separate by Memory Intensity
High memory-intensity applications interfere with low memory-intensity applications in shared memory channels
Map data of low and high memory-intensity applications
to different channels
1
2
3
4
5
Channel 0
Bank 1
Channel 1
Bank 0
Conventional Page Mapping
Red App
Blue App
Time Units
Core
Core
Bank 1
Bank 0
Channel Partitioning
Red App
Blue App
Channel 0
Time Units
1
2
3
4
5
Channel 1
Core
Core
Bank 1
Bank 0
Bank 1
Bank 0
Saved Cycles
Saved Cycles

## Slide 310: Key Insight 2: Separate by Row-Buffer Locality
High row-buffer locality applications interfere with low
row-buffer locality applications in shared memory channels
Conventional Page Mapping
Channel 0
Bank 1
Channel 1
Bank 0
R1
R0
R2
R3
R0
R4
Request Buffer State
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
R0
Channel 0
R1
R2
R3
R0
R4
Request Buffer State
Channel Partitioning
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Saved
Cycles
Map data of low and high row-buffer locality applications to different channels

## Slide 311: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 312: 1. Profile Applications
Hardware counters collect application memory access characteristics
Memory access characteristics
  Memory intensity:
  Last level cache Misses Per Kilo Instruction (MPKI)
  Row-buffer locality:
  Row-buffer Hit Rate (RBH) - percentage of accesses that hit in the row buffer

## Slide 313: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 314: 3. Partition Channels Among Groups: Step 1
Channel 1
Assign number of channels proportional to number of applications in group
.
.
.
High Intensity
Low Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel 3
High Intensity
High Row-Buffer Locality

## Slide 315: 3. Partition Channels Among Groups: Step 2
Channel 1
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
.
.
.
Assign number of channels proportional to bandwidth demand of group
Channel 3
Channel 1
.
.
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel N-1
Channel N
Channel 3
.
.
.

## Slide 316: 4. Assign Preferred Channel to Application
Channel 1
Low Intensity
Channel 2
MPKI: 1
MPKI: 3
MPKI: 4
MPKI: 1
MPKI: 3
MPKI: 4
Assign each application a preferred channel from its group’s allocated channels
Distribute applications to channels such that group’s bandwidth demand is balanced across its channels

## Slide 317: 5. Allocate Page to Preferred Channel
Enforce channel preferences computed in the previous step
On a page fault, the operating system
  allocates page to preferred channel if free page available in preferred channel
  if free page not available, replacement policy tries to allocate page to preferred channel
  if it fails, allocate page to another channel

## Slide 318: Interval Based Operation
time
Current Interval
Next Interval
1. Profile applications
2. Classify applications into groups
3. Partition channels between groups
4. Assign preferred channel to applications
5. Enforce channel preferences

## Slide 319: Integrating Partitioning and Scheduling
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Goal:
Mitigate
Inter-Application Interference

## Slide 320: Observations
Applications with very low memory-intensity rarely access memory  Dedicating channels to them results in precious memory bandwidth waste
They have the most potential to keep their cores busy  We would really like to prioritize them
They interfere minimally with other applications  Prioritizing them does not hurt others

## Slide 321: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications

## Slide 322: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit

## Slide 323: Methodology
Simulation Model
  24 cores, 4 channels, 4 banks/channel
  Core Model
    Out-of-order, 128-entry instruction window
    512 KB L2 cache/core
  Memory Model – DDR2
Workloads
  240 SPEC CPU 2006 multiprogrammed workloads (categorized based on memory intensity)
Metrics
  System Performance

## Slide 324: Previous Work on Memory Scheduling
FR-FCFS [Zuravleff et al., US Patent 1997, Rixner et al., ISCA 2000]
  Prioritizes row-buffer hits and older requests
  Application-unaware
ATLAS [Kim et al., HPCA 2010]
  Prioritizes applications with low memory-intensity
TCM [Kim et al., MICRO 2010]
  Always prioritizes low memory-intensity applications
  Shuffles request priorities of high memory-intensity applications

## Slide 325: Comparison to Previous Scheduling Policies
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Significant performance improvement over baseline FRFCFS
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 326: Interaction with Memory Scheduling
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061
IMPS | 1.1108 | 1.08 | 1.09
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061

IMPS improves performance regardless of scheduling policy
Highest improvement over FRFCFS as IMPS designed for FRFCFS
Averaged over 240 workloads

## Slide 327: MCP Summary
Uncontrolled inter-application interference in main memory degrades system performance
Application-aware memory channel partitioning (MCP)
  Separates the data of badly-interfering applications to different channels, eliminating interference
Integrated memory partitioning and scheduling (IMPS)
  Prioritizes very low memory-intensity applications in scheduler
  Handles other applications’ interference by partitioning
MCP/IMPS provide better performance than application-aware memory request scheduling at lower hardware cost

## Slide 328: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 329: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread that is falling behind the most in a parallel for loop
PAMS Micro 2011 Talk

## Slide 330: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 331: Conclusions: Topic 3
Technology, application, architecture trends dictate new needs from memory system
A fresh look at (re-designing) the memory hierarchy
  Scalability: DRAM-System Codesign and New Technologies
  QoS: Reducing and controlling main memory interference: QoS-aware memory system design
  Efficiency: Customizability, minimal waste, new technologies
QoS-unaware memory: uncontrollable and unpredictable
Providing QoS awareness improves performance, predictability, fairness, and utilization of the memory system