## Slide 1: Memory Systems and Memory-Centric Computing Systems Lec 3 Topic 2: Memory Reliability and Security
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 July 2018
HiPEAC ACACES Summer School 2018

## Slide 2: What Will You Learn in This Course?
Memory Systems and Memory-Centric Computing Systems
  July 9-13, 2018
Topic 1: Main Memory Trends and Basics
Topic 2: Memory Reliability & Security: RowHammer and Beyond
Topic 3: In-memory Computation
Topic 4: Low-Latency and Low-Energy Memory
Topic 5 (unlikely): Enabling and Exploiting Non-Volatile Memory
Topic 6 (unlikely): Flash Memory and SSD Scaling
Major Overview Reading:
  Mutlu and Subramaniam, “Research Problems and Opportunities in Memory Systems,” SUPERFRI 2014.

## Slide 3: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 4: Understanding RowHammer

## Slide 5: Root Causes of Disturbance Errors
Cause 1: Electromagnetic coupling
  Toggling the wordline voltage briefly increases the voltage of adjacent wordlines
  Slightly opens adjacent rows  Charge leakage
Cause 2: Conductive bridges
Cause 3: Hot-carrier injection
Confirmed by at least one manufacturer
Notes: Why do the errors occur? We see three possible causes.
First, there could electromagnetic coupling between adjacent wordlines. When the voltage of one is toggled, it could briefly increase the voltage of the other and facilitate the leakage of charge.
Two other possibilities are conductive bridges and hot-carrier injection.
At least one manufacturer confirmed that these three could play a role in the disturbance errors we see them today.

## Slide 6: Experimental DRAM Testing Infrastructure
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 7: Experimental DRAM Testing Infrastructure
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 8: RowHammer Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 9: 4. Adjacency: Aggressor & Victim
Most aggressors & victims are adjacent
Note: For three modules with the most errors (only first bank)
Adjacent
Adjacent
Adjacent
Non-Adjacent
Non-Adjacent
Notes: In this figure, the x-axis is the row-address difference between an aggressor and its victims. And the y-axis is the number of victim-aggressor pairs that correspond to the row-address difference. For all three modules, we see strong peaks at plus/minus 1. This implies that aggressors and victims have consecutive row-addresses, in other words, they are adjacent.
However, the figure also shows some victims that are not adjacent to the aggressor. We believe this could be caused by two reasons. First, depending on the mapping, two rows that are physically adjacent within the DRAM chip may not have consecutive row-addresses. Second, fault rows are often re-mapped to spare rows that may reside on a different portion of the DRAM chip.
Nevertheless, we conclude that the vast majority of aggressors & victims are adjacent.

## Slide 10: ❶ Access Interval (Aggressor)
Note: For three modules with the most errors (only first bank)
Not Allowed
Less frequent accesses  Fewer errors
55ns
500ns
Notes: In this figure, the x-axis is the interval at which we access the aggressor. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 55ns in our experiments. However, as we increase the access-interval, we see that the number of errors decreases. In particular, at 500ns, there are no errors for all three modules.
From this, we conclude that less frequent accesses induce fewer errors.

## Slide 11: ❷ Refresh Interval
Note: Using three modules with the most errors (only first bank)
More frequent refreshes  Fewer errors
~7x frequent
64ms
Notes: In this figure, the x-axis is the refresh-interval. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 64ms in our experiments. However, as we decrease the refresh-interval, we see that the number of errors decreases. In particular, when the refresh is shortened by 7x, there are no errors for all three modules.
From this, we conclude that more frequent accesses induce fewer errors.

## Slide 12: ❸ Data Pattern
RowStripe
~RowStripe
111111
111111
111111
111111
000000
000000
000000
000000
000000
111111
000000
111111
111111
000000
111111
000000
Solid
~Solid
10x Errors
Errors affected by data stored in other cells
Notes: We tested the modules with four different data-patterns: Solid, inverse Solid, RowStripe, and inverse RowStripe. Solid and inverse Solid give us full coverage since each cell is tested with both 1s and 0s. And the same applies to RowStripe and its inverse.
However, we found that the rowstripe pattern had 10 times as more errors than the solid pattern. We also tested many other data-patterns, including random, but found RowStripe to induce the most errors.
Therefore, we conclude that errors are affected by data stored in other cells due to differences in coupling effects between the cells.

## Slide 13: 6. Other Results (in Paper)
Victim Cells ≠ Weak Cells (i.e., leaky cells)
  Almost no overlap between them
Errors not strongly affected by temperature
  Default temperature: 50°C
  At 30°C and 70°C, number of errors changes <15%
Errors are repeatable
  Across ten iterations of testing, >70% of victim cells had errors in every iteration
Notes: First, we show that victim cells are not weak cells, which are cells that are inherently leaky. According to our experiments, we saw almost no overlap between them.
Second, we show that errors are not strongly affected by temperature. In all of the tests so far, we set the temperature to 50 degrees Celsius. But even when we changed the temperature by 20 degrees, the number of errors changed by less than 15 percent.
Third, we show that errors are repeatable. Across ten iterations of testing, more than 70% of victim cells had errors in every iteration.

## Slide 14: 6. Other Results (in Paper) cont’d
As many as 4 errors per cache-line
  Simple ECC (e.g., SECDED) cannot prevent all errors
Number of cells & rows affected by aggressor
  Victims cells per aggressor: ≤110
  Victims rows per aggressor: ≤9
Cells affected by two aggressors on either side
  Very small fraction of victim cells (<100) have an error when either one of the aggressors is toggled
Notes: Fourth, we show that there are as many as four errors per cacheline. From this, we conclude that simple ECC schemes (for example, SECDED) cannot prevent all errors.
Fifth, we show that the number of cells & rows affected by an aggressor can be as high as 110 or 9, respectively.
Lastly, we show that a very small fraction of victim cells experience an error when either one of the aggressors is toggled.

## Slide 15: More on RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data]

## Slide 16: Retrospective on RowHammer & Future
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 17: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 18: Future Memory Reliability/Security Challenges

## Slide 19: Future of Main Memory
DRAM is becoming less reliable  more vulnerable

## Slide 20: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 21
Intuition: quadratic increase in capacity
DRAM Reliability Reducing
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.

## Slide 22: Aside: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet]

## Slide 23: Future of Main Memory
DRAM is becoming less reliable  more vulnerable
Due to difficulties in DRAM scaling, other problems may also appear (or they may be going unnoticed)
Some errors may already be slipping into the field
  Read disturb errors (Rowhammer)
  Retention errors
  Read errors, write errors
  …
These errors can also pose security vulnerabilities

## Slide 24: DRAM Data Retention Time Failures
Determining the data retention time of a cell/row is getting more difficult
Retention failures may already be slipping into the field

## Slide 25: Analysis of Data Retention Failures [ISCA’13]
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 26: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 27: Two Challenges to Retention Time Profiling
Challenge 1: Data Pattern Dependence (DPD)
  Retention time of a DRAM cell depends on its value and the values of cells nearby it
  When a row is activated, all bitlines are perturbed simultaneously

## Slide 28: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 29: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Retention time of a cell depends on data patterns stored in nearby cells
 need to find the worst data pattern to find worst-case retention time
 this pattern is location dependent
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 30: Two Challenges to Retention Time Profiling
Challenge 2: Variable Retention Time (VRT)
  Retention time of a DRAM cell changes randomly over time
    a cell alternates between multiple retention time states
  Leakage current of a cell changes sporadically due to a charge trap in the gate oxide of the DRAM cell access transistor
  When the trap becomes occupied, charge leaks more readily from the transistor’s drain, leading to a short retention time
    Called Trap-Assisted Gate-Induced Drain Leakage
  This process appears to be a random process [Kim+ IEEE TED’11]
  Worst-case retention time depends on a random process
     need to find the worst case despite this

## Slide 31: Modern DRAM Retention Time Distribution
Newer device families have more weak cells than older ones
Likely a result of technology scaling
OLDER
NEWER
OLDER
NEWER

## Slide 32: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 33: Variable Retention Time
A 2Gb chip family
Min ret time = Max ret time
Expected if no VRT
Most failing cells
exhibit VRT
Many failing cells jump from
very high retention time to very low

## Slide 34: More on Data Retention Failures [ISCA’13]
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 35: Industry Is Writing Papers About It, Too

## Slide 36: Industry Is Writing Papers About It, Too

## Slide 37: Refresh Overhead: Performance
8%
46%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 38: Refresh Overhead: Energy
15%
47%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 39: Retention Time Profile of DRAM

## Slide 40: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 41: More on RAIDR: Perf+Energy Perspective
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 42: Finding DRAM Retention Failures
How can we reliably find the retention time of all DRAM cells?
Goals: so that we can
  Make DRAM reliable and secure
  Make techniques like RAIDR work
   improve performance and energy

## Slide 43: Mitigation of Retention Issues [SIGMETRICS’14]
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 44: Towards an Online Profiling System
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
  But degrades performance
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Notes: Our high-level design for online profiling system is based to thee key observations:

## Slide 45: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 46: Handling Variable Retention Time [DSN’15]
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 47: AVATAR
Insight: Avoid retention failures  Upgrade row on ECC error
Observation: Rate of VRT >> Rate of soft error (50x-2500x)
A
B
C
D
E
F
G
H
DRAM Rows
RETENTION
PROFILING
Weak Cell
0
0
1
0
0
0
1
0
Ref. Rate Table
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
1
AVATAR mitigates VRT by increasing refresh rate on error
Scrub
(15 min)
Row protected from future
retention failures

## Slide 48: RESULTS: REFRESH SAVINGS
AVATAR
No VRT
AVATAR reduces refresh by 60%-70%, similar to multi rate refresh but with VRT tolerance
Retention Testing Once a Year can revert refresh saving from 60% to 70%

## Slide 49: SPEEDUP
Speedup
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 1.04 | 1.065 | 1.13 | 1.35
NoRefresh | 1.05 | 1.09 | 1.21 | 1.54
AVATAR gets 2/3rd the performance of NoRefresh. More gains at higher capacity nodes

## Slide 50: ENERGY DELAY PRODUCT
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 0.95 | 0.88 | 0.75 | 0.52
NoRefresh | 0.91 | 0.83 | 0.68 | 0.41
Energy Delay Product
AVATAR reduces EDP,
Significant reduction at higher capacity nodes

## Slide 51: Handling Data-Dependent Failures [DSN’16]
Samira Khan, Donghyuk Lee, and Onur Mutlu, "PARBOR: An Efficient System-Level Technique to Detect Data-Dependent Failures in DRAM" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Toulouse, France, June 2016. [Slides (pptx) (pdf)]

## Slide 52: Handling Data-Dependent Failures [MICRO’17]
Samira Khan, Chris Wilkerson, Zhe Wang, Alaa R. Alameldeen, Donghyuk Lee, and Onur Mutlu, "Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 53: Handling Both DPD and VRT [ISCA’17]
Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions" Proceedings of the 44th International Symposium on Computer Architecture (ISCA), Toronto, Canada, June 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]
First experimental analysis of (mobile) LPDDR4 chips
Analyzes the complex tradeoff space of retention time profiling
Idea: enable fast and robust profiling at higher refresh intervals & temperatures

## Slide 54: The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions
Minesh Patel Jeremie S. Kim
Onur Mutlu
Notes: Hi, I’m Minesh Patel from ETH Zurich
and today, I’ll talk about the reach profiler, a new methodology for DRAM retention failure profiling

## Slide 55
SA
SA
SA
SA
SA
Row Decoder
DRAM
Leaky
Notes: DRAM is composed of a heterogeneous set of cells with various different leakage rates

## Slide 56
Leaky Cells
Periodic DRAM Refresh
Performance + Energy Overhead
Notes: This requires a process called DRAM refresh in order to periodically restore charge to the leaky cells
However, this results in significant system performance and energy penalties.

## Slide 57
Goal: find all retention failures for
a refresh interval T > default (64ms)
SA
SA
SA
SA
SA
Row Decoder
Notes: Ideally, we would like to identify all the cells that fail at a given refresh interval so that we can extend the default refresh interval past 64ms and mitigate DRAM refresh overhead

## Slide 58
Variable retention time
Data pattern dependence
Process, voltage, temperature
Notes: However, there are a number of unwanted effects that complicate profiling, which I will go into in detail in my talk later this afternoon

## Slide 59
Characterization of
368 LPDDR4 DRAM Chips
1
2
Cells are more likely to fail at an
increased (refresh interval | temperature)
Complex tradeoff space between profiling
(speed & coverage & false positives)
Notes: In order to better understand these effects in modern DRAM, we perform the first extensive characterization of 368 LPDDR4 DRAM chips
We make two major observations
First, we find that cells are more likely to fail at an increased refresh interval or temperature
Second, we identify a complex tradeoff space surrounding profiling, and characterize it in terms of profiling speed, failure coverage, and false positive rate

## Slide 60
refresh interval
temperature
operate
here
Notes: We leverage these observations to develop the reach profiler, which searches for failures NOT at the operating conditions,

## Slide 61
refresh interval
temperature
REACH
PROFILING
profile
here
operate
here
Notes: But rather at reach conditions, where cells are more likely to fail

## Slide 62
+ Faster and more reliable
than current approaches
Reach Profiling
A new DRAM retention failure profiling methodology
+ Enables longer refresh intervals
Notes: We find that this not only increases profiling speed and reliability beyond prior approaches to profiling,
But also enables longer refresh intervals that were previously unreasonable due to profiling overhead

## Slide 63: REAPER Outline
1. DRAM Refresh Background
2. Failure Profiling Challenges
4. LPDDR4 Characterization
5. Reach Profiling
3. Current Approaches
6. End-to-end Evaluation
18/36
Notes: To this end, we perform an extensive characterization of LPDDR4 DRAM chips
[END]

## Slide 64
368 2y-nm LPDDR4 DRAM chips
  4Gb chip size
  From 3 major DRAM vendors
Thermally controlled testing chamber
  Ambient temperature range: {40°C – 55°C} ± 0.25°C
  DRAM temperature is held at 15°C above ambient
Experimental Infrastructure
19/36
Notes: The infrastructure we developed can test 368 state-of-the-art LPDDR4 DRAM chips.
Each chip is 4 gigaBITS in size, and we have chips from across three major DRAM vendors.
[CLICK]
We test within a thermally controlled chamber with an ambient temperature range of 40 to 55 degrees C with a tolerance of 0.25 degrees.
DRAM temperature is always held at 15 degrees C above ambient using a local heat source
[END]

## Slide 65
LPDDR4 Studies
Temperature
Data Pattern Dependence
Retention Time Distributions
Variable Retention Time
Individual Cell Characterization
20/36
Notes: Here are the studies that we did using our infrastructure.
We find that the first three, temperature, data pattern dependence, and retention time distributions, show results similar to those in prior work using DDR3 DRAM.
[CLICK]
Therefore, in this talk I’m going to focus on 4 and 5, variable retention time, and individual cell characterization, which show new results that help motivate our mechanism.
[END]

## Slide 66
New failing cells continue to appear over time
  Attributed to variable retention time (VRT)
The set of failing cells changes over time
Representative chip from Vendor B, 2048ms, 45°C
# New Failing Cells
Time (days)
Long-term Continuous Profiling
21/36
Notes: Here is some data we collected from a representative chip at a fixed refresh interval of 2048ms.
We show the number of new failing cells discovered by continuously profiling over 6 days.
[CLICK]
We see that new failing cells continue to appear over time.
We attribute these to variable retention time effects, which mean that cells can randomly change retention times at any point.
[CLICK]
This shows that the set of failing cells we find at 2048ms changes over time
[CLICK]
This means that error correction codes and online profiling are necessary to manage new failing cells that continue to appear
[END]

## Slide 67
New failing cells continue to appear over time
  Attributed to variable retention time (VRT)
The set of failing cells changes over time
Representative chip from Vendor B, 2048ms, 45°C
# New Failing Cells
Time (days)
Error correction codes (ECC)
and online profiling are necessary
to manage new failing cells
Long-term Continuous Profiling
21/36
Notes: Here is some data we collected from a representative chip at a fixed refresh interval of 2048ms.
We show the number of new failing cells discovered by continuously profiling over 6 days.
[CLICK]
We see that new failing cells continue to appear over time.
We attribute these to variable retention time effects, which mean that cells can randomly change retention times at any point.
[CLICK]
This shows that the set of failing cells we find at 2048ms changes over time
[CLICK]
This means that error correction codes and online profiling are necessary to manage new failing cells that continue to appear
[END]

## Slide 68: Single-cell Failure Probability (Cartoon)
Chart: Refresh Interval (s)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Y-Values
idealized cell
(retention time = 3s)
22/36
Notes: In another study, we analyzed the failure probability of individual cells.
Here we show the probability of read failure for a single cell over different refresh intervals
We show an idealized cell, with never fails below 3.5 seconds, but always fails above 3.5s
We can say that this cell has a retention time of 3.5s.
[CLICK]
However, we find that real cells look more like the blue cartoon, which follows a normal distribution with a mean at 3.5s.
Note that even below 3.5s, there is a nonzero probability of the cell failing.
[END]

## Slide 69: Single-cell Failure Probability (Cartoon)
Chart: Refresh Interval (s)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Y-Values
idealized cell
(retention time = 3s)
actual cell
N(μ, σ) | μ = 3s
22/36
Notes: In another study, we analyzed the failure probability of individual cells.
Here we show the probability of read failure for a single cell over different refresh intervals
We show an idealized cell, with never fails below 3.5 seconds, but always fails above 3.5s
We can say that this cell has a retention time of 3.5s.
[CLICK]
However, we find that real cells look more like the blue cartoon, which follows a normal distribution with a mean at 3.5s.
Note that even below 3.5s, there is a nonzero probability of the cell failing.
[END]

## Slide 70
Chart: 
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 71
Chart: 
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
failed 9 times out of 16 trials
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 72
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 73
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 74
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 75
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 76
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
hard
to find
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 77
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
profile here
hard
to find
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 78
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
profile here
hard
to find
easy
to find
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 79
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
profile here
hard
to find
false
positives
easy
to find
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 80
Chart: Refresh Interval (s)
| 0.25600000000000001 | 0.32 | 0.38400000000000001 | 0.44800000000000001 | 0.51200000000000001 | 0.57599999999999896 | 0.64 | 0.70399999999999896 | 0.76800000000000002 | 0.83199999999999896 | 0.89600000000000002 | 0.95999999999999897 | 1.024 | 1.0880000000000001 | 1.1519999999999899 | 1.21599999999999 | 1.28 | 1.3440000000000001 | 1.4079999999999899 | 1.47199999999999 | 1.536 | 1.6 | 1.6639999999999899 | 1.72799999999999 | 1.792 | 1.8560000000000001 | 1.9199999999999899 | 1.98399999999999 | 2.048 | 2.1120000000000001 | 2.1760000000000002 | 2.2400000000000002 | 2.3039999999999901 | 2.3679999999999901 | 2.4319999999999902 | 2.4959999999999898 | 2.56 | 2.6240000000000001 | 2.6880000000000002 | 2.75199999999999 | 2.8159999999999901 | 2.8799999999999901 | 2.9439999999999902 | 3.008 | 3.0720000000000001 | 3.1360000000000001 | 3.2 | 3.26399999999999 | 3.3279999999999901 | 3.3919999999999901 | 3.4559999999999902 | 3.52 | 3.5840000000000001 | 3.6480000000000001 | 3.7120000000000002 | 3.77599999999999 | 3.8399999999999901 | 3.9039999999999901 | 3.9679999999999902 | 4.032 | 4.0960000000000001
Y-Values
Column1
Column2
Column3
Column4
Column5
Column6
Column7
Column8
Column9
Column10
Column11
Chart: 
Column8
Column9
Column10
Column11
Single-cell Failure Probability (Real)
operate here
profile here
hard
to find
false
positives
easy
to find
Any cell is more likely to fail
at a longer refresh interval
OR a higher temperature
22/36
Notes: TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE TEMPERATURE
Here we show real data from a real chip, [CLICK] which we collected by testing how often the cell failed out of 16 trials for different refresh intervals.
[CLICK]
We now show 8 different cells from the same chip.
[CLICK]
Suppose we are interested in operating at a refresh interval of 1.7 seconds.
[CLICK]
We will find 6 cells with a non-negligible probability of failing
[CLICK]
However, the bottom two cells will be hard to find since they have a low probability of failure at this refresh interval
[CLICK]
Instead, if we profile at an increased refresh interval, [CLICK] the same cells will be much easier to find since they will have a high probability of failure.
[CLICK]
However, we will also identify some additional cells as failing, which can end up being false positives.
[CLICK]
We repeat the same analysis for temperature variation and find that cells behave similarly. We show details of this analysis in the paper.
[CLICK]
The takeaway here is that any given cell is more likely to fail at a longer refresh interval or a higher temperature.
[END]

## Slide 81: REAPER Outline
1. DRAM Refresh Background
2. Failure Profiling Challenges
4. LPDDR4 Characterization
5. Reach Profiling
3. Current Approaches
6. End-to-end Evaluation
23/36
Notes: This leads us into the key idea of reach profiling
[END]

## Slide 82
Reach Profiling
Key idea: profile at a longer refresh interval and/or a higher temperature
refresh interval
temperature
operate
here
24/36
Notes: …which is to profile NOT at the desired operating conditions, but rather at a longer refresh interval and/or a higher tempereature
[CLICK]
The pros of this approach are that it’s faster and more reliable since we are profiling for failures where they are most likely to occur
[CLICK]
However, we may also identify false positives, which fail under profiling conditions but not under operating conditions
[END]

## Slide 83
Reach Profiling
Key idea: profile at a longer refresh interval and/or a higher temperature
refresh interval
temperature
operate
here
profile
here
24/36
Notes: …which is to profile NOT at the desired operating conditions, but rather at a longer refresh interval and/or a higher tempereature
[CLICK]
The pros of this approach are that it’s faster and more reliable since we are profiling for failures where they are most likely to occur
[CLICK]
However, we may also identify false positives, which fail under profiling conditions but not under operating conditions
[END]

## Slide 84
Pros
  Fast + Reliable: reach profiling searches for cells where they are most likely to fail
Cons
  False Positives: profiler may identify cells that fail under profiling conditions, but not under operating conditions
Reach Profiling
Key idea: profile at a longer refresh interval and/or a higher temperature
25/36
Notes: …which is to profile NOT at the desired operating conditions, but rather at a longer refresh interval and/or a higher tempereature
[CLICK]
The pros of this approach are that it’s faster and more reliable since we are profiling for failures where they are most likely to occur
[CLICK]
However, we may also identify false positives, which fail under profiling conditions but not under operating conditions
[END]

## Slide 85
Towards an Implementation
Reach profiling is a general methodology
3 key questions for an implementation:
What are desirable profiling conditions?
How often should the system profile?
What information does the profiler need?
26/36
Notes: Reach profiling as shown is a general methodology.
[CLICK]
In order to turn it into a concrete implementation, we need to answer three key questions
[CLICK]
First, what are the desirable profiling conditions?
[CLICK]
Second, how often must we reprofile?
[CLICK]
Third, what information does the profiler need in order to figure all of this out?
[END]

## Slide 86
  Runtime: how long profiling takes
  Coverage: portion of all possible failures discovered by profiling
  False positives: number of cells observed to fail during profiling but never during actual operation
Three Key Profiling Metrics
27/36
Notes: To this end, we identify three key metrics we can use to characterize any retention failure profiling mechanism.
[CLICK]
Runtime represents how long profiling actually takes
[CLICK]
Coverage represents the portion of all possible failures that are discovered by the profiling mechanism
[CLICK]
False positives represent the number of cells that are observed to fail during profiling, but never during actual operation
[CLICK]
We then perform a detailed exploration of how these three metrics change under many different profiling conditions.
[END]

## Slide 87
  Runtime: how long profiling takes
  Coverage: portion of all possible failures discovered by profiling
  False positives: number of cells observed to fail during profiling but never during actual operation
Three Key Profiling Metrics
We explore how these three metrics
change under many different
profiling conditions
27/36
Notes: To this end, we identify three key metrics we can use to characterize any retention failure profiling mechanism.
[CLICK]
Runtime represents how long profiling actually takes
[CLICK]
Coverage represents the portion of all possible failures that are discovered by the profiling mechanism
[CLICK]
False positives represent the number of cells that are observed to fail during profiling, but never during actual operation
[CLICK]
We then perform a detailed exploration of how these three metrics change under many different profiling conditions.
[END]

## Slide 88
Evaluation Methodology
Simulators
  Performance: Ramulator [Kim+, CAL’15]
  Energy: DRAMPower [Chandrasekar+, DSD’11]
Configuration
  4-core (4GHz), 8MB LLC
  LPDDR4-3200, 4 channels, 1 rank/channel
Workloads
  20 random 4-core benchmark mixes
  SPEC CPU2006 benchmark suite
33/36
Notes: We evaluate REAPER using Ramulator for performance and DRAMPower for DRAM energy.
We model a 4-core system using 4 channels of LPDDR4 DRAM
[CLICK]
We measure performance and energy across 20 random 4-core benchmark mixes drawn from the SPEC CPU2006 benchmark suite
[END]

## Slide 89
Simulated End-to-end Performance
refresh interval (ms)
34/36
Notes: Here is a plot of our simulated end-to-end performance gain for operating at different refresh intervals.
The boxplots show the distribution of benchmark performance for brute-force profiling, REAPER, and the ideal profiling mechanism with no overhead.
[CLICK]
We see that for short refresh intervals, where we reprofile rarely, profiling overhead is not significant and both profiling mechanisms come close to ideal.
[CLICK]
However, for long refresh intervals where we reprofile often, profiling overhead is highly significant and actually begins to cause system performance degradation.
[CLICK]
We see that at 1024 and 1280 milliseconds, visibly REAPER outperforms brute-force profiling, maintaining more of the ideal profiler’s benefit than brute-force profiling is able to.
[CLICK]
Overall, we find that REAPER enables a best-case 16.3% system performance improvement and a 36.4% DRAM power reduction, which is shown in the paper.
[CLICK]
Furthermore, REAPER enables the 1280ms refresh interval, which is unreasonable with brute-force profiling due to profiling overhead.
[END]

## Slide 90
Simulated End-to-end Performance
Reprofile often
Reprofile rarely
refresh interval (ms)
34/36
Notes: Here is a plot of our simulated end-to-end performance gain for operating at different refresh intervals.
The boxplots show the distribution of benchmark performance for brute-force profiling, REAPER, and the ideal profiling mechanism with no overhead.
[CLICK]
We see that for short refresh intervals, where we reprofile rarely, profiling overhead is not significant and both profiling mechanisms come close to ideal.
[CLICK]
However, for long refresh intervals where we reprofile often, profiling overhead is highly significant and actually begins to cause system performance degradation.
[CLICK]
We see that at 1024 and 1280 milliseconds, visibly REAPER outperforms brute-force profiling, maintaining more of the ideal profiler’s benefit than brute-force profiling is able to.
[CLICK]
Overall, we find that REAPER enables a best-case 16.3% system performance improvement and a 36.4% DRAM power reduction, which is shown in the paper.
[CLICK]
Furthermore, REAPER enables the 1280ms refresh interval, which is unreasonable with brute-force profiling due to profiling overhead.
[END]

## Slide 91
Simulated End-to-end Performance
Reprofile often
Reprofile rarely
refresh interval (ms)
34/36
Notes: Here is a plot of our simulated end-to-end performance gain for operating at different refresh intervals.
The boxplots show the distribution of benchmark performance for brute-force profiling, REAPER, and the ideal profiling mechanism with no overhead.
[CLICK]
We see that for short refresh intervals, where we reprofile rarely, profiling overhead is not significant and both profiling mechanisms come close to ideal.
[CLICK]
However, for long refresh intervals where we reprofile often, profiling overhead is highly significant and actually begins to cause system performance degradation.
[CLICK]
We see that at 1024 and 1280 milliseconds, visibly REAPER outperforms brute-force profiling, maintaining more of the ideal profiler’s benefit than brute-force profiling is able to.
[CLICK]
Overall, we find that REAPER enables a best-case 16.3% system performance improvement and a 36.4% DRAM power reduction, which is shown in the paper.
[CLICK]
Furthermore, REAPER enables the 1280ms refresh interval, which is unreasonable with brute-force profiling due to profiling overhead.
[END]

## Slide 92
Simulated End-to-end Performance
Reprofile often
Reprofile rarely
refresh interval (ms)
On average, REAPER enables:
16.3% system performance improvement
36.4% DRAM power reduction
REAPER enables longer refresh intervals, which are unreasonable
using brute-force profiling
34/36
Notes: Here is a plot of our simulated end-to-end performance gain for operating at different refresh intervals.
The boxplots show the distribution of benchmark performance for brute-force profiling, REAPER, and the ideal profiling mechanism with no overhead.
[CLICK]
We see that for short refresh intervals, where we reprofile rarely, profiling overhead is not significant and both profiling mechanisms come close to ideal.
[CLICK]
However, for long refresh intervals where we reprofile often, profiling overhead is highly significant and actually begins to cause system performance degradation.
[CLICK]
We see that at 1024 and 1280 milliseconds, visibly REAPER outperforms brute-force profiling, maintaining more of the ideal profiler’s benefit than brute-force profiling is able to.
[CLICK]
Overall, we find that REAPER enables a best-case 16.3% system performance improvement and a 36.4% DRAM power reduction, which is shown in the paper.
[CLICK]
Furthermore, REAPER enables the 1280ms refresh interval, which is unreasonable with brute-force profiling due to profiling overhead.
[END]

## Slide 93
Other Analyses in the Paper
Detailed LPDDR4 characterization data
  Temperature dependence effects
  Retention time distributions
  Data pattern dependence
  Variable retention time
  Individual cell failure distributions
Profiling tradeoff space characterization
  Runtime, coverage, and false positive rate
  Temperature and refresh interval
Probabilistic model for tolerable failure rates
Detailed results for end-to-end evaluations
35/36
Notes: The paper contains many other analyses that we didn’t have time to cover here today.
[CLICK]
These include a much more detailed characterization of LPDDR4 DRAM chips, including results and takeaways
[CLICK]
A much more in-depth analysis of the tradeoff space surrounding profiling
[CLICK]
A detailed analysis of the probabilistic model we use to compute how often we need to reprofile
[CLICK]
And detailed results for our end-to-end evaluations, including both performance and energy
[END]

## Slide 94
Problem:
DRAM refresh performance and energy overhead is high
Current approaches to retention failure profiling are slow or unreliable
Goals:
Thoroughly analyze profiling tradeoffs
Develop a fast and reliable profiling mechanism
Key Contributions:
First detailed characterization of 368 LPDDR4 DRAM chips
Reach profiling: Profile at a longer refresh interval or higher temperature than target conditions, where cells are more likely to fail
Evaluation:
2.5x faster profiling with 99% coverage and 50% false positives
REAPER enables 16.3% system performance improvement and 36.4% DRAM power reduction
Enables longer refresh intervals that were previously unreasonable
REAPER Summary
36/36
Notes: To conclude, I’ll go over a summary of the talk.
The high level motivation for this work is that DRAM refresh is a major impediment to scaling, especially in terms of energy.
The specific problem that we focus on is that DRAM retention failure profiling is hard.
Our goals in this work are twofold. First, we would like to thoroughly analyze retention failure profiling tradeoffs
Second, we would like to use what we learn to develop a fast, reliable profiling mechanism.
We make two key contributions in this work.
First, we perform the first detailed retention failure characterization of 368 LPDDR4 DRAM chips
Second, we use what we learn to introduce the reach profiler, which profiles for failures at a longer refresh interval and/or a higher temperature, where cells are more likely to fail.
Through our evaluations, we find that reach profiling increases profiling performance by an average of 2.5x while maintaining high coverage and a moderate false positive rate.
Our implementation of reach profiling, called REAPER, enables significant system performance improvement and DRAM power reduction.
Finally, reach profiling enables longer refresh intervals that were previously unreasonable due to profiling overhead.
[END]

## Slide 95: Handling Both DPD and VRT [ISCA’17]
Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions" Proceedings of the 44th International Symposium on Computer Architecture (ISCA), Toronto, Canada, June 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]
First experimental analysis of (mobile) LPDDR4 chips
Analyzes the complex tradeoff space of retention time profiling
Idea: enable fast and robust profiling at higher refresh intervals & temperatures

## Slide 96: The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern Commodity DRAM Devices
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
QR Code for the paper
https://people.inf.ethz.ch/omutlu/pub/dram-latency-puf_hpca18.pdf
HPCA 2018
Notes: Please come to my talk at HPCA 2018, if you would like to learn more or have any questions. Thank you very much.

## Slide 97: How Do We Keep Memory Secure?
DRAM
Flash memory
Emerging Technologies
  Phase Change Memory
  STT-MRAM
  RRAM, memristors
  …

## Slide 98: Solution Direction: Principled Designs
Design fundamentally secure
computing architectures
Predict and prevent
such safety issues

## Slide 99: How Do We Keep Memory Secure?
Understand: Solid methodologies for failure modeling and discovery
  Modeling based on real device data – small scale and large scale
  Metrics for secure architectures
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
  Patch-ability in the field
Design & Test: Principled electronic design, automation, testing
  Design for security
  High coverage and good interaction with reliability methods

## Slide 100
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Understand and Model with Experiments (DRAM)

## Slide 101: Understand and Model with Experiments (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE’17, HPCA’18, SIGMETRICS’18]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 102: Understanding Flash Memory Reliability
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 103: Understanding Flash Memory Reliability
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 104: NAND Flash Vulnerabilities [HPCA’17]
https://people.inf.ethz.ch/omutlu/pub/flash-memory-programming-vulnerabilities_hpca17.pdf
HPCA, Feb. 2017

## Slide 105: 3D NAND Flash Reliability I [HPCA’18]
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "HeatWatch: Improving 3D NAND Flash Memory Device Reliability by Exploiting Self-Recovery and Temperature-Awareness" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 106: 3D NAND Flash Reliability II [SIGMETRICS’18]
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "Improving 3D NAND Flash Memory Lifetime by Tolerating Early Retention Loss and Process Variation" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Irvine, CA, USA, June 2018. [Abstract]

## Slide 107: If Time Permits: NAND Flash Vulnerabilities
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" Proceedings of the IEEE, September 2017.
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.
Luo+, “HeatWatch: Improving 3D NAND Flash Memory Device Reliability by Exploiting Self-Recovery and Temperature-Awareness," HPCA 2018.
Luo+, “Improving 3D NAND Flash Memory Lifetime by Tolerating Early Retention Loss and Process Variation," SIGMETRICS 2018.
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 108: There are Two Other Solution Directions
New Technologies: Replace or (more likely) augment DRAM with a different technology
  Non-volatile memories
Embracing Un-reliability:
Design memories with different reliability
and store data intelligently across them
[Luo+ DSN 2014]
…
Fundamental solutions to security require co-design across the hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 109: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 110: Heterogeneous-Reliability Memory
App 1 data A
App 1 data B
App 2 data A
App 2 data B
App 3 data A
App 3 data B
Step 2: Map application data to the HRM system enabled by SW/HW cooperative solutions
Step 1: Characterize and classify application memory error tolerance
Reliable memory
Parity memory + software recovery (Par+R)
Low-cost memory
Unreliable
Reliable
Vulnerable
Tolerant
App 1 data A
App 2 data A
App 2 data B
App 3 data A
App 3 data B
App 1 data B
Notes: Now we have described the key idea of HRM and Par+R, let’s look at our mechanism to put them together.
First, we characterize and classify application data in terms of their memory error tolerance, rank them from vulnerable to tolerant.
Then, we map application data to HRM according to their error tolerance. As an example here, vulnerable data is mapped to reliable memory, tolerable data is mapped to low-cost memory, and recoverable data is mapped to parity memory with Par+R.

## Slide 111: Evaluation Results
Typical Server
Consumer PC
HRM
Less-Tested (L)
HRM/L
Bigger area means better tradeoff
Outer is better
Inner is worse
Notes: Here is a radar graph for all 5 metrics and systems.
Each axis represents one of the metrics, each closed curve represents the results of the system its color stands for.
We show crashes and incorrect query rates in negative numbers so that, for all of the axes, outer is better.
We conclude that our HRM systems have the largest areas.

## Slide 112: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 113: Summary: Memory Reliability and Security
Memory reliability is reducing
Reliability issues open up security vulnerabilities
  Very hard to defend against
Rowhammer is an example
  Its implications on system security research are tremendous & exciting
Good news: We have a lot more to do.
Understand: Solid methodologies for failure modeling and discovery
  Modeling based on real device data – small scale and large scale
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled electronic design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 114: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 115: One Important Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 116: Memory Systems and Memory-Centric Computing Systems Lec 3 Topic 2: Memory Reliability and Security
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 July 2018
HiPEAC ACACES Summer School 2018

## Slide 117: Flash Memory Reliability and Security

## Slide 118: Evolution of NAND Flash Memory
Flash memory is widening its range of applications
  Portable consumer devices, laptop PCs and enterprise servers
Seaung Suk Lee, “Emerging Challenges in NAND Flash Technology”, Flash Summit 2011 (Hynix)
CMOS scaling
More bits per Cell

## Slide 119: Flash Challenges: Reliability and Endurance
E. Grochowski et al., “Future technology challenges for NAND flash and HDD products”, Flash Memory Summit 2012
P/E cycles (required)
P/E cycles (provided)
A few thousand
Writing
the full capacity
of the drive
10 times per day
for 5 years
(STEC)
> 50k P/E cycles

## Slide 120: NAND Flash Memory is Increasingly Noisy
Noisy NAND
Write
Read

## Slide 121: Future NAND Flash-based Storage Architecture
Memory
Signal
Processing
Error
Correction
Raw Bit
Error Rate
Uncorrectable
BER < 10-15
Noisy
High
Lower
Build reliable error models for NAND flash memory
Design efficient reliability mechanisms based on the model
Our Goals:
Better

## Slide 122: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory”, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery”, HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 123: Our Goals and Approach
Goals:
  Understand error mechanisms and develop reliable predictive models for MLC NAND flash memory errors
  Develop efficient error management techniques to mitigate errors and improve flash reliability and endurance
Approach:
  Solid experimental analyses of errors in real MLC NAND flash memory  drive the understanding and models
  Understanding, models, and creativity  drive the new techniques

## Slide 124: Experimental Testing Platform
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 125: NAND Flash Error Types
Four types of errors [Cai+, DATE 2012]
Caused by common flash operations
  Read errors
  Erase errors
  Program (interference) errors
Caused by flash cell losing charge over time
  Retention errors
    Whether an error happens depends on required retention time
    Especially problematic in MLC flash because threshold voltage window to determine stored value is smaller

## Slide 126: Observations: Flash Error Analysis
retention errors
Raw bit error rate increases exponentially with P/E cycles
Retention errors are dominant (>99% for 1-year ret. time)
Retention errors increase with retention time requirement
P/E Cycles
Raw Bit Error Rate
Cai et al., Error Patterns in MLC NAND Flash Memory, DATE 2012.

## Slide 127: More on Flash Error Analysis
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 128: Solution to Retention Errors
Refresh periodically
Change the period based on P/E cycle wearout
  Refresh more often at higher P/E cycles
Use a combination of in-place and remapping-based refresh
Cai et al. “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime”, ICCD 2012.

## Slide 129: Flash Correct-and-Refresh [ICCD’12]
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (ppt)(pdf)

## Slide 130: Many Errors and Their Mitigation [PIEEE’17]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 131: Many Errors and Their Mitigation [PIEEE’17]
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 132: One Issue: Read Disturb in Flash Memory
All scaled memories are prone to read disturb errors
DRAM
SRAM
Hard Disks: Adjacent Track Interference
NAND Flash

## Slide 133: NAND Flash Memory Background
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Block 0
Block 1
Block N
Read
Pass
Pass
…
Pass
Notes: When we read from one page in a block, we apply a high voltage to all the other pages in the same block. We will explain why later

## Slide 134: Flash Cell Array
Sense Amplifiers
Block X
Page Y
Sense Amplifiers
Row
Column
Notes: Now, let’s zoom in to a single block of flash memory, which consists of an array of flash pages.
Each flash page is written to flash cells located in the same row.
Each row of cells are controlled by the same horizontal wire.
Each column of cells are connected in series with a sense amplifier at the bottom.

## Slide 135: Flash Cell
Floating Gate
Gate
Drain
Source
Floating Gate Transistor
(Flash Cell)
Vth = 2.5 V
Notes: Now let’s zoom in again to look at a single flash cell, or, it can also be called, a floating gate transistor.

## Slide 136: Flash Read
Vread = 2.5 V
Vth = 3 V
Vth = 2 V
1
0
Vread = 2.5 V
Gate
Notes: Now, if we have two flash cells programmed to different threshold voltages, 2V and 3V, we can distinguish them with a read voltage of 2.5V.
When we apply 2.5V to the gate, since the read voltage is higher than the threshold voltage, …
Now if we look back at this example, we can see that the threshold voltage of each flash cell actually represents the value being stored.

## Slide 137: Flash Pass-Through
Vpass = 5 V
Vth = 2 V
1
Vpass = 5 V
Gate
1
Vth = 3 V
Notes: But, for the same cells, when we apply a high voltage to them, regardless of the threshold voltage, any cell will be passed-through.
So we call this voltage pass-through voltage or Vpass

## Slide 138: Read from Flash Cell Array
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
1
1
0
0
Correct values for page 2:
Page 1
Page 2
Page 3
Page 4
Pass (5V)
Read (2.5V)
Pass (5V)
Pass (5V)
Notes: Now, let’s look at an example array of flash cells.
In this example, we make up threshold voltage numbers for each cell.
Let’s say we want to read from the second page in this array.
So we apply a read voltage of 2.5 V to the second page
And since all the other pages are connected in series, we apply a high pass-through voltage of 5 V to the other pages.
As we can see, the high pass through voltage switches on all the flash pages being passed-through, allowing the sense amplifier to read the values stored in the second page.
In this case, the correct values …

## Slide 139: Read Disturb Problem: “Weak Programming” Effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Repeatedly read page 3 (or any page other than page 2)
Read (2.5V)
Pass (5V)
Pass (5V)
Pass (5V)
Page 1
Page 2
Page 3
Page 4
Notes: However, the high pass through voltage can generate read disturb problem, which we will introduce now.
When we want to read page 3, instead of page 2, this high pass through voltage now needs to be applied on the 2nd page.
When we repeatedly read page 3, the pass through voltage induces a weak programming effect on the second page.

## Slide 140: Read Disturb Problem: “Weak Programming” Effect
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
0
1
0
0
High pass-through voltage induces “weak-programming” effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Incorrect values from page 2:
2.4V
2.6V
Page 1
Page 2
Page 3
Page 4
Notes: As the weak programming effect accumulates, the threshold voltage of each flash cell increases, and the threshold voltage state of a cell can be altered.
In this case, when we read page 2 again, we will read incorrect values from page 2, 0001
Flash vendors conservatively set this pass-through voltage to a high voltage.
However, we find in the paper that it is unnecessary to set to this high, and that reducing this voltage by just a bit will reduce read disturb errors significantly in the future.

## Slide 141: Executive Summary [DSN’15]
Read disturb errors limit flash memory lifetime today
  Apply a high pass-through voltage (Vpass) to multiple pages on a read
  Repeated application of Vpass can alter stored values in unread pages
We characterize read disturb on real NAND flash chips
  Slightly lowering Vpass greatly reduces read disturb errors
  Some flash cells are more prone to read disturb
Technique 1: Mitigate read disturb errors online
  Vpass Tuning dynamically finds and applies a lowered Vpass per block
  Flash memory lifetime improves by 21%
Technique 2: Recover after failure to prevent data loss
  Read Disturb Oriented Error Recovery (RDR) selectively corrects cells more susceptible to read disturb errors
  Reduces raw bit error rate (RBER) by up to 36%
Notes: When we read data from one page, we have to apply a high voltage to multiple other flash pages that are connected to this page, and we call this high pass-through voltage.
Over time this high pass-through voltage can alter the values stored in unread flash pages. We call this a read disturb error.
For the first time in open literature, we characterize read disturb on real NAND flash chips, and show that read disturb errors exist in today’s flash chips and is expected to increase in the future.
We make two key observations from the characterization.
Using our characterization, we develop two techniques that can help flash memory tolerate such read disturb errors.

## Slide 142: Read Disturb Prone vs. Resistant Cells
R
P
Disturb-Resistant
Disturb-Prone
Normalized Vth
PDF
N read disturbs
N read disturbs
R
P
Notes: RDR exploits each cell’s read disturb resistance.
Because of process variation, each cell can be classified as either disturb resistant or disturb prone.
After the same amount of read disturbs, the threshold voltage of a disturb-resistant cell does not change much, but the threshold voltage change of a disturb-prone cell is high.

## Slide 143: Observation 2: Some Flash Cells Are More Prone to Read Disturb
P1
ER
Normalized Vth
PDF
P
P
P
P
R
P
R
P
R
P
R
P
Disturb-prone cells have higher threshold voltages
Disturb-resistant cells have lower threshold voltages
After 250K read disturbs:
Disturb-prone ER state
Disturb-resistant P1 state
Notes: As our fourth observation, we find some flash cells are more prone to read disturb.
Now lets look at an example of the erased and P1 state.
With no read disturb, the threshold voltage of disturb prone and resistant cells are randomly distributed.
After a significant amount of read disturb, the cells redistribute because of read disturb.
At this point, we can see that disturb-prone cells have higher threshold voltages within each state,
And disturb-resistant cells have lower threshold voltages.
Now, if we look at the cells susceptible to errors, which are cells with threshold voltage closer to the boundary.
The disturb-prone cells are from the erased state, and the disturb-resistant cells are from the P1 state.

## Slide 144: Read Disturb Oriented Error Recovery (RDR)
Triggered by an uncorrectable flash error
  Back up all valid data in the faulty block
  Disturb the faulty page 100K times (more)
  Compare Vth’s before and after read disturb
  Select cells susceptible to flash errors (Vref−σ<Vth<Vref−σ)
  Predict among these susceptible cells
    Cells with more Vth shifts are disturb-prone  Higher Vth state
    Cells with less Vth shifts are disturb-resistant  Lower Vth state
Reduces total error count by up to 36% @ 1M read disturbs
ECC can be used to correct the remaining errors
Notes: Based on this finding, we propose read disturb oriented error recovery to identify disturb-prone and resistant cells after a failure has happened to recover from read disturb errors.
After an uncorrectable flash error, the following steps are triggered.

## Slide 145: More on Flash Read Disturb Errors [DSN’15]
Yu Cai, Yixin Luo, Saugata Ghose, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015.

## Slide 146: Large-Scale SSD Error Analysis [SIGMETRICS’15]
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 147: Another Lecture: NAND Flash Reliability
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" Proceedings of the IEEE, September 2017.
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.
Luo+, “HeatWatch: Improving 3D NAND Flash Memory Device Reliability by Exploiting Self-Recovery and Temperature-Awareness," HPCA 2018.
Luo+, “Improving 3D NAND Flash Memory Lifetime by Tolerating Early Retention Loss and Process Variation," SIGMETRICS 2018.
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 148: NAND Flash Vulnerabilities [HPCA’17]
https://people.inf.ethz.ch/omutlu/pub/flash-memory-programming-vulnerabilities_hpca17.pdf
HPCA, Feb. 2017

## Slide 149: NAND Flash Errors: A Modern Survey
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 150: Summary: Memory Reliability and Security
Memory reliability is reducing
Reliability issues open up security vulnerabilities
  Very hard to defend against
Rowhammer is an example
  Its implications on system security research are tremendous & exciting
Good news: We have a lot more to do.
Understand: Solid methodologies for failure modeling and discovery
  Modeling based on real device data – small scale and large scale
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled electronic design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 151: Other Works on Flash Memory

## Slide 152: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" , HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 153: Threshold Voltage Distribution
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)

## Slide 154: Program Interference and Vref Prediction
Yu Cai, Onur Mutlu, Erich F. Haratsch, and Ken Mai, "Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation" Proceedings of the 31st IEEE International Conference on Computer Design (ICCD), Asheville, NC, October 2013. Slides (pptx) (pdf) Lightning Session Slides (pdf)

## Slide 155: Neighbor-Assisted Error Correction
Yu Cai, Gulay Yalcin, Onur Mutlu, Eric Haratsch, Osman Unsal, Adrian Cristal, and Ken Mai, "Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. Slides (ppt) (pdf)

## Slide 156: Data Retention
Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 157: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 158: Flash Memory Programming Vulnerabilities
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, and Erich F. Haratsch, "Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA) Industrial Session, Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 159: Accurate and Online Channel Modeling
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory" to appear in IEEE Journal on Selected Areas in Communications (JSAC), 2016.

## Slide 160: 3D NAND Flash Reliability I [HPCA’18]
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "HeatWatch: Improving 3D NAND Flash Memory Device Reliability by Exploiting Self-Recovery and Temperature-Awareness" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 161: 3D NAND Flash Reliability II [SIGMETRICS’18]
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "Improving 3D NAND Flash Memory Lifetime by Tolerating Early Retention Loss and Process Variation" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Irvine, CA, USA, June 2018. [Abstract]

## Slide 162: Backup Slides

## Slide 163: More on DRAM Refresh

## Slide 164: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 165: Summary: Refresh-Access Parallelization
DRAM refresh interferes with memory accesses
  Degrades system performance and energy efficiency
  Becomes exacerbated as DRAM density increases
Goal: Serve memory accesses in parallel with refreshes to reduce refresh interference on demand requests
Our mechanisms:
  1. Enable more parallelization between refreshes and accesses across different banks with new per-bank refresh scheduling algorithms
  2. Enable serving accesses concurrently with refreshes in the same bank by exploiting parallelism across DRAM subarrays
Improve system performance and energy efficiency for a wide variety of different workloads and DRAM densities
  20.2% and 9.0% for 8-core systems using 32Gb DRAM at low cost
  Very close to the ideal scheme without refreshes
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.

## Slide 166: Refresh Penalty
Processor
Memory Controller
DRAM
Refresh
Read
Data
Capacitor
Access transistor
Refresh delays requests by 100s of ns
Refresh interferes with memory accesses

## Slide 167: Existing Refresh Modes
Time
Per-bank refresh in mobile DRAM (LPDDRx)
Time
All-bank refresh in commodity DRAM (DDRx)
Bank 7
Bank 1
Bank 0
…
Bank 7
Bank 1
Bank 0
…
Refresh
Round-robin order
…
Per-bank refresh allows accesses to other banks while a bank is refreshing

## Slide 168: Shortcomings of Per-Bank Refresh
Problem 1: Refreshes to different banks are scheduled in a strict round-robin order
  The static ordering is hardwired into DRAM chips
  Refreshes busy banks with many queued requests when other banks are idle
Key idea: Schedule per-bank refreshes to idle banks opportunistically in a dynamic order

## Slide 169: Our First Approach: DARP
Dynamic Access-Refresh Parallelization (DARP)
  An improved scheduling policy for per-bank refreshes
  Exploits refresh scheduling flexibility in DDR DRAM
Component 1: Out-of-order per-bank refresh
  Avoids poor static scheduling decisions
  Dynamically issues per-bank refreshes to idle banks
Component 2: Write-Refresh Parallelization
  Avoids refresh interference on latency-critical reads
  Parallelizes refreshes with a batch of writes

## Slide 170: Shortcomings of Per-Bank Refresh
Problem 2: Banks that are being refreshed cannot concurrently serve memory requests
Time
Bank 0
RD
Delayed by refresh
Per-Bank Refresh

## Slide 171: Shortcomings of Per-Bank Refresh
Problem 2: Refreshing banks cannot concurrently serve memory requests
Key idea: Exploit subarrays within a bank to parallelize refreshes and accesses across subarrays
Time
Bank 0
Subarray 1
Subarray 0
RD
Subarray Refresh
Time
Parallelize

## Slide 172: Methodology
100 workloads: SPEC CPU2006, STREAM, TPC-C/H, random access
System performance metric: Weighted speedup
DDR3 Rank
Simulator configurations
Memory Controller
8-core processor
Memory Controller
Bank 7
Bank 1
Bank 0
…
L1 $: 32KB
L2 $: 512KB/core

## Slide 173: Comparison Points
All-bank refresh [DDR3, LPDDR3, …]
Per-bank refresh [LPDDR3]
Elastic refresh [Stuecheli et al., MICRO ‘10]:
  Postpones refreshes by a time delay based on the predicted rank idle time to avoid interference on memory requests
  Proposed to schedule all-bank refreshes without exploiting per-bank refreshes
  Cannot parallelize refreshes and accesses within a rank
Ideal (no refresh)

## Slide 174: System Performance
Chart: DRAM Chip Density
All-Bank | 5.5359 | 5.3024 | 4.8311
Per-Bank | 5.7551 | 5.5256 | 5.0271
Elastic | 5.6343 | 5.3803 | 4.8911
DARP | 5.9537 | 5.8162 | 5.2317
SARP | 5.9777 | 5.9152 | 5.7295
DSARP | 5.9723 | 5.9543 | 5.8059
Ideal | 6.0252 | 6.0252 | 6.0252
7.9%
12.3%
20.2%
1. Both DARP & SARP provide performance gains and combining them (DSARP) improves even more
2. Consistent system performance improvement across DRAM densities (within 0.9%, 1.2%, and 3.8% of ideal)

## Slide 175: Energy Efficiency
3.0%
5.2%
9.0%
Consistent reduction on energy consumption
Chart: DRAM Chip Density
All-Bank | 38.2974 | 40.28 | 44.8967
Per-Bank | 38.0134 | 39.9893 | 44.5521
Elastic | 37.5049 | 39.3169 | 44.1509
DARP | 37.191 | 38.5881 | 43.25
SARP | 37.1096 | 38.322 | 41.0809
DSARP | 37.137 | 38.197 | 40.8495
Ideal | 36.6284 | 36.6284 | 36.6284

## Slide 176: More Information on Refresh-Access Parallelization
Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, and Onur Mutlu, "Improving DRAM Performance by Parallelizing Refreshes with Accesses" Proceedings of the 20th International Symposium on High-Performance Computer Architecture (HPCA), Orlando, FL, February 2014. [Summary] [Slides (pptx) (pdf)]

## Slide 177: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 178: Most Refreshes Are Unnecessary
Retention Time Profile of DRAM looks like this:

## Slide 179: RAIDR: Eliminating Unnecessary Refreshes
1. Profiling: Profile the retention time of all DRAM rows
2. Binning: Store rows into bins by retention time
 use Bloom Filters for efficient and scalable storage
3. Refreshing: Memory controller refreshes rows in different bins at different rates
 probe Bloom Filters to determine refresh rate of a row
1.25KB storage in controller for 32GB DRAM memory
Can reduce refreshes by ~75%
 reduces energy consumption and improves performance
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 180: RAIDR: Baseline Design
Refresh control is in DRAM in today’s auto-refresh systems
RAIDR can be implemented in either the controller or DRAM

## Slide 181: RAIDR in Memory Controller: Option 1
Overhead of RAIDR in DRAM controller:
1.25 KB Bloom Filters, 3 counters, additional commands issued for per-row refresh (all accounted for in evaluations)

## Slide 182: RAIDR in DRAM Chip: Option 2
Overhead of RAIDR in DRAM chip:
Per-chip overhead: 20B Bloom Filters, 1 counter (4 Gbit chip)
Total overhead: 1.25KB Bloom Filters, 64 counters (32 GB DRAM)

## Slide 183: RAIDR: Results and Takeaways
System: 32GB DRAM, 8-core; SPEC, TPC-C, TPC-H workloads
RAIDR hardware cost: 1.25 kB (2 Bloom filters)
Refresh reduction: 74.6%
Dynamic DRAM energy reduction: 16%
Idle DRAM power reduction: 20%
Performance improvement: 9%
Benefits increase as DRAM scales in density

## Slide 184: DRAM Device Capacity Scaling: Performance
RAIDR performance benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 185: DRAM Device Capacity Scaling: Energy
RAIDR energy benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 186: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 187: More on RAIDR
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 188: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 189: Motivation: Understanding Retention
Past works require accurate and reliable measurement of retention time of each DRAM row
  To maintain data integrity while reducing refreshes
Assumption: worst-case retention time of each row can be determined and stays the same at a given temperature
  Some works propose writing all 1’s and 0’s to a row, and measuring the time before data corruption
Question:
  Can we reliably and accurately determine retention times of all DRAM rows?

## Slide 190: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 191: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 192: VRT: Implications on Profiling Mechanisms
Problem 1: There does not seem to be a way of determining if a cell exhibits VRT without actually observing a cell exhibiting VRT
  VRT is a memoryless random process [Kim+ JJAP 2010]
Problem 2: VRT complicates retention time profiling by DRAM manufacturers
  Exposure to very high temperatures can induce VRT in cells that were not previously susceptible
   can happen during soldering of DRAM chips
   manufacturer’s retention time profile may not be accurate
One option for future work: Use ECC to continuously profile DRAM online while aggressively reducing refresh rate
  Need to keep ECC overhead in check

## Slide 193: More on DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 194: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 195: Towards an Online Profiling System
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
  But degrades performance
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Notes: Our high-level design for online profiling system is based to thee key observations:

## Slide 196: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 197: More on Online Profiling of DRAM
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 198: How Do We Make RAIDR Work in the Presence of the VRT Phenomenon?

## Slide 199: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 200: AVATAR
Insight: Avoid retention failures  Upgrade row on ECC error
Observation: Rate of VRT >> Rate of soft error (50x-2500x)
A
B
C
D
E
F
G
H
DRAM Rows
RETENTION
PROFILING
Weak Cell
0
0
1
0
0
0
1
0
Ref. Rate Table
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
1
AVATAR mitigates VRT by increasing refresh rate on error
Scrub
(15 min)
Row protected from future
retention failures

## Slide 201: RESULTS: REFRESH SAVINGS
AVATAR
No VRT
AVATAR reduces refresh by 60%-70%, similar to multi rate refresh but with VRT tolerance
Retention Testing Once a Year can revert refresh saving from 60% to 70%

## Slide 202: SPEEDUP
Speedup
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 1.04 | 1.065 | 1.13 | 1.35
NoRefresh | 1.05 | 1.09 | 1.21 | 1.54
AVATAR gets 2/3rd the performance of NoRefresh. More gains at higher capacity nodes

## Slide 203: ENERGY DELAY PRODUCT
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 0.95 | 0.88 | 0.75 | 0.52
NoRefresh | 0.91 | 0.83 | 0.68 | 0.41
Energy Delay Product
AVATAR reduces EDP,
Significant reduction at higher capacity nodes

## Slide 204: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 205: DRAM Refresh: Summary and Conclusions
DRAM refresh is a critical challenge
  in scaling DRAM technology efficiently to higher capacities
Discussed several promising solution directions
  Parallelize refreshes with accesses [Chang+ HPCA’14]
  Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Examined properties of retention time behavior [Liu+ ISCA’13]
  Enable realistic VRT-Aware refresh techniques [Qureshi+ DSN’15]
Many avenues for overcoming DRAM refresh challenges
  Handling DPD/VRT phenomena
  Enabling online retention time profiling and error mitigation
  Exploiting application behavior

## Slide 206: End of Backup Slides