## Slide 1: Memory Systems and Memory-Centric Computing Systems Topic 1: Memory Trends and Basics
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9-13 July 2018
HiPEAC ACACES Summer School 2018

## Slide 2: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich CS (EE), since September 2015
  Strecker Professor @ Carnegie Mellon University ECE (CS), 2009-2016, 2016-…
  PhD from UT-Austin, worked at Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research and Teaching in:
  Computer architecture, hardware security, bioinformatics, computing platforms
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  Architectures for bioinformatics, health, medicine
  …

## Slide 3: Current Research Focus Areas
Research Focus: Computer architecture, HW/SW, bioinformatics, security
Memory and storage (DRAM, flash, emerging), interconnects
Heterogeneous & parallel systems, GPUs, systems for data analytics
System/architecture interaction, new execution models, new interfaces
Hardware security, energy efficiency, fault tolerance, performance
Genome sequence analysis & assembly algorithms and architectures
Biologically inspired systems & system design for bio/medicine
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Broad research
spanning apps, systems, logic
with architecture at the center
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 4: Four Key Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 5: A Motivating Detour: Genome Sequence Analysis

## Slide 6: Our Dream
Can we build devices that can analyze a genome within a minute?

## Slide 7: What Is a Genome Made Of?
Cell
Nucleus
The discovery of DNA’s double-helical structure (Watson+, 1953)
Notes: Unlocking the life’s code requires diving into the nucleus of our body cells, where the double-stranded genome resides. Genome is literally the 'code of life' - it is the set of instructions for making everything from you to zebras, strawberries, and even yeast.
since the discovery of dna’s double-helical structure (watson et al. 1953)

## Slide 8: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 9: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in DNA.
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 10: Untangling Yarn Balls & DNA Sequencing
Notes: untangling yarn ball

## Slide 11
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 12: The Genomic Era
1990-2003: The Human Genome Project (HGP) provides a complete and accurate sequence of all DNA base pairs that make up the human genome and finds 20,000 to 25,000 human genes.
13 year-long
$3,000,000,000
Notes: The 13-year long human project is the starting of the genomic era! It opened the door to remarkable biomedical discoveries by providing the first complete human genome sequence. It cost 3 billion dollars to read the entire sequence.

## Slide 13: The Genomic Era (continued)
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 14
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 15
Example Question: If I give you a bunch of sequences, tell me where they are the same and where they are different.
Multiple sequence alignment

## Slide 16: Genome Sequence Alignment: Example
Source: By Aaron E. Darling, István Miklós, Mark A. Ragan - Figure 1 from Darling AE, Miklós I, Ragan MA (2008).
"Dynamics of Genome Rearrangement in Bacterial Populations". PLOS Genetics. DOI:10.1371/journal.pgen.1000128., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=30550950

## Slide 17: The Genetic Similarity Between Species
99.9%
96%
Human ~ Chimpanzee
Human ~ Human
90%
Human ~ Cat
80%
Human ~ Cow
50-60%
Human ~ Banana

## Slide 18
Metagenomics, genome assembly, de novo sequencing
http://math.oregonstate.edu/~koslickd
uncleaned de Bruijn graph
Question 2: Given a bunch of short sequences, Can you identify the approximate species cluster for genomically unknown organisms (bacteria)?
Notes: organism detection in metagenomes

## Slide 19
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
Bottlenecked in Mapping!!
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 20: The Read Mapping Bottleneck
ACGTACGTACGTACGT
TATATATACGTACTAGTACGT
ACGACTTTAGTACGTACGT
TATATATACGTACTAGTACGT
ACGTACGCCCCTACGTA
ACGACTTTAGTACGTACGT
TATATATACGTACTAAAGTACGT
CCCCCCTATATATACGTACTAGTACGT
TATATATACGTACTAGTACGT
TATATATACGTACTAGTACGT
ACGTTTTTAAAACGTA
ACGACGGGGAGTACGTACGT
TATATATACGTACTAAAGTACGT
150X slower
Illumina HiSeq4000
Million
bases/minute
300
Million
bases/minute
2

## Slide 21: Read Mapping
Map many short DNA fragments (reads) to a known reference genome with some minor differences allowed
Reference genome
Reads
DNA, logically
DNA, physically
Mapping short reads to reference genome is challenging (billions of 50-300 base pair reads)
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 22: Challenges in Read Mapping
Need to find many mappings of each read
  A short read may map to many locations, especially with High-Throughput DNA Sequencing technologies
  How can we find all mappings efficiently?
Need to tolerate small variances/errors in each read
  Each individual is different: Subject’s DNA may slightly differ from the reference (Mismatches, insertions, deletions)
  How can we efficiently map each read with up to e errors present?
Need to map each read very fast (i.e., performance is important)
  Human DNA is 3.2 billion base pairs long  Millions to billions of reads (State-of-the-art mappers take weeks to map a human’s DNA)
  How can we design a much higher performance read mapper?
Notes: There are three main challenges.
First. The mapper needs to find many mappings for each read. Because the read is so short, they can map to multiple locations in the reference genome. How can we efficiently find all mappings of a read?
Second. The mapper needs to tolerate small variance or errors in each read. Since individuals are different, the subject’s DNA might slightly differs from the reference DNA, which can be mismatches, insertions or deletions of base pairs. How can we efficiently map each read with up to a number of e errors present?
Third. The mapper needs to map each read very fast. In another word, performance is important. Because the human DNA is 3.2 billion base-pairs long and each read is only hundreds of base-pairs long, there can be billions of reads subjected to mapping for an individual human. Current state of the art mappers take weeks to map a human’s DNA. So the question is, how can we design a much higher performance read mapper?

## Slide 23: Our First Step: Comprehensive Mapping
+ Guaranteed to find all mappings  sensitive
+ Can tolerate up to e errors
http://mrfast.sourceforge.net/
Alkan+, "Personalized copy number and segmental duplication
maps using next-generation sequencing”, Nature Genetics 2009.
Notes: It turned out the Hash Table based mappers solve the first 2 challenges pretty well. They guarantee to find all mappings with no more than e errors present.

## Slide 24: Read Mapping Execution Time Breakdown
Chart: 
| candidate alignment locations (CAL) | SIMD banded Levenshtein edit distance | SAM printing
Time (sec) | 3738.88 | 81368.0945 | 2269.8755
Notes: An overwhelming majority of the read mapper’s execution time is spent in read alignment.

## Slide 25: Read Alignment/Verification
Edit distance is defined as the minimum number of edits (i.e. insertions, deletions, or substitutions) needed to make the read exactly match the reference segment.
o | - | - | r | g | a | n | i | z | a | t | i | o | n
o | p | e | r | - | - | - | - | - | a | t | i | o | n
o | - | - | r | g | a | n | i | z | a | t | i | o | n
o | p | e | r | - | a | - | - | - | - | t | i | o | n
o | r | g | a | n | i | z | a | t | i | o | n
t | r | - | a | n | s | l | a | t | i | o | n
o | r | g | a | n | - | i | z | a | t | i | o | n
t | r | - | a | n | s | l | - | a | t | i | o | n
o | r | g | a | n | i | z | - | a | t | i | o | n
t | r | - | a | n | - | s | l | a | t | i | o | n
Ref
Read
Ref
Read
Ref
Read
Ref
Read
Ref
Read
organization x operation
organization x translation
match
deletion
insertion
mismatch
Notes: http://www.let.rug.nl/kleiweg/lev/

## Slide 26: Idea
Filter fast before you align
Minimize costly
“approximate string comparisons”

## Slide 27: Our First Filter: Pure Software Approach
Download source code and try for yourself
  Download link to FastHASH

## Slide 28: Next Step: SIMD Acceleration (New Algorithm)
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.

## Slide 29
Our FPGA-based Filter: GateKeeper
Alignment Filter
st
1
FPGA-based Alignment Filter.
Notes: To bridge the widening gap between the sequencer & the mapper, we propose the concept of pre-alignment filtering. We added a new examination step before the accurate alignment step. The main objective of this step is to detect the incorrect mappings accurately and rapidly. Only the mappings that pass our filter are examined by the alignment step. We also explore exploiting todays’ hardware accelerators to further boost the filtering speed of such filters.

## Slide 30: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 31: DNA Read Mapping & Filtering
Problem: Heavily bottlenecked by Data Movement
GateKeeper FPGA performance limited by DRAM bandwidth [Alser+, Bioinformatics 2017]
Ditto for SHD on SIMD [Xin+, Bioinformatics 2015]
Solution: Processing-in-memory can alleviate the bottleneck
However, we need to design mapping & filtering algorithms to fit processing-in-memory

## Slide 32: In-Memory DNA Sequence Analysis
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. arxiv.org Version (pdf)

## Slide 33: Key Principles and Results
Alser et al., “GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA
Short Read Mapping,” Bioinformatics 2017.
Kim et al., “Genome Read In-Memory (GRIM) Filter,” BMC Genomics 2018.
Two key principles:
  Exploit the structure of the genome to minimize computation
  Morph and exploit the structure of the underlying hardware to maximize performance and efficiency
Algorithm-architecture co-design for DNA read mapping
  Speeds up read mapping by ~200X (sometimes more)
  Improves accuracy of read mapping in the presence of errors
Xin et al., “Accelerating Read Mapping with FastHASH,” BMC Genomics 2013.
Xin et al., “Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter to Accelerate
Alignment Verification in Read Mapping,” Bioinformatics 2015.

## Slide 34: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics (BIB), 2018.
[Open arxiv.org version]
Oxford Nanopore MinION

## Slide 35: Nanopore Genome Assembly Pipeline
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly”, Briefings in Bioinformatics, 2018. [Open arxiv.org version]

## Slide 36: More on Genome Analysis: Another Talk

## Slide 37: Recall Our Dream
Can we build devices that can analyze a genome within a minute?
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security
  Huge memory bottleneck

## Slide 38: Four Key Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 39: Memory & Storage

## Slide 40: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)

## Slide 41: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs

## Slide 42: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs

## Slide 43: Memory System: A Shared Resource View
Storage
Most of the system is dedicated to storing and moving data

## Slide 44: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 45: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 46: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 47: Consequence: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years
Lim et al., ISCA 2009

## Slide 48: Example: Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 49: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 50: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 51: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer’03] >40% power in DRAM [Ware, HPCA’10][Paul,ISCA’15]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 52: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 53: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 54: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 55: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RLDRAM, TL-DRAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 56: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RL/TL-DRAM, FLY-RAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4, Voltron) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 57: Major Trend: Hybrid Main Memory
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 58: One Foreshadowing
Main Memory Needs
Intelligent Controllers

## Slide 59: Industry Is Writing Papers About It, Too

## Slide 60: Call for Intelligent Memory Controllers

## Slide 61: Agenda
Brief Introduction
A Motivating Example
Memory System Trends
What Will You Learn In This Course
  And, how to make the best of it…
Memory Fundamentals
Key Memory Challenges and Solution Directions
  Security, Reliability, Safety
  Energy and Performance: Data-Centric Systems
  Latency and Latency-Reliability Tradeoffs
Summary and Future Lookout

## Slide 62: Course Logistics

## Slide 63: What Will You Learn in This Course?
Memory Systems and Memory-Centric Computing Systems
  July 9-13, 2018
Topic 1: Main Memory Trends and Basics
Topic 2: Memory Reliability & Security: RowHammer and Beyond
Topic 3: In-memory Computation
Topic 4: Low-Latency and Low-Energy Memory
Topic 5 (unlikely): Enabling and Exploiting Non-Volatile Memory
Topic 6 (unlikely): Flash Memory and SSD Scaling
Major Overview Reading:
  Mutlu and Subramaniam, “Research Problems and Opportunities in Memory Systems,” SUPERFRI 2014.

## Slide 64: This Course
Will cover many problems and potential solutions related to the design of memory systems in the many core era
The design of the memory system poses many
  Difficult research and engineering problems
  Important fundamental problems
  Industry-relevant problems
  Problems whose solutions can revolutionize the world
Many creative and insightful solutions are needed to solve these problems
Goal: Acquire the basics to develop such solutions (by covering fundamentals and cutting edge research)

## Slide 65: Course Information
My Contact Information
  Onur Mutlu
  omutlu@gmail.com
  https://people.inf.ethz.ch/omutlu
  +41-79-572-1444 (my cell phone)
  Find me during breaks and/or email any time.
Website for Course Slides and Papers
  https://people.inf.ethz.ch/omutlu
  Click on ACACES 2018 course website

## Slide 66: How To Make the Best Out of This Course
Be alert during lectures – they will be fast paced
Do the readings (and explore even more)
  I will provide many references
Go back and reinforce fundamentals (as needed)
  I will provide pointers to basic computer architecture materials (lecture videos, slides, readings, exams, …)
Remember “Chance favors the prepared mind.” (Pasteur)

## Slide 67: Readings, Videos, Reference Materials

## Slide 68: Reference Overview Paper I
https://arxiv.org/pdf/1802.00320.pdf

## Slide 69: Reference Overview Paper II
Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2014/2015.
https://people.inf.ethz.ch/omutlu/pub/memory-systems-research_superfri14.pdf

## Slide 70: Reference Overview Paper III
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 71: Reference Overview Paper IV
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Technical talk at MemCon 2013 (MEMCON), Santa Clara, CA, August 2013. [Slides (pptx) (pdf)] [Video] [Coverage on StorageSearch]
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 72: Reference Overview Paper V
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 73: Related Videos and Course Materials (I)
Undergraduate Computer Architecture Course Lecture Videos (2015, 2014, 2013)
Undergraduate Computer Architecture Course Materials (2015, 2014, 2013)
Graduate Computer Architecture Course Lecture Videos (2017, 2015, 2013)
Graduate Computer Architecture Course Materials (2017, 2015, 2013)
Parallel Computer Architecture Course Materials (Lecture Videos)

## Slide 74: Related Videos and Course Materials (II)
Freshman Digital Circuits and Computer Architecture Course Lecture Videos (2018, 2017)
Freshman Digital Circuits and Computer Architecture Course Materials (2018)
Memory Systems Short Course Materials
(Lecture Video on Main Memory and DRAM Basics)

## Slide 75: Some Open Source Tools (I)
Rowhammer – Program to Induce RowHammer Errors
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim – Simple Memory Simulator
  https://github.com/CMU-SAFARI/memsim
NOCulator – Flexible Network-on-Chip Simulator
  https://github.com/CMU-SAFARI/NOCulator
SoftMC – FPGA-Based DRAM Testing Infrastructure
  https://github.com/CMU-SAFARI/SoftMC
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 76: Some Open Source Tools (II)
MQSim – A Fast Modern SSD Simulator
  https://github.com/CMU-SAFARI/MQSim
Mosaic – GPU Simulator Supporting Concurrent Applications
  https://github.com/CMU-SAFARI/Mosaic
IMPICA – Processing in 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/IMPICA
SMLA – Detailed 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/SMLA
HWASim – Simulator for Heterogeneous CPU-HWA Systems
  https://github.com/CMU-SAFARI/HWASim
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 77: More Open Source Tools (III)
A lot more open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 78: Referenced Papers
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en

## Slide 79: Memory Fundamentals

## Slide 80: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 81: Ideal Memory
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)

## Slide 82: The Problem
Ideal memory’s requirements oppose each other
Bigger is slower
  Bigger  Takes longer to determine the location
Faster is more expensive
  Memory technology: SRAM vs. DRAM vs. Disk vs. Tape
Higher bandwidth is more expensive
  Need more banks, more ports, higher frequency, or faster technology

## Slide 83: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
  Read Liu et al., “RAIDR: Retention-aware Intelligent DRAM Refresh,” ISCA 2012.
row enable
_bitline

## Slide 84: Memory Technology: SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to persist in the “cell”
  4 transistors for storage
  2 transistors for access
row select
bitline
_bitline

## Slide 85: An Aside: Phase Change Memory
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 86: Reading: PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 87: Reading: More on PCM As Main Memory
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 88: Memory Bank: A Fundamental Concept
Interleaving (banking)
  Problem: a single monolithic memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide the array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  An issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 89: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 90: Why Memory Hierarchy?
We want both fast and large
But we cannot achieve both with a single level of memory
Idea: Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and ensure most of the data the processor needs is kept in the fast(er) level(s)

## Slide 91: Memory Hierarchy
Fundamental tradeoff
  Fast memory: small
  Large memory: slow
Idea: Memory hierarchy
Latency, cost, size,
bandwidth
CPU
Main
Memory
(DRAM)
RF
Cache
Hard Disk

## Slide 92: Caching Basics: Exploit Temporal Locality
Idea: Store recently accessed data in automatically managed fast memory (called cache)
Anticipation: the data will be accessed again soon
Temporal locality principle
  Recently accessed data will be again accessed in the near future
  This is what Maurice Wilkes had in mind:
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
    “The use is discussed of a fast core memory of, say 32000 words as a slave to a slower core memory of, say, one million words in such a way that in practical cases the effective access time is nearer that of the fast memory than that of the slow memory.”

## Slide 93: Caching Basics: Exploit Spatial Locality
Idea: Store addresses adjacent to the recently accessed one in automatically managed fast memory
  Logically divide memory into equal size blocks
  Fetch to cache the accessed block in its entirety
Anticipation: nearby data will be accessed soon
Spatial locality principle
  Nearby data in memory will be accessed in the near future
    E.g., sequential instruction access, array traversal
  This is what IBM 360/85 implemented
    16 Kbyte cache with 64 byte blocks
    Liptay, “Structural aspects of the System/360 Model 85 II: the cache,” IBM Systems Journal, 1968.

## Slide 94: A Note on Manual vs. Automatic Management
Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs
  “core” vs “drum” memory in the 50’s
  still done in some embedded processors (on-chip scratch pad SRAM in lieu of a cache)
Automatic: Hardware manages data movement across levels, transparently to the programmer
  ++ programmer’s life is easier
  simple heuristic: keep most recently used items in cache
  the average programmer doesn’t need to know about it
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 95: Automatic Management in Memory Hierarchy
Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
“By a slave memory I mean one which automatically accumulates to itself words that come from a slower main memory, and keeps them available for subsequent use without it being necessary for the penalty of main memory access to be incurred again.”

## Slide 96: A Modern Memory Hierarchy
Register File
32 words, sub-nsec
L1 cache
~32 KB, ~nsec
L2 cache
512 KB ~ 1MB, many nsec
L3 cache,
.....
Main memory (DRAM),
GB, ~100 nsec
Swap Disk
100 GB, ~10 msec
manual/compiler
register spilling
automatic
demand
paging
Automatic
HW cache
management
Memory
Abstraction

## Slide 97: The DRAM Subsystem

## Slide 98: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 99: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 100: The DRAM Bank Structure

## Slide 101: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 102: The DRAM Chip
Consists of multiple banks (8 is a common number today)
Banks share command/address/data buses
The chip itself has a narrow interface (4-16 bits per read)
Changing the number of banks, size of the interface (pins), whether or not command/address/data buses are shared has significant impact on DRAM system cost

## Slide 103: 128M x 8-bit DRAM Chip

## Slide 104: DRAM Rank and Module
Rank: Multiple chips operated together to form a wide interface
All chips comprising a rank are controlled at the same time
  Respond to a single command
  Share address and command buses, but provide different data
A DRAM module consists of one or more ranks
  E.g., DIMM (dual inline memory module)
  This is what you plug into your motherboard
If we have chips with 8-bit interface, to read 8 bytes in a single access, use 8 chips in a DIMM

## Slide 105: A 64-bit Wide DIMM (One Rank)

## Slide 106: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 107: Multiple DIMMs
Advantages:
  Enables even higher capacity
Disadvantages:
  Interconnect complexity and energy consumption can be high
   Scalability is limited by this

## Slide 108: DRAM Channels
2 Independent Channels: 2 Memory Controllers (Above)
2 Dependent/Lockstep Channels: 1 Memory Controller with wide interface (Not shown above)

## Slide 109: Generalized Memory Structure

## Slide 110: Generalized Memory Structure
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.

## Slide 111: The DRAM Subsystem The Top Down View

## Slide 112: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 113: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 114: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 115: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 116: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 117: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 118: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 119: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 120: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 121: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 122: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 123: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 124: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 125: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 126: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 127: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 128: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple CAS (column address strobe) if row is “open” OR
  RAS (row address strobe) + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → Controller transfer time
  Bus latency (BL)
Controller to CPU transfer time

## Slide 129: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 130: How Multiple Banks Help

## Slide 131: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
  Accesses to consecutive cache blocks serviced in a pipelined manner
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 132: Bank Mapping Randomization
DRAM controller can randomize the address mapping to banks so that bank conflicts are less likely
Reading:
  Rau, “Pseudo-randomly Interleaved Memory,” ISCA 1991.
Column (11 bits)
3 bits
Byte in bus (3 bits)
XOR
Bank index (3 bits)

## Slide 133: Address Mapping (Multiple Channels)
Where are consecutive cache blocks?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C

## Slide 134: Interaction with VirtualPhysical Mapping
Operating System influences where an address maps to in DRAM
Operating system can influence which bank/channel/rank a virtual page is mapped to.
It can perform page coloring to
  Minimize bank conflicts
  Minimize inter-application interference [Muralidhara+ MICRO’11]
  Minimize latency in the network [Das+ HPCA’13]
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Page offset (12 bits)
Physical Frame number (19 bits)
Page offset (12 bits)
Virtual Page number (52 bits)
VA
PA
PA

## Slide 135: More on Reducing Bank Conflicts
Read Sections 1 through 4 of:
  Kim et al., “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.

## Slide 136: Subarray Level Parallelism Paper
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, and Onur Mutlu, "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 137: DRAM Refresh (I)
DRAM capacitor charge leaks over time
The memory controller needs to read each row periodically to restore the charge
  Activate + precharge each row every N ms
  Typical N = 64 ms
Implications on performance?
  -- DRAM bank unavailable while refreshed
  -- Long pause times: If we refresh all rows in burst, every 64ms the DRAM will be unavailable until refresh ends
Burst refresh: All rows refreshed immediately after one another
Distributed refresh: Each row refreshed at a different time, at regular intervals

## Slide 138: DRAM Refresh (II)
Distributed refresh eliminates long pause times
How else we can reduce the effect of refresh on performance?
  Can we reduce the number of refreshes?

## Slide 139: Downsides of DRAM Refresh
-- Energy consumption: Each refresh consumes energy
-- Performance degradation: DRAM rank/bank unavailable while refreshed
-- QoS/predictability impact: (Long) pause times during refresh
-- Refresh rate limits DRAM density scaling
  Liu et al., “RAIDR: Retention-aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 140: More on DRAM Refresh (I)
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 141: DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 142: Data Retention in Memory [Liu et al., ISCA 2013]
Data Retention Time Profile of DRAM looks like this:
Location dependent
Stored value pattern dependent
Time dependent

## Slide 143: DRAM Refresh-Access Parallelization
Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, and Onur Mutlu, "Improving DRAM Performance by Parallelizing Refreshes with Accesses" Proceedings of the 20th International Symposium on High-Performance Computer Architecture (HPCA), Orlando, FL, February 2014. [Summary] [Slides (pptx) (pdf)]

## Slide 144: Inside A DRAM Chip

## Slide 145: DRAM Module and Chip

## Slide 146: Goals
Cost
Latency
Bandwidth
Parallelism
Power
Energy
Reliability
…

## Slide 147: DRAM Chip
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O

## Slide 148: Sense Amplifier
enable
top
bottom
Inverter

## Slide 149: Sense Amplifier – Two Stable States
1
1
0
0
VDD
VDD
Logical “1”
Logical “0”

## Slide 150: Sense Amplifier Operation
0
VT
VB
VT > VB
1
0
VDD

## Slide 151: DRAM Cell – Capacitor
Empty State
Fully Charged State
Logical “0”
Logical “1”
1
2
Small – Cannot drive circuits
Reading destroys the state

## Slide 152: Capacitor to Sense Amplifier
1
0
VDD
1
VDD
0

## Slide 153: DRAM Cell Operation
½VDD
½VDD
0
1
0
VDD
½VDD+δ

## Slide 154: DRAM Subarray – Building Block for DRAM Chip
Row Decoder
Cell Array
Cell Array
Array of Sense Amplifiers (Row Buffer) 8Kb

## Slide 155: DRAM Bank
Row Decoder
Array of Sense Amplifiers (8Kb)
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O (64b)
Address
Address
Data

## Slide 156: DRAM Chip
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Shared internal bus
Memory channel - 8bits

## Slide 157: DRAM Operation
Row Decoder
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Data
1
2
ACTIVATE Row
READ/WRITE Column
3
PRECHARGE
Row Address
Column Address

## Slide 158: Simulating Memory

## Slide 159: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 160: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 161: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 162: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 163: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 164: Optional Assignment
Review the Ramulator paper
  Email me your review (omutlu@gmail.com)
Download and run Ramulator
  Compare DDR3, DDR4, SALP, HBM for the libquantum benchmark (provided in Ramulator repository)
  Email me your report (omutlu@gmail.com)
This may help you get into memory systems research quickly

## Slide 165: Memory Controllers

## Slide 166: DRAM versus Other Types of Memories
Long latency memories have similar characteristics that need to be controlled.
The following discussion will use DRAM as an example, but many scheduling and control issues are similar in the design of controllers for other types of memories
  Flash memory
  Other emerging memory technologies
    Phase Change Memory
    Spin-Transfer Torque Magnetic Memory
  These other technologies can place other demands on the controller

## Slide 167: Flash Memory (SSD) Controllers
Similar to DRAM memory controllers, except:
  They are flash memory specific
  They do much more: error correction, garbage collection, page remapping, …
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime”, ICCD 2012.

## Slide 168: Another View of the SSD Controller
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.
https://arxiv.org/pdf/1711.11427.pdf

## Slide 169: DRAM Types
DRAM has different types with different interfaces optimized for different purposes
  Commodity: DDR, DDR2, DDR3, DDR4, …
  Low power (for mobile): LPDDR1, …, LPDDR5, …
  High bandwidth (for graphics): GDDR2, …, GDDR5, …
  Low latency: eDRAM, RLDRAM, …
  3D stacked: WIO, HBM, HMC, …
  …
Underlying microarchitecture is fundamentally the same
A flexible memory controller can support various DRAM types
This complicates the memory controller
  Difficult to support all types (and upgrades)

## Slide 170: DRAM Types (circa 2015)
Kim et al., “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE Comp Arch Letters 2015.

## Slide 171: DRAM Controller: Functions
Ensure correct operation of DRAM (refresh and timing)
Service DRAM requests while obeying timing constraints of DRAM chips
  Constraints: resource conflicts (bank, bus, channel), minimum write-to-read delays
  Translate requests to DRAM command sequences
Buffer and schedule requests to for high performance + QoS
  Reordering, row-buffer, bank, rank, bus management
Manage power consumption and thermals in DRAM
  Turn on/off DRAM chips, manage power modes

## Slide 172: A Modern DRAM Controller (I)

## Slide 173: A Modern DRAM Controller

## Slide 174: DRAM Scheduling Policies (I)
FCFS (first come first served)
  Oldest request first
FR-FCFS (first ready, first come first served)
  1. Row-hit first
  2. Oldest first
  Goal: Maximize row buffer hit rate  maximize DRAM throughput
  Actually, scheduling is done at the command level
    Column commands (read/write) prioritized over row commands (activate/precharge)
    Within each group, older commands prioritized over younger ones

## Slide 175: Review: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 176: DRAM Scheduling Policies (II)
A scheduling policy is a request prioritization order
Prioritization can be based on
  Request age
  Row buffer hit/miss status
  Request type (prefetch, read, write)
  Requestor type (load miss or store miss)
  Request criticality
    Oldest miss in the core?
    How many instructions in core are dependent on it?
    Will it stall the processor?
  Interference caused to other cores
  …

## Slide 177: Row Buffer Management Policies
Open row
  Keep the row open after an access
  + Next access might need the same row  row hit
  -- Next access might need a different row  row conflict, wasted energy
Closed row
  Close the row after an access (if no other requests already in the request buffer need the same row)
  + Next access might need a different row  avoid a row conflict
  -- Next access might need the same row  extra activate latency
Adaptive policies
  Predict whether or not the next access to the bank will be to the same row

## Slide 178: Open vs. Closed Row Policies
Policy | First access | Next access | Commands needed for next access
Open row | Row 0 | Row 0 (row hit) | Read
Open row | Row 0 | Row 1 (row conflict) | Precharge + Activate Row 1 + Read
Closed row | Row 0 | Row 0 – access in request buffer (row hit) | Read
Closed row | Row 0 | Row 0 – access not in request buffer (row closed) | Activate Row 0 + Read + Precharge
Closed row | Row 0 | Row 1 (row closed) | Activate Row 1 + Read + Precharge

## Slide 179: DRAM Power Management
DRAM chips have power modes
Idea: When not accessing a chip power it down
Power states
  Active (highest power)
  All banks idle
  Power-down
  Self-refresh (lowest power)
Tradeoff: State transitions incur latency during which the chip cannot be accessed

## Slide 180: Difficulty of DRAM Control

## Slide 181: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to manage power consumption
Need to optimize performance & QoS (in the presence of constraints)
  Reordering is not simple
  Fairness and QoS needs complicates the scheduling problem

## Slide 182: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 183: More on DRAM Operation
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 184: Why So Many Timing Constraints? (I)
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.

## Slide 185: Why So Many Timing Constraints? (II)
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 186: DRAM Controller Design Is Becoming More Difficult
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 187: Reality and Dream
Reality: It difficult to optimize all these different constraints while maximizing performance, QoS, energy-efficiency, …
Dream: Wouldn’t it be nice if the DRAM controller automatically found a good scheduling policy on its own?

## Slide 188: Self-Optimizing DRAM Controllers
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.

## Slide 189: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.
Goal: Learn to choose actions to maximize r0 + r1 + 2r2 + … ( 0   < 1)

## Slide 190: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 191: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 192: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize long-term data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 193: Performance Results

## Slide 194: Self Optimizing DRAM Controllers
Advantages
  + Adapts the scheduling policy dynamically to changing workload behavior and to maximize a long-term target
  + Reduces the designer’s burden in finding a good scheduling policy. Designer specifies:
  1) What system variables might be useful
  2) What target to optimize, but not how to optimize it
Disadvantages and Limitations
  -- Black box: designer much less likely to implement what she cannot easily reason about
  -- How to specify different reward functions that can achieve different objectives? (e.g., fairness, QoS)
  -- Hardware complexity?

## Slide 195: More on Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 196: Some More Suggested Readings

## Slide 197: Some Key Readings on DRAM (I)
DRAM Organization and Operation
  Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
  https://people.inf.ethz.ch/omutlu/pub/tldram_hpca13.pdf
  Kim et al., “A Case for Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
  https://people.inf.ethz.ch/omutlu/pub/salp-dram_isca12.pdf
  Lee et al., “Simultaneous Multi-Layer Access: Improving 3D-Stacked Memory Bandwidth at Low Cost,” ACM TACO 2016.
  https://people.inf.ethz.ch/omutlu/pub/smla_high-bandwidth-3d-stacked-memory_taco16.pdf

## Slide 198: Some Key Readings on DRAM (II)
DRAM Refresh
  Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012. https://people.inf.ethz.ch/omutlu/pub/raidr-dram-refresh_isca12.pdf
  Chang et al., “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
  https://people.inf.ethz.ch/omutlu/pub/dram-access-refresh-parallelization_hpca14.pdf
  Patel et al., “The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions,” ISCA 2017.
    https://people.inf.ethz.ch/omutlu/pub/reaper-dram-retention-profiling-lpddr4_isca17.pdf

## Slide 199: Reading on Simulating Main Memory
How to evaluate future main memory systems?
An open-source simulator and its brief description
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]

## Slide 200: Some Key Readings on Memory Control 1
  Mutlu+, “Parallelism-Aware Batch Scheduling: Enhancing both Performance and Fairness of Shared DRAM Systems,” ISCA 2008.
    https://people.inf.ethz.ch/omutlu/pub/parbs_isca08.pdf
  Kim et al., “Thread Cluster Memory Scheduling: Exploiting Differences in Memory Access Behavior,” MICRO 2010.
    https://people.inf.ethz.ch/omutlu/pub/tcm_micro10.pdf
  Subramanian et al., “BLISS: Balancing Performance, Fairness and Complexity in Memory Access Scheduling,” TPDS 2016.
    https://people.inf.ethz.ch/omutlu/pub/bliss-memory-scheduler_ieee-tpds16.pdf
  Usui et al., “DASH: Deadline-Aware High-Performance Memory Scheduler for Heterogeneous Systems with Hardware Accelerators,” TACO 2016.
    https://people.inf.ethz.ch/omutlu/pub/dash_deadline-aware-heterogeneous-memory-scheduler_taco16.pdf

## Slide 201: Some Key Readings on Memory Control 2
  Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.
    https://people.inf.ethz.ch/omutlu/pub/rlmc_isca08.pdf
  Ebrahimi et al., “Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems,” ASPLOS 2010.
    https://people.inf.ethz.ch/omutlu/pub/fst_asplos10.pdf
  Subramanian et al., “The Application Slowdown Model: Quantifying and Controlling the Impact of Inter-Application Interference at Shared Caches and Main Memory,” MICRO 2015.
    https://people.inf.ethz.ch/omutlu/pub/application-slowdown-model_micro15.pdf
  Lee et al., “Decoupled Direct Memory Access: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM,” PACT 2015.
    https://people.inf.ethz.ch/omutlu/pub/decoupled-dma_pact15.pdf

## Slide 202: More Readings
To be provided
Search for “DRAM” or “Memory” in:
  https://people.inf.ethz.ch/omutlu/projects.htm

## Slide 203: Memory Systems and Memory-Centric Computing Systems Topic 1: Memory Trends and Basics
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9-13 July 2018
HiPEAC ACACES Summer School 2018

## Slide 204: Backup Slides

## Slide 205: Evaluating New Ideas for New (Memory) Architectures

## Slide 206: Potential Evaluation Methods
How do we assess an idea will improve a target metric X?
A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling/estimation
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 207: The Difficulty in Architectural Evaluation
The answer is usually workload dependent
  E.g., think caching
  E.g., think pipelining
  E.g., think any idea we talked about (RAIDR, Mem. Sched., …)
Workloads change
System has many design choices and parameters
  Architect needs to decide many ideas and many parameters for a design
  Not easy to evaluate all possible combinations!
System parameters may change

## Slide 208: Simulation: The Field of Dreams

## Slide 209: Dreaming and Reality
An architect is in part a dreamer, a creator
Simulation is a key tool of the architect
Simulation enables
  The exploration of many dreams
  A reality check of the dreams
  Deciding which dream is better
Simulation also enables
  The ability to fool yourself with false dreams

## Slide 210: Why High-Level Simulation?
Problem: RTL simulation is intractable for design space exploration  too time consuming to design and evaluate
  Especially over a large number of workloads
  Especially if you want to predict the performance of a good chunk of a workload on a particular design
  Especially if you want to consider many design choices
    Cache size, associativity, block size, algorithms
    Memory control and scheduling algorithms
    In-order vs. out-of-order execution
    Reservation station sizes, ld/st queue size, register file size, …
    …
Goal: Explore design choices quickly to see their impact on the workloads we are designing the platform for

## Slide 211: Different Goals in Simulation
Explore the design space quickly and see what you want to
  potentially implement in a next-generation platform
  propose as the next big idea to advance the state of the art
  the goal is mainly to see relative effects of design decisions
Match the behavior of an existing system so that you can
  debug and verify it at cycle-level accuracy
  propose small tweaks to the design that can make a difference in performance or energy
  the goal is very high accuracy
Other goals in-between:
  Refine the explored design space without going into a full detailed, cycle-accurate design
  Gain confidence in your design decisions made by higher-level design space exploration

## Slide 212: Tradeoffs in Simulation
Three metrics to evaluate a simulator
  Speed
  Flexibility
  Accuracy
Speed: How fast the simulator runs (xIPS, xCPS, slowdown)
Flexibility: How quickly one can modify the simulator to evaluate different algorithms and design choices?
Accuracy: How accurate the performance (energy) numbers the simulator generates are vs. a real design (Simulation error)
The relative importance of these metrics varies depending on where you are in the design process (what your goal is)

## Slide 213: Trading Off Speed, Flexibility, Accuracy
Speed & flexibility affect:
  How quickly you can make design tradeoffs
Accuracy affects:
  How good your design tradeoffs may end up being
  How fast you can build your simulator (simulator design time)
Flexibility also affects:
  How much human effort you need to spend modifying the simulator
You can trade off between the three to achieve design exploration and decision goals

## Slide 214: High-Level Simulation
  Key Idea: Raise the abstraction level of modeling to give up some accuracy to enable speed & flexibility (and quick simulator design)
Advantage
  + Can still make the right tradeoffs, and can do it quickly
  + All you need is modeling the key high-level factors, you can omit corner case conditions
  + All you need is to get the “relative trends” accurately, not exact performance numbers
Disadvantage
  -- Opens up the possibility of potentially wrong decisions
  -- How do you ensure you get the “relative trends” accurately?

## Slide 215: Simulation as Progressive Refinement
High-level models (Abstract, C)
…
Medium-level models (Less abstract)
…
Low-level models (RTL with everything modeled)
…
Real design
As you refine (go down the above list)
  Abstraction level reduces
  Accuracy (hopefully) increases (not necessarily, if not careful)
  Flexibility reduces; Speed likely reduces except for real design
  You can loop back and fix higher-level models

## Slide 216: Making The Best of Architecture
A good architect is comfortable at all levels of refinement
  Including the extremes
A good architect knows when to use what type of simulation
  And, more generally, what type of evaluation method
Recall: A variety of evaluation methods are available:
  Theoretical proof
  Analytical modeling
  Simulation (at varying degrees of abstraction and accuracy)
  Prototyping with a real system (e.g., FPGAs)
  Real implementation

## Slide 217: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 218: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 219: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 220: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 221: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 222: Optional Assignment
Review the Ramulator paper
  Email me your review
Download and run Ramulator
  Compare DDR3, DDR4, SALP, HBM for the libquantum benchmark (provided in Ramulator repository)
  Email me your report
This may help you get into memory systems research quickly

## Slide 223: End of Backup Slides