## Slide 1: Memory System Design for AI/ML Accelerators & ML/AI Techniques for Memory System Design
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
29 September 2021
SRC AIHW Annual Review

## Slide 2: Confidentiality
By reviewing this presentation or participating in a SRC event, you are agreeing not to use the presented information for purposes unrelated to the event until approved by SRC;
Material may be presented that represents current research, some of which has not been published or protected. This material is not for public disclosure and until potential IP rights have been protected, please treat all of the information presented as confidential information which is the property of the researcher and their university.

## Slide 3: Agenda
Problem and Background
Task Overview
Technical Challenges, Goals and Ideas
Ideas, Results and Papers from the Past Year

## Slide 4: The Problem
Computing
is Bottlenecked by Data

## Slide 5: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process

## Slide 6: Data is Key for Future Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 7: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 8
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Future Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 9
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 10: Data is Key for Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 11
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Data → performance & energy bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 12: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Data → performance & energy bottleneck

## Slide 13: Data Overwhelms Modern Machines …
Storage/memory capability
Communication capability
Computation capability
Greatly impacts robustness, energy, performance, cost

## Slide 14
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 15
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 16: Axiom
An Intelligent Architecture
Handles Data Well

## Slide 17: How to Handle Data Well
Ensure data does not overwhelm the components
  via intelligent algorithms
  via intelligent architectures
  via whole system designs: algorithm-architecture-devices
Take advantage of vast amounts of data and metadata
  to improve architectural & system-level decisions
Understand and exploit properties of (different) data
  to improve algorithms & architectures in various metrics

## Slide 18: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 19: Architectures for Intelligent Machines
Data-centric
Data-driven
Data-aware

## Slide 20: Agenda
Problem and Background
Task Overview
Technical Challenges, Goals and Ideas
Ideas, Results and Papers from the Past Year

## Slide 21: In This Task… (Task #2946.001)
We focus on designing memory systems to handle data well
We aim to solve two different yet related and synergistic problems, both focusing on ML/AI and memory system design
We explore (and exploit the synergy between)
  Memory system design for AI/ML workloads/accelerators
  AI/ML techniques for improving memory system designs

## Slide 22: Our Goals in This Task
Two Major Goals:
  1. Memory system design for AI/ML workloads/accelerators
   in-depth exploration of memory system designs for cutting-edge and emerging machine learning accelerators
   more efficient on-chip and off-chip memory systems
  2. AI/ML techniques for improving memory system designs
   take a comprehensive look at memory system design and make it data driven, i.e., based on machine learning
   more effective cache/memory/prefetch/thread controllers and data/resource management/mapping/scheduling policies

## Slide 23: Anticipated Primary Results
Realistic, practical and effective novel memory system designs for ML/AI accelerators
New ML-based techniques to improve memory system efficiency and performance
Open-source workloads, metrics, methodologies & infrastructures to analyze such designs and techniques.

## Slide 24: Task Description

## Slide 25: Task Deliverables (2020)

## Slide 26: Task Deliverables (2021)

## Slide 27: Task Deliverables (2022)

## Slide 28: Task Information #2946.001 (1)
Thrust: AI Hardware
Task Leader: Onur Mutlu
  https://people.inf.ethz.ch/omutlu/
  onur.mutlu@inf.ethz.ch
Students
  Rahul Bera (ETH)
  Amirali Boroumand (CMU)
  Geraldo Francisco de Oliveira Junior (ETH)
  Joao Ferreira (ETH)
  Konstantinos Kanellopoulos (ETH)
  Damla Senol Cali (CMU)

## Slide 29: Task Information #2946.001 (2)
Senior Researchers
  Juan Gomez Luna (ETH)
  Lois Orosa (ETH)
  Jisung Park (ETH)
  Gagandeep Singh (ETH)
More students/postdocs to be added as the task evolves

## Slide 30: Recent PhD Graduates (I)
Amirali Boroumand
  December 2020
  Practical Mechanisms for Reducing Processor-Memory Data Movement in Modern Workloads
Gagandeep Singh
  April 2021
  Designing, Modeling, and Optimizing Data-Intensive Computing Systems
Damla Senol Cali
  August 2021
  Accelerating Genome Sequence Analysis via Efficient Hardware/Algorithm Co-Design
Nastaran Hajinazar
  August 2021
  Data-Centric and Data-Aware Frameworks for Fundamentally Efficient Data Handling in Modern Computing Systems

## Slide 31: Recent PhD Graduates (II)
https://safari.ethz.ch/safari-alumni/
Dr. Saugata Ghose
  Started @ UIUC as Assistant Professor, Fall 2020

## Slide 32: Soon to Finish PhD
Minesh Patel
  Defense date: October 1, 2021
  Enabling Effective Error Mitigation in Memory Chips That Use On-Die Error-Correcting Codes

## Slide 33: Industry Liaisons
Charles Augustine, Intel
Pradip Bose, IBM
Alper Buyuktosunoglu, IBM
Rosario Cammarota, Intel
Ramesh Chauhan, Qualcomm
Prokash Ghosh, NXP
Jose Joao, ARM
Arun Joseph, IBM
Anurag Kar, ARM
Preetham Lobo, IBM
Nithyakalyani Sampath, TI
Willem Sanberg, NXP
Pushkar Sareen, NXP
Sreenivas Subramoney, Intel
Xin Zhang, IBM
We are having and will have regular and irregular meetings with all liaison companies
Very open to other collaborators, feedback, internships

## Slide 34: Agenda
Problem and Background
Task Overview
Technical Challenges, Goals and Ideas
Ideas, Results and Papers from the Past Year

## Slide 35: Two Major Thrusts
  1. Memory system design for AI/ML workloads/accelerators
  2. AI/ML techniques for improving memory system designs

## Slide 36: Thrust 1 Exploration Ideas
1.1. Comprehensive Energy and Performance Analysis of ML/AI Accelerator Execution on Key ML/AI Workloads
1.2. Cache/Buffer, On-Chip Memory, Interconnect, Memory Controller Designs for ML Accelerators and Their Interfaces
1.3. Complete on-chip ML/AI accelerator designs with careful data orchestration and on-chip memory management.
1.4. On-chip & off-chip near-data processing (NDP) designs, interfaces, evaluation, programming for AI/ML workloads
1.5. Evaluation and understanding of both short-term and long-term options for NDP for AI/ML Workloads
1.6. Use of NVM devices, simple customized DRAM and 3D-stacked Memory+Logic for AI/ML Acceleration
1.7. High-Fidelity and Highly-Flexible Open Source Simulation & Modeling Infrastructures for ML/AI Memory Systems
This talk

## Slide 37: Memory System Design for AI/ML
Some background works from the past
"EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM”, MICRO 2019
"SMASH: Co-designing Software Compression and Hardware-Accelerated Indexing for Efficient Sparse Matrix Operations”, MICRO 2019
"Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks”, ASPLOS 2018.

## Slide 38: Two Major Thrusts
  1. Memory system design for AI/ML workloads/accelerators
  2. AI/ML techniques for improving memory system designs

## Slide 39: Thrust 2 Exploration Ideas
2.1. Comprehensive performance and energy analysis of rigid policies in the memory hierarchy – how far are they from the ideal policies? What is the maximum potential ML techniques can achieve?
2.2. New caching, prefetching, mem. controller, runahead, compression policies that are directed with appropriate ML techniques
2.3. Rigorous specification and coordination of ML-based on-chip cache, prefetch, DRAM, NVM, hybrid mem. Controllers
2.4. Design and evaluation of new ML-based techniques to manage hybrid memories consisting of multiple different technologies
2.5. Design and evaluation of new ML-based data mapping policies across on-chip caches and memory controllers
2.6. Design and evaluation of new ML-based thread scheduling policies in both SMT and memory controllers
2.7. High-Fidelity and Highly-Flexible Open Source Simulation & Modeling Infrastructures for ML-Based Controllers
This talk

## Slide 40: AI/ML for Memory System Design
Some background works from the past
"Self Optimizing Memory Controllers: A Reinforcement Learning Approach”, ISCA 2008
"NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning”, DAC 2019

## Slide 41: System Architecture Design Today
Human-driven
  Humans design the policies (how to do things)
Many (too) simple, short-sighted policies all over the system
No automatic data-driven policy learning
(Almost) no learning: cannot take lessons from past actions
Can we design
fundamentally intelligent architectures?

## Slide 42: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
How do we start?

## Slide 43: Two Major Thrusts & Their Synergies
  1. Memory system design for AI/ML workloads/accelerators
  2. AI/ML techniques for improving memory system designs

## Slide 44: Agenda
Problem and Background
Task Overview
Technical Challenges, Goals and Ideas
Ideas, Results and Papers from the Past Year

## Slide 45: Initial Results in Year I (2020 Review)
GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis [MICRO 2020]
NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling [FPL 2020]
An Experimental Study of Reduced-Voltage Operation in Modern FPGAs for Neural Network Acceleration [DSN 2020]
NATSA: A Near-Data Processing Accelerator for Time Series Analysis [ICCD 2020]
Robust Machine Learning Systems: Challenges, Current Trends, Perspectives, and the Road Ahead [IEEE D&T 2020]
Accelerating Genome Analysis: A Primer on an Ongoing Journey [IEEE Micro 2020]
SMASH Open Source Software Code Release [GitHub]

## Slide 46: Initial Results in Year I (2020 Ongoing)
Efficiently Accelerating Edge ML Inference by Exploiting Layer Heterogeneity: An Empirical Study with Google Edge Models [Ongoing]
A New Methodology and Open-Source Benchmark Suite for Evaluating Data Movement Bottlenecks: A Near-Data Processing Case Study [Ongoing]
Accelerating Profile Hidden Markov Models in Computational Biology Applications [Ongoing]
StenCache: A Near-Cache Accelerator for Stencil Computations [Ongoing]
SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM [Ongoing]
Polynesia: Enabling Effective Hybrid Transactional/Analytical Databases with Specialized Hardware/Software Co-Design [Ongoing]
Reinforcement Learning based Prefetch Generation [Ongoing]
Benchmarking a New Paradigm: Understanding a Modern Processing-in-Memory Architecture [Ongoing]

## Slide 47: Year II Results (2021 Annual Review I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 48: Year II Results (2021 Annual Review II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 49: Second Year Results: More Detail

## Slide 50: Year II Results (2021 Annual Review - I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 51: Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks
Amirali Boroumand Saugata Ghose Berkin Akin
Ravi Narayanaswami Geraldo F. Oliveira Xiaoyu Ma
Eric Shiu Onur Mutlu
PACT 2021
Notes: Hi, I’m Geraldo, a PhD Student at ETH Zurich.
Today I will present our work “Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks”
This work was lead by Amirali Boroumand during his internship at Google.

## Slide 52: Executive Summary
Context: We extensively analyze a state-of-the-art edge ML accelerator (Google Edge TPU) using 24 Google edge models
  Wide range of models (CNNs, LSTMs, Transducers, RCNNs)
Problem: The Edge TPU accelerator suffers from three challenges:
  It operates significantly below its peak throughput
  It operates significantly below its theoretical energy efficiency
  It inefficiently handles memory accesses
  Key Insight: These shortcomings arise from the monolithic design of the Edge TPU accelerator
  The Edge TPU accelerator design does not account for layer heterogeneity
  Key Mechanism: A new framework called Mensa
  Mensa consists of heterogeneous accelerators whose dataflow and hardware are specialized for specific families of layers
  Key Results: We design a version of Mensa for Google edge ML models
  Mensa improves performance and energy by 3.0X and 3.1X
  Mensa reduces cost and improves area efficiency
Notes: First, I will give an overview of this work.
[CLICK] In this work, we extensively analyze 24 edge NN models from Google while running inference on the Google Edge TPU accelerator for various types of NN models
[CLICK] We identify that while running NN inference, the accelerator suffers from three main challenges
[CLICK] it operates significantly below its peak throughput
[CLICK] it operates significantly below its theorical peak energy efficiency
[CLICK] and its memory system is not efficient
[CLICK] Our analysis leads to the key insight that these challenges arrive due to the monolithic one-size-fit-all design of the accelerators, which does not account for heterogeneity across different NN layers
[CLICK] To solve this issue, we propose Mensa, a framework that maps the execution of a particular NN layer to its most appropriate hardware accelerator
[CLICK] We extensively evaluate Mensa for Google NN models and we observe that it improves performance and energy efficiency by 3.0x and 3.1x compared to the baseline Edge TPU accelerator while reducing area and cost across 24 edge ML models
[NEXT]

## Slide 53: Google Edge NN Models
  We analyze inference execution using 24 edge NN models
13 CNN
Face Detection
6 RNN Transducers
Speech Recognition
2 LSTMs
Language Translation
Image Captioning
3 RCNN
Google Edge TPU
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [CLICK] We analyze inference execution on the accelerator using 24 edge NN models that serve as internal benchmarks for the Google Edge TPU, including
[CLICK] 6 RNN Transducers, used for applications such as automatic speech recognition.
[CLICK] 13 convolutional neural networks (CNNs), typically used for applications such as image classification and object detection
[CLICK] 2 long short-term memories (LSTMs), used for applications such as language translation and and handwriting recognition, and
[CLICK] 3 recurrent convolutional neural networks (RCNNs), used for applications such as image captioning
[NEXT]

## Slide 54: Diversity Across the Models
Insight 1: there is significant variation in terms of layer characteristics across the models
Chart: Parameter Footprint (MB)
| 1.0986329999999999E-3
CNN3 | 22201
CNN3 | 21609
CNN3 | 11025
CNN3 | 1225
CNN4 | 5329
CNN4 | 5041
CNN4 | 5329
CNN4 | 2628
CNN11 | 3136
CNN11 | 12544
CNN3 | 1
CNN4 | 1
Layers from LSTMs and Transducers
Layers from CNNs and RCNNs
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: We draw key two insights from our model analysis
[CLICK] First, we observe a large variation in terms of layer characteristics across different models.
[CLICK] To illustrate, the figure shows the total parameter footprint vs. the FLOP/B ratio (or reuse) across the layers of representative CNNs, LSTMs, and Transducers
[CLICK] We observe from the figure that that layers from LSTMs and Transducers have larger parameter footprints and lower reuse than layers from CNNs.
[NEXT]

## Slide 55: Diversity Within the Models
For example, our analysis of edge CNN models shows:
1
2
Insight 2: even within each model, layers exhibit
significant variation in terms of layer characteristics
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Chart: CNN5
 | 150.0625 | 12.25 | 110.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 95.7031 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 13.7812 | 13.7812 | 24.5 | 24.5 | 12.25 | 110.25
Chart: CNN13
Variation in FLOP/Byte: up to 244x across layers
Variation in MAC intensity: up to 200x across layers
Notes: [CLICK] Second, even within a single model, layers show variation in terms of layer characteristics
[CLICK] For example, we observe that layers in a single CNN models show
[CLICK] a varying MAC intensity of up to 200x across different layers
and
[CLICK] a varying flop/byte ratio of up to 244x across different layers
[NEXT]

## Slide 56: Root Cause of Accelerator Challenges
The key components of Google Edge TPU are completely
oblivious to layer heterogeneity
  While this approach might work for a specific group of layers, it fails to efficiently execute inference across a wide variety of edge models
DRAM
PE Array
Buffer
Dataflow
Off-chip bandwidth
Edge accelerators typically take a monolithic approach: equip the accelerator with an over-provisioned PE array and on-chip buffer, a rigid dataflow, and fixed off-chip bandwidth
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [CLICK] The main conclusion of our analysis is that the key components of the Edge TPU are oblivious to the layer heterogeneity of different NN models and even within a single NN model
[CLICK] The monolithic design approach of the edge TPU leads to inefficiency and resources under-utilization, since the accelerator design over-provised the size of the PE array and on-chip buffer, while assuming a rigid dataflow and fixed off-chip memory bandwidth
[CLICK] leading to the three accelerator challenges related to performance, energy and memory we identified in our analysis
[NEXT]

## Slide 57: Mensa Framework
  Goal: design an edge accelerator that can efficiently run inference across a wide range of different models and layers
1
2
  Instead of running the entire NN model on a monolithic accelerator:
  Mensa: a new acceleration framework for edge NN inference
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [CLICK] Based on our analysis and insights, the goal of our work is to design an edge NN accelerator that can efficiently run inference across a varying number of different models and layers.
[CLICK] To this end, instead of designing a one-size-fit-all monolithic accelerator
[CLICK] We propose Mensa, a new acceleration framework for NN inference
[NEXT]

## Slide 58: Mensa High-Level Overview
Monolithic Accelerator
Model A
Family 2
Family 3
Edge TPU Accelerator
Mensa
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Model B
Model C
Model A
Model B
Model C
Runtime
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Family 1
Acc. 1
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Acc. 2
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Acc. 3
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [CLICK ] In a baseline system, different machine learning models are execute in a single, monolithic edge accelerator, which leads to performance and energy issues.
[CLICK] On the other hand, Mensa distributes the layers from an NN model using a runtime scheduler across a collection of smaller hardware accelerators that are catered the properties of different layer types. By specializing each accelerator to a subset of layers, Mensa avoids the shortcomings of current monolithic edge ML accelerators, resulting in a highly-efficient and high-performance accelerator with a much smaller area.
Next I will give an brief overview of Mensa’s ruy
[NEXT]

## Slide 59: Mensa Runtime Scheduler
Accelerator characteristics
Layer characteristics
Scheduler
NN model
Layer Mapping
  The goal of Mensa’s software runtime scheduler is to identify which accelerator each layer in an NN model should run on
Generated once during initial setup
of a system
Layers tend to group together into a small number of families
Each of the accelerators caters to a specific family of layers
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [CLICK] The goal of Mensa’s software runtime scheduler is to identify which accelerator each layer in an NN model should run on. It works as follows
[CLICK] The scheduler gets a NN model as an input.
[CLICK] It also has two other pieces of information: (1) the characteristics of each layer; and (2) the key characteristics of the available hardware accelerators.
[CLICK] As I will show next, different layers tend to group into a smaller set of layer families with sharing key properties
[CLICK] In this way we can have a small pool of edge accelerators where each accelerator caters to a specific family of layers
[CLICK] We collect the characteristics of the accelerators and layers once prior to inference execution
[CLICK] With all this information, the scheduler generates a per-layer mapping between layers and accelerators by utilizing a mapping heuristic.
[NEXT].

## Slide 60: Mensa Runtime Scheduler
Accelerator characteristics
Layer characteristics
Scheduler
NN model
Layer Mapping
  The goal of Mensa’s software runtime scheduler is to identify which accelerator each layer in an NN model should run on
Generated once during initial setup
of a system
Layers tend to group together into a small number of families
Each of the accelerators caters to a specific family of layers
Introduction | TPU and Model Characterization | Mensa Framework | Mensa-G | Evaluation | Conclusion
● ● ● | ● ● ● ● ● ● ● ● ● ● | ● ● ● | ● ● ● ● ● | ● ● | ●
Notes: [We invite you to check our paper for more details about our scheduling heuristics.
[NEXT].

## Slide 61: For More on Mensa [PACT 2021]

## Slide 62: Year II Results (2021 Annual Review - I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 63
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
Notes: Hi.
Today Giray and I I will present Charon, a specialized near-memory architecture to accelerate garbage collection. This paper was presented in MICRO 2019.

## Slide 64: Executive Summary
Background: Prefetchers learns to predict future addresses by associating patterns with program context (called feature)
Problem: Three key shortcomings in prior prefetchers:
  Predicts mainly using a single program feature
  Lacks inherent system awareness
  Lacks online customization ability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized online to change features and/or objective
Contribution: Pythia, that formulates prefetching as reinforcement learning
  Adaptive, autonomous learning using multiple features and system-level feedback
  Realistic, practical implementation without any changes to software
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms prior SOTA by 3.4%, 7.7% and 16.9% in 1/4/bandwidth-constrained cores
Open sourced: https://github.com/CMU-SAFARI/Pythia

## Slide 65: Our Goal
A prefetching framework that:
Can learn to prefetch using multiple features and inherent system-level feedback information
Can be easily customized in silicon to change feature type and/or prefetcher’s objective

## Slide 66: Basics of Reinforcement Learning (RL)
Algorithmic approach to learn to take an action in a given situation to maximize a numerical reward
Agent stores Q-values for every state-action pairs
  Given a state, selects action that provides highest Q-value

## Slide 67: Formulating Prefetching as RL

## Slide 68: Pythia Overview
Q-Value Store: Records Q-values for all state-action pairs
Evaluation Queue: A FIFO queue of recently-taken actions
Evaluation Queue (EQ)
Demand Request
1
Assign reward to
corresponding EQ entry
Look up
QVStore
State
Vector
Q-Value Store
(QVStore)
2
3
5
Insert prefetch action &
State-Action pair in EQ
6
Prefetch Fill
A1
A2
A3
Memory
Hierarchy
Generate
prefetch
Evict EQ entry and update QVStore
4
Find the Action with max Q-Value
7
S1
S2
S3
S4
Set filled bit
Max

## Slide 69: Simulation Methodology
Champsim trace-driven simulator
150 single-core memory-intensive workload traces
  SPEC CPU2006 and CPU2017
  PARSEC 2.1
  Ligra
  Cloudsuite
Five state-of-the-art prefetchers
  SPP [Kim+, MICRO’16]
  Bingo [Bakhshalipour+, HPCA’19]
  MLOP [Shakerinava+, Prefetching Championship-3]
  SPP+DSPatch [Bera+, MICRO’19]
  SPP+PPF [Bhatia+, ISCA’20]

## Slide 70: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
1 channel
2 channels
4 channels
3.4%
7.7%

## Slide 71: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
1 channel
2 channels
4 channels
3.4%
7.7%
Pythia consistently provides higher performance in all system configurations from single core to twelve cores

## Slide 72: Pythia is Completely Open Source
https://github.com/CMU-SAFARI/Pythia
MICRO’21 artifact evaluated
Champsim source code + Chisel modeling code
All traces used for evaluation

## Slide 73: More in the Paper
Automatic design-space exploration for Pythia
Details about reward assignment and QVStore update
More results
  Performance comparison against multi-level prefetchers
  Detailed analysis of single-core and four-core performance
  Performance comparison with unseen traces
  Understanding Pythia’s learning with a case study
  Performance benefits via customization

## Slide 74: Year II Results (2021 Annual Review - I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 75: Refresh Triggered Computation

## Slide 76: Refresh Triggered Computation
Syed M. A. H. Jafri, Hasan Hassan, Ahmed Hemani, and Onur Mutlu, "Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators" ACM Transactions on Architecture and Code Optimization (TACO), December 2020.

## Slide 77: Year II Results (2021 Annual Review - I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 78
SynCron
Efficient Synchronization Support
for Near-Data-Processing Architectures
Christina Giannoula
christina.giann@gmail.com
Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas
Ivan Fernandez, Juan Gómez Luna, Lois Orosa
Nectarios Koziris, Georgios Goumas, Onur Mutlu

## Slide 79
Problem:
Synchronization support is challenging for NDP systems
Prior schemes are not suitable or efficient for NDP systems
Contribution:
SynCron: the first end-to-end synchronization solution for NDP architectures
Key Results:
SynCron comes within 9.5% and 6.2% of performance and energy of an Ideal zero-overhead synchronization scheme
Executive Summary

## Slide 80
NDP Synchronization Solution Space
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
NDPs:
SynCron [HPCA’21]
Hardware Message-passing
to Avoid Synchronization via Shared Memory
Hierarchical Communication
to Eliminate Expensive Network Traffic
Specialized Cache Structure
to Minimize Latency Costs
SynCron’s Design Choices

## Slide 81
Synchronization is a major system challenge for NDP systems
Prior schemes are not suitable or efficient for NDP systems
SynCron is the first end-to-end synchronization solution for NDP architectures
Syncron consists of four key techniques:
i. Hardware support for synchronization acceleration
ii. Direct buffering of synchronization variables
iii. Hierarchical message-passing communication
iv. Integrated hardware-only overflow management
SynCron’s benefits: 90.5% and 93.8% of performance and energy of an Ideal zero-overhead scheme
SynCron is highly-efficient, low-cost, easy-to-use, and general to support many synchronization primitives
Summary & Conclusion

## Slide 82: More on SynCron
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 83: Year II Results (2021 Annual Review - I)
Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks [PACT 2021]
Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning [MICRO 2021]
Refresh Triggered Computation: Improving the Energy Efficiency of Convolutional Neural Network Accelerators [TACO 2020]
SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures [HPCA 2021]
SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM [ASPLOS 2021]

## Slide 84: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 85
Motivation: Processing-using-Memory (PuM) architectures can efficiently perform bulk bitwise computation
Problem: Existing PuM architectures are not widely applicable
  Support only a limited and specific set of operations
  Lack the flexibility to support new operations
  Require significant changes to the DRAM subarray
Goals: Design a processing-using-DRAM framework that:
  Efficiently implements complex operations
  Provides the flexibility to support new desired operations
  Minimally changes the DRAM architecture
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations
  Providing the ability to implement arbitrary operations as required
  Using a massively-parallel in-DRAM SIMD substrate that requires minimal changes to DRAM
Key Results: SIMDRAM provides:
  88x and 5.8x the throughput and 257x and 31x the energy efficiency of a baseline CPU and a high-end GPU, respectively, for 16 in-DRAM operations
  21x and 2.1x the performance of the CPU and GPU for seven real-world applications
Executive Summary
2

## Slide 86: SIMDRAM Key Idea
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
23

## Slide 87: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
27
New SIMDRAM Program
Program

## Slide 88: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu

## Slide 89: Processing-using-Memory (PuM)
PuM: Exploits analog operation principles of the memory circuitry to perform computation
  Leverages the large internal bandwidth and parallelism available inside the memory arrays
A common approach for PuM architectures is to perform bulk bitwise operations
  Simple logical operations (e.g., AND, OR, XOR)
  More complex operations (e.g., addition, multiplication)
89

## Slide 90: Motivation, Goal, and Key Idea
Existing PuM mechanisms are not widely applicable
  Support only a limited and mainly basic set of operations
  Lack the flexibility to support new operations
  Require significant changes to the DRAM subarray
Goal: Design a PuM framework that
  Efficiently implements complex operations
  Provides the flexibility to support new desired operations
  Minimally changes the DRAM architecture
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
90

## Slide 91: SIMDRAM: PuM Substrate
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Higher throughput
Lower energy consumption
91

## Slide 92: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
92

## Slide 93: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
Program
MAJ/NOT logic
Step 1: Generate
MAJ logic
93
Step 1:
Builds an efficient MAJ/NOT representation of a given desired operation from its AND/OR/NOT-based implementation

## Slide 94: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Step 2: Generate
sequence of DRAM
commands
Program
94
Step 2:
Allocates DRAM rows to the operation’s inputs and outputs
Generates the sequence of DRAM commands (Program) to execute the desired operation

## Slide 95: SIMDRAM Framework: Overview
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
Step 3: Execution according to Program
Memory Controller
95
Step 3:
Executes the μProgram to perform the operation
Uses a control unit in the memory controller

## Slide 96: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
96

## Slide 97: Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications
97

## Slide 98: Conclusion
SIMDRAM:
  Enables efficient computation of a flexible set and wide range of operations in a PuM massively parallel SIMD substrate
  Provides the hardware, programming, and ISA support, to:
    Address key system integration challenges
    Allow programmers to define and employ new operations without hardware changes
More in the paper:
  Efficiently transposing data
  Programming interface
  Handling page faults, address translation, coherence, and interrupts
  Security implications
  Reliability evaluation
  Comparison to in-cache computing
  And more …
98
  SIMDRAM is a promising PuM framework
  Can ease the adoption of processing-using-DRAM architectures
  Improve the performance and efficiency of processing-using-DRAM architectures

## Slide 99: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu

## Slide 100: More on the SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 101: Year II Results (2021 Annual Review - II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 102: DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks
Geraldo F. Oliveira
Juan Gómez-Luna Lois Orosa Saugata Ghose
Nandita Vijaykumar Ivan Fernandez Mohammad Sadrosadati
Onur Mutlu
Notes: Hi, I’m Geraldo, a PhD Student under the supervision of professor Multu at ETH Zurich and I’ll be talking about our work DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks.
[NEXT]

## Slide 103: Executive Summary
Problem: Data movement is a major bottleneck is modern systems. However, it is unclear how to identify:
− different sources of data movement bottlenecks
  − the most suitable mitigation technique (e.g., caching, prefetching, near-data processing) for a given data movement bottleneck
Goals:
1. Design a methodology to identify sources of data movement bottlenecks
2. Compare compute- and memory-centric data movement mitigation techniques
Key Approach: Perform a large-scale application characterization to identify key metrics that reveal the sources to data movement bottlenecks
Key Contributions:
− Experimental characterization of 77K functions across 345 applications
− A methodology to characterize applications based on data movement bottlenecks and their relation with different data movement mitigation techniques
− DAMOV: a benchmark suite with 144 functions for data movement studies
− Four case-studies to highlight DAMOV’s applicability to open research problems
2
DAMOV: https://github.com/CMU-SAFARI/DAMOV
Notes: First, I will give a glance of what this talk is about.
[CLICK] It is known that data movement is a major bottleneck in modern systems. However, it is unclear how we can identify
[CLICK] the different sources that lead to a data movement bottleneck
[CLICK] and the most suitable data movement mitigation technique, as for example, traditional compute-centric techniques as data caching and prefetching, and memory-centric techniques as near-data processing, for a given data movement bottleneck
[CLICK] Therefore, the goal of our work is twofold
[CLICK] First, we aim to design a methodology that can systematically identify different sources of data movement bottlenecks in a system and
[CLICK] Second, we aim to compare the suitability of compute-centric and memory-centric data movement mitigation techniques for different data movement bottlenecks
[CLICK] To do so, we perform a large-scale application characterization in order to identify key metrics that can reveal a particular source of data movement bottleneck
[CLICK] From such characterization, we draw four key contributions
[CLICK] Our first contribution is our large-scale experimental workload characterization of 77K functions from across 345 different applications from varying domains
[CLICK] Second, we develop and validate a systematic methodology that cluster workloads into six different classes of data movement bottlenecks using four key metrics.
We also analyze how each one of the six classes of data movement bottlenecks correlates with three different data movement mitigation techniques, including near-data processing architectures
[CLICK] Third, by applying our new methodology over a wide-range of workloads, we develop DAMOV, a open-source benchmark suite with 144 application functions that target the study of data movement related topics.
[CLICK] Fourth, we showcase how DAMOV can aid the study of open research problems with four case studies.
[CLICK] We public release and open-source DAMOV in our github, with the hope it can enables further studies and research on hardware and software solutions for data movement bottlenecks
[NEXT]

## Slide 104: Near-Data Processing (2/2)
Samsung FIMDRAM (2021)
  The goal of Near-Data Processing (NDP) is
  to mitigate data movement
UPMEM (2019)
Near-DRAM-banks processing
for neural networks
1.2 TFLOPS compute throughput2
Near-DRAM-banks processing
for general-purpose computing
0.9 TOPS compute throughput1
7
[1] Devaux, "The True Processing In Memory Accelerator,” HCS, 2019
[2] Kwon+, “A 20nm 6GB Function-In-Memory DRAM, Based on HBM2 with a 1.2TFLOPS Programmable Computing Unit Using Bank-Level Parallelism, for Machine Learning Applications," ISSCC, 2021
Notes: Near-data processing in not a new idea. In fact, the idea of near-data processing architectures has been around for at least five decades. However, only recently industry has introduced the first NDP architectures
[CLICK] For example, the UPMEM architecture designed by the company of same name.
[CLICK] integrates a large number of simple CPUs nearby DRAM chips, targeting general-purpose computing
[CLICK] The UPMEM architecture can provide a compute throughput of around 0.9 TOPS
[CLICK] Another example, Samsung recently introduced the FIMDRAM architecture
[CLICK] which integrates processing elements nearby DRAM banks, which aims to accelerate neural networks.
[CLICK] The FIMDRAM architecture can provide up to 1.2 TFLOPS of compute throughput.
[NEXT]

## Slide 105: When to Employ Near-Data Processing?
Near-Data
Processing
Mobile consumer workloads
(GoogleWL2)
Neural networks
(GoogleWL2)
Graph processing
(Tesseract1)
Time series analysis
(NATSA6)
DNA
sequence mapping
(GenASM3; GRIM-Filter4)
...
[1] Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing," ISCA, 2015
[2] Boroumand+, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
[3] Cali+, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis,” MICRO, 2020
[4] Kim+, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies,” BMC Genomics, 2018
[5] Boroumand+, "Polynesia: Enabling Effective Hybrid Transactional/Analytical Databases with Specialized Hardware/Software Co-Design,” arXiv:2103.00798 [cs.AR], 2021
[6] Fernandez+, “NATSA: A Near-Data Processing Accelerator for Time Series Analysis,” ICCD, 2020
8
Databases
(Polynesia5)
Notes: [CLICK] Many recent works explore how NDP can benefit various application domains like
[CLICK] Graph processing,
[CLICK] mobile consumer workloads
[CLICK] neural networks
[CLICK] DNA sequence mapping
[CLICK] Databases
[CLICK] Time series analysis
[CLICK] and more
[NEXT]

## Slide 106: Key Approach
New workload characterization methodology to analyze:
  data movement bottlenecks
  suitability of different data movement mitigation mechanisms
Two main profiling strategies:
Architecture-independent profiling:
  characterizes the memory behavior independently of the underlying hardware
Architecture-dependent profiling:
  evaluates the impact of the system configuration on the memory behavior
15
Notes: [CLICK] We develop a new workload characterization methodology to analyze
[CLICK] data movement bottlenecks and
[CLICK] the suitability of different data movement mitigation mechanisms for these bottlenecks
[CLICK] We use two main profiling strategies to gather key metrics from applications
[CLICK] an architecture-independent profiling that provides metrics that characterize the application memory behavior independently of the underlying hardware.
[CLICK] And an architecture-dependent profiling that evaluates the impact of the system configuration (e.g., cache hierarchy) on the memory behavior.
[NEXT]

## Slide 107: Methodology Overview
DAMOV-SIM Simulator
# Cores
Scalability Analysis
ld 0xFF
st 0xAF
ld 0xFF
st 0xAF
ld 0xFF
Memory Traces
Temp. Locality
LFMR
LFMR
Low
High
High
Low
…
roi_begin
roi_end
Profiler
Step 1
Application Profiling
Target Application
Source Code
User Input
Temporal Locality
Spatial Locality
Step 2
Locality-based Clustering
DRAM Bandwidth
DRAM Latency
L1/L2 Cache Capacity
L3 Cache Contention
L1 Cache Capacity
Compute-Bound
Memory Bottleneck Classes
Methodology Output
LLC MPKI
Last-to-First
Miss Ratio (LFMR)
Arithmetic Intensity
Step 3
Memory Bottleneck Class.
16
Notes: Our methodology has three steps.
[CLICK] It takes as input an application’s source code and its input datasets.
[CLICK] In Step 1, we use a hardware profiling tool to identify memory-bound functions across many applications. This step allows for a quick first-level identification of many applications that suffer from memory bottlenecks and functions that cause these bottlenecks.
[CLICK] We utilize a new simulator, called DAMOV-SIM to collect key metrics and execute performance analysis of the functions identified in Step 1.
[CLICK] In Step 2, we use the architecture-independent profiling tool to collect metrics that provide insights about the memory access behavior of the memory-bottlenecked functions.
[CLICK] In Step 3, we collect architecture-dependent metrics and analyze the performance and energy of each function in an application when each of our three candidate data movement mitigation mechanisms is applied to the system.
[CLICK] By combining the data obtained from all three steps, we can systematically classify the leading causes of data movement bottlenecks in an application or function into different bottleneck classes
[NEXT]

## Slide 108: Step 1: Application Profiling
We analyze 345 applications from distinct domains:
25
Graph Processing
Deep Neural Networks
Physics
High-Performance Computing
Genomics
Machine Learning
Databases
Data Reorganization
Image Processing
Map-Reduce
Benchmarking
Linear Algebra
…
Physics
Security
Machine learning
Database
Graph processing
Data analytics
Data reorganization
Genomics
Deep Neural Networks
Image processing
Linear algebra
Signal processing
Data mining
Notes: In this work, we analyzed 345 applications from distinct domains, from
[CLICK] GRAPH Processing [CLICK] Neural Networks
[CLICK] Physics [CLICK] High-performance computing
[CLICK]Genomics [CLICK] And more
[NEXT]

## Slide 109: Step 3: Memory Bottleneck Analysis
Temporal Locality
Low
High
LFMR
Decreasing
High
MPKI
High
AI
AI
MPKI
AI
LFMR
MPKI
MPKI
Low
Increasing
AI
AI
Low
Low
Low
Low
High
Low
Low
Low
Low
Low
1a: DRAM Bandwidth
1b: DRAM Latency
1c: L1/L2
Cache Capacity
2a: L3 Cache Contention
2c: Compute-Bound
2b: L1 Cache Capacity
Memory Bottleneck Class
  Six classes of
  data movement bottlenecks:
  each class ↔ data movement
  mitigation mechanism
31
Notes: [CLICK] With such classification, we analyze how the functions in each class correlates with different data movement mitigation mechanisms in terms of performance and energy using our scalability analysis.
[NEXT]

## Slide 110: DAMOV is Open-Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
44
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 111: DAMOV is Open-Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmark
44
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: [CLICK] You can download DAMOV from our GitHub repository
[NEXT]

## Slide 112: More on DAMOV
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" Preprint in arXiv, 8 May 2021. [arXiv preprint] [DAMOV Suite and Simulator Source Code]

## Slide 113: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 114: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 115: Year II Results (2021 Annual Review - II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 116: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 119: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 120: Year II Results (2021 Annual Review - II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 121: Near-Data Processing
Samsung FIMDRAM (2021)
  The goal of Near-Data Processing (NDP) is
  to mitigate data movement
UPMEM (2019)
Near-DRAM-banks processing
for neural networks
1.2 TFLOPS compute throughput2
Near-DRAM-banks processing
for general-purpose computing
0.9 TOPS compute throughput1
7
[1] Devaux, "The True Processing In Memory Accelerator,” HCS, 2019
[2] Kwon+, “A 20nm 6GB Function-In-Memory DRAM, Based on HBM2 with a 1.2TFLOPS Programmable Computing Unit Using Bank-Level Parallelism, for Machine Learning Applications," ISSCC, 2021
Notes: Near-data processing in not a new idea. In fact, the idea of near-data processing architectures has been around for at least five decades. However, only recently industry has introduced the first NDP architectures
[CLICK] For example, the UPMEM architecture designed by the company of same name.
[CLICK] integrates a large number of simple CPUs nearby DRAM chips, targeting general-purpose computing
[CLICK] The UPMEM architecture can provide a compute throughput of around 0.9 TOPS
[CLICK] Another example, Samsung recently introduced the FIMDRAM architecture
[CLICK] which integrates processing elements nearby DRAM banks, which aims to accelerate neural networks.
[CLICK] The FIMDRAM architecture can provide up to 1.2 TFLOPS of compute throughput.
[NEXT]

## Slide 122: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 123: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 124: PIM System Organization
UPMEM-based PIM system with 20 UPMEM memory modules of 16 chips each (40 ranks)  2560 DPUs

## Slide 125: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 126: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 127
Juan Gómez Luna, Izzat El Hajj,
Ivan Fernandez, Christina Giannoula,
Geraldo F. Oliveira, Onur Mutlu
Understanding a Modern Processing-in-Memory Architecture:
Benchmarking and Experimental Characterization
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 128: Executive Summary
Data movement between memory/storage units and compute units is a major contributor to execution time and energy consumption
Processing-in-Memory (PIM) is a paradigm that can tackle the data movement bottleneck
  Though explored for +50 years, technology challenges prevented the successful materialization
UPMEM has designed and fabricated the first publicly-available real-world PIM architecture
  DDR4 chips embedding in-order multithreaded DRAM Processing Units (DPUs)
Our work:
  Introduction to UPMEM programming model and PIM architecture
  Microbenchmark-based characterization of the DPU
  Benchmarking and workload suitability study
Main contributions:
  Comprehensive characterization and analysis of the first commercially-available PIM architecture
  PrIM (Processing-In-Memory) benchmarks:
    16 workloads that are memory-bound in conventional processor-centric systems
    Strong and weak scaling characteristics
  Comparison to state-of-the-art CPU and GPU
Takeaways:
  Workload characteristics for PIM suitability
  Programming recommendations
  Suggestions and hints for hardware and architecture designers of future PIM systems
  PrIM: (a) programming samples, (b) evaluation and comparison of current and future PIM systems

## Slide 129: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 130: Observations, Recommendations, Takeaways
GENERAL PROGRAMMING RECOMMENDATIONS
Execute on the DRAM Processing Units (DPUs) portions of parallel code that are as long as possible.
Split the workload into independent data blocks, which the DPUs operate on independently.
Use as many working DPUs in the system as possible.
Launch at least 11 tasklets (i.e., software threads) per DPU.
PROGRAMMING RECOMMENDATION 1
For data movement between the DPU’s MRAM bank and the WRAM, use large DMA transfer sizes when all the accessed data is going to be used.
KEY OBSERVATION 7
Larger CPU-DPU and DPU-CPU transfers between the host main memory and the DRAM Processing Unit’s Main memory (MRAM) banks result in higher sustained bandwidth.
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound. As a result, the most suitable work- loads are memory-bound.

## Slide 131: Outline
Introduction
  Accelerator Model
  UPMEM-based PIM System Overview
UPMEM PIM Programming
  Vector Addition
  CPU-DPU Data Transfers
  Inter-DPU Communication
  CPU-DPU/DPU-CPU Transfer Bandwidth
DRAM Processing Unit
  Arithmetic Throughput
  WRAM and MRAM Bandwidth
PrIM Benchmarks
  Roofline Model
  Benchmark Diversity
Evaluation
  Strong and Weak Scaling
  Comparison to CPU and GPU
Key Takeaways

## Slide 132: Key Takeaway 1
Chart: Operational Intensity (OP/B)
Memory-bound region
Compute-bound region
The throughput saturation point is as low as ¼ OP/B,
i.e., 1 integer addition per every 32-bit element fetched
KEY TAKEAWAY 1
The UPMEM PIM architecture is fundamentally compute bound.
As a result, the most suitable workloads are memory-bound.

## Slide 133: Key Takeaway 2
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 2
The most well-suited workloads for the UPMEM PIM architecture use no arithmetic operations or use only simple operations (e.g., bitwise operations and integer addition/subtraction).

## Slide 134: Key Takeaway 3
Chart: Speedup over CPU (log scale)
| VA | SEL | UNI | BS | HST-S | HST-L | RED | SCAN-SSA | SCAN-RSS | TRNS | GEMV | SpMV | TS | BFS | MLP | NW | GMEAN (1) | GMEAN (2) | GMEAN | More PIM-suitable workloads (1) | Less PIM-suitable workloads (2) |
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 93.4 | 410.1 | 439.4 | 0.4 | 71.1 | 71.1 | 26.1 | 57.6 | 57.6 | 51.3 | 447.2 | 30.7 | 1552.7 | 1.6 | 305 | 68.8 | 52.2336 | 94.5778 | 65.6382
640 DPUs | 38.6 | 167 | 234.4 | 4.4 | 134.4 | 33.6 | 9.1 | 13.5 | 16 | 36.6 | 25.2 | 0.4 | 20.1 | 0.0368 | 5.6 | 0.1 | 34.1541 | 1.269 | 10.1005
2556 DPUs | 149.1 | 498.2 | 629.5 | 23 | 496.6 | 167.1 | 45.3 | 61.3 | 70.2 | 96.3 | 46.3 | 0.9 | 86.6 | 0.0019 | 5.8 | 0.1 | 132.5595 | 1.2587 | 23.2267
KEY TAKEAWAY 3
The most well-suited workloads for the UPMEM PIM architecture require little or no communication across DPUs (inter-DPU communication).

## Slide 135: Key Takeaway 4
KEY TAKEAWAY 4
• UPMEM-based PIM systems outperform state-of-the-art CPUs in terms of performance and energy efficiency on most of PrIM benchmarks.
• UPMEM-based PIM systems outperform state-of-the-art GPUs on a majority of PrIM benchmarks, and the outlook is even more positive for future PIM systems.
• UPMEM-based PIM systems are more energy-efficient than state-of-the-art CPUs and GPUs on workloads that they provide performance improvements over the CPUs and the GPUs.

## Slide 136: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 137: PrIM Repository
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 138
Juan Gómez Luna, Izzat El Hajj,
Ivan Fernandez, Christina Giannoula,
Geraldo F. Oliveira, Onur Mutlu
Understanding a Modern Processing-in-Memory Architecture:
Benchmarking and Experimental Characterization
el1goluj@gmail.com
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 139: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 140: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 141: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 142: More on PRIM Benchmarks
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture" Preprint in arXiv, 9 May 2021. [arXiv preprint] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Long Talk Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [SAFARI Live Seminar Slides (pptx) (pdf)] [SAFARI Live Seminar Video (2 hrs 57 mins)] [Lightning Talk Video (3 minutes)]

## Slide 143: Year II Results (2021 Annual Review - II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 144: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), to appear, 2021.

## Slide 146: Year II Results (2021 Annual Review - II)
DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks [IEEE Access 2021]
Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture [Arxiv, 2021]
FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications [IEEE Micro 2021]
A Modern Primer on Processing in Memory [Arxiv, 2020]
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems [Ongoing]

## Slide 147
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, Juan Gómez-Luna, Onur Mutlu
Sibyl: A Reinforcement Learning Approach to Data Placement in Hybrid Storage Systems
Notes: Hi my name is Gagandeep Singh and I will be presenting

## Slide 148: Executive Summary
Motivation: Complement different storage technologies to extend the overall capacity and reduce the system cost with minimal effect on the application performance
Problem: Data allocation and movement between the heterogeneous devices to achieve optimal (near-optimal) performance of the storage system is challenging
Goal: Develop an efficient, high-performant data-placement mechanism for hybrid storage systems that can flexibly adapt to the behavior of the workload as well as the storage device characteristics
Sibyl
Uses reinforcement learning (RL) to develop a data-placement policy that decides which data should be stored in the fast storage while minimizing the migration overhead
Performs dynamic data-placement decision by learning device characteristics while taking into account workload’s inherent behavior
QRator improves I/O performance by 24.1%, 34.7%, and 27.9% on average compared to two state-of-the-art heuristic-based baselines and a supervised learning-based baseline, respectively, and achieves 80% performance of the oracle policy that has knowledge of future access patterns

## Slide 149: Background: Hybrid Storage Systems
Fast
Slow
Write from host
Read from host
(1)
(1)
(2)
(1)
(2)
(3)
Frozen data eviction: (Migration)
Evict cold data to the slow device
In case of many reads to slow memory (hot data) move data to the fast device. Cold and sequential is read directly from the slow device
(3)
(3)
Read operation:
Read hot and random data from the fast device
Read cold and sequential from the slow device
Write operation:
Write hot and random data to the fast device
Cold and sequential data to the slow device
(2)
(3)
(3)

## Slide 150: Memory System Design for AI/ML Accelerators & ML/AI Techniques for Memory System Design
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
29 September 2021
SRC AIHW Annual Review

## Slide 151
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
Notes: Hi I am Rahul. Today, I’m going to present our work “…”
This work is done by researchers from SAFARI research group at ETH Zurich, in collaboration with Intel Labs and TU Delft.

## Slide 152: Executive Summary
Background: Prefetchers learns to predict addresses of future memory requests by associating patterns with program context (called feature)
Problem: Three key shortcomings in prior prefetchers:
  Predicts mainly using a single program feature
  Lacks inherent system awareness
  Lacks in-silicon customization ability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized in silicon to change features and/or objective
Contribution: Pythia, that formulates prefetching as reinforcement learning
  Adaptive, autonomous learning using multiple features and system-level feedback
  Realistic, practical implementation without any changes to software
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms prior SOTA by 3.4%, 7.7% and 16.9% in 1/4/bandwidth-constrained cores
Open sourced: https://github.com/CMU-SAFARI/Pythia
Notes: First, I am going to start with an executive summary.
[CLICK] Prefetching is a speculative technique that predicts address of future memory requests by associating patterns in memory addresses with some program context. We call this context a feature.
[CLICK] We observe three key shortcomings in prior prefetchers:
First, they mainly use a single program feature for prediction.
Second, they lack inherent system awareness
Third, they also lack any customizability in silicon
[CLICK] Our goal in this work is to design a prefetching framework that
– can learn from multiple program features and inherent system-level feedback
-- and can be customized in silicon to change the features or the objective of the prefetcher
[CLICK] Towards this we propose Pythia, that formulates …
Pythia makes adaptive and autonomous …
Pythia also proposes a realistic and practical …
[CLICK] We evaluate Pythia using …
We show that Pythia outperforms prior state-of-the-art …
Pythia is freely available in our GitHub repository.

## Slide 153: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: First, I am going to start by discussing key shortcomings of prior prefetchers.

## Slide 154: Prefetching Basics
Predicts address of long-latency memory requests and fetches data before the program demands
Associates access patterns from past memory requests to program context information
PC, Page#, Page offset, Cacheline delta, …
  Any combination of these
Program context  Access Pattern
Program Feature
Notes: Prefetching is a speculative technique that predicts …
[CLICK] To predict addresses, a prefetcher typically associates …
[CLICK] We call these context information as program feature.
[CLICK] Some examples of program features are … or any combination of these information

## Slide 155: Key Shortcomings in Prior Prefetchers
We observe three key shortcomings that significantly limits performance benefits
Predicts mainly using a single program feature
Lacks inherent system awareness
Lacks in-silicon customization ability
1
2
3
Notes: We observe three key shortcomings in prior prefetchers that significantly limits their performance improvement
[CLICK] First, they predict mainly …
[CLICK] Second, they lack any inherent …
[CLICK] Third, the also lack any online in-silicon customizability
Let’s take a closer look at each of these shortcomings.
[NEXT]

## Slide 156: (1) Single-Feature Prefetch Prediction
Provides benefits mainly on those workloads where the feature to pattern correlation exists
Bingo performs better
SPP performs better
Notes: Due to the use of a single program feature for prefetch prediction, a prefetcher typically provides performance benefits …
In other types of workloads, the same prefetcher fails to provide performance gains.
To illustrate this [CLICK], we show the coverage, overprediction, and performance improvement of two prior prefetchers SPP and Bingo for six sample workloads.
The top figure shows …
The bottom figure shows …
As we can see, for workloads like [CLICK], … Bingo performs better than SPP, as the program feature exploited by Bingo has stronger correlation with the access pattern than SPP.
On the other hand, for workloads like … [CLICK], SPP’s program feature provides better correlation, and thus performs better than Bingo.

## Slide 157: (1) Single-Feature Prefetch Prediction
Provides benefits mainly on those workloads where the feature to pattern correlation exists
Bingo performs better
SPP performs better
Relying on single feature for prediction leaves significant performance improvement on table
Notes: Thus the key takeaway is that [CLICK], …

## Slide 158: (2) Lack of Inherent System Awareness
Little understanding of undesirable effects (e.g., memory bandwidth usage, cache pollution, …)
  Performance loss in resource-constrained configurations
Similar coverage, lower overpredictions
Yet lower performance
Notes: The second shortcoming is that, all prior prefetchers have …, which often leads to …
To illustrate this, let revisit the previous figure and focus on Bingo’s performance in PARSEC-Canneal and Ligra-CC.
Bingo in Ligra-CC has similar coverage to PARSEC-Canneal with significantly …
The reason is that, in baseline without prefetching, Ligra-CC consumes much higher main memory …
As a result, even a smaller amount of overprediction hurts more performance in Ligra-CC than in PARSEC-Canneal.
This is only happening as Bingo does not take its undesirable effects into account while prefetching.
Thus the key takeaway is that, [CLICK] …

## Slide 159: (2) Lack of Inherent System Awareness
Little understanding of undesirable effects (e.g., memory bandwidth usage, cache pollution, …)
  Performance loss in resource-constrained configurations
Similar coverage, lower overpredictions
Yet lower performance
Prefetchers often lose performance gains due to the lack of inherent system awareness

## Slide 160: (3) Lack of In-silicon Customizability
Feature statically selected at design time
  Rigid hardware designed specifically to exploit that feature
Design from scratch
Verify
Fabricate
Notes: The third key shortcoming is that, all prior prefetcher lack in-silicon customizability.
These prefetchers statically selects the feature to exploit at design time and design a rigid hardware to specifically …
[CLICK] There is no way …
In order to exploit a new program feature, architects need to design a prefetcher from scratch …
[CLICK] and this cycle goes on for every new prefetcher. This wastes precious design time and human resource.

## Slide 161: Our Goal
A prefetching framework that:
Can learn to prefetch using multiple features and inherent system-level feedback information
Can be easily customized in silicon to change feature type and/or prefetcher’s objective
Notes: So our goal in this work is to … that
[CLICK] …
[CLICK] …

## Slide 162: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: To this end, we propose Pythia, which formulates …

## Slide 163: Basics of Reinforcement Learning (RL)
Algorithmic approach to learn to take an action in a given situation to maximize a numerical reward
Agent stores Q-values for every state-action pairs
  Given a state, selects action that provides highest Q-value
Notes: First, let me briefly describe the basics of reinforcement learning.
Reinforcement learning, in its simplest form, is the ...
A RL system contains two components: [CLICK] the agent and the environment.
The agent observes the state of the environment in every timestep [CLICK], takes an action based on the state [CLICK], and receives a reward for that action [CLICK].
[CLICK] The agent stores …
Given a state, the agent …

## Slide 164: Formulating Prefetching as RL
Notes: In Pythia, we formulate prefetching as a reinforcement learning problem.
[CLICK] The prefetcher acts as the agent, while [CLICK] the processor and memory subsystem acts as the environment.
[CLICK] Pythia extracts the program features from every demand request and use it as a state information to take a prefetch action [CLICK]
[CLICK] For every prefetch action, Pythia receives a numerical reward that evaluates the accuracy and timeliness of the prefetch request taking into account of system-level feedback.
Now let’s take a closer look at state, action, and reward definitions.

## Slide 165: What is State?
k-dimensional vector of features
Feature = control-flow + data-flow
Control-flow
  PC
  Branch PC
  Last-3 PCs, …
Data-flow
  Cacheline address
  Page#
  Delta between two cacheline address
  Last 4 deltas, …
Notes: We define the state as a k-dimensional vector of program features.
[CLICK] Each feature is composed of …
[CLICK] Some examples of control-flow information are …
[CLICK] Some examples of data-flow information are …
Though Pythia can theoretically learn from any number of such program features, we limit the size k as per storage budget.

## Slide 166: What is Action?
Selection of a prefetch offset
  Add to demanded cacheline to get
  prefetch cacheline address
A zero offset means no prefetch is generated
Notes: We define the action as the selection of a prefetch offset. Pythia adds this offset to the demanded cacheline to get the prefetched cacheline address.
[CLICK] Note that a zero offset is also a valid action for Pythia, which means no prefetch is generated.
[CLICK] As every post-L1 prefetcher …, the list of actions are limited to the range from -63 to +63 for a traditionally-sized …
[CLICK] However, we can prune the action list by automatic design-space exploration, as we show in the paper.

## Slide 167: What is Reward?
Defines the objective of Pythia
Five distinct levels
  Accurate and timely (RAT)
  Accurate but late (RAL)
  Loss of coverage (RCL)
  Inaccurate
    When memory b/w usage is low (RIN-L)
    When memory b/w usage is high (RIN-H)
  No-prefetch
    When memory b/w usage is low (RNP-L)
    When memory b/w usage is high (RNP-H)
Values are set at design time via automatic design-space exploration
  Can be customized further in silicon for higher performance
Notes: The reward defines the objective of Pythia
[CLICK] A reward encapsulates two metrics: …
[CLICK] Though Pythia can learn from any …, we demonstrate Pythia using a major system-level feedback: mem b/w usage

## Slide 168: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: We now provide a brief overview of Pythia.

## Slide 169: Pythia Overview
Q-Value Store: Records Q-values for all state-action pairs
Evaluation Queue: A FIFO queue of recently-taken actions
Evaluation Queue (EQ)
Demand Request
1
Assign reward to
corresponding EQ entry
Look up
QVStore
State
Vector
Q-Value Store
(QVStore)
2
3
5
Insert prefetch action &
State-Action pair in EQ
6
Prefetch Fill
A1
A2
A3
Memory
Hierarchy
Generate
prefetch
Evict EQ entry and update QVStore
4
Find the Action with max Q-Value
7
S1
S2
S3
S4
Set filled bit
Max
Notes: Pythia consists of two key components:
[CLICK] Q-value store, which is responsible for …
[CLICK] Evaluation queue, which is a first-in-first-out queue that stores the recently taken action.
As Pythia cannot always immediately assign a reward to a taken action
because the usefulness of the corresponding prefetch request is known, Pythia stores the action
in evaluation queue to properly assign rewards to them.
[CLICK] For every demand request, Pythia first checks EQ with deamdned address. If a matching entry is found in EQ, it means the corresponding action in EQ entry has generated a useful prefetch, and Pythia assigns a reward accordingly.
[CLICK] Then Pythia extracts features from the attributes of the demand request to create the state-vector and uses the state-vector to lookup QVStore [CLICK]
[CLICK] For the given state-vector, Pythia finds the action that has the highest Q-value and generates prefetch request accordingly to the memory hierarchy [CLICK]
[CLICK] Next, Pythia inserts the action in the EQ along with the state-action pair.
[CLICK] Pythia uses the reward stored in the evicted EQ entry to update the QVStore.

## Slide 170: Pythia Overview
Q-Value Store: Records Q-values for all state-action pairs
Evaluation Queue: A FIFO queue of recently-taken actions
Evaluation Queue (EQ)
Demand Request
1
Assign reward to
corresponding EQ entry
Look up
QVStore
State
Vector
Q-Value Store
(QVStore)
2
3
5
Insert prefetch action &
State-Action pair in EQ
6
Prefetch Fill
A1
A2
A3
Memory
Hierarchy
Generate
prefetch
Evict EQ entry and update QVStore
4
Find the Action with max Q-Value
7
S1
S2
S3
S4
Set filled bit
Max
Notes: We discuss more about the Q-value store organization and Pythia’s rewarding scheme in our paper.

## Slide 171: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: Next, we provide a brief overview of our evaluation.

## Slide 172: Simulation Methodology
Champsim trace-driven simulator
150 single-core memory-intensive workload traces
  SPEC CPU2006 and CPU2017
  PARSEC 2.1
  Ligra
  Cloudsuite
Five state-of-the-art prefetchers
  SPP [Kim+, MICRO’16]
  Bingo [Bakhshalipour+, HPCA’19]
  MLOP [Shakerinava+, Prefetching Championship-3]
  SPP+DSPatch [Bera+, MICRO’19]
  SPP+PPF [Bhatia+, ISCA’20]
Notes: Pythia is evaluated using ChampSim simulator using [CLICK] a wide range of workloads.
[CLICK] We compare Pythia against five recently-proposed state-of-the-art prefetchers.

## Slide 173: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
3.4%
7.7%
Notes: We analyze the performance of Pythia by varying core count from 1 to 12.
[CLICK] This is how previous prefetchers perform in systems with one core up to 12 cores
[CLICK] As you can see, Pythia significantly outperforms prior prefetchers in every core configuration
[CLICK] In single-core, Pythia outperforms previous best prefetcher MLOP by 3.4%
[CLICK] But in 12-core, Pythia outperforms MLOP by 7.7%.
[CLICK] The key takeaway is that …

## Slide 174: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
1 channel
2 channels
4 channels
3.4%
7.7%
Pythia consistently provides higher performance in all core configurations
Pythia’s gain increases with core count
Notes: We conclude that …
[CLICK]
[CLICK]

## Slide 175: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%
Notes: Next, we analyze Pythia’s performance by varying DRAM bandwidth.
[CLICK] This is how prior prefetchers perform in various DRAM bandwidth configuration.
[CLICK] The baseline DRAM configuration is highlighted in red. The other highlighted configurations closely models per-core DRAM bandwidth in popular commercial processors.
[CLICK] Pythia significantly outperforms prior prefetchers in all DRAM bandwidth configuration.
[CLICK] In the configuration with the highest DRAM bandwidth, Pythia outperforms MLOP by 3%
[CLICK] While in configuration with the lowest DRAM bandwidth, Pythia outperforms MLOP by a massive 17%.

## Slide 176: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%
Pythia consistently outperforms
in all DRAM bandwidth configurations
with 1/16x to 4x bandwidth of the baseline
Notes: We conclude that ...

## Slide 177: More in the Paper
Automatic design-space exploration for Pythia
Details about reward assignment and QVStore update
More results
  Performance comparison against multi-level prefetchers
  Detailed analysis of single-core and four-core performance
  Performance comparison with unseen traces
  Understanding Pythia’s learning with a case study
  Performance benefits via customization
Notes: We show more results in the paper and [CLICK] invite everyone to read it.

## Slide 178: More in the Paper
Automatic design-space exploration for Pythia
Details about reward assignment and QVStore update
More results
  Performance comparison against multi-level prefetchers
  Detailed analysis of single-core and four-core performance
  Performance comparison with unseen traces
  Understanding Pythia’s learning with a case study
  Performance benefits via customization

## Slide 179: Pythia is Open-sourced
https://github.com/CMU-SAFARI/Pythia
MICRO’21 artifact evaluated
Champsim source code + Chisel modeling code
All traces used for evaluation
Notes: Pythia is open-sourced and artifact evaluated.
All necessary source code and traces used for evaluation can be found online in our GitHub repository.

## Slide 180: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: We now conclude our talk.

## Slide 181: Conclusion
Background: Prefetchers learns to predict future addresses by associating patterns with program context (called feature)
Problem: Three key shortcomings in prior prefetchers:
  Predicts mainly using a single program feature
  Lacks inherent system awareness
  Lacks online customization ability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized online to change features and/or objective
Contribution: Pythia, that formulates prefetching as reinforcement learning
  Adaptive, autonomous learning using multiple features and system-level feedback
  Realistic, practical implementation without any changes to software
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms prior SOTA by 3.4%, 7.7% and 16.9% in 1/4/bandwidth-constrained cores
Open sourced: https://github.com/CMU-SAFARI/Pythia
Notes: [CLICK] In this work, we observe three key problems in prior prefetcher
First,
Second,
Third,
[CLICK] Our goal of this work is to…
[CLICK] Towards this we introduce Pythia that …
[CLICK] We evaluate Pythia …
[CLICK] Pythia is freely-available in our GitHub repo.

## Slide 182
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
Notes: Thank you. Now I will be happy to take any questions.

## Slide 183: ``
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu
FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications
Notes: Hello, I am Gagandeep Singh, a postdoctoral researcher at ETH Zurich. I would briefly present our work
FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications

## Slide 184: Near-Memory Acceleration
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]
Notes: This work was recently published in IEEE Micro.
In this work we analyze AND ACCELERATE two modern data intensive applications

## Slide 185: How to Analyze a Genome?
>CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCCAAGAGTTGCAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTAGCCAGAATGGTTGTGGGATGGGAGCCTCTGTGGACCGACCAGGTAGCTCTCTTTTCCACACTGTAGTCTCAAAGCTTCTTCATGTGGTTTCTCTGAGTGAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTTTTCATGTCAAGGACCTAATGTAGCTATACTGAACGTTATCTAGGGGAAAGATTGAAGGGGAGCTCTAAGGTCAACACACCACCACTTCCCAGAAAGCTTCTTCA……
  machine gives the complete sequence of genome as output
NO
Notes: Our first application is genome sequencing where until today, there is no machine THAT gives the complete sequence of genome as an output

## Slide 186: Genome Analysis in Real Life
Current sequencing machine provides
small randomized fragments
of the original DNA sequence
Alser+, "Technology dictates algorithms: Recent developments in read alignment", Genome Biology, 2021
Read Mapping
Reads
Notes: The sequencing machines produce small randomized pieces of the original DNA sequnece, called reads that go through a computationally intenstive step called read mapping

## Slide 187: Bottlenecked in Read Mapping!!
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Human whole
genomes
Human
1
Illumina NovaSeq 6000
48
at 30× coverage
in about 2 days
genome
32 CPU hours
on a 48-core processor
Chart: 
| Read Mapping | Others
Sales | 0.71 | 0.29
Goyal+, "Ultra-fast next generation human genome sequencing data processing using DRAGENTM bio-IT processor for precision medicine”, Open Journal of Genetics, 2017.
Notes: For example: a sequencing machine can sequence 48 genomes in about 2days
However, we A CPU WITH 48 CORES CAN process only 1 human genome in 32 CPU hours.
Therefore we aim to accelerate read mapping part in the genomics pipeline

## Slide 188: Stencil Computation in Weather Modeling
COSMO (Consortium for Small-Scale Modeling)
  Around 80 complex stencils
  Horizontal diffusion Vertical advection
Image Source: NVIDIA/MeteoSwiss: An example of COSMO simulation with cloud patterns over Switzerland and surrounding areas
Notes: In our second use case: We accelerate a real-world weather application
[CLICK] COSMO is a weather prediction model currently being used by a dozen nations including Switzerland, Germany, Italy etc.
[CLICK] It has around 80 different stencils.
Unlike the stencils found in literature weather model consists of complex stencils with varying amount of access patterns
Horizontal diffusion” and “vertical advection” are two complex stencils that are representative of the data access patterns and algorithmic complexity of the entire COSMO model.

## Slide 189: NERO: Weather Prediction Accelerator [FPL 2020]
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (23 minutes)] One of the four papers nominated for the Stamatis Vassiliadis Memorial Best Paper Award.
Notes: We also have a work on accelerating weather prediction application that was published in FPL’2020 and was nominated for the best Paper award

## Slide 190: Motivation and Goal
110 GBps DRAM
3.3 TBps L3-cache
Arithmetic Intensity [flop/byte]
Performance [Gflops]
Vertical Advection
Horizontal Diffusion
Prealignment Filter
POWER9 socket (486.4 Gflops/socket)
29.1 Gflops
(64 threads)
58.5 Gflops
(64 threads)
0.28 Gops
(64 threads)
Goal:
Mitigate the performance bottleneck of modern data-intensive applications in an energy-efficient way
Memory bound with limited performance and high energy consumption on IBM POWER9 CPU
Notes: The figure shows a roofline plot for a [CLICK] state of the art IBM power9 system with [CLICK]
after optimizing these two applications we obseve that we are [CLICK] still memory bound which leads to limited performance and high energy consumption
[CLICK] Therefore, our goal is to mitigate the performance bottleneck of these kernels in an energy-efficient way

## Slide 191: Near-Memory Acceleration
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 192: Key Results of Near-Memory Acceleration
Notes: By our real system evaluation we show that near-memory acceleration[CLICK]

## Slide 193: Key Results of Near-Memory Acceleration
Near-memory acceleration improves performance and energy efficiency by 5-27× and 12-133×, respectively, over a 16-core (64 hardware threads) IBM POWER9 CPU
Notes: can provide tremendous gains in terms of performance and energy efficiency

## Slide 194: Key Results of Near-Memory Acceleration
Single channel & multiple channel HBM designs
Open-source: https://github.com/CMU-SAFARI
Near-memory acceleration improves performance and energy efficiency by 5-27× and 12-133×, respectively, over a 16-core (64 hardware threads) IBM POWER9 CPU
Notes: We provide many more results and insights in our paper
And we also opensource designs on our github page.

## Slide 195: ``
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu
FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications
Notes: I encourage you to read our IEEE Micro and FPL papers.