## Slide 1: Storage-Centric Computing Enabling Fundamentally-Efficient Computers
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
1 December 2024
CCF China Storage Keynote Talk

## Slide 2: Problem
Computing
is Bottlenecked by Data

## Slide 3: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process
  We need to perform more sophisticated analyses on more data

## Slide 4: Huge Demand for Performance & Efficiency
Source: https://youtu.be/Bh13Idwcb0Q?t=283
~4 orders of magnitude increase in memory requirement in just a few years!

## Slide 5: Huge Demand for Performance & Efficiency
development of new
sequencing technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Oxford Nanopore MinION
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 6: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable
(All at the Same Time)

## Slide 7: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 8: Today’s Computing Systems
Processor centric
All data processed in the processor  at great system cost

## Slide 9: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory & storage

## Slide 10: Processor-Centric System Performance
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 11: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.

## Slide 12: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
6400X
A memory access consumes 6400X
the energy of a simple integer addition

## Slide 13
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Energy Waste in Mobile Devices

## Slide 14: Energy Waste in Accelerators
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models

## Slide 15: Example Energy Breakdowns
Chart: Normalized Energy
| Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | Baseline | Base+HB | Mensa | LSTM1 | Transd.1 | Transd.2 | CNN5 | CNN9 | CNN10 | CNN12 | RCNN1 | RCNN3 | Average
Total Static | 0.18337 | 0.028807 | 0.0016648 | 0.18261 | 0.050529 | 0.0029202 | 0.18196 | 0.049265 | 0.0028471 | 0.1816 | 0.17419 | 0.045879 | 0.22843 | 0.2123 | 0.033445 | 0.10425 | 0.071167 | 0.013518 | 0.23801 | 0.21307 | 0.037237 | 0.1827 | 0.083929 | 0.018429 | 0.13761 | 0.059899 | 0.030616 | 0.16493 | 0.086827 | 0.024117
PE | 0.0090239 | 0.0090239 | 0.0090239 | 0.0089025 | 0.0089025 | 0.0089025 | 0.0089121 | 0.0089121 | 0.0089121 | 0.30265 | 0.30265 | 0.30265 | 0.21111 | 0.21111 | 0.21111 | 0.078692 | 0.078692 | 0.078692 | 0.19984 | 0.19984 | 0.19984 | 0.12035 | 0.12035 | 0.12035 | 0.24015 | 0.24015 | 0.24015 | 0.19822 | 0.19822 | 0.19822
Param Buffer+NoC | 0.011732 | 0.011732 | 0 | 0.012646 | 0.012646 | 0 | 0.01223 | 0.01223 | 0 | 0.35617 | 0.35617 | 0.0066224 | 0.3645 | 0.3645 | 0.008601 | 0.62157 | 0.62157 | 0.011434 | 0.35462 | 0.35462 | 0.0081578 | 0.14233 | 0.14233 | 0.0025231 | 0.15703 | 0.15703 | 0.0025904 | 0.19173 | 0.19173 | 0.0038425
Act Buffer+NoC | 0.00029556 | 0.00029556 | 9.2361e-06 | 0.00050107 | 0.00050107 | 1.5659e-05 | 0.00047681 | 0.00047681 | 1.49e-05 | 0.011178 | 0.011178 | 0.00020783 | 0.013214 | 0.013214 | 0.0003118 | 0.024601 | 0.024601 | 0.00046662 | 0.013074 | 0.013074 | 0.00030238 | 0.0044216 | 0.0044216 | 8.4817e-05 | 0.005467 | 0.005467 | 9.3264e-05 | 0.0064591 | 0.0064591 | 0.00013406
Off-chip Interconnect | 0.31791 | 0.31791 | 0 | 0.31782 | 0.31782 | 0 | 0.31825 | 0.31825 | 0 | 0.059303 | 0.059303 | 0.028786 | 0.073025 | 0.073025 | 0.010856 | 0.068287 | 0.068287 | 0.0068711 | 0.077702 | 0.077702 | 0.008003 | 0.21986 | 0.21986 | 0.010914 | 0.18371 | 0.18371 | 0.018103 | 0.19266 | 0.19266 | 0.012536
DRAM | 0.47767 | 0.47767 | 0.16611 | 0.47752 | 0.47752 | 0.16606 | 0.47817 | 0.47817 | 0.16629 | 0.089103 | 0.089103 | 0.030986 | 0.10972 | 0.10972 | 0.038156 | 0.1026 | 0.1026 | 0.03568 | 0.11675 | 0.11675 | 0.040599 | 0.33034 | 0.33034 | 0.11488 | 0.27602 | 0.27602 | 0.095989 | 0.28948 | 0.28948 | 0.10101
In LSTMs and Transducers used by Google,
>90% energy spent on off-chip interconnect and DRAM
https://arxiv.org/pdf/2109.14320

## Slide 16: Fundamental Problem
Processing of data
is performed
far away from the data

## Slide 17: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 18: Process Data Where It Makes Sense
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
SRAM
Storage
Storage
Sensors

## Slide 19: Goal: Processing Inside Memory/Storage
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory/Storage
Database
Graphs
Media
ML model
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 20: An Overview Paper
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/2012.03112.pdf

## Slide 21: Processing in Storage: Two Types
1. Processing near Storage Devices
2. Processing using Storage Devices

## Slide 22: Processing-in-Memory: Two Types
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: Computation logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells & circuitry to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 23: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
And, many other experimental chips and startups
[Alibaba 2022]

## Slide 24: Processing-in-Memory Landscape Today

## Slide 25: Processing-in-Memory Landscape Today
https://www.servethehome.com/samsung-processing-in-memory-technology-at-hot-chips-2023/

## Slide 26: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 27: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 28: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 29: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 30: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 31: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Top Picks Honorable Mention by IEEE Micro. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 32: A Short Retrospective @ 50 Years of ISCA
https://arxiv.org/pdf/2306.16093

## Slide 33: Accelerating Graph Pattern Mining
Maciej Besta, Raghavendra Kanakagiri, Grzegorz Kwasniewski, Rachata Ausavarungnirun, Jakub Beránek, Konstantinos Kanellopoulos, Kacper Janda, Zur Vonarburg-Shmaria, Lukas Gianinazzi, Ioana Stefan, Juan Gómez-Luna, Marcin Copik, Lukas Kapp-Schwoerer, Salvatore Di Girolamo, Nils Blach, Marek Konieczny, Onur Mutlu, and Torsten Hoefler, "SISA: Set-Centric Instruction Set Architecture for Graph Mining on Processing-in-Memory Systems" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pdf)] [Talk Video (22 minutes)] [Lightning Talk Video (1.5 minutes)] [Full arXiv version]

## Slide 34: In-Storage Genomic Data Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]
https://arxiv.org/abs/2202.10400

## Slide 35: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 36: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 37: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 38: Compute-Centric Accelerators
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 39: Key Idea: In-Storage Filtering
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 40: GenStore
SSD Controller
Core
Core
Core
In-SSD DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
Host System
FTL
ACC
ACC
ACC
GenStore
Metadata
GenStore
FTL
Reads that need
substantial processing
Key idea: Filter reads that do not require alignment inside the storage system
Challenges
  Different behavior across read mapping workloads
  Limited hardware resources in the SSD
Notes: Which is the first in-storage processing system designed for genome sequence analysis
Our key idea is to Filter reads that do not require alignment inside the storage system and send the unfiltered data to the host system for further processing
However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD.

## Slide 41: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 42: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 43: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 44: Performance – GenStore-EM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 45: Performance – GenStore-NM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
Notes: We analyze the benefits of GenStore-NM for a 12-GB long read set with very high genetic variation compared the the reference genome where 99.7% of reads do not match any subsequence in the reference genome.
We show the benefit of GS on software and hardware read mappers.
GS provides 22.4× – 27.9× speedup compared to the software Base
GS provides 6.8× – 19.2× speedup compared to the hardware Base
GS provides on average 27.2× energy reduction

## Slide 46: Area and Power Consumption
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 47: In-Storage Genomic Data Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]
https://arxiv.org/abs/2202.10400

## Slide 48: Tight Integration of Genome Analysis Tasks
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, "GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (25 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.08600.pdf

## Slide 49: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 50: In-Storage Metagenomics [ISCA 2024]
Nika Mansouri Ghiasi, Mohammad Sadrosadati, Harun Mustafa, Arvid Gollwitzer, Can Firtina, Julien Eudine, Haiyu Mao, Joel Lindegger, Meryem Banu Cavlak, Mohammed Alser, Jisung Park, and Onur Mutlu, "MegIS: High-Performance and Low-Cost Metagenomic Analysis with In-Storage Processing" Proceedings of the 51st Annual International Symposium on Computer Architecture (ISCA), Buenos Aires, Argentina, July 2024. [Slides (pptx) (pdf)] [arXiv version]
https://arxiv.org/pdf/2406.19113

## Slide 51: MegIS High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing
Nika Mansouri Ghiasi
Mohammed Alser Jisung Park Onur Mutlu
Mohammad Sadrosadati Harun Mustafa Arvid Gollwitzer Can Firtina
Julien Eudine Haiyu Mao Joël Lindegger Meryem Banu Cavlak
Notes: Hi everyone, I am Nika, and today, I will talk about
MegIS: High-Performance, Energy-Efficient, and Low-Cost Metagenomic Analysis with In-Storage Processing

## Slide 52: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Overcomes the limitations of traditional genomics
  Bypasses the need for analyzing individual species in isolation
Notes: Metagenomics: Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)
Metagenomics overcomes the limitations of traditional genomics
Because it bypasses the need for culturing individual species in isolation,
which is not feasible in many important clinical and environmental use cases

## Slide 53: What is Metagenomics?
Has led to groundbreaking advances
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Notes: Therefore, metagenomics has led to ground-breaking advances
In many fields such as
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases

## Slide 54: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 55: Challenges of In-Storage Processing
No metagenomic analysis tool can run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While In-Storage Processing (ISP) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an ISP system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 56: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 57: MegIS’s Steps
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
V. cholerae
E. coli
SARS-CoV-2
Abundance
Estimation
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Step 1
Step 2
Step 3

## Slide 58: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 59: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 60: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 61: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 62: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 63: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 64: Evaluation Methodology Overview
Performance, Energy, and Power Analysis
Baseline Comparison Points
Performance-optimized software, Kraken2 [Genome Biology’19]
Accuracy-optimized software, Metalign [Genome Biology’20]
PIM hardware-accelerated tool (using processing-in-memory), Sieve [ISCA’21]
SSD Configurations
SSD-C: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-P: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Hardware Components
Synthesized Verilog model for the in-storage accelerators
MQSim [Tavakkol+, FAST’18] for SSD’s internal operations
Ramulator [Kim+, CAL’15] for SSD’s internal DRAM
Software Components
Measure on a real system:
AMD® EPYC® CPU with 128 physical cores
1-TB DRAM
Notes: We model performance, energy, and power of the systems based on the latency and throughput of each hardware-based and software-based component
We valuate the following baselines:
...
We evaluate these tools on systems with cost-optimized and performance-optimized SSD configurations

## Slide 65: Speedup over Software (with Cost-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
14.9x
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.43101 | 0.38921 | 0.35039 | 0.38881
MS | 5.3489 | 5.6406 | 6.3871 | 5.7761
SSD-C
5.8x
Sample Genetic Diversity
14.9x
Notes: We analyze the benefits of MegIS for samples with low, medium, and high genetic diversity,
And here I am showing for a cost optimized-SSD
We observe that compared to both P-Opt and A-Opt
MegIS provides significant speedups

## Slide 66: Speedup over Software (with Performance-Optimized SSD)
MegIS provides significant speedup over both
Performance-Optimized and Accuracy-Optimized baselines
Speedup
Performance-Optimized
MegIS
Accuracy-Optimized
Sample Genetic Diversity
Chart: 
| Low | Med | High | GMean
P-Opt | 1 | 1 | 1 | 1
A-Opt | 0.3836 | 0.29101 | 0.31974 | 0.32925
MS | 2.6617 | 3.6664 | 6.5218 | 3.9926
SSD-P
4.0x
12.1x
MegIS improves performance on both
cost-optimized and performance-optimized SSDs

## Slide 67: Speedup over the PIM Hardware Baseline
4.9x
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 4.8422 | 4.8446 | 5.0596 | 4.9144
Chart: 
| Low | Med | High | GMean
 | 1 | 1 | 1 | 1
 | 1.462 | 1.7798 | 2.7359 | 1.9237
Speedup
SSD-C
PIM
MegIS
1.9x
SSD-P
Sample Genetic Diversity
Sample Genetic Diversity
PIM
MegIS
MegIS provides significant speedup over the PIM baseline
Notes: Similarly, we evaluate megis compared to the pim baseline
and show that on systems with cost-optimized
and performance-optimized ssds,
MegiS significantly outperforms the PIM baseline

## Slide 68: Reduction in Energy Consumption
On average across different input sets and SSDs
Chart: 
| Perf-Opt | Acc-Opt | PIM | MegIS
 | 1 | 0.35526 | 2.8421 | 5.4
GeoMean Energy Reduction
(Higher is Better)
MegIS provides significant energy reduction over
the Performance-Optimized, Accuracy-Optimized, and PIM baselines
5.4x
15.2x
1.9x
Same
accuracy
Notes: Next, we show megis's energy reduction on average accross different input sets and SSDs and observe that megis provides...

## Slide 69: Accuracy, Area, and Power
Accuracy
Same accuracy as the accuracy-optimized baseline
Significantly higher accuracy than the performance-optimized and PIM baselines
  4.6 – 5.2× higher F1 score
  3 – 24% lower L1 norm error
Area and Power
Total for an 8-channel SSD:
Area: 0.04 mm2
Power: 7.658 mW
(Only 1.7% of the area and 4.6% of the power consumption
of three ARM Cortex R4 cores in an SSD controller)
Notes: MegIS provides all these benefits while achieving high accuracy

## Slide 70: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 71: System Cost-Efficiency
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
MegIS improves system cost-efficiency
and makes accurate metagenomics more accessible
for wider adoption
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 72: More in the Paper
MegIS’s performance with the cores in the SSD controller
MegIS’s performance outside SSD
Sensitivity analysis with varying
  Database sizes
  Memory capacities
  #SSDs
  #Channels
  #Samples
MegIS’s performance for abundance estimation
https://arxiv.org/abs/2406.19113

## Slide 73: More to Come…

## Slide 74: Processing in Storage: Two Types
1. Processing near Storage Devices
2. Processing using Storage Devices

## Slide 75: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 76: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Notes: In-storage processing leverages cute units inside the storage devices, [Clompick] such as …

## Slide 77: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
…
…
…
Notes: Such as embedded core or FPGA to perform computation inside the storage [Click] and sends …

## Slide 78: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
Results only
ISP can mitigate data movement overhead
by reducing SSD-external data movement
…
…
…
Notes: Sends only the computation results. [Click]
This way, in-storage processing can significatnly mitigate the data movement by reducing external I/Os between the host and the storage device. [Click]

## Slide 79: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
SSD internal I/O bandwidth: ~ 10 GB/s
…
…
…
SSD-internal bandwidth
becomes the new bottleneck in ISP
Notes: However, in-storage processing also needs to read the massive data from underlying NAND flash chips, [Click] and SSD internal bandwidth is not that higher than the external bandwidth even in high-end NAND flash-based SSDs. [Click]
As a result, SSD internal I/Os become the new bottlenck in in-storage processing. [Click]

## Slide 80: In-Flash Processing (IFP)
Performs computation inside NAND flash chips
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
SSD internal I/O bandwidth: ~ 10 GB/s
In-flash processing
…
…
…
Notes: If we can perform computation inside NAND flash chips, [Click] it can reduce …

## Slide 81: In-Flash Processing (IFP)
Performs computation inside NAND flash chips
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
IFP fundamentally mitigates data movement
In-flash processing
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
Results only
SSD internal I/O bandwidth: ~ 10 GB/s
…
…
…
Notes: It can reduce the internal data movement within the SSD by sending only the results to the flash controller and the host, [Click] thereby fundamentally mitigating the data movement from the storage device. [Click]

## Slide 82: Our Proposal: Flash-Cosmos
Flash-Cosmos enables
  Computation on multiple operands with a single sensing operation
  Accurate computation results by eliminating raw bit errors in stored data
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Operand O32
…
Operand O3
Operand O2
Operand O1
O1 & O2 & O3 & … & O32
Simultaneous sensing
Notes: At a very high level, Flash-Cosmos enables [Click] computation while sensing multiple operands at once and accurate computation results by zeroing raw bit errors in stored data. [Click]

## Slide 83: Key Ideas of Flash-Cosmos
Multi-Wordline Sensing (MWS)
to enable in-flash bulk bitwise operations via a single sensing operation
Enhanced SLC-Mode Programming (ESP)
to eliminate raw bit errors in stored data
(and thus in computation results)
Notes: We introduce two techniques, Multi-Wordline Sensing, or MWS in short, that enables in-flash bulk bitwise operations via a single sensing operation, [Click] and Enhanced SLC-Mode Programming, or ESP in short, to achieve zero raw bit errors in stored data and thus no errors in computation results. [Click]

## Slide 84: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Notes: The key observation is that, if we simultaneously activate multiple wordlines within a block, which we call intra-block MWS, it results in the bitwise AND of stored data in the wordlines. [Click]

## Slide 85: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Non-Target Cells:
Operate
as resistors
Notes: As explained all the non-target cell would operate as a resistance, [Click] while …

## Slide 86: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:
Notes: Target cells operate as either a resistance or an open switch depending the stored data. [Click]
In this example, only Bitline 4 can conduct flow, as the other bitlines have at least one cell that operates as an open switch. [Click]

## Slide 87: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: So, the sensing result would be ‘1’ only when all the target cells store bit data ‘1’, which is equivalent to the bitwise AND of all the target cells. [Click]

## Slide 88: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
0
Result:
Notes: This property also holds [Click] when we activate more than two wordlines at the same time, [Click], for example, …

## Slide 89: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: The bitline current cannot flow through Bitline 4 any longer, as it has a cell that stores ‘0’ and blocks the bitline current. [Click]

## Slide 90: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
1
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Flash-Cosmos (Intra-Block MWS) enables
bitwise AND of multiple pages in the same block
via a single sensing operation
Notes: This way, intra-block MWS enables bitwise AND operation on any pages in the same block via a single sensing operation. [Click]

## Slide 91: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
1
1
0
0
…
WLy in Blocki
…
…
…
…
Notes: Flash-Cosmos also enables bitwise OR operations by simultaneously activating multiple wordlines in different blocks, which we call inter-block MWS. [Click]

## Slide 92: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
Notes: In this example, only Bitline 4 cannot conduct current, as both the target NAND string have a cell that operates as an open switch. [Click]

## Slide 93: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: It means that the sensing result would read as ‘0’ only when all the target cells store bit data ‘0’, which is equivalent to the bitwise OR of all the target cells. [Click]

## Slide 94: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Notes: Like intra-block MWS, [Click] this property holds when we activate more than two wordlines in different blocks at the same time, [Click], as we can see …

## Slide 95: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: As we can see the current can flow through Bitline 4 as well, since there is a cell that operates as a resistance. [Click]

## Slide 96: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Flash-Cosmos (Inter-Block MWS) enables
bitwise OR of multiple pages in different blocks
via a single sensing operation
Notes: This way, inter-block MWS enables bitwise OR operations on any pages in different blocks via only a single sensing operation. [Click]

## Slide 97: Other Types of Bitwise Operations
Flash-Cosmos also enables other types of bitwise operations (NOT/NAND/NOR/XOR/XNOR)
leveraging existing features of NAND flash memory
https://arxiv.org/abs/2209.05566.pdf

## Slide 98: Key Ideas
Multi-Wordline Sensing (MWS)
to enable in-flash bulk bitwise operations via a single sensing operation
Enhanced SLC-Mode Programming (ESP)
to eliminate raw bit errors in stored data
(and thus in computation results)
Notes: Now let’s dive into the key ideas of Enhanced SLC-Mode Programming [Click] that elminiates …

## Slide 99: Enhanced SLC-Mode Programming (ESP)
Goal: eliminate raw bit errors in stored data (and computation results)
Key ideas
  Programs only a single bit per cell (SLC-mode programming)
    Trades storage density for reliable computation
  Performs more precise programming of the cells
    Trades programming latency for reliable computaion
Maximizes the reliability margin
between the different states of flash cells
Notes: Eliminates raw bit errors in stored data. [Click]
The key idea is to program only a single bit per cell for the target data of computation, meaning that ESP trades storage density, [Click] and use more precise program-voltage control, meaning that it also trades program latency, [Click] to maximize the reliability margin between the program and erased states of flash cells. [Click]

## Slide 100: Enhanced SLC-Mode Programming (ESP)
To eliminate raw bit errors in stored data (and computation results)
Key ideas
  Programs only a single bit per cell (SLC-mode programming)
    Trades storage density for reliable computation
  More precise program-voltage control
    Trades programming latency for reliable computaion
Maximizes the reliability margin
between the different states of flash cells
Flash-Cosmos (ESP) enables
reliable in-flash computation
by trading storage density & programming latency
Storage & latency overheads affect
only data used in in-flash computation
Notes: So, ESP enables reliable in-flash computation by trading storage density and program performance, [Click] but the overheads occur only for the target data of computation. [Click]

## Slide 101: Evaluation Methodology
Real-device characterization
  To validate the feasibility and reliability of Flash-Cosmos
  Using 160 48-WL-layer 3D Triple-Level Cell NAND flash chips
    3,686,400 tested wordlines
  Under worst-case operating conditions
    Under a 1-year retention time at 10K P/E cycles
    Worst-case data patterns
System-level evaluation
  Using the state-of-the-art SSD simulator (MQSim [Tavakkol+, FAST’18])
  Three real-world applications
    Bitmap Indices (BMI): Bitwise AND of up to ~1,000 operands
    Image Segmentation (IMS): Bitwise AND of 3 operands
    K-clique Star Listing (KCS): Bitwise OR of up to 32 operands
  Baselines
    Outside-Storage Processing (OSP): A multi-core CPU (Intel i7-11700K)
    In-Storage Processing (ISP): An in-storage hardware accelerator
    ParaBit [Gao+, MICRO’21]: State-of-the-art in-flash processing mechanism
Notes: First, we conducted rigorous real-device characterization to validate the feasibility and reliability of Flash-Cosmos, [Click] using 160 3D NAND flash chips, [Click] considering the worst-case operation conditions. [Click]
We also performed system-level evaluation using the state-of-the-art SSD simulator, [Click] for three real-world applications that perform bulk bitwise operations on different numbers of operands. [Click]
We compared Flash-Cosmos against three baselines, a conventional system that uses a multi-core CPU, an in-storage processing system with an in-storage hardware accelerator, and a system that adopts the state-of-the-art in-flash processing mechanism to perform bulk bitwise operations. [Click]

## Slide 102: Results: Real-Device Characterization
No changes to the cell array
of commodity NAND flash chips
Can have many operands
(AND: up to 48, OR: up to 4)
with small increase in sensing latency (< 10%)
ESP significantly improves
the reliability of computation results
(no observed bit error in the tested flash cells)
Notes: Through our real-device characterization, we demnostrated that both MWS operations are possible without requiring any change ot the cell array of commodity NAND flash chips, [Click] and they can reliably activate multiple wordlines at the same time without significant increase in sensing latency. [Click]
We also observed no errors in the tested cells when we program data using ESP, which shows that Flash-Cosmos enables reliable in-flash bulk bitwise operations. [Click]

## Slide 103: Results: Performance & Energy
Speedup over OSP
Chart: 
| BMI | IMS | KCS | AVG
 | 1.3181 | 1.1935 | 1.3007 | 1.2794
 | 14.1649 | 2.9997 | 12.8867 | 9.2742
 | 198.4035 | 2.9998 | 25.8962 | 32.4204
ISP
ParaBit
Flash-Cosmos
Flash-Cosmos provides significant performance & energy benefits over all the baselines
The larger the number of operands,
the higher the performance & energy benefits
Chart: 
| BMI | IMS | KCS | AVG
ISP | 8.2558 | 5.4514 | 7.4777 | 7.1709
ParaBit | 49.449 | 8.7761 | 38.1762 | 29.1277
Flash-Cosmos | 582.8533 | 8.9811 | 76.5954 | 95.9386
Energy benefit over OSP
150×
14×
2.5×
20×
2×
70×
12×
1.6×
10×
2×
25×
3.5×
3.3×
13.4×
Notes: As system-level evaluation, [Click] we evaluate the speedup and [Click] energy benefit over the conventional system. [Click]
We observe that Flash-Cosmos provides significant performance and energy benefits over all the baselines, including the state-of-the-art in-flash bulk bitwise operation technique, [Click] and the larger the number of operands for bulk bitwise operations, the higher the performance and energy benefits that Flash-Cosmos can achieve over other computing platforms. [Click]

## Slide 104: In-Flash Bulk Bitwise Execution
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez-Luna, Myungsuk Kim, and Onur Mutlu, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (44 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.05566.pdf

## Slide 105: More to Come…

## Slide 106: Concluding Remarks

## Slide 107: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 108: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 109: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 110: We Need to Revisit the Entire Stack
With a storage-centric mindset
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 111
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 112: An Overview Paper
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/2012.03112.pdf

## Slide 113: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 114: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 115: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 116: SAFARI Newsletter June 2023 Edition
https://safari.ethz.ch/safari-newsletter-june-2023/

## Slide 117: SAFARI Newsletter July 2024 Edition
https://safari.ethz.ch/safari-newsletter-july-2024/

## Slide 118: PIM Tutorial November 2024 Edition
https://events.safari.ethz.ch/micro24-memorycentric-tutorial/
https://www.youtube.com/watch?v=KV2MXvcBgb0

## Slide 119: Storage-Centric Computing Enabling Fundamentally-Efficient Computers
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
1 December 2024
CCF China Storage Keynote Talk

## Slide 120: Backup Slides

## Slide 121: Processing in Memory: Two Types
1. Processing near Memory
2. Processing using Memory

## Slide 122: Processing using DRAM
We can support
  Bulk bitwise AND, OR, NOT, MAJ
  Bulk bitwise COPY and INIT/ZERO
  True Random Number Generation; Physical Unclonable Functions
  More complex computation using Lookup Tables
At low cost
Using analog computation capability of DRAM
  Idea: activating (multiple) rows performs computation
    Even in commodity off-the-shelf DRAM chips!
30X-257X performance and energy improvements
Seshadri+“RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
Hajinazar+, “SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM,” ASPLOS 2021.
Oliveira+, “MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Processing,” HPCA 2024.

## Slide 123: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 124: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 125: Real Processing-using-Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 126: Real Processing-using-Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 127: Microbenchmark Copy/Initialization Throughput
In-DRAM Copy and Initialization improve throughput by 119x and 89x
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 128: More on PiDRAM
Ataberk Olgun, Juan Gomez Luna, Konstantinos Kanellopoulos, Behzad Salami, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "PiDRAM: A Holistic End-to-end FPGA-based Framework for Processing-in-DRAM" ACM Transactions on Architecture and Code Optimization (TACO), March 2023. [arXiv version] Presented at the 18th HiPEAC Conference, Toulouse, France, January 2023. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (40 minutes)] [PiDRAM Source Code]

## Slide 129: DRAM Chips Are Already (Quite) Capable!
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18736.pdf

## Slide 130: The Capability of COTS DRAM Chips
130
We demonstrate that COTS DRAM chips:
Can copy one row into up to 31 other rows
with >99.98% success rate
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 131: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 132: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 133: We Need to Revisit the Entire Stack
With a memory-centric mindset
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 134: Concluding Remarks
We must design systems to be balanced, high-performance, energy-efficient (all at the same time)  intelligent systems
  Data-centric, data-driven, data-aware
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Future of truly memory-centric computing is bright
  We need to do research & design across the computing stack
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 135: We Need to Revisit the Entire Stack
With a data-centric mindset
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 136: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
NSF
NIH
GSRC
SRC
CyLab
EFCL
SNSF
ACCESS
Thank you!