## Slide 1: Machine Learning Driven Memory and Storage Systems
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
19 December 2023
IBM Research

## Slide 2: The Problem
Computing
is Bottlenecked by Data

## Slide 3: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process
  We need to perform more sophisticated analyses on more data

## Slide 4: Data is Key for Modern Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 5: Huge Demand for Performance & Efficiency
Source: https://youtu.be/Bh13Idwcb0Q?t=283

## Slide 6: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 7
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Modern Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 8
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 9
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 10: Data Movement Overwhelms Accelerators
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models

## Slide 11: Axiom
An Intelligent Architecture
Handles Data Well

## Slide 12: How to Handle Data Well
Ensure data does not overwhelm the components
  via intelligent algorithms, architectures & system designs: algorithm-architecture-devices
Take advantage of vast amounts of data and metadata
  to improve architectural & system-level decisions
Understand and exploit properties of (different) data
  to improve algorithms & architectures in various metrics

## Slide 13: Corollaries: Computing Systems Today …
Are processor-centric vs. data-centric
Make designer-dictated decisions vs. data-driven
Make component-based myopic decisions vs. data-aware

## Slide 14: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 15: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 16: A Blueprint for Fundamentally Better Architectures
Onur Mutlu, "Intelligent Architectures for Intelligent Computing Systems" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Virtual, February 2021. [Slides (pptx) (pdf)] [IEDM Tutorial Slides (pptx) (pdf)] [Short DATE Talk Video (11 minutes)] [Longer IEDM Tutorial Video (1 hr 51 minutes)]

## Slide 17: Data-Driven (Self-Optimizing) Architectures

## Slide 18: System Architecture Design Today
Human-driven
  Humans design the policies (how to do things)
Many (too) simple, short-sighted policies all over the system
No automatic data-driven policy learning
(Almost) no learning: cannot take lessons from past actions
Can we design
fundamentally intelligent architectures?

## Slide 19: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
We need to rethink design
(of all controllers)

## Slide 20: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 21: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2109.12021.pdf

## Slide 22: Learning-Based Off-Chip Load Predictors
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 23: Self-Optimizing Hybrid SSD Controllers
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 24: Self Optimizing Memory Controllers

## Slide 25: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 26: DRAM Controllers Difficult to Design
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to manage power consumption
Need to optimize performance & QoS (in the presence of constraints)
  Reordering is not simple
  Fairness and QoS needs complicates the scheduling problem

## Slide 27: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 28: More on DRAM Operation
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 29: Why So Many Timing Constraints? (I)
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.

## Slide 30: Why So Many Timing Constraints? (II)
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 31: DRAM Controller Design Is Becoming More Difficult
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 32: Reality and Dream
Reality: It is difficult to design a policy that maximizes performance, QoS, energy-efficiency, …
  Too many things to think about
  Continuously changing workload and system behavior
Dream: Wouldn’t it be nice if the DRAM controller automatically found a good scheduling policy on its own?

## Slide 33: Memory Controller: Performance Function
How to schedule requests to maximize system performance?
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 34: Self-Optimizing DRAM Controllers
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.
Problem: DRAM controllers are difficult to design
  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: A memory controller that adapts its scheduling policy to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent
  It dynamically and continuously learns and employs the best scheduling policy to maximize long-term performance.

## Slide 35: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.
Goal: Learn to choose actions to maximize r0 + r1 + 2r2 + … ( 0   < 1)

## Slide 36: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 37: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 38: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize long-term data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 39: Performance Results
Large, robust performance improvements over many human-designed policies

## Slide 40: Self Optimizing DRAM Controllers
+ Continuous learning in the presence of changing environment
+ Reduced designer burden in finding a good scheduling policy. Designer specifies:
1) What system variables might be useful
2) What target to optimize, but not how to optimize it
-- How to specify different objectives? (e.g., fairness, QoS, …)
-- Hardware complexity?
-- Design mindset and flow

## Slide 41: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 42: Pythia: Prefetching using Reinforcement Learning

## Slide 43: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2109.12021.pdf

## Slide 44
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
https://github.com/CMU-SAFARI/Pythia
https://arxiv.org/pdf/2109.12021.pdf
Notes: Hi I am Rahul. Today, I’m going to present our work “…”
This work is done by researchers from SAFARI research group at ETH Zurich, in collaboration with Intel Labs and TU Delft.

## Slide 45: Executive Summary
https://github.com/CMU-SAFARI/Pythia
Background: Prefetchers predict addresses of future memory requests by associating memory access patterns with pieces of program and system information (called feature)
Problem: Three key shortcomings of prior prefetchers:
  Predict mainly using a single program feature
  Lack inherent system awareness (e.g., memory bandwidth usage)
  Lack in-silicon customizability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized in silicon to use different features and/or prefetching objectives
Contribution: Pythia, which formulates prefetching as reinforcement learning problem
  Takes adaptive prefetch decisions using multiple features and system-level feedback
  Can be customized in silicon for target workloads via simple configuration registers
  Proposes a realistic and practical implementation of RL algorithm in hardware
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms best prefetcher by 3.4%, 7.7% and 17% in 1/4/bw-constrained cores
  Customizing Pythia leads to up to 7.8% more performance over basic Pythia across Ligra workloads
Notes: First, I am going to start with an executive summary.
[CLICK] Prefetching is a speculative technique that predicts address of future memory requests by associating patterns in memory addresses with some program context. We call this context a feature.
[CLICK] We observe three key shortcomings in prior prefetchers:
First, they mainly use a single program feature for prediction.
Second, they lack inherent system awareness
Third, they also lack any customizability in silicon
[CLICK] Our goal in this work is to design a prefetching framework that
– can learn from multiple program features and inherent system-level feedback
-- and can be customized in silicon to change the features or the objective of the prefetcher
[CLICK] Towards this we propose Pythia, that formulates …
Pythia makes adaptive and autonomous …
Pythia also proposes a realistic and practical …
[CLICK] We extensively evaluate Pythia using …
We show that Pythia outperforms prior state-of-the-art …
Pythia is freely available in our GitHub repository.

## Slide 46: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia: Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: This is the outline of my talk.
First, I am going to start by discussing key shortcomings of prior prefetchers.

## Slide 47: Prefetching Basics
Predicts addresses of long-latency memory requests and fetches data before the program demands it
Associates access patterns from past memory requests with program context or system information
Example program features
  Program counter (PC)
  Page number
  Page offset
  Cacheline delta
  …
  Or a combination of these attributes
Program context  Access Pattern
Program Feature
Notes: Prefetching is a speculative technique that predicts …
[CLICK] To predict addresses, a prefetcher typically associates …
[CLICK] We call these context information as program feature.
[CLICK] Some examples of program features are … or any combination of these information

## Slide 48: Key Shortcomings in Prior Prefetchers
We observe three key shortcomings that significantly limit performance benefits of prior prefetchers
Predict mainly using a single program feature
Lack inherent system awareness
Lack in-silicon customizability
1
2
3
Notes: We observe three key shortcomings in prior prefetchers that significantly limits their performance improvement
[CLICK] First, they predict mainly …
[CLICK] Second, they lack any inherent …
[CLICK] Third, the also lack any online in-silicon customizability
Let’s take a closer look at each of these shortcomings.
[NEXT]

## Slide 49: (1) Single-Feature Prefetch Prediction
Provides good performance gains mainly on workloads where the feature-to-pattern correlation exists
[1] Bakshalipour et al., HPCA’19
[2] Kim et al., MICRO’16
Chart: IPC improvement over baseline (%)
| 482.sphinx3-417B | PARSEC-Canneal | PARSEC-Facesim | 459.GemsFDTD-765B
SPP | 0.25977 | 0.028455 | 0.11952 | 0.38946
Bingo | 0.41337 | 0.063762 | 0.17478 | 0.3437
Pythia | 0.50416 | 0.077957 | 0.17503 | 0.40433
15.4%
3.5%
5.5%
4.6%
Bingo [1] performs better
SPP [2] performs better
Notes: Due to the use of a single program feature for prefetch prediction, a prefetcher typically provides performance benefits …
In other types of workloads, the same prefetcher fails to provide performance gains.
To illustrate this [CLICK], we show the coverage, overprediction, and performance improvement of two prior prefetchers SPP and Bingo for six sample workloads.
The top figure shows …
The bottom figure shows …
As we can see, for workloads like [CLICK], … Bingo performs better than SPP, as the program feature exploited by Bingo has stronger correlation with the access pattern than SPP.
On the other hand, for workloads like … [CLICK], SPP’s program feature provides better correlation, and thus performs better than Bingo.

## Slide 50: (1) Single-Feature Prefetch Prediction
Provides good performance gains mainly on workloads where the feature-to-pattern correlation exists
[1] Bakshalipour et al., HPCA’19
[2] Kim et al., MICRO’16
Chart: IPC improvement over baseline (%)
| 482.sphinx3-417B | PARSEC-Canneal | PARSEC-Facesim | 459.GemsFDTD-765B
SPP | 0.25977 | 0.028455 | 0.11952 | 0.38946
Bingo | 0.41337 | 0.063762 | 0.17478 | 0.3437
Pythia | 0.50416 | 0.077957 | 0.17503 | 0.40433
15.4%
3.5%
5.5%
4.6%
Bingo [1] performs better
SPP [2] performs better
Relying on a single feature for prediction leaves significant performance improvement on table
Notes: Due to the use of a single program feature for prefetch prediction, a prefetcher typically provides performance benefits …
In other types of workloads, the same prefetcher fails to provide performance gains.
To illustrate this [CLICK], we show the coverage, overprediction, and performance improvement of two prior prefetchers SPP and Bingo for six sample workloads.
The top figure shows …
The bottom figure shows …
As we can see, for workloads like [CLICK], … Bingo performs better than SPP, as the program feature exploited by Bingo has stronger correlation with the access pattern than SPP.
On the other hand, for workloads like … [CLICK], SPP’s program feature provides better correlation, and thus performs better than Bingo.

## Slide 51: (2) Lack of Inherent System Awareness
Little understanding of undesirable effects (e.g., memory bandwidth usage, cache pollution, …)
  Performance loss in resource-constrained configurations
Chart: Fraction of LLC misses
| SPP | Bingo | Pythia | SPP | Bingo | Pythia | Ligra-CC | PARSEC-Canneal
Covered | 0.050822 | 0.22755 | 0.24042 | 0.15097 | 0.27515 | 0.31283
Uncovered | 0.94918 | 0.77245 | 0.75958 | 0.84903 | 0.72485 | 0.68717
Overpredicted | 0.31635 | 2.6825 | 0.57152 | 0.55316 | 4.7397 | 0.27171
Chart: IPC improvement over baseline (%)
| Ligra-CC | PARSEC-Canneal
SPP | 0.028046 | 0.028455
Bingo | -0.018714 | 0.063762
Pythia | 0.069103 | 0.077957
368%
574%
Similar coverage
Lower overpredictions
Yet, lower performance
Notes: The second shortcoming is that, all prior prefetchers have …, which often leads to …
To illustrate this, let revisit the previous figure and focus on Bingo’s performance in PARSEC-Canneal and Ligra-CC.
Bingo in Ligra-CC has similar coverage to PARSEC-Canneal with significantly …
The reason is that, in baseline without prefetching, Ligra-CC consumes much higher main memory …
As a result, even a smaller amount of overprediction hurts more performance in Ligra-CC than in PARSEC-Canneal.
This is only happening as Bingo does not take its undesirable effects into account while prefetching.
Thus the key takeaway is that, [CLICK] …

## Slide 52: (2) Lack of Inherent System Awareness
Little understanding of undesirable effects (e.g., memory bandwidth usage, cache pollution, …)
  Performance loss in resource-constrained configurations
Chart: Fraction of LLC misses
| SPP | Bingo | Pythia | SPP | Bingo | Pythia | Ligra-CC | PARSEC-Canneal
Covered | 0.050822 | 0.22755 | 0.24042 | 0.15097 | 0.27515 | 0.31283
Uncovered | 0.94918 | 0.77245 | 0.75958 | 0.84903 | 0.72485 | 0.68717
Overpredicted | 0.31635 | 2.6825 | 0.57152 | 0.55316 | 4.7397 | 0.27171
Chart: IPC improvement over baseline (%)
| Ligra-CC | PARSEC-Canneal
SPP | 0.028046 | 0.028455
Bingo | -0.018714 | 0.063762
Pythia | 0.069103 | 0.077957
368%
574%
Similar coverage
Lower overpredictions
Yet, lower performance
Prefetchers often lose performance due to lack of inherent system awareness
Notes: The second shortcoming is that, all prior prefetchers have …, which often leads to …
To illustrate this, let revisit the previous figure and focus on Bingo’s performance in PARSEC-Canneal and Ligra-CC.
Bingo in Ligra-CC has similar coverage to PARSEC-Canneal with significantly …
The reason is that, in baseline without prefetching, Ligra-CC consumes much higher main memory …
As a result, even a smaller amount of overprediction hurts more performance in Ligra-CC than in PARSEC-Canneal.
This is only happening as Bingo does not take its undesirable effects into account while prefetching.
Thus the key takeaway is that, [CLICK] …

## Slide 53: (3) Lack of In-silicon Customizability
Feature statically selected at design time
  Rigid hardware designed specifically to exploit that feature
No way to change program feature and/or change prefetcher’s objective in silicon
  Cannot adapt to a wide range of workload demands
Design from scratch
Verify
Fabricate
Notes: The third key shortcoming is that, all prior prefetcher lack in-silicon customizability.
These prefetchers statically selects the feature to exploit at design time and design a rigid hardware to specifically …
[CLICK] There is no way …
In order to exploit a new program feature, architects need to design a prefetcher from scratch …
[CLICK] and this cycle goes on for every new prefetcher. This wastes precious design time and human resource.

## Slide 54: Our Goal
A prefetching framework that can:
Learn to prefetch using multiple features and inherent system-level feedback information
Be easily customized in silicon to use different features and/or change prefetcher’s objectives
Notes: So our goal in this work is to … that
[CLICK] …
[CLICK] …

## Slide 55: Our Proposal
Pythia
Formulates prefetching as a reinforcement learning problem
Pythia is named after the oracle of Delphi, who is known for her accurate prophecies
https://en.wikipedia.org/wiki/Pythia

## Slide 56: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia: Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: To this end, we propose Pythia, which formulates …

## Slide 57: Basics of Reinforcement Learning (RL)
Algorithmic approach to learn to take an action in a given situation to maximize a numerical reward
Agent stores Q-values for every state-action pair
  Expected return for taking an action in a state
  Given a state, selects action that provides highest Q-value
Notes: First, let me briefly describe the basics of reinforcement learning.
Reinforcement learning, in its simplest form, is the ...
A RL system contains two components: [CLICK] the agent and the environment.
The agent observes the state of the environment in every timestep [CLICK], takes an action based on the state [CLICK], and receives a reward for that action [CLICK].
[CLICK] The agent stores …
Given a state, the agent …

## Slide 58: Formulating Prefetching as RL
Notes: In Pythia, we formulate prefetching as a reinforcement learning problem.
[CLICK] The prefetcher acts as the agent, while [CLICK] the processor and memory subsystem acts as the environment.
[CLICK] Pythia extracts the program features from every demand request and use it as a state information to take a prefetch action [CLICK]
[CLICK] For every prefetch action, Pythia receives a numerical reward that evaluates the usefulness of the prefetch request, while considering various system-level feedbacks.
Not let’s concretely define the state, action, and the reward for Pythia.

## Slide 59: What is State?
k-dimensional vector of features
Feature = control-flow + data-flow
Control-flow examples
  PC
  Branch PC
  Last-3 PCs, …
Data-flow examples
  Cacheline address
  Physical page number
  Delta between two cacheline addresses
  Last 4 deltas, …
Notes: We define the state as a k-dimensional vector of program features.
[CLICK] Each feature is composed of …
[CLICK] Some examples of control-flow information are …
[CLICK] Some examples of data-flow information are …
Though Pythia can theoretically learn from any number of such program features, we limit the size k as per storage budget.

## Slide 60: What is State?
S = {PC+Delta, Sequence of last-4 deltas}
Example of a state information
Feature-1 (ɸ1)
Feature-2 (ɸ2)
PC
(Control-flow info.)
Cacheline Delta
(Data-flow info.)
Seq. of last-4 deltas
(Data-flow info.)
Notes: We define the state as a k-dimensional vector of program features.
[CLICK] Each feature is composed of …
[CLICK] Some examples of control-flow information are …
[CLICK] Some examples of data-flow information are …
Though Pythia can theoretically learn from any number of such program features, we limit the size k as per storage budget.

## Slide 61: What is Action?
Given a demand access to address A
the action is to select prefetch offset “O”
Action-space: 127 actions in the range [-63, +63]
  For a machine with 4KB page and 64B cacheline
Upper and lower limits ensure prefetches do not cross physical page boundary
A zero offset means no prefetch is generated
We further prune action-space by design-space exploration
Notes: We define the action as the selection of a prefetch offset. Pythia adds this offset to the demanded cacheline to get the prefetched cacheline address.
[CLICK] Note that a zero offset is also a valid action for Pythia, which means no prefetch is generated.
[CLICK] As every post-L1 prefetcher …, the list of actions are limited to the range from -63 to +63 for a traditionally-sized …
[CLICK] However, we can prune the action list by automatic design-space exploration, as we show in the paper.

## Slide 62: What is Reward?
Defines the objective of Pythia
Encapsulates two metrics:
  Prefetch usefulness (e.g., accurate, late, out-of-page, …)
  System-level feedback (e.g., mem. b/w usage, cache pollution, energy, …)
We demonstrate Pythia with memory bandwidth usage as the system-level feedback in the paper
Notes: The reward defines the objective of Pythia
[CLICK] A reward encapsulates two metrics: …
[CLICK] Though Pythia can learn from any …, in this paper we demonstrate Pythia using a major system-level feedback: mem b/w usage

## Slide 63: What is Reward?
Seven distinct reward levels
  Accurate and timely (RAT)
  Accurate but late (RAL)
  Loss of coverage (RCL)
  Inaccurate
    With low memory b/w usage (RIN-L)
    With high memory b/w usage (RIN-H)
  No-prefetch
    With low memory b/w usage (RNP-L)
    With high memory b/w usage(RNP-H)
Values are set at design time via automatic design-space exploration
  Can be customized further in silicon for higher performance
Notes: We define reward in five distinct levels mentioned as follows [CLICK].
Each reward level corresponds to various usefulness of a prefetch request. The inaccurate and no-prefetch reward levels are further categorized based on the system memory bandwidth usage.
[CLICK] The values of each of these reward levels are set at design time via automatic design-space exploration.
[CLICK] However, one can customize the rewards in silicon via simple configuration registers to specify a dfferent objective for Pythia for extracting higher performance benefits in target workload suites.

## Slide 64: Steering Pythia’s Objective via Reward Values
Example reward configuration for
  Generating accurate prefetches
  Making bandwidth-aware prefetch decisions
+20
+12
-2
-4
-8
-14
RAT
RAL
RNP-H
RNP-L
RIN-L
RIN-H
AT = Accurate & timely; AL = Accurate & late; NP = No-prefetching; IN = Inaccurate;
H = High mem. b/w; L = Low mem. b/w
Highly prefers to generate accurate prefetches
Prefers not to prefetch if memory bandwidth usage is low
Strongly prefers not to prefetch if memory bandwidth usage is high
1
2
3
Notes: Now, let’s take a concrete example of reward values and how they specify the objectives for Pythia.
[CLICK] These are the reward level values in basic Pythia configuration.
Pythia sets three key objectives for prefetching by this reward configuration.
[CLICK] First, we provide much higher perks to Pythia for prefetching accurately, either timely or untimely. Thus, Pythia prefers to generate accurate prefetches.
[CLICK] Second, in case of low memory bandwidth usage, Pythia has higher perks in no prefetching, rather that prefetching inaccurately.
Thus, if the memory bandwidth usage is low, Pythia prefers not to prefetch, rather than prefetching inaccurately.
[CLICK] Third, in case of high memory bandwidth usage, Pythia has much higher perks in no prefetching than prefetching accurately.
Thus, if the memory bandwidth usage is low, Pythia strongly prefers not to prefetch, rather than prefetching inaccurately.
[] Let’s take a look at a reward values to steer Pythia to generate accurate prefetches and make fine-tuned decisions based on b/w usage.

## Slide 65: Steering Pythia’s Objective via Reward Values
Customizing reward values to make Pythia conservative towards prefetching
+20
+12
+2
+1
-20
-22
RAT
RAL
RNP-H
RNP-L
RIN-L
RIN-H
AT = Accurate & timely; AL = Accurate & late; NP = No-prefetching; IN = Inaccurate;
H = High mem. b/w; L = Low mem. b/w
Highly prefers to generate accurate prefetches
1
Otherwise prefers not to prefetch
2
Notes: Now, if we increase the reward for no prefetching while significantly decreasing the rewards for inaccurate prefetching, we set a different prefetching objective for Pythia.
[CLICK] We still provide much higher perks for prefetching accurately. Thus Pythia strives to generate accurate prefetches.
[CLICK] Otherwise, we provide much higher perks for no prefetching as compared to inaccurate prefetching, irrespective of the memory bandwidth usage. Thus, Pythia becomes conservative and simply do not prefetch at all.
This is particularly useful if we are repurposing Pythia for server-class processors which have modest per-core memory bandwidth
or workloads like Ligra whose performance improvement is sensitive to memory bandwidth usage.

## Slide 66: Steering Pythia’s Objective via Reward Values
Customizing reward values to make Pythia conservative towards prefetching
+20
+12
+4
+2
-20
-22
RAT
RAL
RNP-H
RNP-L
RIN-L
RIN-H
AT = Accurate & timely; AL = Accurate & late; NP = No-prefetching; IN = Inaccurate;
H = High mem. b/w; L = Low mem. b/w
Highly prefers to generate accurate prefetches
1
Otherwise prefers not to prefetch
2
Server-class processors
Bandwidth-sensitive workloads
Strict Pythia configuration
Notes: Now, if we increase the reward for no prefetching while significantly decreasing the rewards for inaccurate prefetching, we set a different prefetching objective for Pythia.
[CLICK] We still provide much higher perks for prefetching accurately. Thus Pythia strives to generate accurate prefetches.
[CLICK] Otherwise, we provide much higher perks for no prefetching as compared to inaccurate prefetching, irrespective of the memory bandwidth usage. Thus, Pythia becomes conservative and simply do not prefetch at all.
This is particularly useful if we are repurposing Pythia for server-class processors which have modest per-core memory bandwidth
or workloads like Ligra whose performance improvement is sensitive to memory bandwidth usage.

## Slide 67: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia: Overview
Evaluation of Pythia and Key Results
Conclusion
Notes: We now provide a brief overview and design of Pythia.

## Slide 68: Pythia Overview
Q-Value Store: Records Q-values for all state-action pairs
Evaluation Queue: A FIFO queue of recently-taken actions
Evaluation Queue (EQ)
Demand Request
1
Assign reward to
corresponding EQ entry
Look up
QVStore
State
Vector
Q-Value Store
(QVStore)
2
3
5
Insert prefetch action &
State-Action pair in EQ
6
Prefetch Fill
A1
A2
A3
Memory
Hierarchy
Generate
prefetch
Evict EQ entry and update QVStore
4
Find the Action with max Q-Value
7
S1
S2
S3
S4
Set filled bit
Max
Notes: Pythia consists of two key components:
[CLICK] Q-value store, which is responsible for …
[CLICK] Evaluation queue, which is a first-in-first-out queue that stores the recently taken action.
As Pythia cannot always immediately assign a reward to a taken action
because the usefulness of the corresponding prefetch request is known, Pythia stores the action
in evaluation queue to properly assign rewards to them.
[CLICK] For every demand request, Pythia first checks EQ with deamdned address. If a matching entry is found in EQ, it means the corresponding action in EQ entry has generated a useful prefetch, and Pythia assigns a reward accordingly.
[CLICK] Then Pythia extracts features from the attributes of the demand request to create the state-vector and uses the state-vector to lookup QVStore [CLICK]
[CLICK] For the given state-vector, Pythia finds the action that has the highest Q-value and generates prefetch request accordingly to the memory hierarchy [CLICK]
[CLICK] Next, Pythia inserts the action in the EQ along with the state-action pair.
[CLICK] Pythia uses the reward stored in the evicted EQ entry to update the QVStore.

## Slide 69: Architecting QVStore
S = {PC+Delta,
Sequence of last-4 deltas}
+1
+2
+3
Q-Value Store
(QVStore)
…
Notes: Now let’s take a closer look at how Pythia makes a prefetch prediction.
For every prefetch prediction, Pythia has to look up the QVStore using the state vector, [CLICK] for example, a vector of features: PC+Delta, and seq. of last-4 deltas.
For the given state-vector, Pythia has to retrieve the Q-value for each prefetch action, e.g., [CLICK] prefetch offsets +1, +2, +3 and so on, to find the action that has the maximum Q-value.
Thus, it is necessary to store all state-action Q-values in an efficient way for a fast Q-value retrieval.

## Slide 70: Architecting the QVStore
S = {PC+Delta,
Sequence of last-4 deltas}
+1
+2
+3
Q-Value Store
(QVStore)
…
Fast retrieval of Q-values from QVStore
Efficient storage organization of Q-values in QVStore
Fast prefetch prediction
Notes: Now let’s see an example of how QVStore works.
For every prefetch decision, Pythia looks up the QVStore using the state vector, which in this case …
For the state-vector, Pythia retrieves the Q-value for each prefetch action, e.g., +1, +2, +3 ... to find the action that has the maximum Q-value.
Thus, it is necessary to store all state-action Q-values in an efficient way for a fast Q-value retrieval.

## Slide 71: Organization of QVStore
A monolithic two-dimensional table?
  Indexed by state and action values
State-space increases exponentially with #bits
S = {PC+Delta, Sequence of last-4 deltas}
32b
7b
4x7b
= 67 bits
+
+
 | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9
S1 |  |  |  |  |  |  |  |  | 
S2 |  |  |  |  |  |  |  |  | 
S3 |  |  |  |  |  |  |  |  | 
S4 |  |  |  |  |  |  |  |  | 
S5 |  |  |  |  |  |  |  |  | 
S6 |  |  |  |  |  |  |  |  | 
S7 |  |  |  |  |  |  |  |  | 
Design complexity
Access latency
127 actions
267 states
Notes: [CLICK] Now, a naïve choice for designing the QVStore is to organize as a monolithic two-dimensional table, which is indexed by the state and the action values
[CLICK] However, the state-space increases exponentially with the number of bits used to represent the state.
[CLICK] As you can see, the state information considered in our example requires 67 bits to represent
[CLICK] Which requires an impractically-sized monolithic table to store Q-values for every state-action pairs.
[CLICK] but also significantly increases the access latency.

## Slide 72: Organization of QVStore
We partition QVStore into k vaults [k = number of features in state]
  Each vault corresponds to one feature and stores the Q-values of feature-action pairs
Query each vault in parallel with feature and action
Retrieve feature-action Q-value from each vault
Compute MAX of all feature-action Q-values
MAX ensures the Q(S,A) is driven by the constituent feature that has highest Q(ɸ,A)
To retrieve Q(S,A) for each action
Notes: [CLICK] Thus, we partition the QVStore into k vaults, where k is the number of features in a state information
[CLICK] Each vault corresponds to …
[CLICK] To retrieve the Q-value of a state-action pair …
[CLICK] We do this…
[CLICK] Then we do this …
[CLICK] Then we do this …
[CLICK] The maximum operation ensures that …

## Slide 73: Organization of QVStore
We further partition each vault into multiple planes
  Each plane stores a partial Q-value of a feature-action pair
Query each plane in parallel with hashed feature and action
Retrieve partial feature-action Q-value from each plane
Compute SUM of all partial feature-action Q-values
To retrieve Q(ɸ,A) for each action
Notes: [CLICK] We further partition …
[CLICK] Where each plane stores …
[CLICK] To retrieve the feature-action Q-value,
[CLICK] We query each plane …
[CLICK] We retrieve the partial Q-value from each plane
[CLICK] and finally compute a sum …

## Slide 74: Organization of QVStore
We further partition each vault into multiple planes
  Each plane stores a partial Q-value of a feature-action pair
Query each plane in parallel with hashed feature and action
Retrieve partial feature-action Q-value from each plane
Compute SUM of all parital feature-action Q-values
To retrieve Q(ɸ,A) for each action
1. Enables sharing of partial Q-values between similar feature values, shortens prefetcher training time
2. Reduces chances of sharing partial Q-values
across widely different feature values
Notes: [CLICK] We further partition …
[CLICK] Where each plane stores …
[CLICK] To retrieve the feature-action Q-value,
[CLICK] We query each plane …
[CLICK] We retrieve the partial Q-value from each plane
[CLICK] and finally compute a sum …

## Slide 75: More in the Paper
Pipelined search operation for QVStore
Reward assignment and QVStore update
Automatic design-space exploration
  Feature types
  Actions
  Reward and Hyperparameter values
Notes: We have much more detailed description of Pythia’s design in our paper including …

## Slide 76: More in the Paper
Pipelined search operation for QVStore
Reward assignment and QVStore update
Automatic design-space exploration
  Feature types
  Action
  Reward and Hyperparameter values
https://arxiv.org/pdf/2109.12021.pdf
Notes: We have much more detailed description of Pythia’s design in our paper including …

## Slide 77: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia: Overview
Evaluation of Pythia and Key Results
Conclusion

## Slide 78: Simulation Methodology
Champsim [3] trace-driven simulator
150 single-core memory-intensive workload traces
  SPEC CPU2006 and CPU2017
  PARSEC 2.1
  Ligra
  Cloudsuite
Homogeneous and heterogeneous multi-core mixes
Five state-of-the-art prefetchers
  SPP [Kim+, MICRO’16]
  Bingo [Bakhshalipour+, HPCA’19]
  MLOP [Shakerinava+, 3rd Prefetching Championship, 2019]
  SPP+DSPatch [Bera+, MICRO’19]
  SPP+PPF [Bhatia+, ISCA’20]
[3] https://github.com/ChampSim/ChampSim

## Slide 79: Basic Pythia Configuration
Derived from automatic design-space exploration
State: 2 features
  PC+Delta
  Sequence of last-4 deltas
Actions: 16 prefetch offsets
  Ranging between -6 to +32. Including 0.
Rewards:
  RAT = +20; RAL = +12; RNP-H=-2; RNP-L=-4;
  RIN-H=-14; RIN-L=-8; RCL=-12
Notes: This is the basic Pythia configuration that we are going to evaluate, which is derived from the automatic design-space exploration.

## Slide 80: List of Evaluated Features

## Slide 81: Basic Pythia Configuration

## Slide 82: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
3.4%
7.7%

## Slide 83: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
3.4%
7.7%
1. Pythia consistently provides the highest performance in all core configurations
2. Pythia’s gain increases with core count

## Slide 84: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%

## Slide 85: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%
Pythia outperforms prior best prefetchers for
a wide range of DRAM bandwidth configurations

## Slide 86: Performance Improvement via Customization
Reward value customization
Strict Pythia configuration
  Increase the rewards for no prefetching
  Decrease the rewards for inaccurate prefetching
Strict Pythia is more conservative in generating prefetch requests than the basic Pythia
Evaluate on all Ligra graph processing workloads
Notes: Next, we analyze performance improvement of Pythia via customization.
[CLICK] We show an example of reward value customization, where,
[CLICK] We devise a strict Pythia configuration by increasing the reward level values for no prefetching, while decreasing the rewards values for inaccurate prefetching.
In short, strict Pythia is more conservative than the basic Pythia and strongly prefers not to prefetch, rather than prefetching inaccurately.
We evaluate both basic Pythia and strict Pythia on Ligra workload suite.

## Slide 87: Performance Improvement via Customization
Chart: IPC normalized to no prefetching
| PageRank | PageRankDelta | CC | BFS | BC | GEOMEAN
Basic Pythia | 1.0037 | 1.0598 | 1.07 | 1.5271 | 1.907 | 1.2708
Strict Pythia | 1.0341 | 1.0877 | 1.1036 | 1.6052 | 1.9593 | 1.3131
3.1%
2.8%
3.4%
7.8%
5.2%
2%
Notes: [CLICK] As you can see, strict Pythia outperforms the basic Pythia configuration as much as 7.8% and
[CLICK] 2% on average over the entire Ligra workload suite.

## Slide 88: Performance Improvement via Customization
Chart: IPC normalized to no prefetching
| PageRank | PageRankDelta | CC | BFS | BC | GEOMEAN
Basic Pythia | 1.0037 | 1.0598 | 1.07 | 1.5271 | 1.907 | 1.2708
Strict Pythia | 1.0341 | 1.0877 | 1.1036 | 1.6052 | 1.9593 | 1.3131
3.1%
2.8%
3.4%
7.8%
5.2%
2%
Pythia can extract even higher performance via customization without changing hardware
Notes: [CLICK] As you can see, strict Pythia outperforms the basic Pythia configuration as much as 7.8% and
[CLICK] 2% on average over the entire Ligra workload suite.

## Slide 89: Pythia’s Overhead
25.5 KB of total metadata storage per core
  Only simple tables
We also model functionally-accurate Pythia with full complexity in Chisel [4] HDL
1.03% area overhead
Satisfies prediction latency
0.4% power overhead
of a desktop-class 4-core Skylake processor (Xeon D2132IT, 60W)
[4] https://www.chisel-lang.org
Notes: All of Pythia’s performance benefits comes at a modest cost of 25.5KB of metadata storge, which is invested only in simple storage, without any need to complex structures.
[CLICK] We also model a fully-functionally-accurate Pythia with its full complexity in Chisel and show that, Pythia incurs
[CLICK] a modest area overhead of 1.03%
[CLICK] a power overhead of half-a-percent
[CLICK] while simultaneously satisfying the prediction latency at L2 cache frequency
Of a desktop-class …

## Slide 90: More in the Paper
Performance comparison with unseen traces
  Pythia provides equally high performance benefits
Comparison against multi-level prefetchers
  Pythia outperforms prior best multi-level prefetchers
Understanding Pythia’s learning with a case study
  We reason towards the correctness of Pythia’s decision
Performance sensitivity towards different features and hyperparameter values
Detailed single-core and four-core performance
Notes: We have many more exciting results including, ….
We encourage everyone to read it.

## Slide 91: Performance on Previously-Unseen Workloads
Evaluated with 500 traces from value prediction championship
  No prefetcher has been trained on these traces
Pythia outperforms MLOP and Bingo by
8.3% and 3.5% in single-core
And 9.7% and 5.4% in four-core

## Slide 92: More in the Paper
Performance comparison with unseen traces
  Pythia provides equally high performance benefits
Comparison against multi-level prefetchers
  Pythia outperforms prior best multi-level prefetchers
Understanding Pythia’s learning with a case study
  We reason towards the correctness of Pythia’s decision
Performance sensitivity towards different features and hyperparameter values
Detailed single-core and four-core performance
https://arxiv.org/pdf/2109.12021.pdf
Notes: We have many more exciting results including, ….
We encourage everyone to read it.

## Slide 93: Pythia is Open Source
https://github.com/CMU-SAFARI/Pythia
MICRO’21 artifact evaluated
Champsim source code + Chisel modeling code
All traces used for evaluation

## Slide 94: Talk Outline
Key Shortcomings of Prior Prefetchers
Formulating Prefetching as Reinforcement Learning
Pythia: Overview
Evaluation of Pythia and Key Results
Conclusion

## Slide 95: Executive Summary
https://github.com/CMU-SAFARI/Pythia
Background: Prefetchers predict addresses of future memory requests by associating memory access patterns with pieces of program and system information (called feature)
Problem: Three key shortcomings of prior prefetchers:
  Predict mainly using a single program feature
  Lack inherent system awareness (e.g., memory bandwidth usage)
  Lack in-silicon customizability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized in silicon to use different features and/or prefetching objectives
Contribution: Pythia, which formulates prefetching as reinforcement learning problem
  Takes adaptive prefetch decisions using multiple features and system-level feedback
  Can be customized in silicon for target workloads via simple configuration registers
  Proposes a realistic and practical implementation of RL algorithm in hardware
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms best prefetcher by 3.4%, 7.7% and 17% in 1/4/bw-constrained cores
  Customizing Pythia leads to up to 7.8% more performance over basic Pythia across Ligra workloads
Notes: First, I am going to start with an executive summary.
[CLICK] Prefetching is a speculative technique that predicts address of future memory requests by associating patterns in memory addresses with some program context. We call this context a feature.
[CLICK] We observe three key shortcomings in prior prefetchers:
First, they mainly use a single program feature for prediction.
Second, they lack inherent system awareness
Third, they also lack any customizability in silicon
[CLICK] Our goal in this work is to design a prefetching framework that
– can learn from multiple program features and inherent system-level feedback
-- and can be customized in silicon to change the features or the objective of the prefetcher
[CLICK] Towards this we propose Pythia, that formulates …
Pythia makes adaptive and autonomous …
Pythia also proposes a realistic and practical …
[CLICK] We extensively evaluate Pythia using …
We show that Pythia outperforms prior state-of-the-art …
Pythia is freely available in our GitHub repository.

## Slide 96
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
https://github.com/CMU-SAFARI/Pythia
https://arxiv.org/pdf/2109.12021.pdf
Notes: Hi I am Rahul. Today, I’m going to present our work “…”
This work is done by researchers from SAFARI research group at ETH Zurich, in collaboration with Intel Labs and TU Delft.

## Slide 97: Pythia Discussion
FAQs
  Why RL?
  What about large page?
  What’s the prefetch degree?
  Can customization happen during workload execution?
  Can runtime mixing create problem?
Simulation and Methodology
  Basic Pythia configuration
  System parameters
  Configuration of prefetchers
  Evaluated workloads
  Feature selection
Detailed Design
  Reward structure
  Design overview
  QVStore Organization
More Results
  Comparison against other adaptive prefetchers
  Comparison against Context prefetcher
  Feature combination sensitivity
  Hyperparameter sensitivity
  Comparison with multi-level prefetchers
  Performance in unseen workloads
  Single-core s-curve
  Four-core s-curve
  Detailed performance analysis
  Benefit of bandwidth awareness
  Case study
  Customizing rewards
  Customizing features

## Slide 98: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2109.12021.pdf

## Slide 99: Hermes: Perceptron-Based Off-Chip Load Prediction

## Slide 100: Learning-Based Off-Chip Load Predictors
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 101: Hermes Talk Video
https://www.youtube.com/watch?v=PWWBtrL60dQ&t=3609s

## Slide 102
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran,
David Novo, Ataberk Olgun, Mohammad Sadrosadati, Onur Mutlu
Accelerating Long-Latency Load Requests
via Perceptron-Based Off-Chip Load Prediction
https://github.com/CMU-SAFARI/Hermes
https://arxiv.org/pdf/2209.00188.pdf

## Slide 103: The Key Problem
Long-latency off-chip load requests
Often stall processor by
blocking instruction retirement from
Reorder Buffer (ROB)
Limit performance
Notes: The key problem that we are trying to address in this work is stemming from Off-chip load request
[CLICK] As we know, these off-chip load requests often stall…,
[CLICK] which severely limits the performance of a core.

## Slide 104: Traditional Solutions
Employ sophisticated prefetchers
1
Increase size of on-chip caches
2
Notes: Architects have primarily relied on two key techniques to reduce latency of such loads:
[CLICK] By employing sophisticated data prefetchers
[CLICK] And Increasing size of the on-chip cache hierarchy

## Slide 105: Key Observation 1
Chart: 
| uncovered | covered by prefetcher
 | 0.49685 | 0.50315
50%
successfully prefetched
# off-chip loads without any prefetcher
50%
still go off-chip even with
a state-of-the-art prefetcher
70% of the off-chip loads
block the ROB
Many loads still go off-chip
Notes: In this work, we show that prior prefetchers successfully prefetch a significant fraction of the off-chip load requests.
[CLICK] However, nearly 50% of the off-chip loads in a system without any prefetcher are still going off-chip even in presence of a state-of-the-art prefetcher
[CLICK] And 70% of these off-chip loads even block the ROB.

## Slide 106: Key Observation 2
40% of the stalls can be eliminated by removing
on-chip cache access latency from critical path
On-chip cache access latency
significantly contributes to off-chip load latency
L1
L2
LLC
Main Memory
Saved cycles
Chart: 
| uncovered | covered by prefetcher
 | 0.49685 | 0.50315
50% still go off-chip
L1
L2
LLC
Main Memory
Notes: Now, if we focus on the off-chip loads that are still going to the main memory even in presence of a state-of-the-art prefetcher,
We observe that the on-chip cache access latency…
[CLICK] We show that nearly 40% of …

## Slide 107: Caches are Getting Bigger and Slower…
Hardavellas+, “Database Servers on Chip Multiprocessors: Limitations and Opportunities”, CIDR, 2007
On-chip Cache Size (KB)
Chart: L2 Size (KB)
| Skylake (2015) | Sunny Cove (2019) | Willow Cove (2020) | Golden Cove P-core (2021) | Raptor Lake P-core (2022)
Size | 256 | 512 | 1280 | 1280 | 2048
Chart: L2 Latency (processor cycles)
| Skylake (2015) | Sunny Cove (2019) | Willow Cove (2020) | Golden Cove P-core (2021) | Raptor Lake P-core (2022)
Latency | 12 | 13 | 14 | 15 | 16
Notes: As the cache hierarchy continue to grow in size and complexity, as noted by previous works,
As well as a trend that we see in recent processors,
This problem is only going to get exacerbated even more in future generation processors

## Slide 108: Our Goal
Improve processor performance
by removing on-chip cache access latency
from the critical path of off-chip loads
Notes: Thus to alleviate this problem, the goal of our work is to improve…

## Slide 109
Predicts which load requests
are likely to go off-chip
Starts fetching data directly from main memory while concurrently accessing the cache hierarchy
Notes: Towards this we propose Hermes, which is based on two key ideas.
[CLICK] Hermes predicts which…
[CLICK] Hermes starts fetching …

## Slide 110: Key Contribution
Hermes employs the first
perceptron-based off-chip load predictor
That predicts which loads are likely to go off-chip
By learning from
multiple program context information
Notes: To enable accurate off-chip prediction,
Hermes employs the first perceptron-based off-chip load predictor
[CLICK] that identifies loads …
[CLICK] by only learning from multiple…

## Slide 111: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
Baseline
Processor is stalled
Latency tolerance limit of ROB
Notes: Now let me give you a brief overview of Hermes.
This is how a traditional cache hierarchy looks like in today’s processor.
[CLICK] And this is how the memory latency timeline looks like for an off-chip load in the baseline system
[CLICK] If the ROB has a latency tolerance limit up till here, the processor stalls for the remaining cycles

## Slide 112: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
POPET
L1
L2
LLC
Main Memory
Baseline
Hermes
Saved stall cycles
Processor is stalled
Latency tolerance limit of ROB
Predict
Issue a Hermes request
Wait
Train
Perceptron-based
off-chip load predictor
Notes: Now Hermes employs an off-chip predictor named POPET.
[CLICK] For every load generated in the core, Hermes consults POPET to predict whether this load would go off-chip or not
[CLICK] If the load is predicted to go off-chip, Hermes waits for the address translation to finish, which happens in parallel with L1 cache access
[CLICK] And then issues a speculative memory request, which we call a Hermes request,
directly to the main memory controller to start fetching the data from the main memory,
While also concurrently accessing the cache hierarchy for such a load.
[CLICK] If the off-chip prediction is correct, the load would eventually miss the LLC and arrive at the memory controller
Where it will simply wait for the ongoing Hermes request to finish, thus hiding the entire cache access latency from its critical path.
Once the data returns from the main memory, Hermes returns the data to the core [CLICK],
Thus, saving the precious stall cycles induced by the off-chip load [CLICK], which in turn provides performance benefit.
[CLICK] Hermes trains POPET when the data finally returns to the core, closing the feedback loop.

## Slide 113: Designing the Off-Chip Load Predictor
Tracking cache contents
Learning from program behavior
  Large metadata
  Metadata size increases with cache hierarchy size
  May need to track all cache operations
  Gets complex depending on the cache hierarchy configuration (e.g., inclusivity, bypassing,…)
  Correlate different program features with off-chip loads
MissMap [Loh+, MICRO’11] for the DRAM cache,
D2D [Sembrant+, ISCA’14], D2M [Sembrant+, HPCA’17], LP [Jalili+, HPCA’22] for the cache hierarchy
History-based prediction
HMP [Yoaz+, ISCA’99] for the L1-D cache
Using branch-predictor-like hybrid predictor:
Global, Gshare, and GSkew
Low storage overhead
Low design complexity
POPET provides
both higher accuracy and higher performance
than predictors inspired from these previous works
Notes: Now let’s discuss how to design this off-chip predictor.
So, there are multiple prior works that can be used either directly or with small modifications for off-chip load prediction.
These works can be broadly categorized into two classes.
[CLICK] History-based predictor introduced by HMP, uses a branch-predictor like hybrid predictor design
to identify which requests are going to miss L1 cache.
We can easily extend HMP’s design to predict loads that are going to miss the entire cache hierarchy.
[CLICK] Tracking-based methods, on the other hand, explicitly track cache contents
to predict which load requests are going to miss the cache hierarchy.
[CLICK] These tracking-based methods poses two key challenges…
[CLICK] First,…
[CLICK] Second,…
[CLICK] POPET takes a completely different approach to predict off-chip load requests by learning from program behavior.
[CLICK] It aims to correlate multiple different types of program features with off-chip load requests
to provide accurate predictions with much lower storage overhead and design complexity.
[CLICK] In our paper, we compare POPET against predictors inspired from these prior works and show that
[CLICK] POPET provides both higher accuracy and performance than them.

## Slide 114: POPET: Perceptron-Based Off-Chip Predictor
Multi-feature hashed perceptron model [1]
  Each feature has its own weight table
    Stores correlation between feature value and off-chip prediction
[1] D. Tarjan and K. Skadron, “Merging Path and Gshare Indexing in Perceptron Branch Prediction,” TACO, 2005
Notes: Now let’s deep dive into our off-chip predictor design.
Our predictor, named as POPET, is designed using hashed-perceptron model.
[CLICK] where each feature has its own weight table
That stores the correlation between feature value and the off-chip prediction

## Slide 115: Predicting using POPET
Uses simple table lookups, addition, and comparison
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Extract features from the load request
Notes: Hermes predicts using POPET using simple operations like table lookup, addition, and comparison.
Let me give you an example on how POPET’s prediction works.
POPET’s prediction works in three stages.
[CLICK] In the first stage, POPET extracts the features from the load request
[CLICK] In the second stage, each feature value is hashed and used as an index to retrieve the weights from each individual weight tables
[CLICK] In the third stage, the retrieved weights are accumulated and the cumulative weight is used to compute the activation function.
[CLICK] If the cumulative weight is higher than the activation threshold, POPET predicts that the load would go off-chip.

## Slide 116: Training POPET
Uses simple increment or decrement of feature weights
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Shouldn’t be activated
Cumulative weight < 𝜏act
-1
-1
-1
Notes: Now let’s understand how to train POPET.
For this let’s assume the previous example where the load is predicted to go off-chip.
[CLICK] But in reality, the load didn’t go off-chip
[CLICK] this means the activation which have triggered before, shouldn’t have triggered
Which means, the cumulative weight should be lower than the activation threshold
[CLICK] Now to adjust the feature weights, POPET again indexes each weight table using the hashed feature values
[CLICK] And simply decrement each weight from the individual weight tables.
Thus, by using simple increment and decrement operations, POPET continuously learns from program behavior to accurately predict off-chip loads.

## Slide 117: Features Used in Hermes

## Slide 118: Evaluation
Notes: Now let’s evaluate Hermes.

## Slide 119: Simulation Methodology
ChampSim trace driven simulator
110 single-core memory-intensive traces
  SPEC CPU 2006 and 2017
  PARSEC 2.1
  Ligra
  Real-world applications
220 eight-core memory-intensive trace mixes
Off-Chip Predictors
LLC Prefetchers
History-based: HMP [Yoaz+, ISCA’99]
Tracking-based: Address Tag-Tracking based Predictor (TTP)
Ideal Off-chip Predictor
Pythia [Bera+, MICRO’21]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, 3rd Prefetching Championship’19]
SPP + Perceptron filter [Bhatia+, ISCA’20]
SMS [Somogyi+, ISCA’06]
Notes: We evaluate Hermes using ChampSim simulator,
[CLICK] using a wide range of memory-intensive traces spanning across SPEC CPU, PARSEC, Ligra, and real-world applications
[CLICK] We compare Hermes with five LLC prefetchers
[CLICK] and two off-chip predictors extended from prior works

## Slide 120: Latency Configuration
Cache round-trip latency
  L1-D: 5 cycles
  L2: 15 cycles
  LLC: 55 cycles
Hermes request issue latency (incurred after address translation)
Depends on
  Interconnect between POPET and MC
0 cycles
24 cycles
6 cycles
Notes: For our evaluation, we consider
[CLICK] a 5 cycle L1-D
[CLICK] 15 cycle L2
[CLICK] and 55 cycle LLC round-trip latency.
[CLICK] The latency for Hermes to issue a request directly to the main memory controller (after the address translation) depends on …
[CLICK] For this reason we sweep this latency from 0-cycles to 24-cycles in our paper.
[CLICK] But in this presentation, I am going to show you results considering a 6-cycle latency.

## Slide 121: Single-Core Performance Improvement
Chart: Geomean speedup over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | GEOMEAN
Hermes | 1.0966 | 1.1185 | 1.1061 | 1.1108 | 1.1309 | 1.115
Pythia | 1.2123 | 1.2715 | 1.0568 | 1.1992 | 1.2108 | 1.2034
Pythia + Hermes | 1.2628 | 1.3007 | 1.1279 | 1.2388 | 1.2854 | 1.2574
Pythia + Ideal Hermes | 1.292 | 1.3305 | 1.1417 | 1.261 | 1.3239 | 1.2863
11.5%
20.3%
5.4%
Hermes alone provides nearly
50% performance benefits of Pythia with only 1/5th storage overhead
Hermes on top of Pythia
outperforms Pythia alone in every workload category
Hermes provides nearly 90% performance benefit of Ideal Hermes that has an ideal off-chip load predictor
Notes: Let’s first analyze the single-core performance improvement.
[CLICK] This is how Hermes and a state-of-the-art prefetcher Pythia improves performance on top of a no-prefetching system.
[CLICK] The first takeaway is that Hermes alone provides nearly 50%...
[CLICK] Now if we combine Hermes with Pythia, that provides an additional 5.4% performance improvement on top of a strong baseline that has Pythia.
[CLICK] And finally, if we compare Hermes’s performance benefit with the Ideal Hermes that has an ideal off-chip predictor,
We see that Hermes provides nearly 90% performance benefit of the Ideal Hermes

## Slide 122: Increase in Main Memory Requests
Chart: % increase in main memory requests over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Hermes | 0.056805 | 0.029895 | 0.27038 | 0.072653 | 0.062029 | 0.055441
Pythia | 0.41862 | 0.2408 | 0.48617 | 0.37302 | 0.52323 | 0.38512
Pythia + Hermes | 0.47511 | 0.27921 | 0.65693 | 0.41847 | 0.60518 | 0.44428
5.5%
38.5%
5.9%
11.5%
20.3%
5.4%
For every 1% performance benefit,
increase in main memory requests
Pythia
Hermes on top of Pythia
Hermes alone
2%
1%
0.5%
Hermes is more bandwidth-efficient
than even an efficient prefetcher like Pythia
Notes: This performance improvement comes at a cost of increase in main memory requests.
This graph shows the increase in the main memory request over the no-prefetching system provided by the three configurations.
[CLICK] As we can see, Hermes increases the main memory requests by 5.5% on average on top of the no-prefetching system..
Whereas Pythia increases …
If we combine two together, then it increases the main memory request by an additional 5.9%.
[CLICK] Now, if we compare this increase in the main memory request with the performance improvement each of these configurations are providing,
We see that
[CLICK] For every 1% performance benefit, Pythia …
[CLICK] This basically shows that Hermes is much more bandwidth efficient than a traditional data prefetcher like Pythia.
And for this reason [NEXT]

## Slide 123: Performance with Varying Memory Bandwidth
Chart: Main Memory Bandwidth (in MT/s)
| 200 | 400 | 800 | 1600 | 3200 | 6400 | 12800
Pythia | 0.90608 | 1.0297 | 1.1215 | 1.1842 | 1.2034 | 1.2051 | 1.2044
Hermes | 0.99513 | 1.0581 | 1.0896 | 1.1085 | 1.115 | 1.1174 | 1.1168
Pythia+Hermes | 0.96845 | 1.0682 | 1.1608 | 1.2325 | 1.2574 | 1.2593 | 1.2583
~AMD Threadripper 3990x (Zen 2, 64C/4ch, 2020)
~AMD EPYC Rome 7702P (Zen 2, 64C/8ch, 2019)
~Intel Xeon 6258R
(Cascade Lake, 28C/6ch, 2020)
Pythia
Hermes
Pythia+Hermes
In bandwidth-constrained configurations,
Hermes alone outperforms Pythia
Hermes+Pythia outperforms Pythia
across all bandwidth configurations
Baseline
Notes: If we evaluate Pythia and Hermes over a wide range of memory bandwidth configurations, we see that,
[CLICK] In these extremely-bandwidth constrained configurations, which are in fact roughly modeling per-core main memory bandwidth of commercial processors,
Hermes even outperforms Pythia.
[CLICK] And if we combine both of them, the combination of Hermes and Pythia outperforms Pythia in every bandwidth configurations.

## Slide 124: Performance with Varying Baseline Prefetcher
Chart: Geomean speedup over the No-prefetching system
| Pythia | Bingo | SPP | MLOP | SMS
Prefetcher-only | 1.2034 | 1.1937 | 1.1443 | 1.1347 | 1.0568
Prefetcher + Hermes | 1.2574 | 1.2554 | 1.1948 | 1.2104 | 1.1342
5.4%
6.2%
5.1%
7.6%
7.7%
Hermes consistently improves performance
on top of a wide range of baseline prefetchers
Notes: And these observations are not only true for Pythia.
We evaluate Hermes combined with multiple prior baseline state-of-the-art prefetchers and find that
Hermes consistently improves performance on top of a wide range of baseline prefetchers.

## Slide 125: Effect of Cache Hierarchy Access Latency
3.6%
6.2%
Hermes can provide even higher performance benefit in
future processors with bigger and slower on-chip caches

## Slide 126: Effect of ROB Size
6.7%
5.3%

## Slide 127: Effect of LLC Size
1.3%
2.5%

## Slide 128: Accuracy and Coverage with Different Prefetchers
POPET’s accuracy and coverage increases significantly
in absence of a data prefetcher

## Slide 129: Overhead of Hermes
4 KB storage overhead
1.5% power overhead*
*On top of an Intel Alder Lake-like performance-core [2] configuration
[2] https://www.anandtech.com/show/16881/a-deep-dive-into-intels-alder-lake-microarchitectures/3
Notes: All of these performance benefit comes at a
[CLICK] modest 4KB storage overhead per core and
[CLICK] 1.5% power overhead on top an Intel Alder Lake-like performance-core configuration

## Slide 130: More in the Paper
Performance sensitivity to:
  Cache hierarchy access latency
  Hermes request issue latency
  Activation threshold
  ROB size (in extended version on arXiv)
  LLC size (in extended version on arXiv)
Accuracy, coverage, and performance analysis against HMP and TTP
Understanding usefulness of each program feature
Effect on stall cycle reduction
Performance analysis on an eight-core system
Notes: We have many more evaluation results:
For example, a wide range of performance sensitivity study by varying…in the paper.

## Slide 131: More in the Paper
Performance sensitivity to:
  Cache hierarchy access latency
  Hermes request issue latency
  Activation threshold
  ROB size (in extended version at arXiv)
  LLC size (in extended version at arXiv)
Accuracy, coverage, and performance analysis against HMP and TTP
Understanding usefulness of each program feature
Effect on stall cycle reduction
Performance analysis in eight-core system
https://arxiv.org/pdf/2209.00188.pdf
Notes: We have many more evaluation results:
For example, a wide range of performance sensitivity study by varying…in the paper.

## Slide 132: To Summarize…
Notes: Thus to summarize…

## Slide 133: Summary
Hermes enables off-chip load prediction,
a different form of speculation than
load address prediction employed by prefetchers
Off-chip load prediction can be applied by itself
or combined with load address prediction
to provide performance improvement
Notes: Hermes advocates …
[CLICK] We show that off-chip load prediction…

## Slide 134: Summary
Hermes employs the first
perceptron-based off-chip load predictor
High coverage
(74%)
High accuracy
(77%)
Low storage overhead
(4KB/core)
High performance improvement over best prior baseline
(5.4%)
High performance
per bandwidth

## Slide 135: Hermes is Open Sourced
https://github.com/CMU-SAFARI/Hermes
All workload traces
13 prefetchers
9 off-chip predictors
Notes: That’s why we open-source our artifact.
It can be freely downloaded from our GitHub repository.
In this artifact, [CLICK] you will get all the workload traces we have used to evaluate Hermes,
[CLICK] 13 types of data prefetchers proposed in the past and
[CLICK] 9 types of off-chip predictors out of the box

## Slide 136: Easy To Define Your Own Off-Chip Predictor
Just extend the OffchipPredBase class
Notes: But if you want to impalement your own off-chip predictor, that’s also very easy.
All you have to do is to extend the OffchipPred base class…

## Slide 137: Easy To Define Your Own Off-Chip Predictor
Define your own train() and predict() functions
Get statistics like accuracy (stat name precision) and coverage (stat name recall) out of the box
Notes: And define your own train() and predict() functions
[CLICK] the infrastructure will automatically provide statistics like precision and recall out of the box

## Slide 138: Off-Chip Prediction Can Further Enable…
Prioritizing loads that are likely go off-chip
in cache queues and on-chip network routing
Better instruction scheduling
of data-dependent instructions
Other ideas to improve performance and fairness in multi-core system design...
Notes: We hope that high-accuracy off-chip prediction can further enable a multitude of optimization possibilities, for example:
[CLICK] prioritizing loads … to improve performance and fairness in extreme core processors
[CLICK] better instruction scheduling for data dependent loads
[CLICK] and many more…

## Slide 139
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran,
David Novo, Ataberk Olgun, Mohammad Sadrosadati, Onur Mutlu
Accelerating Long-Latency Load Requests
via Perceptron-Based Off-Chip Load Prediction
https://github.com/CMU-SAFARI/Hermes
https://arxiv.org/pdf/2209.00188.pdf
Notes: With that hope, I will conclude my talk.
I will be very happy to take any question from the audience.

## Slide 140: Hermes Discussion
FAQs
  What are the selected set of program features?
  Can you provide some intuition on why these features work?
  What happens in case of a misprediction?
  What’s the performance headroom for off-chip prediction?
  Do you see a variance of different features in final prediction accuracy?
Simulation Methodology
  System parameters
  Evaluated workloads
More Results
  Percentage of off-chip requests
  Reduction in stall cycles by reducing the critical path
  Fraction of off-chip load requests
  Accuracy and coverage of POPET
  Effect of different features
  Are all features required?
  1C performance
  1C performance line graph
  1C performance against prior predictors
  Effect on stall cycles
  8C performance
  Sensitivity:
    Hermes request issue latency
    Cache hierarchy access latency
    Activation threshold
    ROB size
    LLC size
  Power overhead
  Accuracy without prefetcher
  Main memory request overhead with different prefetchers

## Slide 141: Hermes Paper [MICRO 2022]
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 142: Sibyl: Reinforcement Learning based Data Placement in Hybrid SSDs

## Slide 143: Self-Optimizing Hybrid SSD Controllers
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 144
Sibyl Adaptive and Extensible Data Placement in Hybrid Storage Systems
Using Online Reinforcement Learning
Gagandeep Singh, Rakesh Nadig, Jisung Park,
Rahul Bera, Nastaran Hajinazar, David Novo,
Juan Gómez Luna, Sander Stuijk, Henk Corporaal,
Onur Mutlu
144
Notes: Hi First of all. Thank you very much for staying until this long.
I’m going to present our work “…”

## Slide 145: Executive Summary
Background: A hybrid storage system (HSS) uses multiple different storage devices to provide high and scalable storage capacity at high performance
Problem: Two key shortcomings of prior data placement policies:
  Lack of adaptivity to:
    Workload changes
    Changes in device types and configurations
  Lack of extensibility to more devices
Goal: Design a data placement technique that provides:
  Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
  Easy extensibility to incorporate a wide range of hybrid storage configurations
Contribution: Sibyl, the first reinforcement learning-based data placement technique in hybrid storage systems that:
  Provides adaptivity to changing workload demands and underlying device characteristics
  Can easily extend to any number of storage devices
  Provides ease of design and implementation that requires only a small computation overhead
Key Results: Evaluate on real systems using a wide range of workloads
  Sibyl improves performance by 21.6% compared to the best previous data placement technique in dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-policy policy by 48.2%
  Sibyl achieves 80% of the performance of an oracle policy with storage overhead of only 124.4 KiB
https://github.com/CMU-SAFARI/Sibyl
Notes: First, I am going to start with an executive summary.
[CLICK] Hybrid storage systems use multiple different storage devices to provide high and scalable storage capacity at high performance
[CLICK] We observe two key shortcomings in prior data placement techniques:
First, lack of adaptivity to workload changes and changes in device types and configurations
Second, they also lack extensibility to to more devices.
[CLICK] Our goal in this work is to design a data placement technique that provides
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
Easy extensibility to incorporate a wide range of hybrid storage configurations
[CLICK] to this end we propose Sibyl, an online reinforcement learning-based data placement in Hybrid storage systems that:
  Provides both adaptivity
  and easy extensiblity
  and also Provides ease of design and implementation that requires only a small computation overhead
[CLICK] We extensively evaluate Sibyl on real systems using a wide range of workloads
We show that Sibyl outperforms prior state-of-the-art data placement policeis by 21.6% in dual-hybrid storage system and upto 48.2% on trihybrid system
Sibyl achieves 80% of the performance of an oracle policy that has a complete knowledge of future access patterns while incurring a very modest storage overhead of only 124.4 KiB
The code will be opensourced on our GitHub repository.
https://github.com/CMU-SAFARI/Sibyl

## Slide 146: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: This is the outline of my talk.
First, I am going to start by discussing key shortcomings of prior data placement techniques.

## Slide 147: Hybrid Storage System Basics
Storage Management Layer
Write
Read
Read
Write
Read
Write
Promotion
Eviction
Hybrid Storage System
Fast Device
Slow Device
Address Space (Application/File System View)
Notes: Let's look at some basics on hybrid storage systems. [CLICK] OVER here we show a typical HSS consisting of a fast-yet-small storage device and a slow-yet-large storage device
[CLICK]The address space is divided into a number of logical pages (e.g. 4kib), which are assigned to an application.
[CLICK] The storage management layer in the OS orchestrates host I/O requests across heterogeneous devices,
[CLICK] the storage management layer also manages data migration between the storage devices in an Hybrid storage systems . Eviction usually moves infrequently access data fom the fast storage to the slow storage or when the fast storage device is full.
When data currently stored in the slow storage device is moved to the fast storage device, it is called promotion. Promotion is usually performed when a page in the slow storage device is accessed frequently.
[CLICK] A desirable policy has to effectively utilize the low latency characteristics of the fast device while making optimal use of its small capacity and should provide easy extensibility to a wide range of workloads and Hybrid storage systems configurations

## Slide 148: Hybrid Storage System Basics
Write
Read
Read
Write
Read
Write
Promotion
Eviction
Hybrid Storage System
Performance of a hybrid storage system
highly depends on the ability of the
storage management layer
Notes: [CLICK] Therefore the performance of a hybrid storage system highly depends on the ability of the storage management layer to effectively manage diverse deviaces and workloads

## Slide 149: Key Shortcomings in Prior Techniques
We observe two key shortcomings that significantly limit the performance benefits of prior techniques
Lack of adaptivity to:
  Workload changes
  Changes in device types and configuration
Lack of extensibility to more devices
Notes: We observe two key shortcomings in prior data placement techniques that significantly limits their performance improvement
[CLICK] First, lack of adaptivity to both workload changes and
CLICK] changes in device types and configurations
[CLICK] Second, Lack of extensibility: to more devices
Let’s take a closer look at each of these shortcomings.
[NEXT]

## Slide 150: Lack of Adaptivity (1/2)
Workload Changes
Prior data placement techniques consider only a few workload characteristics that are statically tuned
CDE
RNN-HSS
Oracle
41.1%
Notes: The lower the request latency the better
We observe that all baselines provide reasonable performance under specific workloads [CLICK] while for other they show way lower performance than oracle. [CLICK]
[CLICK] on avg we observe a performance loss for some policies by 41.1% compared to oracle
We conclude, considering only a limited number of workload characteristics leads to
a significant performance gap

## Slide 151: Lack of Adaptivity (2/2)
Changes in Device Types and Configurations
Do not consider underlying storage device characteristics (e.g., changes in the level asymmetry in read/write latencies, garbage collection)
HSS Configuration 1
HSS Configuration 2
Slow-Only
CDE
RNN-HSS
Slow-Only
CDE
RNN-HSS
Oracle
Oracle
Notes: We obseve that performance of some workloads is even worse than slow-only policy that places everything in the slow storage [CLICK] while in another hybrid storage configuration these workloads perform better than slow only[CLICK] [CLICK]
Therefore, we conclude that the high diversity in device characteristics makes it very difficult for a system architect to design a generic data-placement technique that is suitable for all Hybrid storage systems configurations

## Slide 152: Lack of Extensibility (1/2)
Rigid techniques that require significant effort to accommodate more than two devices
Change in storage configuration
Dual-HSS
Notes: The second key shortcoming is that, most of the prior techniques are
[CLICK] rigid that require significant effort to accommodate more than two devices
if we extend from dual hybrid stroage configuration from dual hyrbid to a tri-hybrid configuration

## Slide 153: Lack of Extensibility (2/2)
Rigid techniques that require significant effort to accommodate more than two devices
Change in storage configuration
Design a new policy
Tri-HSS
Notes: [click] design a new data policy to exploit the new device to eviction and promotino from the new storage and update heuristic values as wel. [CLICK]
Therefore system architects need to put significant effort into extending prior data placement techniques to accommodate more than two devices [CLICK] This wastes precious design time and human resource.

## Slide 154: Our Goal
A data-placement mechanism
that can provide:
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
Easy extensibility to incorporate a wide range of hybrid storage configurations
Notes: So our goal in this work is to design a data-placement mechanism that can provide
[CLICK]
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
[CLICK]
Easy extensibility to incorporate a wide range of hybrid storage configurations.

## Slide 155: Our Proposal
Sibyl
Formulates data placement in hybrid storage systems as a reinforcement learning problem
Sibyl is an oracle that makes accurate prophecies
https://en.wikipedia.org/wiki/Sibyl
Notes: To this end, we propose Sibyl
Which formulates data placement in hybrid…

## Slide 156: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: Lets go into the formulation of dataplacement as a reinforcement learning problem

## Slide 157: Basics of Reinforcement Learning (RL)
Agent learns to take an action in a given state
to maximize a numerical reward
Notes: First, let me briefly describe the basics of reinforcement learning.
A RL system contains two components: [CLICK] the agent and the environment.
The agent observes the state of the environment in every timestep [CLICK], takes an action based on the state [CLICK], and receives a reward for that action [CLICK].
[CLICK] Agent’s goal is to find a policy where agent’s action in a given state leads to maximum reward

## Slide 158: Formulating Data Placement as RL
Agent
Environment
State (St)
Action (At)
Reward (Rt+1)
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place the current page
Notes: In Sibyl, we formulate data-placement as a reinforcement learning problem.
[CLICK] Sibyl acts as the agent, while [CLICK] the hybrid storage subsystem acts as the environment.
[CLICK] Sibyl observes workload and system features from every storage request and use it as a state information to take a data placement action [CLICK]
[CLICK] For every data placement action, Sibyl receives a numerical reward that evaluates the effectiveness of the data placement decision
Now we will concretely define the state, action, and the reward for Sibyl.

## Slide 159: What is State?
Limited number of state features:
  Reduce the implementation overhead
  RL agent is more sensitive to reward
6-dimensional vector of state features
We quantize the state representation into bins to reduce storage overhead
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: [CLICK] For the state, we use limited number of state features after performing feature selection to:
reduce implementation overhead
[CLICK] and we observe RL agent's perfromance is more sensitive to the reward than state features. So adding many feature does not help
[CLICK] We define the state as a 6-dimensional vector of program features.
[CLICK] Some examples are the size of the incoming request the type of request etc
[click] we also quantize the state representation into bins to reduce the storage overhead

## Slide 160: Selected State Attributes

## Slide 161: What is Reward?
Defines the objective of Sibyl
We formulate the reward as a function of the request latency
Encapsulates three key aspects:
  Internal state of the device (e.g., read/write latencies, the latency of garbage collection, queuing delays, …)
  Throughput
  Evictions
More details in the paper
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: The reward defines the objective of Sibyl
[CLICK] Though Sibyl can learn from any …, in this paper we formulate the reward as a function of the request latency
[CLICK] A reward encapsulates three metrics: …

## Slide 162: Reward Function

## Slide 163: What is Action?
At every new page request, the action is to select a storage device
Action can be easily extended to any number of storage devices
Sibyl learns to proactively evict or promote a page
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: We define the action as the selection of a storage device to place the current page.
[CLICK] Such an action allows easy extensiblity to any number of storage devices
[CLICK] it makes SIbyl learn to proactively evit or promote a page from the storage device

## Slide 164: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: We now provide a brief overview and design of Sibyl.

## Slide 165: Sibyl Execution
RL Decision Thread
Storage
Request
(from OS)
RL Training Thread
Periodic Policy
Weight Update
State, Reward, and Action Information
Data Placement Decision
Asynchronous
Execution
Sibyl
Notes: FIRST we discuss the execution model for Sibyl. We implement sibyl in the the host OS. [CLICK] Where for every storage request Sibyl uses an RL decision thread to make [CLICK] data placemnet decisions.
Sibyl uses another thread, [CLICK] called the RL training thread that works in the background. It keeps collecting information about Sibyl's state, action and reward, which uses this information to train a data placement policy. [CLICK] periodically we replace the RL decision thread policy with RL training thread policy.
[CLICK] Our two-threaded implementation runs ASYNCHROUNOUS AND avoids that the training in RL training thread interrupts or delays data placement decisions for incoming requests.

## Slide 166: Sibyl Design: Overview
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Weights update
10
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: Now we will go into the implementation of each thread

## Slide 167: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: First we discuss the RL decision thread, where Sibyl decides the data placement of the current storage request while collecting information about its decisions

## Slide 168: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: For every new storage request to the Hybrid storage systems , Sibyl uses the state information to make a data placement action.

## Slide 169: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: The inference network predicts the expected benefits of each action for a given state.
Sibyl policy selects the action with the highest expected benefit
or, a random action for exploration of the Hybrid storage systems

## Slide 170: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: While making data placement decision, Sibyl collects information about the state, action, and reward

## Slide 171: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: in an experience buffer, which in used in RL Training thread

## Slide 172: RL Training Thread
Periodic Weights update
10
RL Training Thread
Batch
Training Dataset
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Policy
Weight Update
Training
Network
Notes: In the RL training thread, Sibyl uses the collected experiences to update its decision making policy online by training a neural network.
Sibyl continuously learns from its past decisions and their impact.

## Slide 173: Periodic Weight Transfer
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Weights update
10
Training
Network
Periodic Policy
Weight Update
RL Training Thread
Batch
Training Dataset
Notes: To enable the parallel execution of the two threads, we duplicate the neural network that is used to make data placement decisions, so the inference network does not have a separate training steps and only uses the weights of the training network, which we periodically update.

## Slide 174: Training and Inference Networks
Training and inference networks allow parallel execution
Observation vector as the input
Produces probability distribution of Q-values
Notes: A deep neural network can be prohibitive due to the long time it requires for training and convergence, preventing Sibyl to adapt to new state-action pairs in a timely manner.
Based on experiments, we find that a simple feed-forward network [135] with only two hidden layers [136] provides good performance for Sibyl’s data placement task.
The network takes the observation vector 𝑂𝑡 as its input and produces a probability distribution of Q-values as its output

## Slide 175: RL-Based Data Placement Algorithm

## Slide 176: Hyperparameter Tuning

## Slide 177: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: We now present our key results

## Slide 178: Evaluation Methodology (1/3)
Real system with various HSS configurations
  Dual-hybrid and tri-hybrid systems
AMD Ryzen7 2700G CPU
Seagate HDD
ST1000DM010
Intel Optane SSD P4800X
Intel SSD D3-S4510
ADATA
SU630 SSD
Notes: [CLICK] We perfrom real system evaluation for both dual-hybrid and tri-hybrid systems
[CLICK] over here we show our evaluation setup that consists of multi different devices
[CLICK] We implement sibyl in the storage management layer of AMD Ryzen 7 2700G CPU

## Slide 179: Evaluation Methodology (2/3)
Cost-Oriented HSS Configuration
High-end SSD
Low-end HDD
Performance-Oriented HSS Configuration
High-end SSD
Middle-end SSD
Notes: First we evalutate a cost-oriented hybrid storage configuration in which we use
[CLICK]a high end ssd with a low-end hard disk drive where the latency difference between the two devices is quite large
[CLICK] Performance oriented hybrid storage configuration we
[CLICK]use a high end ssd with a middle end ssd
where two devices have similar latencies

## Slide 180: Evaluation Methodology (3/3)
18 different workloads from:
  MSR Cambridge and Filebench Suites
Four state-of-the-art data placement baselines:
  CDE [Matsui+, Proc. IEEE’17]
  HPS [Meswani+, HPCA’15]
  Archivist [Ren+, ICCD’19]
  RNN-HSS [Doudali+, HPDC’19]
Heuristic-based
Learning-based
Notes: [CLICK] We use 18 different workloads from MSR CAMBRIDGE and Filebench Suite
[CLICK] and compare Sibyl against four state of heuristic and supervised—learning based data placmenet policies

## Slide 181: Performance Analysis
Cost-Oriented HSS Configuration
Slow-Only
CDE
HPS
Archivist
RNN-HSS
Sibyl
Oracle
High-end SSD
Low-end HDD
Notes: [CLICK]Over here we show the performance results in terms of average request latency for MSR CAMBRIDGE workloads for all the workloads and policies

## Slide 182: Performance Analysis
Sibyl consistently outperforms all the baselines
for all the workloads
Cost-Oriented HSS Configuration
Slow-Only
CDE
HPS
Archivist
RNN-HSS
Sibyl
Oracle
High-end SSD
Low-end HDD
Notes: We observe that Sibyl consistently outperforms all the baselines for all the workloads

## Slide 183: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
High-end SSD
Mid-end SSD
Notes: In a performance oriented Hybrid storage systems configuration, where two devices have similar latencies [CLICK]
[CLICK]

## Slide 184: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Sibyl provides 21.6% performance improvement by dynamically adapting its data placement policy
High-end SSD
Mid-end SSD
Notes: Sibyl provides 21.6% performance improvement by dynamically adapting its data placement policy

## Slide 185: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
High-end SSD
Mid-end SSD
Notes: Sibyl provides slightly lower performance than other baselines in only two workloads for this configuration.
We observe that such workloads are write-intensive and have many random requests (in terms of both access pattern and request size).
Therefore, in the paper we show that for such workloads we need to perform frequent retraining

## Slide 186: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Sibyl achieves 80% of the performance
of an oracle policy that has
complete knowledge of future access patterns
High-end SSD
Mid-end SSD
Notes: on average Sibyl achieves 80% performance of an oracle policy that has complete knowledge of
future access patterns

## Slide 187: Performance on Tri-HSS
Extending Sibyl for more devices:
SibylTri-hybrid
HeuristicTri-hybrid
High-end SSD
Low-end HDD
Mid-end SSD
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
Notes: We also evaluate the EXTENSIBILITY of sibyl to more devices
To extend sibyl for more storage devices we have to only:
1. Add a new action in sibyl’s action space
2. Add the remaining capacity of the new device as a state feature
and sibyl automatically figures out the best policy
Here we show the performanc results for a state of the art heuristic based policy. This heuristic policy is an extended version of CDE policy which requires significant implementation effort for handling all the dataplacement cases because of the new device like eviction and promotion from the new device and where to send that data, set threshold values etc.

## Slide 188: Performance on Tri-HSS
SibylTri-hybrid
HeuristicTri-hybrid
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
High-end SSD
Low-end HDD
Mid-end SSD
Notes: and compare to sibyl for trihybrid system

## Slide 189: Performance on Tri-HSS
SibylTri-hybrid
HeuristicTri-hybrid
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
Sibyl outperforms the state-of-the-art
data placement policy by
48.2% in a real tri-hybrid system
Sibyl reduces the system architect's burden
by providing ease of extensibility
High-end SSD
Low-end HDD
Mid-end SSD
Notes: Sibyl outperforms the state-of-the-art-policy policy by upto 48.2%
[click]
We conclude that Sibyl provides ease of extensibility to new storage system configurations, which reduces the system architect’s burden in designing sophisticated data placement mechanisms.

## Slide 190: Sibyl’s Overhead
124.4 KiB of total storage cost
  Experience buffer, inference and training network
40-bit metadata overhead per page for state features
Inference latency of ~10ns
Training latency of ~2us
Small area overhead
Small inference overhead
Satisfies prediction latency
Notes: All of Sibyl performance benefits comes at a modest cost of 124.4KB storage cost to implement experience buffer, inference and training network
[CLICK] and 40-bit metadata overhead per page
[CLICK] We have inference latency of 10nanos, which are orders of magnitude smaller than the I/O read latency of a even a high end SSD (around 3micro seconds for Samsung ZNAND SSD)
[CLICK] with training latency of 2mico sec
So sibyl provides:
[CLICK]small area and
[CLICK]inference overhead [CLICK] which satisfied the prediction latency for making a data placement decision

## Slide 191: More in the Paper (1/3)
Throughput (IOPS) evaluation
  Sibyl provides high IOPS compared to baseline policies because it indirectly captures throughput (size/latency)
Evaluation on unseen workloads
  Sibyl can effectively adapt its policy to highly dynamic workloads
Evaluation on mixed workloads
  Sibyl provides equally-high performance benefits as in single workloads
Notes: We have many more exciting results in the paper including throughput comparison, evaluation on unseen workloads and mixed workloads

## Slide 192: More in the Paper (2/3)
Evaluation using different features
  Sibyl autonomously decides which features are important to maximize the performance
Evaluation with different hyperparameter values
Sensitivity to fast storage capacity
  Sibyl provides scalability by dynamically adapting its policy to available storage size
Explainability analysis of Sibyl's decision making
  Explain Sibyl’s actions for different workload characteristics and device configurations
Notes: And many more.
For more details we encourage you to read our paper

## Slide 193: More in the Paper (3/3)
https://arxiv.org/pdf/2205.07394.pdf
https://github.com/CMU-SAFARI/Sibyl

## Slide 194: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: Now I will conclude my talk

## Slide 195: Conclusion
We introduced Sibyl, the first reinforcement learning-based data placement technique in hybrid storage systems that provides
  Adaptivity
  Easily extensibility
  Ease of design and implementation
We evaluated Sibyl on real systems using many different workloads
  Sibyl improves performance by 21.6% compared to the best prior data placement policy in a dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-data placement policy by 48.2%
  Sibyl achieves 80% of the performance of an oracle policy with a storage overhead of only 124.4 KiB
https://github.com/CMU-SAFARI/Sibyl
Notes: We introduced Sibyl, the first reinforcement learning-based data placement in HSS that provides
  Adaptivity
  Easily extensibility
  Ease of design and implementation
We evaluated Sibyl on real systems using many different workloads
  Sibyl improves performance by 21.6% compared to the best previous data placement technique in dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-policy policy by 48.2%
  Sibyl achieves 80% performance of an oracle policy with storage overhead of only 124.4 KiB

## Slide 196
Sibyl Adaptive and Extensible Data Placement in Hybrid Storage Systems
Using Online Reinforcement Learning
Gagandeep Singh, Rakesh Nadig, Jisung Park,
Rahul Bera, Nastaran Hajinazar, David Novo,
Juan Gómez Luna, Sander Stuijk, Henk Corporaal,
Onur Mutlu
196
Notes: Hi First of all. Thank you very much for staying until this long.
I’m going to present our work “…”

## Slide 197: ISCA 2022 Paper, Slides, Videos
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 198: SSD Course (Spring 2023)
Spring 2023 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=modern_ssds
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=modern_ssds
Youtube Livestream (Spring 2023):
  https://www.youtube.com/watch?v=4VTwOMmsnJY&list=PL5Q2soXY2Zi_8qOM5Icpp8hB2SHtm4z57&pp=iAQB
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=hqLrd-Uj0aU&list=PL5Q2soXY2Zi9BJhenUq4JI5bwhAMpAp13&pp=iAQB
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 199: Comp Arch (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 200: Machine Learning Driven Memory and Storage Systems
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
19 December 2023
IBM Research

## Slide 201: PYTHIA BACKUP

## Slide 202: Reward Assignment to EQ Entry
Every action gets inserted into EQ
Reward is assigned to each EQ entry before or during the eviction
During EQ insertion: for actions
  Not to prefetch
  Out-of-page prefetch

## Slide 203: Reward Assignment to EQ Entry
Every action gets inserted into EQ
Reward is assigned to each EQ entry before or during the eviction
During EQ insertion: for actions
  Not to prefetch
  Out-of-page prefetch
During EQ residency:
  In case address of a demand matches with address in EQ (signifies accurate prefetch)

## Slide 204: Reward Assignment to EQ Entry
Every action gets inserted into EQ
Reward is assigned to each EQ entry before or during the eviction
During EQ insertion: for actions
  Not to prefetch
  Out-of-page prefetch
During EQ residency:
  In case address of a demand matches with address in EQ (signifies accurate prefetch)
During EQ eviction:
  In case no reward is assigned till eviction (signifies inaccurate prefetch)

## Slide 205: Performance S-curve: Single-core
Chart: Workload number
623.xalancbmk_s-592B
603.bwaves_s-2931B
462.libquantum
streamcluster
429.mcf
BFSCC-22B
pagerank-51B
fluidanimate-9500M

## Slide 206: Performance S-curve: Four-core
Chart: Workload number
429.mcf-184B
pagerank
462.libquantum-1343B
437.leslie3d-271B
Mix-59
raytrace-23.75B
Mix-240

## Slide 207: FAQs

## Slide 208: Pythia Discussion
FAQs
  Why RL?
  What about large page?
  What’s the prefetch degree?
  Can customization happen during workload execution?
  Can runtime mixing create problem?
Simulation and Methodology
  Basic Pythia configuration
  System parameters
  Configuration of prefetchers
  Evaluated workloads
  Feature selection
Detailed Design
  Reward structure
  Design overview
  QVStore Organization
More Results
  Comparison against other adaptive prefetchers
  Comparison against Context prefetcher
  Feature combination sensitivity
  Hyperparameter sensitivity
  Comparison with multi-level prefetchers
  Performance in unseen workloads
  Single-core s-curve
  Four-core s-curve
  Detailed performance analysis
  Benefit of bandwidth awareness
  Case study
  Customizing rewards
  Customizing features

## Slide 209: Why RL? Why Not Supervised Learning?
Determining the benefits of prefetching (i.e., whether a decision was good for performance or not) is not easy
  Depends on a complex set of metrics
    Coverage, accuracy, timeliness
    Effects on system: b/w usage, pollution, cross-application interference, …
  Dynamically-changing environmental conditions change the benefit
  Delayed feedback due to long latency (might not receive feedback at all for inaccurate prefetches!)
Differs from classification tasks (e.g., branch prediction)
  Performance strongly correlates mainly to accuracy
  Does not depend on environment
  Bounded feedback delay

## Slide 210: What About Large Pages?
Pythia’s framework can be easily extended to incorporate additional prefetch actions (i.e., possible prefetch offsets for the page size)
To decrease the storage overhead
  Prune action space via automatic design-space exploration
  Hash action values to retrieve Q-values

## Slide 211: What is the Prefetch Degree? Is It Managed by the RL Agent?
Pythia employs a simple degree selector, separate from the RL agent
  If the agent has selected the same prefetch action (O) multiple times in a row, Pythia increases the degree (A+2O, A+3O, …)
  At most degree 4
Future works on managing degree by the RL agent

## Slide 212: Can the Customization Be Done While the Workload is Running?
Certainly.
Pythia, being an online learning technique, will autonomously adapt (and optimize) its policy to use the new program features or the modified reward values

## Slide 213: Can Runtime Workload Mix Create an Issue?
We implement the bandwidth usage feedback using a counter in the memory controller. Thus Pythia already has a global view of the memory bandwidth usage that incorporates all workloads running on a multi-core system
We evaluate a diverse set (300 of each category) of four-core, eight-core, twelve-core random workload mixes
Based on our evaluation, we observe that Pythia dynamically adapts itself to varying workload demands

## Slide 214: How does Pythia Compare Against Other Adaptive Prefetching Solutions?
We compare Pythia against IBM POWER7[5] prefetcher
  Adaptively selects prefetcher degree/configuration by monitoring program IPC
Chart: Geomean speedup over baseline
| SPEC06 | SPEC17 | PARSEC | Ligra | Cloudsuite | GEOMEAN
POWER7 | 1.3317 | 1.175 | 1.1506 | 1.2944 | 1.0365 | 1.1789
Pythia | 1.4369 | 1.2569 | 1.2326 | 1.3254 | 1.0485 | 1.2242
Chart: Geomean speedup over baseline
| SPEC06 | SPEC17 | PARSEC | Ligra | Cloudsuite | Mix | GEOMEAN
POWER7 | 1.2873 | 1.1382 | 1.1343 | 1.2931 | 1.0386 | 1.3155 | 1.2345
Pythia | 1.3786 | 1.2234 | 1.2156 | 1.3212 | 1.0507 | 1.4086 | 1.299
(a) single-core
(b) four-core
4.5%
6.4%
[5] Jimenez et al., TOPC’14

## Slide 215: How Does Pythia Compare Against the Context Prefetcher?
Pythia widely differs from the Context Prefetcher (CP)[6] in all three aspects: state, action, and reward. The key differences are:
  CP does not consider system-level feedback
  CP models the agent as a contextual bandit which takes myopic prefetch decisions as compared to Pythia
  CP requires compiler support to extract software-level features
Pythia outperforms CP-HW by 5.3% in single-core and 7.6% in four-core system
[6] Leeor et al., ISCA’15

## Slide 216: How Pythia’s Performance Changes With Various State Definitions You Have Swept?
In total we evaluate state defined as any-one, any-two, and any-three combinations of 32 features
Performance gain ranges from 20.7% to 22.4%
Coverage ranges from 66.2% to 71.5%
Overprediction ranges from 26.7% to 32.2%

## Slide 217: Is Pythia Sensitive to Hyperparameters?
Not setting hyperparameters can significantly impact the overall performance improvement
Changing 𝜀 from 0.002 to 1.0 drops perf. by 16%
Changing 𝛼 from 0.0065 to 1.0 drops perf. by 5.4%

## Slide 218: How Does Pythia Compare Against Commercial Multi-level Prefetchers?
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
Stride-L1+Streamer-L2 | 0.9366 | 1.083 | 1.1579 | 1.1975 | 1.2105 | 1.2136 | 1.2152
IPCP | 0.85928 | 1.0124 | 1.121 | 1.1951 | 1.2213 | 1.2285 | 1.2301
Stride-L1+Pythia-L2 | 1.0014 | 1.1296 | 1.1873 | 1.2214 | 1.2341 | 1.2376 | 1.2386
Pythia outperforms IPCP [7] by 14.2% on average in 150-MTPS
[6] Prakalapati et al., ISCA’20

## Slide 219: Does Pythia Perform Equally Well for Unseen Workloads?
Evaluated with 500 traces from value prediction championship
  No prefetcher has been trained on these traces
Pythia outperforms MLOP and Bingo by
8.3% and 3.5% in single-core
And 9.7% and 5.4% in four-core

## Slide 220: Basic Pythia Configuration

## Slide 221: System Parameters

## Slide 222: Configuration of Prefetchers

## Slide 223: Evaluated Workloads

## Slide 224: List of Evaluated Features

## Slide 225: MORE RESULTS

## Slide 226: Performance S-curve: Single-core
Chart: Workload number
623.xalancbmk_s-592B
603.bwaves_s-2931B
462.libquantum
streamcluster
429.mcf
BFSCC-22B
pagerank-51B
fluidanimate-9500M

## Slide 227: Performance S-curve: Four-core
Chart: Workload number
429.mcf-184B
pagerank
462.libquantum-1343B
437.leslie3d-271B
Mix-59
raytrace-23.75B
Mix-240

## Slide 228: Single-core Coverage & Overprediction

## Slide 229: Detailed Performance

## Slide 230: Benefit of Bandwidth Awareness
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
Memory BW-oblivious Pythia | -0.046299 | -0.024802 | -0.012489 | -0.0039965 | -0.0026675 | -0.0019809 | -0.0020878

## Slide 231: Case Study

## Slide 232: Customizing Rewards

## Slide 233: Customizing Features

## Slide 234: Hermes Discussion
FAQs
  What are the selected set of program features?
  Can you provide some intuition on why these features work?
  What happens in case of a misprediction?
  What’s the performance headroom for off-chip prediction?
  Do you see a variance of different features in final prediction accuracy?
Simulation Methodology
  System parameters
  Evaluated workloads
More Results
  Percentage of off-chip requests
  Reduction in stall cycles by reducing the critical path
  Fraction of off-chip load requests
  Accuracy and coverage of POPET
  Effect of different features
  Are all features required?
  1C performance
  1C performance line graph
  1C performance against prior predictors
  Effect on stall cycles
  8C performance
  Sensitivity:
    Hermes request issue latency
    Cache hierarchy access latency
    Activation threshold
    ROB size
    LLC size
  Power overhead
  Accuracy without prefetcher
  Main memory request overhead with different prefetchers

## Slide 235: HERMES BACKUP

## Slide 236: Initial Set of Program Features

## Slide 237: Selected Set of Program Features
Five features
A binary hint that represents whether or not a cacheblock has been recently touched

## Slide 238: When A Feature Works/Does Not Work?
Trace: 462.libquantum-1343B
PC: 0x401442
Cacheline #42
Cacheline #43
…
…
Without prefetcher
PC + first access
Cacheline offset + first access
With a simple stride prefetcher
Cacheline offset + first access

## Slide 239: What Happens in case of a Misprediction?
Two cases of mispredictions:
Predicted on-chip but actually goes off-chip
  Loss of performance improvement opportunity
Predicted off-chip but actually is on-chip
  Memory controller forwards the data to LLC if and only if a load to the same address have already missed LLC and arrived at the memory controller
No need for misprediction detection and recovery
No need for misprediction detection and recovery

## Slide 240: Performance Headroom of Off-Chip Prediction

## Slide 241: System Parameters

## Slide 242: Evaluated Workloads

## Slide 243: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
50%
Nearly 50% of the loads are still not prefetched
1

## Slide 244: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
70% of these off-chip loads blocks ROB
2

## Slide 245: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency

## Slide 246: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency
40% of stall cycles caused by an off-chip load can be eliminated
by removing on-chip cache access latency from its critical path

## Slide 247: What Fraction of Load Requests Goes Off-Chip?

## Slide 248: Off-Chip Prediction Quality: Defining Metrics
Predicted off-chip
Actual off-chip
Predicted and actual off-chip
Accuracy
Coverage

## Slide 249: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%

## Slide 250: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%
POPET provides off-chip predictions with high-accuracy and high-coverage

## Slide 251: Effect of Different Features
Combination of features provides both higher accuracy and higher coverage than any individual feature

## Slide 252: Are All Features Required? (1)
No single feature individually provides
highest prediction accuracy across all workloads

## Slide 253: Are All Features Required? (2)
No single feature individually provides
highest prediction coverage across all workloads

## Slide 254: Single-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone in every workload category

## Slide 255: Single-Core Performance Line Graph

## Slide 256: Single-Core Performance Against Prior Predictors
POPET provides higher performance benefit
than prior predictors
Hermes with POPET achieves nearly 90% performance improvement of the Ideal Hermes

## Slide 257: Effect on Stall Cycles
Hermes reduces off-chip load induced stall cycles
on average by 16.2% (up-to 51.8%)

## Slide 258: Eight-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone by 5.1% on average

## Slide 259: Effect of Hermes Request Issue Latency
3.6%
5.7%
Hermes in combination with Pythia outperforms Pythia alone even with a 24-cycle Hermes request issue latency

## Slide 260: Effect of Cache Hierarchy Access Latency
3.6%
6.2%
Hermes can provide even higher performance benefit in
future processors with bigger and slower on-chip caches

## Slide 261: Effect of Activation Threshold
With increase in activation threshold
Accuracy increases
Coverage decreases

## Slide 262: Power Overhead

## Slide 263: Effect of ROB Size
6.7%
5.3%

## Slide 264: Effect of LLC Size
1.3%
2.5%

## Slide 265: Accuracy and Coverage with Different Prefetchers
POPET’s accuracy and coverage increases significantly
in absence of a data prefetcher

## Slide 266: Increase in Main Memory Requests

## Slide 267: SIBYL BACKUP
267

## Slide 268: Performance on Unseen Workloads
H&M (H&L) HSS configuration, Sibyl outperforms RNN-HSS and Archivist by 46.1% (54.6%) and 8.5% (44.1%), respectively

## Slide 269: Performance Analysis
Sibyl
Oracle
Baseline policies are ineffective for many workloads even when compared to Slow-Only
RNN-HSS
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Notes: For workloads like prn_1, proj_2, etch baseline policies are ineffeciteve even when compared to slow only policy does places everything in the slow storage

## Slide 270: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
Notes: We evaluate mixing two or more workloads at the same time while randomly varying their relative start times.
Such a scenario
leads to unpredictable execution where requests arrive at dif- ferent, unpredictable timesteps,
mimics distributed workloads,
(3) further tests the ability of Sibyl to dynamically adapt its decision-making policy.
shows average request latency for mixed workloads in two different storage configuration.[click] We use two different settings for Sibyl: (a) Sibyl𝐷𝑒 𝑓 , where we use our default hyper-parameters and (b) Sibyl𝑂𝑝𝑡, where we optimize the hyper-parameters for these mixed workloads

## Slide 271: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
SibylDef outperforms baseline data placement techniques by up to 27.9%
Notes: Sibyl𝐷𝑒 𝑓 provides upto 27.9% higher performance than baseline policies

## Slide 272: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
SibylDef outperforms baseline data placement techniques by up to 27.9%
SibylOpt provides 7.2% higher average performance than SibylDef
Notes: With optimized hyper-parameters, Sibyl𝑂𝑝𝑡 provides 5.2% (9.3%) higher average performance for H&M (H&L) HSS configuration than Sibyl𝐷𝑒 𝑓 .
We conclude that Sibyl can effectively adapt its data placement policy online to highly dynamic workloads.

## Slide 273: Performance With Different Features
Sibyl autonomously decides which features are important to maximize the performance of the running workload

## Slide 274: Sensitivity to Fast Storage Capacity

## Slide 275: Explainability Analysis

## Slide 276: Training and Inference Network
Training and inference networks allow parallel execution
Observation vector as the input
Produces probability distribution of Q-values
Notes: A deep neural network can be prohibitive due to the long time it requires for training and convergence, preventing Sibyl to adapt to new state-action pairs in a timely manner.
Based on experiments, we find that a simple feed-forward network [135] with only two hidden layers [136] provides good performance for Sibyl’s data placement task.
The network takes the observation vector 𝑂𝑡 as its input and produces a probability distribution of Q-values as its output