## Slide 1: QoS-Aware Memory Systems (Wrap Up)
Onur Mutlu
onur@cmu.edu
July 9, 2013
INRIA

## Slide 2: Slides for These Lectures
Architecting and Exploiting Asymmetry in Multi-Core
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture1-asymmetry-jul-2-2013.pptx
A Fresh Look At DRAM Architecture
  http://www.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture2-DRAM-jul-4-2013.pptx
QoS-Aware Memory Systems
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture3-memory-qos-jul-8-2013.pptx
QoS-Aware Memory Systems and Waste Management
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture4-memory-qos-and-waste-management-jul-9-2013.pptx

## Slide 3: Videos for Similar Lectures
Basics (of Computer Architecture)
  http://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Advanced (Longer versions of these lectures)
  http://www.youtube.com/playlist?list=PLVngZ7BemHHV6N0ejHhwOfLwTr8Q-UKXj

## Slide 4: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 5: ATLAS Pros and Cons
Upsides:
  Good at improving overall throughput (compute-intensive threads are prioritized)
  Low complexity
  Coordination among controllers happens infrequently
Downsides:
  Lowest/medium ranked threads get delayed significantly  high unfairness

## Slide 6: TCM: Thread Cluster Memory Scheduling
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling:
Exploiting Differences in Memory Access Behavior" 43rd International Symposium on Microarchitecture (MICRO),
pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)
TCM Micro 2010 Talk

## Slide 7: Previous Scheduling Algorithms are Biased
No previous memory scheduling algorithm provides both the best fairness and system throughput
Chart: Weighted Speedup
| 7.21 | 8.166 | 8.26 | 8.527000000000001 | 8.777999999999998
FCFS | 8.513
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput bias
Fairness bias
Ideal
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
Notes: The problem is that previously proposed scheduling algorithms are biased.
Shown here is a plot, where the x-axis is weighted speedup, a metric of system throughput and system throughput increases as you move towards the right on the x-axis.
The y-axis is maximum slowdown, which is the slowdown of the most unfairly treated thread within a workload. Correspondingly, fairness increases as you move downwards on the y-axis.
Ideally, a memory scheduling algorithm would be situated towards the lower right part of the graph where fairness and system throughput are both high.
However, some previous algorithms are biased towards system throughput, whereas some are biased towards fairness, while others are optimized for neither.
The takeaway is that no previous memory scheduling algorithm provides both the best fairness and system throughput.

## Slide 8: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient
Notes: So why do previous algorithms fail?
On the one hand there is the throughput biased approach that prioritizes less memory-intensive threads.
Servicing memory requests from such threads allow them to make progress in the processor, increasing throughput.
However, the most memory-intensive thread, thread C, remains persistently deprioritized and and becomes prone to starvation causing large slowdowns and, ultimately, unfairness.
On the other hand there is the fairness biased approach where threads take turns accessing the memory.
In this case, the most memory-intensive thread does not starve.
However, the least memory-intensive thread, thread A, is not prioritized, leading to reduced throughput.
As you can see, a single policy applied to all threads is insufficient since different threads have different memory access needs.

## Slide 9: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread
Notes: So how do we achieve the best of both worlds? Our algorithm is based on the following insights:
First, we would like to prioritize the memory-non-intensive threads to increase system throughput.
Doing so does not degrade unfairness, since memory-non-intensive threads are inherently “light” and rarely cause interference for the memory-intensive threads.
For fairness, we discovered that unfairness is usually caused when one memory-intensive thread is prioritized over another.
As we’ve seen, the most deprioritized thread can starve.
To address this problem, we would like to shuffle their priority so that no single thread is persistently prioritized over another thread.
However, memory-intensive threads are not created equal.
They have different vulnerability to memory interference.
To address their differences, shuffling should be performed in an asymmetric manner.

## Slide 10: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Notes: Our algorithm, Thread Cluster Memory Scheduling, first groups threads into two clusters.
Among the threads executing in the system, some are memory-non-intensive whereas some are memory-intensive.
We isolate the memory-non-intensive threads into the non-intensive cluster and the memory-intensive threads into the intensive cluster.
This is so that we can apply different policies for different threads.
Subsequently, we prioritize the non-intensive cluster over the intensive cluster since the non-intensive threads have greater potential for making progress IN THEIR CORES [ONUR].
Finally, we apply different policies within each cluster, one optimized for throughput and the other for fairness.

## Slide 11: Clustering Threads
Step1 Sort threads by MPKI (misses per kiloinstruction)
thread
thread
thread
thread
thread
thread
higher
MPKI
T
α < 10% ClusterThreshold
Intensive
cluster
αT
Non-intensive
cluster
T = Total memory bandwidth usage
Step2 Memory bandwidth usage αT divides clusters
Notes: To group threads into two clusters, we first sort threads according to their MPKI, which stands for last-level cache-misses per kiloinstruction and is a metric of memory intensity.
After sorting, the leftmost thread is the thread with the lowest MPKI.
We then define a quantity called T, which is the total memory bandwidth usage across all threads.
Second, we form the non-intensive cluster by including threads whose bandwidth usage sums up to a certain fraction of the memory bandwidth usage.
That fraction is defined by a parameter called the ClusterThreshold. I will show later in the presentation how adjusting this parameter we can trade off between throughput and fairness.
Lastly, the remaining threads become the intensive cluster.

## Slide 12: Prioritization Between Clusters
  Prioritize non-intensive cluster
Increases system throughput
  Non-intensive threads have greater potential for making progress
Does not degrade fairness
  Non-intensive threads are “light”
  Rarely interfere with intensive threads
>
priority
Notes: Between the two clusters, we statically prioritize the non-intensive cluster [ONUR: fixed plural  singular] so that non-intensive threads’ [ONUR: fixed wording] memory requests are serviced first.
This increases system throughput because non-intensive threads have greater potential for making progress BY QUICKLY RETURNING TO COMPUTE PERIODS IN THEIR CORES [ONUR].
Doing so does not degrade fairness, since non-intensive threads are “light” and consequently rarely interfere with intensive threads. [ONUR: removed “by design”… can be confusing if the listener is not in the right mindset]

## Slide 13: Non-Intensive Cluster
Prioritize threads according to MPKI
Increases system throughput
  Least intensive thread has the greatest potential for making progress in the processor
thread
thread
thread
thread
higher
priority
lowest MPKI
highest MPKI
Notes: Within the memory non-intensive cluster, threads are prioritized according to their memory intensity where the least intensive thread receives the highest priority. [ONUR: replaced latency-sensitive]
This is, again, to increase system throughput. The least intensive thread has the greatest potential for making progress.

## Slide 14: Intensive Cluster
Periodically shuffle the priority of threads
Is treating all threads equally good enough?
BUT: Equal turns ≠ Same slowdown
thread
thread
thread
  Increases fairness
  Most prioritized
higher
priority
thread
thread
thread
Notes: Within the intensive cluster, we periodically shuffle the priority of threads.
By shuffling, we can increase fairness, since every thread is given a fair chance of being the most prioritized.
Treating all threads in an such an equal manner may be good enough in some cases.
But we noticed that in other cases, giving each thread equal turns does not necessarily lead to equal slowdowns.
Specifically, threads are not created equal and some threads are more easily slowed down than others.

## Slide 15: Case Study: A Tale of Two Threads
Chart: Slowdown
| random-access | streaming
Series 1 | 11 | 1
Case Study: Two intensive threads contending
  random-access
  streaming
Prioritize random-access
Prioritize streaming
random-access thread is more easily slowed down
Chart: Slowdown
| random-access | streaming
Series 1 | 1 | 7
7x
prioritized
1x
11x
prioritized
1x
Which is slowed down more easily?
Notes: We illustrate how some threads are more easily slowed down than others using a case study, where two memory-intensive threads are contending for memory: a random-access thread and a streaming thread.
Which of these two threads is slowed down more easily?
In the first case, we prioritize the random-access thread and see that the streaming thread is slowed down by a factor of 7.
In the second case, we prioritize the streaming thread and see that the random-access thread is slowed down by a factor of 11.
Clearly, comparing the two cases, we see that the random-access threads is more easily slowed down.

## Slide 16: Why are Threads Different?
random-access
streaming
req
req
req
req
Bank 1
Bank 2
Bank 3
Bank 4
Memory
rows
All requests parallel
High bank-level parallelism
All requests  Same row
High row-buffer locality
req
req
req
req
activated row
req
req
req
req
req
req
req
req
stuck
Vulnerable to interference
Notes: ONUR: Again, if you prefer, you can use “vulnerable” instead of “susceptible.”
So why are these two threads different?
To explain their difference, we must examine their memory access behavior.
First, the memory comprises multiple memory banks which can be accessed in parallel. [ONUR: removed structurally]
Additionally, each bank is basically a two-dimensional bit-array and comprises multiple rows.
The random access thread distributes its memory requests, to different banks.
Across the banks, the requests are serviced concurrently and their individual latencies are overlapped.
Therefore, the random-access thread has high bank-level parallelism.
On the other hand, the streaming thread sends its memory requests to the same bank.
There it is serviced at the same row over and over again.
When consecutive requests are serviced at the same row, it is called a row-buffer hit and has a lower latency.
Therefore, the streaming thread has higher row-buffer locality.
What would happen if we put those threads together?
For the purpose of illustration, we will assume that the streaming thread is prioritized.
You can see that the random-access thread’s request becomes stuck behind those of the streaming thread at Bank 3.
This breaks the bank-level parallelism of the random-access thread and serializes its latency, leading to reduced performance.
This is why, the random-access thread is more susceptible to interference.
If the two threads were prioritized the other way around, the streaming thread would not be interfered with as much, since the random-access thread has only a single request to Bank 3.

## Slide 17: Niceness
How to quantify difference between threads?
  Vulnerability to interference
Bank-level parallelism
  Causes interference
Row-buffer locality
+
Niceness
-
Niceness
High
Low

## Slide 18: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
 What can go wrong?
A
B
C
D
D
A
B
C
D

## Slide 19: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
 What can go wrong?
A
B
C
D
D
A
B
C
D
A
B
D
C
B
C
A
D
C
D
B
A
D
A
C
B
BAD: Nice threads receive lots of interference
GOOD: Each thread prioritized once

## Slide 20: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
A
B
C
D
D
C
B
A
D

## Slide 21: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
A
B
C
D
D
C
B
A
D
D
A
C
B
B
A
C
D
A
D
B
C
D
A
C
B
GOOD: Each thread prioritized once
GOOD: Least nice thread stays
mostly deprioritized

## Slide 22: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Fairness
Throughput

## Slide 23: TCM: Quantum-Based Operation
Time
Previous quantum (~1M cycles)
During quantum:
Monitor thread behavior
Memory intensity
Bank-level parallelism
Row-buffer locality
Beginning of quantum:
Perform clustering
Compute niceness of intensive threads
Current quantum
(~1M cycles)
Shuffle interval
(~1K cycles)
Notes: Clustering is performed at regular time intervals called quanta.
THIS IS DONE [ONUR] to account for phase changes in threads’ memory access behavior.
During A [ONUR] quantum, TCM monitors each thread’s memory access behavior:
memory intensity, bank-level parallelism, and row-buffer locality.
At the beginning of the next quantum, TCM is invoked to perform clustering and calculate niceness for the intensive threads.
Throughout the quantum, shuffling of the intensive threads is performed periodically.

## Slide 24: TCM: Scheduling Algorithm
Highest-rank: Requests from higher ranked threads prioritized
    Non-Intensive cluster > Intensive cluster
    Non-Intensive cluster: lower intensity  higher rank
    Intensive cluster: rank shuffling
Row-hit: Row-buffer hit requests are prioritized
Oldest: Older requests are prioritized
Notes: To bring it all together, TCM comprises three simple request prioritization rules.
The first is the highest-rank rule, where requests from higher ranked threads are prioritized.
The intensive cluster is prioritized over the non-intensive cluster TO IMPROVE SYSTEM [ONUR] throughput.
Within the intensive cluster, threads are assigned higher rank in the order of decreasing intensity. This, again, is to increase SYSTEM [ONUR] throughput.
Within the non-intensive cluster, the rank of threads are periodically shuffled and does not stay constant, TO ACHIEVE FAIRNESS [ONUR].
As a tie-breaker, the second rule is row-hit where row-buffer hitting requests are prioritized.
Lastly, all else being the same, we prioritize the oldest request.

## Slide 25: TCM: Implementation Cost
Required storage at memory controller (24 cores)
No computation is on the critical path
Thread memory behavior | Storage
MPKI | ~0.2kb
Bank-level parallelism | ~0.6kb
Row-buffer locality | ~2.9kb
Total | < 4kbits
Notes: ONUR: Have a separate bullet saying “No computation is on the processor critical path; Can be approximated.”
Basically, DRAM latency is very long so we can afford to do this computation especially since we are doing it over intervals.
You can have 4 cores in the first bullet and remove the subbullet.

## Slide 26: Previous Work
FRFCFS [Rixner et al., ISCA00]: Prioritizes row-buffer hits
  Thread-oblivious  Low throughput & Low fairness
STFM [Mutlu et al., MICRO07]: Equalizes thread slowdowns
  Non-intensive threads not prioritized  Low throughput
PAR-BS [Mutlu et al., ISCA08]: Prioritizes oldest batch of requests while preserving bank-level parallelism
  Non-intensive threads not always prioritized  Low throughput
ATLAS [Kim et al., HPCA10]: Prioritizes threads with less memory service
  Most intensive thread starves  Low fairness

## Slide 27: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.777999999999998 | 9.179
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput
Notes: This figure shows the performance of the four previous scheduling algorithms in addition to TCM, averaged over 96 workloads.
FRFCFS has low system throughput and fairness.
STFM and PAR-BS is biased towards fairness, while ATLAS is biased towards system throughput.
TCM lies towards the lower right part of the figure and provides the best fairness and system throughput.
Compared to ATLAS, TCM provides approx 5% better throughput and 39% better fairness.
Compared to PAR-BS, TCM provides approx 5% better fairness and 8% better throughput.

## Slide 28: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13.0 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 29: Operating System Support
ClusterThreshold is a tunable knob
  OS can trade off between fairness and throughput
Enforcing thread weights
  OS assigns weights to threads
  TCM enforces thread weights within each cluster

## Slide 30: Conclusion
No previous memory scheduling algorithm provides both high system throughput and fairness
  Problem: They use a single policy for all threads
TCM groups threads into two clusters
  Prioritize non-intensive cluster  throughput
  Shuffle priorities in intensive cluster  fairness
  Shuffling should favor nice threads  fairness
TCM provides the best system throughput and fairness

## Slide 31: TCM Pros and Cons
Upsides:
  Provides both high fairness and high performance
Downsides:
  Scalability to large buffer sizes?
  Effectiveness in a heterogeneous system?

## Slide 32: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 33: SMS: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 34: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 35: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 36: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 37: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 38: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 39: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 40: Stronger Memory Service Guarantees
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA),
Shenzhen, China, February 2013. Slides (pptx)

## Slide 41: Strong Memory Service Guarantees
Goal: Satisfy performance bounds/requirements in the presence of shared main memory, prefetchers, heterogeneous agents, and hybrid memory
Approach:
  Develop techniques/models to accurately estimate the performance of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance

## Slide 42: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu
Notes: Hello everyone. My name is Lavanya Subramanian.
Today, I will present “MISE: Providing perfomance …”.
This is work done in collaboration with my co-authors Vivek ….

## Slide 43: Unpredictable Application Slowdowns
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
An application’s performance depends on
which application it is running with
Notes: This graph shows two applications from the SPEC CPU 2006 suite, leslie3d and gcc. These applications are run on either core of a two core system and share main memory. The y-axis shows each application’s slowdown as compared to when the application is run standalone on the same system.
Now, let’s look at leslie3d. It slows down by 2x when run with gcc.
Let’s look at another case when leslie3d is run with another application, mcf. Leslie now slows down by 5.5x, while it slowed down by 2x when run with gcc. Leslie experiences different slowdowns when run with different applications.
More generally, an application’s performance depends on which applications it is running with. Such performance unpredictability is undesirable….

## Slide 44: Need for Predictable Performance
There is a need for predictable performance
  When multiple applications share resources
  Especially if some applications require performance guarantees
Example 1: In mobile systems
  Interactive applications run with non-interactive applications
  Need to guarantee performance for interactive applications
Example 2: In server systems
  Different users’ jobs consolidated onto the same server
  Need to provide bounded slowdowns to critical jobs
Our Goal: Predictable performance
in the presence of memory interference
Notes: …because there is a need for predictable performance
When multiple applications share resources and
Especially when some applications require guarantees on performance.
For example, in mobile systems, interactive applications are run with non-interactive ones.
And there is a need to provide guarantees on performance to the interactive applications.
In server systems, different users’ jobs are heavily consolidated onto the same server.
In such a scenario, there is a need to achieve bounded slowdowns for critical jobs of users.
These are a couple of examples of systems that need predictable performance.
There are many other systems (such as …) in which performance predictability is necessary.
Therefore, our goal in this work is to provide predictable performance in the presence of memory interference.

## Slide 45: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: First, let me describe the key observations that enable us to estimate application slowdowns.

## Slide 46: Slowdown: Definition
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 47: Key Observation 1
For a memory bound application,
Performance  Memory request service rate
Chart: Normalized Request Service Rate
| 0.358607859 | 0.408507739 | 0.532531575 | 0.580993121999996 | 0.632877307000005 | 0.690879954000007 | 0.726945501000005 | 0.796354682 | 0.837558983 | 0.938360254 | 0.948305607000005 | 1.0
omnetpp | 0.34972 | 0.39891 | 0.5217 | 0.56944 | 0.61954 | 0.67835 | 0.71425 | 0.78346 | 0.8265 | 0.928 | 0.94883 | 1
mcf | 0.34876 | 0.39942 | 0.4869 | 0.53653 | 0.54337 | 0.55102 | 0.58278 | 0.61457 | 0.65149 | 0.74316 | 0.84741 | 0.93386 | 0.9689 | 1
astar | 0.41586 | 0.48052 | 0.66786 | 0.72536 | 0.77686 | 0.79876 | 0.84877 | 0.88035 | 0.92559 | 0.95012 | 0.98596 | 1
Easy
Harder
Intel Core i7, 4 cores
Mem. Bandwidth: 8.5 GB/s
Notes: We observe that for a memory bound application, its performance is roughly proportional to the rate at which its memory requests are serviced.
This plot shows the results of our experiment on an Intel, 4-core system. We run omnetpp, a SPEC CPU 2006 benchmark along with another memory hog, whose memory intensity can be varied. This, in turn, lets us vary the rate at which the memory requests of omnetpp are serviced.
The x-axis shows the normalized request service rate of omnetpp, normalized to when it is run alone.
The y-axis shows the performance of omnetpp, normalized to when it is run alone.
As can be seen, there is a very strong, y=x like correlation between request service rate and performance.
We observe the same trend for various memory bound applications. Here are a couple of more examples.
Therefore, memory request service rate can be used as a proxy for performance.
Now, going back to the slowdown equation. We can replace performance by request service rate, based on our first observation, enabling us to express slowdown as the ratio of alone to shared request service rates.
Shared request service rate can be measured in a relatively straightforward manner when an application is run along with other applications.
Measuring alone request service rate, without actually running an application alone is harder. This is where our second observation comes into play.

## Slide 48: Key Observation 2
Request Service Rate Alone (RSRAlone) of an application can be estimated by giving the application highest priority in accessing memory
Highest priority  Little interference
(almost as if the application were run alone)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 49: Key Observation 2
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 50
Memory Interference-induced Slowdown Estimation (MISE) model for memory bound applications
Notes: Based on these two observations, our memory interference induced slowdown estimation (MISE) model for memory bound applications is as follows. Now, let’s analyze why this request service rate ratio based model holds for memory bound applications

## Slide 51: Key Observation 3
Memory-bound application
No interference
Compute Phase
Memory Phase
With interference
Memory phase slowdown dominates overall slowdown
time
time
Req
Req
Req
Req
Req
Req
Notes: A memory-bound application spends significant fraction of its execution time waiting for memory.
Let’s first look at the case when a memory-bound application is not receiving any interference.
The application does a small amount of compute at the core and then sends out a bunch of memory requests. The application cannot do any more compute until these requests are serviced.
Now, when this application experiences interference, the length of its compute phase does not change. However, the time taken to service the memory requests increases. In essence, since the application spends most of its time in the memory phase, the memory induced slowdown of the application dominates the overall slowdown of the application.

## Slide 52: Key Observation 3
Non-memory-bound application
time
time
No interference
Compute Phase
Memory Phase
With interference
Only memory fraction ( ) slows down with interference
Memory Interference-induced Slowdown Estimation (MISE) model for non-memory bound applications
Notes: However, this is not the case for a non-memory-bound application.
A non-memory-bound application spends a sizeable fraction of its time doing compute at the core and a smaller fraction of time waiting for memory. When the application experiences interference, the length of the compute phase does not change, whereas the memory phase slows down with interference.
Specifically, if alpha is the fraction of time the application spends in the memory phase, then 1 – alpha is the fraction of time it spends in the compute phase. The 1 – alpha fraction does not change with memory interference, however the alpha fraction slows down as the ratio of request service rate alone to request service rate shared.
We augment the MISE model to take this into account. Slowdown for non-memory-bound applications can be expressed as the sum of two quantities - 1 – alpha, the compute fraction that does not change with interference and the memory induced slowdown.

## Slide 53: Measuring RSRShared and α
Request Service Rate Shared (RSRShared)
  Per-core counter to track number of requests serviced
  At the end of each interval, measure
Memory Phase Fraction ( )
  Count number of stall cycles at the core
  Compute fraction of cycles stalled for memory
Notes: Shared request service rate can be measured using per-core counters to track the number of requests serviced during each interval.
At the end of the interval, SRSR can be computed as the number of requests serviced divided by the length of the interval.
Memory phase fraction of each application can be computed by counting the number of cycles the core stalls waiting for memory and then computing what fraction are these cycles of the interval length.
Measuring SRSR and alpha is the straightforward part. Now, for the more interesting part, estimating alone request service rate.

## Slide 54: Estimating Request Service Rate Alone (RSRAlone)
Divide each interval into shorter epochs
At the beginning of each epoch
  Memory controller randomly picks an application as the highest priority application
At the end of an interval, for each application, estimate
Goal: Estimate RSRAlone
How: Periodically give each application highest priority in accessing memory
Notes: Our goal is to estimate alone request service rate. To do this, we periodically give each application the highest priority in accessing memory, based on observation 2.
How exactly do we do this. First, each interval is divided into shorter epochs. At the beginning of each epoch, the memory controller picks one application at random and designates it the highest priority application. This way each application is given highest priority at different epochs during the interval.
At the end of the interval, ARSR is estimated for each application as the ratio of the number of requests of the application serviced during the high priority epochs to the number of cycles the application was given highest priority.
Now, is this an accurate way of estimating ARSR. It turns out not. We have been ignoring an inaccuracy all along.

## Slide 55: Inaccuracy in Estimating RSRAlone
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
When an application has highest priority
  Still experiences some interference
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
Time units
Service order
Main Memory
1
2
3
Interference Cycles
High Priority
Main Memory
Time units
Service order
Main Memory
1
2
3
Request Buffer
State
Notes: That is, even when an application has highest priority, it still experiences some interference from other applications.
Here is an example showing why.
The red application has highest priority and is run along with another application, the blue application. First, there is just one request in the request buffer and it is from the red application. Since this is the only request, it is scheduled by the memory controller and completes in one time unit.
While this request is being serviced, there comes another request from the blue application. Our memory controller is work conserving and schedules another application’s request, if there is no request from the red application. So, it schedules the blue application’s request next.
However, just as the blue application’s request is being scheduled comes another request from the red application. Ideally, we would like to pre-empt the blue application’s request. However, because of the way DRAM operates, preempting the blue application’s request incurs overhead. Therefore, the red application’s request would have to wait until the blue application’s request completes and only then is it serviced. These extra cycles that the red application spent waiting for the blue application’s request to complete are interference cycles that it would not have experienced had it been running alone.

## Slide 56: Accounting for Interference in RSRAlone Estimation
Solution: Determine and remove interference cycles from RSRAlone calculation
A cycle is an interference cycle if
  a request from the highest priority application is waiting in the request buffer and
  another application’s request was issued previously
Notes: The solution to account for this interference is to determine and remove such interference cycles from the ARSR computation.
How we do this is to subtract these cycles from the number of high priority epoch cycles.
Now, the question is how do we determine which cycles are interference cycles.
We deem a cycle an interference cycle if …. (read from slide)

## Slide 57: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having described the key observations behind our model and its implementation, we will put it all together

## Slide 58: MISE Model: Putting it All Together
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 59: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu+, MICRO ‘07]
  FST (Fairness via Source Throttling) [Ebrahimi+, ASPLOS ‘10]
  Per-thread Cycle Accounting [Du Bois+, HiPEAC ‘13]
Basic Idea:
Hard
Easy
Count number of cycles application receives interference
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 60: Two Major Advantages of MISE Over STFM
Advantage 1:
  STFM estimates alone performance while an application is receiving interference  Hard
  MISE estimates alone performance while giving an application the highest priority  Easier
Advantage 2:
  STFM does not take into account compute phase for non-memory-bound applications
  MISE accounts for compute phase  Better accuracy
Notes: Let me now present the two major advantages of MISE over STFM, qualitatively.
First, STFM estimates alone performance of an application while it is receiving interference. This is hard because of BLP effects.
MISE addresses this difficulty by giving an application highest priority and then estimating its alone performance.
Second, STFM does not take into account compute phase for non-mem-bound applications. MISE accounts for compute phase and hence achieves better accuracy.

## Slide 61: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1066 DRAM
  512 KB private cache/core
Workloads
  SPEC CPU2006
  300 multi programmed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 62: Quantitative Comparison
Chart: Million Cycles
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 2.7467 | 2.8146 | 2.981 | 2.6916 | 3.5156 | 2.4446 | 3.3601 | 3.2667 | 2.8783 | 2.9401 | 2.7229 | 2.9719 | 2.71 | 2.1736 | 2.0285 | 2.4098 | 2.0056 | 2.2585 | 2.1279 | 2.4625
STFM | 1.8517 | 1.9219 | 1.8786 | 1.8294 | 1.9487 | 1.8759 | 1.7936 | 1.7677 | 1.83 | 1.817 | 1.7232 | 1.7709 | 1.704 | 1.6746 | 1.6715 | 1.7352 | 1.6427 | 1.7084 | 1.6918 | 1.7477
MISE | 2.6655 | 2.8713 | 2.8244 | 2.6053 | 3.1741 | 2.6867 | 3.5471 | 3.4317 | 3.3 | 2.6747 | 2.8604 | 3.0821 | 2.8909 | 2.235 | 2.1161 | 2.3639 | 1.999 | 2.0667 | 2.1632 | 2.3161
SPEC CPU 2006 application
leslie3d
Notes: This graph shows the actual slowdown of leslie3d, a memory-bound application, with time (in million cycles).
Here are slowdown estimates from STFM and here are slowdown estimates from MISE. As can be seen, MISE’s slowdown estimates are much closer to the actual slowdowns. This is because MISE estimates leslie’s alone performance while giving it highest priority, whereas STFM tries to estimate it while leslie receives interference from other applications.

## Slide 63: Comparison to STFM
cactusADM
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.495 | 1.5295 | 1.6709 | 1.5475 | 1.6605 | 1.5731 | 1.9783 | 1.7095 | 1.5337 | 1.5256 | 1.4754 | 1.5235 | 1.5214 | 1.7913 | 1.6855 | 1.6301 | 1.5933 | 1.6732 | 1.5495 | 1.6973
STFM | 1.25 | 1.3555 | 1.3435 | 1.3721 | 1.3293 | 1.3149 | 1.2341 | 1.3128 | 1.3228 | 1.3579 | 1.3509 | 1.344 | 1.4008 | 1.3967 | 1.5397 | 1.5867 | 1.5517 | 1.5683 | 1.5638 | 1.3614
MISE | 1.5723 | 1.5685 | 1.6897 | 1.5829 | 1.73 | 1.6866 | 2.1706 | 1.8114 | 1.5947 | 1.5898 | 1.5347 | 1.5537 | 1.6001 | 1.8673 | 1.7348 | 1.6758 | 1.6313 | 1.7322 | 1.6362 | 1.7298
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.7536 | 1.697 | 1.8734 | 1.7248 | 1.9225 | 1.6413 | 1.9296 | 2.1339 | 2.0504 | 1.9754 | 1.8732 | 2.1705 | 2.0085 | 2.239 | 2.2425 | 2.2469 | 1.9042 | 2.3715 | 2.0927 | 2.5902
STFM | 1.3661 | 1.3843 | 1.3635 | 1.3908 | 1.3589 | 1.35 | 1.3746 | 1.5894 | 1.5811 | 1.5995 | 1.5987 | 1.5832 | 1.5771 | 2.0246 | 1.9878 | 1.9883 | 1.9797 | 1.9406 | 1.9709 | 1.9629
MISE | 1.8607 | 1.9645 | 1.9765 | 1.8835 | 2.5202 | 1.8326 | 2.2231 | 2.3347 | 2.178 | 2.097 | 2.1736 | 2.1054 | 2.0591 | 2.3181 | 2.2502 | 2.3946 | 2.1703 | 2.5387 | 2.2735 | 2.6647
GemsFDTD
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.9414 | 2.1412 | 2.406 | 2.0632 | 2.7223 | 2.6572 | 3.1068 | 3.1879 | 2.6035 | 2.4937 | 2.4704 | 2.8774 | 2.6478 | 2.6947 | 2.7804 | 2.9653 | 2.8228 | 2.5796 | 2.6027 | 2.7846
STFM | 1.5023 | 1.4705 | 1.8931 | 1.4971 | 1.6676 | 1.6306 | 1.8055 | 1.7004 | 1.5827 | 1.7021 | 1.7571 | 1.8054 | 1.974 | 2.2827 | 2.3098 | 2.107 | 1.6316 | 2.0168 | 2.0447 | 2.0375
MISE | 1.916 | 2.3469 | 2.5021 | 2.481 | 2.7434 | 2.413 | 3.2611 | 3.5557 | 2.6948 | 2.6542 | 3.0171 | 2.4489 | 2.5681 | 2.7574 | 3.1405 | 3.0343 | 2.527 | 2.8438 | 3.1033 | 3.2769
soplex
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0179 | 1.0228 | 1.5311 | 1.2016 | 1.0185 | 1.0121 | 1.0059 | 1.0071 | 1.1261 | 1.5714 | 1.0808 | 1.0167 | 1.0097 | 1.2303 | 1.0956 | 1.0308 | 1.0187 | 1.3242 | 1.3257 | 1.0134
STFM | 2.6564 | 2.8136 | 2.323 | 1.9913 | 2.1243 | 2.8472 | 2.9844 | 2.4594 | 2.5397 | 2.2388 | 3.0174 | 2.8437 | 3.3951 | 3.9402 | 2.5308 | 2.8686 | 3.3191 | 2.5052 | 2.3033 | 2.0445
MISE | 1.0005 | 1.0032 | 1.7563 | 1.0691 | 0.99707 | 1.0011 | 1.0016 | 0.99869 | 1.0593 | 1.3748 | 1.0555 | 1.0003 | 1.0006 | 1.0639 | 1.0105 | 0.98886 | 1.0009 | 0.9221 | 1.0907 | 1.0039
wrf
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0394 | 1.0432 | 1.0258 | 1.0358 | 1.031 | 1.0316 | 1.0304 | 1.0232 | 1.0226 | 1.0158 | 1.0543 | 1.0328 | 1.0751 | 1.0632 | 1.0517 | 1.053 | 1.029 | 1.0322 | 1.031 | 1.0246
STFM | 2.1276 | 2.0414 | 1.9127 | 1.8201 | 2.3708 | 1.9609 | 1.9559 | 2.062 | 2.2477 | 2.173 | 3.9673 | 2.3084 | 2.4138 | 2.5477 | 2.8093 | 2.6087 | 2.1795 | 1.9627 | 1.8871 | 2.0011
MISE | 1.0191 | 1.0068 | 1.0168 | 0.98223 | 1.031 | 0.96844 | 1.0017 | 1.0177 | 0.99417 | 1.0091 | 1.0383 | 1.0293 | 1.0276 | 1.0128 | 1.0242 | 1.0231 | 0.99687 | 1.0223 | 0.89507 | 1.0191
calculix
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0008 | 1.0011 | 1.0029 | 1.0014 | 1.0016 | 1.0015 | 1.0038 | 1.0016 | 1.0011 | 1.0034 | 1.0391 | 1.1297 | 1.0014 | 1.0018 | 1.0019 | 1.002 | 1.0012 | 1.0008 | 1.0011 | 1.0012
STFM | 2.5587 | 2.6401 | 2.5897 | 1.8924 | 2.9635 | 3.1523 | 2.659 | 2.2124 | 3.2205 | 2.9929 | 3.5898 | 2.7107 | 2.1336 | 3.0915 | 3.0289 | 3.0638 | 3.0873 | 2.3554 | 2.7464 | 2.2834
MISE | 1.0002 | 1.0002 | 1.0015 | 1.0003 | 1.0007 | 0.99984 | 1.0012 | 0.99949 | 0.99671 | 1.0015 | 0.99044 | 0.86466 | 1.0003 | 1.0004 | 1.0006 | 0.99474 | 0.99903 | 0.99882 | 1.0001 | 1.0004
povray
Average error of MISE: 8.2%
Average error of STFM: 29.4%
(across 300 workloads)
Notes: Several more applications. For most applications, MISE’s slowdown estimates are more accurate.
On average, MISE’s error is 8.2%, while STFM’s error is 29.4%, across our 300 workloads.

## Slide 64: Providing “Soft” Slowdown Guarantees
Goal
  1. Ensure QoS-critical applications meet a prescribed slowdown bound
  2. Maximize system performance for other applications
Basic Idea
  Allocate just enough bandwidth to QoS-critical application
  Assign remaining bandwidth to other applications
Notes: The goal of this mechanism is to .. <read off slide>.
The basic idea is to allocate just enough bandwidth the QoS-critical application, while assigning the remaining bandwidth among the other applications.

## Slide 65: MISE-QoS: Mechanism to Provide Soft QoS
Assign an initial bandwidth allocation to QoS-critical application
Estimate slowdown of QoS-critical application using the MISE model
After every N intervals
  If slowdown > bound B +/- ε, increase bandwidth allocation
  If slowdown < bound B +/- ε, decrease bandwidth allocation
When slowdown bound not met for N intervals
  Notify the OS so it can migrate/de-schedule jobs
Notes: SLIDE NEEDS WORK

## Slide 66: Methodology
Each application (25 applications in total) considered the QoS-critical application
Run with 12 sets of co-runners of different memory intensities
Total of 300 multiprogrammed workloads
Each workload run with 10 slowdown bound values
Baseline memory scheduling mechanism
  Always prioritize QoS-critical application
  [Iyer+, SIGMETRICS 2007]
  Other applications’ requests scheduled in FRFCFS order
  [Zuravleff +, US Patent 1997, Rixner+, ISCA 2000]
Notes: Read off slide

## Slide 67: A Look at One Workload
Chart: Slowdown
| leslie3d | hmmer | lbm | omnetpp
AlwaysPrioritize | 1.9301 | 2.511 | 2.8159 | 2.7346
MISE-QoS-10/1 | 2.8374 | 2.2769 | 2.0523 | 2.0142
MISE-QoS-10/3 | 2.6976 | 2.3196 | 2.1221 | 2.084
MISE-QoS-10/5 | 2.0128 | 2.5056 | 2.6593 | 2.5534
MISE-QoS-10/7 | 1.9063 | 2.508 | 2.8014 | 2.6609
MISE-QoS-10/9 | 1.9063 | 2.508 | 2.8014 | 2.6609
QoS-critical
non-QoS-critical
MISE is effective in
meeting the slowdown bound for the QoS-critical application
improving performance of non-QoS-critical applications
Slowdown Bound = 10
Slowdown Bound = 3.33
Slowdown Bound = 2

## Slide 68: Effectiveness of MISE in Enforcing QoS
 | Predicted Met | Predicted Not Met
QoS Bound Met | 78.8% | 2.1%
QoS Bound Not Met | 2.2% | 16.9%
Across 3000 data points
MISE-QoS meets the bound for 80.9% of workloads
AlwaysPrioritize meets the bound for 83% of workloads
MISE-QoS correctly predicts whether or not the bound is met for 95.7% of workloads

## Slide 69: Performance of Non-QoS-Critical Applications
Chart: Number of Memory Intensive Applications
| 0 | 1 | 2 | 3 | Avg
AlwaysPrioritize | 1.2932 | 0.92684 | 0.63783 | 0.47247 | 0.83259
MISE-QoS-10/1 | 1.3105 | 1.0515 | 0.75708 | 0.556 | 0.91875
MISE-QoS-10/3 | 1.3105 | 1.0471 | 0.75276 | 0.54982 | 0.91504
MISE-QoS-10/5 | 1.3104 | 1.0268 | 0.71476 | 0.51722 | 0.89229
MISE-QoS-10/7 | 1.3101 | 0.96233 | 0.65406 | 0.47556 | 0.85051
MISE-QoS-10/9 | 1.2966 | 0.92898 | 0.64287 | 0.47149 | 0.83499
Higher performance when bound is loose
When slowdown bound is 10/3
MISE-QoS improves system performance by 10%

## Slide 70: Other Results in the Paper
Sensitivity to model parameters
  Robust across different values of model parameters
Comparison of STFM and MISE models in enforcing soft slowdown guarantees
  MISE significantly more effective in enforcing guarantees
Minimizing maximum slowdown
  MISE improves fairness across several system configurations

## Slide 71: Summary
Uncontrolled memory interference slows down applications unpredictably
Goal: Estimate and control slowdowns
Key contribution
  MISE: An accurate slowdown estimation model
  Average error of MISE: 8.2%
Key Idea
  Request Service Rate is a proxy for performance
  Request Service Rate Alone estimated by giving an application highest priority in accessing memory
Leverage slowdown estimates to control slowdowns
  Providing soft slowdown guarantees
  Minimizing maximum slowdown

## Slide 72: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu

## Slide 73: Memory Scheduling for Parallel Applications
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin,
Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 74: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread that is falling behind the most in a parallel for loop
PAMS Micro 2011 Talk

## Slide 75: Aside: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA),
pages 39-50, Beijing, China, June 2008. Slides (pptx)

## Slide 76: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to optimize for performance (in the presence of constraints)
  Reordering is not simple
  Predicting the future?

## Slide 77: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 78: More on DRAM Operation and Constraints
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 79: Self-Optimizing DRAM Controllers
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.

## Slide 80: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 81: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 82: Performance Results

## Slide 83: QoS-Aware Memory Systems: The Dumb Resources Approach

## Slide 84: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 85: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 86: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
86

## Slide 87: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 88: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 89: Fairness via Source Throttling (FST) [ASPLOS’10]
89
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 90: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 91: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control

## Slide 92: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 93: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 94: Another Way to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 95: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 96: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 97: Summary: Memory QoS
Technology, application, architecture trends dictate new needs from memory system
A fresh look at (re-designing) the memory hierarchy
  Scalability: DRAM-System Codesign and New Technologies
  QoS: Reducing and controlling main memory interference: QoS-aware memory system design
  Efficiency: Customizability, minimal waste, new technologies
QoS-unaware memory: uncontrollable and unpredictable
Providing QoS awareness improves performance, predictability, fairness, and utilization of the memory system

## Slide 98: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request/thread scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 99: Cache Potpourri: Managing Waste
Onur Mutlu
onur@cmu.edu
July 9, 2013
INRIA

## Slide 100: More Efficient Cache Utilization
Compressing redundant data
Reducing pollution and thrashing

## Slide 101: Base-Delta-Immediate Cache Compression
Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 102: Executive Summary
Off-chip memory latency is high
  Large caches can help, but at significant cost
Compressing data in cache enables larger cache at low cost
Problem: Decompression is on the execution critical path
Goal: Design a new compression scheme that has
1. low decompression latency, 2. low cost, 3. high compression ratio
Observation: Many cache lines have low dynamic range data
Key Idea: Encode cachelines as a base + multiple differences
Solution: Base-Delta-Immediate compression with low decompression latency and high compression ratio
  Outperforms three state-of-the-art compression mechanisms

## Slide 103: Motivation for Cache Compression
Significant redundancy in data:
0x00000000
How can we exploit this redundancy?
  Cache compression helps
  Provides effect of a larger cache without making it physically larger
0x0000000B
0x00000003
0x00000004
…

## Slide 104: Background on Cache Compression
Key requirements:
  Fast (low decompression latency)
  Simple (avoid complex hardware changes)
  Effective (good compression ratio)
CPU
L2 Cache
Uncompressed
Compressed
Decompression
Uncompressed
L1 Cache
Hit

## Slide 105: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 

## Slide 106: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 

## Slide 107: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 

## Slide 108: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 
Our proposal: BΔI |  |  | 

## Slide 109: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 110: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 111: How Common Are These Patterns?
Chart: Cache Coverage (%)
| libquantum | lbm | mcf | tpch17 | sjeng | omnetpp | tpch2 | sphinx3 | xalancbmk | bzip2 | tpch6 | leslie3d | apache | gromacs | astar | gobmk | soplex | gcc | hmmer | wrf | h264ref | zeusmp | cactusADM | GemsFDTD | Average
Zero | 1.2e-05 | 7e-06 | 0.008911 | 0.033323 | 0.032362 | 2.7e-05 | 0.065765 | 0.022031 | 0.000272 | 0.000176 | 0.12314 | 0.16955 | 0.072498 | 0.065675 | 0.016314 | 0.34373 | 0.26863 | 0.30068 | 0.003261 | 0.81434 | 0.00837 | 0.83736 | 0.66632 | 0.99428 | 0.20196
Repeated Values | 0.0001 | 6.5e-05 | 0.0001 | 0.000508 | 0.000146 | 0.0001 | 0.000529 | 0.008812 | 2e-06 | 0.036901 | 0.002005 | 0.095993 | 0.005072 | 0.010873 | 0.005914 | 0.020917 | 0.29969 | 0.038812 | 0.031345 | 0.083856 | 0.006414 | 0.13684 | 0.32178 | 0.001628 | 0.046184
Other Patterns | 0.000177 | 0.000138 | 0.060209 | 0.045394 | 0.070763 | 0.11701 | 0.075432 | 0.1168 | 0.21336 | 0.18863 | 0.12998 | 0.016265 | 0.23912 | 0.24082 | 0.42076 | 0.086109 | 0.18536 | 0.45647 | 0.84697 | 0.017818 | 0.91843 | 0.000306 | 0.000699 | 0.000345 | 0.18531
SPEC2006, databases, web workloads, 2MB L2 cache
“Other Patterns” include Narrow Values
  43% of the cache lines belong to key patterns

## Slide 112: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves

## Slide 113: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio

## Slide 114: Can We Do Better?
Uncompressible cache line (with a single base):
Key idea:
Use more bases, e.g., two instead of one
Pro:
  More cache lines can be compressed
Cons:
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…

## Slide 115: B+Δ with Multiple Arbitrary Bases
Chart: Compression Ratio
| GeoMean
1 | 1.3961
2 | 1.5113
3 | 1.4982
4 | 1.4326
8 | 1.3118
10 | 1.2742
16 | 1.2242
   2 bases – the best option based on evaluations

## Slide 116: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
Advantages over 2 arbitrary bases:
  Better compression ratio
  Simpler compression logic
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 117: B+Δ (with two arbitrary bases) vs. BΔI
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
B+Δ (2 bases) | 1.0625 | 1.0125 | 1.0254 | 1.1979 | 1.1332 | 1.375 | 1.7477 | 1.5346 | 1.3347 | 1.2446 | 1.5238 | 1.447 | 1.2608 | 1.4753 | 1.7447 | 1.3954 | 1.9793 | 1.7868 | 1.9739 | 1.9919 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5113
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
  Average compression ratio is close, but BΔI is simpler

## Slide 118: BΔI Implementation
Decompressor Design
  Low latency
Compressor Design
  Low cost and complexity
BΔI Cache Organization
  Modest complexity

## Slide 119: BΔI Decompressor Design
Δ0
B0
Δ1
Δ2
Δ3
Compressed Cache Line
V0
V1
V2
V3
+
+
Uncompressed Cache Line
+
+
B0
Δ0
B0
B0
B0
B0
Δ1
Δ2
Δ3
V0
V1
V2
V3
  Vector addition

## Slide 120: BΔI Compressor Design
32-byte Uncompressed Cache Line
8-byte B0
1-byte Δ
CU
8-byte B0
2-byte Δ
CU
8-byte B0
4-byte Δ
CU
4-byte B0
1-byte Δ
CU
4-byte B0
2-byte Δ
CU
2-byte B0
1-byte Δ
CU
Zero
CU
Rep.
Values
CU
Compression Selection Logic (based on compr. size)
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
Compression Flag & Compressed Cache Line
CFlag &
CCL
Compressed Cache Line

## Slide 121: BΔI Compression Unit: 8-byte B0 1-byte Δ
32-byte Uncompressed Cache Line
V0
V1
V2
V3
8 bytes
-
-
-
-
B0=
V0
V0
B0
B0
B0
B0
V0
V1
V2
V3
Δ0
Δ1
Δ2
Δ3
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Is every element within 1-byte range?
Δ0
B0
Δ1
Δ2
Δ3
B0
Δ0
Δ1
Δ2
Δ3
Yes
No

## Slide 122: BΔI Cache Organization
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
Conventional 2-way cache with 32-byte cache lines
BΔI: 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments
2.3% overhead for 2 MB cache

## Slide 123: Qualitative Comparison with Prior Work
Zero-based designs
  ZCA [Dusser+, ICS’09]: zero-content augmented cache
  ZVC [Islam+, PACT’09]: zero-value cancelling
  Limited applicability (only zero values)
FVC [Yang+, MICRO’00]: frequent value compression
  High decompression latency and complexity
Pattern-based compression designs
  FPC [Alameldeen+, ISCA’04]: frequent pattern compression
    High decompression latency (5 cycles) and complexity
  C-pack [Chen+, T-VLSI Systems’10]: practical implementation of FPC-like algorithm
    High decompression latency (8 cycles)

## Slide 124: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 125: Methodology
Simulator
  x86 event-driven simulator based on Simics [Magnusson+, Computer’02]
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  4GHz, x86 in-order core, 512kB - 16MB L2, simple memory model (300-cycle latency for row-misses)

## Slide 126: Compression Ratio: BΔI vs. Prior Work
BΔI achieves the highest compression ratio
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
ZCA | 1 | 1.0125 | 1.0002 | 1.0055 | 1.0288 | 1 | 1.1561 | 1.0914 | 1.0241 | 1 | 1.0005 | 1.1898 | 1 | 1.1083 | 1.0549 | 1 | 1.0013 | 1.2794 | 1.9738 | 1.5235 | 1.5406 | 1.801 | 1.9951 | 1.9966 | 1.2005
FVC | 1.0297 | 1.0125 | 1.0012 | 1.017 | 1.1457 | 1.4988 | 1.1857 | 1.1438 | 1.4157 | 1.3573 | 1.0143 | 1.4596 | 1.3574 | 1.3745 | 1.1968 | 1.3874 | 1.9381 | 1.7894 | 1.9738 | 1.9859 | 1.9598 | 1.9947 | 1.995 | 1.9966 | 1.4212
FPC | 1.004 | 1.0125 | 1.0225 | 1.0568 | 1.2307 | 1.3121 | 1.1774 | 1.4064 | 1.4705 | 1.5235 | 1.5442 | 1.5994 | 1.5763 | 1.7269 | 1.2651 | 1.6749 | 1.9072 | 1.9167 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5149
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
1.53
SPEC2006, databases, web workloads, 2MB L2

## Slide 127: Single-Core: IPC and MPKI
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 1.0859 | 1.1498 | 1.1819 | 1.2753 | 1.3788
BΔI | 1.0817 | 1.1425 | 1.2085 | 1.2401 | 1.346 | 1.4285
8.1%
5.2%
5.1%
4.9%
5.6%
3.6%
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 0.819 | 0.59143 | 0.46593 | 0.37544 | 0.27527
BΔI | 0.84292 | 0.62368 | 0.466 | 0.40552 | 0.30364 | 0.23666
16%
24%
21%
13%
19%
14%
BΔI achieves the performance of a 2X-size cache
Performance improves due to the decrease in MPKI

## Slide 128: Multi-Core Workloads
Application classification based on
  Compressibility: effective cache size increase
  (Low Compr. (LC) < 1.40, High Compr. (HC) >= 1.40)
  Sensitivity: performance gain with more cache
  (Low Sens. (LS) < 1.10, High Sens. (HS) >= 1.10; 512kB -> 2MB)
Three classes of applications:
  LCLS, HCLS, HCHS, no LCHS applications
For 2-core - random mixes of each possible class pairs (20 each, 120 total workloads)

## Slide 129: Multi-Core: Weighted Speedup
BΔI performance improvement is the highest (9.5%)
Chart: Normalized Weighted Speedup
| LCLS - LCLS | LCLS - HCLS | HCLS - HCLS | LCLS - HCHS | HCLS - HCHS | HCHS - HCHS | Low Sensitivity | High Sensitivity | GeoMean
ZCA | 1.0268 | 1.0154 | 1.0259 | 1.0182 | 1.1193 | 1.01 | 1.0353
FVC | 1.0277 | 1.0179 | 1.0345 | 1.0727 | 1.1468 | 1.08 | 1.0624
FPC | 1.0312 | 1.0197 | 1.0276 | 1.1 | 1.1495 | 1.176 | 1.0822
BΔI | 1.0446 | 1.0342 | 1.0431 | 1.1091 | 1.1651 | 1.18 | 1.0944
If at least one application is sensitive, then the performance improves

## Slide 130: Other Results in Paper
IPC comparison against upper bounds
  BΔI almost achieves performance of the 2X-size cache
Sensitivity study of having more than 2X tags
  Up to 1.98 average compression ratio
Effect on bandwidth consumption
  2.31X decrease on average
Detailed quantitative comparison with prior work
Cost analysis of the proposed changes
  2.3% L2 cache area increase

## Slide 131: Conclusion
A new Base-Delta-Immediate compression mechanism
Key insight: many cache lines can be efficiently represented using base + delta encoding
Key properties:
  Low latency decompression
  Simple hardware implementation
  High compression ratio with high coverage
Improves cache hit ratio and performance of both single-core and multi-core workloads
  Outperforms state-of-the-art cache compression techniques: FVC and FPC

## Slide 132: The Evicted-Address Filter
Vivek Seshadri, Onur Mutlu, Michael A. Kozuch, and Todd C. Mowry, "The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 133: Executive Summary
Two problems degrade cache performance
  Pollution and thrashing
  Prior works don’t address both problems concurrently
Goal: A mechanism to address both problems
EAF-Cache
  Keep track of recently evicted block addresses in EAF
  Insert low reuse with low priority to mitigate pollution
  Clear EAF periodically to mitigate thrashing
  Low complexity implementation using Bloom filter
EAF-Cache outperforms five prior approaches that address pollution or thrashing
Notes: …

## Slide 134: Cache Utilization is Important
Core
Last-Level Cache
Memory
Core
Core
Core
Core
Increasing contention
Effective cache utilization is important
Large latency
Notes: All high-performance processors employ on-chip caches.
In most modern systems, multiple cores share the last-level cache.
With the large latency of main memory access and increasing contention between multiple cores, effective cache utilization is critical for system performance.
For effective cache utilization, the cache should be filled with blocks that are likely to be reused.

## Slide 135: Reuse Behavior of Cache Blocks
A
B
C
A
B
C
S
T
U
V
W
X
Y
A
B
C
Different blocks have different reuse behavior
Access Sequence:
High-reuse block
Low-reuse block
Z
Ideal Cache
A
B
C
.
.
.
.
.
Notes: However, different blocks have different reuse behaviors.
For example, consider the following access sequence.
Blocks A, B and C are accessed repeatedly.
We refer to such blocks as High reuse blocks.
On the other hand, the remaining blocks are not reused. We refer to such blocks as low-reuse blocks.
Ideally, the cache should be filled with high-reuse blocks such as A, B and C.
But traditional cache management policies such as LRU suffer from two problems.

## Slide 136: Cache Pollution
H
G
F
E
D
C
B
A
S
H
G
F
E
D
C
B
T
S
H
G
F
E
D
C
U
T
S
H
G
F
E
D
MRU
LRU
LRU Policy
Prior work: Predict reuse behavior of missed blocks. Insert low-reuse blocks at LRU position.
H
G
F
E
D
C
B
A
S
T
U
MRU
LRU
A
B
A
C
B
A
A
S
A
T
S
A
Cache
Problem: Low-reuse blocks evict high-reuse blocks
Notes: The first problem, referred to as cache pollution, is one where blocks with low-reuse evict blocks with high-reuse from the cache.
Consider the following example of a cache following the LRU policy. Although the cache is filled with high–reuse blocks, the LRU policy inserts even blocks with low-reuse at the MRU position, evicting more useful blocks from the cache. So the future accesses to blocks A, B and C will miss in the cache.
To address this problem, prior work proposed the idea of predicting the reuse behavior of missed cache blocks and inserting low-reuse blocks at the LRU position. This mitigates the impact of pollution as shown in the example.

## Slide 137: Cache Thrashing
H
G
F
E
D
C
B
A
I
H
G
F
E
D
C
B
J
I
H
G
F
E
D
C
K
J
I
H
G
F
E
D
MRU
LRU
LRU Policy
A
B
C
D
E
F
G
H
I
J
K
A
B
A
C
B
A
Prior work: Insert at MRU position with a very low probability (Bimodal insertion policy)
Cache
H
G
F
E
D
C
B
A
I
J
K
MRU
LRU
A
I
A
J
I
A
A fraction of working set stays in cache
Cache
Problem: High-reuse blocks evict each other
Notes: The second problem, referred to as thrashing, occurs when the number of high-reuse blocks is more than what the cache can handle, as shown in the example.
In this case, the LRU policy leads to these high-reuse blocks evicting each other from the cache, leading to zero cache hits.
Prior work proposed to achieve this using the bimodal insertion policy, which inserts blocks at the MRU position with a very low probability.
As a result, majority of the blocks are inserted at the LRU position.
For a thrashing working set, this results in a fraction of the working set to be retained in the cache, leading to cache hits for at least that fraction.

## Slide 138: Shortcomings of Prior Works
Prior works do not address both pollution and thrashing concurrently
Prior Work on Cache Pollution
No control on the number of blocks inserted with high priority into the cache
Prior Work on Cache Thrashing
No mechanism to distinguish high-reuse blocks from low-reuse blocks
Our goal: Design a mechanism to address both pollution and thrashing concurrently
Notes: The motivation behind this work is that prior works do not address both pollution and thrashing concurrently.
Prior works on pollution do not have control over the number of high-reuse blocks. As a result, if there are more high-reuse blocks than what the cache can handle, these approaches can suffer from thrashing.
On the other hand, prior works on cache thrashing have no mechanism to distinguish high-reuse blocks from low-reuse blocks. As a result, when a working set is not thrashing, these approaches can suffer from pollution.
Our goal in this work is to design a mechanism to address both cache pollution and thrashing. In this talk, I will present our mechanism, the Evicted-address filter, that achieves our goal.

## Slide 139: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 140: Reuse Prediction
Miss
Missed-block
High reuse
Low reuse
?
Keep track of the reuse behavior of every cache block in the system
Impractical
High storage overhead
Look-up latency
Notes: The reuse prediction problem asks the following question. On a cache miss, does the missed cache block have high reuse or low reuse?
One possible way to answer this question is to keep track of the reuse behavior of every block in the system.
But such an approach is impractical due to its high storage overhead and look-up latency.
So, how do prior works address this problem?

## Slide 141: Prior Work on Reuse Prediction
Use program counter or memory region information.
B
A
T
S
PC 1
PC 2
B
A
T
S
PC 1
PC 2
PC 1
PC 2
C
C
U
U
1. Group Blocks
2. Learn group behavior
3. Predict reuse
Same group → same reuse behavior
No control over number of high-reuse blocks
Notes: Previous approaches proposed to predict the reuse behavior of missed blocks indirectly using program-counter or memory-region information. At a high level, the program-counter based mechanism operates in three steps.
First, the mechanism groups blocks based on the program counter that caused their cache miss.
Second, the mechanism learns the reuse behavior of each group based on the blocks that were previously accessed by the program counter.
Third, the learned behavior of each group is used to predict the reuse behavior of future blocks accessed by the corresponding program counter.
Such an approach has two shortcomings.
First, blocks belonging to the same program counter may not have the same reuse behavior.
Second, the mechanism has no control over the number of blocks predicted to have high reuse. As a result, this approach can potentially suffer from thrashing.

## Slide 142: Our Approach: Per-block Prediction
Use recency of eviction to predict reuse
A
Time
Time of eviction
A
Accessed soon after eviction
S
Time
S
Accessed long time after eviction
Notes: In this work, we propose a mechanism to predict the reuse behavior of a block based on its own past behavior.
The key idea behind our mechanism is to use the recency of eviction of a block to predict its reuse on its next access.
More specifically, if a block is accessed soon after getting evicted, our mechanism concludes that the block was prematurely evicted and predicts it to have high reuse.
On the other hand, if a block is accessed a long time after eviction, our mechanism concludes that the block is unlikely to be accessed in the near future and predicts it to have low reuse.
The above idea suggests that it is sufficient to keep track of a small number of recently evicted blocks to distinguish between high-reuse blocks and low-reuse blocks.

## Slide 143: Evicted-Address Filter (EAF)
Cache
EAF
(Addresses of recently evicted blocks)
Evicted-block address
Miss
Missed-block address
In EAF?
Yes
No
MRU
LRU
High Reuse
Low Reuse
Notes: Based on this observation, our mechanism augments the cache with a structure called the Evicted-address filter that keeps track of addresses of recently evicted blocks.
When a block is evicted from the cache, our mechanism inserts its address into the EAF.
On a cache miss, if the missed block address is present in the EAF, then the block was evicted recently. Therefore, our mechanism predicts that the block has high reuse and inserts it at the MRU position. It also removes the block address from the EAF to create space for more evicted addresses.
On the other hand, if the missed block address is not present in the EAF, there is one of two possibilities: either the block was accessed before and evicted a long time ago or the block is accessed for the first time. In both cases, our mechanism predicts that the block has low reuse and inserts it at the LRU position.
Although the EAF is a simple mechanism to predict the reuse behavior of missed blocks, one natural question is how to implement it in hardware?

## Slide 144: Naïve Implementation: Full Address Tags
EAF
1. Large storage overhead
2. Associative lookups – High energy
Recently evicted address
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 145: Low-Cost Implementation: Bloom Filter
EAF
Implement EAF using a Bloom Filter
Low storage overhead + energy
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 146: Bloom Filter
Y
Compact representation of a set
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1. Bit vector
2. Set of hash functions
H1
H2
H1
H2
X
1
1
1
Insert
Test
Z
W
Remove
X
Y
May remove multiple addresses
Clear


False positive
Inserted Elements:
X
Y
Notes: Let me give you a quick overview of a Bloom filter. A Bloom filter is a compact representation of a set, in this case, a set of addresses.
It consists of a bit vector and a set of hash functions.
All the bits in the bit-vector are initialized to zero.
To insert an address X into the set, the Bloom filter computes the values of the two hash functions and sets the corresponding elements in the filter.
To insert another address Y, the Bloom filter repeats the process.
To test if an address is present in the filter, the Bloom filter computes the values of the hash functions and checks if all the corresponding bits are set. If yes, the Bloom filter concludes that the address is present in the set. This is the case for the address X.
However, even if one of the bits is not set, the Bloom filter concludes that the address is not present in the set.
When we test for the address W, the Bloom filter will conclude that W is present in the set. But W was never inserted. The left bit was set due to the insertion of X and the right bit was set due to the insertion of Y. This situation is referred to as a false positive. The false positive rate of a Bloom filter can be made low by controlling the parameters of the Bloom filter.
Since multiple addresses can map to the same bits, a Bloom filter does not support removing individual addresses from the set.
However, all the addresses can be cleared from the set by simply resetting all the bits in the Bloom filter.
Now, let us look at how we can implement EAF using a Bloom filter.

## Slide 147: EAF using a Bloom Filter
EAF
Insert
Test
Evicted-block address
Remove
FIFO address
Missed-block address
Bloom Filter
Remove
If present
when full
Clear




1
2
when full
Bloom-filter EAF: 4x reduction in storage overhead, 1.47% compared to cache size
Notes: Let us quickly revisit the operations performed on the EAF.
First, on a cache eviction, the evicted block address is inserted into the EAF.
Second, on a cahce miss, our mechanism tests if the missed block address is present in the EAF. If yes, the address is also removed from the EAF.
Finally, when the EAF is full, an address is removed in a FIFO manner to create space for more recently evicted addresses.
A Bloom filter based implementation of EAF will support the insert and the test operations.
However, as we saw in the previous slide, the Bloom filter does not support the remove operations. So we need to somehow eliminate these remove operations. For this purpose, we propose two changes to the EAF design.
First, on a cache miss, if the missed block address is present in the EAF, we choose to retain the block address in the EAF instead of removing it.
Second, when the EAF becomes full, we propose to clear the EAF completely instead of removing an address in a FIFO manner.
With these changes, we can implement the EAF using a Bloom filter.
Doing so can reduce the storage overhead of EAF by 4x, to around 1.47% compared to the cache size.

## Slide 148: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 149: Large Working Set: 2 Cases
Cache
EAF
A
E
K
J
I
H
G
F
L
C
B
D
Cache
EAF
R
Q
P
O
N
M
L
S
J
I
H
G
F
E
D
K
C
B
A
1
2
Cache < Working set < Cache + EAF
Cache + EAF < Working Set
Notes: Thrashing happens when the working set is larger than the cache size. In the context of EAF, there are two cases. In the first case, the working set is larger than the cache but smaller than the blocks tracked by the cache and EAF together. In the second case, the working set is larger than the cache and EAF together. In both cases, the traditional LRU policy will lead to thrashing. I will discuss the operation of EAF in these two cases one by one.

## Slide 150: Large Working Set: Case 1
Cache
EAF
A
E
K
J
I
H
G
F
L
C
B
D


B
F
L
K
J
I
H
G
A
D
C
E
C
G
A
L
K
J
I
H
B
E
D
F

A
L
K
J
I
H
G
B
E
D
F
C












A
Sequence:
B
C
D
E
F
G
H
I
J
K
L
A
B
C
EAF Naive:
D

A
B
C
Cache < Working set < Cache + EAF
Notes: In the first case, the working set is smaller than the cache and EAF put together. Let us first look at how the original FIFO based implementation of EAF works.
Consider the following access sequence that accesses the blocks of the working set in a cyclic manner.
First, the access to block A misses in the cache. However, since the address is present in the EAF, it is inserted with a high priority into the cache.
The same thing happens with block B
and Block C after than.
In fact, every block in the access sequence will miss in the cache. As a result, the FIFO based implementation of EAF performs no better than traditional LRU.

## Slide 151: Large Working Set: Case 1
Cache
EAF
E
A
K
J
I
H
G
F
L
C
B
D
A
Sequence:
B
C
D
E
F
G
H
I
J
K
L
A
B
C
A
B
EAF BF:








A






EAF Naive:















A
L
K
J
I
H
G
B
E
D
C
A
B
F
A
L
K
J
I
H
G
B
E
D
F
C
A
B
D
H
G
B
E
D
F
C
A
A
L
K
J
I
B
C
D
D


Not removed
Not present in the EAF
Bloom-filter based EAF mitigates thrashing
H

G
F
E
I
Cache < Working set < Cache + EAF
Notes: Now lets look at how the Bloom-filter based EAF performs on this access sequence.
When block A is accessed, it misses in the cache but is present in the EAF. It is inserted with a high priority.
But unlike EAF-FIFO, the address is not removed from the EAF.
The same thing happens with Block B.
Moving forward, after the access to block D which also misses in the cache, the EAF becomes full.
At this point, the Bloom-filter based implementation will completely clear the EAF.
As a result, even though the next four accesses to E, F, G and H miss in the cache, their addresses will not be present in the EAF. Therefore, they will be inserted at the LRU position evicting only block I from the cache. As a result, 7 of the next 8 accesses will hit in the cache.
In fact, if the access sequence continues, the bloom-filter based implementation will periodically clear the EAF leading to cache hits to a fraction of the blocks.
So, the Bloom-filter based implementation of EAF mitigates caceh thrashing.

## Slide 152: Large Working Set: Case 2
Cache
EAF
R
Q
P
O
N
M
L
S
J
I
H
G
F
E
D
K
C
B
A
Problem: All blocks are predicted to have low reuse
Use Bimodal Insertion Policy for low reuse blocks. Insert few of them at the MRU position
Allow a fraction of the working set to stay in the cache
Cache + EAF < Working Set
Notes: Now lets move on to the second case of large working sets. In this case, since the working set is larger than both the cache and EAF together, none of the missed addresses will be present in the EAF.
As a result, all blocks will be predicted to have low reuse and inserted with low priority. If the cache is already filled with some other blocks, none of the blocks will get into the cache.
In this case, we would ideally like to allow a fraction of the working set to stay in the cache.
For this purpose, we propose to use the bimodal insertion policy for low reuse blocks. As a result, a few blocks of the working set will be inserted at the MRU position improving the cache utilization.

## Slide 153: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 154: EAF-Cache: Final Design
Cache
Bloom Filter
Counter
1
2
3
Cache eviction
Cache miss
Counter reaches max
Insert address into filter
Increment counter
Test if address is present in filter
Yes, insert at MRU. No, insert with BIP
Clear filter and counter
Notes: Lets take a look at the final design of our mechanism, the EAF-cache.
It augments the cache with a Bloom filter and a counter that keeps track of the number of addresses inserted into the Bloom filter.
On a cache eviction, the evicted address is inserted into the filter and the counter is incremented.
On a cache miss, if the missed block address is present in the Bloom filter, the block is inserted at the MRU position. Otherwise it is inserted with the bimodal insertion policy.
Finally, when the counter reaches a maximum, both the filter and the counter are cleared.

## Slide 155: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 156: EAF: Advantages
Cache
Bloom Filter
Counter
1. Simple to implement
2. Easy to design and verify
3. Works with other techniques (replacement policy)
Cache eviction
Cache miss
Notes: Apart from its ability to mitigate both pollution and thrashing, EAF has three other advantages.
First, it adds only a Bloom filter and a counter. Hardware implementations of the Bloom filter are well studied. So, EAF-cache is simple to implement.
Second, both the Bloom filter and the counter are outside the cache. As a result, our mechanism is easy to design and verify on top of existing cache implementations.
Finally, all operations on the EAF happen on a cache miss. As a result, EAF can work well with other techniques that monitor cache hits to improve performance, for example, the cache replacement policy.

## Slide 157: EAF: Disadvantage
Cache
A
First access
A
A
A
Second access
Miss
Problem: For an LRU-friendly application, EAF incurs one additional miss for most blocks
Dueling-EAF: set dueling between EAF and LRU
In EAF?
Notes: One limitation of the EAF is that when a high-reuse block is accessed for the first time, EAF will falsely predict the block to have low reuse and insert it at the LRU position. So the block will likely get evicted causing the second access to also be a cache miss.
Although this does not affect performance significantly for most applications, for LRU friendly applications, EAF incurs one additional miss for most blocks.
To mitigate this problem, we propose to use a previously proposed technique called set dueling to choose the best between the EAF and the LRU policies. Please read our paper for more details.

## Slide 158: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 159: Methodology
Simulated System
  In-order cores, single issue, 4 GHz
  32 KB L1 cache, 256 KB L2 cache (private)
  Shared L3 cache (1MB to 16MB)
  Memory: 150 cycle row hit, 400 cycle row conflict
Benchmarks
  SPEC 2000, SPEC 2006, TPC-C, 3 TPC-H, Apache
Multi-programmed workloads
  Varying memory intensity and cache sensitivity
Metrics
  4 different metrics for performance and fairness
  Present weighted speedup

## Slide 160: Comparison with Prior Works
Addressing Cache Pollution
- No control on number of blocks inserted with high priority ⟹ Thrashing
Run-time Bypassing (RTB) – Johnson+ ISCA’97
- Memory region based reuse prediction
Single-usage Block Prediction (SU) – Piquet+ ACSAC’07
Signature-based Hit Prediction (SHIP) – Wu+ MICRO’11
- Program counter based reuse prediction
Miss Classification Table (MCT) – Collins+ MICRO’99
- One most recently evicted block
Notes: We compare EAF to five previous approaches.
Three of them address the cache pollution problem. Run time cache bypassing learns the reuse behavior of course grain memory regions to predict the reuse of individual cache blocks. Single usage block prediction and signature based hit prediction both use a program counter based reuse prediction mechanism, similar to the memory region approach. The miss classification table keeps track of one most recently evicted block to filter low-reuse blocks. The main drawback of these approaches is that they do not have inherent mechanism to control the number of high reuse blocks. As a result, when the working set is larger than the cache size, they will likely lead to thrashing.
The two other mechanisms we compare to address cache thrashing. They both use set dueling to identify applications with thrashing working sets and use the bimodal insertion policy for such applications. TA-DIP uses the traditional LRU replacement policy as the base policy and TA-DRRIP uses a different replacement policy called RRIP.

## Slide 161: Comparison with Prior Works
Addressing Cache Thrashing
- No mechanism to filter low-reuse blocks ⟹ Pollution
TA-DIP – Qureshi+ ISCA’07, Jaleel+ PACT’08
TA-DRRIP – Jaleel+ ISCA’10
- Use set dueling to determine thrashing applications
Notes: We compare EAF to five previous approaches.
Three of them address the cache pollution problem. Run time cache bypassing learns the reuse behavior of course grain memory regions to predict the reuse of individual cache blocks. Single usage block prediction and signature based hit prediction both use a program counter based reuse prediction mechanism, similar to the memory region approach. The miss classification table keeps track of one most recently evicted block to filter low-reuse blocks. The main drawback of these approaches is that they do not have inherent mechanism to control the number of high reuse blocks. As a result, when the working set is larger than the cache size, they will likely lead to thrashing.
The two other mechanisms we compare to address cache thrashing. They both use set dueling to identify applications with thrashing working sets and use the bimodal insertion policy for such applications. TA-DIP uses the traditional LRU replacement policy as the base policy and TA-DRRIP uses a different replacement policy called RRIP.

## Slide 162: Results – Summary
Chart: Performance Improvement over LRU
| 1-Core | 2-Core | 4-Core
TA-DIP | 0.01 | 0.04 | 0.02
TA-DRRIP | 0.05 | 0.08 | 0.11
RTB | 0.01 | 0.06 | 0.07
MCT | 0.01 | 0.1 | 0.06
SHIP | 0.04 | 0.1 | 0.13
EAF | 0.05 | 0.15 | 0.21
D-EAF | 0.07 | 0.15 | 0.205
Notes: This slide presents the summary of our performance results for systems with different number of cores.
As shown, our mechanisms outperform all prior approaches for all the three systems. Also, the multicore results are significantly better than the single core results. This is because, in a multicore system, pollution or thrashing caused by an application will affect useful blocks of other concurrently running applications.
SAY THAT LAST TWO BARS ARE EAF AND D-EAF

## Slide 163: 4-Core: Performance
Chart: Workload Number (135 workloads)
Notes: This figure compares the performance of EAF with the SHIP (BEST PREVIOUS MECHANISM) for all 4-core workloads. Each point on the x-axis corresponds to a 4-core workload and the workloads are sorted based on the performance improvements due to EAF. I would like to draw two conclusions. First, the average improvements of EAF is not due to few workloads. Rather, EAF outperforms SHIP for most workloads.
Second, EAF degrades performance for a few LRU-friendly workloads. However, Dueling-EAF mitigates this degradation while not significantly affecting the performance for other workloads.

## Slide 164: Effect of Cache Size
Chart: Weighted Speedup Improvement over LRU
| 1MB | 2MB | 4MB | 8MB | 2MB | 4MB | 8MB | 16MB | 2-Core | 4-Core
SHIP | 10 | 8 | 6 | 5 | 13 | 9 | 8 | 6
EAF | 15 | 10 | 8 | 6 | 21 | 15 | 11 | 7
D-EAF | 15 | 10 | 9 | 7 | 20.5 | 16 | 12 | 7
Notes: This figure shows the effect of varying the cache size on the performance of different schemes. As expected, the gap between different schemes decrease with increasing cache size. With larger cache sizes, the negative impact of pollution and thrashing also reduces.
However, our EAF-based approaches still provide better performance compared to both the LRU baseline and SHIP.

## Slide 165: Effect of EAF Size
Chart: # Addresses in EAF / # Blocks in Cache
| 0.0 | 0.2 | 0.4 | 0.600000000000001 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6
1 Core | 1 | 2 | 2 | 4 | 5 | 5 | 5 | 4 | 4
2 Core | 10 | 11 | 13 | 14 | 15 | 15 | 15 | 15 | 15
4 Core | 12 | 15 | 18 | 19 | 20 | 21 | 21 | 20 | 20
Notes: Finally, let’s take a look at the effect of the number of addresses kept track in the EAF on its performance. The x-axis shows the ratio of the number of addresses in the EAF and the number of blocks in the cache.
When the number of addresses in the EAF is low, it falsely predicts many high reuse blocks as low reuse blocks.
On the other extreme, when the number of addresses in the EAF is high, it predicts too many blocks to have high reuse, more than what the cache can handle.
We find that having as many addresses in the EAF as there are blocks in the cache provides the best performance. Our paper describes the intuition behind this behavior.

## Slide 166: Other Results in Paper
EAF orthogonal to replacement policies
  LRU, RRIP – Jaleel+ ISCA’10
Performance improvement of EAF increases with increasing memory latency
EAF performs well on four different metrics
  Performance and fairness
Alternative EAF-based designs perform comparably
  Segmented EAF
  Decoupled-clear EAF
Notes: …

## Slide 167: Conclusion
Cache utilization is critical for system performance
  Pollution and thrashing degrade cache performance
  Prior works don’t address both problems concurrently
EAF-Cache
  Keep track of recently evicted block addresses in EAF
  Insert low reuse with low priority to mitigate pollution
  Clear EAF periodically and use BIP to mitigate thrashing
  Low complexity implementation using Bloom filter
EAF-Cache outperforms five prior approaches that address pollution or thrashing
Notes: …

## Slide 168: Cache Potpourri: Managing Waste
Onur Mutlu
onur@cmu.edu
July 9, 2013
INRIA

## Slide 170: Additional Material

## Slide 171: Main Memory Compression
Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency" SAFARI Technical Report, TR-SAFARI-2012-005, Carnegie Mellon University, September 2012.

## Slide 172: Caching for Hybrid Memories
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf) Best paper award (in Computer Systems and Applications track).

## Slide 173: Four Works on Memory Interference (I)
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems" Proceedings of the 15th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 174: Four Works on Memory Interference (II)
Reetuparna Das, Rachata Ausavarungnirun, Onur Mutlu, Akhilesh Kumar, and Mani Azimi, "Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 175: Enabling Emerging Memory Technologies

## Slide 176: Aside: Scaling Flash Memory [Cai+, ICCD’12]
NAND flash memory has low endurance: a flash cell dies after 3k P/E cycles vs. 50k desired  Major scaling challenge for flash memory
Flash error rate increases exponentially over flash lifetime
Problem: Stronger error correction codes (ECC) are ineffective and undesirable for improving flash lifetime due to
  diminishing returns on lifetime with increased correction strength
  prohibitively high power, area, latency overheads
Our Goal: Develop techniques to tolerate high error rates w/o strong ECC
Observation: Retention errors are the dominant errors in MLC NAND flash
  flash cell loses charge over time; retention errors increase as cell gets worn out
Solution: Flash Correct-and-Refresh (FCR)
  Periodically read, correct, and reprogram (in place) or remap each flash page before it accumulates more errors than can be corrected by simple ECC
  Adapt “refresh” rate to the severity of retention errors (i.e., # of P/E cycles)
Results: FCR improves flash memory lifetime by 46X with no hardware changes and low energy overhead; outperforms strong ECCs

## Slide 177: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 178: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 179: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 180: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 181: PCM-Based Memory Systems: Research Challenges
Partitioning
  Should DRAM be a cache or main memory, or configurable?
  What fraction? How many controllers?
Data allocation/movement (energy, performance, lifetime)
  Who manages allocation/movement?
  What are good control algorithms?
  How do we prevent degradation of service due to wearout?
Design of cache hierarchy, memory controllers, OS
  Mitigate PCM shortcomings, exploit PCM advantages
Design of PCM/DRAM chips and modules
  Rethink the design of PCM/DRAM with new requirements

## Slide 182: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 183: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 184: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 185: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 186: Hybrid Memory Systems
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies
(5-9 years of average lifetime)

## Slide 187: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two idea directions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 188: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 189: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Bridges half of the performance gap between all-DRAM and all-PCM memory on memory-intensive workloads
Yoon et al., “Row Buffer Locality-Aware Caching Policies for Hybrid Memories,” ICCD 2012.

## Slide 190: Row-Locality-Aware Data Placement: Mechanism
For a subset of rows in PCM, memory controller:
  Tracks row conflicts as a predictor of future locality
  Tracks accesses as a predictor of future reuse
Cache a row in DRAM if its row conflict and access counts are greater than certain thresholds
Determine thresholds dynamically to adjust to application/workload characteristics
  Simple cost/benefit analysis every fixed interval

## Slide 191: Implementation: “Statistics Store”
Goal: To keep count of row buffer misses to recently used rows in PCM
Hardware structure in memory controller
  Operation is similar to a cache
    Input: row address
    Output: row buffer miss count
  128-set 16-way statistics store (9.25KB) achieves system performance within 0.3% of an unlimited-sized statistics store
Notes: The implementation of our mechanism requires a statistics store, or what we simply call a stats store.
The goal of the stats store is to keep count of the row buffer misses to recently used rows in PCM.
The stats store is a hardware structure in the memory controller, and its operation is similar to a cache.
It is organized into sets and ways, and is indexed using the row address of the row we wish to find the row buffer miss count for.
If the queried row is currently in the stats store, then its row buffer miss count will be output.
We find that a 128-set 16-way stats store, 9.25KB in size, achieves system performance within 0.3% of an unlimited-sized stats store.

## Slide 192: Evaluation Methodology
Cycle-level x86 CPU-memory simulator
  CPU: 16 out-of-order cores, 32KB private L1 per core, 512KB shared L2 per core
  Memory: 1GB DRAM (8 banks), 16GB PCM (8 banks), 4KB migration granularity
36 multi-programmed server, cloud workloads
  Server: TPC-C (OLTP), TPC-H (Decision Support)
  Cloud: Apache (Webserv.), H.264 (Video), TPC-C/H
Metrics: Weighted speedup (perf.), perf./Watt (energy eff.), Maximum slowdown (fairness)
Notes: Here’s our evaluation methodology.
We use a cycle-level x86 simulator to test our hybrid memory caching policies.
We simulate a 16-core system with 1GB of DRAM and 16GB of PCM.
We use 36 multi-programmed server and cloud workloads to test our caching policies.
For server workloads, we use TPC-C, which is an online transaction processing benchmark, and TPC-H, which is a decision support benchmark.
For cloud workloads, we use Apache, which is a webserver application, and H.264, a video processing application, as well as TPC-C and H.
We report multi-core performance in terms of weighted speedup, multi-core fairness in terms of maximum slowdown, and energy efficiency in terms of performance per Watt.

## Slide 193: Comparison Points
Conventional LRU Caching
FREQ: Access-frequency-based caching
  Places “hot data” in cache [Jiang+ HPCA’10]
  Cache to DRAM rows with accesses  threshold
  Row buffer locality-unaware
FREQ-Dyn: Adaptive Freq.-based caching
  FREQ + our dynamic threshold adjustment
  Row buffer locality-unaware
RBLA: Row buffer locality-aware caching
RBLA-Dyn: Adaptive RBL-aware caching
Notes: And here are our comparison points.
The standard conventional LRU caching caches any row from PCM to DRAM when the data is touched. We find this scheme to generate too much data movement between DRAM and PCM and consequently to not perform well. So we’re not going to use it as a comparison point in this talk.
Frek is access frequency based caching. It is inspired by prior work that selectively caches hot data.
The downsides of frek is that it is row buffer locality aware. Hence, it would place a row with high row buffer locality in DRAM, although that row may be accessed as efficiently in PCM.
Frek-Dyn augments frek with the adaptive threshold adjustment technique.
It has the same drawback as frek, in that it is row buffer locality unaware.
Our mechanisms, RBLA and RBLA-Dyn, are specifically designed to be aware of row buffer locality and to exploit it.

## Slide 194: System Performance
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
17%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 3: Balanced memory request load between DRAM and PCM
Notes: Here are the system performance results of the different hybrid memory caching policies.
RBLA-Dyn achieves 17% performance improvement over frek in server workloads, 10% in cloud, and 14% overall.
This is due to a number of reasons.
The first is that RBLA-Dyn increases row buffer locality in PCM by moving low row buffer locality data to DRAM.
The second is that RBLA-Dyn reduces memory bandwidth consumption due its stricter caching criteria.
And RBLA-Dyn also has the effect of balancing the memory request load between DRAM and PCM by letting rows with high row buffer locality remain in PCM, instead of fetching all accessed data to DRAM.

## Slide 195: Average Memory Latency
Chart: Workload
| Server | Cloud | Avg
FREQ | 1.1028 | 0.9068 | 1
FREQ-Dyn | 1.0156 | 0.85733 | 0.9331
RBLA | 1.0006 | 0.8704 | 0.93324
RBLA-Dyn | 0.94644 | 0.82222 | 0.88214
14%
9%
12%
Notes: These benefits are also reflected in the average memory latency, which RBLA-Dyn reduces by 14% over frek in server workloads, by 9% in cloud, and by 12% overall.

## Slide 196: Memory Energy Efficiency
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.99688 | 1.0031 | 1
FREQ-Dyn | 1.0786 | 1.0475 | 1.0629
RBLA | 1.0901 | 1.0386 | 1.064
RBLA-Dyn | 1.1281 | 1.0731 | 1.1002
Increased performance & reduced data movement between DRAM and PCM
7%
10%
13%
Notes: RBLA-Dyn improves memory system energy efficiency by 13% in server workloads, 7% in cloud, and 10% overall.
This is partly due to the increased system performance, and partly due to the reduced data movement between DRAM and PCM because of RBLA-Dyn’s stricter caching criteria.

## Slide 197: Thread Fairness
Chart: Workload
| Server | Cloud | Avg
FREQ | 1.1145 | 0.89726 | 1
FREQ-Dyn | 1.0492 | 0.87701 | 0.95924
RBLA | 1.0703 | 0.86925 | 0.96457
RBLA-Dyn | 1.0303 | 0.85386 | 0.93795
7.6%
4.8%
6.2%
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 198: Compared to All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
Our mechanism achieves 31% better performance than all PCM, within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 199: The Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 200: Idea 1: Tags in Memory
Store tags in the same row as data in DRAM
  Store metadata in same row as their data
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 201: Idea 2: Cache Tags in SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 202: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
  Group main memory into sets of rows
  Some row sets follow a fixed caching granularity
  The rest of main memory follows the best granularity
    Cost–benefit analysis: access latency versus number of cachings
    Performed every quantum

## Slide 203: TIMBER Tag Management
A Tag-In-Memory BuffER (TIMBER)
  Stores recently-used tags in a small amount of SRAM
Benefits: If tag is cached:
  no need to access DRAM twice
  cache hit determined quickly
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Row Tag
LOAD X
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 204: TIMBER Tag Management Example (I)
Case 1: TIMBER hit
Bank
Bank
Bank
Bank
CPU
Mem Ctlr
Mem Ctlr
LOAD X
TIMBER: X  DRAM
X
Access X
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Our proposal

## Slide 205: TIMBER Tag Management Example (II)
Case 2: TIMBER miss
CPU
Mem Ctlr
Mem Ctlr
LOAD Y
Y  DRAM
Bank
Bank
Bank
Bank
Access Metadata(Y)
Y
1. Access M(Y)
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Miss
M(Y)
2. Cache M(Y)
Row143
3. Access Y (row hit)

## Slide 206: Methodology
System: 8 out-of-order cores at 4 GHz
Memory: 512 MB direct-mapped DRAM, 8 GB PCM
  128B caching granularity
  DRAM row hit (miss): 200 cycles (400 cycles)
  PCM row hit (clean / dirty miss): 200 cycles (640 / 1840 cycles)
Evaluated metadata storage techniques
  All SRAM system (8MB of SRAM)
  Region metadata storage
  TIM metadata storage (same row as data)
  TIMBER, 64-entry direct-mapped (8KB of SRAM)

## Slide 207
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 208
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 209: Hybrid Main Memory: Research Topics
Many research ideas from technology layer to algorithms layer
Enabling NVM and hybrid memory
  How to maximize performance?
  How to maximize lifetime?
  How to prevent denial of service?
Exploiting emerging tecnologies
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to minimize cost?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 210: Security Challenges of Emerging Technologies
1. Limited endurance  Wearout attacks
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
3. Multiple bits per cell  Information leakage (via side channel)

## Slide 211: Securing Emerging Memory Technologies
1. Limited endurance  Wearout attacks
Better architecting of memory chips to absorb writes
Hybrid memory system management
Online wearout attack detection
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
Efficient encryption/decryption of whole main memory
Hybrid memory system management
3. Multiple bits per cell  Information leakage (via side channel)
System design to hide side channel information

## Slide 212: Linearly Compressed Pages
Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency" SAFARI Technical Report, TR-SAFARI-2012-005, Carnegie Mellon University, September 2012.

## Slide 213: Executive Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid latency increase?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
1. Increases capacity (69% on average)
2. Decreases bandwidth consumption (46%)
3. Improves overall performance (9.5%)

## Slide 214: Challenges in Main Memory Compression
Address Computation
Mapping and Fragmentation
Physically Tagged Caches

## Slide 215: Address Computation
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
0
?
?
?
Address Offset
Uncompressed Page

## Slide 216: Mapping and Fragmentation
Virtual Page
(4kB)
Physical Page
(? kB)
Fragmentation
Virtual
Address
Physical
Address

## Slide 217: Physically Tagged Caches
Core
TLB
tag
tag
tag
Physical Address
data
data
data
Virtual
Address
Critical Path
Address Translation
L2 Cache
Lines

## Slide 218: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 

## Slide 219: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 

## Slide 220: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
LCP: Our Proposal |  |  |  | 

## Slide 221: Linearly Compressed Pages (LCP): Key Idea
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B):
? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4kB: 64*64B)
Compressed Data
(1kB)

## Slide 222: LCP Overview
Page Table entry extension
  compression type and size
  extended physical base address
Operating System management support
  4 memory pools (512B, 1kB, 2kB, 4kB)
Changes to cache tagging logic
  physical page base address + cache line index
  (within a page)
Handling page overflows
Compression algorithms: BDI [PACT’12] , FPC [ISCA’04]

## Slide 223: LCP Optimizations
Metadata cache
  Avoids additional requests to metadata
Memory bandwidth reduction:
Zero pages and zero cache lines
  Handled separately in TLB (1-bit) and in metadata
  (1-bit per cache line)
Integration with cache compression
  BDI and FPC
64B
64B
64B
64B
1 transfer
instead of 4

## Slide 224: Methodology
Simulator
  x86 event-driven simulators
    Simics-based [Magnusson+, Computer’02] for CPU
    Multi2Sim [Ubal+, PACT’12] for GPU
Workloads
  SPEC2006 benchmarks, TPC, Apache web server, GPGPU applications
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  512kB - 16MB L2, simple memory model

## Slide 225: Compression Ratio Comparison
Chart: GeoMean
| GeoMean
Zero Page | 1.2982
FPC | 1.5908
LCP (BDI) | 1.6239
LCP (BDI+FPC-fixed) | 1.6909
MXT | 2.3051
LZ | 2.6049
SPEC2006, databases, web workloads, 2MB L2 cache
LCP-based frameworks achieve competitive average compression ratios with prior work

## Slide 226: Bandwidth Consumption Decrease
SPEC2006, databases, web workloads, 2MB L2 cache
Chart: Normalized BPKI
| GeoMean
FPC-cache | 0.92005
BDI-cache | 0.89057
FPC-memory | 0.57215
(None, LCP-BDI) | 0.62549
(FPC, FPC) | 0.5362
(BDI, LCP-BDI) | 0.55124
(BDI, LCP-BDI+FPC-fixed) | 0.53836
LCP frameworks significantly reduce bandwidth (46%)
Better
Notes: BPKI – bandwidth per kilo instruction – lower means better.

## Slide 227: Performance Improvement
Cores | LCP-BDI | (BDI, LCP-BDI) | (BDI, LCP-BDI+FPC-fixed)
1 | 6.1% | 9.5% | 9.3%
2 | 13.9% | 23.7% | 23.6%
4 | 10.7% | 22.6% | 22.5%
LCP frameworks significantly improve performance

## Slide 228: Conclusion
A new main memory compression framework called LCP (Linearly Compressed Pages)
  Key idea: ﬁxed size for compressed cache lines within a page and fixed compression algorithm per page
LCP evaluation:
  Increases capacity (69% on average)
  Decreases bandwidth consumption (46%)
  Improves overall performance (9.5%)
  Decreases energy of the off-chip bus (37%)

## Slide 229: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 230: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
230

## Slide 231: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 232: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 233
A4
B1
A1
A2
A3
Oldest
⎧
⎪
⎪
⎩
Shared Memory
Resources
A:
Compute
Stall on A1
Stall on A2
Stall on A3
Stall on A4
Compute
Stall waiting for shared resources
Stall on B1
B:
Request Generation Order:
A1, A2, A3, A4, B1
Unmanaged Interference
Core A’s stall time
Core B’s stall time
A4
B1
A1
A2
A3
⎧
⎪
⎪
⎩
Shared Memory
Resources
A:
Compute
Stall on A1
Stall on A2
Compute
Stall wait.
Stall on B1
B:
Dynamically detect application A’s interference for application B and throttle down application A
Core A’s stall time
Core B’s stall time
Fair Source Throttling
Stall wait.
Request Generation Order
A1,
A2, A3, A4,
B1
B1,
A2, A3, A4
queue of requests to
shared resources
queue of requests to
shared resources
Saved Cycles Core B
Oldest
Intensive application A generates many requests and causes long stall times for less intensive application B
Throttled
Requests
Stall on A4
Stall on A3
Extra Cycles
Core A
Notes: Lets look at an example of how this approach can intuitively work
Lets assume two concurrently executing applications A, and B,
and we compare two scenarios, one where interference is left unmanaged, and in the second we show how fair source throttling can improve unfairness and performance.
Here we see the queue of requests to shared resources which will be filled with entries from both applications.
Now each of the applications does compute for some time, during which each of them generates some memory requests. Lets say application A is very memory intensive and generates many more memory requests than application B.
This results in the requests being generated in the order shown on the slide. Lets assume that these requests all interfere with one another. First four requests are generated from application A and then one request from application B.
These requests fill in the queue of requests to shared resources. Lets say requests are issued to the shared memory resources from this queue based on a first come first served policy. As a result,
Application A’s requests get serviced by the shared resources first, and
result in the shown memory related stall time for application A
During this time application B stalls waiting for application A’s requests to get serviced,
and only then gets its request serviced. This results in the shown memory related stall time for application B.
In summary the intensive application A generates many requests which cause long stall times for the less intensive application B.
Now our approach with fair source throttling was to pose the question: what if at runtime we could dynamically detect that application A was interfering significantly with application B, and upon detecting this situation we could throttle application A back such that
some of its requests would be generated after the request from application B
the queue of requests to the shared resources
would now be filled in as shown in the slide. As a result,
The first access to be serviced by the shared resources is A1.
and As A1 is being serviced, application B stalls waiting for the shared resources.
Then request B1 gets serviced by the shared resources
which results in a much smaller stall time for application B than in the first scenario.
After this, the throttled requests from application A get serviced, and
This results in the shown stall time for application A which is slightly longer than the first scenario. However we managed to
reduce application B’s memory related stall time a lot. Overall, this can improve fairness as application A is a memory intensive application that has large stall times even when running in isolation, so increasing application A’s stall time a little bit only slightly increases its slowdown compared to the first scenario. But the large reduction in the stall time of application B significantly reduces its associated slowdown. This can also improve system throughput as the less memory intensive application B can now go back to its compute phase faster and stall less.
so we want to be able to dynamically detect application A’s interference for application B, and throttle the cores appropriately to improve fairness and performance.
-----

## Slide 234: Fairness via Source Throttling (FST)
Two components (interval-based)
Run-time unfairness evaluation (in hardware)
  Dynamically estimates the unfairness in the memory system
  Estimates which application is slowing down which other
Dynamic request throttling (hardware or software)
  Adjusts how aggressively each core makes requests to the shared resources
  Throttles down request rates of cores causing unfairness
    Limit miss buffers, limit injection rate

## Slide 235: Fairness via Source Throttling (FST)
235
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 236: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
236

## Slide 237: Estimating System Unfairness
Unfairness =
Slowdown of application i =
How can be estimated in shared mode?
is the number of extra cycles it takes application i to execute due to interference
Max{Slowdown i} over all applications i
Min{Slowdown i} over all applications i
Shared
Ti
Ti
Alone
Ti
Alone
Ti
Excess
Ti
Shared
=
Ti
Alone
-
Ti
Excess

## Slide 238: Tracking Inter-Core Interference
0
0
0
0
Interference per core
bit vector
Core #
0
1
2
3
Core 0
Core 1
Core 2
Core 3
Bank 0
Bank 1
Bank 2
Bank 7
...
Memory Controller
Shared Cache
Three interference sources:
1. Shared Cache
2. DRAM bus and bank
3. DRAM row-buffers
FST hardware
Bank 2
Row

## Slide 239: Tracking DRAM Row-Buffer Interference
Row A
Core 0
Core 1
Bank 0
Bank 1
Bank 2
Bank 7
…
Shadow Row Address Register
(SRAR) Core 1:
Shadow Row Address Register
(SRAR) Core 0:
Queue of requests to bank 2
0
0
Row B
Row A
Row A
Row B
Row B
Interference
per core bit vector
Row Conflict
Row Hit
Interference
induced row conflict
1
Row A

## Slide 240: Tracking Inter-Core Interference
0
0
0
0
Interference per core
bit vector
Core #
0
1
2
3
0
0
0
0
Excess Cycles
Counters per core
1
T
Cycle Count
T+1
1
T+2
2
FST hardware
1
T+3
3
1
Core 0
Core 1
Core 2
Core 3
Bank 0
Bank 1
Bank 2
Bank 7
...
Memory Controller
Shared Cache
Ti
Excess
⎪
⎪
Ti
Shared
=
Ti
Alone
-
Ti
Excess

## Slide 241: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
241
Notes: The runtime unfairness evaluation component should also determine which application causes most interference for Appslowest, this application is called app-interfering

## Slide 242: Tracking Inter-Core Interference
To identify App-interfering, for each core i
  FST separately tracks interference caused by each core j ( j ≠ i )
Cnt 3
Cnt 2
Cnt 1
Cnt 0
0
0
0
0
-
Interference per core
bit vector
Core #
0
1
2
3
-
Cnt 1,0
Cnt 2,0
Cnt 3,0
Excess Cycles
Counters per core
0
0
-
0
0
-
0
0
-
0
0
0
⎪
⎨
⎪
⎧
⎩
⎪
⎨
⎪
⎧
⎩
Interfered with core
Interfering
core
Cnt 0,1
-
Cnt 2,1
Cnt 3,1
Cnt 0,2
Cnt 1,2
-
Cnt 3,2
Cnt 0,3
Cnt 1,3
Cnt 2,3
-
1
core 2
interfered
with
core 1
Cnt 2,1+
0
1
2
3
Row with largest count
determines App-interfering
App-slowest = 2
Pairwise interference
bit matrix
Pairwise excess cycles
matrix

## Slide 243: Fairness via Source Throttling (FST)
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering

## Slide 244: Dynamic Request Throttling
Goal: Adjust how aggressively each core makes requests to the shared memory system
Mechanisms:
  Miss Status Holding Register (MSHR) quota
    Controls the number of concurrent requests accessing shared resources from each application
  Request injection frequency
    Controls how often memory requests are issued to the last level cache from the MSHRs

## Slide 245: Dynamic Request Throttling
Throttling level assigned to each core determines both MSHR quota and request injection rate
Throttling level | MSHR quota | Request Injection Rate
100% | 128 | Every cycle
50% | 64 | Every other cycle
25% | 32 | Once every 4 cycles
10% | 12 | Once every 10 cycles
5% | 6 | Once every 20 cycles
4% | 5 | Once every 25 cycles
3% | 3 | Once every 30 cycles
2% | 2 | Once every 50 cycles
Total # of
MSHRs: 128

## Slide 246: FST at Work
Time
Interval i
Interval i+1
Interval i+2
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
FST
Unfairness Estimate
App-slowest
App-interfering
Throttling Levels
Core 0
Core 1
Core 3
50%
100%
10%
100%
25%
100%
25%
100%
25%
50%
50%
100%
Interval i
Interval i + 1
Interval i + 2
3
Core 2
Core 0
Core 0
Core 2
Throttle down
Throttle up
2.5
Core 2
Core 1
Throttle down
Throttle up
System software fairness goal: 1.4
Slowdown
Estimation
⎪
⎨
⎪
⎧
⎩
Slowdown
Estimation
⎪
⎨
⎪
⎧
⎩

## Slide 247: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 248: FST Hardware Cost
Total storage cost required for 4 cores is ~12KB
FST does not require any structures or logic that are on the processor’s critical path

## Slide 249: FST Evaluation Methodology
x86 cycle accurate simulator
Baseline processor configuration
  Per-core
    4-wide issue, out-of-order, 256 entry ROB
  Shared (4-core system)
    128 MSHRs
    2 MB, 16-way L2 cache
  Main Memory
    DDR3 1333 MHz
    Latency of 15ns per command (tRP, tRCD, CL)
    8B wide core to memory bus

## Slide 250: FST: System Unfairness Results
grom+art+astar+h264
lbm+omnet+apsi+vortex
art+leslie+games+grom
art+astar+leslie+crafty
lbm+Gems+astar+mesa
gcc06+xalanc+lbm+cactus
gmean
44.4%
36%
art+games+Gems+h264
art+milc+vortex+calculix
lucas+ammp+xalanc+grom
mgrid+parser+soplex+perlb

## Slide 251: FST: System Performance Results
251
gmean
25.6%
14%
grom+art+astar+h264
art+games+Gems+h264
lbm+omnet+apsi+vortex
art+leslie+games+grom
art+astar+leslie+crafty
art+milc+vortex+calculix
lucas+ammp+xalanc+grom
lbm+Gems+astar+mesa
mgrid+parser+soplex+perlb
gcc06+xalanc+lbm+cactus
251

## Slide 252: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control
FST ASPLOS 2010 Talk

## Slide 253: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 254: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 255: Outline
Goal:
Mitigate
Inter-Application Interference
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling

## Slide 256: Application-Aware Memory Request Scheduling
Monitor application memory access characteristics
Rank applications based on memory access characteristics
Prioritize requests at the memory controller, based on ranking

## Slide 257: An Example: Thread Cluster Memory Scheduling
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Figure: Kim et al., MICRO 2010

## Slide 258: Application-Aware Memory Request Scheduling
Advantages
Reduces interference between applications by
request reordering
Improves system performance
Disadvantages
Requires modifications to memory scheduling logic for
  Ranking
  Prioritization
Cannot completely eliminate interference by request reordering

## Slide 259: Our Approach
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Goal:
Mitigate
Inter-Application Interference

## Slide 260: Observation: Modern Systems Have Multiple Channels
A new degree of freedom
Mapping data across multiple channels
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory

## Slide 261: Data Mapping in Current Systems
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Causes interference between applications’ requests
Page

## Slide 262: Partitioning Channels Between Applications
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Page
Eliminates interference between applications’ requests

## Slide 263: Overview: Memory Channel Partitioning (MCP)
Goal
  Eliminate harmful interference between applications
Basic Idea
  Map the data of badly-interfering applications to different channels
Key Principles
  Separate low and high memory-intensity applications
  Separate low and high row-buffer locality applications

## Slide 264: Key Insight 1: Separate by Memory Intensity
High memory-intensity applications interfere with low memory-intensity applications in shared memory channels
Map data of low and high memory-intensity applications
to different channels
1
2
3
4
5
Channel 0
Bank 1
Channel 1
Bank 0
Conventional Page Mapping
Red App
Blue App
Time Units
Core
Core
Bank 1
Bank 0
Channel Partitioning
Red App
Blue App
Channel 0
Time Units
1
2
3
4
5
Channel 1
Core
Core
Bank 1
Bank 0
Bank 1
Bank 0
Saved Cycles
Saved Cycles

## Slide 265: Key Insight 2: Separate by Row-Buffer Locality
High row-buffer locality applications interfere with low
row-buffer locality applications in shared memory channels
Conventional Page Mapping
Channel 0
Bank 1
Channel 1
Bank 0
R1
R0
R2
R3
R0
R4
Request Buffer State
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
R0
Channel 0
R1
R2
R3
R0
R4
Request Buffer State
Channel Partitioning
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Saved
Cycles
Map data of low and high row-buffer locality applications to different channels

## Slide 266: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 267: 1. Profile Applications
Hardware counters collect application memory access characteristics
Memory access characteristics
  Memory intensity:
  Last level cache Misses Per Kilo Instruction (MPKI)
  Row-buffer locality:
  Row-buffer Hit Rate (RBH) - percentage of accesses that hit in the row buffer

## Slide 268: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 269: 3. Partition Channels Among Groups: Step 1
Channel 1
Assign number of channels proportional to number of applications in group
.
.
.
High Intensity
Low Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel 3
High Intensity
High Row-Buffer Locality

## Slide 270: 3. Partition Channels Among Groups: Step 2
Channel 1
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
.
.
.
Assign number of channels proportional to bandwidth demand of group
Channel 3
Channel 1
.
.
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel N-1
Channel N
Channel 3
.
.
.

## Slide 271: 4. Assign Preferred Channel to Application
Channel 1
Low Intensity
Channel 2
MPKI: 1
MPKI: 3
MPKI: 4
MPKI: 1
MPKI: 3
MPKI: 4
Assign each application a preferred channel from its group’s allocated channels
Distribute applications to channels such that group’s bandwidth demand is balanced across its channels

## Slide 272: 5. Allocate Page to Preferred Channel
Enforce channel preferences computed in the previous step
On a page fault, the operating system
  allocates page to preferred channel if free page available in preferred channel
  if free page not available, replacement policy tries to allocate page to preferred channel
  if it fails, allocate page to another channel

## Slide 273: Interval Based Operation
time
Current Interval
Next Interval
1. Profile applications
2. Classify applications into groups
3. Partition channels between groups
4. Assign preferred channel to applications
5. Enforce channel preferences

## Slide 274: Integrating Partitioning and Scheduling
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Goal:
Mitigate
Inter-Application Interference

## Slide 275: Observations
Applications with very low memory-intensity rarely access memory  Dedicating channels to them results in precious memory bandwidth waste
They have the most potential to keep their cores busy  We would really like to prioritize them
They interfere minimally with other applications  Prioritizing them does not hurt others

## Slide 276: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications

## Slide 277: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit

## Slide 278: Methodology
Simulation Model
  24 cores, 4 channels, 4 banks/channel
  Core Model
    Out-of-order, 128-entry instruction window
    512 KB L2 cache/core
  Memory Model – DDR2
Workloads
  240 SPEC CPU 2006 multiprogrammed workloads (categorized based on memory intensity)
Metrics
  System Performance

## Slide 279: Previous Work on Memory Scheduling
FR-FCFS [Zuravleff et al., US Patent 1997, Rixner et al., ISCA 2000]
  Prioritizes row-buffer hits and older requests
  Application-unaware
ATLAS [Kim et al., HPCA 2010]
  Prioritizes applications with low memory-intensity
TCM [Kim et al., MICRO 2010]
  Always prioritizes low memory-intensity applications
  Shuffles request priorities of high memory-intensity applications

## Slide 280: Comparison to Previous Scheduling Policies
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Significant performance improvement over baseline FRFCFS
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 281: Interaction with Memory Scheduling
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061
IMPS | 1.1108 | 1.08 | 1.09
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061

IMPS improves performance regardless of scheduling policy
Highest improvement over FRFCFS as IMPS designed for FRFCFS
Averaged over 240 workloads

## Slide 282: MCP Summary
Uncontrolled inter-application interference in main memory degrades system performance
Application-aware memory channel partitioning (MCP)
  Separates the data of badly-interfering applications to different channels, eliminating interference
Integrated memory partitioning and scheduling (IMPS)
  Prioritizes very low memory-intensity applications in scheduler
  Handles other applications’ interference by partitioning
MCP/IMPS provide better performance than application-aware memory request scheduling at lower hardware cost

## Slide 283: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 284: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 285: Main Memory is a Bottleneck
All cores contend for limited off-chip bandwidth
  Inter-application interference degrades system performance
  The memory scheduler can help mitigate the problem
How does the memory scheduler deliver good performance and fairness?
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
Memory Request Buffer
Req
Req
Req
Req
Req
Req
Req
Data
Data
Req
Req
Notes: Main memory is a major bottleneck in current multi-core systems
<click three times>,
Because memory requests from different core contend for a limited off-chip bandwidth
<click>
This inter-application interference degrades system performance. And designing a good memory scheduler can mitigate the problem…
<click>
But how does memory scheduler deliver good performance and fairness.
<click to the next slide>

## Slide 286: Three Principles of Memory Scheduling
Currently open row
B
Prioritize row-buffer-hit requests [Rixner+, ISCA’00]
  To maximize memory bandwidth
Prioritize latency-sensitive applications [Kim+, HPCA’10]
  To maximize system throughput
Ensure that no application is starved [Mutlu and Moscibroda, MICRO’07]
  To minimize unfairness
Req 1 | Row A
Req 2 | Row B
Req 3 | Row C
Req 4 | Row A
Req 5 | Row B
Application | Memory Intensity (MPKI)
1 | 5
2 | 1
3 | 2
4 | 10
Older
Newer
Notes: State-of-the-art memory schedulers can deliver good performance and fairness generally based on three principles.
<click>
The first principle is to prioritize row-buffer-hit requests over other requests. The reason is because DRAM can service row-buffer-hit requests faster than requests that miss in the row buffer. This principle will maximize memory bandwidth
<click>
For example, suppose that there are five requests sorted by age as shown, and the current open row is row B. Even though request 1 is older than request 2, in this case, servicing a row hitting requests 2 first is faster than servicing requests that go to other rows. As a result, request 2 is prioritized over other requests.
<click>
The second principle is the scheduler should prioritize latency sensitive applications. Previous works have shown that latency sensitive applications can make faster forward progress when their memory requests are serviced quickly. In order to identify a latency sensitive application, memory intensity is generally used as a metric because application with lower memory intensity can make faster progress when a memory request is serviced.
<click>
For example, suppose that there are four applications in the system, and the memory intensity is defined by misses per thousand instructions. In this case, application number two will have more priority than other applications because it has the lowest memory intensity.
<click>
The third principle is the scheduler needs to make sure that the system is fair by ensuring that every application are making progress and none of the applications are starved.
<transition>
So far I have talked about memory scheduling in CPU-only systems. Now I will talk about the CPU-GPU heterogeneous system because current and future systems integrate a GPU along with multiple cores.

## Slide 287: Memory Scheduling for CPU-GPU Systems
Current and future systems integrate a GPU along with multiple cores
GPU shares the main memory with the CPU cores
GPU is much more (4x-20x) memory-intensive than CPU
How should memory scheduling be done when GPU is integrated on-chip?
Notes: So far I have talked about memory scheduling in CPU-only systems. Now I will talk about the CPU-GPU heterogeneous system because current and future systems integrate a GPU along with multiple cores.
This integrated GPU shares the main memory with the CPU cores; however, the GPU is four to twenty times more memory-intensive compared to CPU. So, how should the memory scheduling be done when GPU is integrated on-chip?
Let’s see how does the memory scheduling problem change when we add a GPU into the system
[picture of the current APU/Sandy Bridge]

## Slide 288: Introducing the GPU into the System
GPU occupies a significant portion of the request buffers
  Limits the MC’s visibility of the CPU applications’ differing memory behavior  can lead to a poor scheduling decision
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
Req
Req
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Notes: When GPU is introduced into the system <click>, because the GPU is memory-intensive, requests from cores contend heavily with request from the GPU, as you can see from this example
<click>
The memory-intensive GPU application will send a lot of request to the memory request buffer
<click>
As a result, some of the requests are unable to be inject into the request buffer, as illustrated by this blue request from core 2.
<click>
When only some of the memory requests can inject into the request buffer, memory scheduler cannot observe full applications behavior. This can lead to a poor scheduling decision
<click… transition>
A naïve solution to this problem is to increase the size of the monolithic request buffer…

## Slide 289: Naïve Solution: Large Monolithic Buffer
Memory Scheduler
To DRAM
Core 1
Core 2
Core 3
Core 4
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
GPU
Notes: The naïve solution is to increase the size of the batch scheduler
<click> transition: however …

## Slide 290: Problems with Large Monolithic Buffer
A large buffer requires more complicated logic to:
  Analyze memory requests (e.g., determine row buffer hits)
  Analyze application characteristics
  Assign and enforce priorities
This leads to high complexity, high power, large die area
Memory Scheduler
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
More Complex Memory Scheduler
Notes: <However (continue from the previous slide) a large buffer requires more complicated logic to analyze memory requests (for example, to determine if each request is a row hit), analyze application characteristics, assign and enforce priorities.
<click>
This leads to high complexity, high power, and large die area
<click, the big Mem sched. Appears>
<click, transition>
Our goal in this project is…

## Slide 291: Our Goal
Design a new memory scheduler that is:
  Scalable to accommodate a large number of requests
  Easy to implement
  Application-aware
  Able to provide high performance and fairness, especially in heterogeneous CPU-GPU systems
Notes: Our goal in this project is to design a new memory scheduler that is <click> scalable to accommodate a large number of requests, <click> easy-to-implement, <click> application-aware and <click> able to provide high performance and fairness especially in heterogeneous CPU-GPU systems.
<transition … >
To this end, we have made several observations that lead to our new memory scheduler design

## Slide 292: Key Functions of a Memory Controller
Memory controller must consider three different things concurrently when choosing the next request:
1) Maximize row buffer hits
  Maximize memory bandwidth
2) Manage contention between applications
  Maximize system throughput and fairness
3) Satisfy DRAM timing constraints
Current systems use a centralized memory controller design to accomplish these functions
  Complex, especially with large request buffers
Notes: … we observe that there are three key functions that an application aware memory scheduler need to provide concurrently when choosing the next request
<click>
First, a memory scheduler should maximize row buffer hits because this increases the bandwidth utlization
<click>
Second, a memory scheduler should be able to manage contention between different applications. This will increase system throughput and fairness
<click>
Third, a memory scheduler need to satisfy DRAM timing constraints
<click>
Current systems use a centralized memory controller design to accomplish these functions, which is complex when the request buffer is large
<click … transition>
So, our key idea is to …

## Slide 293: Key Idea: Decouple Tasks into Stages
Idea: Decouple the functional tasks of the memory controller
  Partition tasks across several simpler HW structures (stages)
1) Maximize row buffer hits
  Stage 1: Batch formation
  Within each application, groups requests to the same row into batches
2) Manage contention between applications
  Stage 2: Batch scheduler
  Schedules batches from different applications
3) Satisfy DRAM timing constraints
  Stage 3: DRAM command scheduler
  Issues requests from the already-scheduled order to each bank
Notes: Our key idea is to decouple these functional tasks <click> into different stages.
<click>
We partition these three <click> tasks across several simpler hardware structures, which we call stages.
<click>
Stage 1 is the batch formation. This stage maximizes row buffer hits by grouping requests that access the same row within each application into batches
<click>
Stage 2 is the batch scheduler. This stage manages contention by scheduling batches from different applications
<click>
And stage 3 is the DRAM command scheduler. This stage issues requests from an already scheduled order and make sure that it satisfy DRAM timing constraints
<click … transition>
With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through …

## Slide 294: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 295: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 296: Stage 1: Batch Formation
Goal: Maximize row buffer hits
At each core, we want to batch requests that access the same row within a limited time window
A batch is ready to be scheduled under two conditions
  1) When the next request accesses a different row
  2) When the time window for batch formation expires
Keep this stage simple by using per-core FIFOs
Notes: The goal in the batch formation stage is to maximize row buffer hits.
<click>
At each core, we want to batch request that access the same row within a limited time window
<click>
And a batch is ready to be scheduled by the batch scheduler under to conditions. The first condition is when the next request accesses a different row. The second condition is when the time window for batch formation expires to ensure forward progress
<click>
We keep this stage simple by using per-core FIFO queues
<click … transition>
And now I will show an example of how batch formation works.

## Slide 297: Stage 1: Batch Formation Example
Core 1
Core 2
Core 3
Core 4
Row A
Row B
Row B
Row C
Row D
Row D
Row E
Row F
Row E
Batch Boundary
To Stage 2 (Batch Scheduling)
Row A
Time window expires
Next request goes to a different row
Stage 1
Batch Formation
Notes: I will show an example of how the batch formation work
<click>
When there is an incoming requests that access the same row as an earlier requests. (This yellow request that accesses row B), they will be batched. And a batch will become ready to be scheduled under two conditions. First, it will become ready when a subsequent request wants to access a different row, in this case row C. The earlier request to row B will become ready to be scheduled.
A batch can become ready to be scheduled under another condition, which is when the time window for the batch formation expires, which is shown in this example in core 1. this batch formation will happen across all the cores including the GPU.

## Slide 298: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: <transition>
Now, let me tell you how Stage 2 works: the batch scheduler.

## Slide 299: Stage 2: Batch Scheduler
Goal: Minimize interference between applications
Stage 1 forms batches within each application
Stage 2 schedules batches from different applications
  Schedules the oldest batch from each application
Question: Which application’s batch should be scheduled next?
Goal: Maximize system performance and fairness
  To achieve this goal, the batch scheduler chooses between two different policies
Notes: The goal for the batch scheduler is to minimize interference between applications.
Because the batch formation forms batches within each application
<click>
The batch scheduler only need schedule batches among different applications
<click>
And because batches in stage 1 is sorted in a FIFO order, the batch scheduler only needs to consider the oldest batch from each application
<click>
The question is how can the scheduler pick the next batch?
<click>
The goal is to maximize system performance and fairness. And in order to achieve this goal, we employ two batch scheduling algorithms.
<click … transition>

## Slide 300: Stage 2: Two Batch Scheduling Algorithms
Shortest Job First (SJF)
  Prioritize the applications with the fewest outstanding memory requests because they make fast forward progress
  Pro: Good system performance and fairness
  Con: GPU and memory-intensive applications get deprioritized
Round-Robin (RR)
  Prioritize the applications in a round-robin manner to ensure that memory-intensive applications can make progress
  Pro: GPU and memory-intensive applications are treated fairly
  Con: GPU and memory-intensive applications significantly slow down others
Notes: The first algorithm we employ is the Shortest Job First policy, which
  Prioritizes the applications with the fewest outstanding memory requests because they make fast forward progress
    The benefit is shortest job first policy is it provides good system performance and fairness
    However, the GPU and memory-intensive applications get deprioritized
In order to mitigate this problem, the batch scheduler can use Round-Robin policy, which
  Prioritizes the applications in a round-robin manner to ensure that memory-intensive applications can make progress
    The benefit of using a round-robin policy is it provides high GPU performance (because it is memory-intensive)
    However, the GPU and memory-intensive applications significantly slow down others

## Slide 301: Stage 2: Batch Scheduling Policy
The importance of the GPU varies between systems and over time  Scheduling policy needs to adapt to this
Solution: Hybrid Policy
At every cycle:
  With probability p : Shortest Job First  Benefits the CPU
  With probability 1-p : Round-Robin  Benefits the GPU
System software can configure p based on the importance/weight of the GPU
  Higher GPU importance  Lower p value
Notes: The importance of the GPU varies between systems and also over time. The batch scheduling policy needs to adapt to this change.<click>
In order to adapt to this change, we propose a hybrid policy, where at every cycle:
<click> at every cycle <click>
With a probability of p, the scheduler will use SJF policy. <click>
With a probability of 1-p, the scheduler will use RR policy.<click>
And the system software can configure p based on the importance of the GPU. The more important the GPU, the low p value
<transition>
And with these two stages, batch formation and batch scheduler, both inter-application and intra-application ordering are handled. Now, I will explain the last stage of our design: the DRAM command scheduler.

## Slide 302: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: And with these two stages, batch formation and batch scheduler, both inter-application and intra-application ordering are handled. Now, I will explain the last stage of our design, which is the DRAM command scheduler.

## Slide 303: Stage 3: DRAM Command Scheduler
High level policy decisions have already been made by:
  Stage 1: Maintains row buffer locality
  Stage 2: Minimizes inter-application interference
Stage 3: No need for further scheduling
Only goal: service requests while satisfying DRAM timing constraints
Implemented as simple per-bank FIFO queues
Notes: Because high level policy decisions have already been made by stages 1 and 2, where stage 1 maintains row buffer locality and stage 2 minimizes inter-application interference. There is no need for this stage to optimize for row buffer locality, performance or fairness.
<click>
As a result, the goal of this stage is to service requests while satisfying DRAM timing constraints
<click>
And this can be implemented as simpler per-bank FIFO queues
<transition>
Now, we will show an example of how the three stages work with each other.

## Slide 304: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 305: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 306: Methodology
Simulation parameters
  16 OoO CPU cores, 1 GPU modeling AMD Radeon™ 5870
  DDR3-1600 DRAM 4 channels, 1 rank/channel, 8 banks/channel
Workloads
  CPU: SPEC CPU 2006
  GPU: Recent games and GPU benchmarks
  7 workload categories based on the memory-intensity of CPU applications
     Low memory-intensity (L)
     Medium memory-intensity (M)
     High memory-intensity (H)
Notes: We use an in-house cycle level simulator that models 16 OoO CPU cores and 1 GPU modeling AMD Radeon 5870. We model the main memory using DDR3 DRAM with 4 channels, 1 rank and 8 banks.
<click>
We use SPEC 2006 for the CPU applications and recent games and GPU Benchmarks for the GPU. We divide the workload into 7 workload categories based on the memory intensity of the CPU and this varies from low, medium and high memory-intensity applications measured based on LLC MPKI
<click, transition>

## Slide 307: Comparison to Previous Scheduling Algorithms
FR-FCFS [Rixner+, ISCA’00]
  Prioritizes row buffer hits
  Maximizes DRAM throughput
  Low multi-core performance  Application unaware
ATLAS [Kim+, HPCA’10]
  Prioritizes latency-sensitive applications
  Good multi-core performance
  Low fairness  Deprioritizes memory-intensive applications
TCM [Kim+, MICRO’10]
  Clusters low and high-intensity applications and treats each separately
  Good multi-core performance and fairness
  Not robust  Misclassifies latency-sensitive applications
Notes:     We compare our proposed mechanism with three previous state-of-the-art memory scheduling algorithms.
    <click>
    The first algorithm we compare to is a row-hit first algorithm that prioritize row buffer hitting requests first. And this will maximizes DRAM throughput. However, as previous work have shown, FR-FCFS has low multi-core performance because it is application unaware
    <click>
    The second algorithm we compare to is adaptive per thread least attained service memory scheduling algorithm, which prioritizes latency sensitive applications. This algorithm gives good multi-core performance. However, previous work has shown that this algorithm is unfair because memory-intensive applications are deprioritized
    <click>
    The last algorithm we compare to is thread cluster memory scheduling algorithm, which cluster low and high memory intensity applications into two different clusters, and treats each cluster differently to improve both performance and fairness. However, we observe that TCM is not robust enough in the context of CPU-GPU heterogeneous system. Because TCM misclassify latency sensitive applications and put these applications in a wrong cluster, and it uses a wrong scheduling policy on these miss-classified applications.
    <click … transition>

## Slide 308: Evaluation Metrics
CPU performance metric: Weighted speedup
GPU performance metric: Frame rate speedup
CPU-GPU system performance: CPU-GPU weighted speedup
Notes: We evaluated CPU performance using weighted speedup which is defined by the sum of IPC of the CPU when it is running with other applications compared to when it is running alone
<click>
We evaluated GPU performance using GPU speedup which is defined by the frame rate speedup of the GPU when it is running with other applications compared to when it is running alone
<click>
In terms of the system performance, we use CPU-GPU weighted speedup, which is the sum of CPU weighted speedup and the GPU speedup. However, we multiply the GPU speedup with the GPU weight <click> which can be changed based on the important of the GPU.
<click … transition>

## Slide 309: Evaluated System Scenario: CPU Focused
GPU has low weight (weight = 1)
Configure SMS such that p, SJF probability, is set to 0.9
  Mostly uses SJF batch scheduling  prioritizes latency-sensitive applications (mainly CPU)
1
Notes: On a CPU-focused system <click> The GPU has low weight of 1, and in this case, SMS is configured such that P, the probablity of using the shortest job first batch scheduling policy, is set to 0.9. This will mostly use shortest job first batch scheduling, which prioritize latency sensitive applications.
<click>

## Slide 310: Performance: CPU-Focused System
SJF batch scheduling policy allows latency-sensitive applications to get serviced as fast as possible
Chart: CGWS
| L | ML | M | HL | HML | HM | H | Avg
FR-FCFS | 7.066 | 5.678 | 3.023 | 4.0314 | 3.6181 | 2.2517 | 1.5751 | 3.8919
ATLAS | 7.8662 | 6.6578 | 4.0265 | 5.4299 | 5.0318 | 3.0926 | 1.9522 | 4.8653
TCM | 7.6659 | 6.388 | 3.5808 | 5.0101 | 4.5112 | 2.744 | 1.8778 | 4.5397
SMS_0.9 | 11.0198 | 8.6314 | 4.5778 | 5.801 | 5.2337 | 3.0224 | 1.6682 | 5.7077
+17.2% over ATLAS
SMS is much less complex than previous schedulers
p=0.9
Workload Categories
Notes: This plot shows the performance of SMS on a CPU focused system. The y-axis represents the system performance measured by the CPU-GPU weighted speedup with the GPU weight of 1, and the X-axis is the performance on each workload categories sorted from low intensity to high intensity.
<click>
When the CPU performance is important, setting the probability of using the shortest job first batch scheduling policy to a high value, allows the latency-sensitive applications to get serviced as fast as possible. <click> This improve system performance by 17.2% on average compared to the previous best scheduling mechanism.
<click>
In addition to the performance gain, the design of SMS is much simpler compared to previous designs.

## Slide 311: Evaluated System Scenario: GPU Focused
GPU has high weight (weight = 1000)
Configure SMS such that p, SJF probability, is set to 0
  Always uses round-robin batch scheduling  prioritizes memory-intensive applications (GPU)
1000
Notes: On a GPU-focused system <click> The GPU has high weight of 1000, and in this case, SMS is configured such that P, the probability of using the shortest job first batch scheduling policy, is set to 0. This will use round-robin batch scheduling policy all the time, which gives priority to the GPU.
<click>

## Slide 312: Performance: GPU-Focused System
Round-robin batch scheduling policy schedules GPU requests more frequently
Chart: CGWS
| L | ML | M | HL | HML | HM | H | Avg
FR-FCFS | 980.2029 | 951.8914 | 939.388 | 783.8121 | 862.3228 | 800.7138 | 779.8686 | 871.1714
ATLAS | 950.0175 | 865.8395 | 746.4181 | 537.4795 | 577.1246 | 525.2205 | 467.7448 | 667.1207
TCM | 967.3195 | 914.1203 | 869.5664 | 649.7908 | 726.5373 | 632.6294 | 562.7337 | 760.3854
SMS_0 | 927.6489 | 910.4414 | 908.4153 | 847.6915 | 891.603 | 870.5232 | 839.1282 | 885.0645
+1.6% over FR-FCFS
SMS is much less complex than previous schedulers
p=0
Workload Categories
Notes: This plot shows the performance of SMS on a GPU focused system. The y-axis represents the system performance measured by the CPU-GPU weighted speedup with the GPU weight of 1000, and the X-axis is the performance on each workload categories sorted from low intensity to high intensity.
<click>
When the GPU performance is important, always using the round-robin policy will schedule GPU requests more frequently.
<click> This improve system performance by 1.6% on average compared to the previous best scheduling mechanism, which is FR-FCFS.
<click>
In addition to the performance gain, the design of SMS is much simpler compared to previous designs.

## Slide 313: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 314: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 315: Additional Results in the Paper
Fairness evaluation
  47.6% improvement over the best previous algorithms
Individual CPU and GPU performance breakdowns
CPU-only scenarios
  Competitive performance with previous algorithms
Scalability results
  SMS’ performance and fairness scales better than previous algorithms as the number of cores and memory channels increases
Analysis of SMS design parameters
Notes: In addition to the previous results, we also provide other key results in the paper. We have shown that SMS provides significant fairness improvement over previous algorithms. We also provided individual CPU and GPU performance breakdowns. SMS performs competitively in CPU-only scenarios. We have shown that SMS scales better with the increasing number of cores and memory channels, and we also provide an analysis of different design parameters in the paper.

## Slide 316: Conclusion
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer size
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution is to decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.