## Slide 1: Rethinking Memory System Design (and the Platforms We Design Around It)
Onur Mutlu
onur.mutlu@inf.ethz.ch
https://people.inf.ethz.ch/omutlu
April 4, 2017
ARC 2017 Keynote

## Slide 2: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)
FPGAs
GPUs

## Slide 3: Memory System: A Shared Resource View
Storage

## Slide 4: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 5: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 6: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 7: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 8: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years
Lim et al., ISCA 2009

## Slide 9: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer 2003]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 10: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 11: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 12: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 13: An Example of the DRAM Scaling Problem
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly opening and closing a row enough times within a refresh interval induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 14: Most DRAM Modules Are at Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 15
DRAM Module
x86 CPU
Y
X
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 16
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 17
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 18
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 19: Observed Errors in Real Systems
A real reliability & security issue
In a more controlled environment, we can induce as many as ten million disturbance errors
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 20: Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 21: Experimental DRAM Testing Infrastructure
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 22: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 23: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 24: RowHammer Security Attack Example
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows (Kim et al., ISCA 2014).
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
  Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)

## Slide 25: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 26: More Security Implications
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript

## Slide 27: More Security Implications
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms

## Slide 28: More Security Implications?

## Slide 29: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP and Lenovo released similar patches

## Slide 30: Challenge and Opportunity
Reliability
(and Security)

## Slide 31: Departing From “Business as Usual”
More Intelligent
Memory Controllers
Online System-Level Tolerance
of Memory “Issues”

## Slide 32: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 33
Intuition: quadratic increase in capacity
DRAM Reliability Reducing

## Slide 34: Aside: Flash Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet]

## Slide 35: Aside: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017]

## Slide 36: Another Talk: NAND Flash Scaling Challenges
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.

## Slide 37: Recap: The DRAM Scaling Problem

## Slide 38: How Do We Solve The Problem?
Fix it: Make memory and controllers more intelligent
  New interfaces, functions, architectures: system-mem codesign
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
  New technologies and system-wide rethinking of memory & storage
Embrace it: Design heterogeneous memories (none of which are perfect) and map data intelligently across them
  New models for data management and maybe usage
…
Solutions (to memory scaling) require
software/hardware/device cooperation
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 39: Solution 1: New Memory Architectures
Overcome memory shortcomings with
  Memory-centric system design
  Novel memory architectures, interfaces, functions
  Better waste management (efficient utilization)
Key issues to tackle
  Enable reliability at low cost
  Reduce energy
  Improve latency and bandwidth
  Reduce waste (capacity, bandwidth, latency)
  Enable computation close to data

## Slide 40: Solution 1: New Memory Architectures
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri+, “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Pekhimenko+, “Linearly Compressed Pages: A Main Memory Compression Framework,” MICRO 2013.
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field,” DSN 2015.
Kim+, “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE CAL 2015.
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM,” IEEE CAL 2015.
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing,” ISCA 2015.
Ahn+, “PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture,” ISCA 2015.
Lee+, “Decoupled Direct Memory Access: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM,” PACT 2015.
Seshadri+, “Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses,” MICRO 2015.
Lee+, “Simultaneous Multi-Layer Access: Improving 3D-Stacked Memory Bandwidth at Low Cost,” TACO 2016.
Hassan+, “ChargeCache: Reducing DRAM Latency by Exploiting Row Access Locality,” HPCA 2016.
Chang+, “Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Migration in DRAM,” HPCA 2016.
Chang+, “Understanding Latency Variation in Modern DRAM Chips Experimental Characterization, Analysis, and Optimization,” SIGMETRICS 2016.
Khan+, “PARBOR: An Efficient System-Level Technique to Detect Data Dependent Failures in DRAM,” DSN 2016.
Hsieh+, “Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems,” ISCA 2016.
Hashemi+, “Accelerating Dependent Cache Misses with an Enhanced Memory Controller,” ISCA 2016.
Boroumand+, “LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory,” IEEE CAL 2016.
Pattnaik+, “Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities,” PACT 2016.
Hsieh+, “Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation,” ICCD 2016.
Hashemi+, “Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads,” MICRO 2016.
Khan+, “A Case for Memory Content-Based Detection and Mitigation of Data-Dependent Failures in DRAM",” IEEE CAL 2016.
Hassan+, “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Avoid DRAM:
  Seshadri+, “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko+, “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Seshadri+, “The Dirty-Block Index,” ISCA 2014.
  Pekhimenko+, “Exploiting Compressed Block Size as an Indicator of Future Reuse,” HPCA 2015.
  Vijaykumar+, “A Case for Core-Assisted Bottleneck Acceleration in GPUs: Enabling Flexible Data Compression with Assist Warps,” ISCA 2015.
  Pekhimenko+, “Toggle-Aware Bandwidth Compression for GPUs,” HPCA 2016.

## Slide 41: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Expected to scale to 9nm (2022 [ITRS])
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, IEEE Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” TACO 2014.
Ren+, “ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems,” MICRO 2015.
Chauhan+, “NVMove: Helping Programmers Move to Byte-Based Persistence,” INFLOW 2016.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 42: Solution 3: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Technology X (e.g., PCM)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 43: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 44: Challenge and Opportunity
Providing the Best of
Multiple Metrics

## Slide 45: Departing From “Business as Usual”
Heterogeneous Memory Systems
Configurable Memory Systems

## Slide 46: An Orthogonal Issue: Memory Interference
Main
Memory
Core
Core
Core
Core
Cores’ interfere with each other when accessing shared main memory
This is uncontrolled today  Unpredictable, uncontrollable system
Notes: In a multicore system, multiple applications running on the different cores share the main memory.
These applications interfere at the main memory. The result of this interference is unpredictable application slowdowns.

## Slide 47: Goal: Predictable Performance in Complex Systems
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories
How to allocate resources to heterogeneous agents
to mitigate interference and provide predictable performance?

## Slide 48: QoS-Aware Memory Systems
Solution: QoS-Aware Memory Systems
Hardware provides a configurable QoS substrate
  Application-aware memory scheduling, partitioning, throttling
Software configures the substrate to satisfy various QoS goals
QoS-aware memory systems provide predictable performance and higher efficiency
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Subramanian et al., “The Application Slowdown Model,” MICRO 2015.

## Slide 49: Challenge and Opportunity
Strong
Memory Service
Guarantees

## Slide 50: Departing From “Business as Usual”
Predictable Memory Management
Programmable Memory Systems

## Slide 51: Some Promising Directions
New memory architectures
  Memory-centric system design
Enabling and exploiting emerging NVM technologies
  Hybrid memory systems
  Unified interface to all data
System-level QoS and predictability
  Predictable systems with configurable QoS

## Slide 52: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 53: Rethinking Memory Architecture
Compute-capable memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 54: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation
Dally, HiPEAC 2015

## Slide 55: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory
  PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture (Ahn et al., ISCA 2015)
  A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing (Ahn et al., ISCA 2015)
  Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation (Hsieh et al., ICCD 2016)

## Slide 56: Bulk Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 57: Today’s Memory: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 58: Future: RowClone (In-Memory Copy)
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
90ns, 0.04uJ

## Slide 59: DRAM Subarray Operation (load one byte)
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row
Transfer row
Step 2: Read
Transfer byte onto bus
Notes: say you want a byte

## Slide 60: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Notes: copy

## Slide 61: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)
0.01% area cost

## Slide 62: RowClone: Latency and Energy Savings
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 63: RowClone: Application Performance

## Slide 64: RowClone: Multi-Core Performance

## Slide 65: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How to communicate occurrences of bulk copy/initialization across layers?
How to maximize latency and energy savings?
How to ensure data coherence?
How to handle data reuse?

## Slide 66: Goal: Ultra-Efficient Processing Near Data
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 67: Enabling In-Memory X
What is a flexible and scalable memory interface?
What is the right partitioning of computation capability?
What is the right low-cost memory substrate?
What memory technologies are the best enablers?
How do we rethink/ease X algorithms/applications?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results

## Slide 68: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 69: In-DRAM AND/OR Results
20X improvement in AND/OR throughput vs. Intel AVX
50.5X reduction in memory energy consumption
At least 30% performance improvement in range queries
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.
Size of Vectors to be ANDed
Throughput of AND operations (GB/s)
In-DRAM AND (2 banks)
In-DRAM AND (1 bank)
Intel AVX

## Slide 70: Going Forward
A bulk computation model in memory
New memory & software interfaces to enable bulk in-memory computation
New programming models, algorithms, compilers, and system designs that can take advantage of the model
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 71: Gather-Scatter DRAM [MICRO 2015]
Seshadri+, “Gather-Scatter DRAM: In-DRAM Address Translation to
Improve the Spatial Locality of Non-unit Strided Accesses”, MICRO 2015.

## Slide 72: Challenge and Opportunity
Primitives and Interfaces
for
Computation in Memory

## Slide 74: Departing From “Business as Usual”
Memory No Longer a Dumb Device

## Slide 75: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory
  PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture (Ahn et al., ISCA 2015)
  A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing (Ahn et al., ISCA 2015)
  Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation (Hsieh et al., ICCD 2016)

## Slide 76: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 77: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 78: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communication via Remote Function Calls

## Slide 79: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 80: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
(with FDP)
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
(with FDP)
Tesseract
32 Tesseract Cores
(32-entry MQ, 4KB PF Buffer)
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 81: Workloads
Five graph processing algorithms
  Average teenage follower
  Conductance
  PageRank
  Single-source shortest path
  Vertex cover
Three real-world large graphs
  ljournal-2008 (social network)
  enwiki-2003 (Wikipedia)
  indochina-0024 (web graph)
  4~7M vertices, 79~194M edges

## Slide 82: Tesseract Graph Processing Performance
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 83: Tesseract Graph Processing Performance

## Slide 84: Memory Energy Consumption (Normalized)
8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 85: Challenge and Opportunity
Memory
Bandwidth
and
Energy

## Slide 86: Departing From “Business as Usual”
Memory No Longer a Dumb Device
Autonomous and Self-Managing
Memory

## Slide 87: More on PIM: PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 88: More on PIM Design: 3D-Stacked GPU I
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 89: More on PIM Design: 3D-Stacked GPU II
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 90: Key Challenge 1
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 91: Key Challenge 1
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
?
Main GPU
3D-stacked memory
(memory stack)
Challenge 1: Which operations should be executed on the logic layer SMs?
?
SM (Streaming Multiprocessor)

## Slide 92: Key Challenge 2
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
Challenge 2: How should data be mapped to different 3D memory stacks?
SM (Streaming Multiprocessor)

## Slide 93: More on PIM Design: Dependent Misses
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 94: More on PIM: Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 95: More on PIM Design: Coherence
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 96: An FPGA-based Test-bed for PIM?
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 97: Simulation Infrastructures for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator

## Slide 98: Rethinking Memory Architecture
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 99: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Activate each row every N ms
  Typical N = 64 ms
Downsides of refresh
-- Energy consumption: Each refresh consumes energy
  -- Performance degradation: DRAM rank/bank unavailable while refreshed
  -- QoS/predictability impact: (Long) pause times during refresh
  -- Refresh rate limits DRAM capacity scaling

## Slide 100: Refresh Overhead: Performance
8%
46%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 101: Refresh Overhead: Energy
15%
47%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 102: Retention Time Profile of DRAM

## Slide 103: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 104: Experimental DRAM Testing Infrastructure
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 105: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 106: More Information [ISCA’13]

## Slide 107: More Information [SIGMETRICS’14]

## Slide 108: Online Profiling of DRAM In the Field
Optimize DRAM and mitigate errors online
without disturbing the system and applications
Initially protect DRAM
with ECC
1
Periodically test
parts of DRAM
2
ECC
Test
Test
Test
Adjust refresh rate and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 109: Online Profiling of DRAM [DSN’15]

## Slide 110: Online Profiling of DRAM [DSN’16]

## Slide 111: Online Profiling of DRAM [IEEE CAL’16]

## Slide 112: Challenge and Opportunity
Minimizing Refresh
(and Other Technology Taxes)

## Slide 113: Departing From “Business as Usual”
Online Detection and
Management of Memory Errors
(Online Avoidance of Technology Taxes)

## Slide 114: Rethinking Memory Architecture
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression
Many More
Challenges and Opportunities

## Slide 115: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 116: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 117: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 118: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 119: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 120: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 121: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 122: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 123: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 124: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 125: A More Viable Approach: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 126: Data Placement Between DRAM and PCM
Idea: Characterize data access patterns and guide data placement in hybrid memory
Streaming accesses: As fast in PCM as in DRAM
Random accesses: Much faster in DRAM
Idea: Place random access data with some reuse in DRAM; streaming data in PCM
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 127: Hybrid vs. All-PCM/DRAM [ICCD’12]
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 128: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 129: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 130: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 131: Challenge and Opportunity
Enabling an Emerging Technology
to Replace DRAM

## Slide 132: Departing From Business As Usual
Hybrid Memory
Persistent Memory

## Slide 133: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 134: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 135: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 136: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 137: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 138: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 139: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 140: Challenge and Opportunity
Combined
Memory & Storage

## Slide 141: Departing From “Business as Usual”
A Unified Interface to All Data

## Slide 142: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 143: Principles (So Far)
Better interfaces between layers of the system stack
  Expose more information judiciously across the system stack
  Design more flexible and efficient interfaces
Better-than-worst-case design
  Do not optimize for the worst case
  Worst case should not determine the common case
Heterogeneity in design (specialization, asymmetry)
  Enables a more efficient design (No one size fits all)
These principles are coupled (and require broad thinking)
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 144: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 145: Summary
Business as Usual | Opportunity
RowHammer | Memory controller anticipates and fixes errors
Fixed, frequent refreshes | Heterogeneous refresh rate across memory
Fixed, high latency | Heterogeneous latency in time and space
Slow page copy & initialization | Exploit internal connectivity in memory to move data
Fixed reliability mechanisms | Heterogeneous reliability across time and space
Memory as a dumb device | Memory as an accelerator and autonomous agent
DRAM-only main memory | Emerging memory technologies and hybrid memories
Two-level data storage model | Unified interface to all data
Large timing and error margins | Online adaptation of timing and error margins
Poor performance guarantees | Strong service guarantees and configurable QoS
Fixed policies in controllers | Configurable and programmable memory controllers
… | …

## Slide 146: Summary
Memory problems are a critical bottleneck for system performance, efficiency, and usability
New memory architectures
  Compute capable and autonomous memory
Enabling emerging NVM technologies
  Persistent and hybrid memory
System-level memory/storage QoS
  Predictable systems with configurable QoS
Many opportunities and challenges that will change the systems and software we design

## Slide 147: Acknowledgments
My current and past students and postdocs
  Rachata Ausavarungnirun, Abhishek Bhowmick, Amirali Boroumand, Rui Cai, Yu Cai, Kevin Chang, Saugata Ghose, Kevin Hsieh, Tyler Huberty, Ben Jaiyen, Samira Khan, Jeremie Kim, Yoongu Kim, Yang Li, Jamie Liu, Lavanya Subramanian, Donghyuk Lee, Yixin Luo, Justin Meza, Gennady Pekhimenko, Vivek Seshadri, Lavanya Subramanian, Nandita Vijaykumar, HanBin Yoon, Jishen Zhao, …
My collaborators
  Can Alkan, Chita Das, Phil Gibbons, Sriram Govindan, Norm Jouppi, Mahmut Kandemir, Mike Kozuch, Konrad Lai, Ken Mai, Todd Mowry, Yale Patt, Moinuddin Qureshi, Partha Ranganathan, Bikash Sharma, Kushagra Vaid, Chris Wilkerson, …

## Slide 148: Funding Acknowledgments
NSF
GSRC
SRC
CyLab
AMD, Google, Facebook, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware

## Slide 149: Some Open Source Tools
Rowhammer
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim
  https://github.com/CMU-SAFARI/memsim
NOCulator
  https://github.com/CMU-SAFARI/NOCulator
DRAM Error Model
  http://www.ece.cmu.edu/~safari/tools/memerr/index.html
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 150: Referenced Papers
All are available at
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
A detailed accompanying overview paper
  Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2015.

## Slide 151: Related Videos and Course Materials
Undergraduate Computer Architecture Course Lecture Videos (2013, 2014, 2015)
Undergraduate Computer Architecture Course Materials (2013, 2014, 2015)
Graduate Computer Architecture Lecture Videos (2013, 2015)
Graduate Computer Architecture Course Materials (2013, 2015)
Parallel Computer Architecture Course Materials (Lecture Videos)
Memory Systems Short Course Materials
(Lecture Video on Main Memory and DRAM Basics)

## Slide 152: Thank you.
onur.mutlu@inf.ethz.ch
https://people.inf.ethz.ch/omutlu

## Slide 153: Rethinking Memory System Design (and the Platforms We Design Around It)
Onur Mutlu
onur.mutlu@inf.ethz.ch
https://people.inf.ethz.ch/omutlu
April 4, 2017
ARC 2017 Keynote

## Slide 154: Backup Slides

## Slide 155: NAND Flash Memory Scaling

## Slide 156: Another Talk: NAND Flash Scaling Challenges
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.

## Slide 157: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash
[Cai+, DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015]

## Slide 158: Error Management in MLC NAND Flash
Problem: MLC NAND flash memory reliability/endurance is a key challenge for satisfying future storage systems’ requirements
Our Goals: (1) Build reliable error models for NAND flash memory via experimental characterization, (2) Develop efficient techniques to improve reliability and endurance
This talk provides a “flash” summary of our recent results published in the past 3 years:
  Experimental error and threshold voltage characterization [DATE’12&13]
  Retention-aware error management [ICCD’12]
  Program interference analysis and read reference V prediction [ICCD’13]
  Neighbor-assisted error correction [SIGMETRICS’14]

## Slide 159: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 160: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 161: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 162: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 163: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 164: DRAM Infrastructure

## Slide 165: Experimental DRAM Testing Infrastructure
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 166: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 167: ThyNVM

## Slide 168: One Challenge
How to ensure consistency of system/data if all memory is persistent?
Two extremes
  Programmer transparent: Let the system handle everything
  Programmer only: Let the programmer handle everything
  Many alternatives in-between…

## Slide 169: CHALLENGE: CRASH CONSISTENCY
System crash can result in
permanent data corruption in NVM
Persistent Memory System

## Slide 170: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile data
Burden on the programmers

## Slide 171: OUR APPROACH: ThyNVM
Goal:
Software transparent consistency in
persistent memory systems

## Slide 172: ThyNVM: Summary
Checkpoints at multiple granularities to reduce both checkpointing latency and metadata overhead
Overlaps checkpointing and execution to reduce checkpointing latency
Adapts to DRAM and NVM characteristics
Performs within 4.9% of an idealized DRAM with zero cost consistency
A new hardware-based
checkpointing mechanism

## Slide 173: More About ThyNVM
Ren+, “ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems,” MICRO 2015.

## Slide 174: CHALLENGE: CRASH CONSISTENCY
System crash can result in
permanent data corruption in NVM
Persistent Memory System

## Slide 175: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile data
Burden on the programmers

## Slide 176: OUR APPROACH: ThyNVM
Goal:
Software transparent consistency in
persistent memory systems

## Slide 177: ThyNVM: Summary
Checkpoints at multiple granularities to reduce both checkpointing latency and metadata overhead
Overlaps checkpointing and execution to reduce checkpointing latency
Adapts to DRAM and NVM characteristics
Performs within 4.9% of an idealized DRAM with zero cost consistency
A new hardware-based
checkpointing mechanism

## Slide 178: DRAM Latency

## Slide 179: Rethinking Memory Architecture
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 180: DRAM Latency vs. Capacity vs. Bandwidth
DRAM latency continues to be a critical bottleneck, especially for response time-sensitive workloads
64x
16x
1.2x

## Slide 181: A Closer Look …
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 182: Why the Long Latency?
Design of DRAM uArchitecture
  Goal: Maximize capacity/area, not minimize latency
One size fits all approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips (e.g., rows)
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 183: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency

## Slide 184: AL-DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 185
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 186
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 187
1.4%
6.7%
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves single-core performance
on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 188
14.0%
2.9%
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance on
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 189: Heterogeneous Latency within A Chip
17.6%
19.5%
19.7%
13.3%
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 190: And, What If …
… we can sacrifice reliability of some data to access it with even lower latency?

## Slide 191: ChargeCache

## Slide 192: ChargeCache: Executive Summary
Goal: Reduce average DRAM access latency with no modification to the existing DRAM chips
Observations:
  A highly-charged DRAM row can be accessed with low latency
  A row’s charge is restored when the row is accessed
  A recently-accessed row is likely to be accessed again:
  Row Level Temporal Locality (RLTL)
Key Idea: Track recently-accessed DRAM rows and use lower timing parameters if such rows are accessed again
ChargeCache:
  Low cost & no modifications to the DRAM
  Higher performance (8.6-10.6% on average for 8-core)
  Lower DRAM energy (7.9% on average)
Notes: Let’s first take a high level glance at this work.
[CLICK]
DRAM latency is a critical bottleneck for system performance. Given that the DRAM chips are difficult to change, our goal in this work is to reduce average DRAM access latency with no modifications to the existing DRAM chips.
[CLICK]
We achieve that goal by exploiting three key observations.
First, a highly-charged DRAM row can be accessed with low latency.
Second, a row’s charge is restored when the row is accessed.
Third, we find that a recently-accessed row is likely to be accessed again. We call that
Row Level Temporal Locality and we find that many applications, both single-core and multi-core, exhibit that phenomenon.
Based on that we develop the key idea of ChargeCache.
The key idea is to track recently-accessed rows and use lower timing parameters if they are accessed again.
We show that ChargeCache is low cost and requires no modifications to the existing DRAM chips.
According to our evaluations, ChargeCache improves performance between 8.6% and 10.6% on average for 8-core system, depending on the ChargeCache capacity. It also saves 7.9% energy on average.

## Slide 193
Data 0
Data 1
Cell
time
charge
Sense-Amplifier
DRAM Charge over Time
Sensing
Restore
Cell
Sense
Amplifier
Precharge
R/W
ACT
PRE
Ready to Access
Charge Level
tRCD
tRAS
Ready to Access
Ready to
Precharge
Notes: Let’s look at the same phases from the charge level perspective.
[CLICK]
The figure shows the change of charge levels of a DRAM Cell and Sense Amplifier in Y-axis, and the time in X-axis.
Initially, our cell contains charge that matches the region of Data 1, which can be treated as 0 or 1.
[CLICK]
To access the data stored in the cell, the charge of the sense amplifier should reach «Read to Access Charge Level».
The memory controller initiates Sensing phase by issuing Activate command.
On Sensing, the charge is transferred from the Cell to the Sense-Amplifier.
That slightly increases the charge of the Sense Amplifier. When the Sense Amplifier reaches
The threshold charge to recognize the data, Sensing phase finishes and Restore begins.
[CLICK]
During restore, both the
Sense Amplifier and the DRAM cell are driven back to fully charged state.
At the point where the sense amplifier reaches «ready to access charge level», the
Memory controller is free to issue Read or Write command.
[CLICK]
The time passed since ACT to READ or WRITE is called tRCD. [CLICK]
At the end of restore, the memory controller could issue PRE command if needed. [CLICK]
That triggers the Precharge phase where the Sense Amplifier charge gets back to its pre-sensing value.
The time from the start of the Sensing upon the completion of Restore is called tRAS. [CLICK]
The main takeaway in this slide is that the memory controller accesses DRAM using DRAM commands and determines the Access latency by satisfying the timing parameters.

## Slide 194
Accessing Highly-charged Rows
Data 0
Data 1
Cell
time
charge
Sense-Amplifier
Sensing
Restore
Precharge
R/W
ACT
PRE
tRCD
tRAS
R/W
PRE
Ready to Access
Ready to Precharge
Notes: The blue dots show the points where the sense amplifier reaches ready to access
And ready to precharge charge levels for a cell with the current initial charge.
Now, Let’s see how these points change when accessing a cell with higher initial charge.
[CLICK]
When the cell’s initial charge is close to the maximum level, Sensing and Restore phases
complete quicker. Hence, READ or WRITE and PRE commands can be issued
Eairlier. That corresponds to reduction on tRCD and tRAS timing parameters.
[CLICK]
Please refer to our paper to get more detailed explanation for that phenomenon.

## Slide 195: Observation 1
A highly-charged DRAM row can be accessed with low latency
tRCD: 44%
tRAS: 37%
How does a row become highly-charged?
Notes: So, we can access highly-charged rows faster.
[CLICK]
According to our SPICE simulations, highly-charged rows can be accessed
With 44% lower tRCD and 37% lower tRAS.
[CLICK]
Now, the question is: «How does a row become highly-charged?»

## Slide 196
How Does a Row Become Highly-Charged?
DRAM cells lose charge over time
Two ways of restoring a row’s charge:
Refresh Operation
Access
time
Refresh
charge
Refresh
Access
Notes: One thing to note is that DRAM cells are leaky, which means they lose charge over time.
To reliably store the data, cell’s charge needs to be restored.
[CLICK]
There are two ways of restoring the charge of the cells in a DRAM row. [CLICK]
The memory controller periodically issues REFRESH commands to continuously preserve data in DRAM.
[CLICK]
Second, as I showed in the previous slides, data accesses also inherently replenish the charge of the Cells.
As a result, we could know that the cell is in highly-charged state, if it was either recently refreshed Or recently-accessed.

## Slide 197: Observation 2
  A row’s charge is restored when the row is accessed
How likely is a recently-accessed row to be accessed again?
Notes: So, a row’s charge is restored when the row is accessed.
And now the question is: «How likely is a recently-accessed row to be accessed again?»

## Slide 198
Row Level Temporal Locality (RLTL)
86%
97%
A recently-accessed DRAM row is likely to be accessed again.
t-RLTL: Fraction of rows that are accessed within time t after their previous access
8ms – RLTL for single-core workloads
8ms – RLTL for eight-core workloads
Notes: We observe that when DRAM row is accessed, it is likely
to be accessed again. We call this phenomenon Row Level Temporal Locality (RLTL).
We define t-RLTL of an application,
as the fraction of rows that are accessed within time t after their previous access.
If an application has high RLTL for low T time, that application mostly accesses highly-charged DRAM rows, since the rows preserve most of their charge until the next access, which happens in a very Short interval.
Now, I’ll show the RLTL characteristics of 22 single-core workloads that we evaluted.
On Y-axis we have the fraction of accesses and on the X-axis we have the workloads.
[CLICK]
Our results show that, on average, 86% of the accesses are made to rows previously accessed within 8 ms.
Only one application has low RLTL. It is because that application makes very
Few accesses to the memory since it highly benefits from the caches.
For eight-core evaluations, the applications show even higher RLTL, 97%. It is due to the interference that the simultaneously runnning applications create on the memory.

## Slide 199: Key Idea
Track recently-accessed DRAM rows and use lower timing parameters if such rows are accessed again
Notes: The key idea of our mechanism is to
Track recently-accessed DRAM rows and use lower timing parameters
if such rows are accessed again.

## Slide 200: ChargeCache Overview
Memory Controller
ChargeCache
A
:B
:D
:C
:E
:F
Requests:
:A
D
A
DRAM
A
D
ChargeCache Miss:
Use Default Timings
ChargeCache Hit:
Use Lower Timings
Notes: We named our mechanism ChargeCache as it provides a cache-like benefit by reducing access
Latency and does so by taking advantage of the charge level stored in the row.
Now, I will demonstrate how ChargeCache works.
We have ChargeCache inside the Memory Controller.
On the right, you see a respesentation of DRAM where we have rows labeled from A to F.
[CLICK]
When the memory controller receives the first request to row A, it serves that request with typical timing parameters since we have
Nothing in ChargeCache. When
The request completes, it inserts the row address to one of the ChargeCache entries since we know that the row is highly-charged at that time. So, after that point,
The first entry points to Row A.
[CLICK]
The next request targets Row D. The memory controller probes the ChargeCache. It misses since we have only
Row A there. Similarly, Row D is inserted to ChargeCache.
[CLICK]
However, when we receive a request targetting row that we have in ChargeCache, the memory controller knows that the access
Goes to a highly-charged Row and tunes the DRAM Timing parameters to lower the access latency.
If there are not incoming requests to the Rows stored in ChargeCache for a long time, these rows will leak significant
Amount of charge and won’t be highly-charged rows anymore. For that reason, they need to be discarded from ChargeCache. [CLICK]
ChargeCache implements a low-cost mechanism to automatically invalidate its entries to ensure that its entries always
Point to highly-charged rows.

## Slide 201: Area and Power Overhead
Modeled with CACTI
Area
  ~5KB for 128-entry ChargeCache
  0.24% of a 4MB Last Level Cache (LLC) area
Power Consumption
  0.15 mW on average (static + dynamic)
  0.23% of the 4MB LLC power consumption
Notes: ChargeCache improves average DRAM access latency with low area and
Power consumption overhead. We evaluated that using CACTI tool.
A 128-entry ChargeCache totally requires only approximately 5KB of storage.
That is equal to 0.24% of the area of a 4MB Last Level Cache.
According to our evaluations, ChargeCache consumes only total 0.15 milli watts
Power on average. That is equal to 0.23% of the power consumption of a 4MB LLC.
We conclude that ChargeCache is a low cost mechanism in terms of area requirement and
Power consumption.

## Slide 202: Methodology
Simulator
  DRAM Simulator (Ramulator [Kim+, CAL’15])
    https://github.com/CMU-SAFARI/ramulator
Workloads
  22 single-core workloads
    SPEC CPU2006, TPC, STREAM
  20 multi-programmed 8-core workloads
    By randomly choosing from single-core workloads
  Execute at least 1 billion representative instructions per core (Pinpoints)
System Parameters
  1/8 core system with 4MB LLC
  Default tRCD/tRAS of 11/28 cycles
Notes: To evaluate ChargeCache, we used Ramulator, a cycle-accurate DRAM simulator.
For single-core evaluations, we analyzed 22 workloads from benchmark sets SPEC2006, TPC, and STREAM.
For multi-core evaluations we analyzed 20 multi-programmed workloads by assigning randomly-chosen
Single-core workload to each core.
For all workloads, we executed at least 1 billion representative instructions per core that we obtained using Pinpoints.
We evaluated both single and eight core systems with 4MB shared LLC.
Default tRCD and tRAS timings are 11 and 28 cycles respectively.

## Slide 203: Single-core Performance
NUAT
ChargeCache
ChargeCache + NUAT
LL-DRAM (Upper bound)
ChargeCache improves
single-core performance
Notes: Lets see how these mechanisms perform in single-core systems.
Here, on the Y-axis we have speedup and on the X-axis we have the workloads.
On this slide I show results for 10 most memory intensive workloads. However, the
Average includes all 22 applications that we evaluate.
As you see, NUAT improves performance slightly as expected.
On the other hand, ChargeCache significantly outperforms NUAT.
When used in combination, ChargeCache and NUAT provides some improvement over ChargeCache alone.
And LL-DRAM shows the maximum level of performance that we can achieve assuming all the rows are Highly-charged.
Generally, ChargeCache performs relatively close to LL-DRAM with a few exceptions. ChargeCache cannot perform As good as LL-DRAM because these workloads have significantly large working set which does not fit well in ChargeCache. We have analysis on ChargeCache with larger capacities in our paper.
So, as a conclusion, we can say that ChargeCache improves single-core performance.

## Slide 204: Eight-core Performance
NUAT
ChargeCache
ChargeCache + NUAT
LL-DRAM (Upperbound)
2.5%
9%
13%
ChargeCache significantly improves multi-core performance
Notes: For eight-core workloads, we again show only results for 10 most memory intensive workloads
And provide average of all 20 multi-programmed workloads we evalated.
NUAT again performs here relatively poorly and achieves only up to 2.5% speedup on average.
ChargeCache performs significantly better than NUAT. With eight-core workloads, ChargeCache
Achieves 9% improvement, on average.
ChargeCache performs better in eight-core systems due to interference that simultaneously running cores create on the main memory subsystem.
ChargeCache and NUAT, can improve the performance more when used together.
And finally LL-DRAM shows the upper bound that we can achieve. ChargeCache covers a relatively large portion of the performance that a LL-DRAM can provide.
We conclude that ChargeCache significantly improves multi-core performance.

## Slide 205: DRAM Energy Savings
ChargeCache reduces DRAM energy
Notes: ChargeCache provides energy savings due to the reduced execution time.
Here we show the average and maximum energy savings on the DRAM subsystem
For both single-core and eight-core evaluations.
ChargeCache can save up to almost 15% energy on the DRAM subsystem.
Note that, we also get system-wide energy savings due to the reduced execution time.
So, we conclude that ChargeCache saves DRAM energy.

## Slide 206: More on ChargeCache
Hasan Hassan, Gennady Pekhimenko, Nandita Vijaykumar, Vivek Seshadri, Donghyuk Lee, Oguz Ergin, and Onur Mutlu, "ChargeCache: Reducing DRAM Latency by Exploiting Row Access Locality" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)]
Source code will be released as part of Ramulator (May 2016)
  https://github.com/CMU-SAFARI/ramulator

## Slide 207: Tiered Latency DRAM

## Slide 208: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 209: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 210: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 211: Trade-Off: Area (Die Size) vs. Latency
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 212: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 213: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 214: Commodity DRAM vs. TL-DRAM [HPCA 2013]
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 215: Trade-Off: Area (Die-Area) vs. Latency
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 216: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 217: Performance & Power Consumption
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 218: Rethinking Memory Architecture
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 219: Large DRAM Power in Modern Systems
>40% in POWER7 (Ware+, HPCA’10)
  >40% in GPU (Paul+, ISCA’15)

## Slide 220: Why Is Power Large?
Design of DRAM uArchitecture
  A lot of waste (granularity, latency, …)
High Voltage
  Can we scale it down reliably?
High Frequency
  Can we scale it down with low performance impact?
DRAM Refresh
…

## Slide 221: Memory Dynamic Voltage/Freq. Scaling
Howard David, Chris Fallin, Eugene Gorbatov, Ulf R. Hanebutte, and Onur Mutlu, "Memory Power Management via Dynamic Voltage/Frequency Scaling" Proceedings of the 8th International Conference on Autonomic Computing (ICAC), Karlsruhe, Germany, June 2011. Slides (pptx) (pdf)

## Slide 222: New Memory Architectures
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 223: Readings on Memory Compression (I)
Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx) Source Code

## Slide 224: Readings on Memory Compression (II)
Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Low-Complexity, Low-Latency Main Memory Compression Framework" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Poster (pptx) (pdf)]

## Slide 225: Readings on Memory Compression (III)
Gennady Pekhimenko, Tyler Huberty, Rui Cai, Onur Mutlu, Phillip P. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Exploiting Compressed Block Size as an Indicator of Future Reuse" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 226: Readings on Memory Compression (IV)
Gennady Pekhimenko, Evgeny Bolotin, Nandita Vijaykumar, Onur Mutlu, Todd C. Mowry, and Stephen W. Keckler, "A Case for Toggle-Aware Compression for GPU Systems" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)]

## Slide 227: Readings on Memory Compression (V)
Nandita Vijaykumar, Gennady Pekhimenko, Adwait Jog, Abhishek Bhowmick, Rachata Ausavarungnirun, Chita Das, Mahmut Kandemir, Todd C. Mowry, and Onur Mutlu, "A Case for Core-Assisted Bottleneck Acceleration in GPUs: Enabling Flexible Data Compression with Assist Warps" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 228: End of Backup Slides

## Slide 229: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich CS, since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked @ Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research, Education, Consulting in
  Computer architecture and systems, bioinformatics
  Memory and storage systems, emerging technologies
  Many-core systems, heterogeneous systems, core design
  Interconnects
  Hardware/software interaction and co-design (PL, OS, Architecture)
  Predictable and QoS-aware systems
  Hardware fault tolerance and security
  Algorithms and architectures for genome analysis
  …