## Slide 1: Rethinking Memory System Design (for Data-Intensive Computing)
Onur Mutlu
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/
October 24, 2014
Samsung

## Slide 2: First, A Brief Research Overview

## Slide 3: Brief Self Introduction
Onur Mutlu
  Associate Professor @ Carnegie Mellon University ECE/CS
  PhD from UT-Austin 2006, worked at Microsoft Research, Intel, AMD
  http://www.ece.cmu.edu/~omutlu
  omutlu@gmail.com (Best way to reach me)
  http://users.ece.cmu.edu/~omutlu/projects.htm
Research, Teaching, Consulting in
  Computer architecture and systems, hardware/software interaction
  Memory and storage systems, emerging technologies
  Many-core systems, heterogeneous systems, core design
  Interconnects
  Hardware/software interaction and co-design (PL, OS, Architecture)
  Predictable and QoS-aware systems
  Hardware fault tolerance and security
  Algorithms and architectures for genome analysis
  …
  Interested in developing efficient, high-performance, and scalable systems; solving difficult architectural problems at low cost & complexity

## Slide 4: My Group: SAFARI
http://www.ece.cmu.edu/~safari/
http://www.ece.cmu.edu/~safari/pubs.html

## Slide 5: My Research Group: SAFARI
14 PhD students
2 Postdoctoral researchers
1 Visiting professor
3+ Undergraduate researchers
3+ Masters researchers
3 Visiting students and scholars
More than 15 graduates (masters and undergraduate)

## Slide 6
Research Focus: Computer architecture, HW/SW, bioinformatics
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
Onur Mutlu
Computer Architecture
and Systems
General Purpose GPUs
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Broad research
spanning systems to logic
with architecture at center
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for 3 students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does Broad research spanning systems to logic with architecture at center

## Slide 7
Some Current Directions and Projects
Rethinking Memory System Design for Data-Intensive Computing
  All aspects of DRAM, Flash Memory, Emerging Technologies
Single-Level Stores: Merging Memory and Storage with Fast NVM
GPUs as First-Class Computing Engines
In-memory Computing: Enabling Near-Data Processing
Predictable Systems: QoS Everywhere in the System
Secure and Easy-to-Program/Manage Memories: DRAM, Flash, NVM
Heterogeneous Systems: Architecting and Exploiting Asymmetry
Efficient and Scalable Interconnects
Genome Sequence Analysis & Assembly: Algorithms and Architectures
Onur Mutlu
Computer Architecture
and Systems
Notes: Some concrete current directions his group is exploring are:
Rethinking Memory System Design for Data-Intensive Computing
  Rethinking DRAM, Flash Memory, Emerging Technologies
Single-Level Stores: Merging Memory and Storage with Fast NVM
GP-GPUs as First-Class Computing Engines
In-memory computing
Predictable computing: QoS from the ground up
Secure Memories: DRAM, Flash, NVM
Genome Sequence Analysis and Assembly Algorithms and Architectures

## Slide 8
Example Infrastructure for Future Memory Designs
Onur Mutlu
Computer Architecture
and Systems
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is an example infrastructure his group has developed
to aggressively test and design modern DRAMs.
Onur’s research mixes experimental, analytical, simulation approaches to
Design the next generation systems in a scalable fashion.

## Slide 9: Experimental Infrastructure (DRAM)
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.

## Slide 10: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash
[Cai+, DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014]

## Slide 11: Related Videos and Course Materials
Computer Architecture Lecture Videos on Youtube
  https://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Computer Architecture Course Materials
  http://www.ece.cmu.edu/~ece447/s13/doku.php?id=schedule
Advanced Computer Architecture Course Materials
  http://www.ece.cmu.edu/~ece740/f13/doku.php?id=schedule
Advanced Computer Architecture Lecture Videos on Youtube
  https://www.youtube.com/playlist?list=PL5PHm2jkkXmgDN1PLwOY_tGtUlynnyV6D

## Slide 12: Referenced Papers
All are available at
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en

## Slide 13: Memory Systems Research Center @ Carnegie Mellon

## Slide 14: Memory Center @ CMU
Industry supported research center to solve industry-wide problems in memory systems
Focusing on cross layer software/hardware research in memory from devices to applications: new functions, new interfaces, new organizations, new uses, new technologies, …
Mission is to
  Design memory systems of the next decade
  Solve difficult memory system issues (DRAM, Flash, NVM scaling/uses, in-memory compute, management, reliability, QoS, …)
  Enable adoption via a neutral, collaborative forum
  Provide a source of professionals trained well in memory

## Slide 15: Rethinking Memory System Design (for Data-Intensive Computing)
Onur Mutlu
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/
October 24, 2014
Samsung

## Slide 16: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processor
and caches
Main Memory
Storage (SSD/HDD)

## Slide 17: Memory System: A Shared Resource View
Storage

## Slide 18: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 19: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 20: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 21: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 22: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years

## Slide 23: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer 2003]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 24: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 25: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 26: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 27: An Example of The Scaling Problem
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows in most real DRAM chips [Kim+ ISCA 2014]
Opened
Closed

## Slide 28: Most DRAM Modules Are At Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 29
DRAM Module
x86 CPU
Y
X
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 30
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 31
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 32
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 33: Observed Errors in Real Systems
In a more controlled environment, we can induce as many as ten million disturbance errors
A real reliability & security issue
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 34: Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 35: Experimental Infrastructure (DRAM)
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.

## Slide 36: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 37: Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 38: How Do We Solve The Problem?
Tolerate it: Make DRAM and controllers more intelligent
  Just like flash memory and hard disks
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
Embrace it: Design heterogeneous-reliability memories that map error-tolerant data to less reliable portions
…

## Slide 39: Exploiting Memory Error Tolerance
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search application
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 40: More on DRAM Disturbance Errors
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. Slides (pptx) (pdf) Lightning Session Slides (pptx) (pdf) Source Code and Data

## Slide 41: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. Slides (pptx) (pdf) Coverage on ZDNet

## Slide 42: Solutions to the DRAM Scaling Problem
Two potential solutions
  Tolerate DRAM (by taking a fresh look at it)
  Enable emerging memory technologies to eliminate/minimize DRAM
Do both
  Hybrid memory systems

## Slide 43: Solution 1: Tolerate DRAM
Overcome DRAM shortcomings with
  System-DRAM co-design
  Novel DRAM architectures, interface, functions
  Better waste management (efficient utilization)
Key issues to tackle
  Reduce energy
  Enable reliability at low cost
  Improve bandwidth and latency
  Reduce waste
  Enable computation close to data

## Slide 44: Solution 1: Tolerate DRAM
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri+, “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Pekhimenko+, “Linearly Compressed Pages: A Main Memory Compression Framework,” MICRO 2013.
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Avoid DRAM:
Seshadri+, “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
Pekhimenko+, “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
Seshadri+, “The Dirty-Block Index,” ISCA 2014.

## Slide 45: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Expected to scale to 9nm (2022 [ITRS])
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009, CACM 2010, Top Picks 2010.
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 46: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 47: An Orthogonal Issue: Memory Interference
Main
Memory
Core
Core
Core
Core
Cores’ interfere with each other when accessing shared main memory
Notes: In a multicore system, multiple applications running on the different cores share the main memory.
These applications interfere at the main memory. The result of this interference is unpredictable application slowdowns.

## Slide 48: An Orthogonal Issue: Memory Interference
Problem: Memory interference between cores is uncontrolled
   unfairness, starvation, low performance
   uncontrollable, unpredictable, vulnerable system
Solution: QoS-Aware Memory Systems
  Hardware designed to provide a configurable fairness substrate
    Application-aware memory scheduling, partitioning, throttling
  Software designed to configure the resources to satisfy different QoS goals
QoS-aware memory controllers and interconnects can provide predictable performance and higher efficiency

## Slide 49: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 50: A Mechanism to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 51: More on Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 52: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 53: QoS-Aware Memory Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 54: Goal: Predictable Performance in Complex Systems
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories
How to allocate resources to heterogeneous agents
to mitigate interference and provide predictable performance?

## Slide 55: Strong Memory Service Guarantees
Goal: Satisfy performance/SLA requirements in the presence of shared main memory, prefetchers, heterogeneous agents, and hybrid memory/storage
Approach:
  Develop techniques/models to accurately estimate the performance of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance
Example work: Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.

## Slide 56: Some Current Directions
New memory/storage + compute architectures
  Rethinking DRAM and flash memory
  Processing close to data; accelerating bulk operations
  Ensuring memory/storage reliability and robustness
Enabling emerging NVM technologies
  Hybrid memory systems with automatic data management
  Coordinated management of memory and storage with NVM
System-level memory/storage QoS
  QoS-aware controller and system design
  Coordinated memory + storage QoS

## Slide 57: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 58: Tolerating DRAM: Example Techniques
Retention-Aware DRAM Refresh: Reducing Refresh Impact
Refresh Access Parallelization: Reducing Refresh Impact
Tiered-Latency DRAM: Reducing DRAM Latency
RowClone: Accelerating Page Copy and Initialization
Subarray-Level Parallelism: Reducing Bank Conflict Impact
Base-Delta-Immediate Compression and Linearly Compressed Pages: Efficient Cache & Memory Compression

## Slide 59: Today’s Memory: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 60: Future: RowClone (In-Memory Copy)
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
90ns, 0.04uJ

## Slide 61: DRAM Subarray Operation (load one byte)
Row Buffer (4 Kbits)
Data Bus
8 bits
DRAM array
4 Kbits
Step 1: Activate row
Transfer row
Step 2: Read
Transfer byte onto bus
Notes: say you want a byte

## Slide 62: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbits)
Data Bus
8 bits
DRAM array
4 Kbits
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
0.01% area cost
Notes: copy

## Slide 63: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 64: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How does the software communicate occurrences of bulk copy/initialization to hardware?
How to maximize latency and energy savings?
How to ensure cache coherence?
How to handle data reuse?

## Slide 65: RowClone: Overall Performance
Chart: % Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 15 | 9 | 43 | 4 | 4 | 40
Energy Reduction | 40 | 32 | 60 | 15 | 17 | 67

## Slide 66: RowClone: Multi-Core Performance
Chart: 50 Workloads (4-core)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RowClone | 1.02 | 1.04 | 1.07 | 1.07 | 1.08 | 1.08 | 1.08 | 1.08 | 1.08 | 1.09 | 1.09 | 1.09 | 1.1 | 1.1 | 1.11 | 1.11 | 1.12 | 1.12 | 1.12 | 1.12 | 1.13 | 1.15 | 1.16 | 1.16 | 1.18 | 1.2 | 1.2 | 1.2 | 1.2 | 1.21 | 1.21 | 1.21 | 1.21 | 1.23 | 1.23 | 1.23 | 1.23 | 1.24 | 1.26 | 1.27 | 1.27 | 1.27 | 1.28 | 1.3 | 1.31 | 1.32 | 1.32 | 1.34 | 1.34 | 1.39

## Slide 67: Goal: Ultra-Efficient Processing Near Data
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 68: Enabling Ultra-Efficient Search
What is the right partitioning of computation capability?
What is the right low-cost memory substrate?
What memory technologies are the best enablers?
How do we rethink/ease (visual) search algorithms/applications?
Cache
Processor
Core
Interconnect
Memory
Database
Query vector
Results

## Slide 69: Enabling In-Memory Computation
Virtual Memory Support
Cache Coherence
DRAM Support
RowClone
(MICRO 2013)
Dirty-Block Index
(ISCA 2014)
Page Overlay
In-DRAM Gather Scatter
Randomization
Bitwise Operations
?
?
Non-contiguous Cache lines
Gathered Pages

## Slide 70: Tolerating DRAM: Example Techniques
Retention-Aware DRAM Refresh: Reducing Refresh Impact
Refresh Access Parallelization: Reducing Refresh Impact
Tiered-Latency DRAM: Reducing DRAM Latency
RowClone: Accelerating Page Copy and Initialization
Subarray-Level Parallelism: Reducing Bank Conflict Impact
Base-Delta-Immediate Compression and Linearly Compressed Pages: Efficient Cache & Memory Compression

## Slide 71
DRAM Latency-Capacity Trend
Chart: Year
| 2000.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0
Capacity | 0.125 | 0.25 | 0.5 | 1 | 2
Latency (tRC) | 65 | 60 | 57.5 | 49.5 | 47.91
16X
-20%
DRAM latency continues to be a critical bottleneck, especially for response time-sensitive workloads
Notes: The figure shows the historical trends of DRAM during the last 12-years, from 2000 to 2011.
We can see that, during this time, DRAM capacity has increased by 16 times.
On the other hand, during the same period of time, DRAM latency has reduced by only 20%.
As a result, the high DRAM latency continues to be a critical bottleneck for system performance.

## Slide 72: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 73: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 74: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 75: Trade-Off: Area (Die Size) vs. Latency
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 76: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 77: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 78: Tiered-Latency DRAM
Near Segment
Far Segment
Isolation Transistor
Divide a bitline into two segments with an isolation transistor
Sense Amplifier
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: Again, the key idea is to divide a subarray into two segments with isolation transistors.
The segment, directly connected to the sense amplifier, is called the near segment.
The other segment is called the far segment.

## Slide 79: Commodity DRAM vs. TL-DRAM
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 80: Trade-Off: Area (Die-Area) vs. Latency
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 81: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 82: Performance & Power Consumption
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 83: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 84: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 85: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 86: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 87: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 88: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 89: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 90: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 91: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 92: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 93: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Yoon et al., “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 94: Hybrid vs. All-PCM/DRAM
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 95: Aside: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ)
  Reference layer: Fixed
  Free layer: Parallel or anti-parallel
Cell
  Access transistor, bit/sense lines
Read and Write
  Read: Apply a small voltage across bitline and senseline; read the current.
  Write: Push large current through MTJ. Direction of current determines new orientation of the free layer.
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 96: Aside: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 97: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 98: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 99: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 100: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 101: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 102: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 103: Performance Benefits of a Single-Level Store
Results for PostMark
~5X
~24X

## Slide 104: Energy Benefits of a Single-Level Store
Results for PostMark
~5X
~16X

## Slide 105: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 106: Principles (So Far)
Better cooperation between devices and the system
  Expose more information about devices to upper layers
  More flexible interfaces
Better-than-worst-case design
  Do not optimize for the worst case
  Worst case should not determine the common case
Heterogeneity in design (specialization, asymmetry)
  Enables a more efficient design (No one size fits all)
These principles are related and sometimes coupled

## Slide 107: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies: Hybrid Memory Systems
How Can We Do Better?
Summary

## Slide 108: Summary: Memory Scaling
Memory scaling problems are a critical bottleneck for system performance, efficiency, and usability
New memory/storage + compute architectures
  Rethinking DRAM; processing close to data; accelerating bulk operations
Enabling emerging NVM technologies
  Hybrid memory systems with automatic data management
  Coordinated management of memory and storage with NVM
System-level memory/storage QoS
Three principles are essential for scaling
  Software/hardware/device cooperation
  Better-than-worst-case design
  Heterogeneity (specialization, asymmetry)

## Slide 109: Thank you.
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/

## Slide 110: Rethinking Memory System Design (for Data-Intensive Computing)
Onur Mutlu
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/
October 24, 2014
Samsung

## Slide 111: A Quote from A Famous Architect
“architecture […] based upon principle, and not upon precedent”

## Slide 112: Tolerating DRAM: Example Techniques
Retention-Aware DRAM Refresh: Reducing Refresh Impact
Refresh Access Parallelization: Reducing Refresh Impact
Tiered-Latency DRAM: Reducing DRAM Latency
RowClone: Accelerating Page Copy and Initialization
Subarray-Level Parallelism: Reducing Bank Conflict Impact
Base-Delta-Immediate Compression and Linearly Compressed Pages: Efficient Cache & Memory Compression

## Slide 113: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Activate each row every N ms
  Typical N = 64 ms
Downsides of refresh
-- Energy consumption: Each refresh consumes energy
  -- Performance degradation: DRAM rank/bank unavailable while refreshed
  -- QoS/predictability impact: (Long) pause times during refresh
  -- Refresh rate limits DRAM capacity scaling

## Slide 114: Refresh Overhead: Performance
8%
46%

## Slide 115: Refresh Overhead: Energy
15%
47%

## Slide 116: Retention Time Profile of DRAM

## Slide 117: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 118: Going Forward (for DRAM and Flash)
How to find out and expose weak memory cells/rows
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Low-cost system-level tolerance of memory errors
  Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
  Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
  Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Tolerating cell-to-cell interference at the system level
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
  Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.

## Slide 119: Experimental Infrastructure (DRAM)
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.

## Slide 120: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 121: More Information

## Slide 122: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 123: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
  Takeaway: Preserving within-thread bank-parallelism improves performance; request batching improves fairness
ATLAS memory scheduler [Kim+ HPCA’10]
  Idea: Prioritize threads that have attained the least service from the memory scheduler
  Takeaway: Prioritizing “light” threads improves performance

## Slide 124: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13] [Kim+, RTAS’14]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 125: SALP: Reducing DRAM Bank Conflict Impact
Kim, Seshadri, Lee, Liu, Mutlu
A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM
ISCA 2012.

## Slide 126: SALP: Reducing DRAM Bank Conflicts
Problem: Bank conflicts are costly for performance and energy
  serialized requests, wasted energy (thrashing of row buffer, busy wait)
Goal: Reduce bank conflicts without adding more banks (low cost)
Key idea: Exploit the internal subarray structure of a DRAM bank to parallelize bank conflicts to different subarrays
  Slightly modify DRAM bank to reduce subarray-level hardware sharing
Kim, Seshadri+ “A Case for Exploiting Subarray-Level
Parallelism in DRAM,” ISCA 2012.
-19%
+13%

## Slide 127: SALP: Key Ideas
A DRAM bank consists of mostly-independent subarrays
  Subarrays share some global structures to reduce cost
Key Idea of SALP: Minimally reduce sharing of global structures
Reduce the sharing of …
Global decoder  Enables pipelined access to subarrays
Global row buffer  Utilizes multiple local row buffers

## Slide 128: SALP: Reduce Sharing of Global Decoder
Local row-buffer
Local row-buffer
Global row-buffer
···
Global Decoder
Latch
Latch
Latch
Instead of a global latch, have per-subarray latches

## Slide 129: SALP: Reduce Sharing of Global Row-Buffer
Wire
Global bitlines
Global row-buffer
Local row-buffer
Local row-buffer
Switch
Switch
READ
READ
D
D
D
D
Selectively connect local row-buffers to global row-buffer using a Designated single-bit latch

## Slide 130: SALP: Baseline Bank Organization
Local row-buffer
Local row-buffer
Global row-buffer
Global Decoder
Global
bitlines
Latch

## Slide 131: SALP: Proposed Bank Organization
Local row-buffer
Local row-buffer
Global row-buffer
Global Decoder
Latch
Latch
D
D
Global
bitlines
Overhead of SALP in DRAM chip: 0.15%
1. Global latch  per-subarray local latches
2. Designated bit latches and wire to selectively enable a subarray

## Slide 132: SALP: Results
Wide variety of systems with different #channels, banks, ranks, subarrays
Server, streaming, random-access, SPEC workloads
Dynamic DRAM energy reduction: 19%
  DRAM row hit rate improvement: 13%
System performance improvement: 17%
  Within 3% of ideal (all independent banks)
DRAM die area overhead: 0.15%
  vs. 36% overhead of independent banks

## Slide 133: More on SALP
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, and Onur Mutlu, "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 134: Retention Time Characterization of Modern DRAM Devices
Liu, Jaiyen, Kim, Wilkerson and Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”
ISCA 2013.

## Slide 135: Summary (I)
DRAM requires periodic refresh to avoid data loss
  Refresh wastes energy, reduces performance, limits DRAM density scaling
Many past works observed that different DRAM cells can retain data for different times without being refreshed; proposed reducing refresh rate for strong DRAM cells
  Problem: These techniques require an accurate profile of the retention time of all DRAM cells
Our goal: To analyze the retention time behavior of DRAM cells in modern DRAM devices to aid the collection of accurate profile information
Our experiments: We characterize 248 modern commodity DDR3 DRAM chips from 5 manufacturers using an FPGA based testing platform
Two Key Issues:
  1. Data Pattern Dependence: A cell’s retention time is heavily dependent on data values stored in itself and nearby cells, which cannot easily be controlled.
  2. Variable Retention Time: Retention time of some cells change unpredictably from high to low at large timescales.

## Slide 136: Summary (II)
Key findings on Data Pattern Dependence
  There is no observed single data pattern that elicits the lowest retention times for a DRAM device  very hard to find this pattern
  DPD varies between devices due to variation in DRAM array circuit design between manufacturers
  DPD of retention time gets worse as DRAM scales to smaller feature sizes
Key findings on Variable Retention Time
  VRT is common in modern DRAM cells that are weak
  The timescale at which VRT occurs is very large (e.g., a cell can stay in high retention time state for a day or longer)  finding minimum retention time can take very long
Future work on retention time profiling must address these issues

## Slide 137: Retention Failure Coverage of Data Patterns
A 2Gb chip family
6.1s retention time
Walk is the most effective data pattern for this device
Coverage of fixed patterns is low: ~30% for All 0s/1s
No data pattern achieves 100% coverage
Different data patterns have widely different coverage:
Data pattern dependence exists and is severe

## Slide 138: Data Pattern Dependence: Observations (I)
A cell’s retention time is heavily influenced by data pattern stored in other cells
  Pattern affects the coupling noise, which affects cell leakage
No tested data pattern exercises the worst case retention time for all cells (no pattern has 100% coverage)
  No pattern is able to induce the worst-case coupling noise for every cell
  Problem: Underlying DRAM circuit organization is not known to the memory controller  very hard to construct a pattern that exercises the worst-case cell leakage
   Opaque mapping of addresses to physical DRAM geometry
   Internal remapping of addresses within DRAM to tolerate faults
   Second order coupling effects are very hard to determine

## Slide 139: Data Pattern Dependence: Observations (II)
Fixed, simple data patterns have low coverage
  They do not exercise the worst-case coupling noise
The effectiveness of each data pattern varies significantly between DRAM devices (of the same or different vendors)
  Underlying DRAM circuit organization likely differs between different devices  patterns leading to worst coupling are different in different devices
Technology scaling appears to increase the impact of data pattern dependence
  Scaling reduces the physical distance between circuit elements, increasing the magnitude of coupling effects

## Slide 140: Effect of Technology Scaling on DPD
A 1Gb chip family
A 2Gb chip family
The lowest-coverage data pattern achieves much lower coverage for the smaller technology node

## Slide 141: DPD: Implications on Profiling Mechanisms
Any retention time profiling mechanism must handle data pattern dependence of retention time
Intuitive approach: Identify the data pattern that induces the worst-case retention time for a particular cell or device
Problem 1: Very hard to know at the memory controller which bits actually interfere with each other due to
  Opaque mapping of addresses to physical DRAM geometry  logically consecutive bits may not be physically consecutive
  Remapping of faulty bitlines/wordlines to redundant ones internally within DRAM
Problem 2: Worst-case coupling noise is affected by non-obvious second order bitline coupling effects

## Slide 142: Variable Retention Time
A 2Gb chip family
Min ret time = Max ret time
Expected if no VRT
Most failing cells
exhibit VRT
Many failing cells jump from
very high retention time to very low

## Slide 143: VRT: Implications on Profiling Mechanisms
Problem 1: There does not seem to be a way of determining if a cell exhibits VRT without actually observing a cell exhibiting VRT
  VRT is a memoryless random process [Kim+ JJAP 2010]
Problem 2: VRT complicates retention time profiling by DRAM manufacturers
  Exposure to very high temperatures can induce VRT in cells that were not previously susceptible
   can happen during soldering of DRAM chips
   manufacturer’s retention time profile may not be accurate
One option for future work: Use ECC to continuously profile DRAM online while aggressively reducing refresh rate
  Need to keep ECC overhead in check

## Slide 144: Online Retention Time Profiling

## Slide 145: Towards an Online Profiling System
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
  But degrades performance
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Notes: Our high-level design for online profiling system is based to thee key observations:

## Slide 146: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 147: Summary and Conclusions
DRAM refresh is a critical challenge
  in scaling DRAM technology efficiently to higher capacities
Discussed several promising solution directions
  Parallelize refreshes with accesses [Chang+ HPCA’14]
  Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Examined properties of retention time behavior [Liu+ ISCA’13]
Many avenues for overcoming DRAM refresh challenges
  Handling DPD/VRT phenomena
  Enabling online retention time profiling and error mitigation
  Exploiting application behavior

## Slide 148: DRAM Reliability

## Slide 149: How Do We Solve The Problem?
Tolerate it: Make DRAM and controllers more intelligent
  Just like flash memory and hard disks
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
Embrace it: Design heterogeneous-reliability memories that map error-tolerant data to less reliable portions
…

## Slide 150: Exploiting Memory Error Tolerance
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search application
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 151: Aside: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA),
pages 39-50, Beijing, China, June 2008. Slides (pptx)

## Slide 152: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to optimize for performance (in the presence of constraints)
  Reordering is not simple
  Predicting the future?

## Slide 153: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 154: More on DRAM Operation and Constraints
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 155: Self-Optimizing DRAM Controllers
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.

## Slide 156: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 157: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 158: Performance Results

## Slide 159: Hybrid Memory Management

## Slide 160: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 161: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Yoon et al., “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 162: Row-Locality-Aware Data Placement: Results
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
17%
Memory energy-efficiency and fairness also improve correspondingly

## Slide 163: Building Large Caches for Hybrid Memories
Meza, Chang, Yoon, Mutlu, and Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management”
IEEE Comp Arch Letters 2012.

## Slide 164: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two ideas:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 165: The Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 166: Idea 1: Store Tags in Main Memory
Store tags in the same row as data in DRAM
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 167: Idea 2: Cache Tags in On-Chip SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 168: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 169
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 170
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 171: Hybrid Main Memory: Research Topics
Many research topics from technology layer to algorithms layer
Enabling NVM and hybrid memory
  How to maximize performance?
  How to maximize lifetime?
  How to prevent denial of service?
Exploiting emerging tecnologies
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to minimize cost?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 172: Security Challenges of Emerging Technologies
1. Limited endurance  Wearout attacks
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
3. Multiple bits per cell  Information leakage (via side channel)

## Slide 173: Refresh-Access Parallelization

## Slide 174: Refresh Penalty
Processor
Memory Controller
DRAM
Refresh
Read
Data
Capacitor
Access transistor
Refresh delays requests by 100s of ns
Refresh interferes with memory accesses

## Slide 175: Existing Refresh Modes
Time
Per-bank refresh in mobile DRAM (LPDDRx)
Time
All-bank refresh in commodity DRAM (DDRx)
Bank 7
Bank 1
Bank 0
…
Bank 7
Bank 1
Bank 0
…
Refresh
Round-robin order
…
Per-bank refresh allows accesses to other banks while a bank is refreshing

## Slide 176: Shortcomings of Per-Bank Refresh
Problem 1: Refreshes to different banks are scheduled in a strict round-robin order
  The static ordering is hardwired into DRAM chips
  Refreshes busy banks with many queued requests when other banks are idle
Key idea: Schedule per-bank refreshes to idle banks opportunistically in a dynamic order

## Slide 177: Our First Approach: DARP
Dynamic Access-Refresh Parallelization (DARP)
  An improved scheduling policy for per-bank refreshes
  Exploits refresh scheduling flexibility in DDR DRAM
Component 1: Out-of-order per-bank refresh
  Avoids poor static scheduling decisions
  Dynamically issues per-bank refreshes to idle banks
Component 2: Write-Refresh Parallelization
  Avoids refresh interference on latency-critical reads
  Parallelizes refreshes with a batch of writes

## Slide 178: Shortcomings of Per-Bank Refresh
Problem 2: Banks that are being refreshed cannot concurrently serve memory requests
Time
Bank 0
RD
Delayed by refresh
Per-Bank Refresh

## Slide 179: Shortcomings of Per-Bank Refresh
Problem 2: Refreshing banks cannot concurrently serve memory requests
Key idea: Exploit subarrays within a bank to parallelize refreshes and accesses across subarrays
Time
Bank 0
Subarray 1
Subarray 0
RD
Subarray Refresh
Time
Parallelize

## Slide 180: Methodology
100 workloads: SPEC CPU2006, STREAM, TPC-C/H, random access
System performance metric: Weighted speedup
DDR3 Rank
Simulator configurations
Memory Controller
8-core processor
Memory Controller
Bank 7
Bank 1
Bank 0
…
L1 $: 32KB
L2 $: 512KB/core

## Slide 181: Comparison Points
All-bank refresh [DDR3, LPDDR3, …]
Per-bank refresh [LPDDR3]
Elastic refresh [Stuecheli et al., MICRO ‘10]:
  Postpones refreshes by a time delay based on the predicted rank idle time to avoid interference on memory requests
  Proposed to schedule all-bank refreshes without exploiting per-bank refreshes
  Cannot parallelize refreshes and accesses within a rank
Ideal (no refresh)

## Slide 182: System Performance
Chart: DRAM Chip Density
All-Bank | 5.5359 | 5.3024 | 4.8311
Per-Bank | 5.7551 | 5.5256 | 5.0271
Elastic | 5.6343 | 5.3803 | 4.8911
DARP | 5.9537 | 5.8162 | 5.2317
SARP | 5.9777 | 5.9152 | 5.7295
DSARP | 5.9723 | 5.9543 | 5.8059
Ideal | 6.0252 | 6.0252 | 6.0252
7.9%
12.3%
20.2%
1. Both DARP & SARP provide performance gains and combining them (DSARP) improves even more
2. Consistent system performance improvement across DRAM densities (within 0.9%, 1.2%, and 3.8% of ideal)

## Slide 183: Energy Efficiency
3.0%
5.2%
9.0%
Consistent reduction on energy consumption
Chart: DRAM Chip Density
All-Bank | 38.2974 | 40.28 | 44.8967
Per-Bank | 38.0134 | 39.9893 | 44.5521
Elastic | 37.5049 | 39.3169 | 44.1509
DARP | 37.191 | 38.5881 | 43.25
SARP | 37.1096 | 38.322 | 41.0809
DSARP | 37.137 | 38.197 | 40.8495
Ideal | 36.6284 | 36.6284 | 36.6284

## Slide 184: NVM

## Slide 185: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 186: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 187: Memory Interference and QoS

## Slide 188: Many Cores on Chip
What we want:
  N times the system performance with N times the cores
What do we get today?

## Slide 189: (Un)expected Slowdowns
Memory Performance Hog
Low priority
High priority
(Core 0)
(Core 1)
Moscibroda and Mutlu, “Memory performance attacks: Denial of memory service
in multi-core systems,” USENIX Security 2007.
Attacker
(Core 1)
Movie player
(Core 2)
Notes: What kind of performance do we expect when we run two applications on a multi-core system? To answer this question, we performed an experiment. We took two applications we cared about, ran them together on different cores in a dual-core system, and measured their slowdown compared to when each is run alone on the same system. This graph shows the slowdown each app experienced. (DATA explanation…)
Why do we get such a large disparity in the slowdowns?
Is it the priorities? No. We went back and gave high priority to gcc and low priority to matlab. The slowdowns did not change at all. Neither the software or the hardware enforced the priorities.
Is it the contention in the disk? We checked for this possibility, but found that these applications did not have any disk accesses in the steady state. They both fit in the physical memory and therefore did not interfere in the disk.
What is it then? Why do we get such large disparity in slowdowns in a dual core system?
I will call such an application a “memory performance hog”
Now, let me tell you why this disparity in slowdowns happens.
Is it that there are other applications or the OS interfering with gcc, stealing its time quantums? No.

## Slide 190: Why? Uncontrolled Memory Interference
CORE 1
CORE 2
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2
Shared DRAM
Memory System
Multi-Core
Chip
unfairness
INTERCONNECT
attacker
movie player
DRAM
Bank 3
Notes: -In a multi-core chip, different cores share some hardware resources. In particular, they share the DRAM memory system. The shared memory system consists of this and that.
When we run matlab on one core, and gcc on another core, both cores generate memory requests to access the DRAM banks. When these requests arrive at the DRAM controller, the controller favors matlab’s requests over gcc’s requests. As a result, matlab can make progress and continues generating memory requests. These requests are again favored by the DRAM controller over gcc’s requests. Therefore, gcc starves waiting for its requests to be serviced in DRAM whereas matlab makes very quick progress as if it were running alone.
Why does this happen? This is because the algorithms employed by the DRAM controller are unfair.
But, why are these algorithms unfair? Why do they unfairly prioritize matlab accesses?
To understand this, we need to understand how a DRAM bank operates.
Almost all systems today contain multi-core chips
Multi-core systems consist of multiple on-chip cores and caches
Cores share the DRAM memory system
DRAM memory system consists of
  DRAM banks that store data (multiple banks to allow parallel accesses)
  DRAM memory controller that mediates between cores and DRAM memory
    It schedules memory operations generated by cores to DRAM
This talk is about exploiting the unfair algorithms in the memory controllers to perform denial of service to running threads
To understand how this happens, we need to know about how each DRAM bank operates

## Slide 191: A Memory Performance Hog
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = rand();
A[index] = B[index];
…
}
STREAM
Sequential memory access
Very high row buffer locality (96% hit rate)
Memory intensive
RANDOM
Random memory access
Very low row buffer locality (3% hit rate)
Similarly memory intensive
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = j*linesize;
A[index] = B[index];
…
}
streaming
random
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Streaming through memory by performing operations on two 1D arrays.
Sequential memory access
Each access is a cache miss (elements of array larger than a cache line size)  hence, very memory intensive
Link to the real code…

## Slide 192: What Does the Memory Hog Do?
Row Buffer
Row decoder
Column mux
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
Memory Request Buffer
T0: STREAM
T1: RANDOM
Row size: 8KB, cache block size: 64B
128 (8KB/64B) requests of T0 serviced before T1
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Pictorially demonstrate how stream denies memory service to rdarray
Stream continuously accesses columns in row 0 in a streaming manner (streams through a row after opening it)
In other words almost all its requests are row-hits
RDarray’s requests are row-conflicts (no locality)
The DRAM controller reorders streams requests to the open row over other requests (even older ones) to maximize DRAM throughput
Hence, rdarray’s requests do not get serviced as long as stream is issuing requests at a fast-enough rate
In this example, the red thread’s request to another row will not get serviced until stream stops issuing a request to row 0
With those parameters, 128 requests of stream would be serviced before 1 from rdarray
As row-buffer size increases, which is the industry trend, this problem will become more severe
This is not the worst case, but it is easy to construct and understand
  Stream falls off the row buffer at some point
I leave it to the listeners to construct a case worse than this (it is possible)

## Slide 193: DRAM Controllers
A row-conflict memory access takes significantly longer than a row-hit access
Current controllers take advantage of the row buffer
Commonly used scheduling policy (FR-FCFS) [Rixner 2000]*
  (1) Row-hit first: Service row-hit memory accesses first
  (2) Oldest-first: Then service older accesses first
This scheduling policy aims to maximize DRAM throughput
    But, it is unfair when multiple threads share the DRAM system
*Rixner et al., “Memory Access Scheduling,” ISCA 2000.
*Zuravleff and Robinson, “Controller for a synchronous DRAM …,” US Patent 5,630,096, May 1997.

## Slide 194: Effect of the Memory Performance Hog
Chart: 
| STREAM | RANDOM
Column1 | 1.18 | 2.82
1.18X slowdown
2.82X slowdown
Results on Intel Pentium D running Windows XP
(Similar results for Intel Core Duo and AMD Turion, and on Fedora Linux)
Slowdown
Chart: 
| STREAM | gcc
Column1 | 1.23 | 2.91
Chart: 
| STREAM | Virtual PC
Column1 | 1.21 | 2.59
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: RANDOM was given higher OS priority in the experiments

## Slide 195: Greater Problem with More Cores
Vulnerable to denial of service (DoS)
Unable to enforce priorities or SLAs
Low system performance
Uncontrollable, unpredictable system

## Slide 196: Greater Problem with More Cores
Vulnerable to denial of service (DoS) [Usenix Security’07]
Unable to enforce priorities or SLAs [MICRO’07,’10,’11, ISCA’08’11’12, ASPLOS’10]
Low system performance [IEEE Micro Top Picks ’09,’11a,’11b,’12]
Uncontrollable, unpredictable system

## Slide 197: Distributed DoS in Networked Multi-Core Systems
Attackers
(Cores 1-8)
Stock option pricing application
(Cores 9-64)
Cores connected via
packet-switched
routers on chip
~5000X slowdown
Grot, Hestness, Keckler, Mutlu,
“Preemptive virtual clock: A Flexible,
Efficient, and Cost-effective QOS
Scheme for Networks-on-Chip,“
MICRO 2009.

## Slide 198: How Do We Solve The Problem?
Inter-thread interference is uncontrolled in all memory resources
  Memory controller
  Interconnect
  Caches
We need to control it
  i.e., design an interference-aware (QoS-aware) memory system

## Slide 199: QoS-Aware Memory Systems: Challenges
How do we reduce inter-thread interference?
  Improve system performance and core utilization
  Reduce request serialization and core starvation
How do we control inter-thread interference?
  Provide mechanisms to enable system software to enforce QoS policies
  While providing high system performance
How do we make the memory system configurable/flexible?
  Enable flexible mechanisms that can achieve many goals
    Provide fairness or throughput when needed
    Satisfy performance guarantees when needed

## Slide 200: Solution: QoS-Aware, Predictable Memory
Problem: Memory interference is uncontrolled  uncontrollable, unpredictable, vulnerable system
Goal: We need to control it  Design a QoS-aware system
Solution: Hardware/software cooperative memory QoS
  Hardware designed to provide a configurable fairness substrate
    Application-aware memory scheduling, partitioning, throttling
  Software designed to configure the resources to satisfy different QoS goals
  E.g., fair, programmable memory controllers and on-chip networks provide QoS and predictable performance
  [2007-2012, Top Picks’09,’11a,’11b,’12]

## Slide 201: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 202: A Mechanism to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 203: More on Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 204: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 205: QoS-Aware Memory Scheduling: Evolution

## Slide 206: QoS-Aware Memory Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 207: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
ATLAS memory scheduler [Kim+ HPCA’10]

## Slide 208: Within-Thread Bank Parallelism
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread A
thread B
thread execution timeline
WAIT
WAIT
thread B
thread A
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread execution timeline
WAIT
WAIT
rank
thread B
thread A
thread A
thread B
SAVED CYCLES
Key Idea:
Notes: A memory scheduler can actively exploit bank-level parallelism to reduce the effective memory access latency. Here’s how.
Let us assume a case where two threads send two memory requests to two different banks.
A naïve memory scheduler that doesn’t exploit bank-level parallelism would schedule the requests in the order they arrived.
As shown in their thread execution timeline, both threads must wait for two bank latencies before all their requests are serviced.
In contrast, a memory scheduler that is aware of bank-level parallelism was proposed by Mutlu and Moscibroda.
Their key idea was to rank the threads so that thread’s memory requests are prioritized in the same order across all the banks.
In this case, let us assume that the blue thread’s request are the most prioritized.
The scheduler would then reorder the requests at bank 1’s request buffer…
so that the blue requests are serviced concurrently, after which the red requests can be serviced concurrently.
The memory service timeline shows how the access latencies for requests from the same thread are overlapped.
And, as a result, thread A has to wait less for its requests to be serviced.

## Slide 209: Parallelism-Aware Batch Scheduling [ISCA’08]
Principle 1: Schedule requests from a thread back to back
  Preserves each thread’s bank parallelism
  But, this can cause starvation…
Principle 2: Group a fixed number of oldest requests from each thread into a “batch”
  Service the batch before all other requests
  Form a new batch when the current batch is done
  Eliminates starvation, provides fairness
Bank 0
Bank 1
T0
T0
T1
T1
T3
T3
T2
T2
T3
T3
T3
Batch
T1
T0
T0
Notes: Threads are ordered such that 1) system throughput is maximized and 2) stall-time fairness is maintained
(An ordering/ranking is formed among threads)
The key idea of this ordering is to maximize system throughput

## Slide 210: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
  Takeaway: Preserving within-thread bank-parallelism improves performance; request batching improves fairness
ATLAS memory scheduler [Kim+ HPCA’10]
  Idea: Prioritize threads that have attained the least service from the memory scheduler
  Takeaway: Prioritizing “light” threads improves performance

## Slide 211: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient
Notes: So why do previous algorithms fail?
On the one hand there is the throughput biased approach that prioritizes less memory-intensive threads.
Servicing memory requests from such threads allow them to make progress in the processor, increasing throughput.
However, the most memory-intensive thread, thread C, remains persistently deprioritized and and becomes prone to starvation causing large slowdowns and, ultimately, unfairness.
On the other hand there is the fairness biased approach where threads take turns accessing the memory.
In this case, the most memory-intensive thread does not starve.
However, the least memory-intensive thread, thread A, is not prioritized, leading to reduced throughput.
As you can see, a single policy applied to all threads is insufficient since different threads have different memory access needs.

## Slide 212: Previous Scheduling Algorithms are Biased
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.778
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput
bias
Fairness
bias
No previous memory scheduling algorithm provides both the best fairness and system throughput
Ideal
Better system throughput
Better fairness

## Slide 213: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread
Notes: So how do we achieve the best of both worlds? Our algorithm is based on the following insights:
First, we would like to prioritize the memory-non-intensive threads to increase system throughput.
Doing so does not degrade unfairness, since memory-non-intensive threads are inherently “light” and rarely cause interference for the memory-intensive threads.
For fairness, we discovered that unfairness is usually caused when one memory-intensive thread is prioritized over another.
As we’ve seen, the most deprioritized thread can starve.
To address this problem, we would like to shuffle their priority so that no single thread is persistently prioritized over another thread.
However, memory-intensive threads are not created equal.
They have different vulnerability to memory interference.
To address their differences, shuffling should be performed in an asymmetric manner.

## Slide 214: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Notes: Our algorithm, Thread Cluster Memory Scheduling, first groups threads into two clusters.
Among the threads executing in the system, some are memory-non-intensive whereas some are memory-intensive.
We isolate the memory-non-intensive threads into the non-intensive cluster and the memory-intensive threads into the intensive cluster.
This is so that we can apply different policies for different threads.
Subsequently, we prioritize the non-intensive cluster over the intensive cluster since the non-intensive threads have greater potential for making progress IN THEIR CORES [ONUR].
Finally, we apply different policies within each cluster, one optimized for throughput and the other for fairness.

## Slide 215: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.777999999999998 | 9.179
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput
Notes: This figure shows the performance of the four previous scheduling algorithms in addition to TCM, averaged over 96 workloads.
FRFCFS has low system throughput and fairness.
STFM and PAR-BS is biased towards fairness, while ATLAS is biased towards system throughput.
TCM lies towards the lower right part of the figure and provides the best fairness and system throughput.
Compared to ATLAS, TCM provides approx 5% better throughput and 39% better fairness.
Compared to PAR-BS, TCM provides approx 5% better fairness and 8% better throughput.

## Slide 216: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13.0 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 217: More on TCM
Kim et al., “Thread Cluster Memory Scheduling: Exploiting Differences in Memory Access Behavior,” MICRO 2010, Top Picks 2011.

## Slide 218: QoS-Aware Memory Scheduling: Evolution
Thread cluster memory scheduling [Kim+ MICRO’10]
  Idea: Cluster threads into two groups (latency vs. bandwidth sensitive); prioritize the latency-sensitive ones; employ a fairness policy in the bandwidth sensitive group
  Takeaway: Heterogeneous scheduling policy that is different based on thread behavior maximizes both performance and fairness
Integrated Memory Channel Partitioning and Scheduling [Muralidhara+ MICRO’11]
    Idea: Only prioritize very latency-sensitive threads in the scheduler; mitigate all other applications’ interference via channel partitioning
    Takeaway: Intelligently combining application-aware channel partitioning and memory scheduling provides better performance than either

## Slide 219: Memory Control in CPU-GPU Systems
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 220: SMS: Our Goal
Design a new memory scheduler that is:
  Scalable to accommodate a large number of requests
  Easy to implement
  Application-aware
  Able to provide high performance and fairness, especially in heterogeneous CPU-GPU systems
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Notes: Our goal in this project is to design a new memory scheduler that is <click> scalable to accommodate a large number of requests, <click> easy-to-implement, <click> application-aware and <click> able to provide high performance and fairness especially in heterogeneous CPU-GPU systems.
<transition … >
To this end, we have made several observations that lead to our new memory scheduler design

## Slide 221: SMS Key Idea: Decouple Tasks into Stages
Idea: Decouple the functional tasks of the memory controller
  Partition tasks across several simpler HW structures (stages)
1) Maximize row buffer hits
  Stage 1: Batch formation
  Within each application, groups requests to the same row into batches
2) Manage contention between applications
  Stage 2: Batch scheduler
  Schedules batches from different applications
3) Satisfy DRAM timing constraints
  Stage 3: DRAM command scheduler
  Issues requests from the already-scheduled order to each bank
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Notes: Our key idea is to decouple these functional tasks <click> into different stages.
<click>
We partition these three <click> tasks across several simpler hardware structures, which we call stages.
<click>
Stage 1 is the batch formation. This stage maximizes row buffer hits by grouping requests that access the same row within each application into batches
<click>
Stage 2 is the batch scheduler. This stage manages contention by scheduling batches from different applications
<click>
And stage 3 is the DRAM command scheduler. This stage issues requests from an already scheduled order and make sure that it satisfy DRAM timing constraints
<click … transition>
With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through …

## Slide 222: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 223: Memory QoS in a Parallel Application
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread that is falling behind the most in a parallel for loop
Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.

## Slide 224: QoS-Aware Memory Scheduling: Evolution
Parallel application memory scheduling [Ebrahimi+ MICRO’11]
  Idea: Identify and prioritize limiter threads of a multithreaded application in the memory scheduler; provide fast and fair progress to non-limiter threads
  Takeaway: Carefully prioritizing between limiter and non-limiter threads of a parallel application improves performance
Staged memory scheduling [Ausavarungnirun+ ISCA’12]
    Idea: Divide the functional tasks of an application-aware memory scheduler into multiple distinct stages, where each stage is significantly simpler than a monolithic scheduler
    Takeaway: Staging enables the design of a scalable and relatively simpler application-aware memory scheduler that works on very large request buffers

## Slide 225: QoS-Aware Memory Scheduling: Evolution
MISE [Subramanian+ HPCA’13]
    Idea: Estimate the performance of a thread by estimating its change in memory request service rate when run alone vs. shared  use this simple model to estimate slowdown to design a scheduling policy that provides predictable performance or fairness
    Takeaway: Request service rate of a thread is a good proxy for its performance; alone request service rate can be estimated by giving high priority to the thread in memory scheduling for a while
Easy
Harder

## Slide 226: QoS-Aware Memory Scheduling: Evolution
Prefetch-aware shared resource management [Ebrahimi+ ISCA’12] [Ebrahimi+ MICRO’09] [Lee+ MICRO’08]
  Idea: Prioritize prefetches depending on how they affect system performance; even accurate prefetches can degrade performance of the system
  Takeaway: Carefully controlling and prioritizing prefetch requests improves performance and fairness
DRAM-Aware last-level cache policies [Lee+ HPS Tech Report’10] [Lee+ HPS Tech Report’10] [Seshadri+ ISCA’14]
  Idea: Design cache eviction and replacement policies such that they proactively exploit the state of the memory controller and DRAM (e.g., proactively evict data from the cache that hit in open rows)
  Takeaway: Coordination of last-level cache and DRAM policies improves performance and fairness

## Slide 227: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request/thread scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 228: Readings on Memory QoS (I)
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Mutlu and Moscibroda, “Stall-Time Fair Memory Access Scheduling,” MICRO 2007.
Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008, IEEE Micro 2009.
Kim et al., “ATLAS: A Scalable and High-Performance Scheduling Algorithm for Multiple Memory Controllers,” HPCA 2010.
Kim et al., “Thread Cluster Memory Scheduling,” MICRO 2010, IEEE Micro 2011.
Muralidhara et al., “Memory Channel Partitioning,” MICRO 2011.
Ausavarungnirun et al., “Staged Memory Scheduling,” ISCA 2012.
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Das et al., “Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems,” HPCA 2013.

## Slide 229: Readings on Memory QoS (II)
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS 2010, ACM TOCS 2012.
Lee et al., “Prefetch-Aware DRAM Controllers,” MICRO 2008, IEEE TC 2011.
Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.
Ebrahimi et al., “Prefetch-Aware Shared Resource Management for Multi-Core Systems,” ISCA 2011.

## Slide 230: Strong Memory Service Guarantees
Goal: Satisfy performance bounds/requirements in the presence of shared main memory, prefetchers, heterogeneous agents, and hybrid memory
Approach:
  Develop techniques/models to accurately estimate the performance of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance

## Slide 231: Need for Predictable Performance
There is a need for predictable performance
  When multiple applications share resources
  Especially if some applications require performance guarantees
Example 1: In mobile systems
  Interactive applications run with non-interactive applications
  Need to guarantee performance for interactive applications
Example 2: In server systems
  Different users’ jobs consolidated onto the same server
  Need to provide bounded slowdowns to critical jobs
Our Goal: Predictable performance
in the presence of memory interference
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Notes: …because there is a need for predictable performance
When multiple applications share resources and
Especially when some applications require guarantees on performance.
For example, in mobile systems, interactive applications are run with non-interactive ones.
And there is a need to provide guarantees on performance to the interactive applications.
In server systems, different users’ jobs are heavily consolidated onto the same server.
In such a scenario, there is a need to achieve bounded slowdowns for critical jobs of users.
These are a couple of examples of systems that need predictable performance.
There are many other systems (such as …) in which performance predictability is necessary.
Therefore, our goal in this work is to provide predictable performance in the presence of memory interference.

## Slide 232: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
Notes: Towards this goal, we propose to first estimate application slowdowns due to main memory interference.
And once we have accurate slowdown estimates, we propose to leverage them to control application slowdowns.

## Slide 233: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: First, let me describe the key observations that enable us to estimate application slowdowns.

## Slide 234: Slowdown: Definition
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 235: Key Observation 1
For a memory bound application,
Performance  Memory request service rate
Chart: Normalized Request Service Rate
| 0.358607859 | 0.408507739 | 0.532531575 | 0.580993121999996 | 0.632877307000005 | 0.690879954000007 | 0.726945501000005 | 0.796354682 | 0.837558983 | 0.938360254 | 0.948305607000005 | 1.0
omnetpp | 0.34972 | 0.39891 | 0.5217 | 0.56944 | 0.61954 | 0.67835 | 0.71425 | 0.78346 | 0.8265 | 0.928 | 0.94883 | 1
mcf | 0.34876 | 0.39942 | 0.4869 | 0.53653 | 0.54337 | 0.55102 | 0.58278 | 0.61457 | 0.65149 | 0.74316 | 0.84741 | 0.93386 | 0.9689 | 1
astar | 0.41586 | 0.48052 | 0.66786 | 0.72536 | 0.77686 | 0.79876 | 0.84877 | 0.88035 | 0.92559 | 0.95012 | 0.98596 | 1
Easy
Harder
Intel Core i7, 4 cores
Mem. Bandwidth: 8.5 GB/s
Notes: We observe that for a memory bound application, its performance is roughly proportional to the rate at which its memory requests are serviced.
This plot shows the results of our experiment on an Intel, 4-core system. We run omnetpp, a SPEC CPU 2006 benchmark along with another memory hog, whose memory intensity can be varied. This, in turn, lets us vary the rate at which the memory requests of omnetpp are serviced.
The x-axis shows the normalized request service rate of omnetpp, normalized to when it is run alone.
The y-axis shows the performance of omnetpp, normalized to when it is run alone.
As can be seen, there is a very strong, y=x like correlation between request service rate and performance.
We observe the same trend for various memory bound applications. Here are a couple of more examples.
Therefore, memory request service rate can be used as a proxy for performance.
Now, going back to the slowdown equation. We can replace performance by request service rate, based on our first observation, enabling us to express slowdown as the ratio of alone to shared request service rates.
Shared request service rate can be measured in a relatively straightforward manner when an application is run along with other applications.
Measuring alone request service rate, without actually running an application alone is harder. This is where our second observation comes into play.

## Slide 236: Key Observation 2
Request Service Rate Alone (RSRAlone) of an application can be estimated by giving the application highest priority in accessing memory
Highest priority  Little interference
(almost as if the application were run alone)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 237: Key Observation 2
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 238
Memory Interference-induced Slowdown Estimation (MISE) model for memory bound applications
Notes: Based on these two observations, our memory interference induced slowdown estimation (MISE) model for memory bound applications is as follows. Now, let’s analyze why this request service rate ratio based model holds for memory bound applications

## Slide 239: Key Observation 3
Memory-bound application
No interference
Compute Phase
Memory Phase
With interference
Memory phase slowdown dominates overall slowdown
time
time
Req
Req
Req
Req
Req
Req
Notes: A memory-bound application spends significant fraction of its execution time waiting for memory.
Let’s first look at the case when a memory-bound application is not receiving any interference.
The application does a small amount of compute at the core and then sends out a bunch of memory requests. The application cannot do any more compute until these requests are serviced.
Now, when this application experiences interference, the length of its compute phase does not change. However, the time taken to service the memory requests increases. In essence, since the application spends most of its time in the memory phase, the memory induced slowdown of the application dominates the overall slowdown of the application.

## Slide 240: Key Observation 3
Non-memory-bound application
time
time
No interference
Compute Phase
Memory Phase
With interference
Only memory fraction ( ) slows down with interference
Memory Interference-induced Slowdown Estimation (MISE) model for non-memory bound applications
Notes: However, this is not the case for a non-memory-bound application.
A non-memory-bound application spends a sizeable fraction of its time doing compute at the core and a smaller fraction of time waiting for memory. When the application experiences interference, the length of the compute phase does not change, whereas the memory phase slows down with interference.
Specifically, if alpha is the fraction of time the application spends in the memory phase, then 1 – alpha is the fraction of time it spends in the compute phase. The 1 – alpha fraction does not change with memory interference, however the alpha fraction slows down as the ratio of request service rate alone to request service rate shared.
We augment the MISE model to take this into account. Slowdown for non-memory-bound applications can be expressed as the sum of two quantities - 1 – alpha, the compute fraction that does not change with interference and the memory induced slowdown.

## Slide 241: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having discussed the key observations behind our MISE model, let me describe its implementation.

## Slide 242: Interval Based Operation
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
This repeats during every interval.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 243: Measuring RSRShared and α
Request Service Rate Shared (RSRShared)
  Per-core counter to track number of requests serviced
  At the end of each interval, measure
Memory Phase Fraction ( )
  Count number of stall cycles at the core
  Compute fraction of cycles stalled for memory
Notes: Shared request service rate can be measured using per-core counters to track the number of requests serviced during each interval.
At the end of the interval, SRSR can be computed as the number of requests serviced divided by the length of the interval.
Memory phase fraction of each application can be computed by counting the number of cycles the core stalls waiting for memory and then computing what fraction are these cycles of the interval length.
Measuring SRSR and alpha is the straightforward part. Now, for the more interesting part, estimating alone request service rate.

## Slide 244: Estimating Request Service Rate Alone (RSRAlone)
Divide each interval into shorter epochs
At the beginning of each epoch
  Memory controller randomly picks an application as the highest priority application
At the end of an interval, for each application, estimate
Goal: Estimate RSRAlone
How: Periodically give each application highest priority in accessing memory
Notes: Our goal is to estimate alone request service rate. To do this, we periodically give each application the highest priority in accessing memory, based on observation 2.
How exactly do we do this. First, each interval is divided into shorter epochs. At the beginning of each epoch, the memory controller picks one application at random and designates it the highest priority application. This way each application is given highest priority at different epochs during the interval.
At the end of the interval, ARSR is estimated for each application as the ratio of the number of requests of the application serviced during the high priority epochs to the number of cycles the application was given highest priority.
Now, is this an accurate way of estimating ARSR. It turns out not. We have been ignoring an inaccuracy all along.

## Slide 245: Inaccuracy in Estimating RSRAlone
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
When an application has highest priority
  Still experiences some interference
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
Time units
Service order
Main Memory
1
2
3
Interference Cycles
High Priority
Main Memory
Time units
Service order
Main Memory
1
2
3
Request Buffer
State
Notes: That is, even when an application has highest priority, it still experiences some interference from other applications.
Here is an example showing why.
The red application has highest priority and is run along with another application, the blue application. First, there is just one request in the request buffer and it is from the red application. Since this is the only request, it is scheduled by the memory controller and completes in one time unit.
While this request is being serviced, there comes another request from the blue application. Our memory controller is work conserving and schedules another application’s request, if there is no request from the red application. So, it schedules the blue application’s request next.
However, just as the blue application’s request is being scheduled comes another request from the red application. Ideally, we would like to pre-empt the blue application’s request. However, because of the way DRAM operates, preempting the blue application’s request incurs overhead. Therefore, the red application’s request would have to wait until the blue application’s request completes and only then is it serviced. These extra cycles that the red application spent waiting for the blue application’s request to complete are interference cycles that it would not have experienced had it been running alone.

## Slide 246: Accounting for Interference in RSRAlone Estimation
Solution: Determine and remove interference cycles from RSRAlone calculation
A cycle is an interference cycle if
  a request from the highest priority application is waiting in the request buffer and
  another application’s request was issued previously
Notes: The solution to account for this interference is to determine and remove such interference cycles from the ARSR computation.
How we do this is to subtract these cycles from the number of high priority epoch cycles.
Now, the question is how do we determine which cycles are interference cycles.
We deem a cycle an interference cycle if …. (read from slide)

## Slide 247: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having described the key observations behind our model and its implementation, we will put it all together

## Slide 248: MISE Model: Putting it All Together
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 249: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Now, having described the model and its implementation, let me present an evaluation of the model.

## Slide 250: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu+, MICRO ‘07]
  FST (Fairness via Source Throttling) [Ebrahimi+, ASPLOS ‘10]
  Per-thread Cycle Accounting [Du Bois+, HiPEAC ‘13]
Basic Idea:
Hard
Easy
Count number of cycles application receives interference
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 251: Two Major Advantages of MISE Over STFM
Advantage 1:
  STFM estimates alone performance while an application is receiving interference  Hard
  MISE estimates alone performance while giving an application the highest priority  Easier
Advantage 2:
  STFM does not take into account compute phase for non-memory-bound applications
  MISE accounts for compute phase  Better accuracy
Notes: Let me now present the two major advantages of MISE over STFM, qualitatively.
First, STFM estimates alone performance of an application while it is receiving interference. This is hard because of BLP effects.
MISE addresses this difficulty by giving an application highest priority and then estimating its alone performance.
Second, STFM does not take into account compute phase for non-mem-bound applications. MISE accounts for compute phase and hence achieves better accuracy.

## Slide 252: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1066 DRAM
  512 KB private cache/core
Workloads
  SPEC CPU2006
  300 multi programmed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 253: Quantitative Comparison
Chart: Million Cycles
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 2.7467 | 2.8146 | 2.981 | 2.6916 | 3.5156 | 2.4446 | 3.3601 | 3.2667 | 2.8783 | 2.9401 | 2.7229 | 2.9719 | 2.71 | 2.1736 | 2.0285 | 2.4098 | 2.0056 | 2.2585 | 2.1279 | 2.4625
STFM | 1.8517 | 1.9219 | 1.8786 | 1.8294 | 1.9487 | 1.8759 | 1.7936 | 1.7677 | 1.83 | 1.817 | 1.7232 | 1.7709 | 1.704 | 1.6746 | 1.6715 | 1.7352 | 1.6427 | 1.7084 | 1.6918 | 1.7477
MISE | 2.6655 | 2.8713 | 2.8244 | 2.6053 | 3.1741 | 2.6867 | 3.5471 | 3.4317 | 3.3 | 2.6747 | 2.8604 | 3.0821 | 2.8909 | 2.235 | 2.1161 | 2.3639 | 1.999 | 2.0667 | 2.1632 | 2.3161
SPEC CPU 2006 application
leslie3d
Notes: This graph shows the actual slowdown of leslie3d, a memory-bound application, with time (in million cycles).
Here are slowdown estimates from STFM and here are slowdown estimates from MISE. As can be seen, MISE’s slowdown estimates are much closer to the actual slowdowns. This is because MISE estimates leslie’s alone performance while giving it highest priority, whereas STFM tries to estimate it while leslie receives interference from other applications.

## Slide 254: Comparison to STFM
cactusADM
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.495 | 1.5295 | 1.6709 | 1.5475 | 1.6605 | 1.5731 | 1.9783 | 1.7095 | 1.5337 | 1.5256 | 1.4754 | 1.5235 | 1.5214 | 1.7913 | 1.6855 | 1.6301 | 1.5933 | 1.6732 | 1.5495 | 1.6973
STFM | 1.25 | 1.3555 | 1.3435 | 1.3721 | 1.3293 | 1.3149 | 1.2341 | 1.3128 | 1.3228 | 1.3579 | 1.3509 | 1.344 | 1.4008 | 1.3967 | 1.5397 | 1.5867 | 1.5517 | 1.5683 | 1.5638 | 1.3614
MISE | 1.5723 | 1.5685 | 1.6897 | 1.5829 | 1.73 | 1.6866 | 2.1706 | 1.8114 | 1.5947 | 1.5898 | 1.5347 | 1.5537 | 1.6001 | 1.8673 | 1.7348 | 1.6758 | 1.6313 | 1.7322 | 1.6362 | 1.7298
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.7536 | 1.697 | 1.8734 | 1.7248 | 1.9225 | 1.6413 | 1.9296 | 2.1339 | 2.0504 | 1.9754 | 1.8732 | 2.1705 | 2.0085 | 2.239 | 2.2425 | 2.2469 | 1.9042 | 2.3715 | 2.0927 | 2.5902
STFM | 1.3661 | 1.3843 | 1.3635 | 1.3908 | 1.3589 | 1.35 | 1.3746 | 1.5894 | 1.5811 | 1.5995 | 1.5987 | 1.5832 | 1.5771 | 2.0246 | 1.9878 | 1.9883 | 1.9797 | 1.9406 | 1.9709 | 1.9629
MISE | 1.8607 | 1.9645 | 1.9765 | 1.8835 | 2.5202 | 1.8326 | 2.2231 | 2.3347 | 2.178 | 2.097 | 2.1736 | 2.1054 | 2.0591 | 2.3181 | 2.2502 | 2.3946 | 2.1703 | 2.5387 | 2.2735 | 2.6647
GemsFDTD
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.9414 | 2.1412 | 2.406 | 2.0632 | 2.7223 | 2.6572 | 3.1068 | 3.1879 | 2.6035 | 2.4937 | 2.4704 | 2.8774 | 2.6478 | 2.6947 | 2.7804 | 2.9653 | 2.8228 | 2.5796 | 2.6027 | 2.7846
STFM | 1.5023 | 1.4705 | 1.8931 | 1.4971 | 1.6676 | 1.6306 | 1.8055 | 1.7004 | 1.5827 | 1.7021 | 1.7571 | 1.8054 | 1.974 | 2.2827 | 2.3098 | 2.107 | 1.6316 | 2.0168 | 2.0447 | 2.0375
MISE | 1.916 | 2.3469 | 2.5021 | 2.481 | 2.7434 | 2.413 | 3.2611 | 3.5557 | 2.6948 | 2.6542 | 3.0171 | 2.4489 | 2.5681 | 2.7574 | 3.1405 | 3.0343 | 2.527 | 2.8438 | 3.1033 | 3.2769
soplex
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0179 | 1.0228 | 1.5311 | 1.2016 | 1.0185 | 1.0121 | 1.0059 | 1.0071 | 1.1261 | 1.5714 | 1.0808 | 1.0167 | 1.0097 | 1.2303 | 1.0956 | 1.0308 | 1.0187 | 1.3242 | 1.3257 | 1.0134
STFM | 2.6564 | 2.8136 | 2.323 | 1.9913 | 2.1243 | 2.8472 | 2.9844 | 2.4594 | 2.5397 | 2.2388 | 3.0174 | 2.8437 | 3.3951 | 3.9402 | 2.5308 | 2.8686 | 3.3191 | 2.5052 | 2.3033 | 2.0445
MISE | 1.0005 | 1.0032 | 1.7563 | 1.0691 | 0.99707 | 1.0011 | 1.0016 | 0.99869 | 1.0593 | 1.3748 | 1.0555 | 1.0003 | 1.0006 | 1.0639 | 1.0105 | 0.98886 | 1.0009 | 0.9221 | 1.0907 | 1.0039
wrf
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0394 | 1.0432 | 1.0258 | 1.0358 | 1.031 | 1.0316 | 1.0304 | 1.0232 | 1.0226 | 1.0158 | 1.0543 | 1.0328 | 1.0751 | 1.0632 | 1.0517 | 1.053 | 1.029 | 1.0322 | 1.031 | 1.0246
STFM | 2.1276 | 2.0414 | 1.9127 | 1.8201 | 2.3708 | 1.9609 | 1.9559 | 2.062 | 2.2477 | 2.173 | 3.9673 | 2.3084 | 2.4138 | 2.5477 | 2.8093 | 2.6087 | 2.1795 | 1.9627 | 1.8871 | 2.0011
MISE | 1.0191 | 1.0068 | 1.0168 | 0.98223 | 1.031 | 0.96844 | 1.0017 | 1.0177 | 0.99417 | 1.0091 | 1.0383 | 1.0293 | 1.0276 | 1.0128 | 1.0242 | 1.0231 | 0.99687 | 1.0223 | 0.89507 | 1.0191
calculix
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0008 | 1.0011 | 1.0029 | 1.0014 | 1.0016 | 1.0015 | 1.0038 | 1.0016 | 1.0011 | 1.0034 | 1.0391 | 1.1297 | 1.0014 | 1.0018 | 1.0019 | 1.002 | 1.0012 | 1.0008 | 1.0011 | 1.0012
STFM | 2.5587 | 2.6401 | 2.5897 | 1.8924 | 2.9635 | 3.1523 | 2.659 | 2.2124 | 3.2205 | 2.9929 | 3.5898 | 2.7107 | 2.1336 | 3.0915 | 3.0289 | 3.0638 | 3.0873 | 2.3554 | 2.7464 | 2.2834
MISE | 1.0002 | 1.0002 | 1.0015 | 1.0003 | 1.0007 | 0.99984 | 1.0012 | 0.99949 | 0.99671 | 1.0015 | 0.99044 | 0.86466 | 1.0003 | 1.0004 | 1.0006 | 0.99474 | 0.99903 | 0.99882 | 1.0001 | 1.0004
povray
Average error of MISE: 8.2%
Average error of STFM: 29.4%
(across 300 workloads)
Notes: Several more applications. For most applications, MISE’s slowdown estimates are more accurate.
On average, MISE’s error is 8.2%, while STFM’s error is 29.4%, across our 300 workloads.

## Slide 255: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: I have described our MISE model to estimate application slowdowns. Now, once we have slowdown estimates from our model, we can leverage them to control slowdowns. Let me present our first mechanism to control slowdowns – providing soft slowdown guarantees.

## Slide 256: Providing “Soft” Slowdown Guarantees
Goal
  1. Ensure QoS-critical applications meet a prescribed slowdown bound
  2. Maximize system performance for other applications
Basic Idea
  Allocate just enough bandwidth to QoS-critical application
  Assign remaining bandwidth to other applications
Notes: The goal of this mechanism is to .. <read off slide>.
The basic idea is to allocate just enough bandwidth the QoS-critical application, while assigning the remaining bandwidth among the other applications.

## Slide 257: MISE-QoS: Mechanism to Provide Soft QoS
Assign an initial bandwidth allocation to QoS-critical application
Estimate slowdown of QoS-critical application using the MISE model
After every N intervals
  If slowdown > bound B +/- ε, increase bandwidth allocation
  If slowdown < bound B +/- ε, decrease bandwidth allocation
When slowdown bound not met for N intervals
  Notify the OS so it can migrate/de-schedule jobs
Notes: SLIDE NEEDS WORK

## Slide 258: Methodology
Each application (25 applications in total) considered the QoS-critical application
Run with 12 sets of co-runners of different memory intensities
Total of 300 multi programmed workloads
Each workload run with 10 slowdown bound values
Baseline memory scheduling mechanism
  Always prioritize QoS-critical application
  [Iyer+, SIGMETRICS 2007]
  Other applications’ requests scheduled in FRFCFS order
  [Zuravleff +, US Patent 1997, Rixner+, ISCA 2000]
Notes: Read off slide

## Slide 259: A Look at One Workload
Chart: Slowdown
| leslie3d | hmmer | lbm | omnetpp
AlwaysPrioritize | 1.9301 | 2.511 | 2.8159 | 2.7346
MISE-QoS-10/1 | 2.8374 | 2.2769 | 2.0523 | 2.0142
MISE-QoS-10/3 | 2.6976 | 2.3196 | 2.1221 | 2.084
MISE-QoS-10/5 | 2.0128 | 2.5056 | 2.6593 | 2.5534
MISE-QoS-10/7 | 1.9063 | 2.508 | 2.8014 | 2.6609
MISE-QoS-10/9 | 1.9063 | 2.508 | 2.8014 | 2.6609
QoS-critical
non-QoS-critical
MISE is effective in
meeting the slowdown bound for the QoS-critical application
improving performance of non-QoS-critical applications
Slowdown Bound = 10
Slowdown Bound = 3.33
Slowdown Bound = 2

## Slide 260: Effectiveness of MISE in Enforcing QoS
 | Predicted Met | Predicted Not Met
QoS Bound Met | 78.8% | 2.1%
QoS Bound Not Met | 2.2% | 16.9%
Across 3000 data points
MISE-QoS meets the bound for 80.9% of workloads
AlwaysPrioritize meets the bound for 83% of workloads
MISE-QoS correctly predicts whether or not the bound is met for 95.7% of workloads

## Slide 261: Performance of Non-QoS-Critical Applications
Chart: Number of Memory Intensive Applications
| 0 | 1 | 2 | 3 | Avg
AlwaysPrioritize | 1.2932 | 0.92684 | 0.63783 | 0.47247 | 0.83259
MISE-QoS-10/1 | 1.3105 | 1.0515 | 0.75708 | 0.556 | 0.91875
MISE-QoS-10/3 | 1.3105 | 1.0471 | 0.75276 | 0.54982 | 0.91504
MISE-QoS-10/5 | 1.3104 | 1.0268 | 0.71476 | 0.51722 | 0.89229
MISE-QoS-10/7 | 1.3101 | 0.96233 | 0.65406 | 0.47556 | 0.85051
MISE-QoS-10/9 | 1.2966 | 0.92898 | 0.64287 | 0.47149 | 0.83499
Higher performance when bound is loose
When slowdown bound is 10/3
MISE-QoS improves system performance by 10%

## Slide 262: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown

## Slide 263: Other Results in the Paper
Sensitivity to model parameters
  Robust across different values of model parameters
Comparison of STFM and MISE models in enforcing soft slowdown guarantees
  MISE significantly more effective in enforcing guarantees
Minimizing maximum slowdown
  MISE improves fairness across several system configurations
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.

## Slide 264: Summary
Uncontrolled memory interference slows down applications unpredictably
Goal: Estimate and control slowdowns
Key contribution
  MISE: An accurate slowdown estimation model
  Average error of MISE: 8.2%
Key Idea
  Request Service Rate is a proxy for performance
  Request Service Rate Alone estimated by giving an application highest priority in accessing memory
Leverage slowdown estimates to control slowdowns
  Providing soft slowdown guarantees
  Minimizing maximum slowdown

## Slide 265: Efficient Cache Utilization

## Slide 266: More Efficient Cache Utilization
Compressing redundant data
  Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)
  Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Low-Complexity, Low-Latency Main Memory Compression Framework" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. Slides (pptx) (pdf) Lightning Session Slides (pptx) (pdf)
Reducing pollution and thrashing
  Vivek Seshadri, Onur Mutlu, Michael A. Kozuch, and Todd C. Mowry, "The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 267: Evicted Address Filter: Executive Summary
Two problems degrade cache performance
  Pollution and thrashing
  Prior works don’t address both problems concurrently
Goal: A mechanism to address both problems
EAF-Cache
  Keep track of recently evicted block addresses in EAF
  Insert low reuse with low priority to mitigate pollution
  Clear EAF periodically to mitigate thrashing
  Low complexity implementation using Bloom filter
EAF-Cache outperforms five prior approaches that address pollution or thrashing
Seshadri et al., “The Evicted Address Filter,” PACT 2012.
Notes: …

## Slide 268: EAF-Cache: Final Design
Cache
Bloom Filter
Counter
1
2
3
Cache eviction
Cache miss
Counter reaches max
Insert address into filter
Increment counter
Test if address is present in filter
Yes, insert at MRU. No, insert with BIP
Clear filter and counter
Notes: Lets take a look at the final design of our mechanism, the EAF-cache.
It augments the cache with a Bloom filter and a counter that keeps track of the number of addresses inserted into the Bloom filter.
On a cache eviction, the evicted address is inserted into the filter and the counter is incremented.
On a cache miss, if the missed block address is present in the Bloom filter, the block is inserted at the MRU position. Otherwise it is inserted with the bimodal insertion policy.
Finally, when the counter reaches a maximum, both the filter and the counter are cleared.

## Slide 269: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash
[Cai+, DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014]

## Slide 270: Another Talk: NAND Flash Scaling Challenges
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Tech Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.

## Slide 271: Error Management in MLC NAND Flash
Problem: MLC NAND flash memory reliability/endurance is a key challenge for satisfying future storage systems’ requirements
Our Goals: (1) Build reliable error models for NAND flash memory via experimental characterization, (2) Develop efficient techniques to improve reliability and endurance
This talk provides a “flash” summary of our recent results published in the past 3 years:
  Experimental error and threshold voltage characterization [DATE’12&13]
  Retention-aware error management [ICCD’12]
  Program interference analysis and read reference V prediction [ICCD’13]
  Neighbor-assisted error correction [SIGMETRICS’14]

## Slide 272: Tolerating DRAM: Example Techniques
Retention-Aware DRAM Refresh: Reducing Refresh Impact
Refresh Access Parallelization: Reducing Refresh Impact
Tiered-Latency DRAM: Reducing DRAM Latency
RowClone: Accelerating Page Copy and Initialization
Subarray-Level Parallelism: Reducing Bank Conflict Impact
Base-Delta-Immediate Compression and Linearly Compressed Pages: Efficient Cache & Memory Compression

## Slide 273: SALP: Reducing DRAM Bank Conflicts
Problem: Bank conflicts are costly for performance and energy
  serialized requests, wasted energy (thrashing of row buffer, busy wait)
Goal: Reduce bank conflicts without adding more banks (low cost)
Key idea: Exploit the internal subarray structure of a DRAM bank to parallelize bank conflicts to different subarrays
  Slightly modify DRAM bank to reduce subarray-level hardware sharing
Results on Server, Stream/Random, SPEC
  19% reduction in dynamic DRAM energy
  13% improvement in row hit rate
  17% performance improvement
  0.15% DRAM area overhead
Kim, Seshadri+ “A Case for Exploiting Subarray-Level
Parallelism in DRAM,” ISCA 2012.
Chart: Normalized Dynamic Energy
| gmean
Baseline | 1
MASA | 0.81324
-19%
Chart: Row-Buffer Hit-Rate
| gmean
Baseline | 0.56896
MASA | 0.69801
+13%

## Slide 274: More on SALP
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, and Onur Mutlu, "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 275: Tolerating DRAM: Example Techniques
Retention-Aware DRAM Refresh: Reducing Refresh Impact
Refresh Access Parallelization: Reducing Refresh Impact
Tiered-Latency DRAM: Reducing DRAM Latency
RowClone: Accelerating Page Copy and Initialization
Subarray-Level Parallelism: Reducing Bank Conflict Impact
Base-Delta-Immediate Compression and Linearly Compressed Pages: Efficient Cache & Memory Compression

## Slide 276: More Efficient Cache/Memory Utilization
Compressing redundant data
  Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)
  Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Low-Complexity, Low-Latency Main Memory Compression Framework" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. Slides (pptx) (pdf) Lightning Session Slides (pptx) (pdf)
Reducing pollution and thrashing
  Vivek Seshadri, Onur Mutlu, Michael A. Kozuch, and Todd C. Mowry, "The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 277: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves

## Slide 278: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio

## Slide 279: Can We Do Better?
Uncompressible cache line (with a single base):
Key idea:
Use more bases, e.g., two instead of one
Pro:
  More cache lines can be compressed
Cons:
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…

## Slide 280: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
Advantages over 2 arbitrary bases:
  Better compression ratio
  Simpler compression logic
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 281: Compression Ratio
BΔI achieves the highest compression ratio
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
ZCA | 1 | 1.0125 | 1.0002 | 1.0055 | 1.0288 | 1 | 1.1561 | 1.0914 | 1.0241 | 1 | 1.0005 | 1.1898 | 1 | 1.1083 | 1.0549 | 1 | 1.0013 | 1.2794 | 1.9738 | 1.5235 | 1.5406 | 1.801 | 1.9951 | 1.9966 | 1.2005
FVC | 1.0297 | 1.0125 | 1.0012 | 1.017 | 1.1457 | 1.4988 | 1.1857 | 1.1438 | 1.4157 | 1.3573 | 1.0143 | 1.4596 | 1.3574 | 1.3745 | 1.1968 | 1.3874 | 1.9381 | 1.7894 | 1.9738 | 1.9859 | 1.9598 | 1.9947 | 1.995 | 1.9966 | 1.4212
FPC | 1.004 | 1.0125 | 1.0225 | 1.0568 | 1.2307 | 1.3121 | 1.1774 | 1.4064 | 1.4705 | 1.5235 | 1.5442 | 1.5994 | 1.5763 | 1.7269 | 1.2651 | 1.6749 | 1.9072 | 1.9167 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5149
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
1.53

## Slide 282: Performance
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 1.0859 | 1.1498 | 1.1819 | 1.2753 | 1.3788
BΔI | 1.0817 | 1.1425 | 1.2085 | 1.2401 | 1.346 | 1.4285
8.1%
5.2%
5.1%
4.9%
5.6%
3.6%
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 0.819 | 0.59143 | 0.46593 | 0.37544 | 0.27527
BΔI | 0.84292 | 0.62368 | 0.466 | 0.40552 | 0.30364 | 0.23666
16%
24%
21%
13%
19%
14%
BΔI achieves the performance of a 2X-size cache
Performance improves due to the decrease in MPKI

## Slide 283: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 284: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 285: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 287: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 288: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a huge (DRAM) cache at low cost?
Two solutions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 289: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 290: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Yoon et al., “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 291: Row-Locality-Aware Data Placement: Results
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
17%
Memory energy-efficiency and fairness also improve correspondingly

## Slide 292: Transparent Hybrid Non-Volatile Memory
Problem: How do you provide consistency and prevent data corruption in NVM upon a system crash?
Goal: Provide efficient programmer-transparent consistency in hybrid NVM
  Efficiency: use hybrid DRAM/NVM for high performance
    DRAM is not (only) a transparent cache
  Transparency: no library APIs or explicit interfaces to access NVM; just loads and stores
    Makes life easier for the programmer
    Easier to support legacy code and hypervisors
Challenges to Solve
  How to guarantee consistency
  How to maximize performance

## Slide 293: THNVM: Solution Overview
Idea 1: Transparent checkpointing
  Need to overlap checkpointing and execution
Idea 2: Differentiated consistency schemes for DRAM and NVM
  Writeback: buffer sequential writes in DRAM
  Address Remapping: handle random writes in NVM
Idea 3: Dynamic migration of data for performance
  High write-locality data placed in DRAM
Running
Checkpoint’g
Running
Checkpoint’g
Epoch 0
Epoch 1
time
Epoch 0
Epoch 1
time

## Slide 294: Memory Systems Research Center @ CMU

## Slide 295: What?
Industry-supported research center to solve industry-wide problems in memory systems
Focusing on cross layer software/hardware research in memory from devices to applications: new functions, new interfaces, new organizations, new uses, new technologies, …
Mission is to
  Research memory systems of the next decade
  Provide solutions to industry-wide problems
  Enable adoption of ideas, interfaces, and methodologies via a neutral, collaborative forum
  Provide a source of professionals trained well in memory
  Enable many other unforeseen benefits
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 296: Why?
Problems are industry-wide and difficult
Many solutions require cross-layer cooperation and/or out-of-the-box thinking
Adoption of new ideas difficult but seems necessary
  New interfaces
  New functions, execution models
  New use cases
  …
We may miss disruptive opportunities without a concerted and unique effort in memory

## Slide 297: Key Mission
Perform the fundamental research needed to manage and design the memory systems within the decade and going forward
All aspects of memory systems will be considered in the center, from software to hardware, based upon feedback from supporting industrial partners.

## Slide 298: What I Expect the Center Looks Like
Sits in-between PDL and DSSC
  PDL: Parallel Data Laboratory (software storage and data focus)
  Memory Center: Memory Architecture, Systems, Circuits, …
  DSSC: Data Storage Systems Center (storage device focus)
Focused on everthing related to (main) memory, including memory+computation, new functions, new interfaces, new organizations, new uses, new technologies, …
Cross-layer with architecture at “center”
Sustained by gifts from funding companies and institutions
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 299: Potential Benefits/Hopes of Such a Center
Enables a good way to influence/steer research on all aspects of memory systems
  Annual retreats and visit days
  More fine-grained discussions with professors and students
Enables a neutral forum for information exchange and discussion between participants
Enables close interaction with faculty and students who are focusing on memory, early access to research ideas/results
Enables a source of professionals who are well-trained in memory (and across the system stack)
Enhances the probability of adoption of disruptive ideas

## Slide 300: Research Topics in the Center
DRAM
NVM: emerging tecnologies
Flash
New memory interfaces and architectures
Memory scaling issues
In-memory computation
Memory management
Hybrid memory systems
…

## Slide 301: More Information
Memory center description document
PDL model