## Slide 1: Hermes & Sibyl: ML-Driven Memory & Storage Management
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
27 September 2023
VMware

## Slide 2: Data-Driven (Self-Optimizing) Architectures

## Slide 3: System Architecture Design Today
Human-driven
  Humans design the policies (how to do things)
Many (too) simple, short-sighted policies all over the system
No automatic data-driven policy learning
(Almost) no learning: cannot take lessons from past actions
Can we design
fundamentally intelligent architectures?

## Slide 4: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
We need to rethink design
(of all controllers)

## Slide 5: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008. Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 6: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version] Officially artifact evaluated as available, reusable and reproducible.
https://arxiv.org/pdf/2109.12021.pdf

## Slide 7: Learning-Based Off-Chip Load Predictors
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 8: Self-Optimizing Hybrid SSD Controllers
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 9: Hermes: Perceptron-Based Off-Chip Load Prediction

## Slide 10: Learning-Based Off-Chip Load Predictors
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 11: Hermes Talk Video
https://www.youtube.com/watch?v=PWWBtrL60dQ&t=3609s

## Slide 12
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran,
David Novo, Ataberk Olgun, Mohammad Sadrosadati, Onur Mutlu
Accelerating Long-Latency Load Requests
via Perceptron-Based Off-Chip Load Prediction
https://github.com/CMU-SAFARI/Hermes
https://arxiv.org/pdf/2209.00188.pdf

## Slide 13: The Key Problem
Long-latency off-chip load requests
Often stall processor by
blocking instruction retirement from
Reorder Buffer (ROB)
Limit performance
Notes: The key problem that we are trying to address in this work is stemming from Off-chip load request
[CLICK] As we know, these off-chip load requests often stall…,
[CLICK] which severely limits the performance of a core.

## Slide 14: Traditional Solutions
Employ sophisticated prefetchers
1
Increase size of on-chip caches
2
Notes: Architects have primarily relied on two key techniques to reduce latency of such loads:
[CLICK] By employing sophisticated data prefetchers
[CLICK] And Increasing size of the on-chip cache hierarchy

## Slide 15: Key Observation 1
Chart: 
| uncovered | covered by prefetcher
 | 0.49685 | 0.50315
50%
successfully prefetched
# off-chip loads without any prefetcher
50%
still go off-chip even with
a state-of-the-art prefetcher
70% of the off-chip loads
block the ROB
Many loads still go off-chip
Notes: In this work, we show that prior prefetchers successfully prefetch a significant fraction of the off-chip load requests.
[CLICK] However, nearly 50% of the off-chip loads in a system without any prefetcher are still going off-chip even in presence of a state-of-the-art prefetcher
[CLICK] And 70% of these off-chip loads even block the ROB.

## Slide 16: Key Observation 2
40% of the stalls can be eliminated by removing
on-chip cache access latency from critical path
On-chip cache access latency
significantly contributes to off-chip load latency
L1
L2
LLC
Main Memory
Saved cycles
Chart: 
| uncovered | covered by prefetcher
 | 0.49685 | 0.50315
50% still go off-chip
L1
L2
LLC
Main Memory
Notes: Now, if we focus on the off-chip loads that are still going to the main memory even in presence of a state-of-the-art prefetcher,
We observe that the on-chip cache access latency…
[CLICK] We show that nearly 40% of …

## Slide 17: Caches are Getting Bigger and Slower…
Hardavellas+, “Database Servers on Chip Multiprocessors: Limitations and Opportunities”, CIDR, 2007
On-chip Cache Size (KB)
Chart: L2 Size (KB)
| Skylake (2015) | Sunny Cove (2019) | Willow Cove (2020) | Golden Cove P-core (2021) | Raptor Lake P-core (2022)
Size | 256 | 512 | 1280 | 1280 | 2048
Chart: L2 Latency (processor cycles)
| Skylake (2015) | Sunny Cove (2019) | Willow Cove (2020) | Golden Cove P-core (2021) | Raptor Lake P-core (2022)
Latency | 12 | 13 | 14 | 15 | 16
Notes: As the cache hierarchy continue to grow in size and complexity, as noted by previous works,
As well as a trend that we see in recent processors,
This problem is only going to get exacerbated even more in future generation processors

## Slide 18: Our Goal
Improve processor performance
by removing on-chip cache access latency
from the critical path of off-chip loads
Notes: Thus to alleviate this problem, the goal of our work is to improve…

## Slide 19
Predicts which load requests
are likely to go off-chip
Starts fetching data directly from main memory while concurrently accessing the cache hierarchy
Notes: Towards this we propose Hermes, which is based on two key ideas.
[CLICK] Hermes predicts which…
[CLICK] Hermes starts fetching …

## Slide 20: Key Contribution
Hermes employs the first
perceptron-based off-chip load predictor
That predicts which loads are likely to go off-chip
By learning from
multiple program context information
Notes: To enable accurate off-chip prediction,
Hermes employs the first perceptron-based off-chip load predictor
[CLICK] that identifies loads …
[CLICK] by only learning from multiple…

## Slide 21: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
Baseline
Processor is stalled
Latency tolerance limit of ROB
Notes: Now let me give you a brief overview of Hermes.
This is how a traditional cache hierarchy looks like in today’s processor.
[CLICK] And this is how the memory latency timeline looks like for an off-chip load in the baseline system
[CLICK] If the ROB has a latency tolerance limit up till here, the processor stalls for the remaining cycles

## Slide 22: Hermes Overview
Core
L1-D
L2
LLC
MC
Off-Chip
Main Memory
L1
L2
LLC
Main Memory
POPET
L1
L2
LLC
Main Memory
Baseline
Hermes
Saved stall cycles
Processor is stalled
Latency tolerance limit of ROB
Predict
Issue a Hermes request
Wait
Train
Perceptron-based
off-chip load predictor
Notes: Now Hermes employs an off-chip predictor named POPET.
[CLICK] For every load generated in the core, Hermes consults POPET to predict whether this load would go off-chip or not
[CLICK] If the load is predicted to go off-chip, Hermes waits for the address translation to finish, which happens in parallel with L1 cache access
[CLICK] And then issues a speculative memory request, which we call a Hermes request,
directly to the main memory controller to start fetching the data from the main memory,
While also concurrently accessing the cache hierarchy for such a load.
[CLICK] If the off-chip prediction is correct, the load would eventually miss the LLC and arrive at the memory controller
Where it will simply wait for the ongoing Hermes request to finish, thus hiding the entire cache access latency from its critical path.
Once the data returns from the main memory, Hermes returns the data to the core [CLICK],
Thus, saving the precious stall cycles induced by the off-chip load [CLICK], which in turn provides performance benefit.
[CLICK] Hermes trains POPET when the data finally returns to the core, closing the feedback loop.

## Slide 23: Designing the Off-Chip Load Predictor
Tracking cache contents
Learning from program behavior
  Large metadata
  Metadata size increases with cache hierarchy size
  May need to track all cache operations
  Gets complex depending on the cache hierarchy configuration (e.g., inclusivity, bypassing,…)
  Correlate different program features with off-chip loads
MissMap [Loh+, MICRO’11] for the DRAM cache,
D2D [Sembrant+, ISCA’14], D2M [Sembrant+, HPCA’17], LP [Jalili+, HPCA’22] for the cache hierarchy
History-based prediction
HMP [Yoaz+, ISCA’99] for the L1-D cache
Using branch-predictor-like hybrid predictor:
Global, Gshare, and GSkew
Low storage overhead
Low design complexity
POPET provides
both higher accuracy and higher performance
than predictors inspired from these previous works
Notes: Now let’s discuss how to design this off-chip predictor.
So, there are multiple prior works that can be used either directly or with small modifications for off-chip load prediction.
These works can be broadly categorized into two classes.
[CLICK] History-based predictor introduced by HMP, uses a branch-predictor like hybrid predictor design
to identify which requests are going to miss L1 cache.
We can easily extend HMP’s design to predict loads that are going to miss the entire cache hierarchy.
[CLICK] Tracking-based methods, on the other hand, explicitly track cache contents
to predict which load requests are going to miss the cache hierarchy.
[CLICK] These tracking-based methods poses two key challenges…
[CLICK] First,…
[CLICK] Second,…
[CLICK] POPET takes a completely different approach to predict off-chip load requests by learning from program behavior.
[CLICK] It aims to correlate multiple different types of program features with off-chip load requests
to provide accurate predictions with much lower storage overhead and design complexity.
[CLICK] In our paper, we compare POPET against predictors inspired from these prior works and show that
[CLICK] POPET provides both higher accuracy and performance than them.

## Slide 24: POPET: Perceptron-Based Off-Chip Predictor
Multi-feature hashed perceptron model[1]
  Each feature has its own weight table
    Stores correlation between feature value and off-chip prediction
[1] D. Tarjan and K. Skadron, “Merging Path and Gshare Indexing in Perceptron Branch Prediction,” TACO, 2005
Notes: Now let’s deep dive into our off-chip predictor design.
Our predictor, named as POPET, is designed using hashed-perceptron model.
[CLICK] where each feature has its own weight table
That stores the correlation between feature value and the off-chip prediction

## Slide 25: Predicting using POPET
Uses simple table lookups, addition, and comparison
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Extract features from the load request
Notes: Hermes predicts using POPET using simple operations like table lookup, addition, and comparison.
Let me give you an example on how POPET’s prediction works.
POPET’s prediction works in three stages.
[CLICK] In the first stage, POPET extracts the features from the load request
[CLICK] In the second stage, each feature value is hashed and used as an index to retrieve the weights from each individual weight tables
[CLICK] In the third stage, the retrieved weights are accumulated and the cumulative weight is used to compute the activation function.
[CLICK] If the cumulative weight is higher than the activation threshold, POPET predicts that the load would go off-chip.

## Slide 26: Training POPET
Uses simple increment or decrement of feature weights
0x7ffe0+12
42
-4
12
3
3 >= -2
-5
Predict that the load would go off-chip
Shouldn’t be activated
Cumulative weight < 𝜏act
-1
-1
-1
Notes: Now let’s understand how to train POPET.
For this let’s assume the previous example where the load is predicted to go off-chip.
[CLICK] But in reality, the load didn’t go off-chip
[CLICK] this means the activation which have triggered before, shouldn’t have triggered
Which means, the cumulative weight should be lower than the activation threshold
[CLICK] Now to adjust the feature weights, POPET again indexes each weight table using the hashed feature values
[CLICK] And simply decrement each weight from the individual weight tables.
Thus, by using simple increment and decrement operations, POPET continuously learns from program behavior to accurately predict off-chip loads.

## Slide 27: Features Used in Hermes

## Slide 28: Evaluation
Notes: Now let’s evaluate Hermes.

## Slide 29: Simulation Methodology
ChampSim trace driven simulator
110 single-core memory-intensive traces
  SPEC CPU 2006 and 2017
  PARSEC 2.1
  Ligra
  Real-world applications
220 eight-core memory-intensive trace mixes
Off-Chip Predictors
LLC Prefetchers
History-based: HMP [Yoaz+, ISCA’99]
Tracking-based: Address Tag-Tracking based Predictor (TTP)
Ideal Off-chip Predictor
Pythia [Bera+, MICRO’21]
Bingo [Bakshalipour+, HPCA’19]
MLOP [Shakerinava+, 3rd Prefetching Championship’19]
SPP + Perceptron filter [Bhatia+, ISCA’20]
SMS [Somogyi+, ISCA’06]
Notes: We evaluate Hermes using ChampSim simulator,
[CLICK] using a wide range of memory-intensive traces spanning across SPEC CPU, PARSEC, Ligra, and real-world applications
[CLICK] We compare Hermes with five LLC prefetchers
[CLICK] and two off-chip predictors extended from prior works

## Slide 30: Latency Configuration
Cache round-trip latency
  L1-D: 5 cycles
  L2: 15 cycles
  LLC: 55 cycles
Hermes request issue latency (incurred after address translation)
Depends on
  Interconnect between POPET and MC
0 cycles
24 cycles
6 cycles
Notes: For our evaluation, we consider
[CLICK] a 5 cycle L1-D
[CLICK] 15 cycle L2
[CLICK] and 55 cycle LLC round-trip latency.
[CLICK] The latency for Hermes to issue a request directly to the main memory controller (after the address translation) depends on …
[CLICK] For this reason we sweep this latency from 0-cycles to 24-cycles in our paper.
[CLICK] But in this presentation, I am going to show you results considering a 6-cycle latency.

## Slide 31: Single-Core Performance Improvement
Chart: Geomean speedup over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | GEOMEAN
Hermes | 1.0966 | 1.1185 | 1.1061 | 1.1108 | 1.1309 | 1.115
Pythia | 1.2123 | 1.2715 | 1.0568 | 1.1992 | 1.2108 | 1.2034
Pythia + Hermes | 1.2628 | 1.3007 | 1.1279 | 1.2388 | 1.2854 | 1.2574
Pythia + Ideal Hermes | 1.292 | 1.3305 | 1.1417 | 1.261 | 1.3239 | 1.2863
11.5%
20.3%
5.4%
Hermes alone provides nearly
50% performance benefits of Pythia with only 1/5th storage overhead
Hermes on top of Pythia
outperforms Pythia alone in every workload category
Hermes provides nearly 90% performance benefit of Ideal Hermes that has an ideal off-chip load predictor
Notes: Let’s first analyze the single-core performance improvement.
[CLICK] This is how Hermes and a state-of-the-art prefetcher Pythia improves performance on top of a no-prefetching system.
[CLICK] The first takeaway is that Hermes alone provides nearly 50%...
[CLICK] Now if we combine Hermes with Pythia, that provides an additional 5.4% performance improvement on top of a strong baseline that has Pythia.
[CLICK] And finally, if we compare Hermes’s performance benefit with the Ideal Hermes that has an ideal off-chip predictor,
We see that Hermes provides nearly 90% performance benefit of the Ideal Hermes

## Slide 32: Increase in Main Memory Requests
Chart: % increase in main memory requests over the No-prefetching system
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Hermes | 0.056805 | 0.029895 | 0.27038 | 0.072653 | 0.062029 | 0.055441
Pythia | 0.41862 | 0.2408 | 0.48617 | 0.37302 | 0.52323 | 0.38512
Pythia + Hermes | 0.47511 | 0.27921 | 0.65693 | 0.41847 | 0.60518 | 0.44428
5.5%
38.5%
5.9%
11.5%
20.3%
5.4%
For every 1% performance benefit,
increase in main memory requests
Pythia
Hermes on top of Pythia
Hermes alone
2%
1%
0.5%
Hermes is more bandwidth-efficient
than even an efficient prefetcher like Pythia
Notes: This performance improvement comes at a cost of increase in main memory requests.
This graph shows the increase in the main memory request over the no-prefetching system provided by the three configurations.
[CLICK] As we can see, Hermes increases the main memory requests by 5.5% on average on top of the no-prefetching system..
Whereas Pythia increases …
If we combine two together, then it increases the main memory request by an additional 5.9%.
[CLICK] Now, if we compare this increase in the main memory request with the performance improvement each of these configurations are providing,
We see that
[CLICK] For every 1% performance benefit, Pythia …
[CLICK] This basically shows that Hermes is much more bandwidth efficient than a traditional data prefetcher like Pythia.
And for this reason [NEXT]

## Slide 33: Performance with Varying Memory Bandwidth
Chart: Main Memory Bandwidth (in MT/s)
| 200 | 400 | 800 | 1600 | 3200 | 6400 | 12800
Pythia | 0.90608 | 1.0297 | 1.1215 | 1.1842 | 1.2034 | 1.2051 | 1.2044
Hermes | 0.99513 | 1.0581 | 1.0896 | 1.1085 | 1.115 | 1.1174 | 1.1168
Pythia+Hermes | 0.96845 | 1.0682 | 1.1608 | 1.2325 | 1.2574 | 1.2593 | 1.2583
~AMD Threadripper 3990x (Zen 2, 64C/4ch, 2020)
~AMD EPYC Rome 7702P (Zen 2, 64C/8ch, 2019)
~Intel Xeon 6258R
(Cascade Lake, 28C/6ch, 2020)
Pythia
Hermes
Pythia+Hermes
In bandwidth-constrained configurations,
Hermes alone outperforms Pythia
Hermes+Pythia outperforms Pythia
across all bandwidth configurations
Baseline
Notes: If we evaluate Pythia and Hermes over a wide range of memory bandwidth configurations, we see that,
[CLICK] In these extremely-bandwidth constrained configurations, which are in fact roughly modeling per-core main memory bandwidth of commercial processors,
Hermes even outperforms Pythia.
[CLICK] And if we combine both of them, the combination of Hermes and Pythia outperforms Pythia in every bandwidth configurations.

## Slide 34: Performance with Varying Baseline Prefetcher
Chart: Geomean speedup over the No-prefetching system
| Pythia | Bingo | SPP | MLOP | SMS
Prefetcher-only | 1.2034 | 1.1937 | 1.1443 | 1.1347 | 1.0568
Prefetcher + Hermes | 1.2574 | 1.2554 | 1.1948 | 1.2104 | 1.1342
5.4%
6.2%
5.1%
7.6%
7.7%
Hermes consistently improves performance
on top of a wide range of baseline prefetchers
Notes: And these observations are not only true for Pythia.
We evaluate Hermes combined with multiple prior baseline state-of-the-art prefetchers and find that
Hermes consistently improves performance on top of a wide range of baseline prefetchers.

## Slide 35: Overhead of Hermes
4 KB storage overhead
1.5% power overhead*
*On top of an Intel Alder Lake-like performance-core [2] configuration
[2] https://www.anandtech.com/show/16881/a-deep-dive-into-intels-alder-lake-microarchitectures/3
Notes: All of these performance benefit comes at a
[CLICK] modest 4KB storage overhead per core and
[CLICK] 1.5% power overhead on top an Intel Alder Lake-like performance-core configuration

## Slide 36: More in the Paper
Performance sensitivity to:
  Cache hierarchy access latency
  Hermes request issue latency
  Activation threshold
  ROB size (in extended version on arXiv)
  LLC size (in extended version on arXiv)
Accuracy, coverage, and performance analysis against HMP and TTP
Understanding usefulness of each program feature
Effect on stall cycle reduction
Performance analysis on an eight-core system
Notes: We have many more evaluation results:
For example, a wide range of performance sensitivity study by varying…in the paper.

## Slide 37: More in the Paper
Performance sensitivity to:
  Cache hierarchy access latency
  Hermes request issue latency
  Activation threshold
  ROB size (in extended version at arXiv)
  LLC size (in extended version at arXiv)
Accuracy, coverage, and performance analysis against HMP and TTP
Understanding usefulness of each program feature
Effect on stall cycle reduction
Performance analysis in eight-core system
https://arxiv.org/pdf/2209.00188.pdf
Notes: We have many more evaluation results:
For example, a wide range of performance sensitivity study by varying…in the paper.

## Slide 38: To Summarize…
Notes: Thus to summarize…

## Slide 39: Summary
Hermes advocates for off-chip load prediction,
a different form of speculation than
load address prediction employed by prefetchers
Off-chip load prediction can be applied by itself
or combined with load address prediction
to provide performance improvement
Notes: Hermes advocates …
[CLICK] We show that off-chip load prediction…

## Slide 40: Summary
Hermes employs the first
perceptron-based off-chip load predictor
High coverage
(74%)
High accuracy
(77%)
Low storage overhead
(4KB/core)
High performance improvement over best prior baseline
(5.4%)
High performance
per bandwidth

## Slide 41: Hermes is Open Sourced
https://github.com/CMU-SAFARI/Hermes
All workload traces
13 prefetchers
9 off-chip predictors
Notes: That’s why we open-source our artifact.
It can be freely downloaded from our GitHub repository.
In this artifact, [CLICK] you will get all the workload traces we have used to evaluate Hermes,
[CLICK] 13 types of data prefetchers proposed in the past and
[CLICK] 9 types of off-chip predictors out of the box

## Slide 42: Easy To Define Your Own Off-Chip Predictor
Just extend the OffchipPredBase class
Notes: But if you want to impalement your own off-chip predictor, that’s also very easy.
All you have to do is to extend the OffchipPred base class…

## Slide 43: Easy To Define Your Own Off-Chip Predictor
Define your own train() and predict() functions
Get statistics like accuracy (stat name precision) and coverage (stat name recall) out of the box
Notes: And define your own train() and predict() functions
[CLICK] the infrastructure will automatically provide statistics like precision and recall out of the box

## Slide 44: Off-Chip Prediction Can Further Enable…
Prioritizing loads that are likely go off-chip
in cache queues and on-chip network routing
Better instruction scheduling
of data-dependent instructions
Other ideas to improve performance and fairness in multi-core system design...
Notes: We hope that high-accuracy off-chip prediction can further enable a multitude of optimization possibilities, for example:
[CLICK] prioritizing loads … to improve performance and fairness in extreme core processors
[CLICK] better instruction scheduling for data dependent loads
[CLICK] and many more…

## Slide 45
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran,
David Novo, Ataberk Olgun, Mohammad Sadrosadati, Onur Mutlu
Accelerating Long-Latency Load Requests
via Perceptron-Based Off-Chip Load Prediction
https://github.com/CMU-SAFARI/Hermes
https://arxiv.org/pdf/2209.00188.pdf
Notes: With that hope, I will conclude my talk.
I will be very happy to take any question from the audience.

## Slide 46: Hermes Discussion
FAQs
  What are the selected set of program features?
  Can you provide some intuition on why these features work?
  What happens in case of a misprediction?
  What’s the performance headroom for off-chip prediction?
  Do you see a variance of different features in final prediction accuracy?
Simulation Methodology
  System parameters
  Evaluated workloads
More Results
  Percentage of off-chip requests
  Reduction in stall cycles by reducing the critical path
  Fraction of off-chip load requests
  Accuracy and coverage of POPET
  Effect of different features
  Are all features required?
  1C performance
  1C performance line graph
  1C performance against prior predictors
  Effect on stall cycles
  8C performance
  Sensitivity:
    Hermes request issue latency
    Cache hierarchy access latency
    Activation threshold
    ROB size
    LLC size
  Power overhead
  Accuracy without prefetcher
  Main memory request overhead with different prefetchers

## Slide 47: Hermes Paper [MICRO 2022]
Rahul Bera, Konstantinos Kanellopoulos, Shankar Balachandran, David Novo, Ataberk Olgun, Mohammad Sadrosadati, and Onur Mutlu, "Hermes: Accelerating Long-Latency Load Requests via Perceptron-Based Off-Chip Load Prediction" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Talk Video (12 minutes)] [Lecture Video (25 minutes)] [arXiv version] [Source Code (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best paper award at MICRO 2022.
https://arxiv.org/pdf/2209.00188.pdf

## Slide 48: Sibyl: Reinforcement Learning based Data Placement in Hybrid SSDs

## Slide 49: Self-Optimizing Hybrid SSD Controllers
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 50
Sibyl Adaptive and Extensible Data Placement in Hybrid Storage Systems
Using Online Reinforcement Learning
Gagandeep Singh, Rakesh Nadig, Jisung Park,
Rahul Bera, Nastaran Hajinazar, David Novo,
Juan Gómez Luna, Sander Stuijk, Henk Corporaal,
Onur Mutlu
50
Notes: Hi First of all. Thank you very much for staying until this long.
I’m going to present our work “…”

## Slide 51: Executive Summary
Background: A hybrid storage system (HSS) uses multiple different storage devices to provide high and scalable storage capacity at high performance
Problem: Two key shortcomings of prior data placement policies:
  Lack of adaptivity to:
    Workload changes
    Changes in device types and configurations
  Lack of extensibility to more devices
Goal: Design a data placement technique that provides:
  Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
  Easy extensibility to incorporate a wide range of hybrid storage configurations
Contribution: Sibyl, the first reinforcement learning-based data placement technique in hybrid storage systems that:
  Provides adaptivity to changing workload demands and underlying device characteristics
  Can easily extend to any number of storage devices
  Provides ease of design and implementation that requires only a small computation overhead
Key Results: Evaluate on real systems using a wide range of workloads
  Sibyl improves performance by 21.6% compared to the best previous data placement technique in dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-policy policy by 48.2%
  Sibyl achieves 80% of the performance of an oracle policy with storage overhead of only 124.4 KiB
https://github.com/CMU-SAFARI/Sibyl
Notes: First, I am going to start with an executive summary.
[CLICK] Hybrid storage systems use multiple different storage devices to provide high and scalable storage capacity at high performance
[CLICK] We observe two key shortcomings in prior data placement techniques:
First, lack of adaptivity to workload changes and changes in device types and configurations
Second, they also lack extensibility to to more devices.
[CLICK] Our goal in this work is to design a data placement technique that provides
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
Easy extensibility to incorporate a wide range of hybrid storage configurations
[CLICK] to this end we propose Sibyl, an online reinforcement learning-based data placement in Hybrid storage systems that:
  Provides both adaptivity
  and easy extensiblity
  and also Provides ease of design and implementation that requires only a small computation overhead
[CLICK] We extensively evaluate Sibyl on real systems using a wide range of workloads
We show that Sibyl outperforms prior state-of-the-art data placement policeis by 21.6% in dual-hybrid storage system and upto 48.2% on trihybrid system
Sibyl achieves 80% of the performance of an oracle policy that has a complete knowledge of future access patterns while incurring a very modest storage overhead of only 124.4 KiB
The code will be opensourced on our GitHub repository.
https://github.com/CMU-SAFARI/Sibyl

## Slide 52: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: This is the outline of my talk.
First, I am going to start by discussing key shortcomings of prior data placement techniques.

## Slide 53: Hybrid Storage System Basics
Storage Management Layer
Write
Read
Read
Write
Read
Write
Promotion
Eviction
Hybrid Storage System
Fast Device
Slow Device
Address Space (Application/File System View)
Notes: Let's look at some basics on hybrid storage systems. [CLICK] OVER here we show a typical HSS consisting of a fast-yet-small storage device and a slow-yet-large storage device
[CLICK]The address space is divided into a number of logical pages (e.g. 4kib), which are assigned to an application.
[CLICK] The storage management layer in the OS orchestrates host I/O requests across heterogeneous devices,
[CLICK] the storage management layer also manages data migration between the storage devices in an Hybrid storage systems . Eviction usually moves infrequently access data fom the fast storage to the slow storage or when the fast storage device is full.
When data currently stored in the slow storage device is moved to the fast storage device, it is called promotion. Promotion is usually performed when a page in the slow storage device is accessed frequently.
[CLICK] A desirable policy has to effectively utilize the low latency characteristics of the fast device while making optimal use of its small capacity and should provide easy extensibility to a wide range of workloads and Hybrid storage systems configurations

## Slide 54: Hybrid Storage System Basics
Write
Read
Read
Write
Read
Write
Promotion
Eviction
Hybrid Storage System
Performance of a hybrid storage system
highly depends on the ability of the
storage management layer
Notes: [CLICK] Therefore the performance of a hybrid storage system highly depends on the ability of the storage management layer to effectively manage diverse deviaces and workloads

## Slide 55: Key Shortcomings in Prior Techniques
We observe two key shortcomings that significantly limit the performance benefits of prior techniques
Lack of adaptivity to:
  Workload changes
  Changes in device types and configuration
Lack of extensibility to more devices
Notes: We observe two key shortcomings in prior data placement techniques that significantly limits their performance improvement
[CLICK] First, lack of adaptivity to both workload changes and
CLICK] changes in device types and configurations
[CLICK] Second, Lack of extensibility: to more devices
Let’s take a closer look at each of these shortcomings.
[NEXT]

## Slide 56: Lack of Adaptivity (1/2)
Workload Changes
Prior data placement techniques consider only a few workload characteristics that are statically tuned
CDE
RNN-HSS
Oracle
41.1%
Notes: The lower the request latency the better
We observe that all baselines provide reasonable performance under specific workloads [CLICK] while for other they show way lower performance than oracle. [CLICK]
[CLICK] on avg we observe a performance loss for some policies by 41.1% compared to oracle
We conclude, considering only a limited number of workload characteristics leads to
a significant performance gap

## Slide 57: Lack of Adaptivity (2/2)
Changes in Device Types and Configurations
Do not consider underlying storage device characteristics (e.g., changes in the level asymmetry in read/write latencies, garbage collection)
HSS Configuration 1
HSS Configuration 2
Slow-Only
CDE
RNN-HSS
Slow-Only
CDE
RNN-HSS
Oracle
Oracle
Notes: We obseve that performance of some workloads is even worse than slow-only policy that places everything in the slow storage [CLICK] while in another hybrid storage configuration these workloads perform better than slow only[CLICK] [CLICK]
Therefore, we conclude that the high diversity in device characteristics makes it very difficult for a system architect to design a generic data-placement technique that is suitable for all Hybrid storage systems configurations

## Slide 58: Lack of Extensibility (1/2)
Rigid techniques that require significant effort to accommodate more than two devices
Change in storage configuration
Dual-HSS
Notes: The second key shortcoming is that, most of the prior techniques are
[CLICK] rigid that require significant effort to accommodate more than two devices
if we extend from dual hybrid stroage configuration from dual hyrbid to a tri-hybrid configuration

## Slide 59: Lack of Extensibility (2/2)
Rigid techniques that require significant effort to accommodate more than two devices
Change in storage configuration
Design a new policy
Tri-HSS
Notes: [click] design a new data policy to exploit the new device to eviction and promotino from the new storage and update heuristic values as wel. [CLICK]
Therefore system architects need to put significant effort into extending prior data placement techniques to accommodate more than two devices [CLICK] This wastes precious design time and human resource.

## Slide 60: Our Goal
A data-placement mechanism
that can provide:
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
Easy extensibility to incorporate a wide range of hybrid storage configurations
Notes: So our goal in this work is to design a data-placement mechanism that can provide
[CLICK]
Adaptivity, by continuously learning and adapting to the application and underlying device characteristics
[CLICK]
Easy extensibility to incorporate a wide range of hybrid storage configurations.

## Slide 61: Our Proposal
Sibyl
Formulates data placement in hybrid storage systems as a reinforcement learning problem
Sibyl is an oracle that makes accurate prophecies
https://en.wikipedia.org/wiki/Sibyl
Notes: To this end, we propose Sibyl
Which formulates data placement in hybrid…

## Slide 62: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: Lets go into the formulation of dataplacement as a reinforcement learning problem

## Slide 63: Basics of Reinforcement Learning (RL)
Agent learns to take an action in a given state
to maximize a numerical reward
Notes: First, let me briefly describe the basics of reinforcement learning.
A RL system contains two components: [CLICK] the agent and the environment.
The agent observes the state of the environment in every timestep [CLICK], takes an action based on the state [CLICK], and receives a reward for that action [CLICK].
[CLICK] Agent’s goal is to find a policy where agent’s action in a given state leads to maximum reward

## Slide 64: Formulating Data Placement as RL
Agent
Environment
State (St)
Action (At)
Reward (Rt+1)
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place the current page
Notes: In Sibyl, we formulate data-placement as a reinforcement learning problem.
[CLICK] Sibyl acts as the agent, while [CLICK] the hybrid storage subsystem acts as the environment.
[CLICK] Sibyl observes workload and system features from every storage request and use it as a state information to take a data placement action [CLICK]
[CLICK] For every data placement action, Sibyl receives a numerical reward that evaluates the effectiveness of the data placement decision
Now we will concretely define the state, action, and the reward for Sibyl.

## Slide 65: What is State?
Limited number of state features:
  Reduce the implementation overhead
  RL agent is more sensitive to reward
6-dimensional vector of state features
We quantize the state representation into bins to reduce storage overhead
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: [CLICK] For the state, we use limited number of state features after performing feature selection to:
reduce implementation overhead
[CLICK] and we observe RL agent's perfromance is more sensitive to the reward than state features. So adding many feature does not help
[CLICK] We define the state as a 6-dimensional vector of program features.
[CLICK] Some examples are the size of the incoming request the type of request etc
[click] we also quantize the state representation into bins to reduce the storage overhead

## Slide 66: What is Reward?
Defines the objective of Sibyl
We formulate the reward as a function of the request latency
Encapsulates three key aspects:
  Internal state of the device (e.g., read/write latencies, the latency of garbage collection, queuing delays, …)
  Throughput
  Evictions
More details in the paper
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: The reward defines the objective of Sibyl
[CLICK] Though Sibyl can learn from any …, in this paper we formulate the reward as a function of the request latency
[CLICK] A reward encapsulates three metrics: …

## Slide 67: What is Action?
At every new page request, the action is to select a storage device
Action can be easily extended to any number of storage devices
Sibyl learns to proactively evict or promote a page
Hybrid Storage System
Sibyl
Features of the current request and system
Request latency
(of last served request)
Select storage device to place
the current page
Notes: We define the action as the selection of a storage device to place the current page.
[CLICK] Such an action allows easy extensiblity to any number of storage devices
[CLICK] it makes SIbyl learn to proactively evit or promote a page from the storage device

## Slide 68: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: We now provide a brief overview and design of Sibyl.

## Slide 69: Sibyl Execution
RL Decision Thread
Storage
Request
(from OS)
RL Training Thread
Periodic Policy
Weight Update
State, Reward, and Action Information
Data Placement Decision
Asynchronous
Execution
Sibyl
Notes: FIRST we discuss the execution model for Sibyl. We implement sibyl in the the host OS. [CLICK] Where for every storage request Sibyl uses an RL decision thread to make [CLICK] data placemnet decisions.
Sibyl uses another thread, [CLICK] called the RL training thread that works in the background. It keeps collecting information about Sibyl's state, action and reward, which uses this information to train a data placement policy. [CLICK] periodically we replace the RL decision thread policy with RL training thread policy.
[CLICK] Our two-threaded implementation runs ASYNCHROUNOUS AND avoids that the training in RL training thread interrupts or delays data placement decisions for incoming requests.

## Slide 70: Sibyl Design: Overview
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Weights update
10
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: Now we will go into the implementation of each thread

## Slide 71: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: First we discuss the RL decision thread, where Sibyl decides the data placement of the current storage request while collecting information about its decisions

## Slide 72: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: For every new storage request to the Hybrid storage systems , Sibyl uses the state information to make a data placement action.

## Slide 73: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: The inference network predicts the expected benefits of each action for a given state.
Sibyl policy selects the action with the highest expected benefit
or, a random action for exploration of the Hybrid storage systems

## Slide 74: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: While making data placement decision, Sibyl collects information about the state, action, and reward

## Slide 75: RL Decision Thread
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Training
Network
RL Training Thread
Batch
Training Dataset
Periodic Policy
Weight Update
Notes: in an experience buffer, which in used in RL Training thread

## Slide 76: RL Training Thread
Periodic Weights update
10
RL Training Thread
Batch
Training Dataset
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Policy
Weight Update
Training
Network
Notes: In the RL training thread, Sibyl uses the collected experiences to update its decision making policy online by training a neural network.
Sibyl continuously learns from its past decisions and their impact.

## Slide 77: Periodic Weight Transfer
Inference
Network
Max
HSS
Collect
Experiences
Experience Buffer (in host DRAM)
Observation
Vector
Storage
Request
(from OS)
State
State
Action
Reward
RL Decision Thread
Sibyl Policy
Periodic Weights update
10
Training
Network
Periodic Policy
Weight Update
RL Training Thread
Batch
Training Dataset
Notes: To enable the parallel execution of the two threads, we duplicate the neural network that is used to make data placement decisions, so the inference network does not have a separate training steps and only uses the weights of the training network, which we periodically update.

## Slide 78: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: We now present our key results

## Slide 79: Evaluation Methodology (1/3)
Real system with various HSS configurations
  Dual-hybrid and tri-hybrid systems
AMD Ryzen7 2700G CPU
Seagate HDD
ST1000DM010
Intel Optane SSD P4800X
Intel SSD D3-S4510
ADATA
SU630 SSD
Notes: [CLICK] We perfrom real system evaluation for both dual-hybrid and tri-hybrid systems
[CLICK] over here we show our evaluation setup that consists of multi different devices
[CLICK] We implement sibyl in the storage management layer of AMD Ryzen 7 2700G CPU

## Slide 80: Evaluation Methodology (2/3)
Cost-Oriented HSS Configuration
High-end SSD
Low-end HDD
Performance-Oriented HSS Configuration
High-end SSD
Middle-end SSD
Notes: First we evalutate a cost-oriented hybrid storage configuration in which we use
[CLICK]a high end ssd with a low-end hard disk drive where the latency difference between the two devices is quite large
[CLICK] Performance oriented hybrid storage configuration we
[CLICK]use a high end ssd with a middle end ssd
where two devices have similar latencies

## Slide 81: Evaluation Methodology (3/3)
18 different workloads from:
  MSR Cambridge and Filebench Suites
Four state-of-the-art data placement baselines:
  CDE [Matsui+, Proc. IEEE’17]
  HPS [Meswani+, HPCA’15]
  Archivist [Ren+, ICCD’19]
  RNN-HSS [Doudali+, HPDC’19]
Heuristic-based
Learning-based
Notes: [CLICK] We use 18 different workloads from MSR CAMBRIDGE and Filebench Suite
[CLICK] and compare Sibyl against four state of heuristic and supervised—learning based data placmenet policies

## Slide 82: Performance Analysis
Cost-Oriented HSS Configuration
Slow-Only
CDE
HPS
Archivist
RNN-HSS
Sibyl
Oracle
High-end SSD
Low-end HDD
Notes: [CLICK]Over here we show the performance results in terms of average request latency for MSR CAMBRIDGE workloads for all the workloads and policies

## Slide 83: Performance Analysis
Sibyl consistently outperforms all the baselines
for all the workloads
Cost-Oriented HSS Configuration
Slow-Only
CDE
HPS
Archivist
RNN-HSS
Sibyl
Oracle
High-end SSD
Low-end HDD
Notes: We observe that Sibyl consistently outperforms all the baselines for all the workloads

## Slide 84: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
High-end SSD
Mid-end SSD
Notes: In a performance oriented Hybrid storage systems configuration, where two devices have similar latencies [CLICK]
[CLICK]

## Slide 85: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Sibyl provides 21.6% performance improvement by dynamically adapting its data placement policy
High-end SSD
Mid-end SSD
Notes: Sibyl provides 21.6% performance improvement by dynamically adapting its data placement policy

## Slide 86: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
High-end SSD
Mid-end SSD
Notes: Sibyl provides slightly lower performance than other baselines in only two workloads for this configuration.
We observe that such workloads are write-intensive and have many random requests (in terms of both access pattern and request size).
Therefore, in the paper we show that for such workloads we need to perform frequent retraining

## Slide 87: Performance Analysis
RNN-HSS
Sibyl
Oracle
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Sibyl achieves 80% of the performance
of an oracle policy that has
complete knowledge of future access patterns
High-end SSD
Mid-end SSD
Notes: on average Sibyl achieves 80% performance of an oracle policy that has complete knowledge of
future access patterns

## Slide 88: Performance on Tri-HSS
Extending Sibyl for more devices:
SibylTri-hybrid
HeuristicTri-hybrid
High-end SSD
Low-end HDD
Mid-end SSD
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
Notes: We also evaluate the EXTENSIBILITY of sibyl to more devices
To extend sibyl for more storage devices we have to only:
1. Add a new action in sibyl’s action space
2. Add the remaining capacity of the new device as a state feature
and sibyl automatically figures out the best policy
Here we show the performanc results for a state of the art heuristic based policy. This heuristic policy is an extended version of CDE policy which requires significant implementation effort for handling all the dataplacement cases because of the new device like eviction and promotion from the new device and where to send that data, set threshold values etc.

## Slide 89: Performance on Tri-HSS
SibylTri-hybrid
HeuristicTri-hybrid
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
High-end SSD
Low-end HDD
Mid-end SSD
Notes: and compare to sibyl for trihybrid system

## Slide 90: Performance on Tri-HSS
SibylTri-hybrid
HeuristicTri-hybrid
Extending Sibyl for more devices:
  Add a new action
  Add the remaining capacity of the new device as a state feature
Sibyl outperforms the state-of-the-art
data placement policy by
48.2% in a real tri-hybrid system
Sibyl reduces the system architect's burden
by providing ease of extensibility
High-end SSD
Low-end HDD
Mid-end SSD
Notes: Sibyl outperforms the state-of-the-art-policy policy by upto 48.2%
[click]
We conclude that Sibyl provides ease of extensibility to new storage system configurations, which reduces the system architect’s burden in designing sophisticated data placement mechanisms.

## Slide 91: Sibyl’s Overhead
124.4 KiB of total storage cost
  Experience buffer, inference and training network
40-bit metadata overhead per page for state features
Inference latency of ~10ns
Training latency of ~2us
Small area overhead
Small inference overhead
Satisfies prediction latency
Notes: All of Sibyl performance benefits comes at a modest cost of 124.4KB storage cost to implement experience buffer, inference and training network
[CLICK] and 40-bit metadata overhead per page
[CLICK] We have inference latency of 10nanos, which are orders of magnitude smaller than the I/O read latency of a even a high end SSD (around 3micro seconds for Samsung ZNAND SSD)
[CLICK] with training latency of 2mico sec
So sibyl provides:
[CLICK]small area and
[CLICK]inference overhead [CLICK] which satisfied the prediction latency for making a data placement decision

## Slide 92: More in the Paper (1/3)
Throughput (IOPS) evaluation
  Sibyl provides high IOPS compared to baseline policies because it indirectly captures throughput (size/latency)
Evaluation on unseen workloads
  Sibyl can effectively adapt its policy to highly dynamic workloads
Evaluation on mixed workloads
  Sibyl provides equally-high performance benefits as in single workloads
Notes: We have many more exciting results in the paper including throughput comparison, evaluation on unseen workloads and mixed workloads

## Slide 93: More in the Paper (2/3)
Evaluation on different features
  Sibyl autonomously decides which features are important to maximize the performance
Evaluation with different hyperparameter values
Sensitivity to fast storage capacity
  Sibyl provides scalability by dynamically adapting its policy to available storage size
Explainability analysis of Sibyl's decision making
  Explain Sibyl’s actions for different workload characteristics and device configurations
Notes: And many more.
For more details we encourage you to read our paper

## Slide 94: More in the Paper (3/3)
https://arxiv.org/pdf/2205.07394.pdf
https://github.com/CMU-SAFARI/Sibyl

## Slide 95: Talk Outline
Key Shortcomings of Prior Data Placement Techniques
Formulating Data Placement as Reinforcement Learning
Sibyl: Overview
Evaluation of Sibyl and Key Results
Conclusion
Notes: Now I will conclude my talk

## Slide 96: Conclusion
We introduced Sibyl, the first reinforcement learning-based data placement technique in hybrid storage systems that provides
  Adaptivity
  Easily extensibility
  Ease of design and implementation
We evaluated Sibyl on real systems using many different workloads
  Sibyl improves performance by 21.6% compared to the best prior data placement policy in a dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-data placement policy by 48.2%
  Sibyl achieves 80% of the performance of an oracle policy with a storage overhead of only 124.4 KiB
https://github.com/CMU-SAFARI/Sibyl
Notes: We introduced Sibyl, the first reinforcement learning-based data placement in HSS that provides
  Adaptivity
  Easily extensibility
  Ease of design and implementation
We evaluated Sibyl on real systems using many different workloads
  Sibyl improves performance by 21.6% compared to the best previous data placement technique in dual-HSS configuration
  In a tri-HSS configuration, Sibyl outperforms the state-of-the-art-policy policy by 48.2%
  Sibyl achieves 80% performance of an oracle policy with storage overhead of only 124.4 KiB

## Slide 97
Sibyl Adaptive and Extensible Data Placement in Hybrid Storage Systems
Using Online Reinforcement Learning
Gagandeep Singh, Rakesh Nadig, Jisung Park,
Rahul Bera, Nastaran Hajinazar, David Novo,
Juan Gómez Luna, Sander Stuijk, Henk Corporaal,
Onur Mutlu
97
Notes: Hi First of all. Thank you very much for staying until this long.
I’m going to present our work “…”

## Slide 98: ISCA 2022 Paper, Slides, Videos
Gagandeep Singh, Rakesh Nadig, Jisung Park, Rahul Bera, Nastaran Hajinazar, David Novo, Juan Gomez-Luna, Sander Stuijk, Henk Corporaal, and Onur Mutlu, "Sibyl: Adaptive and Extensible Data Placement in Hybrid Storage Systems Using Online Reinforcement Learning" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [Sibyl Source Code] [Talk Video (16 minutes)]
https://arxiv.org/pdf/2205.07394.pdf

## Slide 99: SSD Course (Spring 2023)
Spring 2023 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=modern_ssds
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=modern_ssds
Youtube Livestream (Spring 2023):
  https://www.youtube.com/watch?v=4VTwOMmsnJY&list=PL5Q2soXY2Zi_8qOM5Icpp8hB2SHtm4z57&pp=iAQB
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=hqLrd-Uj0aU&list=PL5Q2soXY2Zi9BJhenUq4JI5bwhAMpAp13&pp=iAQB
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 100: Comp Arch (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 101: Hermes & Sibyl: ML-Driven Memory & Storage Management
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
27 September 2023
VMware

## Slide 102: Hermes Discussion
FAQs
  What are the selected set of program features?
  Can you provide some intuition on why these features work?
  What happens in case of a misprediction?
  What’s the performance headroom for off-chip prediction?
  Do you see a variance of different features in final prediction accuracy?
Simulation Methodology
  System parameters
  Evaluated workloads
More Results
  Percentage of off-chip requests
  Reduction in stall cycles by reducing the critical path
  Fraction of off-chip load requests
  Accuracy and coverage of POPET
  Effect of different features
  Are all features required?
  1C performance
  1C performance line graph
  1C performance against prior predictors
  Effect on stall cycles
  8C performance
  Sensitivity:
    Hermes request issue latency
    Cache hierarchy access latency
    Activation threshold
    ROB size
    LLC size
  Power overhead
  Accuracy without prefetcher
  Main memory request overhead with different prefetchers

## Slide 103: HERMES BACKUP

## Slide 104: Initial Set of Program Features

## Slide 105: Selected Set of Program Features
Five features
A binary hint that represents whether or not a cacheblock has been recently touched

## Slide 106: When A Feature Works/Does Not Work?
Trace: 462.libquantum-1343B
PC: 0x401442
Cacheline #42
Cacheline #43
…
…
Without prefetcher
PC + first access
Cacheline offset + first access
With a simple stride prefetcher
Cacheline offset + first access

## Slide 107: What Happens in case of a Misprediction?
Two cases of mispredictions:
Predicted on-chip but actually goes off-chip
  Loss of performance improvement opportunity
Predicted off-chip but actually is on-chip
  Memory controller forwards the data to LLC if and only if a load to the same address have already missed LLC and arrived at the memory controller
No need for misprediction detection and recovery
No need for misprediction detection and recovery

## Slide 108: Performance Headroom of Off-Chip Prediction

## Slide 109: System Parameters

## Slide 110: Evaluated Workloads

## Slide 111: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
50%
Nearly 50% of the loads are still not prefetched
1

## Slide 112: Observation: Not All Off-Chip Loads are Prefetched
Chart: Fraction of off-chip loads in the No-prefetching system
| No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | No-prefetching | Pythia | SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
Blocking | 0.59586 | 0.27156 | 0.50345 | 0.19755 | 0.64046 | 0.42323 | 0.68078 | 0.23748 | 0.71751 | 0.56666 | 0.63334 | 0.35497
Non-blocking | 0.40414 | 0.13884 | 0.49655 | 0.097339 | 0.35954 | 0.12376 | 0.31922 | 0.10632 | 0.28249 | 0.2031 | 0.36666 | 0.14188
MPKI | 16.72 | 8.4511 | 19.6554 | 4.7661 | 9.5423 | 5.7169 | 18.2326 | 8.423 | 20.7412 | 10.4891 | 18.0321 | 7.9886
70% of these off-chip loads blocks ROB
2

## Slide 113: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency

## Slide 114: Observation: With Large Cache Comes Longer Latency
On-chip cache access latency significantly contributes to the latency of an off-chip load
Chart: # stall cycles due to an off-chip load blocking instruction retirement from ROB
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
On-chip cache access latency | 58.4907 | 63.496 | 55.0896 | 61.496 | 56.0957 | 58.9336
Remaining | 76.5749 | 74.4995 | 96.2024 | 100.5303 | 94.7627 | 88.1545
58
On-chip cache hierarchy access latency
40% of stall cycles caused by an off-chip load can be eliminated
by removing on-chip cache access latency from its critical path

## Slide 115: What Fraction of Load Requests Goes Off-Chip?

## Slide 116: Off-Chip Prediction Quality: Defining Metrics
Predicted off-chip
Actual off-chip
Predicted and actual off-chip
Accuracy
Coverage

## Slide 117: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%

## Slide 118: Off-Chip Prediction Quality: Analysis
Accuracy
Coverage
Chart: Accuracy %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.4412 | 0.40588 | 0.49015 | 0.32147 | 0.61767 | 0.47032
TTP | 0.11337 | 0.11045 | 0.16348 | 0.11497 | 0.27204 | 0.16612
POPET | 0.82929 | 0.77941 | 0.72326 | 0.79347 | 0.73138 | 0.77141
Chart: Coverage %
| SPEC06 | SPEC17 | PARSEC | Ligra | CVP | AVG
HMP | 0.2149 | 0.17874 | 0.2214 | 0.09024 | 0.34055 | 0.22308
TTP | 0.95587 | 0.95967 | 0.94187 | 0.9398 | 0.94131 | 0.94785
POPET | 0.77488 | 0.67572 | 0.83355 | 0.69819 | 0.76205 | 0.74276
47%
22%
16%
95%
77%
74%
POPET provides off-chip predictions with high-accuracy and high-coverage

## Slide 119: Effect of Different Features
Combination of features provides both higher accuracy and higher coverage than any individual feature

## Slide 120: Are All Features Required? (1)
No single feature individually provides
highest prediction accuracy across all workloads

## Slide 121: Are All Features Required? (2)
No single feature individually provides
highest prediction coverage also across all workloads

## Slide 122: Single-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone in every workload category

## Slide 123: Single-Core Performance Line Graph

## Slide 124: Single-Core Performance Against Prior Predictors
POPET provides higher performance benefit
than prior predictors
Hermes with POPET achieves nearly 90% performance improvement of the Ideal Hermes

## Slide 125: Effect on Stall Cycles
Hermes reduces off-chip load induced stall cycles
on average by 16.2% (up-to 51.8%)

## Slide 126: Eight-Core Performance
Hermes in combination with Pythia
outperforms Pythia alone by 5.1% on average

## Slide 127: Effect of Hermes Request Issue Latency
3.6%
5.7%
Hermes in combination with Pythia outperforms Pythia alone even with a 24-cycle Hermes request issue latency

## Slide 128: Effect of Cache Hierarchy Access Latency
3.6%
6.2%
Hermes can provide even higher performance benefit in
future processors with bigger and slower on-chip caches

## Slide 129: Effect of Activation Threshold
With increase in activation threshold
Accuracy increases
Coverage decreases

## Slide 130: Power Overhead

## Slide 131: Effect of ROB Size
6.7%
5.3%

## Slide 132: Effect of LLC Size
1.3%
2.5%

## Slide 133: Accuracy and Coverage with Different Prefetchers
POPET’s accuracy and coverage increases significantly
in absence of a data prefetcher

## Slide 134: Increase in Main Memory Requests

## Slide 135: SIBYL BACKUP
135

## Slide 136: Performance on Unseen Workloads
H&M (H&L) HSS configuration, Sibyl outperforms RNN-HSS and Archivist by 46.1% (54.6%) and 8.5% (44.1%), respectively

## Slide 137: Performance Analysis
Sibyl
Oracle
Baseline policies are ineffective for many workloads even when compared to Slow-Only
RNN-HSS
Slow-Only
CDE
HPS
Archivist
Performance-Oriented HSS Configuration
Notes: For workloads like prn_1, proj_2, etch baseline policies are ineffeciteve even when compared to slow only policy does places everything in the slow storage

## Slide 138: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
Notes: We evaluate mixing two or more workloads at the same time while randomly varying their relative start times.
Such a scenario
leads to unpredictable execution where requests arrive at dif- ferent, unpredictable timesteps,
mimics distributed workloads,
(3) further tests the ability of Sibyl to dynamically adapt its decision-making policy.
shows average request latency for mixed workloads in two different storage configuration.[click] We use two different settings for Sibyl: (a) Sibyl𝐷𝑒 𝑓 , where we use our default hyper-parameters and (b) Sibyl𝑂𝑝𝑡, where we optimize the hyper-parameters for these mixed workloads

## Slide 139: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
SibylDef outperforms baseline data placement techniques by up to 27.9%
Notes: Sibyl𝐷𝑒 𝑓 provides upto 27.9% higher performance than baseline policies

## Slide 140: Performance on Mixed Workloads
Slow-Only
CDE
HPS
Archivist
RNN-HSS
SibylDef
SibylOpt
Oracle
Performance-Oriented
Cost-Oriented
SibylDef outperforms baseline data placement techniques by up to 27.9%
SibylOpt provides 7.2% higher average performance than SibylDef
Notes: With optimized hyper-parameters, Sibyl𝑂𝑝𝑡 provides 5.2% (9.3%) higher average performance for H&M (H&L) HSS configuration than Sibyl𝐷𝑒 𝑓 .
We conclude that Sibyl can effectively adapt its data placement policy online to highly dynamic workloads.

## Slide 141: Performance With Different Features
Sibyl autonomously decides which features are important to maximize the performance of the running workload

## Slide 142: Sensitivity to Fast Storage Capacity

## Slide 143: Explainability Analysis

## Slide 144: Training and Inference Network
Training and inference network allow parallel execution
Observation vector as the input
Produces probability distribution of Q-values
Notes: A deep neural network can be prohibitive due to the long time it requires for training and convergence, preventing Sibyl to adapt to new state-action pairs in a timely manner.
Based on experiments, we find that a simple feed-forward network [135] with only two hidden layers [136] provides good performance for Sibyl’s data placement task.
The network takes the observation vector 𝑂𝑡 as its input and produces a probability distribution of Q-values as its output