## Slide 1: Page Overlays An Enhanced Virtual Memory Framework to Enable Fine-grained Memory Management
Vivek Seshadri
Gennady Pekhimenko, Olatunji Ruwase,
Onur Mutlu, Phillip B. Gibbons, Michael A. Kozuch,
Todd C. Mowry, Trishul Chilimbi
@CMU

## Slide 2: Executive Summary
Sub-page memory management has several applications
  More efficient capacity management, protection, metadata, …
Page-granularity virtual memory → inefficient implementations
  Low performance and high memory redundancy
          Page Overlays: New Virtual Memory Framework
          Virtual Page → (physical page, overlay)
            Overlay contains new versions of subset of cache lines
            Efficiently store pages with mostly similar data
Largely retains existing virtual memory structure
  Low cost implementation over existing frameworks
Powerful access semantics – Enables many applications
  E.g., overlay-on-write, efficient sparse data structure representation
Improves performance and reduces memory redundancy
V
P
O

## Slide 3: Existing Virtual Memory Systems
Virtual memory enables many OS functionalities
  Flexible capacity management
  Inter-process data protection, sharing
  Copy-on-write, page flipping
Virtual page
4KB
Physical Page
4KB
Page
Tables

## Slide 4: Case Study: Copy-on-Write
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space

## Slide 5: Shortcomings of Page-granularity Management
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space
High memory redundancy

## Slide 6: Shortcomings of Page-granularity Management
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space
4KB copy: High Latency

## Slide 7: Shortcomings of Page-granularity Management
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space
TLB Shootdown
High Latency
Wouldn’t it be nice to map pages at a
finer granularity (smaller than 4KB)?

## Slide 8: Fine-grained Memory Management
Fine-grained
Memory Management
Fine-grained
data protection
(simpler programs)
More efficient
capacity management
(avoid internal fragmentation, deduplication)
Fine-grained
metadata management
(better security, efficient software debugging)
Higher Performance
(e.g., more efficient
copy-on-write)

## Slide 9: Goal: Efficient Fine-grained Memory Management
Existing Virtual Memory Framework
Low performance
High memory redundancy
V
P
O
Enable efficient fine-grained management
Low implementation cost
New Virtual Memory Framework

## Slide 10: Outline
Shortcomings of Existing Framework
Page Overlays – Overview
Implementation
  Challenges and solutions
Applications and Evaluation
Conclusion

## Slide 11: The Page Overlay Framework
C0
C1
C2
C3
C4
C5
Virtual Page
C0
C1
C2
C3
C4
C5
Physical Page
C2
C5
Overlay
The overlay contains only a subset of cache lines from the virtual page
Access Semantics:
Only cache lines not present in the overlay are accessed from the physical page
C1
C1
C5
C5
Overlay maintains the newer version of a subset of cache lines from the virtual page

## Slide 12: Overlay-on-Write: An Efficient Copy-on-Write
Virtual page
Physical Page
Write
Copy-on-Write
Page
Tables
Virtual Address Space
Physical Address Space
Overlay
Overlay contains only modified cache lines
Does not require full page copy

## Slide 13: Outline
Shortcomings of Existing Framework
Page Overlays – Overview
Implementation
  Challenges and solutions
Applications and Evaluation
Conclusion

## Slide 14: Implementation Overview
V
Virtual Address Space
P
O
Main Memory
Regular Physical Pages
Overlays
No changes!
Three challenges

## Slide 15: Implementation Challenges
C0
C1
C2
C3
C4
C5
Virtual Page
C0
C1
C2
C3
C4
C5
Physical Page
C2
C5
Overlay
C5
C5
?
1
Does the cache line belong to the overlay?
2
What is the address/tag of the overlay cache line?
C3
3
How to keep the TLBs coherent?

## Slide 16: Identifying Overlay Cache Lines: Overlay Bit Vector
C0
C1
C2
C3
C4
C5
Virtual Page
C0
C1
C2
C3
C4
C5
Physical Page
C2
C5
Overlay
C5
C5
?
1
Does the cache line belong to the overlay?
0
0
1
0
0
1
Overlay Bit Vector
Indicates which cache lines belong to the overlay

## Slide 17: Addressing Overlay Cache Lines: Naïve Approach
V
Virtual Address Space
P
O
Main Memory
Use the location of the overlay in main memory to tag overlay cache lines
1. Processor must compute the address
2. Does not work with virtually-indexed caches
3. Complicates overlay cache line insertion

## Slide 18: Addressing Overlay Cache Lines: Dual Address Design
V
Virtual Address Space
P
O
Main Memory
P
O
Page Tables
Physical Address Space
Unused physical address space
Overlay cache address space
same size

## Slide 19: Virtual-to-Overlay Mappings
V
Virtual Address Space
P
O
Main Memory
P
O
Page Tables
Physical Address Space
Overlay cache address space
Direct Mapping
Overlay Mapping Table (OMT)
(maintained by memory controller)

## Slide 20: Keeping TLBs Coherent
C0
C1
C2
C3
C4
C5
Virtual Page
C0
C1
C2
C3
C4
C5
Physical Page
C2
C5
Overlay
C5
C5
C3
3
How to keep the TLBs coherent?
Use the cache coherence protocol to keep TLBs coherent!

## Slide 21: Final Implementation
CPU
L1 Cache
Last Level Cache
Regular Physical Pages
Memory Controller
TLB
OMT Cache
OMT
Overlay Bit Vectors
3
1
2
Overlays

## Slide 22: Other Details in the Paper
Virtual-to-overlay mapping
TLB and cache coherence
OMT management (by the memory controller)
Hardware cost
  94.5 KB of storage
OS Support

## Slide 23: Outline
Shortcomings of existing frameworks
Page Overlays – Overview
Implementation
  Challenges and solutions
Applications and Evaluation
Conclusion

## Slide 24: Methodology
Memsim memory system simulator [Seshadri+ PACT 2012]
2.67 GHz, single core, out-of-order, 64 entry instruction window
64-entry L1 TLB, 1024-entry L2 TLB
64KB L1 cache, 512KB L2 cache, 2MB L3 cache
Multi-entry Stream Prefetcher [Srinath+ HPCA 2007]
Open row, FR-FCFS, 64 entry write buffer, drain when full
64-entry OMT cache
DDR3 1066 MHz, 1 channel, 1 rank, 8 banks

## Slide 25: Overlay-on-Write
Lower memory redundancy
Lower latency
Virtual page
Physical Page
Write
2
3
1
Copy-on-Write
Virtual page
Physical Page
Write
Copy-on-Write
Overlay
Copy-on-Write
Overlay-on-Write

## Slide 26: Fork Benchmark
Additional memory consumption
Performance (cycles per instruction)
Parent Process
Fork
(child idles)
Copy-on-Write
Overlay-on-Write
Time
write
300 million insts
Applications from SPEC CPU 2006 (varying write working sets)

## Slide 27: Overlay-on-Write vs. Copy-on-Write on Fork
Chart: Write Working Set
| Small | Dense | Sparse | Mean
Copy-on-write | 1.764 | 14.246 | 53.744 | 23.25
Overlay-on-write | 1.58 | 14.062 | 16.918 | 10.85
Chart: Write Working Set
| Small | Dense | Sparse | Mean
Copy-on-write | 1.318 | 4.626 | 7.13 | 3.07
Overlay-on-write | 1.318 | 4.5 | 5.824 | 2.59
Copy-on-Write
Overlay-on-Write
53%
15%

## Slide 28: Conclusion
Sub-page memory management has several applications
  More efficient capacity management, protection, metadata, …
Page-granularity virtual memory → inefficient implementations
  Low performance and high memory redundancy
          Page Overlays: New Virtual Memory Framework
          Virtual Page → (physical page, overlay)
            Overlay contains new versions of subset of cache lines
            Efficiently store pages with mostly similar data
Largely retains existing virtual memory structure
  Low cost implementation over existing frameworks
Powerful access semantics – Enables many applications
  E.g., overlay-on-write, efficient sparse data structure representation
Improves performance and reduces memory redundancy
V
P
O

## Slide 29: Page Overlays An Enhanced Virtual Memory Framework to Enable Fine-grained Memory Management
Vivek Seshadri
Gennady Pekhimenko, Olatunji Ruwase,
Onur Mutlu, Phillip B. Gibbons, Michael A. Kozuch,
Todd C. Mowry, Trishul Chilimbi
@CMU