## Slide 1: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management
Yixin Luo, Yu Cai, Saugata Ghose, Jongmoo Choi*, Onur Mutlu
Carnegie Mellon University, *Dankook University
WARM

## Slide 2: Executive Summary
Flash memory can achieve 50x endurance improvement by relaxing retention time using refresh [Cai+ ICCD ’12]
Problem: Refresh consumes the majority of endurance improvement
Goal: Reduce refresh overhead to increase flash memory lifetime
Key Observation: Refresh is unnecessary for write-hot data
Key Ideas of Write-hotness Aware Retention Management (WARM)
  Physically partition write-hot pages and write-cold pages within the flash drive
  Apply different policies (garbage collection, wear-leveling, refresh) to each group
Key Results
  WARM w/o refresh improves lifetime by 3.24x
  WARM w/ adaptive refresh improves lifetime by 12.9x (1.21x over refresh only)
Notes: As you know, flash memory has limited write endurance.

## Slide 3: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 4: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 5: Retention Time Relaxation for Flash Memory
Flash memory has limited write endurance
  Retention time significantly affects endurance
  The duration for which flash memory correctly holds data
Chart: Retention Time
| 3-day | 3-week | 3-month | 3-year
P/E Cycles | 150000 | 20000 | 8000 | 3000
Typical flash retention guarantee
Requires refresh to reach this
[Cai+ ICCD ’12]

## Slide 6: NAND Flash Refresh
Flash Correct and Refresh (FCR), Adaptive Rate FCR (ARFCR) [Cai+ ICCD ‘12]
Problem: Flash refresh operations reduce extended lifetime
Goal: Reduce refresh overhead, improve flash lifetime
Nominal endurance
Extended endurance
Unusable endurance (consumed by refresh)
3000
150000
Notes: Prior work proposes Flash correct and refresh FCR which applies periodic refresh operations to extend flash endurance.
Adaptive rate FCR is another technique that adaptively change the refresh rate to wear-out levels.

## Slide 7: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 8: Observation 1: Refresh Overhead is High
Chart: % of Extended Endurance Consumed by Refresh
| iozone | postmark | financial | proj | prxy | prn | hm | web-vm | src | stg | usr | web | rsrch | ts | wdev | homes | GMEAN
3-day refresh | 0.013367 | 0.028721 | 0.48359 | 0.65361 | 0.7675 | 0.84382 | 0.91026 | 0.91325 | 0.93367 | 0.93379 | 0.94295 | 0.94661 | 0.95023 | 0.95406 | 0.96606 | 0.97177 | 0.53366
Notes: Evaluated 16 real workload traces to find % of

## Slide 9: Observation 2: Write-Hot Pages Can Skip Refresh
Write-Cold Page
Write-Cold Page
Write-Cold Page
Write-Hot Page
Write-Cold Page
Write-Hot Page
Write-Hot Page
Invalid Page
Write-Hot Page
Invalid Page
Write-Hot Page
Retention Effect
Update
Invalid Page
Write-Cold Page
Need Refresh
Skip Refresh
Write-Hot Page

## Slide 10: Conventional Write-Hotness Oblivious Management
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Hot Page 1
Cold Page 2
Hot Page 1
Cold Page 3
Hot Page 4
Cold Page 5
Hot Page 4
Hot Page 1
Hot Page 4
Cold Page 2
Cold Page 3
Cold Page 4
Read
Write
Erase
Unable to relax retention time for blocks with write-hot and cold pages

## Slide 11: Key Idea: Write-Hotness Aware Management
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Hot Page 1
Cold Page 2
Hot Page 1
Cold Page 3
Hot Page 4
Cold Page 5
Hot Page 4
Hot Page 1
Hot Page 4
Hot Page 1
Hot Page 4
Hot Page 1
Can relax retention time for blocks with write-hot pages only

## Slide 12: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 13: WARM Overview
Design Goal:
  Relax retention time w/o refresh for write-hot data only
WARM: Write-hotness Aware Retention Management
  Write-hot/write-cold data partitioning algorithm
  Write-hotness aware flash policies
    Partition write-hot and write-cold data into separate blocks
    Skip refreshes for write-hot blocks
    More efficient garbage collection and wear-leveling

## Slide 14: Write-Hot/Write-Cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
1. Initially, all data is cold and is stored in the cold virtual queue.
Notes: Dynamically partitions write-hot and write-cold data into separate queues, allowing WARM to quickly adapt to workload behavior.

## Slide 15: Write-Hot/Write-Cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
2. On a write operation, the data is pushed to the tail of the cold virtual queue.
②

## Slide 16: Write-Hot/Write-Cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
Recently-written data is at the tail of cold virtual queue.
②

## Slide 17: Write-Hot/Write-Cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
②
①
③
TAIL
TAIL
HEAD
3, 4. On a write hit in the cooldown window, the data is promoted to the hot virtual queue.

## Slide 18: Write-Hot/Write-Cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
②
①
③
TAIL
HEAD
TAIL
HEAD
Data is sorted by write-hotness in the hot virtual queue.

## Slide 19: Write-Hot/Write-Cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
⑤
②
①
③
TAIL
HEAD
TAIL
HEAD
5. On a write hit in hot virtual queue, the data is pushed to the tail.

## Slide 20: Write-Hot/Write-Cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
⑥
⑤
②
①
③
TAIL
HEAD
TAIL
HEAD
6. Unmodified hot data will be demoted to the cold virtual queue.

## Slide 21: Conventional Flash Management Policies
Flash Translation Layer (FTL)
  Map data to erased blocks
  Translate logical page number to physical page number
Garbage Collection
  Triggered before erasing a victim block
  Remap all valid data on the victim block
Wear-leveling
  Triggered to balance wear-level among blocks

## Slide 22: Write-Hotness Aware Flash Policies
Flash Drive
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Block 8
Block 9
Block 10
Block 11
Hot Block Pool
Cold Block Pool
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Block 8
Block 9
Block 10
Block 11
Write-hot data  naturally relaxed retention time
Program in block order
Garbage collect in block order
All blocks naturally wear-leveled
Write-cold data  lower write frequency, less wear-out
Conventional garbage collection
Conventional wear-leveling algorithm

## Slide 23: Dynamically Sizing the Hot and Cold Block Pools
All blocks are divided between the hot and cold block pools
Find the maximum hot pool size
Reduce hot virtual queue size to maximize cold pool lifetime
Size the cooldown window to minimize ping-ponging of data between the two pools
Notes: Guarantees data in the hot block pool is hot enough to skip refresh
Cold pool lifetime usually limits overall lifetime
Ping ponging hurts flash lifetime

## Slide 24: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 25: Methodology
DiskSim 4.0 + SSD model
Parameter | Value
Page read to register latency | 25 μs
Page write from register latency | 200 μs
Block erase latency | 1.5 ms
Data bus latency | 50 μs
Page/block size | 8 KB/1 MB
Die/package size | 8 GB/64 GB
Total capacity | 256 GB
Over-provisioning | 15%
Endurance for 3-year retention time | 3,000 PEC
Endurance for 3-day retention time | 150,000 PEC

## Slide 26: WARM Configurations
WARM-Only
  Relax retention time in hot block pool only
  No refresh needed
WARM+FCR
  First apply WARM-Only
  Then also relax retention time in cold block pool
  Refresh cold blocks every 3 days
WARM+ARFCR
  Relax retention time in both hot and cold block pools
  Adaptively increase the refresh frequency over time
Notes: Add color

## Slide 27: Flash Lifetime Improvements
Chart: Normalized Lifetime Improvement
| 15% Capacity Over-provisioning
Baseline | 1
WARM | 3.239
FCR | 8.0149
WARM+FCR | 10.4478
ARFCR | 10.6849
WARM+ARFCR | 12.8817
Baseline
WARM-Only
FCR
WARM+FCR
ARFCR
WARM+ARFCR
WARM-Only
3.24x
WARM+FCR
30%
WARM+ARFCR
21%
12.9x

## Slide 28: WARM-Only Endurance Improvement
Chart: 
| iozone | postmark | financial | homes | web-vm | hm | prn | proj | prxy | rsrch | src | stg | ts | usr | wdev | web | GMEAN
Cold pool | 0.9 | 0.98 | 0.30712 | 0.15239 | 0.13396 | 0.38488 | 0.9 | 0.24831 | 0.12781 | 0.063735 | 0.10053 | 0.078074 | 0.090213 | 0.18183 | 0.069639 | 0.15077 | 0.19722
Hot pool | 4.4536 | 0.10136 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 2.892 | 5 | 5 | 5 | 2.892 | 2.892 | 2.892 | 3.3929
3.58x
Notes: One reason for WARM’s lifetime improvement is endurance improvement.

## Slide 29: WARM+FCR Refresh Operation Reduction
Chart: % of Refresh Writes
| iozone | postmark | financial | proj | prxy | prn | hm | web-vm | src | stg | usr | web | rsrch | ts | wdev | homes | GMEAN
FCR | 0.013367 | 0.028721 | 0.48359 | 0.65361 | 0.7675 | 0.84382 | 0.91026 | 0.91325 | 0.93367 | 0.93379 | 0.94295 | 0.94661 | 0.95023 | 0.95406 | 0.96606 | 0.97177 | 0.53366
WARM+FCR | 0.0084218 | 0.019484 | 0.3699 | 0.53996 | 0.67255 | 0.76879 | 0.86293 | 0.86736 | 0.90029 | 0.90033 | 0.91458 | 0.92037 | 0.92588 | 0.93132 | 0.94993 | 0.95623 | 0.47527
Notes: WARM also reduces unnecessary refresh operations in extended lifetime.

## Slide 30: WARM Performance Impact
Chart: Normalized Avg. Resp. Time
| iozone | postmark | financial | homes | web-vm | hm | prn | proj | prxy | rsrch | src | stg | ts | usr | wdev | web | GMean
Normalized average response time | 0.99879 | 1.0212 | 1.0023 | 1.0578 | 1.0126 | 1.0402 | 1.0268 | 1.0364 | 0.99391 | 1.0009 | 1.0008 | 1.0017 | 1.0002 | 1.0012 | 1.0011 | 1.0071 | 1.0125
Worst Case: < 6%
Avg. Case: < 2%
Notes: Talk about partition -> garbage collection efficiency is lower in some cases

## Slide 31: Other Results in the Paper
Breakdown of write frequency into host writes, garbage collection writes, refresh writes in the hot and cold block pools
  WARM reduces refresh writes significantly while having low garbage collection overhead
Sensitivity to different capacity over-provisioning amounts
  WARM improves flash lifetime more as over-provisioning increases
Sensitivity to different refresh intervals
  WARM improves flash lifetime more as refresh frequency increases

## Slide 32: Outline
Problem and Goal
Key Observations
WARM: Write-hotness Aware Retention Management
Results
Conclusion

## Slide 33: Conclusion
Flash memory can achieve 50x endurance improvement by relaxing retention time using refresh [Cai+ ICCD ’12]
Problem: Refresh consumes the majority of endurance improvement
Goal: Reduce refresh overhead to increase flash memory lifetime
Key Observation: Refresh is unnecessary for write-hot data
Key Ideas of Write-hotness Aware Retention Management (WARM)
  Physically partition write-hot pages and write-cold pages within the flash drive
  Apply different policies (garbage collection, wear-leveling, refresh) to each group
Key Results
  WARM w/o refresh improves lifetime by 3.24x
  WARM w/ adaptive refresh improves lifetime by 12.9x (1.21x over refresh only)

## Slide 34: Other Work by SAFARI on Flash Memory
J. Meza, Q. Wu, S. Kumar, and O. Mutlu. A Large-Scale Study of Flash Memory Errors in the Field, SIGMETRICS 2015.
Y. Cai, Y. Luo, S. Ghose, E. F. Haratsch, K. Mai, O. Mutlu. Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation, DSN 2015.
Y. Cai, Y. Luo, E. F. Haratsch, K. Mai, O. Mutlu. Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery, HPCA 2015.
Y. Cai, G. Yalcin, O. Mutlu, E. F. Haratsch, O. Unsal, A. Cristal, K. Mai. Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories, SIGMETRICS 2014.
Y. Cai, O. Mutlu, E. F. Haratsch, K. Mai. Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation, ICCD 2013.
Y. Cai, G. Yalcin, O. Mutlu, E. F. Haratsch, A. Cristal, O. Unsal, K. Mai. Error Analysis and Retention-Aware Error Management for NAND Flash Memory, Intel Technology Jrnl. (ITJ), Vol. 17, No. 1, May 2013.
Y. Cai, E. F. Haratsch, O. Mutlu, K. Mai. Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling, DATE 2013.
Y. Cai, G. Yalcin, O. Mutlu, E. F. Haratsch, A. Cristal, O. Unsal, K. Mai. Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime, ICCD 2012.
Y. Cai, E. F. Haratsch, O. Mutlu, K. Mai. Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis, DATE 2012.

## Slide 35: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management
Yixin Luo, Yu Cai, Saugata Ghose, Jongmoo Choi*, Onur Mutlu
Carnegie Mellon University, *Dankook University
WARM